CONTENTS


      1.  ZMODEM Features at a Glance....................................   1

      2.  CUSTOMIZING GSZ................................................   3
          2.1    Setting the GSZ Screen Size.............................   4
          2.2    Speeding up GSZ.........................................   4

      3.  TUTORIAL INTRODUCTION..........................................   5

      4.  CALLING GSZ FROM COMM PROGRAMS.................................   6
          4.1    USE AN INTERFACE PROGRAM?...............................   6
          4.2    Ms-Kermit 3.00..........................................   6
          4.3    PROCOMM PLUS............................................   6
          4.4    Qmodem..................................................   8
          4.5    TELIX...................................................   9

      5.  BULLETIN BOARD CONSIDERATIONS..................................  12

      6.  DESCRIPTION....................................................  13

      7.  COMMANDS.......................................................  15
          7.1    List of Commands........................................  15
          7.2    Interrupt Keys..........................................  21

      8.  NUMERIC PARAMETERS.............................................  22

      9.  ENVIRONMENT VARIABLES..........................................  26

     10.  EXIT STATUS....................................................  30

     11.  EXAMPLES.......................................................  31

     12.  BACKGROUND OPERATION...........................................  32
          12.1   Windows 3...............................................  33
          12.2   VM......................................................  33

     13.  FLOW CONTROL...................................................  34

     14.  ERROR MESSAGES.................................................  35
          14.1   Got ZRPOS...............................................  36
          14.2   Subpacket too Long......................................  37
          14.3   Bad CRC.................................................  37
          14.4   Garbled Data Subpacket..................................  37
          14.5   Serial Input Error: Line Status Register xx ............  38
          14.6   No Carrier Detect.......................................  40
          14.7   Port %d (%X) defective..................................  40
          14.8   COMMAND NOT FOUND.......................................  40
          14.9   Out of Environment......................................  40










     15.  SLOW TRANSFERS.................................................  41

     16.  IN CASE OF DIFFICULTY..........................................  42
          16.1   LOCKUPS.................................................  42
                 16.1.1  Insufficient Memory  42
                 16.1.2  Environment TOO BIG  42
                 16.1.3  Bad COM Port Configuration  42
                 16.1.4  LAN Manager Conflicts  43
          16.2   Incorrect Batch Files...................................  44
          16.3   Cheap Internal Modems...................................  44
          16.4   Commands Entered in Upper Case..........................  44
          16.5   No Carrier Detect.......................................  44
          16.6   DOS 3.x.................................................  45
          16.7   Perstor Controllers.....................................  45
          16.8   IBM PS/2 Model 50Z......................................  45
          16.9   Brain Damaged UARTS.....................................  45
                 16.9.1  Everex Internal Modems  47
          16.10  Weird Iron..............................................  47
          16.11  PKARC 3.6...............................................  48
          16.12  Will the real YMODEM please stand up?...................  48
          16.13  286 and 386 Extended Memory.............................  48
          16.14  Disk Caches.............................................  48

     17.  ASSOCIATED DOCUMENTS...........................................  50

     18.  FILES..........................................................  51

     19.  Other Omen Technology Products.................................  53
          19.1   Professional-YAM COMMS TOOLS............................  53
          19.2   ZCOMM: Industrial Strength COMMS Shareware..............  53
          19.3   ZMODEM Developer's Collection...........................  53

     20.  FAIR PLAY......................................................  54
          20.1   Sharing GSZ Files.......................................  55
          20.2   REGISTRATION............................................  56
          20.3   Files on Registration Disk..............................  58
          20.4   Bulletin Board Registration.............................  59

     21.  CHANGES........................................................  61

     22.  ACKNOWLEDGEMENTS...............................................  64




















                                  Chuck Forsberg

                               Omen Technology Inc


                                     ABSTRACT



                   ZMODEM-90(TM) - Not just another XMODEM hack

     GSZ is one of many available programs that implement the ZMODEM file
     transfer protocol.  GSZ features the ZMODEM-90(TM) extensions including
     ZMODEM compression and MobyTurbo(TM) accelerator.

     GSZ's ZMODEM provides advanced file management features including two
     levels of Intelligent Crash Recovery(TM), and flexible control of
     selective file transfers.

     The ZMODEM file transfer protocol provides reliable file and command
     transfers with complete END-TO-END data integrity between application
     programs.  GSZ's 32 bit CRC protects against errors that sneak by "error
     free" modems and even the most advanced networks.

     ZMODEM safeguards all data and supervisory information with effective
     error detection.  (XMODEM and many recently introduced protocols do not
     protect vital supervisory data.)

     ZMODEM rapidly transfers files, particularly with modern modems,
     timesharing systems, satellite relays, and packet switched networks.
     ZMODEM's streaming operation eliminates delays caused by
     Kermit/XMODEM/YMODEM/JMODEM block acknowledgements.  ZMODEM eliminates
     traditional protocols' PACKET LENGTH compromises between transfer
     efficiency and error recovery; ZMODEM's packet length is the entire
     file.

     User Friendliness is an important ZMODEM feature.  ZMODEM
     AutoDownload(TM) (Automatic file Download without user intervention)
     provides a level of convenience unimaginable to users of traditional
     protocols.















       GSZ - a ZMODEM-90(TM), True YMODEM(TM), XMODEM File Transfer Program


                               Omen Technology Inc


     1.  ZMODEM Features at a Glance

     _______________________________________________________________________
     |   Feature              | ProCm | RZSZ | DSZ  | GSZ | ZCOMM | Pro-YAM |
     |________________________|_______|______|______|_____|_______|_________|
     |Security Verification   | no    | no   | no   | no  | no    | YES     |
     |Cybnertic Data Recovery | no    | no   | YES  | YES | YES   | YES     |
     |                        |       |      |      |     |       |         |
     |Command Download        | no    | YES  | no   | no  | YES   | YES     |
     |                        |       |      |      |     |       |         |
     |Update Directory Tree   | no    | YES* | no   | no  | YES   | YES     |
     | Create Directories     | no    | YES* | no   | no  | YES   | YES     |
     | Newer files Only       | no    | YES  | YES  | YES | YES   | YES     |
     | Protect files          | ?     | YES  | YES  | YES | YES   | YES     |
     | Common files Only      | no    | YES  | YES  | YES | YES   | YES     |
     |                        |       |      |      |     |       |         |
     |Collision Avoidance     | ?     | no   | YES* | YES | YES   | YES     |
     |                        |       |      |      |     |       |         |
     |Crash Recoverey         | YES   | YES  | YES  | YES | YES   | YES     |
     | Verified Accuracy      | no    | SZ   | YES  | YES | YES   | YES     |
     |                        |       |      |      |     |       |         |
     |ZMODEM-90(TM)           | no    | YES  | YES  | YES | YES   | YES     |
     | Compression            | no    | YES  | YES  | YES | YES   | YES     |
     | MobyTurbo(TM)          | no    | YES* | YES  | YES | YES   | YES     |
     | 7-bit Paths OK         | no    | YES* | YES* | YES | YES   | YES     |
     |                        |       |      |      |     |       |         |
     |OPERATING SYSTEMS       |       |      |      |     |       |         |
     | Text Translation       | no    | YES  | YES  | YES | YES   | YES     |
     | Record Format Support  | no    | YES  | YES  | YES | YES   | YES     |
     | DOS Shared Files       | ?     | -    | YES  | YES | no    | no      |
     | OS/2                   | no    | no   | no   | no  | no    | YES     |
     | VMS                    | no    | YES  | no   | no  | no    | YES     |
     | Unix/Xenix             | no    | YES  | no   | no  | no    | YES     |
     |                        |       |      |      |     |       |         |
     |True YMODEM(TM)         | no    | YES  | YES  | YES | YES   | YES     |
     |Demand Upgrade(TM)      | no    | YES  | YES  | YES | YES   | YES     |
     |File Transfer Display   | YES   | no   | no   | YES | YES   | YES     |
     | TOTAL File Xfer Data   | no    | YES  | YES  | YES | YES   | YES     |
     |________________________|_______|______|______|_____|_______|_________|

     ProCm = ProComm Plus
     * Not available on all flavors or platforms












     Chapter 1 Pg 2        GSZ Reference Rev May-29-93        Typeset 5-29-93


     *************************************************************************
                           GSZ registration is special.
     With most programs, registration only applies only to today's version.
     Not GSZ!

     GSZ registration bypasses the shareware announcement and unlocks
     advanced features in all future versions of GSZ.  You don't have to pay
     and pay again for new GSZ versions.  Omen's Demand Upgrade(TM)
     technology allows you to download and activate future GSZ versions
     without further registration!
     *************************************************************************


     DSZ Upgrade!!  Include your PAID REGISTRATION DSZ SNP CARD and take
     $15.00 off the registration fee!!  (The card must be mailed with the
     order.) (Be sure to copy your DSZ SNP for safe keeping.)









































     Chapter 1 Pg 3        GSZ Reference Rev May-29-93        Typeset 5-29-93


     2.  CUSTOMIZING GSZ

     The GCOLORS program customizes GSZ for your environment.  GCOLORS
     performs the following functions:

       + Customize GSZ's color complement (registration not required).

       + Save and fetch the color selection separately to allow "colorizing"
         new copies of GSZ

       + Insert your GSZ serial number and activation key

       + Initialize GSZ with your default communications port (registration
         required).[1]

       + Initialize GSZ with your default download directory.  (registration
         required).

     GCOLORS is menu driven and is mostly self explanatory.  First GCOLORS
     asks for the file name to modify; answer GSZ.EXE.

     Sight impaired users can disable the blinking selection pointer by
     calling "gcolors -q".

     The top menu provides several choices.

     Choose colors       Modify the GSZ file transfer display color scheme.

     Fetched saved colors Fetch the color scheme stored in GCOLORS.T.

     adjust for Monochrome display Adjust the color scheme for better
                         visibility on monochrome displays.

     Register            Accept your GSZ activation key and insert it in GSZ.

     Save changes        Save the color scheme in GSZ and GCOLORS.T.

     Quit

     If your copy of GSZ is registered, two additional choices appear.

     set download Directory




     __________

      1. The default port may be up to 7 characters, so portx definitions may
         be used.  The validity of the port specification is not checked.







     Chapter 2 Pg 4        GSZ Reference Rev May-29-93        Typeset 5-29-93


     set default Port

     Some Color Selection menu choices are not shown on the display:

     space     increment foreground color

     Enter     select the next field

     F         decrement foreground color (f increments)

     B         decrement background color (b increments)

     GCOLORS requires the file GREGDAT.$$$ to serialize GSZ.


     2.1  Setting the GSZ Screen Size

     Some BBS programs display status information such as the name of the
     caller at the bottom of the screen.  Normally GSZ clears all 25 screen
     lines,  but this can be modified with the GSZWINDOW environment
     variable:

     SET GSZWINDOW=24    protects the 25th line and disables the frame
                         shadow.

     SET GSZWINDOW=23    protects the 24th and 25th lines and disables the
                         frame and frame shadow.

     SET GSZWINDOW=21    Protects lines 22-25, disables the frame, frame
                         shadow, and the static data GSZ normally shows in
                         lines 22 and 23.

     SET GSZWINDOW=2     Starts the window at line 2.  This allows the
                         calling program to protect information on the top
                         line.  GSZWINDOW values of 3 and 4 also work.
     Setting GSZWINDOW does not affect the GSZ t command.

     2.2  Speeding up GSZ

     GSZ has a V numeric parameter that can be set to 1 to use direct video
     I/O for the status display.  This speeds up displays but may cause
     serial input errors when CGA equipped computers are used at high speeds.

     EXAMPLE: GSZ pV1 t

     sets direct video output.











     Chapter 3 Pg 5        GSZ Reference Rev May-29-93        Typeset 5-29-93


     3.  TUTORIAL INTRODUCTION

     If you are just starting out with GSZ, or if you have difficulty getting
     GSZ to work, please follow the procedure given below.

     Do not run any TSR or other COMM program.  This includes LAN programs.
     Reboot a clean DOS if necessary.

     Start with the following command given directly from the DOS prompt:

                             gsz port 1 speed 2400 d t

     Type it exactly as it appears above; do NOT use upper case.

     (Change the port number and speed as necessary.  Use only COM1 or COM2
     for testing.)

     This connects you to the modem.  Dial a bulletin board by typing AT
     commands to the modem ("ATDP621-3746 <enter>")[1] to make it dial the
     BBS.  Log in as usual.  Then, request a ZMODEM download of a file you
     don't already have.  The file will download automatically, you don't
     have to do anything.  This procedure verifies the correct operation of
     GSZ.

     Next you might try calling the BBS using a higher "baud rate".  This
     requires setting a higher speed with the "speed" command.  A "handshake
     on" command may be necessary along with commands to the modem to enable
     hardware handshaking in the CTS and RTS leads.

     Perhaps you got some error messages before or during the download.  The
     "ERROR MESSAGES" chapter explains all the commonly seen error messages
     and suggests solutions to the underlying problems.














     __________

      1. If your modem has a non standard setting the ATDT621-3746 command
         you type to the modem may not echo on the screen.







     Chapter 4 Pg 6        GSZ Reference Rev May-29-93        Typeset 5-29-93


     4.  CALLING GSZ FROM COMM PROGRAMS

     It may be necessary to add the DOS command: SET COMSPEC=C:\COMMAND.COM
     (change as needed) to your AUTOEXEC.BAT file to allow programs to call
     GSZ.

     Note: NO SPACES in the SET command!

     4.1  USE AN INTERFACE PROGRAM?

     A number of third party programs have been developed to provide a
     congenial interface to DSZ if you have enough memory to spare.  The
     XFER, POE, PCALL, DSZ_ZAP, and PROZ programs have been popular in
     interfacing DSZ to ProComm's editor gateway.  Many of these support GSZ
     as well.  These programs are available on many bulletin boards.

     Hint: the DOS PATH environment variable must include ProComm's directory
     to allow POE to locate all the POE files,.  The POE files should be
     stored in the ProComm directory.  Setting the "PROCOMM" environment
     variable is insufficient.


     Calling DSZ with these programs requires more memory than calling DSZ
     directly.

     4.2  Ms-Kermit 3.00

     The "push" command (^[p) in MS-Kermit 3.00 sends an XOFF character to
     the modem before calling DOS.

     Using this to activate GSZ's term mode with a "gsz t" command causes
     most remote hosts to stop.  The remote host can be un-wedged by
     keyboarding XON (Ctrl-Q) from GSZ's terminal mode.

     Add these macros to your MSKERMIT.INI file.  Courtesy Keith Petersen
     W8SDZ

     define sx run gsz F port 2 sx 1 2,define 1,define 2,
     define rz run gsz F ha on port 2 pY129 rz -r
     define sz run gsz F ha bo port 2 pY129 pB4096 sz 1 2,define 1,define 2,
     define t run gsz F ha on port 2 pY129 t -r


     4.3  PROCOMM PLUS

     It's easy to add GSZ to ProComm Plus 2.X.

     Datastorm has not licensed ZMODEM-90(TM) technology despite allegations
     that DSZ is now "built in" to ProComm Plus version 2.  Many users of
     ProComm Plus version 2.x use GSZ to get MobyTurbo(TM), Intelligent Crash
     Recovery(TM), and other ZMODEM-90(TM) features.






     Chapter 4 Pg 7        GSZ Reference Rev May-29-93        Typeset 5-29-93


     Make sure the GSZ program is in your search path.  If you don't see GSZ
     announce itself when called from ProComm, GSZ is not in your search
     path.

     Here are some handy settings for ProComm Plus.

     First, you may need to set the DOS environment before running ProComm.
     Give these commands to DOS before running ProComm Plus.  (These lines
     may be added to your AUTOEXEC.BAT file.)

     Note: NO SPACES in the SET command!
     SET DSZPORT=2                   (Only needed for COM2)
     SET DSZLOG=GSZ.LOG      (Only if you wish a log file)

     Then set ProComm's external protocol strings.  From terminal mode hit
     ALT-S, then select the PROTOCOL OPTIONS menu item.

     From that menu select EXTERNAL PROTOCOL OPTIONS.  Then set ProComm's
     external protocol strings to:
     A- External protocol 1 upload filename:  ZMODEMU
     B- External protocol 1 download filename: ZMODEMD
     C- External protocol 2 download filename: ZMODEMMD

     The following batch files are included in the GSZ zipfile:
     ZMODEMU.BAT (contains:  GSZ sz %1 %2 %3 %4 %5 %6 %7 %8 %9)
     ZMODEMD.BAT (contains:   GSZ rz)
     ZMODEMDR.BAT (contains:   GSZ rz -r)
     ZMODEMMD.BAT (contains:   GSZ rz -mr)
     ZMODEMAD.BAT (contains: GSZ t)

     !!!!IMPORTANT USE lower case (small letters) EXCEPT WHERE SHOWN!!!!


     *******************************************************************
     Select the ZMODEM PROTOCOL OPTIONS menu and turn off Auto downloading!
     *******************************************************************


     When sending (uploading) files with ZMODEMU.BAT give the ProComm window
     the full pathname (c:/foo/bar/file.ext) for *each* file not residing in
     the current directory.

     When downloading files with one of the other batch files shown above,
     Procomm will also prompt for parameters; just hit ENTER.  Or, you can
     enter options such as "-mr" if they are't included in the batch file
     itself.

     Once you've got the hang of things the "ProComm way", try the "gsz t"
     command described above to give you automatic ZMODEM-90(TM) downloads
     (Look Ma, no keystrokes!!!)..







     Chapter 4 Pg 8        GSZ Reference Rev May-29-93        Typeset 5-29-93


     You can also set the editor hot key (ALT-A) or view program hot key
     (ALT-V) by using the ALT-S "FILE/PATH OPTIONS" menu.  The strings for
     these keys are long enough to store an entire GSZ command line without
     need for a batch file.

     COM3 and COM4 on Procomm Plus are non standard; in case of difficulty
     use COM1 or COM2, or use the portx command.

     GSZ may not operate properly when called from ProComm if ProComm has
     files open at the time.

     A number of reports have been received of problems running GSZ from
     ProComm Plus because of insufficient memory.  Please refer to the
     subchapter on LOCKUPS.

     When running under ProComm's Host mode, failure to use the GSZ CON
     command may cause ProComm to interfere with file transfers or lock up
     the computer.

     EXAMPLE: GSZ CON sz %1


     Hint: the DOS PATH environment variable must include ProComm's directory
     to allow POE to locate all the POE files,.  The POE files should be
     stored in the ProComm directory.  Setting the "PROCOMM" environment
     variable is insufficient.


     4.4  Qmodem

     Changes in the Qmodem interface (arguments passed to the batch file) may
     require changes in the batch files shown below, depending on which
     version of Qmodem is used.

     If you define a protocol with 'Z' as its letter, the latest Qmodem will
     detect automatic ZMODEM downloads.  Defining an external 'Z' protocol
     disables Qmodem's internal ZMODEM, allowing GSZ to be called.

     The following is based on a message from Mike Cody, sysop of HomePlate
     313-385-9969 3/12/24/96 HST

     Go into Qinstall and go to frame 3 Directories. Then select External
     protocols #3 I think. Now you will see a definition area to tell Qmodem
     the Letter,batchfile combo to use.

     Now put Z in the letter definition, Zup.bat in the u/l batch zdown.bat
     in the d/l batch, and Y in the batch protocol. Now save it at the menu
     with f10 and S.

     Then go to DOS and create the following batch files in your Qmodem
     directory...






     Chapter 4 Pg 9        GSZ Reference Rev May-29-93        Typeset 5-29-93


     zdown.bat: GSZ port %2 speed %1 rz -rr

     zmdown.bat: GSZ port %2 speed %1 rz -mrr      ((FOR MOBYTURBO!!))

     zmdown2.bat: GSZ port %2 speed %1 est 0 %3 rz -mrr

     zup.bat: GSZ port %2 speed %1 sz %4

     !!!!IMPORTANT USE lower case (small letters) EXCEPT WHERE SHOWN!!!!

     These are the batch files that will be called by Qmodem.  If you did
     everything right when you hit PGDN or PGUP you will see an external
     protocol called Z) Zmodem in the box. For an easier time do a search for
     either External.arc or maybe the string "Qmodem" in the file database as
     there is a file with several external protocols and batch files
     available in the Mahoney file section (EXEC-PC BBS).

     The following batch files for Qmodem are included in the GSZ zipfile:

     ZDOWN.BAT contains:     GSZ port %2 speed %1 rz -rr
     ZUP.BAT contains:       GSZ port %2 speed %1 sz %4

     !!!!IMPORTANT USE lower case (small letters) EXCEPT WHERE SHOWN!!!!

     A variation on the receive batch file:
     c:elecomqmodem\*y.com ha slow est 0 %3 rz -mrr
     A variation on the send batch file:
     c:elecomqmodem\*y.com ha cts est 0 %3 sz %4


     If Qmodem says "unable to allocate swap space": QMODEM 4.2 will swap all
     but approx. 5K to memory or disk when you shell out to GSZ. Go into
     QINSTALL and make sure that /O /R Optimum Shell and Disk Shell are both
     set to ON.

     For older Qmodem versions (before 4.2) change the %4 in upload scripts
     to %3.

     4.5  TELIX

     Telix has an internal ZMODEM, but some users prefer to use GSZ for
     performance and/or reliability reasons.  Mat Fisher has published a
     Telix script to call GSZ for automatic downloads.

     For those of you who use GSZ with Telix, here is a sample script
     file to use instead of batch files:

     //////////////////////////////////////////////////////////////////
     //Protocol salt file for Telix's external protocols by Matt Fisher
     //Last edited (02/24/90)
     //used for the GSZ ZMODEM protocol.  (for u/ling & d/ling)






     Chapter 4 Pg 10       GSZ Reference Rev May-29-93        Typeset 5-29-93


     //////////////////////////////////////////////////////////////////

     str upload[80]  =
        "c:\telix\protocol\DSZ port 1 pW1 pB4096 ha off sz -b -m -rr ";

     str download[80]=
        "c:\telix\protocol\DSZ port 1 pW1 pB4096 ha off rz -b -m -rr ";

     //////////////////////////////////////////////////////////////////

     Main ()
     {
      if (_ext_filespec == "")
       { strcat(download,_down_dir); dos(download,0); }
      else
       { strcat(upload,_up_dir); strcat(upload,_ext_filespec); dos(upload,0); }
     alarm(1);
     }
     //////////////////////// THE END //////////////////////////////////

     Simple but effective...
     --- TAGMAIL v2.20
      * Origin: CRIMP/John Galt [Node 1] (1:120/144)
     INTERNET: Matt.Fisher@f144.n120.z1.FIDONET.ORG

     NOTE: The DSZ command strings given above are quite unusual.  Instead of
     the  "pW1  pB4096 ha off" one would be more likely to use "ha on" or "ha
     sw" depending on the modem's flow control settings.


        From : Bill Logan
     Subject : Help With Gsz For Telix

     I test and use a variety of terminal programs for individuals.
     One of which is telix.  I found the script language to be less
     than user friendly and installed GSZ via batch files and as an
     external protocol.  Here are the batch files:

     ZMUP.BAT

     GSZ pV1 port %2 speed %1 sz -mr %3

     ZMDN.BAT

     GSZ pV1 port %2 speed %1 rz -mrr %3

     Then go to ALT O in Telix and insert those batch names in the protocols.

     They worked fine for me.

     Bill






     Chapter 4 Pg 11       GSZ Reference Rev May-29-93        Typeset 5-29-93



     ---
      * Origin: PCConsultingAgencyII {=Telecom Node=} (1:300/22)

     Use the Telix ALT-O screen to disable Telix's automatic ZMODEM download.




















































     Chapter 5 Pg 12       GSZ Reference Rev May-29-93        Typeset 5-29-93


     5.  BULLETIN BOARD CONSIDERATIONS

     Note to the wise BBS operator: be sure you understand the restrict
     command, how and WHY to use it!

     When installing GSZ on a bulletin board or host system, be sure to check
     for proper operation when the caller hangs up while a file is being sent
     or received.

     Some bulletin boards do not call GSZ to send a file until they have
     verified the file's presence by actually opening the file.  If this
     checking is done in DOS's default exclusive open mode, gsz's file
     sharing will be defeated.

     If using a FOSSIL driver, you may need to call DSZ thru a batchfile.
     That file should call XU to disable X00 before running DSZ and reenable
     X00 afterwards. Failure to take this precaution may cause FOSSIL to
     steal the COM port from GSZ before file transfers are completed.







































     Chapter 6 Pg 13       GSZ Reference Rev May-29-93        Typeset 5-29-93


     6.  DESCRIPTION

     GSZ is a "protocol driver" that uses ZMODEM-90(TM), True YMODEM(TM), or
     XMODEM to transfer files over a serial port with a variety of programs.

     GSZ has two main commands for ZMODEM transfers: "sz" sends file(s), and
     "rz" receives them.

     When calling bulletin boards to download files with ZMODEM you can avoid
     the bother of starting GSZ for each transfer by GSZ's terminal emulator,
     before asking the BBS for the download.

                             gsz t

     The "t" command allows you to keyboard the file request directly to the
     BBS.  (The "t" stands for "terminal emulation".) Just give the "gsz t"
     command from DOS or your comms program's DOS GATEWAY.  GSZ's ZMODEM
     AutoDownload then receives the file automatically, using the filename
     provided by the BBS, without any wasted keystrokes or delay.  Try it,
     you'll like it!  (The "t" command is described below.)

     YMODEM downloads are almost as easy.  Use the "t" command as shown
     above, and hit the F3 key after telling the board to download a file
     with YMODEM.

     ZMODEM and True YMODEM(TM) transfers preserve exact file length and
     modification time.

     GSZ supports XMODEM-1k (XMODEM with 1024 byte blocks, sometimes
     mislabeled as ymodem) and CRC-16 with the sx -k and rc commands.

     GSZ is usually called from a communications or bulletin board program.

     GSZ uses its own modem I/O.  The original interrupt vector, UART parity,
     and interrupt configuration are restored on exit.  The original state of
     the 8259 interrupt mask bit for this vector is also restored on exit.

     GSZ uses DOS standard output (stdout) for messages.  GSZ never writes
     directly to the screen.  GSZ expects its standard output to point to the
     console, a logging file, or NUL, but never the modem port.  If gsz's
     standard output is redirected to the modem (as with ProComm's Host mode
     DOS shell), the combination will lock up the computer.  When necessary,
     gsz's standard output can be redirected back to the console device with
     the CON command.

     DSZ and GSZ automatically support Doorway 2.2 without extra commands.

     The RZ.BAT and SZ.BAT files are supplied for convenience when operating
     under Doorway.  RZ.BAT allows calling programs that emit an "rz" command
     to automatically start GSZ from the DOS command prompt.  SZ.BAT is a
     convenient command interface that complements RZ.BAT.  You may modify






     Chapter 6 Pg 14       GSZ Reference Rev May-29-93        Typeset 5-29-93


     SZ.BAT and RZ.BAT with your favorite options.
























































     Chapter 6 Pg 15       GSZ Reference Rev May-29-93        Typeset 5-29-93


     7.  COMMANDS

           ***********************************************************
                                    NOTE WELL
      Except as noted, all commands and options must be typed in lower case.
                             DO NOT USE UPPER CASE!!
                               Case is significant!
           ***********************************************************

     Optional commands or arguments are shown in square brackets [].

     When used (in any combination), the A, CON, port, speed, handshake,
     estimate, and d commands must be used in exactly this order.

     gsz [CON] [F] [port N] [speed S] [handshake XX] [pxN... ] [z pxN... ]
     [D] [d] [restrict] command

     The shareware program DOORWAY 2.2 interfaces well with DSZ, and provides
     many of the same functions, including the ability to run direct screen
     writing applications remotely.  DSZ and GSZ automatically support
     Doorway 2.2 without extra commands.


     7.1  List of Commands

     CON   Redirect message output to the DOS "CON" (console) device,
           overriding any previous redirections.  This is necessary to avoid
           lockups caused by ProComm host mode.  Most programs do not require
           this hack.

     F     Leave the 16550A UART FIFO enabled on exit.  Since GSZ has no way
           to read the 16550A DMA mode and trigger level bits, these values
           are not restored.

     port N select port N (n = 1,2,3,4,5,6,7,8, or 9) Default is 1 (COM1) or
           whatever is read from the DOS DSZPORT dos environment variable.
           COM11 to COM18 refer to the COM1 to COM8 ports on the PS/2.

           *****************************************************************
                                          NOTE
           Only COM1 and COM2 are standard on all PC compatible computers.
           Multiple standards exist for COM3 and above, so use only COM1 or
           COM2 when first installing GSZ.
           *****************************************************************

           GSZ COM3 uses 3E8 and IRQ4.  GSZ COM4 uses 2E8 and IRQ3.

           GSZ COM7 uses 2E8 and IRQ5.  GSZ COM8 uses 3E8 and IRQ5.

           If you wish to use COM3 or COM4 and your computer is not wired as
           shown above, you MUST use the "portx" command to specify the






     Chapter 7 Pg 16       GSZ Reference Rev May-29-93        Typeset 5-29-93


           actual base address and interrupt vector.

           EXAMPLE: to use COM2:
           gsz port 2 rz

           In multitasking operation, accessing a port used by another
           running program will hang the machine.


     portx base,irq[,divisor] To select an arbitrary port address and
           interrupt vector, the portx command must be used instead of the
           port command.  The portx command replaces the portcommand in the
           same place on the command line.  Please refer to GSZBG.DOC
           (provided on the Registration Diskette) or the Professional-YAM or
           ZCOMM (ZCOMMDOC.ZIP) manuals for details on this command.

           EXAMPLE: gsz portx 3e8,15 speed 19200 handshake on rz

           Newer UART chips can use raw bit rate sources up to 8 MHz or more,
           more than 4 times as fast as the IBM standard 1.84320 MHz.  Some
           386 and 486 machines support MobyBaud(TM) operation above 115200
           bps.  To support a nonstandard bit rate source, multiply 5760 by
           the new raw bit rate source frequency in MHz divided by 1.84320.

           EXAMPLE: gsz portx 3e8,15,57600 speed 19200 handshake on rz
           supports the 18.432 MHz clock option on the Boffin Electronics
           "WinSport II" 2 port serial board.  Your hardware configuration,
           BIOS firmware, operating system, device drivers, and TSR programs
           will determine the maximum useful speed.



     speed S Set the specified speed.  This command is rarely needed because
           GSZ reads the port's current speed by default.  Please refer to
           the FLOW CONTROL, MAIN COMMANDS and SOFTWARE COEXISTENCE chapters
           in DSZBG.ZOO or the ZCOMM or Pro-YAM manual for important
           information about the speed command.

           Please study all the chapters of this document when using speeds
           above 2400 bps.

           GSZ supports a maximum speed of 115200.  Not all hardware can
           support that speed without errors.


     handshake XX Enable one of several choices of hardware handshake.  (The
           default is XOFF/XON software handshake).  This command is
           documented in the ZCOMM or Pro-YAM manual, and in DSZBG.DOC.  (The
           ZCOMM manual is available on all bulletin boards registered for
           DSZ or GSZ as ZCOMMDOC.ZIP.) On GSZ the "handshake" command may be







     Chapter 7 Pg 17       GSZ Reference Rev May-29-93        Typeset 5-29-93


           abbreviated to "ha".

     D     Disables the modem (drops Data Terminal Ready, DTR) if carrier is
           lost.  This may be used to prevent spurious events (phone ringing)
           from interfering with the calling bulletin board's recovery from
           carrier loss.

     d     Disables carrier dropout monitoring, for modems that do not
           properly drive the "Carrier Detect" input on the PC.  If you see a
           No Carrier Detect message, you need to give the d command.  Before
           using the d command, make sure you have the proper port
           selected!!!


     estimate length [speed] Use the specified length and/or optional
           specified effective transfer speed to estimate transfer time for
           the next file to be sent or received.  The length argument is
           mainly used with XMODEM downloads; YMODEM and ZMODEM normally
           transfer the file length in the filename packet.  The estimate
           command must come after any port, speed, or handshake commands.

           The estimate command does not affect actual throughput.  It only
           affects GSZ's prediction of how much time a file transfer will
           take.

           The following makes GSZ calculate file transfer times based on 290
           character per second throughput.  Some error correcting 2400 bps
           modems can attain this throughput when MobyTurbo(TM) is used.

           EXAMPLE: gsz port 2 speed 9600 estimate 0 2900 rz



           EXAMPLE: gsz port 2 speed 9600 estimate 0 2900 sz bigmama.zip



     pxN   Set numeric parameter x to N.

           GSZ has two sets of numeric parameters, a base set and a "zmodem"
           set.  Parameters in the base control such things as date stamping
           of files, error exit value, etc.  The "zmodem" numeric parameters
           control timeouts, window sizes, and other ZMODEM, YMODEM, and
           XMODEM protocol parameters.

           These parameters are mostly a subset of the Pro-YAM/ZCOMM numeric
           parameters, and are listed below.  They assume their defaults each
           time GSZ is called.  Without an argument, p displays the numeric
           parameters and their values.

           EXAMPLE: gsz p






     Chapter 7 Pg 18       GSZ Reference Rev May-29-93        Typeset 5-29-93


     z pxN Set zmodem numeric parameter x to N.  All further numeric
           parameter commands are taken as zmodem parameters.  The zmodem
           numeric parameters correspond to the Pro-YAM or ZCOMM "zmodem"
           parameters and rarely need changing.  These parameters assume
           their defaults each time GSZ is called.  Without an argument, z p
           displays the zmodem numeric parameters and their values.


     restrict Restrict incoming pathnames (YMODEM/ZMODEM) to the current disk
           and directory tree, and disallow modification or overwriting of
           existing files.  This command is vital for bulletin boards
           uploading files.  The restrict command causes partially received
           files to be deleted.  When GSZ is restricted, it will refuse to
           transfer files containing the string autoexec.bat and command.com
           in upper or lower case.  This provides some defense from malicious
           uploaded files.

           EXAMPLE: gsz restrict rz


     t     [-T] [-8g] [-h] [-H] Talk with ZMODEM AutoDownload.

           The optional -T forces GSZ to exit after it has recognized a
           ZMODEM AutoDownload(TM) request.

           The optional -8g (available on registered copies only) enables
           reception of "BBS (ANSI) graphics" displays.  (A video device
           driver such as ANSI.SYS must be loaded to support some types of
           graphics.)

           The optional -h enables local echo of keyboarded characters ("half
           duplex").  In addition, -H makes the Enter key perform a local
           newline (CR/LF).

           A small subset of ZCOMM/Pro-YAM term function subcommands are
           recognized:

           Keyboard F1 or ALT-X to exit.

           F3 receives file(s) with True YMODEM(TM),

           ALT-P toggles parity between the 8n default and 8g (enables ANSI
           "graphics").

           ALT-H toggles two local echo ("Half Duplex") modes; the second
           displays a newline (CR/LF) when Enter is keyboarded.

           Keyboarded ASCII characters are sent to the modem.

           ALT-B sends a break.







     Chapter 7 Pg 19       GSZ Reference Rev May-29-93        Typeset 5-29-93


           Characters from the modem print on the screen.  A device driver
           such as ANSI.SYS may be used to recognize escape sequences.
           Standard ANSI.SYS is limited to a small subset of ANSI escape
           sequences; NANSI.SYS, FANSI-Console and other replacement console
           drivers provide faster screen updates and better ANSI terminal
           emulation.

           GSZ's ZMODEM AutoDownload(TM) detects the start of a ZMODEM file
           download and accepts the file(s) without operator intervention.

     rz    [-abeEmMnpPrt+YZy] [dir] [file ...]     (ZMODEM-90 receive) **

     rz    [-abenprt+Yy] [dir] [file ...]          (ZMODEM receive) **

     rb    [-abt+y] [dir] [file ...]     (YMODEM receive) **

     rb -g [-abt+y] [dir] [file ...]     (YMODEM-g receive) **

     rc    [-abt+y] file1                (XMODEM/CRC receive)

     ro    [-abt+y] file1                (XMODEM OverThruster receive)

     rx    [-abt+y] file1                (XMODEM receive)

     rx -g [-abt+y] file1                (Qmodem-G receive) **

           ** Download directory specification and -g ignored w/o
           registration


     sz    [-abefnprtFYQS+yZ] [-w[N]]  [PREFIX=p | ONAME=n] file ...(ZMODEM
           send)

     sz    [-abeEfmMnpPrtFYQS+yZ] [-w[N]]  [PREFIX=p | ONAME=n] file
           ...(ZMODEM-90 send)

           Pathnames are separated by spaces.  Wildcards are OK.

           EXAMPLE: gsz port 2 sz -r /tmp/file1 /tmp/file3 *.c


           The "sz" and "sb" commands exploit DOS's tree structured file
           system.  A directory or disk specifier expands to all files in
           that directory.

           EXAMPLE: gsz port 2 sz -r C:srcdir


           If you use PREFIX= or ONAME= with the "sb" or "sz" commands, these
           pathnames must be entered in lower case unless the underlying file
           system supports upper AND lower case.






     Chapter 7 Pg 20       GSZ Reference Rev May-29-93        Typeset 5-29-93


           EXAMPLE: gsz port 2 sz -r ONAME=newsrc.c temp.c



     sb    [-ft] [PREFIX=p | ONAME=n] file ...     (YMODEM or YMODEM-g send)

     sb -k [-ft] [PREFIX=p | ONAME=n] file ...     (YMODEM-1k or YMODEM-g
           send)

     sx    [-t] file1                    (XMODEM, XMODEM/CRC, Qmodem-G send)

     sx -k [-t] file1                    (XMODEM-1k send)


     v     Verify the serial number by writing a log entry (see DSZLOG).

           v      1     0 bps    0 cps   0 errors     0  128 s/n 666

           The letter "v" indicates a verification entry.  The first numeric
           field is 1 if YMODEM-g is supported.  The last field is the serial
           number.  Unregistered copies show a s/n of 0.


     o     Turn off Data Terminal Ready (DTR), terminating ("offing") the
           connection if the modem responds to DTR.  Useful with the "t"
           command to disconnect afterwards.

           EXAMPLE: gsz t o



     LARG  Convert ARG to lower case, then parse arg.


     The meanings of optional arguments to the file transfer commands are
     described in DSZBG.DOC and the ZCOMM/Pro-YAM manual.

     The s (SlugBait) option prevents a receiver from receiving a file
     without accounting for it.  Attempts to do so are flagged with a Q
     status in the log file.  This option can cause a transfer that
     legitimately fails near the end of the file to be reported as
     Questionable rather than ERROR.  SlugBait causes GSZ to return success
     if at least one file is transferred.

     Send files may be specified indirectly:
                               gsz sz @C:files.lst
     sends the files in C:files.lst.  This provides another means of
     bypassing the DOS command line limit.  The first letter must be "@" and
     the third letter must be ":" to distinguish this from an ordinary
     pathname.  Pathnames in the indirection file may be separated by any
     combination of space(s), tab(s), CR and/or LF.  No spaces may appear






     Chapter 7 Pg 21       GSZ Reference Rev May-29-93        Typeset 5-29-93


     inside a pathname; "FOO     .BAR" won't work.

     A list of files to send may be built up with a command like:

     EXAMPLE: dir *.zip > files.tmp

     This file can be edited to remove unwanted files.  Then you send the
     files with:
     GSZ sz -m @c:files.tmp


     7.2  Interrupt Keys

     Ctrl-Break Terminates the transfer in progress.

     ALT-N Abruptly terminates (NUKES) the transfer in progress.

     Ctrl-X Typing a dozen Ctrl-X characters to another ZMODEM program
          terminates ZMODEM operations.

     ALT-F Skips the current file in ZMODEM transfers.

     ALT-B Cancels the current ZMODEM session.


































     Chapter 8 Pg 22       GSZ Reference Rev May-29-93        Typeset 5-29-93


     8.  NUMERIC PARAMETERS

     GSZ uses the following main numeric parameters, settable with the pxN
     command.

     EXAMPLE: gsz pQ0 rz -rr


     **************************************************************************
     NOTE: Parameter setting commands such as "pd0" cannot be added to
     DSZOPT, they must be included in the command line.
     **************************************************************************

     In addition, GSZ uses the Pro-YAM/ZCOMM zmodem numeric parameters
     described in the Pro-YAM/ZCOMM reference manual (ZCOMMDOC.ZIP) and in
     DSZBG.DOC.


     B   Set the size of buffer used for disk reads and writes.  The default
         is 1024, 4096 maximum (16384 max on GSZ and DSZ.EXE).  If your copy
         of GSZ is running on a floppy disk system or a very slow turkey hard
         disk, a larger value may give better results.  Too large a value may
         exhaust memory, induce receiver timeouts, cause disconnects(!), or
         generate spurious CRC errors.  If performance logging doesn't work,
         this parameter is too big.

         EXAMPLE: gsz pB4096 sz A:floppy.fil

         Setting the buffer size may lock out the performance log, DSZFILES,
         and/or indirect pathname list in GSZ.COM.

         IF YOU AREN'T BLOODY SURE YOU NEED A BIGGER BUFFER, DON'T USE ONE.

         Please understand that the B parameter has nothing to do with
         anything you've heard about 128, 1024 or 8192 byte XMODEM style
         blocks.  Normally, ZMODEM's block size is the entire file!

     G   This parameter controls the number of bytes loaded into the 16550A
         transmit FIFO (First In First Out) storage register on each
         interrupt.

         For maximum efficiency, GSZ fills the 16 byte transmit FIFO when the
         UART generates a FIFO Empty interrupt.  Once loaded, data
         transmission from the transmit FIFO cannot be stopped, so many bytes
         may be sent after the modem sends XOFF or asserts hard flow control
         restraint.  Good engineering practice requires that modems accept a
         large number of bytes after asserting flow control restraint, but
         some modems and operating systems won't.

         This parameter is effective only with PCDOS machines using FIFO
         buffered UART devices.  To optimize gsz's responsiveness to flow






     Chapter 8 Pg 23       GSZ Reference Rev May-29-93        Typeset 5-29-93


         control restraint, set this parameter to 0.

         EXAMPLE: pG0


     O   This parameter controls XMODEM OverThruster(TM).  It is described in
         DSZBG.DOC.

     P   After a "speed" command, if you give a p command (display
         parameters), the P parameter value will indicate the type of serial
         I/O UART chip detected.  GSZ automatically detects and enables the
         FIFO on the NS16550A, NS16550AFN, Goldstar GM82C550, and Intel 82510
         chips.

         EXAMPLE: gsz port 1 speed 19200 p


         0  Indicates a standard 8250 or 16450 UART with no special features.

         1  Indicates an NS16550AN or NS16550AFN with 16 deep receive FIFO.
            These are the preferred chips.

         2  Indicates an Intel 82510 with 3 deep receive FIFO.

         The sequence "port 1 pP1 speed 19200" bypasses GSZ's verification
         checks normally performed on the FIFO configuration and may allow
         defective FIFO logic on certain chips to be used.  This incantation
         is not required for the NS16550AN or NS16550AFN.

         The sequence "pP-1 speed 2400" should be used with the Western
         Digital WD16550 chip to disable the brain damaged FIFO on that chip.
         The WD16550 FIFO has been observed to lose data when transmitting at
         2400 bps and slower speeds.  The minimum speed for normal transmit
         FIFO operation with the WD16C550 may vary with different computers.


     Q   Error code returned to DOS (default 1).  (Success always returns 0.)
         Some programs toss cookies when confronted with certain exit codes.

         EXAMPLE: gsz pQ-1 sz foo.bar


         GSZ reports an error if no files have been transferred, even if the
         command used wasn't supposed to transfer any file(s).


     R   If set to 1, causes partially received files to be deleted.

         EXAMPLE: GSZ pR1 rz








     Chapter 8 Pg 24       GSZ Reference Rev May-29-93        Typeset 5-29-93


     S   Timeout in seconds (default 15) waiting for restraint release (XON
         and/or handshake).

     V   (DSZ.COM and GSZ only) Set this to 1 to use direct to screen video.
         This speeds up displays but may cause serial input errors when CGA
         equipped computers are used at high speeds.

         EXAMPLE: GSZ pV1 rz

         sets direct video output.

     W   Wait for Enter key before exiting after an error.  Useful when
         calling GSZ from DESQview, allows the window to close unless there
         is an error message that should remain visible.

         EXAMPLE: gsz pW1 sz foo.bar


     Y   Control byte for the NS16550AN/NS16550AFN FCR register.  If you
         don't know what the FCR does, don't mess with this parameter.  It
         has been suggested that a different value (129) may improve
         multitasking under DESQview when multiple copies of GSZ are active.

     a   Calibrates certain protocol timeouts used with XMODEM and YMODEM
         transfers (Cybernetic Data Recovery(TM)).  This parameter does not
         affect ZMODEM transfers.

         The a numeric parameter is automatically set to 2000 for a 4.77 mHz
         PC or XT, 4000 for a PS2/30, 6000 for an 8 mHz 1ws AT, and 12000 for
         a PS2/80.  If your computer has a speedup card or otherwise runs
         unusually fast (or slow!) for its type, you may set the a numeric
         parameter to a value that reflects its speed.

         EXAMPLE: gsz port 2 pa4000 rb


         NOTE: Setting this parameter does not suppress the "Unknown Machine
         Type" message which is displayed before the command line is scanned.

     d   A non zero value (the default) causes incoming files received with
         ZMODEM and full YMODEM transfers to have their Date set to that sent
         in the file header.  ZMODEM's file management features depend on the
         transmission of each file's modification date.  Files will have the
         same creation date, even if the two machines are in different time
         zones.  When transferring files to/from a Unix system, creation
         dates are interpreted according to GMT or Universal Coordinated
         Time.  File dating may be disabled with a pd0 command, which causes
         files to assume the date and time they were received.
         NOTE: Backdating file creation times may confuse some backup
         programs.







     Chapter 8 Pg 25       GSZ Reference Rev May-29-93        Typeset 5-29-93


     v   Verbose level (debugging output) Negative values inhibit some
         routine messages.  Setting v to 1 or greater causes serialized
         copies to ring the bell when a transfer is done.

         EXAMPLE: gsz port 2 pv1 rz


     z   Timezone in minutes behind GMT, used for ZMODEM and True YMODEM file
         transfers to coordinate the actual date of the file with computers
         in other time zones.  PDT or MST corresponds to 420.  This may be
         preset with the ZONE DOS environment variable.














































     Chapter 9 Pg 26       GSZ Reference Rev May-29-93        Typeset 5-29-93


     9.  ENVIRONMENT VARIABLES

     The following DOS environment variables may be set to modify GSZ
     operation.  DOS environment variables are set by giving a command to DOS
     before running GSZ.  You can add these commands to your autoexec.bat
     file.


     EXAMPLE: set DSZPORT=2


     The following form may be used for arbitrary address/vector
     combinations:

     EXAMPLE: set DSZPORT=3e8,4

     These DOS "set" commands may be placed in your AUTOEXEC.BAT file or
     given just before you run your communications program.

     IMPORTANT! Do not add spaces to these commands!!
     set DSZPORT  =  2 WILL NOT WORK!


     DIRRX (Registered copies only.) Specifies the directory to receive
         (download) files.  If the sting in DIRRX ends with "/", directory
         and/or disk designators in the incoming pathname are stripped, and
         only the stem (name and extension) is used.  Otherwise, if an
         incoming file has an absolute pathname, the incoming pathname is
         used.

         EXAMPLE: set DIRRX=C:/modem/download/gsz/
         gsz rz -r
         downloads files to the /modem/download/gsz directory on the C:
         drive, with ZMODEM Crash Recovery..


         EXAMPLE: set DIRRX=B:/

         The DOS "set" command defining the receive directory may be placed
         in your AUTOEXEC.BAT file.  Make certain there is enough environment
         space to hold this value.  Confirm this by typing "set" to the DOS
         prompt and verifying the DIRRX value is listed correctly.

     DSZFILES May contain a list of up to 9999 pathnames to transmit, with
         entries separated by spaces.  If present, DSZFILES is used in place
         of a normal command line list of files to send with the sb and sz
         commands.

         EXAMPLE: set DSZFILES=file1 file2 file3 *.c
         gsz port 2 handshake on sz -rr







     Chapter 9 Pg 27       GSZ Reference Rev May-29-93        Typeset 5-29-93


         In practice, this string would be built up by a calling program and
         passed to GSZ with a "spawnvpe", "execvpe", or similar subroutine
         call.

         SEE ALSO: Pathname list specification @C:files.lst

     DSZLOG log file to receive entries for files sent and received.
         (Default null).  Sample entries:

     Z  46532 38400 bps 3324 cps   0 errors    66 1024 GSZ.COM 1177
     Z 124087 19200 bps 1880 cps   0 errors     6 1024 MXY.TMP 1177

         Transfer times are based on the DOS time of day clock and have up to
         two seconds' uncertainty.  As with all protocol throughput reports
         generated by Omen Technology programs (and contrary to the false
         claims of some critics), GSZ's throughput figures for ZMODEM,
         Kermit, and True YMODEM(TM) transfers do not take "credit" for
         pathname and/or protocol overhead characters.  GSZ's throughput
         reports do not include the time required to send the pathname.  This
         understates the true time required to transfer files, but the time
         required to send the pathname often depends on the alacrity of the
         operator, and thus does not always reflect the performance of the
         protocol itself.

         Transfers measuring less than one second are reported as having 9999
         characters per second throughput.

         The unlabeled numeric field after the error (retry) count is the
         number of flow control stoppages encountered sending the file.  Flow
         control restrictions are normal when the interface speed exceeds the
         communications speed (DTE > DCE).  This number gives an indication
         of flow control restrictions (overloaded networks, etc.) encountered
         during the transfer.

         The last numeric field before the file name is the YMODEM block size
         or ZMODEM subpacket length used for the last block in the file.

         The last field is the serial number of the other program, or -1 if
         this information is not available.  When sending files, the
         receiving program's serial number is not normally available unless
         the -S option is used.

         The code letter indicates the type of transfer, Z (ZMODEM), S
         (X/YMODEM), R (X/YMODEM), E (error), or L (transfer terminated by
         loss of data carrier).

         WARNING: If GSZ encounters a loss of carrier or other fatal error
         condition before a file COMMENCES transmission, a log entry may not
         be made.








     Chapter 9 Pg 28       GSZ Reference Rev May-29-93        Typeset 5-29-93


         EXAMPLE: set DSZLOG=C:/yam/gszlog


         IMPORTANT! NO SPACES!!


     DSZOPT (Registered copies only) String containing default options for
         GSZ file transfers.  Legal option letters for DSZOPT are the
         optional modifiers to the GSZ sz, rz, sx, rx, sb, rb commands.

         A T may be appended to the string to force GSZ to exit after it has
         recognized a ZMODEM AutoDownload(TM) request.

         An 8g may be appended to the string to make BBS (ANSI) graphics the
         default for GSZ's t command.  The ability to preset these options is
         especially helpful for controlling ZMODEM automatic downloads from
         GSZ's t command.

         EXAMPLE: set DSZOPT=r
         Enables GSZ's Intelligent Crash Recovery(TM) as a default.

         Let's say you wish ZMODEM crash recovery, and BBS "graphics" for the
         GSZ term function:
         set DSZOPT=r8g


         If you're downloading files from GEnie with an MNP modem, the
         following will speed up your downloads with Genie's ZMODEM-90Tm.
         (You can recognize ZMODEM-90 on GEnie two ways: 1) MobyTurboTm is
         used to speed ZIP and ARC downloads, 2) "sz 4.xx" is displayed at
         the end of transfer.  As of this writing, ZMODEM-90 may not be
         available in all libraries.) Note that (as usual with GSZ) case is
         significant: the "r" must be lower case, the "W" upper case.
         set DSZOPT=rW16384


         WARNING: Do NOT include "ena" or any other commands in the DSZOPT
         string.  With the exception of the "8g" mode, only **options** may
         be placed in the DSZOPT string!  (Options are the letters that
         modify the sz, rz, sb, etc. commands.  In "rz -r", "r" is an
         option.)

         Parameters can not be set in DSZOPT.

     MAXBYTES Maximum number of bytes allowed for transfer.  If this number
         is exceeded, GSZ skips the offending files (ZMODEM) or aborts
         remaining files in the batch (YMODEM).

     DSZPORT Default communications port override, default 1.

         EXAMPLE: set DSZPORT=2






     Chapter 9 Pg 29       GSZ Reference Rev May-29-93        Typeset 5-29-93


         IMPORTANT! NO SPACES!!



     ZONE sets the z numeric parameter to the number of minutes the current
         local time lags GMT time.  PDT or MST corresponds to 420.  PST
         corresponds to 480.
         EXAMPLE:
         set ZONE=420
















































     Chapter 10 Pg 30      GSZ Reference Rev May-29-93        Typeset 5-29-93


     10.  EXIT STATUS

     GSZ exits with 0 status for successful transfers or the value of the Q
     numeric parameter (default 1) if a file transfer failed, or if no files
     were transferred.  Many languages and "door" programs do not return this
     information to the calling program.  Some languages and "door" programs
     freak out (hang) on certain non-zero exit values.

     A batch file that calls GSZ directly may be used to detect the GSZ exit
     status with the DOS "errorlevel" construct.  Please refer to the Q
     numeric parameter below for more information.

     GSZ's log file entries may also be examined to determine the success or
     failure of a file transfer.

     GSZ commands are an improper subset of Pro-YAM/PowerCom/ZCOMM commands.
     The file transfer commands are fully described in ZCOMMDOC.ZIP, the
     ZCOMM User's Manual.  (ZCOMM is a full featured shareware communications
     program with autodialing, autolearn scripting, and terminal emulation.)
     Portions of the ZCOMM User's Manual are also provided in DSZBG.ZOO.  You
     may refer to one of those documents for details on the following
     commands.



































     Chapter 11 Pg 31      GSZ Reference Rev May-29-93        Typeset 5-29-93


     11.  EXAMPLES

     gsz sz c:foo.zip              (send 1 file with ZMODEM)

     gsz sz -m c:*.zip             (send all .ZIP files with MobyTurbo(TM))

     gsz sz f1.c f2.c f3.c         (send 3 files with ZMODEM)

     gsz sz c:foo.* b:*.c          (send multiple files with ZMODEM)

     gsz sz -Z *.lst               (send text files with ZMODEM compression)

     gsz sz -r bigone.zip          (CRASH RECOVERY: resume interrupted
     transfer)

     gsz rz -r                     (CRASH RECOVERY: resume interrupted
     transfer)

     gsz rz -rr                    (CRASH RECOVERY with file comparison)

     gsz handshake both sz yamdemo.zip       (Hardware+Software handshake)

     gsz sz -n *.*                 (send files that are newer or rx has no
     copy)

     gsz sz -Yn *.*                (Only send files that are newer than
     receiver's copy)
                                   (Do not send files that do not exist on
     receiver's disk)

     gsz rz C:/UPLOADS             (receive files to specified directory *)

     gsz port 2 speed 38400 handshake both restrict rz
                                   (Restrict provides protection for BBS's)

     gsz rz  -y prog.zip           (ZMODEM, single file pathname override)

     gsz z pr1 rx foo.dat          (XMODEM receive, remove file if error)

     gsz pO60 ro foo.dat           (XMODEM/OverThruster receive, GEnie MNP *)

     GSZ LRC L-Y NEWPROG.ZIP       (generate lower case "rc -y" command)

     gsz sz foo >debug.dmp         (Debugging data dump)

     gsz sz @C:/bbs/files.lst      (Indirect file list)

     gsz sz -u *.lst               (Unlink (Delete) files as they are sent)

     * Registered copies only







     Chapter 11 Pg 32      GSZ Reference Rev May-29-93        Typeset 5-29-93


     12.  BACKGROUND OPERATION

     Three DESQview description files are provided to demonstrate background
     operation with modest (66 kb window) memory requirements.  DSZ uses
     tight C/ASM code, table driven CRC generators, and buffered receive and
     transmit for good performance in the background without hogging CPU
     cycles.  On a QIC Labs 8 mHz PC-AT clone, DSZ can download files in the
     background (3 background clock ticks, 9 foreground clock ticks) with a
     throughput better than 9600 bps.

     GSZ operates under DESQview with 128k of memory.

     HINT: make sure "Separate Shift State" is set to "N".

     2S   Prompts for file name(s) and sends them with ZMODEM protocol.
          File: 2S-PIF.DVP

     2T   Talks to the modem and allows manual YMODEM (F3) or automatic
          ZMODEM downloads.  File: 2T-PIF.DVP

     2A   Like 2T, but using Quarterdeck's dvansi.com memory resident ANSI
          CRT device driver to process ANSI screen codes.  File: 2A-PIF.DVP
          DS.BAT is the batch file used by 2A.

     These files are written for a port 2 local connection and \TMP
     directory, but may be modified to suit your requirements using the
     DESQview CP command.  The W numeric allows DESQview to close the window
     after DSZ finishes, providing a pleasant user interface.

     Other DVPs, Scripts, and Batch files are available on the DESQView
     conference on the Sound of Music as DVDSZ20Z.ARC.

     Please consult the DESQview documentation for instructions on
     installation procedure for the DVP files.

     Operation at high speed (above 9600 bps) may require the DESQview
     "Optimize communications" performance Advanced Setup option.

     Newer versions of DESQview may require more "common memory" allocation
     (6-8 k bytes) to operate with DSZ.  Some versions of DESQview do not
     operate properly with DSZ; DESQview 2.0 is known to work, and DESQview
     2.25 is reported to have fixed bugs in intermediate versions.

     On 286 and 386 machines, some DESQview operations involve swapping
     memory contents with buffers in extended memory.  As with extended
     memory ramdisks and disk caches, this causes errors with high speed
     communications.  The considerations discussed in the "286 and 386
     Extended Memory" subchapter apply here.  Since this DESQview extended
     memory swapping is asynchronous with respect to DSZ's file transfers,
     "handshake slow" doesn't help here.  The solution is to force DESQview's
     memory swaps to use smaller blocks (with interrupts allowed between






     Chapter 12 Pg 33      GSZ Reference Rev May-29-93        Typeset 5-29-93


     blocks) and/or use NS16550AN or NS16550AFN or Goldstar GM82C550 chips
     for the serial interface.

     If you see funny characters on the screen while a program is loading,
     you have a conflict between the display adapter and QEMM memory manager
     which may cause lockups.  If so you must explicitly exclude the display
     adapter's memory with an EXCLUDE clause in QEMM's config.sys entry.

           ***********************************************************
                                     WARNING
     When running GSZ under a multi tasking system such as DESQview, do not
     allow two programs to access the same comm port at the same time.  At
     best, such actions will disrupt communications.  At worst, your computer
     will attempt to open a subspace channel to V'ger.

     Tell DESQview to use the SPECIFIC port number you are using, and not "Y"
     to the question: "Uses serial Ports (Y, N, 1, 2)"

     When running a comm program under DESQview or any related multitasking
     executive, GSZ must be called directly from the comm program, in the
     same window.  DO NOT open a separate window for DSZ unless you were
     about to power down the computer anyway.
           ***********************************************************

     With some communications programs, you can make the call, log in, and
     then exit (closing the window) without disconnecting the modem.  At this
     time you can fire up DSZ with the "t" command to allow YMODEM or ZMODEM
     downloads in a small window.
     Example File: 2A-PIF.DVP

     Alternatively, you can start DSZ from the DOS prompt, then type "AT"
     commands to the modem to call the bulletin board.  DESQview's "learn"
     facility may be helpful here.

     12.1  Windows 3

     Communications programs do not operate well under Windows 3 because
     Windows does not have true multitasking.

     12.2  VM

     According to Marshall Sutherland, Be sure to set IOPL3 mode to YES.















     Chapter 13 Pg 34      GSZ Reference Rev May-29-93        Typeset 5-29-93


     13.  FLOW CONTROL

     If you plan to send files over Telenet (PC-Pursuit), you must refer to
     the Pro-YAM or ZCOMM Reference manual (in ZCOMMDOC.ZIP) FLOW CONTROL
     chapter for vital information on flow control considerations necessary
     for proper operation of ZMODEM and other streaming protocols.  (ZCOMM is
     a full featured shareware communications program with autodialing,
     autolearn scripting, and terminal emulation.)

















































     Chapter 14 Pg 35      GSZ Reference Rev May-29-93        Typeset 5-29-93


     14.  ERROR MESSAGES

     COM2 1200 bps Carrier Detect enabled Handshake slow
     Command line = (commands)
     This is a normal message displayed to help resolve problems with
     incorrect batch files.  The port number, speed, carrier detect
     ("enabled" or "DISABLED") and "handshake" indicate the selected mode of
     operation.

     GSZ FINISHED! exit code = 0
     This is GSZ's normal exit when at least one file has been transferred
     and no unrecoverable errors have been detected.  If an error such as a
     failed file transfer had been detected, the exit code would be 1, or the
     value set in the Q numeric parameter.

     As the message implies, GSZ has done all of its processing, and has
     return the communications port and vector to its original value before
     displaying this message.  If the computer locks up after this message is
     displayed, there's something wrong with the program that called GSZ, not
     with GSZ itself.

     Unknown Machine Type XX, 'a' parameter preset to 6000 indicates a ROM
     BIOS that does not follow the IBM specification for identifying the
     machine type.  If your computer causes GSZ to display this message, you
     may set the a numeric parameter described elsewhere in this document.
     This message is generated before any commands are read, so do not be
     alarmed when you "discover" that setting the a parameter doesn't make
     this message go away.  The a parameter does not affect ZMODEM transfers.

     Please send us a postcard or letter indicating the reported hex value
     for machine Type, name of the computer, and its speed so we can include
     that machine type in a future release.

     Need more memory to run GSZ or Abnormal program termination is displayed
     by the TurboC startup routine if GSZ is run in too small a memory
     partition.  If you see this message, use a larger memory partition for
     GSZ or remove some memory resident programs.  This message may also
     appear if the calling program fails to free memory before calling GSZ.

     No Carrier Detect is displayed when GSZ recognizes a lack of carrier
     detect signal from the modem.  Most support calls concerning "No Carrier
     Detect" are caused by the user failing to tell GSZ to use the correct
     port.  GSZ does not magically divine the COM port number; if the default
     COM1 is incorrect, GSZ must be told what port to use with the port
     command or the DPORT environment variable.

     The No Carrier Detect message may also be caused by a line disconnect,
     defective cable, or incorrect modem strapping.  Sometimes this is caused
     by setting the B parameter to too large a value.

     The No Carrier Detect message may be disabled with the d command.  The d






     Chapter 14 Pg 36      GSZ Reference Rev May-29-93        Typeset 5-29-93


     command must be given after any port or speed commands.

     Garbage Count Exceeded Indicates ZMODEM has not detected a valid start
     of header in a reasonable number of characters.

     If GSZ becomes "stuck" on emitting this messages, it is possible the
     sending program may not be able to recognize and act upon transmission
     requests (ZROPS headers).  The sending program should be corrected.  In
     the meantime, setting a ZMODEM packet length with the "zmodem pl4096"
     ("l" is the small letter l) command will force the sender to wait for
     the receivers' progress reports.

     Permission denied comes from the Microsoft C Library.  This is caused by
     attempts to modify a read only file or directory, or to create a file in
     a nonexistent directory.

     Appearance of XOFF or FLOW during ZMODEM or YMODEM-g file sending
     signifies GSZ is responding to flow control restraint.  This is normal
     operation when error correcting modems or packet switched networks are
     used.  ZMODEM's robustness and reliability allow creative users to
     transfer files over unusual multiple computer lash-ups, causing modem
     data lights and computer status displays to dance in unfamiliar rhythms.

     Output FLow Control Restraint RELEASED Indcates GSZ has not received a
     positive flow control signal (XON and/or CTS as specified by the
     handshake command) within the timeout specified by the S numeric
     parameter.  This message may appear as the result of line noise.  If it
     appears often, it may indicate improper flow control settings, defective
     modem and/or cable, or (rarely) too small a value for the S numeric
     parameter.  A TSR program that monitors ring detect has also caused this
     problem.

     Not allowed to overwrite %s By default, GSZ will not overwrite an
     existing file.  Use the -y or -n or -r option to overwrite/update
     existing files.


     14.1  Got ZRPOS

     Got ZRPOS indicates the receiving program has detected a transmission
     error and has requested retransmission.  In other words, ZMODEM is doing
     its job of detecting and correcting missing and garbled data.

     If this happens with error correcting modems, or more often than
     observed line noise would suggest, the receiver's error messages must be
     studied.  "Line Status Register 01" messages indicate a flow control
     problem.  "Line Status Register 02" messages suggest a receiver problem
     with interrupt latency.

     Otherwise, the sender may have a flow control problem in one of four
     areas:






     Chapter 14 Pg 37      GSZ Reference Rev May-29-93        Typeset 5-29-93


       + Between the sending program and its modem.  If using an interface
         speed higher than the transmission speed, or modem to modem error
         correction (MNP, LAPB, PEP, etc.), check that the modem and the
         sending program are configured for the same flow control methods.
         Omen Technology's software is faster than most other programs, and
         may expose flow control problems not seen with slower software.

       + Between the sending modem and the network.  Correcting this requires
         "handshake both" to allow the sending program to honor both hardware
         (CTS) flow control from the modem and software flow control
         (XON/XOFF) from the network.

       + Between parts of the network, or between the host computer and its
         terminal server(s).  We have received a number of reports of
         problems with Cisco terminal servers.

       + Between the receiving modem and the receiving program.  This can
         happen at high transmission speeds when the receiver has specified a
         large I/O buffer size with the B numeric parameter.

         Excessive interrupt latency from extended memory ramdisks or disk
         caches, and poorly written hard disk drivers also wreak havoc on
         streaming protocols but do not affect start-stop protocols (XMODEM,
         etc.).  Problems with extended memory disk caches may cause errors
         at regular intervals; check the receiver's error messages.

         To work around these problems, give the "handshake slow" command to
         the receiver.

     14.2  Subpacket too Long

     This error may be caused by flow control problems at the sender (see
     above).

     14.3  Bad CRC

     This error may be caused by flow control problems at the sender (see
     above).


     14.4  Garbled Data Subpacket

     This error may be caused by flow control problems at the sender (see
     above).

     Byte NNNN retry M: <error message> These messages appear when the
     protocol has detected an error and is attempting to retransmit the
     garbled data.  These are normal messages.









     Chapter 14 Pg 38      GSZ Reference Rev May-29-93        Typeset 5-29-93


     14.5  Serial Input Error: Line Status Register xx

     Serial Input Error: Line Status Register HH indicates a hardware
     problem, slow device driver, TSR program, or other software is disabling
     interrupts too long for the program to accept incoming data, and some
     characters are lost.  A slow response to folow control also triggers
     this message.

     The value of the line status register is displayed in HEX.  The
     following error conditions are OR'ed into the Line Status Register.


     01   The Interrupt level circular buffer has been overrun.  This
          indicates a flow control problem.  The remote did not respond to
          GSZ's XOFF or hardware flow control signal, and continued to send
          characters after being told not to.  This problem is alleviated by
          matching flow control between the sending computer, modems, and the
          receiving computer.  Usually, the mismatch exists between the
          sending computer and its modem.


     02   An 02 value for the LSR indicates Data Overrun.  "Data Overrun"
          means the computer was not able to respond to an incoming character
          from the UART (modem) in time to make room for the next incoming
          character.  Data Overruns are caused by poorly designed software
          (or ROM BIOS "firmware") locking out interrupts for excessive
          periods.  These lockouts prevent the communications program from
          responding to the incoming characters quickly enough.

          Common causes of excessively long interrupt lockouts ("critical
          code regions") are disk drivers (BIOS), window managers (Windows 3
          is terrible), disk cache programs, TSR programs, and EGA/VGA board
          auto-select.

          Slowing the CPU to allow games and other time dependent programs to
          be used can generate excessive interrupt latency.

          Some BIOS programs are written without regard to their effect on
          high speed communications.  Better versions of the offending BIOS
          programs may be made available if enough users complain about poor
          performance.

          Interrupt latency caused by EGA/VGA board auto-select can be often
          corrected by disabling the board's Auto-Select.

          Device drivers and TSRs loaded in high memory sometimes cause
          interrupt latency problems that can be corrected by moving them
          into low memory.

          Poorly written disk caches and disk drivers cause interrupt latency
          that affects streaming protocols (ZMODEM) but not start-stop






     Chapter 14 Pg 39      GSZ Reference Rev May-29-93        Typeset 5-29-93


          protocols such as XMODEM, YMODEM, JMODEM, Lynx, etc.

          To correct Data Overruns, you must correct the offending
          condition(s) to allow the communications program to operate
          properly.

          The handshake slow command can be used to stop reception during
          disk transfers.  However, handshake slow is not always an effective
          alternative to correcting the real problem.

          Other chapters in this document give suggestions for working around
          excessive interrupt latency by using the NS16550AN UART chip.
          Please refer to the "Brain Damaged UARTS" subchapter.

          Please try all the suggestions mentioned here before contacting
          Omen Technology about data overruns.


     08   Framing Error generally caused by line noise or an incorrect
          transmission speed ("baud rate") or format (number of bits).  Also
          caused by some cheap internal modems.  Most protocols require 8
          bits no parity (-8n) for proper operation.  This is set
          automatically by Omen Technology programs, but other programs may
          not be so smart.


     10   Break Interrupt generally caused by line noise or an incorrect
          transmission speed ("baud rate") or format (number of bits).  Also
          caused by some cheap internal modems.


     18   Framing Error and Break Interrupt (see above) in combination.

          This error may also be caused by defective 8250 UART chips.  Some
          internal modem cards have slow 8250 chips that do not operate
          properly with computers faster than 4.77 mHz.  Replacing the 8250
          with a NS16550AN is recommended.  Please refer to the "Brain
          Damaged UARTS" subchapter for details.

     Please refer to the In Case of Difficulty chapter of this document for
     solutions.

     Less commonly encountered GSZ error messages are explained in the Pro-
     YAM manual.













     Chapter 14 Pg 40      GSZ Reference Rev May-29-93        Typeset 5-29-93


     14.6  No Carrier Detect

     If you see a No Carrier Detect message, and you haven't lost the
     connection, you should fix your modem cable or modem settings to allow
     proper operation of the Carrier Detect signal (CD).

     A poorer alternative is to give the d command:  gsz port 1 speed 2400 d
     t


     14.7  Port %d (%X) defective

     When GSZ selects a serial port, it performs a quick hardware check to
     verify the presence and minimal functionality of the 8250 family UART.
     This message usually means a nonexistent port has been selected.

     Reports have been received of functional but nonstandard UART chips
     triggering this message.


     14.8  COMMAND NOT FOUND

     If you see this message, make sure GSZ is in the DOS PATH.  Sometimes
     this error is caused by having too many environment variable strings.


     14.9  Out of Environment

     means there is not enough room in the program environment to accept more
     data.

     DOS prints this message when it cannot allocate more memory to
     accommodate a "set" command, such as "set dirrx=c:/downloads/".

     Try moving the "set" commands to the batch file that calls your comms
     program, or to your AUTOEXEC.BAT file.

     To increase environment, use the /E switch. The default is 160 bytes.

     An example for your CONFIG.SIS file: SHELL=C:COMMAND.COM/E:256

     NOTE: Large environments may cause GSZ.COM to lockup.  This is less of a
     problem with GSZ.EXE.














     Chapter 15 Pg 41      GSZ Reference Rev May-29-93        Typeset 5-29-93


     15.  SLOW TRANSFERS

     Some users report slower than expected file transfers even when few or
     no errors are reported.  Some possible causes are:

     If "handshake slow" is used, throughput may suffer.  Try one of the
     other solutions to the "Line Status Register = 02" errors discussed
     above.  When using "handshake slow" it may be possible to increase the
     modem's interface speed to 19200 bps or faster.

     Bad phone lines will silently slow MNP modems, sometimes without any
     error indications.  If the modems disconnect fairly often you should
     suspect marginal phone line conditions that are being hidden by MNP
     error correction.

     One of the programs may have set a parameter or option that acts to slow
     the transfer under certain conditions.








































     Chapter 16 Pg 42      GSZ Reference Rev May-29-93        Typeset 5-29-93


     16.  IN CASE OF DIFFICULTY

     16.1  LOCKUPS

     16.1.1  Insufficient Memory
     GSZ complains when it detects insufficient memory to operate.  When
     calling GSZ from another program, there may be ALMOST enough memory for
     proper operation, but GSZ locks up during a transfer or the calling
     program freezes after GSZ displays the "GSZ Finished" message.

     Sometimes there is a message about insufficient memory, sometimes just a
     lockup and no message.  To verify this problem, call CHKDSK from within
     your comms program (not from DOS!) by defining it as an external
     protocol.  If you use an interface program (Hotkeyz, Prodoor, etc.), you
     must call CHKDSK from that program, as those programs also reduce the
     memory available to GSZ.

     CHKDSK should report at least 64k free memory.  If less memory is
     reported, reduce the size of the COMMS program's capture buffer, or
     reboot the system with fewer/smaller device drivers and TSR programs.
     Calling GSZ directly from the comms program instead of from an interface
     also saves memory.


     16.1.2  Environment TOO BIG
     A large environment may cause GSZ.COM to lockup.  The size of the
     environment (the amount of text you get when you give the DOS "set"
     command) is subtracted from the data space available to 8086 C programs.
     This can be a problem with GSZ.COM, whose 8086 tiny model limits code,
     data, stack, and environment to 64 kb TOTAL.  Use GSZ.EXE (compiled with
     8086 small model) to alleviate this problem.


     16.1.3  Bad COM Port Configuration
     GSZ is fastidious about which interrupt vectors it takes over.  Unlike
     some programs, GSZ uses only the correct interrupt vector for its
     interrupt service routine.  (This allows multitasking.)

     GSZ obtains and releases this vector with standard DOS function calls.
     This allows multi line operation under DESQview and other multitasking
     systems.

     Incorrectly configured serial ports that work with programs that pig out
     both IRQ3 and IRQ4 will lock up with GSZ.  If GSZ locks up the machine
     as soon as it tries to send or receive data, this is usually the fault.
     Make sure the comm port is strapped correctly; COM1 uses IRQ4, COM2 uses
     IRQ3.  GSZ will lock up if the comm port is not properly set up.

     In addition, GSZ will not work properly if two devices are connected to
     the same IRQ line, even when some other programs (that don't use
     interrupts as intensively) do work normally on the same machine.






     Chapter 16 Pg 43      GSZ Reference Rev May-29-93        Typeset 5-29-93


     COM3 and above are not widely standardized.  If you have problems with
     COM3, chances are your "COM3" is non standard.


     16.1.4  LAN Manager Conflicts
     Some Local Area Network (LAN) managers take over comm ports using code
     that interferes with GSZ.

     The following hint is from Tom Louvaris, LANtastic Sales/Support - New
     York.  Other LAN managers may require similar incantations to keep the
     LAN manager from messing with GSZ's comm port.

     Problem: When the lan is running, GSZ intermittently fails.  GSZ starts
     the transfer by displaying "Ready to send pathname".  The receiving
     system does noting.  Eventually, GSZ exits with code 1, and no file is
     sent.

     To release one or more Com Ports with LANtastic 3.x, enter the
     following...

             Net Queue Halt \Sever-name Comn


     Note: You must be logged on to "Server-name" with Queue privileges to

































     Chapter 16 Pg 44      GSZ Reference Rev May-29-93        Typeset 5-29-93


     enable the operation of this command.

     16.2  Incorrect Batch Files

     Incorrect batch files are the number one source of problems using GSZ
     for uploads and downloads.  Bulletin board programs with convoluted
     batch file mechanisms exacerbate the problem.

     GSZ's command line echo was added to assist in correcting defective
     batch files.  You should see a display like:

     Command line = 'rz '
     or
     Command line = 'port 2 speed 9600 sz foo.baz '

     You may have to add a "pause" command at the end of the batch file to
     allow GSZ's messages to be seen.  Another possibility is to turn on the
     printer with ^P before running GSZ, so GSZ's message can be saved on
     paper.

     In general, the Command line display should look like one of the
     examples in this document or those displayed by GSZ itself.  (The
     Command line display does not include the name of the GSZ program
     itself.)

     Try running GSZ by itself, without any batch files or TSR programs,
     calling it directly from DOS as described above.


     16.3  Cheap Internal Modems

     Numerous trouble reports have been received lately caused by cheap
     internal modems causing errors on ZMODEM transfers but not XMODEM.  A
     similar problem was experienced in the mid 80's during beta testing of
     some 2400 bps modems.  Perhaps defective LSI chips left over from those
     days were cloned or recovered from the trash bin.


     16.4  Commands Entered in Upper Case

     Most GSZ commands and options must be entered in lower case (small
     letters, not big letters).  Where the documentation or help screen
     indicates "rz", you must use "rz" and not "RZ".


     16.5  No Carrier Detect

     If you see a No Carrier Detect message, and you haven't lost the
     connection, you should fix your modem cable or modem settings to allow
     proper operation of the Carrier Detect signal (CD).







     Chapter 16 Pg 45      GSZ Reference Rev May-29-93        Typeset 5-29-93


     A poorer alternative is to give the d command:  gsz port 1 speed 2400 d
     t


     16.6  DOS 3.x

     DOS 3.x systems may need to have a "STACKS = 8,256" line in CONFIG.SYS
     to prevent antisocial behavior. This is required on the NEC Multispeed,
     or if certain TSR's are used.


     16.7  Perstor Controllers

     Several reports have been received indicating Perstor disk controllers
     interfere with data communications.  Perstor is reportedly working on a
     fix.


     16.8  IBM PS/2 Model 50Z

     Early samples of this machine have a design error on the motherboard
     that causes comms programs to lock up the machine.  Replacing the
     motherboard with a correctly functioning unit from current production
     corrects the problem.  The part number of the replacement PS2/50 Z
     motherboard is 35F5928.  (Information provided by John M. Choma
     73047,3566) U.S. IBM stonewalled on this issue, but in December 1988
     agreed to replace the defective motherboards under warranty.


     16.9  Brain Damaged UARTS

     Omen Technology has received reports of problems with buggy 8250 type
     UART integrated circuits in Leading Edge modem boards, serial port
     interfaces, and computers.  The defective chip logic affects high
     performance software.  Replacing the buggy chip with a newer chip
     (NS16550AFN) corrects the problem.

     The UM82450 chip in the Zoom 2400HC also appears to cause problems.
     Zoom Telephonics advises that this problem is limited to their old
     model.  The old model has an external volume control.

     You can identify an old chip by inspecting the serial interface board
     for 8250 or UM82450 type devices.  A service technician or hardware
     hacker can help if you are not familiar with reading chip numbers.

     Dsz users can identify old chips with the following software command:

     EXAMPLE: dsz port 1 speed 2400 p

     The value for the P numeric parameter should be 1.  A value of 0
     indicates a non-buffered chip or a chip with a defective buffer.






     Chapter 16 Pg 46      GSZ Reference Rev May-29-93        Typeset 5-29-93


     ZCOMM and Professional-YAM users can look at the printout produced by
     the s command;  old UART chips register as TYP 0.

     The National Semiconductor NS16550AFN is a pin compatible plug in
     replacement for 8250 and 16450 serial chips.  Omen Technology PCDOS
     software enables the FIFO buffer in the NS16550AFN to prevents loss of
     data from poorly written device drivers, TSR programs, etc.

     We are also using the Goldstar GM82C550 chip with a 9025 date code.
     This Goldstar chip is plug compatible with the National chips.  No
     problems have been discovered with this chip.

     The NS16550AFN has better electrical characteristics than the older UART
     chips.  386 and fast 286 machines should use the NS16550AFN for best
     results.  Omen Technology software has been written to allow time for
     the older UART chips to operate. However, there is a limit to how much
     the software can rearrange chip accesses without resorting to
     performance robbing wait loops.  Some other software is not as forgiving
     of slow chips.

     Be sure to ask for the NS16550AFN.  It is VITAL to get the National
     Semiconductor "AFN" or "AN" chip.  Other vendors' chips not mentioned
     above won't do.  Current Western Digital WD16C550 chips do not function
     properly at low speeds.

     As of this writing, the Goldstar GM82C550, National Semiconductor
     NS16550AN and NS16550AFN are the only plug compatible chips that are
     known to work.

     If your UART chip is soldered in or otherwise not replaceable, you will
     need a new plug-in board with a good UART chip.  The cheapest such board
     to date is the KW-524E-1 Serial/Parallel/Game card, $30.90 from TSD
     Systems, 800-331-9130 (FAX 407-331-8130).  A board populated with two
     FIFO UARTS is $41.85.

     The Hayes ESP board comes with two serial ports with NS16550AFN devices.
     The ESP definitions for COM3 and COM4 agree with the industry standard
     definitions used by Omen Technology.  All option switches on the ESP
     board should be OFF except those used to select the port number (COMn).


     The $99 "WinSport II" from Boffin LTD 612-894-0595 has two NS16550AFN
     FIFO UARTS and also supports MobyBaud (18.432 MHz clock).  This card
     also supports higher IRQ numbers, freeing up the low IRQs for other
     applications.

     Software Electronics 503-640-1946 sells a $59 board with two FIFO UARTS
     and a bidirectional enhanced parallel port.

     The following information comes from a number of people:







     Chapter 16 Pg 47      GSZ Reference Rev May-29-93        Typeset 5-29-93


     "I have located a small dealer in New York who has the cards with or
     without the 16550.  I believe the price is around $50.00.  The company
     is RJK Consulting and the number is 718-968-9167. The gentleman to speak
     to is a Mr. RJ Kulman. ...  I got this information off the "Interlink"
     BBS system." Fm: Nick Braak [TRICON] 75156,1254

     Fry's - 415-770-FRYS.  This is a Silicon Valley electronic department
     store.

     Jameco Electronics at 415-592-8097 800-538-5000 sells National
     NS16550AFN chips mail order (credit card) in small quantities.
     Unfortunately, we received a number of reports (none recently) that
     their serial i/o card was supplied with the defective WD16C550 soldered
     in, even when ordered with specific instructions to include 16550AFN
     chips.

     TSD Systems advertise a 2 serial/parallel/game card with one or two
     NS16550-AFN chips.  800-331-9130(voice) 407-331-8130(fax)

     Microprocessors Unlimited, 24000 South Peoria, Beggs, OK. (918) 267-
     4961. The price for the chip is $13.50 plus shipping costs.

     Consolidated Computers 4 Shoppers Lane Suite 121 Turnersville, NJ  08012
     (609)751-9595(voice) (609)751-3843(bbs) (609)751-3840(fax)

     Arrow Electronics at 800-932-7769 (516-467-1000).

     Willies Computer Software Company: 800/835-4832.

     N.B.: Current Western Digital WD16C550 chips do not function properly at
     low speeds.  This has been confirmed with samples received directly from
     Western Digital.  WD is aware of this problem, but has not informed us
     of a corrected chip.



     16.9.1  Everex Internal Modems
     Numerous reports have been received concerning difficulties with Everex
     modem cards.  Some of these cards contain buggy 8250 chips which are not
     up to the demands of full duplex streaming protocols such as ZMODEM.
     Replacing the buggy 8250 chip with NS16550AN chip corrects these
     problems.


     16.10  Weird Iron

     A few machines, some with V20 CPUs, reportedly don't like DSZ.COM.  We
     have not been able to repeat this; TeleGodzilla (using a V20) runs
     DSZ.COM without a hitch.  Switching to DSZ.EXE has cleared up the
     problems on other machines.







     Chapter 16 Pg 48      GSZ Reference Rev May-29-93        Typeset 5-29-93


     16.11  PKARC 3.6

     It has been reported that PK36 grabs some interrupts and doesn't restore
     them on exit in an attempt to prevent hacks of the program.  Since
     eliminating that particular version and cleaning up memory, high speed
     transfers even with 8250 UARTS work properly again.

     The problem with PK 3.6 appears to be most severe if a BBS operator has
     doorware, etc that accesses the PK programs from a shell of some sort.
     This info may be helpful to users who are having otherwise inexplicable
     file transfer problems.

     Phil Katz has written me that this problem has been corrected in
     subsequent versions.


     16.12  Will the real YMODEM please stand up?

     Some XMODEM programs claiming to support YMODEM neither send nor accept
     the YMODEM pathname block.  1024 byte XMODEM is XMODEM-1k, not the
     YMODEM defined by Ward Christensen in 1985 when he invented the term
     YMODEM.  1987 and later versions of YMODEM.DOC remind the reader of the
     official YMODEM definition, which has not changed since YMODEM's coinage
     in 1985.


     16.13  286 and 386 Extended Memory

     Virtual memory disk caches and ramdisks using 80286 or 80386 extended
     memory require a kludge hardware reset of the CPU chip to return to the
     normal "real mode" after accessing extended memory.  This interference
     to the interrupt response time causes lost characters on comm ports, and
     may be minimized by specifying shorter memory transfers.

     Switching to a Goldstar GM82C550, National NS16550AN or NS16550AFN UART
     chip helps tremendously, allowing transfers at 115200 bps instead of
     9600 bps with a standard 8250.  Please refer to the subchapter on "Brain
     Damaged UARTs".  The GSZ "handshake slow" command may also help.


     16.14  Disk Caches

     Cache programs often interfere with ZMODEM transfers.  In one instance,
     replacing Microsoft's SMARTDRV.SYS with Multisoft's SUPERPCK.EXE helped.
     Norton NCACHE and and Multisoft PCQWIK have also caused errors.

     Some cache programs can be turned on and off; try turning it off when
     running GSZ.

     Switching to a National NS16550AN or NS16550AFN UART chip helps
     tremendously, allowing transfers at 115200 bps instead of 9600 bps with






     Chapter 16 Pg 49      GSZ Reference Rev May-29-93        Typeset 5-29-93


     a standard 8250.  Please refer to the subchapter on "Brain Damaged
     UARTs".  The GSZ "handshake slow" command may also help.























































     Chapter 17 Pg 50      GSZ Reference Rev May-29-93        Typeset 5-29-93


     17.  ASSOCIATED DOCUMENTS

     Consult the Professional-YAM, PowerCom, or ZCOMM manual chapter "OPTIONS
     FOR FILE TRANSFERS" for descriptions of the file transfer options.
     (ZCOMM is a full featured shareware communications program with
     autodialing, autolearn scripting, and terminal emulation.) The "FILE
     TRANSFER BASICS" chapter explains the relative merits of XMODEM, YMODEM,
     ZMODEM, and other protocols and gives tips on their use.  The "MAIN
     COMMANDS" chapter describes the rb, rx, rc, rz, sb, and sz commands.
     The "MODEM INTERFACING" and "FLOW CONTROL" chapters contain important
     information on the use of buffered modems with GSZ.

     Information on the ZMODEM Inter Application File Transfer Protocol is
     available in Omen Technology's "ZMODEM DEVELOPER's COLLECTION" ($89.00).

     Unix/Xenix C Source code for XMODEM, YMODEM, and ZMODEM transfers
     to/from Omen Technology Products is included in RZSZ.ZOO.[1] This file
     includes a Pro-YAM/ZCOMM script to upload a bootstrap file to a Unix
     system, compile it, and (if the compilation is successful) upload the
     rz/sz source files.  (ZCOMM is a full featured shareware communications
     program with autodialing, autolearn scripting, and terminal emulation.)


























     __________

      1. Technical support for rzsz is available on a paid consulting basis.







     Chapter 18 Pg 51      GSZ Reference Rev May-29-93        Typeset 5-29-93


     18.  FILES

     Some of the batch files mentioned in this document are not included in
     the archives.  Those that are needed can be readily created with your
     favorite editor.

     DSZ.COM, DSZ.DOC, 2A-PIF.DVP, 2S-PIF.DVP, 2T-PIF.DVP, BBS_REG.TXT,
     DS.BAT, FIX.BAT, MAILER, ZMODEMAD.BAT, ZMODEMD.BAT, ZMODEMDR.BAT, and
     ZMODEMU.BAT constitute Omen Technology's DSZ.ZIP.  These same files are
     in DSZ.ZOO on the distribution diskette mailed to registered users.[1]

     2S-PIF.DVP, 2A-PIF.DVP, DS.BAT, and 2T-PIF.DVP are used with Quarterdeck
     Office Systems' DESQview multitasking executive for background
     operation.  Their use is described in a previous chapter of this
     document.

     DGSZ.ZOO is distributed to GSZ registrants.  It contains GSZ.EXE and
     GCOLORS.EXE in addition to the above.

     ZCOMMDOC.ZIP (manual), ZCOMMEXE.ZIP (programs), ZCOMMHLP.ZIP (help
     processor and database), make up the ZCOMM communications tools
     shareware distribution.  The ZCOMM files are available on finer bulletin
     boards.  (ZCOMM is a full featured shareware communications program with
     autodialing, autolearn scripting, and terminal emulation.)

     RZSZ.ZOO contains ZMODEM "C" source code for COMPLETE Unix/Xenix
     programs licensed for use transferring files to/from licensed Omen
     Technology products.[2]

     RZSZ.TLB The ZMODEM rz/sz programs are available in native VMS flavors
     with wild cards, record format support, etc..  Pre compiled VAX/VMS
     files are contained in the RZSZ.TLB compressed text library, available
     in the TeleGodzilla (503-621-3746) upgrade/vms subdirectory, Compuserve
     VAXFORUM, GEnie, and other bulletin boards.

     DSZ.EXE compiled with the Xenix to DOS XC may give moderately higher
     maximum throughput noticeable on slower machines.  Sending from a faster
     machine to an 8 MHz IBM AT with 16550AFN, using 115200 bps and "sz -yZ
     rttypix":



     __________

      1. DSZ.ZOO is supplied to registrants instead of DSZ.ZIP because not
         all registrants have copies of unarchiving programs.  The
         registration disk includes a copy of BOOZ, a simple dearchiver for
         ZOO files.

      2. Technical support for rzsz is available on a paid consulting basis.







     Chapter 18 Pg 52      GSZ Reference Rev May-29-93        Typeset 5-29-93


     Program                       Throughput

     DSZ.EXE                       12735 cps
     DSZ.COM                       7164 cps

     ProComm+2.0                   5928 cps

     (Compare these speeds to those listed on Page 159 of the April 30, 1991
     issue of PC Magazine.  Results are even better with the compressible
     file used in the PC Magazine tests.)

     DSZ.EXE supports ZMODEM over 7 bit paths (E and P options), and
     specified control character quoting (-Q<string> option).  The DSZ.EXE
     requires somewhat more memory than DSZ.COM.  The maximum DSZ.EXE I/O
     buffer size available with the B numeric parameter is 16384.  DSZ.EXE is
     available in DSZEXE.ZIP and DSZEXE.ZOO.

     ZCOMM and Pro-YAM also run faster than DSZ.COM.  (ZCOMM is a full
     featured shareware communications program with autodialing, autolearn
     scripting, and terminal emulation.)

     DSZBG.ZOO contains DSZBG.DOC.  Part of the GSZ registration disk, this
     file provides background information on the ZCOMM/Pro-YAM commands
     provided in DSZ and GSZ.

     The ZOO archive format is a machine independent improvement on the PC-
     DOS specific .ARC format. The ZOO format has been precisely defined, and
     stable ZOO archivers/dearchivers are available on a wide variety of
     systems.

     BOOZ.EXE unpacks .ZOO archives.  BOOZ.DOC describes BOOZ.EXE.


























     Chapter 19 Pg 53      GSZ Reference Rev May-29-93        Typeset 5-29-93


     19.  Other Omen Technology Products

     19.1  Professional-YAM COMMS TOOLS

     Omen Technology makes Professional-YAM, a comprehensive comms program
     with unmatched power.  (Professional-YAM is a full featured commercial
     communications program with autodialing, autolearn scripting, and
     terminal emulation.) Flavors are available for PC-DOS, Unix, Xenix, and
     OS/2 Protected mode.  Unix source code is available under license.


     19.2  ZCOMM: Industrial Strength COMMS Shareware

     ZCOMM is a full featured shareware version with a $40.00 basic
     registration.  Registered GSZ users upgrading to ZCOMM get a free
     binder!


     19.3  ZMODEM Developer's Collection

     Omen Technology sells the "ZMODEM Developer's Collection" for $89.00.
     This diskette includes the most recent public domain versions of
     YMODEM.DOC, ZMODEM.DOC and the Unix/VMS rz/sz C source code for YMODEM
     and ZMODEM.  Porting to the intended application is the sole
     responsibility of the purchaser.  For many developers, this collection
     affords a significant labor savings in obtaining these materials.































     Chapter 20 Pg 54      GSZ Reference Rev May-29-93        Typeset 5-29-93


     20.  FAIR PLAY

     Unlike snazzy menu interfaces, reliable high speed transfer protocols
     take many hours of testing, often over expensive phone connections, to
     develop.  Two decades of communications experience and protocol testing
     are distilled in GSZ.

     GSZ is a user supported program developed and supported by Chuck
     Forsberg, owner of Omen Technology.  Countless hours of work and
     expen$ive resources went to develop and support GSZ for the myriad
     environments users use it in.  The fact that most of the problems people
     encounter with GSZ are caused by other software, hardware problems,
     failure to read the supplied documentation, or pirating has not kept
     users from seeking and getting help, even if it means calling the author
     in the middle of his sleep.

     Beyond this, the world of communications is constantly evolving, and it
     requires a significant ongoing effort to keep GSZ and its documentation
     up to date with the current state of the art.  Individuals with little
     knowledge of the dynamic nature of telecommunications (or hidden
     agendas) have misrepresented the frequency of enhancements to GSZ as a
     sign that GSZ is "unstable" and unworthy of "serious consideration".  If
     you think such sniping is fair play, you are more than welcome to use
     one of the many other protocol programs available, each of which claim
     to offer speed and reliability comparable to GSZ.

     Non registered users are welcome to use GSZ for a reasonable evaluation
     period.  "Reasonable" means "until you've decided whether the program is
     worth $30.00." It does not mean "until some competing program gets
     around to adding ZMODEM or True Ymodem(TM)".  Once you've evaluated GSZ,
     ethical use of GSZ requires registering the copy.

     GSZ is not and never has been Public Domain.  Every version of GSZ has
     included a Copyright Notice and a prohibition against sale or
     modification.  There is no usage counter or other Trojan Horse in GSZ,
     but if you use this program, you have a moral and ethical obligation to
     register it.

     Paid registration enables t -8g, DIRRX, DSZOPT, OverThruster(TM),
     YMODEM-g, and other advanced features that are present in GSZ.ZIP in
     encrypted form.  The registration package serializes and decodes all
     past and future versions of GSZ.COM and GSZ.EXE.  You can get a fully
     featured upgrade of GSZ simply by downloading a newer version from
     TeleGodzilla (503-621-3746), BIX, GEnie (IBM Roundtable), CompuServe,
     and trusted bulletin boards.












     Chapter 20 Pg 55      GSZ Reference Rev May-29-93        Typeset 5-29-93


     20.1  Sharing GSZ Files

     You are welcome to share unmodified copies of GSZ.ZIP or GSZ.ZOO with
     your friends and associates for their evaluation.  This documentation
     file and the MAILER file must be provided with all copies of GSZ except
     by prior written permission from Omen Technology Inc.  Because of piracy
     problems, Omen Technology must INSIST that GSZ be distributed only as
     part of the GSZ.ZIP file EXACTLY as provided by Omen Technology Inc, or
     in an archive which displays a CRC value for GSZ.COM equal to that shown
     in the Changes chapter.  If GSZ.ZIP is repacked, no files may be added
     to or removed from the archive.

     If you see an improperly packed or otherwise modified GSZ archive or
     parts thereof in a bulletin board, please ask the board's operator to
     replace such files with GSZ.ZIP exactly as provided by Omen Technology
     Inc.  Flame them until they behave ethically.

     Unmodified copies of Omen Technology shareware and demo files including
     GSZ.ZIP, DSZ.ZIP and DSZBG.ZIP may be distributed by "shareware
     distributors" provided 1) the files are clearly identified as
     unregistered shareware, 2) the cost of the distribution is nominal.
     Otherise, no version of GSZ may be sold without the prior written
     permission of Omen Technology Inc.

     GSZ is not and never has been Copy Protected.  "GSZ unprotect" files
     have no function whatsoever except to aid and encourage the theft of
     Omen Technology's Intellectual Property.

     Distribution or use of programs or procedures that modify, patch,
     disassemble, decompile, or otherwise reverse engineer GSZ without the
     prior written permission by Omen Technology Inc is a bloody theft of
     intellectual property and services and is a violation of Federal
     Copyright Law.  The same applies to debug scripts and documentation
     written for the same purposes.  These perform the same function as
     pirate satellite and/or cable descramblers, to obtain benefit from
     encrypted communications without proper payment.  Piracy has been
     investigated by the FBI and prosecuted under federal statutes.
     Applicable law provides for damages and recovery of attorney's fees.
     Omen Technology has received reports of serious problems caused by
     unauthorized patches to GSZ, and cannot assume liability for the
     performance of the resultant code.  So far, none of the slime producing
     such bilge have seen fit to sign their real name and address to their
     cretinous attempts at ego gratification.

     Distribution of GSZ in any medium without this documentation file is an
     unauthorized modification to GSZ that deprives the rightful author of
     registration revenues.  That is a theft of intellectual property.  Such
     distribution damages the author by forcing the user and author to waste
     time and phone bills scrounging for the documentation, and answering
     questions that are fully covered in the documentation.







     Chapter 20 Pg 56      GSZ Reference Rev May-29-93        Typeset 5-29-93


     If any version of GSZ is distributed with any other product, software or
     hardware, the product documentation must clearly and prominently state
     that the customer's continued use of GSZ requires registration directly
     with Omen Technology or its duly authorized agent(s).  When unregistered
     copies of GSZ are distributed on disk, a contemporary copy of
     ZCOMMDOC.ZIP should be included on the same disk.

     Thank you for your support.

     20.2  REGISTRATION


     DSZ Upgrade!!  Include your PAID REGISTRATION DSZ SNP card and take
     $15.00 off the registration fee!!  (The card must be mailed with the
     order.) (Be sure to copy your DSZ SNP for safe keeping.)  After a short
     evaluation period, ethical users must register their copy of GSZ with a
     check for $30.00 in U.S. funds sent to:

            Omen Technology Inc.
            P.O. Box 4681
            Portland, OR 97208

     The address on your check is sufficient, no need to fill out forms.

            For VISA/MC Registrations, you can also:
            Call VOICE: 503-621-3406

            Or register online: 503-621-3746  300-1200-2400-9600 bps
            Or FAX the INSTANT MAILER to: 503-621-3735

     Don't bother scrounging for an envelope, just print the INSTANT MAILER
     included in this archive!

     Overseas registrations are sent out International Air Mail.  Users,
     especially those overseas, may choose to register their copy of GSZ for
     $35.00 U.S.  by providing their VISA or Mastercard card number with
     expiration date and their name as it appears on their credit card.

     Purchase orders for less than $150 must be prepaid.  Omen Technology Inc
     Federal TAX ID #: 930858776 Oregon TAX ID #: 536565
      .ne 12

     "Das Recht zur Benutzung von DSZ in Deutschland, Oesterreich und der
     Schweiz erwerben Sie durch Bezahlung der Lizenzgebuehr von DM 57,00
     (incl. Mwst) an RzK

     Doris Koepke
     Bitzenstr. 11
     D-5464 Asbach

     Tel. 02683-4547, FAX 49 2683 4537, Telex 86 3705 rzk d, CIS






     Chapter 20 Pg 57      GSZ Reference Rev May-29-93        Typeset 5-29-93


     [70126,1660]. Sie erhalten dann von dort sowohl die neueste Version, als
     auch Ihren individuellen Software-Key, mit dem Sie auch kuenftige
     Shareware-Versionen "aufschliessen", also die in der Shareware Version
     nicht zugnglichen Programmfunktionen nutzbar machen koennen, per Post.
     Die Benutzung nicht registrierter Versionen stellt einen Verstoss
     geltenden Rechts dar und wird strafrechtlich verfolgt."


     *************************************************************************
     The user registration package includes a printed serial number password
     (SNP) card.  The registration "care package" diskette contains the
     latest versions of the GSZ programs, additional user documentation, and
     the installation program which uses your personal SNP to enable advanced
     features and bypass the opening advertisement.

     The registration package unlocks the extra value in all past and future
     versions of GSZ.COM and GSZ.EXE.
     *************************************************************************

     The unique serial number on the registration card is registered to the
     user, and is acceptable proof of registration to corporate auditors.

     The putsnp program inserts your unique DSZ Serial Number Password (SNP)
     into you copy of DSZ with the following command:
            putsnp dsz.com
     Putsnp prompts for your SNP and asks appropriate questions before
     inserting the SNP to enable the extra value in DSZ.

     GSZ is serialized with the GCOLORS program described above.

     Some TSR programs and device deivers interfere with putsnp.  If you have
     a lockup running putsnp, run it without any device drivers or TSR
     programs (boot a plain DOS from floppy disk).

     Your disk directory entry for GSZ will show the date and time you
     serialized your copy of GSZ.  This does not affect the revision date GSZ
     announces when GSZ is run.


     The only legitimate way to disable the opening advertisement in GSZ is
     to insert an authorized serial number and activation key obtained from
     Omen Technology into GSZ with the gcolors program.  Any other
     suppression or modification of the opening screen is an illegal,
     unethical theft of services.  Omen Technology has received reports of
     serious problems caused by unauthorized patches to GSZ, and cannot
     assume liability for the performance of the resultant code.

     Piracy is stealing.









     Chapter 20 Pg 58      GSZ Reference Rev May-29-93        Typeset 5-29-93


     20.3  Files on Registration Disk

     The following files are currently included on the Registration Disk sent
     to paid registrants.

     BOOZ.EXE       Program to unpack .ZOO archives.  BOOZ.DOC describes
                    BOOZ.EXE.


     DSZEXE.ZOO     Contains DSZ.EXE.

                    To dearchive with booz: booz x dszexe

                    Type "booz" without arguments to see the help message.



     DSZ.ZOO        Contains DSZ.COM, DSZ.DOC, DESQview description files.

                    To dearchive with booz: booz x dsz


     DGSZ.ZOO       Contains GSZ, DSZ, GSZ.DOC, and DESQview description
                    files.

                    To dearchive with booz: booz x dsz

                    RZSZ.ZOO contains ZMODEM "C" source code for COMPLETE
                    Unix/Xenix programs licensed for use transferring files
                    to/from licensed Omen Technology products.[1]

                    To dearchive RZSZ with booz: booz x rzsz


     PUTSNP.EXE     Installs your unique registered serial number to enable
                    the extra value in DSZ.  (GCOLORS is used for GSZ.)


     DSZBG.DOC      (in DSZBG.ZOO) Background information for GSZ and DSZ,
                    consisting of relevant parts of the ZCOMM User's Manual.

                    To dearchive with booz: booz x dszbg





     __________

      1. Technical support for rzsz is available on a paid consulting basis.







     Chapter 20 Pg 59      GSZ Reference Rev May-29-93        Typeset 5-29-93


     20.4  Bulletin Board Registration

     Note to the wise BBS operator: be sure you understand the GSZ restrict
     command and how to use it.

     Use and/or copying of GSZ by bulletin board sysops and/or systems is
     allowed according to the following conditions:

     I agree to feature the ZCOMM files (ZCOMMEXE.ZIP, ZCOMMDOC.ZIP,
     ZCOMMHLP.ZIP) for downloading, and to announce the availability and
     features of ZCOMM in any bulletins, help displays, or other displays
     that mention communications programs.  It is my responsibility to
     maintain reasonably current versions of the ZCOMM files on the BBS shown
     above.

     I understand that I am welcome to use GSZ on my bulletin board(s) from
     the time I sign and mail this document as long as I abide by the
     conditions above, including featuring the above mentioned ZCOMM files.

     I shall distribute GSZ.COM only as part of the GSZ.ZIP EXACTLY as
     provided by Omen Technology Inc, or "zipped" without any file additions,
     deletions, or modifications.  If I distribute GSZEXE.ZOO, I shall also
     maintain GSZ.ZIP in the same directory since GSZEXE.ZOO references files
     in GSZ.ZIP.

     If I see a modified GSZ archive or parts thereof in a file or collection
     of files (e.g., archive) on a bulletin board, I shall replace such files
     or archive members with the contents of GSZ.ZIP exactly as provided by
     Omen Technology Inc.  I shall report instances of noncompliance to Omen
     Technology.

     I shall not allow any version of gsz to be sold, modified, patched,
     hacked, disassembled, decompiled, or otherwise reverse engineered
     without the prior written permission of Omen Technology Inc.

     I understand that GSZ is not and never has been Copy Protected.  I fully
     understand that "GSZ unprotect" files have no function whatsoever except
     to aid and encourage the theft of Omen Technology's Intellectual
     Property.

     (For this BBS registration, a multi node bulletin board operating from a
     single, common file system counts as one machine.)

     The purpose of bulletin board registrations is to support and promote
     ZCOMM and Professional-YAM by popularizing the ZMODEM protocol and
     featuring the ZCOMM shareware files available for downloading.

     BBS registrations must be submitted on the bbs_reg form with signature
     and date, and must accompany a new paid GSZ or ZCOMM registration.  The
     paid registration that must accompany your BBS registration can be one
     submitted by one of your board's users.  Most boards have many






     Chapter 20 Pg 60      GSZ Reference Rev May-29-93        Typeset 5-29-93


     unregistered GSZ users, so getting one of them to register their GSZ
     should pose no difficulty.  Since the paid registration may be from one
     of your board's users, you can get your BBS registered for free by
     getting one of your users to register his/her GSZ at the same time.





















































     Chapter 20 Pg 61      GSZ Reference Rev May-29-93        Typeset 5-29-93


     21.  CHANGES

     Be sure to save your serial number/password (SNP) card and the putsnp
     program you received from Omen Technology to use with future versions of
     DSZ you may download!  (Use GCOLORS to serialize GSZ.)

     Current GSZ and DSZ versions are maintained on EXEC-PC BBS, BIX, GEnie
     (IBM Roundtable), CompuServe (IBMCOM and CONSULT SIGs) as well as Omen's
     TeleGodzilla (503-621-3746).

     DSZ is a popular program which has been the object of virus attacks.
     Pirated/hacked versions of DSZ have cost users and DSZ's developer
     thousands of dollars in lost time and other expenses, in addition to
     injuring of Omen Technology's reputation.

     Virus and Trojan code hidden in hacked/pirated copies of DSZ and
     programs claiming to "register DSZ" have caused loss of data.




     -rw-r--r--   1 caf      omen       32864 Apr 26  1992 gcolors.exe
     -rw-r--r--   1 caf      omen       70608 May 29 22:57 gsz.exe
     PKZIP -vt 32 bit CRC: AEFF337B   70608  gsz.exe
     PKZIP -vt 32 bit CRC: E83AEFB2   32864  gcolors.exe


     Your copy of GSZ should show the same CRC values.  ZIP uses a 32 bit CRC
     compatible with the Professional-YAM and ZCOMM "crc" command.
           pkzip -vt gsz
     The following Pro-YAM/ZCOMM command gives the 32 bit CRC for GSZ.COM:

     EXAMPLE: >>>c: crc gsz.com


     If your copy shows a different CRC or file length, insist on a
     legitimate copy and report the source of the bogus/pirated copy to Omen
     Technology Inc.  Omen Technology has received reports of serious
     problems caused by unauthorized patches to DSZ, and cannot assume
     liability for the performance of the resultant code.


     Good news for tired frog stompers!  The ZMODEM rz/sz programs are
     available in native VMS flavors with wild cards, record format support,
     etc..  Pre compiled VAX/VMS files are contained in the RZSZ.TLB
     compressed text library, available in the TeleGodzilla (503-621-3746)
     upgrade/vms subdirectory, Compuserve VAXFORUM, GEnie, and other bulletin
     boards.

     The DSZ and GSZ "t" command uses the DOS console driver for terminal
     emulation.  Standard ANSI.SYS is limited to a small subset of ANSI






     Chapter 21 Pg 62      GSZ Reference Rev May-29-93        Typeset 5-29-93


     escape sequences; NANSI.SYS, FANSI-Console and other replacement console
     drivers provide faster screen updates and better ANSI terminal
     emulation.

     DESQview users: make sure "Separate Shift State" is set to "N".  (Tnx to
     Tim Trott for this info.)

     May 29 1993: The portx command now works with IRQ's up to 15, and,
     optionally, nonstandard baudrate clocks.
     EXAMPLE: dsz portx 3e8,15 rz -m

     Newer UART chips can use raw bit rate sources higher than the standard
     1.8432 MHz.  Some 386 and 486 machines support MobyBaud(TM) operation
     above 115200 bps.

     To support a nonstandard bit rate source, multiply 5760 by the new raw
     bit rate source frequency in MHz divided by 1.84320.
     EXAMPLE: dsz portx 3e8,15,57600   sp 38400 rz -m
     supports the 18.432 MHz clock option on the Boffin Electronics "WinSport
     II" 2 port serial board.

     May 3 1993: SlugBait should now work for XMODEM and YMODEM.  Some
     problems with file transfers over 7-bit paths were fixed (DSZ.EXE,
     GSZ.EXE).

     Nov 9 1992: Unwanted registration info message removed from registered
     copies.  Enhancements to accomodate non standard XMODEM programs.
     Corrected spurious automatic recognition of hardware handshake
     configuration.

     May 3 1992: Recompiled to correct bad file size/CRC values in DSZ.DOC
     and DSZNEW, pruned some unused code.  No functional changes from April
     27 vsn.

     April 27 1992: The GSZWINDOW environment variable can be set to 1, 2 or
     3 to leave the top 1, 2 or 3 lines unmolested.  DSZ.EXE is compiled on a
     newer compiler and now supports file sharing.

     Bogus/hacked/infected files with early 1992 revision dates have been
     reported.

     Dec 13 1991: DSZ and GSZ automatically support Doorway 2.2 without extra
     commands.

     The RZ.BAT and SZ.BAT files are supplied for convenience.  RZ.BAT allows
     calling programs that emit an "rz" command to automatically start GSZ
     from the DOS command prompt.  SZ.BAT is a convenient command interface
     that complements RZ.BAT.  You may modify SZ.BAT and RZ.BAT with your
     favorite options.

     The GSZ file transfer display now shows a distinct color at the






     Chapter 21 Pg 63      GSZ Reference Rev May-29-93        Typeset 5-29-93


     locations where error retries occurred.  This gives a visual impression
     of the distribution of error retries.

     Oct 15 1991:  To accommodate other vendors' programs which do not
     provide a convenient way to control crash recovery, the "restrict"
     command security check is not performed if the destination file does not
     exist.

     Oct 8 1991: Some versions of putsnp were confused by a data pattern in
     the Oct 7 dsz.com, misplacing the installed serial number.  Oct 7 1991:
     The "t" (talk) command now accepts -h and -H to enable local echo.  Oct
     1 1991: Fixed an interaction between FIFO uarts and YMODEM-g termination
     after all files have been sent.  Fixed problem of some options being
     ignored on XMODEM and YMODEM downloads.  Fixed graphics display problem
     involving more than 40 MB of files.  Sep 4 1991: GCOLORS now saves the
     color scheme in a separate file GCOLORS.T.  Many small improvements in
     the GSZ file xfer display.  GCOLORS adds a "m" menu choice to remove
     color from the color scheme.

     A conflict between crash recovery and user specified short packets has
     been corrected.

     DSZ.EXE and GSZ now accept the "c" option to force incoming files to use
     a changed file name when a file with the same name exists.  The
     receiving program must support this new ZMODEM option or file
     disposition will be undefined.

     Aug 7 1991: Serial I/O modifications have solved a Wedge-O-Matic(R)
     problem with one hardware configuration (antique 2400 bps internal
     modem).  Hopefully this will solve similar non-replicatable problems for
     other users.

     A number of display fixes/enhancements to GSZ, including the addition of
     the GSZWINDOW environment variable enabling BBS sysops to protect BBS
     status lines at the bottom of the screen.


     July 29 1991: Corrections to gcolors registration function.

     July 28 1991: Some changes to GSZ and CGOLORS to improve human factors.

     "GCOLORS -q" disables the flashing reminder of which field is being
     modified.  This was added to help users with certain visual impairments.

     A few users have reported hung transfers wither certain hardware and/or
     software configurations.  We have not been able to replicate the
     problem, but have added code that recovers from lost interrupts.

     July 21 1991: Preview release of GSZ!!








     Chapter 21 Pg 64      GSZ Reference Rev May-29-93        Typeset 5-29-93


     22.  ACKNOWLEDGEMENTS

     32 bit CRC code courtesy Gary S. Brown.

     ZMODEM-90(TM), MobyTurbo(TM), The High Reliability Software(TM), Demand
     Upgrade(TM), TurboLearn Script Writer(TM), Cybernetic Data Recovery(TM),
     ZMODEM AutoDownload(TM), Intelligent Crash Recovery(TM), Error
     Containment(TM), Full Time Capture(TM), True YMODEM(TM),
     OverThruster(TM), Password Guardian(TM), CryptoScript(TM), and
     TurboDial(TM) are Omen Technology trademarks.

     PowerCom was trademarked in 1985 by POLYTRON Corporation, Hillsboro
     Oregon.

     True YMODEM(TM) is an Omen Technology Trademark signifying YMODEM
     protocol support that meets the full YMODEM specification.

     GSZ and this documentation are Copyright 1991 by Omen Technology Inc,
     all rights reserved.  GSZ is not and never has been Public Domain.
     Every version of DSZ has included a Copyright Notice and a prohibition
     against sale or modification.  This prohibition applies to any theft of
     the intellectual property and trade secrets contained in GSZ by
     decompilation, disassembly, or any other form of reverse engineering
     including but not limited to profiling, tracing, data analysis, or
     monitoring the operation of GSZ.

     Omen Technology copyright applies to its expression of the encoding and
     compression ideas expressed as code and byte streams used in the
     ZMODEM-90 enhancements.

     GSZ is not and never has been Copy Protected.  "GSZ unprotect" files
     have no function whatsoever except to aid and encourage the theft of
     Omen Technology's Intellectual Property.

                           Omen Technology Incorporated
                          The High Reliability Software

                       17505-V Northwest Sauvie Island Road
                              Portland Oregon 97231
                     Modem: 503-621-3746 Speed 1200,2400,V.32
                                FAX: 503-621-3735
                 CompuServe:70007,2304  GEnie:CAF   BIX:cforsberg