*********
                                      * ETCAI *
                                      *********

                         Electrical & Electronics Technology
                              Computer Aided Instruction


                          COPYRIGHT 1992,1993 by C. E. ORMON

                                    P.O. Box 1046
                                     Gautier, MS
                                         USA

                                     601-497-2566

















                                DISCLAIMER OF WARRANTY

          THIS SOFTWARE AND  DOCUMENTATION ARE   SOLD "AS  IS" AND  WITHOUT
          WARRANTIES  AS TO  PERFORMANCE  OF MERCHANTABILITY  OR ANY  OTHER
          WARRANTIES WHETHER  EXPRESSED OR IMPLIED. BECAUSE  OF THE VARIOUS
          HARDWARE AND SOFTWARE ENVIRONMENTS  INTO WHICH THESE PROGRAMS MAY
          BE  PUT, NO  WARRANTY  OF FITNESS  FOR  A PARTICULAR  PURPOSE  IS
          OFFERED. GOOD DATA PROCESSING PROCEDURE DICTATES THAT ANY PROGRAM
          BE THOROUGHLY TESTED WITH NON-CRITICAL DATA BEFORE RELYING ON IT.
          THE USER MUST  ASSUME THE ENTIRE  RISK OF USING THE  PROGRAM. ANY
          LIABILITY  OF THE SELLER  WILL BE LIMITED  EXCLUSIVELY TO PRODUCT
          REPLACEMENT OR REFUND OF PURCHASE PRICE.






                                  TABLE OF CONTENTS

          DISCLAIMER OF WARRANTY  . . . . . . . . . . . . . . . . . . .   1

          ETCAI FILE LIST . . . . . . . . . . . . . . . . . . . . . . .   3

          WHAT IS ETCAI?  . . . . . . . . . . . . . . . . . . . . . . .   4

          EQUIPMENT REQUIRED  . . . . . . . . . . . . . . . . . . . . .   5

          INSTALLATION  . . . . . . . . . . . . . . . . . . . . . . . .   6

          MAKING ETCAI EASIER TO USE  . . . . . . . . . . . . . . . . .   7

          OPTIONS . . . . . . . . . . . . . . . . . . . . . . . . . . .   7

          PRINTING  . . . . . . . . . . . . . . . . . . . . . . . . . .   7

          SCREEN PRINTING . . . . . . . . . . . . . . . . . . . . . . .   8

          SOUND . . . . . . . . . . . . . . . . . . . . . . . . . . . .   8

          VIDEO  DRIVERS  . . . . . . . . . . . . . . . . . . . . . . .   8

          NETWORK SUPPORT . . . . . . . . . . . . . . . . . . . . . . .   9

          RUNNING ETCAI FROM FLOPPY DISKS . . . . . . . . . . . . . . .   9

          GRADING STANDARDS . . . . . . . . . . . . . . . . . . . . . .   9

          QUESTIONS and PROBLEMS  . . . . . . . . . . . . . . . . . . .  10

          CUSTOMIZED VERSIONS . . . . . . . . . . . . . . . . . . . . .  12

          DEFINITION OF SHAREWARE . . . . . . . . . . . . . . . . . . .  12

          AGREEMENT . . . . . . . . . . . . . . . . . . . . . . . . . .  12

          UPDATE HISTORY  . . . . . . . . . . . . . . . . . . . . . . .  13

          SUPPORT . . . . . . . . . . . . . . . . . . . . . . . . . . .  14

          ORDERING INSTRUCTIONS . . . . . . . . . . . . . . . . . . . .  15

          INVOICE . . . . . . . . . . . . . . . . . . . . . . . . . . .  16








                                          2






                                   ETCAI FILE LIST

               ETCAI  distribution disks  should contain  the files  listed
          below after de-archive  and decompression has  been accomplished.
          See the topic "installation" for  decompression instructions. The
          only program designed to be executed directly from DOS is GO.EXE.
          The  remaining .EXE and .COM files are loaded and executed by the
          shell program GO.  Direct execution of some of the .COM files may
          hang your computer necessitating a re-boot. 
          GO.EXE     - This is the main shell program for all the exercises
                    in ETCAI. This program  allows the users to select  the
                    desired  exercise  using  a  familiar   pull-down  menu
                    process.  The  overlay   containing  the  exercise   is
                    automatically loaded  and  executed by  GO  after  user
                    selection.  GO.EXE  is the  only  file  in ETCAI  which
                    should  be executed  directly  from the  keyboard other
                    than  batch  programs.  Do  not  directly  execute  the
                    overlay programs listed below. 
          DC1.EXE        - Exercise overlay
          DC2.EXE        - Exercise overlay
          DM1.EXE        - Exercise overlay
          DM2.EXE        - Exercise overlay
          DIG1.EXE       - Exercise overlay
          ETCAI.DOC      -   This  file  contains   the  documentation  and
                         installation instructions for ETCAI.
          INSTALL.DOC    - This is a brief version of ETCAI.DOC containing 
                         the installation procedure.
          MATRIX.COM     - This is the active graphics screen driver. The  
                         distribution package  has MATRIX.COM set for  EGA 
                         and  VGA monitors.  The batch  programs MONO  and 
                         EGAVGA can be used to change  the active graphics 
                         driver.
          HERCULES.COM   - This file  contains the  graphics screen  driver
                         for HGA monochrome monitors.
          VEGA.COM       - A graphic screen driver for use with EGA and VGA
                          monitors.
          PRINTER.COM    -The   graphic  printer   driver  for   Epson  and
                         compatible  printers. 
          INVOICE.TXT    - Print and complete this form to register this   
                         software  or  use  a  school or  company  purchase
                         order.
          MONO.BAT       - A batch program used to install a graphic screen
                         driver  for   systems  using  hercules  monochrome
                         monitors.
          EGAVGA.BAT     - A batch program used to install a graphic screen
                         driver for EGA and VGA monitors.
          ETNET.BAT      - A  batch program  used to install  network file-
                         locking
          MATHDATA.CRD   - A data file containing welcome  screen data and 
                         system integrity information.
          CASIO.BBX      - A calculator overlay called on request by users.
          CALENDAR.BBX   - A calendar overlay called on request by users.

                                          3






                                    WHAT IS ETCAI?

               The ETCAI software  system consist of a  series of exercises
          useful for  aiding instruction of electricity  and electronics. A
          significant  feature  of  the  exercises  is  that  each  problem
          presented  consist of  randomly  selected  component  values  and
          parameters.  Further, the sequence  of presentation is randomized
          where  possible.   The topics  covered are  appropriate for  high
          school,  community  college,  and  trade  school  electrical  and
          electronics  training.  The exercises  can  be used  for  drill &
          practice, testing, remediation, and placement determination. Each
          exercise  prints out  a  "certificate" after  each  run with  the
          student name, elapsed time, and grade earned. Future versions are
          planned with  disk  based  record  keeping if  this  version  has
          reasonable success.  All programs  in this system  have extremely
          simple  user interfaces to focus  attention on the subject matter
          instead of "computerese". The simplicity of operation makes ETCAI
          a good  first introduction  to computers. Graphics  are presented
          where useful with the screen kept as clean as possible.  

               ETCAI  operates  within a  pull-down  menu  shell named  GO.
          Students  need only  type GO  to start  ETCAI. The  exercises are
          selected  from the menus using  either a mouse,  the keyboard, or
          both.  Where  useful,  the  ESC  key  will  evoke  an  on  screen
          calculator. All  ETCAI programs  have  full-screen editing  while
          accepting answers from students. This allows students to make any
          number of changes prior to selecting READY.  Several long running
          exercises have a QUIT option which can be found on  the ESC menu.
          Considerable  effort has  gone into  reducing the  possibility of
          accidentally  quitting  an  exercise.  Pressing the  ESC  key  in
          general  either  produces  an  innocuous  action  or  will  offer
          options.

               The  set of exercises within ETCAI were developed to aid and
          supplement  training,  not act  as  the  prime delivery  vehicle.
          Instructors should  find some  exercises useful whether  the main
          delivery vehicle  be self-paced, lecture/laboratory  or CAI.  The
          exercises can  play various roles in a training program including
          competency   testing,   drill   and   practice,   and   placement
          determination. In any  application, the exercises provide  varied
          on-line activity  with the  advantages of immediate  feedback and
          scoring.  More  and more  students  are  enrolling in  Electronic
          Technology  training   programs  with  weak  math   and  academic
          backgrounds. The typical student today requires more practice and
          individual attention  to reach an acceptable  level of competence
          than was required in times past. Computers and suitable  software
          can help in this  situation. A computer and  ETCAI can present  a
          student with any  number of drills which  are instantly corrected
          and graded at the students request.  This process encourages even
          the  struggling student to master the  process or procedure. With
          computers  having infinite  patience,  the diligent  student  can
          practice as long as needed to master a procedure. 

                                          4






               There is no expectation that all training programs will  use
          all the exercises in ETCAI. For some instructors, a few exercises
          may be so simple as to be a waste of time for their students. The
          simple exercises are included  to provide a "ground-up" structure
          to the exercise  set. Additionally,  a few exercises  may be  too
          difficult  or  conflict  with   methodology  taught  at  a  given
          institution.   An  example  might   be  the  exercise  "AMPLIFIER
          ANALYSIS".    This  exercise   not  only  generates  problems  on
          transistor circuit  analysis with "good"  components but  various
          "bad" components as well. This results in some rather challenging
          analysis  exercises. Adding to the challenge is the fact that few
          textbooks explain analysis  of amplifier circuits with  defective
          components.

               The development of  ETCAI was to a great extent  driven by a
          lack of  suitable software to support  electrical and electronics
          training. The CAI  materials currently on the  market tend toward
          two extremes. One, Systems can  be purchased which are  extremely
          expensive  and often require users  to buy not  only software but
          training  hardware   as  well.  Such  systems   often  require  a
          commitment  to  the  methodology  and  content  of  the  software
          package.  Two,   systems  are  available  which   have  extremely
          attractive graphics  ( moving  electrons, etc.) but  virtually no
          substance  (requirement  for  students   to  act,  analyze,  make
          decisions, etc.). Another  frequent shortcoming of  available CAI
          software is  a lack  of variability  in presentations.  A student
          repeating  an exercise in most systems will be presented the same
          activities and questions  in the  same order each  run. The  rote
          memorization  which   results  is   sometimes  mistaken   for  an
          understanding of  the lesson. ETCAI  certainly does not  fill all
          the shortcomings pointed  out above. The  material in ETCAI  does
          get computers actively and usefully involved in training students
          at  a small cost and without dictating a particular instructional
          methodology.
           






                                  EQUIPMENT REQUIRED

               The  minimum  equipment required  to  run  ETCAI is  an  IBM
          compatible computer with 512KB  memory, hard disk drive, printer,
          MS-DOS 3.3  or higher, and a  EGA, VGA, or  Hercules monitor. All
          processors from the  8088 up  can be used.  CGA monitors are  not
          supported because of insufficient graphic resolution.





                                          5






                                     INSTALLATION

               There should be at least  2 MB of free storage on  your hard
          disk  before  starting  the  installation  process  below.  ETCAI
          actually  occupies  approximately  1.3MB  of   disk  space  after
          installation. The installation process described below is for the
          authors  distribution package.  Most shareware  disk distributors
          use  the  same distribution  format  but  may include  additional
          files. Some copies of ETCAI may be repackaged by disk vendors and
          require a somewhat different installation process.
               ETCAI is  distributed in a compressed and archived format to
          reduce  the number of disks  required. Follow the  steps below to
          install  ETCAI on  your computer.  The distribution  disks should
          contain the listed files:
                         ETCAI.DOC
                         INSTALL.DOC
                         ET1.EXE
                         ET2.EXE
          STEP(1)   Prepare a directory  on your hard  disk for ETCAI.  Any
                    directory  name can  be  used. The  command line  below
                    could be given to produce a directory named ETCAI.

                         MD ETCAI

          STEP(2)   Enter the  directory prepared  for  ETCAI. The  command
                    line below could be used.

                         CD ETCAI

          STEP(3)   Copy the  contents of  all distribution disks  into the
                    directory. The number of disks will depend on the media
                    capacity. There are two 360KB disks, one  720KB disk or
                    1.44MB disks in  the distribution. Follow the  sequence
                    listed below to copy the files to the hard drive.
                         (Insert disk 1 in drive A:)

                         COPY A:*.*   C:

                    (INSERT disk 2 in drive A: if 360KB) 

                         COPY A:*.*   C:

          STEP(4)   Decompress the files  by running each of the .EXE files
                    as is detailed below.

                 (a) In response to the DOS prompt type the command line:

                         ET1

                    This will execute ET1.EXE which will decompress and de-
                    archive approximately half the ETCAI files.


                                          6






                 (b) In response to the DOS prompt type the command line:

                         ET2

                    This will decompress  and de-archive the remainder  the
                    ETCAI files.

          STEP(5)   Installation is  finished if you  have a VGA  (color or
                    mono) or EGA monitor. Proceed to step (7). Perform step
                    (6) only if you have a hercules monochrome monitor.

          STEP(6)   Type  MONO  to install  the hercules  monochrome screen
                    driver. Proceed to step (7).

          STEP(7)   Make sure your printer is on. Type GO to start ETCAI. A
                    menu should  appear on  the screen. Select  your option
                    using a mouse or the cursor keys on the keyboard.

                              MAKING ETCAI EASIER TO USE

               Beginning  students  who are unfamiliar with  DOS  can  more
          easily use the programs if a the batch file below is created  and
          stored in the root directory of the hard disk. 


               REM Batch File GO.BAT
               @ECHO OFF
               CD ETCAI    REM ( change to the directory containing ETCAI )
                    GO


          Name the batch file GO.BAT. Now all a student need do is boot the
          computer  then  type GO to start ET-CAI. The CD must  be  to  the
          directory containing ET-CAI which may be some other name.

                                       OPTIONS

          PRINTING - ETCAI is delivered with printing set to the text mode.
          This  produces a rapid but plain student certificate.  A  graphic
          print  mode  can  be installed which  prints  a  more  attractive
          certificate with graphics. The graphic print mode is considerably
          slower  than  text mode printing. The print mode  can  be  easily
          changed by starting  ETCAI in the setup  mode. The setup mode  is
          evoked by typing the command line GO SETUP in response to the DOS
          prompt   while  in   the  directory   containing  ETCAI.   A menu
          will appear which will allow you to choose either graphic or text
          printing. Some printer  models  may  not  be  compatible with the
          graphic printing  mode. Use the  setup mode  to set your   system
          back to  text  mode if  the  printer does  not produce  a  proper
          graphic printout.



                                          7






          SCREEN PRINTING - The  graphics screens produced by ETCAI  can be
          printed. The DOS file  GRAPHICS.COM must be made active  prior to
          running ETCAI in order to get graphic output to the printer. This
          can be  done in two ways.  (1) Execute the command  GRAPHICS/R in
          response to the DOS prompt prior to running  ETCAI. (2) Edit your
          AUTOEXEC.BAT file  adding the line GRAPHICS/R.  The second method
          is preferred in  that the graphics  capability is installed  upon
          booting your system. The /R option  tells DOS to print a  reverse
          image to  the printer which appears as dark on light as in ETCAI.
          A   graphic screen print-out can now  be requested at any time by
          pressing  the PRINTSCREEN  key or Shift/PrtSc  combination (which
          one depends  on the  keyboard type). Move the mouse cursor to the
          edge of the   screen before  requesting graphic printouts  unless
          you  want to use it as a  pointer. Being able to print screens is
          useful  to  both  students  and  instructors.  Students  can  get
          printouts of  problems missed  to determine  how they went  wrong
          off-line. Instructors can use screen printouts to "cut and paste"
          handouts, examples, and test items. For example, get a problem on
          the screen. Do a  screen print with the requested  answers blank.
          Next, select the ready button. ETCAI will, of course, say you are
          wrong  on all  items and  print the  correct answers.  Do another
          print screen. You now have a test item and the answer sheet! 

               The  previous  paragraph assumes  DOS  5.0  and   a  printer
          compatible  with the graphics output  from DOS. No assurances can
          be given that  graphics screen printing will  perform properly on
          all hardware/software combinations. 

          SOUND  - Several programs in the ETCAI series produce  sounds  at
          various  times while executing. The sounds may be distracting  if
          several  users  are  in a small area or an  open  computer  room.
          Sounds  made  by  most programs can be  disabled  or  enabled  by
          use of the setup mode.  Setup mode is entered by typing  GO SETUP
          in   response   to  the  DOS prompt  while   in   the   directory
          containing  ETCAI. Changes  made  in SETUP  mode  will remain  in
          force until GO SETUP is run again. 

          VIDEO   DRIVERS - ETCAI comes   with   the  EGA and  VGA graphics
          screen driver initially installed. The initially installed screen
          driver is  suitable for  EGA, VGA(color), and  VGA(monochrome). A
          driver  for hercules monochrome can be installed by executing the
          batch   program  MONO.BAT   by simply typing MONO  in response to
          the  DOS   prompt.  In  the  event you upgrade your  computer the
          EGA-  VGA  graphic  screen  driver can be  reinstalled by running
          the   batch   program    EGAVGA.BAT. The  program is  executed by
          typing EGAVGA   in  response   to   the   DOS prompt. Having  the
          wrong  graphic   screen  driver  installed  will cause the screen
          to go  "blank" when   ETCAI   is   started.  For systems used  by
          students, the  files  EGAVGA.BAT  and  MONO.BAT should be removed
          to  prevent accidental installation  of  the wrong screen driver.
          Copies of MONO.BAT  and EGAVGA.BAT should be retained  for future
          use.

                                          8






          NETWORK  SUPPORT -  File locking capability  can be  activated by
          running the batch file ETNET. The command ETNET ON activates file
          locking while  ETNET OFF  deactivates file locking.  File locking
          should be  activated only on systems  with a server disk.  Do not
          activate file  locking on stand  alone systems  unless SHARE  has
          been activated prior to executing ETCAI.
           
          RUNNING ETCAI  FROM FLOPPY  DISKS - ETCAI  requires approximately
          1.3MB  of  disk storage.  Therefore, it  is  possible to  run the
          system from 1.44MB floppy  disks. To run from floppy  disk, first
          install the system to a hard drive directory as  explained in the
          installation  section  of this  document.  Delete  the compressed
          files  ET1.EXE  and  ET2.EXE from  the  directory.  Copy all  the
          remaining  files in  the directory  to a  1.44MB floppy  disk. To
          execute the system,  log the floppy then type the  command GO. IF
          you choose to operate ETCAI from floppy disk, you should register
          the maximum number  of copies that  will be running at  your site
          simultaneously plus  the  number of  copies issued  or loaned  to
          students for off campus or evening work. Students at a registered
          site may  use one registered  copy each  away from the   physical
          registered site.

               Installation of  options will create,  or use  if exists,  a
          subdirectory  named SYSTEM  within the  directory in  which ETCAI
          resides. The  existence or nonexistence of  the files PRINTER.COM
          and NOSOUND.TXT set the printer mode and sound generation status.

                                  GRADING STANDARDS

               ETCAI  grades   numeric  student answers  to  a  percent  of
          accuracy.  The  tolerance  percentage  varies  from  4  %  to  7%
          depending on the number of "chained" calculations required in the
          exercise. Under certain circumstances this method of grading  can
          appear  to  defy Kirchhoff's law. For example, suppose  a  series
          circuit  consisting  of two resistors with 10 volts  applied  has
          actual  voltage  drops  of 9 volts and  1  volt  respectively.  A
          student  solves  the  problem inaccurately  with  the  respective
          answers 9.35 volts and .65 volts. The second answer being derived
          logically from Kirchhoff's law. The first answer would be  judged
          correct  with  an error less than 7 %. The second  answer  judged
          wrong  with an error of 35 % . You can quickly see that  students
          will  ask  " How can the first answer be right if the  second  is
          wrong  ?".  Yet the judgment is correct based  on  percentage  of
          accuracy.

               Students  should be cautioned not to use zero and letter "O"
          interchangeably.  Doing so  will cause  the program to  appear to
          grade items wrong. Entering  the characters 1O6,(one, letter "O",
          six )  looks like 106,  ( one hundred  six ) on the  screen after
          being  typed. However,  the exercise  program considers  a number
          ended  after the last numeric symbol. The exercise would consider
          1O6, (one, letter"O", six ) to have the numeric value 1 , (one ).

                                          9








               Digital  and  multiple  choice  answers are  graded  for  an
          absolute match with the correct answer. 

               String (text) answers require that students answer with term
          variables in a standard order. The exercises will accept terms in
          any order. Instructions for  order are present on the  screen for
          such  items when needed.  Students should  be cautioned  to avoid
          inserting extraneous  spaces in  answers. ETCAI handles  all non-
          decimal numbers as text. The binary number 101 ,one zero one, and
          101_ ,one  zero one space,  are not identical.  Extraneous spaces
          can cause  what appears  to  be a  correct  answer to  be  scored
          "wrong". 

                                QUESTIONS and PROBLEMS

          The large font headings  on my monochrome monitor look  "ugly" on
          the right side of my screen. What's wrong ? 

               Nothing. The screen appearances were primarily  designed for
          VGA  monitors.  Then compromised  somewhat  to  work on  hercules
          monochrome. The minor aberrations  seen on monochrome screens are
          purely cosmetic and appear only on welcome screens.

          I typed GO and the screen went blank. what's wrong ? 

               Most likely you  have the wrong  screen driver installed  or
          the  screen driver file is  missing. Check to  see that the files
          HERCULES.COM,  VEGA.COM, MATRIX.COM, MONO.BAT  and EGAVGA.BAT are
          present in the ETCAI directory. If you have a hercules monochrome
          monitor  type MONO  in  response to  the  DOS prompt  to  install
          hercules graphics screen driver. If you have a EGA or VGA monitor
          (color or monochrome)  type EGAVGA to install the graphics screen
          driver for EGA and VGA monitors. 
               Another  possibility is that  the switches on  your VGA card
          are set  locked to  the  CGA, VGA,  or other  mode.  Set you  VGA
          graphics card switches to the automatic mode if this is the case.
          Almost  all  software  will  work  properly  with  VGA  cards  in
          automatic mode.
               If you have a CGA monitor, ETCAI cannot possibly work. ETCAI
          uses 348 scan lines to display  images on the monitor screen. CGA
          only has 200 lines of display.
               You may  have a  corrupted file. Students  sometimes examine
          .COM and .EXE files using word processors then save the result  !
          The executable file is then corrupt. You must reload the software
          from scratch if this happens.

          I typed HERCULES just to see what HERCULES.COM does. The keyboard
          then locked up. Is the HERCULES program defective ?

               No.  HERCULES.COM like most .COM and .EXE files in ETCAI are

                                          10






          not intended to run from a keyboard command. You must start ETCAI
          from  the  GO shell.  The shell  program  loads and  executes the
          appropriate drivers and programs.

          I  got a printout  with the top portion  out of alignment. What's
          wrong ?

               The printer should generally be  turned on prior to starting
          ETCAI with the GO command. Turning  the printer on while ETCAI is
          running will occasionally  cause the effect  you describe on  the
          first print  request. ETCAI expects  DOS to have  initialized the
          printer. Requesting a printout and answering YES to printer ready
          while the printer  power is  off on some  systems using  hercules
          monochrome monitors  may cause a  keyboard lock-up. How  to avoid
          the problem ? Turn the printer on before starting ETCAI.

          Can ETCAI teach electronics by itself ?

               No. ETCAI is designed to support and complement conventional
          lecture/laboratory or self paced multi-media delivery systems. No
          pretence is  made to be  a self-instruction system.  The author's
          contention is that students learn best when a variety of delivery
          systems  operate  together  to  create  a  interesting   learning
          environment. ETCAI  is one of several tools and aids which can be
          used to enhance instruction.

          Are there plans to expand ETCAI ?

               Yes.  A number  of concepts  are being  developed. Exercises
          dealing  with Servos,  timers,  OP AMPs,  FETs, oscillators,  and
          numerous other topics are needed. A  version 2 is in the planning
          stages which will have a disk based record keeping feature and an
          expanded  set of exercises.  The actual development  of version 2
          awaits market support and acceptance of version 1.XX. 

          Why are the colors used in ETCAI so dull ?

               The color schemes used  in ETCAI are somewhat less  exciting
          than desirable. The colors were selected not only for appearances
          on  color monitors but for compatibility with hercules monochrome
          monitors. Monochrome compatibility does not allow adjacent colors
          except  where one color is  white. Several of  the exercises were
          originally developed on hercules monochrome. 










                                          11






                                 CUSTOMIZED VERSIONS

               The  author  of  ETCAI   will  consider  producing  modified
          versions of  the ETCAI system or  portions of the system  to suit
          specific  purposes.  The  fee  will,  of  course,  depend on  the
          complexity of the modification. Some types of modifications which
          can be done inexpensively  are: (1) changing the number  of items
          produced by an exercise, (2) adding your programs to the ETCAI GO
          menu, (3)  adding a school logo (.PCX image must be provided ) to
          the GO menu. Please send a description of the desired changes for
          a quotation of charges for a custom revision. 

                               DEFINITION OF SHAREWARE

               Shareware distribution gives users  a chance to try software
          before buying it.  If you  try a Shareware  program and  continue
          using  it,  you are  expected  to  register. Individual  programs
          differ  on  details --  some  request  registration while  others
          require   it,  some   specify  a   maximum  trial   period.  With
          registration, you  get anything from the simple right to continue
          using the software to an updated program with printed manual.

               Copyright  laws  apply  to  both  Shareware  and  commercial
          software, and the copyright holder retains all rights, with a few
          specific  exceptions  as  stated  below.  Shareware  authors  are
          accomplished programmers, just  like commercial authors, and  the
          programs  are of comparable  quality. (In  both cases,  there are
          good programs and bad ones!) The main difference is in the method
          of distribution. The author specifically grants the right to copy
          and distribute  the software,  either to all  and sundry or  to a
          specific  group.  For  example,   some  authors  require  written
          permission  before  a  commercial  disk  vendor  may  copy  their
          Shareware.

               Shareware is a distribution method,  not a type of software.
          You  should find software  that suits your  needs and pocketbook,
          whether it's commercial or  Shareware. The Shareware system makes
          fitting  your needs easier, because  you can try  before you buy.
          And because the overhead  is low, prices are low  also. Shareware
          has the ultimate  money-back guarantee  -- if you  don't use  the
          product, you don't pay for it.

                                      AGREEMENT

               Users  of ETCAI  must  accept this  disclaimer of  warranty:
          "ETCAI is supplied as  is.  The author disclaims  all warranties,
          expressed   or  implied,   including,  without   limitation,  the
          warranties of merchantability and of fitness for any purpose. The
          author assumes no liability for damages, direct or consequential,
          which may result from the use of ETCAI."



                                          12






               ETCAI  is a "shareware program" and is provided at no charge
          to the  user for  evaluation.   Feel free to  share it  with your
          associates, but  please do not give it away altered or as part of
          another system.  The  essence of "user-supported" software  is to
          provide  personal  computer users  with quality  software without
          high  prices, and  yet to  provide  incentive for  programmers to
          continue to develop new products. If you find this program useful
          and find that you are using ETCAI and continue to use ETCAI after
          a reasonable trial period, you must make  a registration payment.
          The registration fee for a single copy  of ETCAI for personal use
          is $45.00.  Sites can be registered for a fee of  $15.00 per user
          station for up to ten units and $10.00 per user station beyond 10
          units  ( minimum fee $90.00  per  site ). Each physical site must
          register  separately. A registered site may  issue or loan copies
          of ETCAI  to students for use  after school hours. The  site must
          register the number  of on  site user stations  plus the  maximum
          number  of  copies issued  to students  from  the site.  The site
          registration  fee also  covers  preparation of  a custom  welcome
          message  which will  appear  on the  screen  each time  an  ETCAI
          program  is started.  You must  treat this  software just  like a
          book.  An example is that this software may be used by any number
          of  people and may be freely  moved from one computer location to
          another on the  same site, so long as there  is no possibility of
          it being used  simultaneously by  more than the  number of  users
          licensed at this site. 


               You are encouraged  to pass a  copy of ETCAI  along to  your
          associates and  other institutions for their  evaluation.  Please
          encourage them to  register their copy if they find that they can
          use  it.  All registered users will  receive a copy of the latest
          version of the ETCAI system.   


                                    UPDATE HISTORY

          V0.1  - V0.8, 1/90 to  10/91. Stand alone  floppy based exercises
          developed and tested.

          V0.9  , 1/91.  Beta  testing  started  on  the  21  floppy  based
          exercises.

          V1.0  , 3/92. Tested and debugged programs converted to run under
          a shell for convenient operation on hard drive based systems.

          V1.1  ,  8/92.  10  additional  exercises  added  to  the system.
          Additional minor bugs  eliminated. Calculator and other  features
          added.

          V1.11 , 9/92. A "quit" option added to long running  exercises to
          prevent  trapping the  user into  answering all  questions before
          returning to the main shell menu.

                                          13






          V1.12  , 11/92.  File  locking option  added  to the  main  shell
          program to  allow reliable  operation on  disk  server based  LAN
          systems.

          V1.23  ,  1/93.  Restructured  program procedures  and  compiling
          methods to reduce disk  storage requirements. Also, converted bit
          mapped  graphics in  programs to  language primitives  to achieve
          reduced  code size. ETCAI system size has been reduced from 4.2MB
          to 1.3MB with insignificant performance trade-offs.

          V1.23b  , 3/93.  "Boolean  algebra" exercise  modified to  always
          properly handle input answers of  "1" .

          V1.24 , 5/93.  (a)  The user interfaces  for several  problems in
          the  DC/AC circuits group have been changed to eliminate the need
          for answering  certain items in sequential  order. This sometimes
          gave problems on the PR2 and  P(A) student answers if PR3 or P(T)
          were answered first. 
                         (b) The possibility of resonance in the series and
          parallel RLC circuits exercises has been eliminated. The resonant
          and near  resonant circuits  required calculations to  agree near
          perfectly  in  order  that the  phase  angle  item  be graded  as
          correct.

                                       SUPPORT

               Registered users  can obtain support information  by mail or
          telephone at  the address and phone number  on the cover sheet of
          this document. Primary support is via mail. All inquiries will be
          responded to  promptly.   Telephone support is  available between
          the hours  of 3:45 and 9:00 pm  CST USA on most  week days. Three
          months  of support are included in the registration fee.  Contact
          ETCAI products for extended support  service pricing. Significant
          updates within the  same version of ETCAI will  be supplied at no
          cost  during  the free support interval. 

               Registered  users will  be informed  of the  availability of
          updates, "add on" items, and new version releases. 

               The author  of ETCAI  invites comments and  suggestions from
          registered users and reviewers of the shareware distribution. 












                                          14



                                ORDERING INSTRUCTIONS

          SINGLE COPY :

                Send your payment of $45.00 to:     ETCAI Products
                                                    P. O. Box 1046
                                                    Gautier, MS 39553
                                                          USA 

               Your payment  can be  made in  the   form  of USA  currency,
          Western  European currency,  check ( USA banks), USA postal money
          orders, and  international  postal money  orders.   Your copy  of
          ETCAI with your name appearing on the welcome screen and  a bound
          manual will be sent promptly.

          SITE REGISTRATION:

               Purchase   orders  are   accepted  from   any  credit-worthy
          institution  or organization. Payment can  also be made by check,
          U.S postal  money order,   International postal money  order, USA
          currency, and Western  European currencies. Complete  the invoice
          on the next page and send it to the business  office for payment.
          A copy  of the  invoice should  also be sent  to ETCAI  to supply
          welcome message  data.  Alternately, complete  a  institution  or
          company purchase order with  the data shown on the  invoice form.
          ETCAI is  registered on a  site license basis.  Registration fees
          are  $15.00  per user  station for  the  first 10  user stations.
          $10.00 for each user station beyond 10 users at a  site. The user
          station count  should include direct  on site copies  plus copies
          issued  or loaned to students to run on their personal computers.
          The  minimum fee per site is $90.00.  Send all orders and fees to
          the address given on the invoice form on the next page.

               Registered sites will receive  a personalized copy of ETCAI,
          a printed and bound copy of the ETCAI documentation, three months
          of support for the current version of ETCAI, and a signed license
          agreement. Registered sites  will also be informed of new version
          releases and ETCAI extensions as such items become available. 

               European orders can be processed and paid in local  currency
          through selected disk vendors.  One such vendor is TRAX  Computer
          Applications of Belgium. The text  file EUROPE.TXT can be printed
          to  get the  full address  data for  vendors with  local currency
          agreements  with ETCAI.  EUROPE.TXT  is not  included in  the USA
          distribution of ETCAI.














                                          15



                                     ***********
                                     * INVOICE *
                                     ***********
          REMIT TO:                                    FROM:

          ETCAI Products                  ________________________________
          P. O. Box 1046
          Gautier,  MS  39553             ________________________________
          USA 
                                          ________________________________

                                          ________________________________

           QTY            ITEM NAME             UNIT PRICE        TOTAL   
          ----------------------------------------------------------------

          _____    Single user copy of ETCAI    @ $41.00     _____________
           
          _____    ETCAI software Registration  @ $15.00 ea  _____________
                   up to 10 units. (min. 6)
          _____    ETCAI software Registration  @ $10.00 ea  _____________
                   of over 10 units per site.
                   Shipping, handling, media    @ $4.00          $4.00     
                                                                           
          ________________________________________________________________

                                   ***** TOTAL *****        ______________
          ________________________________________________________________
              
                 DISK TYPE  3 1/2 _______    5 1/4  ________

          PRINT OR  TYPE THE WELCOME  MESSAGE DESIRED: (  Site registration
          only)

          All lines do not  have to be filled. Maximum characters  per line
          is 26. Any text on the first three lines will be in a large font.
          Remaining  lines  will be  in a  smaller  size font.  The welcome
          message  for registered sites can be changed later by sending the
          new message along with $20.00 cash, check, or Purchase Order. The
          necessary modified files will be shipped promptly.
             Do not complete this area  if you are a single copy  purchaser
          of ETCAI. Single user copies are branded to the users name.

          line(1)__________________________________________________

          line(2)__________________________________________________

          line(3)__________________________________________________

          line(4)__________________________________________________

          line(5)__________________________________________________