S P L O T  -  The Pen Plotter Simulator V2.52
	       ---------------------------------------------
		   Copyright (C) 1989-94 by Alexandr NOVY
			     All rights reserved.



	  U S E R ' S   M A N U A L   F O R   MS-DOS   V E R S I O N
	  ----------------------------------------------------------
				  July 1994




                1. INTRODUCTION
                ---------------

          The SPLOT program is  a highly effective tool  intended for
        simulating the pen plotter on the display of an IBM PC.   The
        SPLOT program is  the very thing  you need to  make your work
        with the plotter more effective. The SPLOT program will  give
        you a guarantee you will always draw on your plotter what you
        really want. That is why it will save your nerves, your time,
        your plotter, pens and paper, that means your money.


         The SPLOT program can offer:

         - active support of about 50 HP-GL instructions (according
	   to the type of your plotter).

         - active support of 20 DXY-GL instructions (for ROLAND
           plotters).

         - possibility of exporting a  picture to the printer and  in
           this way to obtain an output of a high quality. The  SPLOT
           program uses the  best graphics resolutions  available for
           each printer  that it  supports and  optionally uses  data
           packing to improve transfer speed.  In this way the  SPLOT
           program will  make a  fast and  excellent plotter  of your
           printer. It supports all usual types of printers including
           color ones.

         - exporting  a  picture  to  the  HP-GL,  HP-GL/2,  DXY-GL,
	   PLOTCALL,  DXF  and  PostScript  formats.

         - possibility of making picture cuts (the ZOOM function). In
           this way you can scan,  draw on the plotter or  print only
           the selected part of the picture.

         - possibility  of  completing  the  picture  with  a    text
           including multilingual characters - in this way the  SPLOT
           program will teach  your plotter German  (Spanish, French,
           etc.)  easily  and  quickly  without complicated switching
	   between  character  sets!   The  built-in  HP-GL or DXY-GL
           exports respectively, will make it possible. Due to  these
           exports it is also possible:

           -  to  offer  a  highly  optimized output for your plotter
             (where each pen is grasped only once).

           - to  teach  your  plotter  the advanced instructions  you
             would get only  if you buy  a more expensive  plotter or
             additional  hardware  (e.g.,   the  SPLOT  program   can
             simulate  connecting  an  additional  HP 17440A graphics
             enhancement cartridge to the HP 7440A ColorPro plotter).


        The SPLOT program can be used by:

        - anybody who wants to work with his plotter in the WYSIWYG
          style (What You See Is What You Get).

        - anybody  who  wants  to  develop  his  own plotter  program
          applications.   You  can  reach  it  with the SPLOT program
          easily even if you do not own the plotter at all!

        - anybody  who  wants  to  use  his  printer  as  a   plotter
          occasionally or constantly. In  many cases using a  printer
          may be faster and moreover, this may be an alternative of a
          high quality.

        - anybody who wants to program a printer in graphics mode and
          at  a  high  level  and  who  does  not  want  to   develop
          complicated software which would enable it. In these  cases
          using  the  HP-GL  language  in  connection  with the SPLOT
          program  seems  to  be  very  advantageous for creating own
          graphics outputs. The HP-GL  language can  be learned  very
          easily and in addition, it offers unexpected possibilities.



          The  SPLOT  program  is   available  in  various   versions
        according to  the type of simulated plotter. This  means that
        each SPLOT.EXE  module is  designated for  a certain  plotter
        type.   This  principle  gives  the  maximum  reliability  of
        simulation of the given plotter type. At present versions for
        the following plotter types are at your disposal:

           Plotter type                          | Plotter syntax
         ------------------------------------------------------------
	   HP 7470A                              | HP-GL
	   HP 7475A                              | HP-GL
	   HP 7440A ColorPro                     | HP-GL
	   HP 7550A                              | HP-GL
	   HP 7570A/7575A/7576A DraftPro DXL/EXL | HP-GL
	   HP 7595A/7596A DraftMaster I/II       | HP-GL
	   ROLAND DXY 1100/1200/1300             | DXY-GL / RD-GL I
	   ROLAND GRX 300/400                    | RD-GL II

	  An UNREGISTERED COPY  of the program  is available only  in
        the version for the HP 7475A plotter. The versions for  other
        plotter types can  be received only  on the basis  of regular
        registration. See next chapter  for licensing, evaluation and
        registration information or see file LICENCE.DOC for details.

          The  SPLOT  program  is  designated  for  using with IBM PC
        computers  and  compatibles,  and  for  the MS-DOS and PC-DOS
	version  3.00  and  higher  ones ( the MS-WINDOWS version  is
	available too ).  In the  DOS version  graphics  cards EGA or
	VGA  are  required.  To  run  the  program  comfortably it is
	recommended to use a Microsoft Mouse or a compatible one.



                2. LICENSING, EVALUATION and REGISTRATION INFORMATION
                -----------------------------------------------------

        SPLOT  is  distributed  as  "Shareware"  or  "User  Supported
        Software"  and  is  fully  copyrighted.  If  you register the
        program you will receive these benefits:

          1) The latest version of SPLOT.
          2) A printed user's manual.
          3) A printed technical reference which describes
             all plotter instructions supported by SPLOT.
          4) An end to the nag screens and opening banners.
          5) Deep discounts on the next major versions.
          6) A collection of useful utilities:
             - BPRINT.COM - prints binary files on a printer
                            on time background with many options.
             - BPLOT.COM  - plots files on a pen plotter on time
                            background with many options.
             - CLPT.COM - redirects printer ports to a disk file.
             - CPORT.COM - redirects serial ports to a disk file.


        The  single  user  registration  fee  for SPLOT is $70.00 US.
        The multisystem site fee for SPLOT is $150.00. Users  outside
        of   Europe   should   include   an   additional   $5.00  for
        international airmail.

	Author can accept payment in these three ways:

	 1) In cash (money enclosed) - this is the most quick method,
	    but at your risk.

	 2) Credit card  -  MasterCard, VISA and American Express are
	    accepted.  Please,  fill out  carefully  the  credit card
	    information in order form.

	 3) Bank or travelers cheque enclosed - please make  a cheque
	    payable in US funds.

	 4)  Author can send to you first an invoice with an  account
	    number.  Then you will receive the SPLOT program as  soon
	    as your payment will be done to this account number.

	Since the SPLOT program is always distributed in the  version
	adapted for a certain plotter type, do not forget to  mention
	the  plotter  type  with  which  you  want  to  use the SPLOT
	program.  A list of plotters you can choose from is given  in
	the  first  chapter  or  in  the  PLOTTERS.DOC  file.  In the
	PLOTTERS.DOC  file  there  are  also  given the parameters of
	these   plotters   together   with   a   list   of  supported
	instructions. It makes possible to choose a suitable  plotter
	type even if  your plotter is  not listed (most  plotters are
	compatible with some plotter from the list).  Of course,  you
	can order more SPLOT  program versions for different  plotter
	types.  In this case the single user registration fee for any
	further version is  $20.00 (+ $5.00  outside Europe) and  the
	multisystem site fee is $40.00 (+ $5.00 outside Europe). This
	principle  is  also  valid  for  an  upgrade.   If  you  have
	registered at  least one  SPLOT program  version at  the full
	price of $70.00 ($150.00), now and in the future only  $20.00
	($40.00) is to be paid for all other versions.

	Special offer:
	Registered  users  of  the  MS-Windows  version  of the SPLOT
	program  can  order  the  MS-DOS  version  for  $50.00   only
	( $100.00 for the multisystem site licence ) (+ $5.00 outside
	Europe). In this  case fill out  your serial number  in order
	form and mark  it as `upgrade  from Windows version'.
	Note:  The latest MS-Windows version of the SPLOT program  is
	available  on  all  SIMTEL20  archives  in   <MSDOS.WINDOWS3>
	directory as SPLTXXXW.ZIP file (recently SPLT221W.ZIP).


        To register, please use the registration/order form  supplied
	with this package (as provided in the file ORDER.FRM).
	Please send the completed form along with a payment to:

            Alexandr Novy
            Havlickova 2209
            390 01 TABOR
            Czech Republic

        NOTE: Czech users of SPLOT should contact Czech distributor

	      PESKA & BRTNA Computer Service
	      Krakovska 2805
	      390 05 Tabor
	      Czech Republic
	      Tel./Fax 0042-361-42138

              or

              SOFTECH
	      P.O.B. 69
	      323 00 Plzen 23
              Czech Republic
              Tel./Fax  0042-19-226294

              A special Czech language version of the package is
	      available from them as well.


                       EVALUATION AGREEMENT

        SPLOT  is not  and  has never been  public  domain  software,
        nor is it free software.

        Non-licensed users are granted a limited license to use SPLOT
        on  a  14-day  trial  basis  for  the  purpose of determining
        whether SPLOT is suitable for their needs.  The use of SPLOT,
        except for the initial 14-day trial,  requires  registration.
        The use of unlicensed copies of SPLOT by any person,business,
        corporation or any other entity is strictly prohibited.

        No one may modify or  patch the SPLOT executable file  in any
        way, including but not limited to decompiling, disassembling,
        or otherwise reverse engineering the program.

        A limited  license is  granted to  copy and  distribute SPLOT
        only  for  the  trial  use  of  others,  subject to the above
        limitations, and also the following:

        1) SPLOT must be  copied in unmodified form,  complete
           with the file containing this license information.

        2) The full machine-readable SPLOT documentation  must
           be included with each copy.

        3) SPLOT  may not  be distributed  in conjunction with
           any other product without a specific license to  do
           so from author.

        4) No  fee,  charge,  or  other  compensation  may  be
           requested or accepted, except as authorized below:

           a) Operators of  electronic bulletin board  systems
              (sysops)   may   make   SPLOT   available    for
              downloading as long as the above conditions  are
              met.   An overall  or time-dependent  charge for
              the  use  of  the   bulletin  board  system   is
              permitted as  long as  there is  not a  specific
              charge for the download of SPLOT.

           b) Vendors of user-supported or shareware  software
              may  distribute  SPLOT  after  obtaining written
              permission  from  author.  Such  permission   is
              usually granted. Vendors may charge a reasonable
              disk duplication and handling fee.



                       LICENSING AGREEMENT

        Licensed user are bound to the following licensing agreement.

        You may not transfer your license without written  permission
        from author.  A single  user license  permits a  user to  use
        SPLOT only on a single computer at a time.

        This product is distributed  AS IS.  The  author specifically
        disclaims all  warranties, expressed  or implied,  including,
        but not limited to, implied warranties of merchantability and
        fitness for a particular  purpose with respect to  defects in
        the diskette and  documentation, and program  license granted
        herein,  in  particular,  without  limiting  operation of the
        program license with  respect to any  use or purpose.   In no
        event shall the author  be  liable for any loss of  profit or
        damage  including  but  not  limited  to special, incidental,
        consequential or other damages.

        By licensing SPLOT you agree to the above licensing agreement.



                3. THE SPLOT WORKING PRINCIPLES
                -------------------------------

          The plotter  simulation consists  in  interpreting  plotter
        instructions contained  in a  disk file.   The SPLOT  program
        reads these instructions from the file and plots them on  the
        screen of the computer in  the same way as the  plotter would
        do  on  paper.  The  file  is  plotted  in  the  window which
        represents the plotting paper of the plotter.  The boundaries
        of this window normally correspond to the hard clip limits of
        the plotter (i. e., to the physical limits in which a plotter
        pen  can  move  for  the  selected  paper  size). If the ZOOM
        function is used,  the chosen plotting  area is displayed  in
        this window.



                4. WORKING WITH THE PROGRAM
                ---------------------------

          The SPLOT program can be  operated using the keyboard or  a
        mouse. From the keyboard the program is operated by  pressing
        the keys the list of which is given in chapters 4.2 and  4.3.
        If you have a mouse installed, its cursor will appear on  the
        screen.  The shape of the cursor is a cross which appears  in
        the plotting  area (paper)  (see chapter  4.1), outside  this
        area it is a rectangle of  one letter size.  The function  of
	this cursor is to choose, activate and change items displayed
        visually. You can make a  choice by moving the cursor  on the
        selected item  and by  pressing any  button of  the mouse. At
        this moment a  tick off character  appears on the  cursor and
        only after releasing the pressed button the action associated
	with the selected item is  realized. If you choose from  more
        items in the menu (e.g., choosing a file to be plotted),  you
        have to make a double  click since the first pressing  serves
        to highlighting an item.

          The program can perform plotting the chosen file on one  of
        two pages, they are called "a small view" and "a large  view"
        here.

          A small view is used for setting the chosen parameters  and
        selecting  the  file  to  be  plotted.  The  file can be also
        plotted in a small area.

          The choice of the file to be plotted can be made either  by
        entering its name  or by choosing  it from the  menu. In this
        menu there are all the files of the given directory with  the
        extension  .PLT  displayed  and   there  are  also  all   the
        subdirectories the contents of which can be displayed  simply
        by choosing a subdirectory from the menu. Any file group  can
        be displayed also  by means of  the wildcards *  and ? (e.g.,
        '*.*' will display all the files in the given directory).  As
        soon as the file to be plotted is chosen, its plotting starts
        on  the  page that is set up  by the F1 key (A SMALL VIEW  or
        A LARGE VIEW).

          Plotting the file can be  stopped by pressing the keys  F1,
        Esc, Ctrl-C or  Ctrl-Break at any  time. If the  plotting was
        performed in a large view, after finishing plotting you  will
        stay on the page of a large view.

          Returning from the large view page can be performed by  the
        F1 key.



		4.1 ZOOMING
                -----------

          With the cursor run by the mouse or the keyboard resp., you
	can make and enlarge the chosen cuts of the plotted area. The
        control of the cursor is realized by the mouse control or  by
        pressing the appropriate keyboard keys.

          There are two possible zoom modes named SLACK and EXACT.
          In the SLACK mode the aspect ratio of the displayed cut  is
        identical to the aspect  ratio of the original  plotting area
        regardless of the aspect ratio of the selected cut. To ensure
        proportional aspect ratio of  the displayed cut in  the SLACK
        mode the  size of  the displayed  cut area  is usually larger
        than the size of the selected cut area.
          In the EXACT mode the aspect ratio of the displayed cut  is
        exactly identical to  the aspect ratio  of the selected  cut.
        To ensure proportional aspect  ratio of the displayed  cut in
        the EXACT mode the screen plotting area is usually reduced.
          You can set the default zoom mode in the OPTIONS menu  (see
        chapter 6). However you  can apply the opposite  mode without
        this setting (see below).


	  The movement of  the cross cursor  in the plotting  area is
        realized by the mouse movement or by pressing the  Ctrl+arrow
        keys (or plain  arrow keys in  large view).   By pressing any
        mouse button or the Ins(ert) key when the cross cursor is  in
	the plotting area you define first corner of the zooming box.
        The next  mouse movement  or the  pressing of  the arrow  (or
	Ctrl+arrow) keys expands and contracts the zooming box around
        the area you desire to expand. If the Scroll Lock is switched
        on or  the Shift  key is  pressed, or  if you  press the left
        mouse button with the right mouse button simultaneously,  the
        box moves as a whole.  By pressing the right mouse  button or
	by pressing  the Enter  key you  can start  zooming. Starting
	zooming with the Ctrl key depressed selects the opposite zoom
        mode to  the default  (i.e., when  the default  zoom mode  is
	SLACK  (EXACT),  you  must  press  Ctrl+right mouse button or
	Ctrl+Enter key to perform zooming in EXACT (SLACK) mode). The
        left button or  the Esc key  or the Ins(ert)  key cancels the
        box cursor mode and  you get back to  the mode of the  simple
        movement of the cross cursor.

	  To expand the picture into the original size press the  Tab
        key or  press both  the mouse  buttons simultaneously  in the
        cross cursor mode.

          If you have a  three button mouse with  appropriate driver,
        pressing the  middle mouse  button is  equivalent to pressing
        the right and left buttons simultaneously.

          Note  that  in  the  small  view  the  Enter and arrow keys
        normally serve  for control  of the  file menu  and the  edit
	line. However in  the mode of  defining the zooming  box they
        serve for this operation.



                4.2  LIST OF KEYS IN "A SMALL VIEW"
                -----------------------------------

        F1 - It selects "A SMALL VIEW" or "A LARGE VIEW" for plotting
             the file.

        F2 - The choice of a disk.

        F3 - It replots the selected file in the given picture box.

        F4 - The choice of parameters. In the menu initiated by  this
             key it  is possible  to set  various program  parameters
             concerning  also  exporting  a  picture to the supported
             formats. See chapter 6 for more details.

        F5 - It changes the paper size according to the plotter  type
             and the selected paper norm.

        Alt_F5 -  It switches  among the  paper norms (ISO,ANSI,ARCH)
             defining the paper size according to the plotter type.

        Ctrl_F5, Alt_E - It switches  the EXPAND mode on and  off (on
             condition it is supported for the given plotter type).

	F6 - In the ROLAND plotter version it switches between  RD-GL
	     and   DXY-GL   command   mode   (Note: the  RD-GL syntax
             corresponds with the HP-GL syntax). In some versions  it
             makes  a  choice  of  the  plotter  type (e.g. in the HP
             DraftPro   version   it   switches   among   the   types
             7570A/7575A/7576A). In the version for HP 7440A ColorPro
             it switches on  or off the  simulation of the  HP 17440A
             graphics enhancement cartridge.

        Alt_F6,Alt_U - In the  ROLAND plotter version in  DXY-GL mode
             it changes the  plotter unit size  from 0.1 mm  to 0.025
             mm.  In RD-GL mode  or HP-GL mode the plotter  unit size
             is always 0.025 mm.

        Alt_F7, Alt_F - In the  ROLAND plotter version the choice  of
             an initial font (the font set up after switching on  the
             plotter or after its initialization).

        F7 - It switches on or off a multilingual TEXT filter in  the
             LB command of HP-GL mode (or in the P command of  DXY-GL
             mode  of  the  ROLAND  plotter).  See chapter 7 for more
	     detailed information.

        F8 - It activates  the export  of the  displayed part of  the
             HP-GL or DXY-GL  file to alternative  formats (including
             printing).  See chapter 5 for more details.

        F9 - It switches  on or  off the  tracing of  the  individual
             plotter commands during plotting  the file. It is  valid
             only  for  "A  LARGE  VIEW".  First  every  command   is
             executed,  then  it  is  displayed  in  the  information
             window.  The  next  command  is  executed after pressing
             Enter  or  F7.  In  this  mode  the  S key or the F8 key
             switches on  and off  automatic tracing.  The tracing is
	     disabled during printing or exporting.

        F10 - It stops  the program.  The program  can be stopped  by
             using the F10 key practically at any moment.

        Alt_1 - Alt_0 - The identification of pens. See chapter 9 for
             more details.

	Alt_P - The information about assigning colors to pens.

        Alt_S - It saves the  selected palette of colors assigned  to
             individual pens to be registered in the setup file.

        Alt_R - It restores the original palette unless the saving of
             the palette has been already done.

        Alt_I - The initialization of graphics mode (it can be  used,
             e.g., if the screen graphics mode is damaged -  possibly
             by a popup resident program).

        Alt_V -
        Alt_F10 - Video configuration. More details in chapter 8.



                4.3  LIST OF KEYS IN "A LARGE VIEW"
                -----------------------------------

	F3, F4, F8, F9, F10,
        Alt_F10, Alt_V
        Alt_P, Alt_S, Alt_R, Alt_I - See "A SMALL VIEW".

	F1 - The return to the page of "A SMALL VIEW".

	F2 - Opens a file selection dialog. Pressing F2 in this
	     dialog opens a drive selection dialog.

        1 - 0
        Alt_1 - Alt_0 - See the identification of pens (chapter 9).

        F5 - Inserting a text  into the picture and the  manipulation
             with it (see chapter 7 for more detailed information).

	Page_Up, Page_Dn - It switches between informative pages.  On
                 the  first  page  there  is  the  size  of a plotted
                 picture box expressed  in mm units.   On the  second
                 page there is the  position in the plotted  file and
                 the  position  of  the  cursor  in the plotting area
                 expressed in plotter units. On both the pages  there
                 are  the  most  important  parameters describing the
                 state of the plotter.



                5. EXPORT
                ---------

          The SPLOT program  enables to export  a plotted picture  to
        the following formats:

                - HP-GL
		- HP-GL/2
                - DXY-GL (ROLAND)
                - PLOTCALL
                - DXF (AutoCAD)
                - POSTSCRIPT (color)
                -----------------
                - IBM Graphics (IBM 9 pin printer)
                - IBM X24 (IBM 24 pin printer)
                - EPSON LX
                - EPSON EX/FX (color)
                - EPSON LQ (color)
		- NEC 24 pin (color)
                - HP LaserJet
                - HP DeskJet (color)
                - HP PaintJet (color)
                - HP QuietJet
                - HP ThinkJet (HP mode)

          The HP-GL format executes  the export of a  plotted picture
        to the HP-GL  plotter. It can  be employed, for  example, for
        plotting a picture  cut on the  plotter, for the  output of a
        multilingual text on the plotter (see chapter 7), or in  case
        your  plotter  does  not  support  all  the  HP-GL   commands
        supported  by   the  SPLOT   program.   The   last  case   is
        characteristic especially  of the  situation you  own the  HP
        ColorPro  7440A  plotter  and  you  have  not  the additional
        graphics enhancement cartridge HP 17440A.

          The HP-GL/2 format can be  used for exporting a picture  to
	any HP-GL/2 device. It may be a pen, ink-jet or electrostatic
	plotter as well as a printer of any type. The HP-GL/2 is  the
	standardized next generation  of the HP-GL  ( Hewlett-Packard
	Graphics Language ).

          The DXY-GL format realizes the  export of a picture to  the
        DXY plotter (usually the ROLAND plotter).

	  The PLOTCALL  format is  used in  the GoldenSoftware's PLOT
        program which  supports a  wide range  of peripheral  devices
        (printers, plotters).

          The DXF format converts a  picture to a form applicable  by
        the AutoCAD program. From AutoCAD you can read this DXF  file
        via the DXFIN command. The exported picture is written in the
        form  of  LINES  where  each  pen  of the plotter has its own
        LAYER. Pen  1 has  a layer  with the  name PEN1,  pen 2 has a
        layer with the name PEN2, etc.

          The PostScript format can be used by any peripheral  device
        which  has  implemented   PostScript  interpreter  (such   as
        PostScript printer).

          The function of the other formats is to export a picture to
        the corresponding peripheral devices - printers. The  (color)
        word  indicates  a  possibility  of  color  printing  for the
        appropriate format. Naturally, all formats can be used on all
        printers compatible with these ones.

          The picture  can be  exported either  to the  disk file  or
        directly to the corresponding peripheral device (a plotter, a
        printer).  If  your  peripheral  device  is  connected to the
        parallel interface, use PRN or LPT1 resp., LPT2, etc. as  the
        output file. If it is connected to the serial interface,  use
        COM1  or  COM2  respectively.  Set  the  parameters  of   the
        corresponding serial interface by  the DOS MODE command  with
        the parameter "p" beforehand, like this:

             MODE COM1:9600,,,,p

	  If  you  export  a  picture  to  a disk file, which is less
	time-consuming, you can use  the enclosed  programs BPLOT  or
	BPRINT resp.,  for exporting  this file  to the corresponding
	peripheral device  (in the  registered version  only).  These
	programs  perform  exporting  files  to  the chosen serial or
	parallel interface, on the time background.  Please,  realize
	that it  is not  possible to  use the  DOS PRINT  command for
	exporting binary files  (the files containing  graphics data)
	to the printer.

	  The export of the picture is started with the F8 key. In the
	EXPORT menu you can specify:
	   - an exporting format,
	   - the size of the resultant picture,
	   - resolution (the size of a plotter unit) - in the case of
	     the DXY-GL export only,
	   - print density - if exporting to the printer,
	   - the output file name.

	  You can choose from the following export sizes:
	   - ZOOM size,
	   - ORIGINAL size,
	   - A3, A4 or A5 size,
	   - USER size.

	  The ZOOM size is offered only if a zoom cut is exported. It
	is exactly identical  to the original  size of the  displayed
	cut (1:1 scaling). When  the HP-GL, HP-GL/2 or  DXY-GL export
	is performed it is possible to keep the original position  of
	the  selected  cut  (note  that  the optional left and bottom
	margins are added to this  position too - for specifying  the
	left and  bottom margins  see chapter  6).   This way you can
	make an HP-GL, HP-GL/2 or DXY-GL picture which contains  more
	selected cuts positioned as on original picture.

	  The ORIGINAL size is the whole size of the selected plotter
	paper size (as defined by the F5, Alt_F5 or Ctrl_F5 keys). If
	you use  this size  for exporting  the original  (non-zoomed)
	image, you ensure the 1:1 scale for that export.

	  The A3, A4 and A5 sizes are the predefined sizes.

          To  ensure  proportional  aspect  ratio  of  the  resultant
        picture for ORIGINAL, A3, A4 and A5 sizes, only the one  side
        from  selected  size  is  used.  This  determinant  side   is
        displayed in bright color. The other side is counted so  that
        the resultant picture would be proportional.  By default  the
        choice  of  the  determinant  side  is  performed so that the
        resultant size  lies entirely  within the  selected size. You
        can override this by selecting the other determinant side. To
        do this click  on the non-bright  side item or  press the Tab
        key.

	  The USER size serves for setting of the user defined  size.
	If you set your  own size of the  output format, you have  to
	give  only  the  size  of  the  one  side , the other side is
	counted automatically so that the resultant picture would  be
	proportional. Use the Tab key  or mouse control to switch  to
	the editing of the desired side.

	  The size is  given in cm  units or inch  units according to
	the choice  from the  OPTIONS menu  (see chapter  6). The DXF
	format is an exception -  here the output size is  understood
	in units to be defined in AutoCAD.

	  The  chosen  size  corresponds  with  the  real size of the
	resultant picture realized by  exporting. It is necessary  to
	consider it as the maximum  limits into which a picture  seen
	in   the   program   plotting   area   can   be   transformed
	proportionally. Therefore, for example, if you choose A4 size
	paper  as  the  output  size  for  printing and if you have a
        printer  of  the  same  size,  you  will reach a satisfactory
        result only if you choose the LANDSCAPE orientation. For  the
        PORTRAIT orientation it is necessary to choose the maximum A5
        size for the  output so that  the resultant picture  could be
        positioned on A4 size paper.

          The other parameters influencing the look of the  resultant
        picture  can  be  set  in  the  menu activated by F4 key (see
        chapter 6).



		6. OPTIONS
		----------

	With the menu activated by the F4 key it is possible to set:

	1. DEFAULT EXTENSIONS - this item sets default extensions
		 of the following file types:
	   1.1 PLOT FILES - the files given in the menu of files from
		 which  the  files  for  plotting  are  selected. For
		 example, if this extension is PLT, the displaying of
		 all  the  files  with  the  PLT  extension  will  be
		 standard. If this extension is *, the displaying  of
		 all the files will be standard.
	   1.2 HP-GL EXPORT -
	   1.3 HP-GL/2 EXPORT -
	   1.4 DXY-GL EXPORT -
	   1.5 PLOTCALL EXPORT -
	   1.6 DXF EXPORT  -
	   1.7 POSTSCRIPT EXPORT -  sets standard  extensions  of the
		 output files according to  the  type of  export. The
                 name of the output file is composed of the base part
		 derived  from  the name of  the exported file + this
                 standard extension.  However, the  file name  of the
                 output file can be  changed before the beginning  of
		 any export.
           1.8 PRINT - sets  standard extensions of the  output files
                 during  exporting  a  picture  designated  for   the
                 printer.
	   1.9 TEXT - sets the standard extension of the output  file
		 determined for storing texts on the disk.

        2. SORT ORDER FOR FILES - the choice of order in which  files
                 are displayed. The sorting can be done by the  NAME,
                 EXTENSION or SIZE.

	3. BACKGROUND - switches between NORMAL  and BRIGHT intensity
		 of background white color  of plotting area  (paper)
		 (in color modes only).

	4. VIDEO SETUP - more detailed information in chapter 8.

	5. SOUND - switches on and off sound signals.

	6. DEFAULT ZOOM - sets the default zoom mode as SLACK or
		EXACT (see chapter 4.1 for details).

	7. PEN WIDTHS  -   this  menu  item  enables  you  to  manage
		a variable  pen widths feature  provided by the SPLOT
		program:
	  7.1 SET PEN WIDTHS -  It  determines  the line  width   for
		individual  pens.  By  default  the  line  width   is
		determined  by  the  PT  (pen thickness) instruction.
		The   line   width   is   controlled   by  the  HP-GL
		instructions and   will  vary   according  to   value
		issued  in  PT  instruction.  However note that  each
		SP (select pen) instruction  resets  the  PT  to  its
		default  value (mostly 0.3 mm).
		The other way is to set the line width to fixed  user
		defined value.  Unlike the  other measurement  values
		the line width is expressed in millimeters (mm).
	  7.2 USE ON SCREEN - Check  this  option if you want  to use
		variable pen widths for screen drawing.
	  7.3 USE ON PRINTER - Check  this option if you want to  use
		variable pen widths for printing and for HP-GL/2  and
		PostScript exporting (the variable pen widths are not
		supported  for  HP-GL,  DXY-GL,  PLOTCALL and AutoCAD
		exports).
	  7.4 ON PRINTER -  Select here  a mode  for use  of the  pen
	        widths when printing or exporting. It can be:
		Absolute  -  a  real  printed  line  width  will   be
			   absolutely  equal  to  the  specified  pen
			   width.
		Relative - a real printed line width will be computed
			   from the specified pen width relatively to
			   the  original  plotter  page  size (or its
			   printed cut).
		Only  checking  of  the  relative  mode  can   ensure
		printing in  the WYSIWYG  style. However  by checking
		the absolute mode  along with PT  width type for  all
		pens you get a native plotter simulation.
		Note  that  on  screen  the  pen  widths  are  always
		displayed in relative mode.
	  7.5 ZOOM PEN WIDTHS  -  Check  this option  if you  want to
		enlarge the pen widths  along with enlarging an image
		cut (see the ZOOMING section).


	8. TEMPORARY  PATH -  this menu  item sets  the directory  in
	       which  the  SPLOT  program  will  create its auxiliary
	       files  in  some  types  of  picture  exporting. If the
	       picture   exporting   stops   with  an  error  message
	       "DISK FULL", it means,  that there  is not  sufficient
	       disk space for the  created output or auxiliary  file.
	       In the latter  case you can  try to set  the temporary
	       directory to another disk.  You can choose from  three
	       possibilities:
	   8.1 The directory defined by the environment variable  TMP
	       by means of the DOS SET command (e.g., SET TMP=D:\).
	   8.2 The directory defined by the environment variable TEMP.
	   8.3 A current work directory i.e., the directory given  on
	       the  information  board  of  the  program  in "a small
	       view".

	9. USED UNITS  - it defines  units used for  setting the size
		and distances during picture exporting. The units may
		be given in cm (centimeters) or inch (inches).

	A. EDIT USER COLORS - sets the RGB values of the user colors.
		They can be used in the PEN --> COLOR assignments for
		PostScript and  HP-GL/2 exports.  The RGB  values are
		expressed in percents.

	B. Parameters for the HP-GL EXPORT :
	  B.1 PEN --> PEN - by  means of this item it is  possible to
		assign each  pen on  the input  a pen  on the output.
		Thus  it  is  possible,  for  example, to convert the
		picture that uses more pens to a single colored  one,
		or it is  possible to exclude  using some pen (if you
		assign PEN 0 as the output pen to it).
	  B.2 PEN OPTIMIZATION - if ON, the number of the grasping of
		pens when the picture is exported will be  optimized.
		This means that when the resultant  picture is  being
		drawn, each pen is grasped only once.
	  B.3 PEN ORDER - specifies the sequence of pens according to
		which the optimized picture will be drawn.
	  B.4 OUTPUT FORMAT can be like this:
	      * NORMAL - every HP-GL  command is given on a  separate
			 line and it is ended with a character ";".
	      * PACKED - all the HP-GL  commands follow closely   one
			 after  another  without  any separators. The
			 number of uses of PU and PD instructions  is
			 minimized.
	  B.5 ORIGIN IN CENTER - Activate this parameter only if  the
		resultant HP-GL file is designated for the plotter in
		which the origin of the coordinate system is situated
		in the center of the plotting area (it is usual  with
		large paper size  plotters,  e.g. HP  DraftPro or  HP
		DraftMaster).
	  B.6 LEFT MARGIN -  specifies   the offset of  the  exported
		picture from the left margin - it is on the X axis  -
		it can also be a negative number.
	  B.7 BOTTOM MARGIN - specifies the  offset of the   exported
		picture from the bottom margin - it is on the Y  axis
		- it can also be a negative number.
	  B.8 90 DEGREES ROTATION - It determines  the orientation of
		an  exported  picture.  The 90  degrees  rotation  is
		forced by the RO90 instruction.
	  B.9 PG AT END - specifies if the PG (Page Feed) instruction
		will be attached to the end of the output file.

	C. Parameters for the HP-GL/2 EXPORT :
	  C.1 DEVICE TYPE - select here to which HP-GL/2 device type
		you will export. It can be:
		 * PEN PLOTTER
		 * MONOCHROME (B&W) RASTER DEVICE (e.g. electrostatic
		   plotter, laser printer etc.)
		 * COLOR RASTER DEVICE (e.g. color ink-jet plotter or
		   printer etc.)
	  C.2 DUAL CONTEXT DEVICE - for raster devices it  determines
		if  the  device  supports  along  with  HP-GL/2   the
		Hewlett-Packard's  printer  command  language  (PCL).
		Check  your  printer/plotter  documentation  to   see
		whether or not your device supports this extension.
	  C.3 PEN --> PEN - see the HP-GL export.
	        Valid for PEN PLOTTER device type only.
	  C.3 PEN --> COLOR  -  It  assigns   the  output  colors  to
		individual pens for the RASTER COLOR device type.
	  C.3 PEN --> SHADE  -  It  assigns   the  output shades   to
		individual pens for the RASTER B&W device type.
		The shades are expressed in percents. The value of 0%
		represents black pen, the  value of 100%   represents
		white pen  and other  values represent  corresponding
		gray levels.
	  C.4 PEN OPTIMIZATION - see the HP-GL export.
	        Valid for PEN PLOTTER device type only.
	  C.5 PEN ORDER - see the HP-GL export.
	        Valid for PEN PLOTTER device type only.
	  C.6 OUTPUT FORMAT - see the HP-GL export.
	  C.7 LEFT MARGIN - see the HP-GL export.
	  C.8 BOTTOM MARGIN - see the HP-GL export.
	  C.9 90 DEGREES ROTATION - see the HP-GL export.
	  C.A USE PS INSTRUCTION - switches  on or off  using of  the
	        PS (plot size) instruction in  the  HP-GL/2   output.
		Allowing  the  use  of  PS  instruction is especially
		useful  with  plotters  drawing  on rollfeed media to
		avoid paper waste  when  drawing  a  small size plot.
		However using PS instruction on a dual context device
		can scale the resultant picture by the picture  frame
		scaling factor (that is the ratio of the PCL  picture
		frame size to the HP-GL/2 plot size).
	  C.B PLOT FRAME ADVANCE  - Set  this option  to VERTICAL  if
	  	your  plotter  frame  advance  is  parallel  with the
	  	longer side of paper.  Set this option to  HORIZONTAL
		if your  plotter frame  advance is  parallel with the
	  	shorter side of paper.
	  C.C ENABLE CUTTER -  enables   or  disables  the  automatic
	        cutter  function  of  your  HP-GL/2  plotter.  If the
		cutter is enabled,  cutting is done  after exporting.
		Note:  Not  all  devices  have  an  automatic cutter.
	  	Rollfeed devices that do not have a cutter may draw a
		line where the paper should be cut.
	  C.D MEDIA TYPE - selects  the type of media loaded  in your
	  	HP-GL/2 device. Your device uses this information  to
		change  resolution,  drop  volume,  alter  plot/print
		speed,   change   from   bidirectional   printing  to
		unidirectional  printing   etc.  according   to   its
		plotting  or  printing   technology,  quality   level
		setting, internal knowledge of  the pen type and  any
		control-panel setups.
	  C.E QUALITY LEVEL -  specifies the  quality level  of  your
		output from 0 (draft quality) to 100 (presentation or
		final quality).  On raster  devices  it  can optimize
		a toner usage  when final  quality  is not necessary.
		For a pen plotter, quality level is primarily a speed
	  	control. The pen speed  set by the plotter's  control
	  	panel  is  the  maximum  speed  which  corresponds to
	   	quality level of 0. If the pen speed is not set,  the
	  	plotter  determines  the  maximum  speed based on its
		knowledge of media type  and pen type. Minimum  speed
		(corresponding to quality  level of 100)  is linearly
		interpolated between the media and pen types.
		Note: The default quality level in the SPLOT  program
		is 0  (maximum speed)  for pen  plotters and  100 for
		raster devices.

	D. Parameters for the DXY-GL EXPORT:
	  D.1 PEN --> PEN - see the HP-GL export.
	  D.2 PEN OPTIMIZATION - see the HP-GL export.
	  D.3 PEN ORDER - see the HP-GL export.
	  D.4 OUTPUT FORMAT can be like this:
	       * NORMAL - every DXY-GL command is given on a separate
			  line.
	       * PACKED - all the DXY-GL commands follow closely  one
			  after another  without any  separators. The
			  number of uses of  M and D instructions  is
			  minimized.
	  D.5 ORIGIN IN CENTER - activate this parameter only if  the
		resultant DXY-GL file  is designated for  the plotter
		whose origin of the  originate system is situated  in
		the center of the plotting area.
	  D.6 LEFT MARGIN - see the HP-GL export.
	  D.7 BOTTOM MARGIN - see the HP-GL export.

	E. Parameters for the PLOTCALL EXPORT:
	  E.1 NUMBER OF DECIMAL DIGITS - It determines the number  of
		figures  written  after  the  decimal  point  at  the
		numbers on the output.
	  E.2 PEN --> PEN  - see the HP-GL export.
	  E.3 LEFT MARGIN - see the HP-GL export.
	  E.4 BOTTOM MARGIN - see the HP-GL export.

	F. Parameters for the DXF EXPORT:
	  F.1 NUMBER OF DECIMAL DIGITS - see the PLOTCALL export.
	  F.2 PEN --> PEN  - see the HP-GL export.
	  F.3 LEFT MARGIN - see the HP-GL export.
	  F.4 BOTTOM MARGIN - see the HP-GL export.

	G. Parameters for the POSTSCRIPT EXPORT:
	  G.1 PEN --> COLOR  -  It  assigns   the  output  colors  to
		individual pens for the color PostScript export.
	  G.2 PEN --> SHADE  -  It  assigns   the  output  shades  to
		individual  pens  for  the  black & white  PostScript
		export. The  shades are  expressed in  percents.  The
		value of  0% represents black pen,  the value of 100%
		represents  white  pen  and  other  values  represent
		corresponding gray levels.
	  G.3 LEFT MARGIN - specifies   the offset of  the   exported
		picture from the left margin - it is on the X axis  -
		it can also be a negative number.
	  G.4 BOTTOM/TOP MARGIN  -   specifies  the   offset  of  the
		exported picture from the bottom margin (when the  90
		degrees  rotation  is  suppressed)  or  from  the top
		margin (when the 90  degrees rotation is demanded)  -
		it is  on the  Y   axis -  it can  also be a negative
		number.
	  G.5 90 DEGREES ROTATION - It determines the orientation of
		an exported picture.


	H. ALL PRINTERS - It sets   up various  parameters valid  for
		printing on all kinds of printers:
	  H.1 ORIENTATION -   It  determines  the  orientation  of  a
		printed  picture on the paper.  It may be either  the
		LANDSCAPE orientation (breadthwise)  or  the PORTRAIT
		orientation (heightwise).
	  H.2 FRAME - It  determines if  a printed  picture is  to be
		situated in the frame limiting the plotted area.
	  H.3 PEN FOR A FRAME - It determines  the number of the  pen
		with which the frame  will be drawn. Its  function is
		important for color printers, where the color of  the
		frame is determined by assigning PEN --> COLOR.   The
		frame is drawn always with a thin line regardless  of
		the current pen widths settings.
	  H.4 PAGE BREAK AT END - specifies  if the page break  (form
		feed) command  will be  attached  to the end  of  the
		output file.
	  H.5 LEFT MARGIN - specifies the distance from the left stop
		of  the  printhead  to  the  start  printing position
		independently of the orientation.
	  H.6 TOP MARGIN - specifies the size of shift of the printer
		platen before starting printing independently of  the
		orientation.
	     The  LEFT MARGIN  and  TOP MARGIN  parameters  enable to
	     place the printed picture in any place on the paper.  At
	     laser printers which have neither printheads nor platens
	     in a classic  sense of word,  the terms LEFT  MARGIN and
	     TOP MARGIN always  relate to the  paper oriented in  the
	     vertical   position   independently   of   the   picture
	     orientation on the paper.

	I.  DOT MATRIX PRINTERS -  In  this  item it is  possible  to
		increase the  number of  the printhead  passes during
		printing.  It can be used for emphasizing printing or
		when the ribbon is written up.

	J. Parameters for IBM X24 - it sets parameters for the IBM
	      24 pin printers:
	  J.1 OUTPUT FORMAT can be like this:
	       * NORMAL - without use of relative shift instructions.
	       * PACKED - the instructions for the relative shift  of
			  the  printhead  are  used  for reducing the
			  output  code  size.
	  J.2 PANASONIC X24 - switches on and off Panasonic X24  mode
		 in which is used a different format for selecting  a
		 base line feed unit. This format is not strictly IBM
		 compatible and should be used with Panasonic 24  pin
		 printers in X24 mode.

	K. Parameters for EPSON - it sets parameters for the EPSON
	      printers:
	  K.1 OUTPUT FORMAT can be like this:
	       * NORMAL - without use of relative shift instructions.
	       * PACKED - the instructions for the relative shift  of
			  the  printhead  are  used  for reducing the
			  output  code  size  (not  used for EPSON LX
			  printers), but on  some older types  it may
			  cause substantial reducing print rate.
	  K.2 PEN --> COLOR  - It   assigns   the  output  color   to
		individual pens  on the  color printers  of the EPSON
		EX/LQ type. It is possible to choose from a fixed set
		of 7 colors.

	L. Parameters for NEC 24 - it sets parameters for the NEC 24
	      pin printers:
	  L.1 OUTPUT FORMAT can be like this:
	       * NORMAL - without use of relative shift instructions.
	       * PACKED - the instructions for the relative shift  of
			  the  printhead  are  used  for reducing the
			  output  code  size.
	  L.2 PEN --> COLOR  - It   assigns   the  output  color   to
		individual pens on the NEC 24 pin color printers.  It
		is possible to choose from a fixed set of 8 colors.

	M. Parameters for HP LaserJet - it sets parameters for the HP
		LaserJet printers:
	  M.1 OUTPUT FORMAT can be like this:
	       * NORMAL - no special coding used.
	       * PACKED - special  coding   is used for  reducing the
			  output code size. This coding is NOT a
			  standard feature of the HP LaserJet and
			  compatible printers and you must be sure
			  that your laser printer supports this (it
			  must support ESC*b1M instruction - I have
			  tested this on the HP LaserJet IIIp model).

	N. Parameters for HP DeskJet - it sets parameters for  the HP
		DeskJet printers:
	  N.1 OUTPUT FORMAT can be like this:
	       * NORMAL - no special coding used.
	       * PACKED - special  coding   is used for  reducing the
			  output code size. This coding is a standard
			  feature of the HP DeskJet printers.
	  N.2 PEN --> COLOR -  It  assigns   the   output   color  to
		individual pens for color printing on the  HP DeskJet
		printer. It is possible to choose from a fixed set of
		7 colors.

	O. Parameters for HP PaintJet - it sets parameters for the HP
		PaintJet printers (but not for XL300 model):
	  O.1 OUTPUT FORMAT can be like this:
	       * NORMAL - no special coding used.
	       * PACKED - special  coding   is used for  reducing the
			  output code size. This coding is a standard
			  feature of the HP PaintJet printers.
	  O.2 PEN --> COLOR -  It  assigns   the   output   color  to
		individual pens for color printing on the HP PaintJet
		printer.  It  is  possible  to  choose  from  a fixed
		(standard) or variable (extended) set of colors. Both
		color sets have 7 colors.  The extended color set can
		be redefined by user from offer of 17 colors.
	  O.3 COLOR SET  -   switches  between standard and  extended
		color  set.  The  selected  color  set  is  used  for
		defining assignment PEN --> COLOR.
	  O.4 EXTENDED COLOR SET - It is used  for setting individual
		colors in the  extended color set.   If the  extended
		color set is  selected as used  color set, then  if a
		color  in  this  set  is  changed,  the corresponding
		assignment  PEN --> COLOR  is changed  automatically.
	  O.5 MEDIA TYPE -  It selects  output media type -  paper or
		foil.

	P. Parameters for HP PaintJet XL300 - it sets parameters for
		the HP PaintJet XL300 printer:
	  P.1 OUTPUT FORMAT can be like this:
	       * NORMAL - no special coding used.
	       * PACKED - special  coding   is used for  reducing the
			  output code size. This coding is a standard
			  feature of the HP PaintJet XL300 printer.
	  P.2 PEN --> COLOR -  It  assigns   the   output   color  to
		individual pens for color printing on the HP PaintJet
		XL300 printer.  It is possible to choose from a fixed
		set of 7 colors.


	Q. TEXT FILTER  - It switches on or off  a multilingual  TEXT
		filter in the LB command  of HP-GL mode (or in  the P
		command of  DXY-GL mode  of the  ROLAND plotter). See
		chapter 7 for more detailed information.

	R. CODE PAGE SELECTION  -  It  sets a  code page  for a  text
		filter (see chapter 7).  The code page can  look like
		this:
		- United States
		- German
		- Multilingual
		- Portugal
		- Canada - French
		- Norway



		7. INSERTING TEXTS INTO PICTURES
		--------------------------------

	  The SPLOT program is able to process a multilingual text in
	your HP-GL (or DXY-GL) files. As known, plotters receive only
	the ASCII characters in the range of 0 to 127.  Therefore, if
	the instruction for the output of the text (LB at HP-GL and P
	at DXY-GL resp.) contains the ASCII characters with the value
	higher  than  127,  the  plotter  will  not draw them or will
	ignore  the  highest  bit  of  characters  and  will draw the
	corresponding characters  from the  lower half  of the  ASCII
	table.  For  example, if you  use the following  statement in
	GW-BASIC (handle #1 represents the plotter),

	    PRINT #1, "LBGr”áe";CHR$(3)

	the plotter will draw only the text

	    Gre  or  Grae  respectively.

        If you want to draw the  text correctly, you have to use  the
       following statements, e.g.:

            PRINT #1, "CS0;CA33;SS;LBGr";CHR$(3)
            PRINT #1, "SA;LB|~";CHR$(3)
            PRINT #1, "SS;LBe;CHR$(3)

        However,  e.g.,  if  you  own  the  HP ColorPro 7440A plotter
        without an  additional HP  17440A graphics cartridge, it will
        not help you either.

        The  above  mentioned  example  concerns  the use of a German
        text,  but  similar  problems  occur  also in other languages
        which use  the ASCII  characters from  the upper  half of the
        table.

        Therefore, the SPLOT program offers the TEXT FILTER  function
        with the  F7 key.  If you  switch on  this function,  all the
        ASCII  characters  from  the  value  of  128  to  175  and  á
        character will be plotted according to the selected code page
        (see chapter 6).  And  it does not matter what  character set
        of  the  plotter  is  just  set.  This will enable  to  write
        multilingual  texts  in  your  HP-GL  (DXY-GL) files directly
        without complicated  switching of  character sets.  The HP-GL
        (DXY-GL) file created in this  way must be exported to  a new
        HP-GL (DXY-GL)  form through  the HP-GL  (DXY-GL) export (see
        chapter 5) with the TEXT filter switched on, and only such  a
        newly originated file can be drawn on the plotter.

        To demonstrate  using this   method of  writing  multilingual
        texts  we   recommend  you   to  study   over  the   enclosed
        demonstration file ASCII.PLT and display it at first with the
        TEXT filter being switched off and then on.



          Another function which the SPLOT program can offer for your
        work  with  the  HP-GL  text   is  the  function  of   direct
        (interactive) inserting texts into a picture. To do it, it is
        necessary to define its  position (XY), size (SI),  direction
        (DI), slant (SL), the character set number (CS), the selected
        pen (SP) and, naturally, the text itself.

          By means of the menu activated by the F5 key on the page of
        a  large  view  you  can  choose  the  following   individual
        functions necessary for the text manipulation :

         - define a new text item
         - edit already existing items
         - read the text items from the disk file
         - save the text items to the disk file

          On defining, editing or reading texts the SPLOT program  is
        brought  into  the  initial  state  which  corresponds   with
        executing IN;RO;IP;IW; instructions. The user's scale (if  it
        was set before) and rotation,  if there is any,  is cancelled
        then. The  position of  the text  is given  in plotter  units
        absolutely, the size  of the text  is in cm  (SI) absolutely,
        the direction of the text is also in degrees (DI) absolutely,
        the slant is  understood as a  tangent of the  required angle
        (SL).

          The position of the text and its size can be defined either
        by setting numeric  values from the  keyboard or by  moving a
        quadrangle which  demonstrates the  outline of  the text  and
        which is  controlled by  the mouse  in a  similar way as when
	making picture cuts (zooming). To do this it is necessary  to
        move the cursor  of the mouse  to the plotting  area. Then by
        pressing the  left button  and moving  the mouse  at the same
        time the position of the text changes, by pressing the  right
        button and moving the mouse at the same time the size of  the
        text changes. The other values are set in a numeric form from
        the keyboard.

          Of course,  the text  itself can  be written  in a  desired
        language  with  the  ASCII  characters  >  127.  In the HP-GL
        (DXY-GL) picture these characters will be displayed according
        to the  code page  you will  choose in  the OPTIONS menu. The
        corresponding  support  of  the  national environment must be
        installed in MS-DOS  (it must support graphics modes) if  you
        want to have the same characters on the edit line.

          The  function  of  direct  inserting  a  text  accepts  the
        following keys :

          a) when  defining  a  new  text item or correcting  already
             existing text items:

               Alt_T - setting the text string for plotting

               Alt_X - setting the position of the text (X,Y) [pu]

               Alt_S - setting the size (X,Y) [cm] (i.e. the size  of
                       one text character)

               Alt_D - setting the direction of the text [deg]

               Alt_L - setting the slant of the text

               Alt_C - setting the character set number

               Alt_P - setting the  number of a pen for  plotting the
                       text

               F1    - finishing  the editing of  the text with   the
                       changes saved

               F2    - the redrawing of the edited text

               F9 or Esc - finishing   the editing  of the text  with
                           canceling the changes

          b) when correcting already existing text items :

               F3 - skip to the correction of the previous text  item
                    (if it exists)

               F4 - skip to the correction of the next text item  (if
                    it exists)

               F6 - the choice of a text item for correcting (if  you
                    have defined more than one text item)

               F8 - the  canceling (erasing  from memory)  of a  text
                    item according to your choice

          In this  way it  is possible  to define  any number of text
        items  that  are  loaded  into  memory  and  after  finishing
        plotting the respective file they are drawn.

          It is  supposed that  the set  of the  text items  you have
        created relates to the plotted file. That is why when  coming
        to the plotting of  a new file (i.e.  when the plotting of  a
        file is  activated otherwise  than by  the F3  key or  F8 key
        resp.), all  the text  items are  always erased  from memory.
        Before it happens, the program enables to put the text on the
        disk if you did not do that before.

        There are two ways how to save the created texts :

        1) In the  HP-GL (or DXY-GL  resp.) form in  the plotted file
           (according to the item in the menu in the ORIGINAL  file).
           Respective commands for plotting the defined text items on
           the plotter are attached to  the end of the plotted  file.
           After the texts are saved on the disk in this manner, they
           are always erased from memory of the program, even if  you
           do not start plotting a  new file. This is the  final form
           of storing texts  which you can  use on condition  you are
           already satisfied with the  created texts and you  want to
           attach them to the displayed file for ever. If you want to
           display the texts  together with the  plotted file on  the
           plotter or on  the printer and  you do not  want to attach
           the texts to the original file for ever, use directly  the
           appropriate export format  with the F8  key (as the  texts
           loaded in the  memory of the  program are also  exported).
           Then  you  can  put  the  texts  on  the disk in the other
           described way.

        2) In a special format in a EXTRA file.  Only the texts saved
           in such a  way can be  read into the  program memory later
           again and thus you can continue in their editing.




                8. VIDEO CONFIGURATION
                ----------------------

          The  SPLOT  program  is  a  graphics  program  requiring  a
        graphics  card  EGA  or  VGA  and  supporting  the  following
        graphics modes:

          1) monochrome mode

             - EGA 640x350

          2) 16 color modes

             - EGA 640x350
             - VGA 640x380
             - SUPER EGA 640x480, 640x258, 800x600
	     - SUPER VGA 800x600, 1024x768, 1280x1024

          The choice  of the  required mode  can be  made in the menu
        which is initiated by the Alt_F10 key or Alt_V key resp.   In
        this menu there are the following items :

         - AUTOMATIC MODE  - is determined  to set up  the video mode
              automatically according to the type of a video card and
              according to this it sets up the following modes:
              - EGA mono 640x350
              - EGA 16 color 640x350
              - VGA 16 color 640x480

         - BIOS MODE - is determined  to set up the mode you  require
              according  to  the  number  and  resolution.  The  mode
              numbers together with the appropriate resolution should
              be given  in the  documentation of  your graphics card.
              The BIOS  mode   number  is  to   be  set  in   decimal
              units standardly, if you want to set it in  hexadecimal
              units, write the H character  at  its end. This  way of
              setting the video mode is useful if you own an EGA card
              or  VGA card with high  resolution (SUPER EGA  or  VGA)
              and  you will  not find it in  the list of SUPER  cards
              offered  by the SPLOT program.

	  - SUPER VIDEO  CARDS - contains  the lists of  SUPER EGA or
	      VGA  cards  divided  according  to resolution (640x480,
	      640x528, 800x600, 1024x768, 1280x1024).  Even  if  your
	      card is not  in the list,  it is  possible that it will
	      function when you choose  another card of the list.  In
	      the other case you can try to set the  required mode by
	      means of the BIOS MODE item  (except the resolutions of
	      1024x768  and  1280x1024  which  are  highly   hardware
	      dependent).
	      Notice - not all listed SVGA cards have been tested.
	      Only standard VESA video modes are supported (not OEM).

	  - the other items of  the menu contain standard EGA  or VGA
	    modes  in  which  the  SPLOT  program  can work (EGA mono
            640x350, EGA color 640x350 and VGA color 640x480). It  is
            possible to set any of  these three modes on VGA,  but on
            the  EGA  cards  it  is  possible  to  set only EGA modes
            according to the type  of the connected monitor  (mono or
            color).

          - the last item of the menu called `VGA GRAY-SCALE'  serves
            to  switch  ON/OFF  the  gray-scale  summing on VGA video
            adapter.  You will need switch ON this option in case you
            have an VGA video adapter with mono monitor and your  VGA
            adapter   doesn't   perform   the   gray-scale    summing
            automatically.   The  gray-scale  summing  enables use of
            color video modes  along with VGA  mono monitor.   If the
            gray-scale summing is  active, each color  is transformed
            to  corresponding  gray  level  and  thus you are able to
            distinguish  individual  colors  even  when  using a mono
            monitor.   If the  gray-scale summing  is inactive,  some
            colors are  undistinguishable on  mono monitor  (e.g., in
            SPLOT program you may not see some pen colors unless  you
            change its color value). The `VGA GRAY-SCALE' item is not
            displayed  if  your  video  adapter  or active video mode
            doesn't support it.



                9. PEN IDENTIFICATION
                ---------------------

          The identification of pens  serves to emphasizing parts  of
        the picture drawn  with the same  pen and to  informing about
        the number  of pens  used during  drawing the  given picture.
        This information is useful namely for the correct loading  of
        the plotter pens in case you decide to draw the given picture
        on the plotter.

          The keys from Alt_1 to Alt_0  in a small view and the  keys
        from 1 to 0 in a  large view are determined for indicating  a
        part of the picture drawn by the same pen.  If you press  the
        appropriate  key,  a  part  of  the  picture  drawn  by   the
        appropriate pen will begin to  flash and it will be  flashing
        until you press the key corresponding with the identification
        of another pen or if you do not cancel the identification  by
        pressing the Alt_0  key or 0  key resp.   This identification
        functions only in color video modes.

        Example: If you press  the key Alt_1 (in  a small view) or  1
                 (in a  large view)  resp., the  part of  the picture
                 drawn by the pen number 1 will begin to flash (Alt_2
                 or 2 resp. by the pen number 2, etc.).

          In color modes in the SPLOT program each pen is  associated
        with appropriate  color. It  is possible  to choose  from the
        palette of 62 colors for  each pen. You can change  the color
        of the pen when the identification of this pen is switched on
        by pressing  the Gray-Plus  key or  the Gray-Minus  key resp.
        (increasing or decreasing the number of the color  associated
        with this pen). When  the pen identification is  switched on,
        information about the color number of the pen in a large view
        is given in the right  bottom corner of the screen.  In large
        view you can change pen colors also after pressing the  Alt_1
        key, the Alt_2 key etc.  In this case there is no flashing of
        the part of the  picture as it is  in a small view,  but only
        information about the color number  of the pen, which can  be
        changed in  the described  way, appears  in the  right bottom
        corner.   You can  save the  palette of  the colors  you have
        chosen by  pressing the  Alt_S key,  or you  can restore  the
        original palette by the Alt_R key.

          The information panel containing the individual pen numbers
        serves to identify  the numbers of  pens used during  drawing
        the picture. At the beginning of drawing all the pen  numbers
        are  gray,   during  drawing   the  color   of  the    number
        corresponding with the  pen just being  used is white,  after
        finishing drawing the color of the numbers corresponding with
        all the used pens is white.



                10. NOTES
                ---------

        - When  the  SPLOT  program  is  started, it is in the  state
          corresponding with the state of the simulated plotter  just
          switched  on.  When  coming  to  plotting  a  new file, the
          program performs only the  operation of changing paper.  In
          this case the program (plotter) is in the state in which it
          has been left by the commands of the previous file. That is
          why  it  is  generally  recommended  to place an initiating
          command sequence  to the  beginning of  each file.  It will
          bring the plotter  to the well-known  state.  Otherwise  it
          can happen that the same  file can be drawn in  another way
          every time,  dependently of  the contents  of the  previous
          plotted files. The author recommends to use the  initiating
          sequence IN;RO;IP;IW; (in some plotters the IN command does
          not influence the setting of rotation).
            In  other  cases  the  program  is  brought  to the state
          corresponding with the switching off and on the plotter  in
          these cases:
           - at any change of the format or the paper size,
           - at the change of the language syntax (HP-GL <--> DXY-GL),
           - at  switching  on/off  the  simulation  of the  graphics
             cartridge HP 17440A (ColorPro).

        - After  finishing  the  SPLOT  program  saves  the important
          parameters (a palette of colors for pens, a choice of  view
          for plotting, a size of  paper, command mode, etc.) in  the
          SPLOT.INI file in  the directory in  which the program  EXE
          file is situated.  When starting the program, the SPLOT.INI
          file is used for resetting these parameters. If you want to
          set a permanent configuration of the program which will not
          be changed,set on the READ ONLY attribute of this file.


          NOTICE

          -  Hewlett-Packard, HP-GL, HP-GL/2, HP, DraftPro,
	     DraftMaster, LaserJet, DeskJet and PainJet are
	     registered  trademarks of the Hewlett-Packard Company.

          -  Microsoft,  MS,   MS-DOS  and  GW-BASIC  are  registered
             trademarks  and  Windows  is  a  trademark  of Microsoft
	     Corporation.

          -  IBM and PC-DOS are registered trademarks of
             International Business Machines Corporation.

          -  EPSON is a registered trademark of EPSON Corporation.

          -  AutoCAD is a registered trademark of Autodesk, Inc.

	  -  PostScript is a trademark of Adobe Systems, Inc.