A EYE OPENING VIEW OF INFORMATION COLLECTED BY signal level meters     

   *COMSONICS WINDOW II signal level meter or *TRILITHIC TRICORDER

       By using software furnished by the manufacture to make a 
  "WR.###" file, which will be a single lotus or 123 file of all
  BINS.  CDB will make new files ALLOWING THE VIEWING OF VIDEO
  AND AUDIO LEVELS WITH LINE LEVELS AND GRAPHICS OF PEAKS.

       Levels which MAY NOT MEET FCC SPECIFICATIONS are INDICATED.
  Readings may be SEARCHED and COMPARED. The SCALE can be FIXED or
  AUTO SCALE for COMPARISON on screen display.  The MENU is
  Displayed around the screen for fast and EASY USE. There are
  several special keys not menued. "F" toggles FIXED and AUTO SCALE.
  "I" stores a displayed reading as and output level and then use
  "I" again to store a different reading as the INPUT to the next
  amplifier so an evaluation of the cable between the two can be
  made. The tab key will show level of high and low pilot. End key
  or Home key will clear and redraw the last level. The (c) Dif_lev_
  function has also been added. "d" stores the reading to be COMPARED
  and "D" toggles ON and OFF if a reading is stored.

       Sample readings will show COMMENTS/LOCATIONS which were added
  when a WR.* FILE was CONVERTED to files that are smaller for use
  by the viewer PROGRAM. The files maybe typed to the screen or printed.
  IF GRAPHICS.COM is LOADED before starting, SHIFT PRINT SCREEN will
  produce the current view on some PRINTERS, as it is on the SCREEN.

       This program has been developed over a period of many years and
  has evolved to this latest version.  With the FCC SPECIFICATIONS
  changing, YOUR personal CDB.DAT file must be kept current.

       To make use of different versions of DOS, support programs which
  sort and find readings are used by CDB. Because the data files are
  small, the complete system and data files will fit on a single disk.
  If it's preferred that no outside files be put on a company computer,
  a version is available that will only work on an external disk drive.
  CDB is for ANYWHERE USE and CDBDISK will work only on a DISK DRIVE.
  If the support files are not in the "path", the program will abort.

       THIS AND ALL VERSIONS MAY BE USED WITHOUT MODIFICATION UNTIL
       THEY DIE...USUALLY ONE YEAR!
 
       REQUIRED UTILITIES THAT MUST BE IN PATH:

             SORT.*   COMMAND.COM   GRAPHICS.*  WHERE.COM


  For more information write: E H ELLZEY
                              RT 1 BOX 211C
                              ELLISVILLE MS 39437

  or call 601-649-5391 or leave a message on the HAWK'S NEST
  BBS - 601-649-0596 - 24 hours - 2400/14400-N-8-1