VIPER VLB Installation/Utilities/Drivers Diskette v1.02
                           Release Notes
        
Release 1.02 of the Viper VLB Installation/Utilities/Drivers Diskette 
includes changes to a number of items, including the Windows 3.1 drivers,
the VPRMODE.EXE utility program, and the GO.EXE installation program.  These 
changes include:


Windows 3.1

1.  The problem with MS Access has been corrected.
2.  The "flashing" cursor seen in some low resolution modes has been fixed.
3.  Performance of the Windows drivers have been improved in a number of 
    areas, including text handling and circle drawing.


VPRMODE.EXE

1.  Several new monitor types have been added to the Monitor Menu.
2.  The default memory base address for the Viper VLB has been changed
    from A0000000 to 80000000.  This was done to offer greater compatibility
    with VESA Local Bus motherboards.  The A0000000 address remains one of
    the six options for the memory base address.
3.  The VESA BIOS Extentions (VPRMODE VESA) have been changed to eliminate
    lockup problems with some applications (CSHOW, FRACTINT, VPIC). 
    Additionally, the palette roll feature in VPIC is now supported in 
    resolutions below 1152x960.


GO.EXE

1.  GO.EXE will now automatically run the VPRMODE program during first-time
    installations, eliminating potential software initialization problems.

2.  The TurboDLD Deluxe drivers are now included on the 
    Installation/Utilities/Drivers diskette, eliminating the need for a
    separate ACAD driver disk.


***************************************************************************        
        ** IMPORTANT VIPER VLB SOFTWARE INSTALLATION NOTES **

1.      DO NOT INSTALL THE VIPER VLB WINDOWS 3.1 DRIVERS INTO YOUR WINDOWS
        DIRECTORY. DUPLICATE FILES NAMES EXIST!!

2.      It is best to use the VPRMODE.EXE utility to properly configure
        the Viper VLB for your monitor BEFORE using Windows 3.1 or AutoCAD.       

   !!!  BEFORE USING THE VIPER VLB WINDOWS 3.1 OR AUTOCAD DRIVERS, USE  !!!  
   !!!  GO.EXE TO INSTALL THE VIPER VLB UTILITIES, AND USE VPRMODE.EXE  !!!
   !!!  TO PROPERLY CONFIGURE THE VIPER VLB FOR YOUR MONITOR            !!!


        ** IMPORTANT WINDOWS 3.1 DRIVER INSTALLATION/CONFIGURATION NOTES **

1.      When the Windows 3.1 drivers are copied to your hard drive, a
        driver setup & configuration utility, INSTALL.EXE, is also copied.
        INSTALL.EXE should be used from within Windows to setup Windows 
        for the Viper VLB.

2.      Insure that Windows is configured for standard VGA mode before
        using INSTALL.EXE. This can be done with the SETUP.EXE program found
        in your WINDOWS subdirectory.

3.      INSTALL.EXE should be started by using the File|Run command in the 
        Windows Program Manager (File|Run  C:\VIPER\WIN31\INSTALL).  

4.      After running INSTALL.EXE from within Windows, a Diamond Viper Setup
        icon will be placed into the Windows Control Panel.  The Diamond     
        Viper Setup program can be used to change resolutions, colors, fonts,
        and palette type.


UTILITY FILES

VPRMODE.EXE     command line and menu driven mode and monitor setting 
                utility.  Use VPRMODE.EXE to configure the Viper VLB 
                for your particular monitor, to change the VIPER VLB 
                memory address, to select a text display mode, and to
                run Viper VLB diagnostics.
                VPRMODE saves monitor timing information to the 
                VIPER.INI file.  
                
                NOTES:  1. use VPRMODE ? for command line option list. 
                        
                        2. the VPRMODE monitor configuration save screen          
                           may be displayed after running some of the
                           VPRMODE commands.  If this happens, select 
                           ENTER to save. The screen will not appear again.
                        
                        3. KNOW YOUR MONITOR! Please refer to your monitor
                           manual or manufacturer for correct monitor timing
                           information before running VPRMODE, and before
                           contacting Diamond for technical assistance. If
                           you do not have this information, DIAMOND WILL
                           NOT BE ABLE TO HELP YOU with VPRMODE problems.
                           
VIP.EXE         utility which will display or write to a file important
                system configuration information which can be used as 
                an aid in trouble-shooting. Type VIP to display to screen, 
                and VIP <filename> to save to a file.

                NOTES:  1. the VPRMODE save configuration screen may be 
                           displayed after running VIP.  If this happens,
                           select Enter to save.  The screen will not  
                           appear again.

VDIAG.EXE       diagnotic utility which will display color test patterns       
                in each resolution supported.

                NOTES:  1. to test extended modes, load the VESA BIOS 
                           extentions before running VDIAG.  This can
                           be done by typing  VPRMODE VESA at the command
                           prompt.

CHKPATH.EXE     utility which checks the PATH environment variable for the          
                specified string.  Is used in the AUTOEXEC.BAT file with
                the VIPERPATH statement.

MD2.EXE         utility which allows for the creation of multiple 
                sub-directories.  Used by VPRMODE.EXE.

VIPER.INI       this file is used to store the monitor and configuration
                information for the Viper VLB, and is updated each
                time you choose to Save Configuration from the VPRMODE.EXE
                program.  Drivers find the location of the VIPER.INI file
                by checking the VIPERPATH environment variable. 

VIPERPATH       an environment variable which is used by device drivers
                (Windows 3.1, AutoCAD) to locate the VIPER.INI file.  
                This variable is set by the DOS SET command, and is 
                automatically appended to your AUTOEXEC.BAT file during
                Viper VLB Utility installation.


                        !!!!!  IMPORTANT !!!!! 

                   THE VIPER.INI FILE AND THE VIPERPATH STATEMENT ARE
                   NEEDED FOR PROPER USE OF THE VIPER VLB WINDOWS AND
                   AUTOCAD DRIVERS!  DO NOT REMOVE THEM FROM YOUR SYSTEM.