Qmodem Operations Manual

                                                      The Forbin Project, Inc




                               Table Of Contents


Preface..........................................1

Accolades........................................1

Tools of the trade...............................1

System Requirements..............................1

How to Contact The Forbin Project................2

License..........................................3
 Single User.....................................3
 Giving a copy to a friend.......................3
 Sysops - what you need to know..................3
 Distributors of PD or ShareWare.................3

Ordering Information.............................3
 Registration....................................3
  Registration only..............................3
 Site License....................................6
  Discounts......................................6

Warranty.........................................7

Operating Environment............................8
 Multi-Tasking Systems...........................8
 Other Background Software.......................8

Installing Qmodem................................9
 Back up your diskettes!.........................9
 Floppy Disks....................................9
  Starting Qmodem in a Floppy Setup.............10
 Hard Disk Installation.........................10
  Subdirectory Structure........................11

ONLINE Help.....................................11
 Getting Help when you need it..................11

Upgrading from a previous release...............13

Command Line Parameters.........................14

The Status Line.................................14

The Home Menu...................................16

Configuration...................................19
 Menu Navigation................................19
 First time setup...............................20
 Video..........................................20
  Custom Colors.................................20
   Customization Window.........................21
   BIOS Video...................................23
   Linefeed after CR............................23
   Snow Checking................................23


                                                                Qmodem SST     i



   Growing Windows..............................24
   Status Line..................................24
   Destructive backspace........................24
   Line Wrap....................................24
   Video Restore................................25
   Jump Scroll..................................25
   Emulation....................................25
  Communications Parameters.....................26
   Default Baud Rate............................26
   Default Data Bits............................26
   Default Parity...............................26
   Default Stop Bits............................27
   Command Before Baud Change...................27
   Command After Baud Change....................27
   Cycle Delay..................................27
   Timeout Delay................................27
   Modem Command delay..........................28
   Serial Port..................................28
  Modem Commands................................28
   Initialization Command.......................29
   Prefix Dial Command..........................29
   Suffix Dial Command..........................29
   Connect Message..............................29
   Error Messages 1-4...........................29
   Abort Dial Command...........................30
   Hangup Command...............................30
   Redial Hangup Text...........................30
  Port Addresses................................32
   COM1-COM8 Base...............................32
   COM1-COM8 IRQ................................33
   Xon/Xoff.....................................38
   CTS/RTS Flow Control.........................38
   CTS when Writing.............................38
   FIFO during Shell............................39
   Lock DTE Baud Rate...........................39
   High Speed Xmit..............................40
   16550 UART Enable............................40
   Init Ignores CD..............................40
 Directories....................................40
  Upload........................................40
  Download......................................41
  Scripts.......................................41
  SWAP..........................................41
  Batch Directories.............................41
  Alt-W Pick....................................42
 Host...........................................42
  Type of System................................42
  Download Dir..................................43
  Upload Dir....................................43
  Maximum Time..................................43
  DOS Password..................................44
  Shutdown Password.............................44
  Init Command..................................44
  Answer Command................................44
  OK Message....................................44
  Ring Detect...................................44
  Busy Command..................................45
  # Rings and Answer............................45


ii   The Forbin Project, Inc.



 Protocols......................................45
  Protocol Revisions............................46
   Select Character.............................46
   Protocol Name................................46
   Upload BAT...................................46
   Download BAT.................................47
   Filename Prompt..............................47
  Installing an external protocol...............47
  ASCII Options.................................48
   ASCII Receive................................49
    Use INPUT Translate Table...................49
    Carriage Return Handling....................49
    LineFeed Handling...........................49
   ASCII Transmit...............................50
    Use OUTPUT Translate Table..................51
    Carriage Return Handling....................51
    LineFeed Handling...........................51
    Pacing Speed................................51
    Pacing Character............................51
    Blank Line Expansion........................51
    End Of Line Character.......................52
  Protocol Toggles..............................53
   Overwrite Files..............................53
   Auto-Increment Filenames.....................53
   Save Partials................................54
   Clear Batch Screen...........................54
   Zmodem Auto-Start............................54
 Files..........................................55
  Online Help...................................55
  Screen Dump...................................55
  Capture.......................................55
  Log...........................................56
  Backscroll....................................56
  View..........................................56
  Printer.......................................57
  Time/Date Stamp...............................57
 Options........................................57
  Toggles.......................................57
   Beeps & Bells................................58
   ANSI Music...................................58
   Del/^H Backspace.............................58
   Auto Start Log...............................58
   Keypad emulation.............................58
   ENQ Response.................................59
   Guard Alt-H..................................59
   0xE0 Doorway Codes...........................59
   Alt-D FON Book...............................60
    Tag Advance.................................60
    Auto Start..................................60
    Clear tags on FKey..........................60
    Write FBK File..............................61
  Toggles.......................................61
   EMS for Overlays.............................61
   Int16 Enable.................................62
   Share IRQ's..................................62
   Optimum Shell................................62
   Disk Shell...................................62
   Calibrate Delay..............................63


                                                            Qmodem SST       iii



  Memory........................................63
   Script Variables.............................63
   Download Buffer..............................63
   Overlay Buffer...............................63
  Sounds........................................64
   Upload tone..................................64
   Download tone................................64
   Connect Tones................................65
    Connect Tone 1..............................65
    Connect Tone 2..............................65
    Connect Tone 3..............................65
    Max Repeats.................................65
  Delays........................................66
   Status Windows...............................66
   File Transfers...............................66
   BREAK Timing.................................66
   DTR Timing...................................67
  Characters....................................67
   Beeps & Bells................................67
   ANSI Music...................................68
   Status Line Filler...........................68
   Phone Book Tag...............................68
   Notes Tag....................................68
   Date Mask....................................69
   Time Mask....................................69
   Elapsed Mask.................................69
 Exit...........................................70
  Save Changes..................................70
  Abandon.......................................71

Qmodem Keyboard Commands........................72
 Strip/Replace Tables [Alt-A]...................72
  Changing an incoming character................72
  Changing the High-Bits........................73
 Bells and Beeps Toggle [Alt-B].................74
 Clearing the screen [Alt-C]....................74
 Dialing Directory [Alt-D]......................74
  Moving around in the Directory................75
   Using Up & Down Arrows.......................75
   Using PgUp & PgDn............................75
   Using ^PgUp & ^PgDn..........................75
   Revising this Screen.........................78
   Untag All....................................81
   Starting the Dialer..........................82
  Dialing from ALT-D............................82
  Primary Commands..............................82
  Status messages...............................83
  Parameters passed to Scripts..................84
   Manual Dial mode.............................84
   {F2}-{F12} Speed Dialing.....................85
   How to use Prefixes..........................86
   Editing Attached Notes.......................87
   Other info in the Phone Book.................91
 Changing Duplex Mode [Alt-E]...................95
 Script Files [Alt-F]...........................96
  What is a Script?.............................96
 Terminal Emulation [Alt-G].....................97
 Hangup the phone [Alt-H]......................101


iv   The Forbin Project, Inc.



 Information screen [Alt-I]....................101
 Function Key Macros [Alt-J]...................102
  Editing Key Macros...........................103
  DOS Shell Macros.............................104
  A Dial Macro.................................105
  An Edit Macro................................105
  A Help Macro.................................106
  A Script Macro...............................106
  A LOG Macro..................................107
  The $PASSWORD Variable.......................107
  Loading a new Key file.......................108
 Changing COM Ports [Alt-K]....................108
 Changing the Logged Drive [Alt-L].............108
 Music Toggle [Alt-M]..........................109
 Changing Subdirectories [Alt-O]...............109
 COM Port Settings [Alt-P].....................110
 QuickLearn Script Recorder [Alt-Q]............111
  Saving the Current Setup.....................112
  Commands that are recorded...................113
  Putting it all together......................116
 DOS Shell [Alt-R].............................119
 Split Screen Mode [Alt-S].....................121
 Screen Dump [Alt-T]...........................122
 Scroll Back Toggle [Alt-U]....................122
 View a File [Alt-V]...........................123
 Disk Directory [Alt-W]........................123
 Exiting Qmodem [Alt-X]........................125
 Delete a File [Alt-Y].........................126
 Xon/Xoff Toggle [Alt-Z].......................126
 Uploading & Downloading   (PgUp/PgDn].........127
  Selecting a Protocol.........................127
   ASCII protocol..............................128
   Xmodem......................................128
   Xmodem CRC..................................128
   Relaxed Xmodem..............................128
   1k-Xmodem...................................129
   Ymodem......................................129
   1K-Xmodem/G & Ymodem-G......................130
  External protocols...........................130
 Scroll Back   (UpArrow].......................137
 Capture to Disk   (Ctrl-Home].................139
 Sending a BREAK   (Ctrl-End]..................139
 Backspace / DEL Toggle [Alt-1]................140
 EGA/VGA Modes [Alt-2/Alt-4]...................140
 Hi Bit Stripping Toggle [Alt-8]...............141
 Copying to the Printer   (Ctrl-PrtSc].........141
 Logging activity to a File [Alt-0]............142
 Host Mode [Alt-5].............................144
  Host Setup...................................144
  External Files Required......................144
  Files created by the Host....................145
  Optional Files...............................145
  Logging on Locally...........................146
  Starting the Host while ONLINE...............146
  Sysop Commands...............................146
   F2 Chat.....................................146
   F5 Drop to DOS Locally......................147
   F10 Disconnect Caller.......................147


                                                              Qmodem SST       v



  Host Functions...............................148
   R  Reading Messages.........................148
   E  Entering a Message.......................149
   P  Page the Sysop...........................150
   F  File List................................151
   D  Download.................................151
   U  Upload...................................151
   O  Open Script..............................151
   S  Shell to DOS.............................153
   G  Goodbye (Hang-up]........................154
   ?  Help with Host Commands..................154
   Z  Shut down the Host.......................155
  Packing the Message Base.....................155
 Status Line Toggle [Alt-Minus]................156
 Doorway Mode Toggle [Alt-Equal]...............156
 Alt. Status Line Toggle [Alt-Enter]...........156

The Internal Editor............................157
 The Editing Screen............................158
 Basic Movement Commands.......................160
 Insert and Delete Commands....................162
 Block Commands................................164
 Miscellaneous Commands........................165

EDINSTAL.......................................167
 Running EDINSTAL..............................168
  Fast Entry...................................168
  Random Access................................168
  Quitting the Program.........................169

The Qmodem Script Language.....................170
 What is a script?.............................170
 Physical vs. Logical Screen...................170
 Input and Output Commands.....................170
 Variable Handling.............................171
 Running Scripts...............................171
 Script Commands...............................171

SCRIPT LANGUAGE................................171
 Different types of Scripts....................171
 How to create and name a Script file..........172
  Using an Editor..............................172
 Starting a Script.............................172
 /S= command line switch.......................172
 The explicit .i.Alt-F.........................172
 Linked-Script.................................173
 Stopping a Script.............................173
 Debugging a Script............................173
 Special characters in Scripts.................177
 Definitions and Parameters....................178
  Labels.......................................178
  Pre-defined String variables.................179
  Pre-defined System variables.................180
  Connect Information variables................181
  General Coding Information...................184
 Script Commands...............................184
 Scripts Command Reference.....................186
  ATWRITE......................................187


vi   The Forbin Project, Inc.



  ASSIGN.......................................187
  BEEP.........................................188
  BOX..........................................188
  BREAK........................................188
  CHDIR........................................189
  CLOSEFILE....................................190
  CLRSCR.......................................190
  COLOR........................................190
  COLORBG......................................191
  COLORFG......................................192
  DEBUG........................................192
  DECR.........................................192
  DELAY........................................193
  DIAL.........................................193
  DISPLAY......................................194
  DISPLAYLN....................................194
  DOS/BIGDOS...................................195
  DOWNLOAD.....................................196
  DRIVE........................................197
  EGA..........................................197
  EXIST........................................198
  EXIT.........................................198
  FKEY.........................................198
  FLUSH........................................199
  GET..........................................199
  GETR.........................................199
  GETN.........................................200
  GETNR........................................201
  GETSCR.......................................201
  GETX.........................................202
  GOSUB........................................202
  GOTO.........................................203
  GOTOXY.......................................203
  GRAPHICS.....................................204
  HANGUP.......................................204
  IF...........................................204
  INCR.........................................206
  INKEY........................................206
  LOADFON......................................206
  LOADKEY......................................207
  LOG..........................................207
  NOTE.........................................208
  OPENFILE.....................................208
  PAUSE........................................209
  POP..........................................210
  PORT.........................................210
  PUSH.........................................211
  PUTSCR.......................................211
  READFILE.....................................212
  RETURN.......................................212
  SCRIPT.......................................213
  SEND.........................................213
  SETCOMM......................................214
  STAMP........................................214
  STRING.......................................215
  SYSTEM.......................................215
  TIMEOUT......................................216
  TURNOFF......................................216


                                                            Qmodem SST       vii



  TURNON.......................................216
  UPLOAD.......................................217
  WAITFOR......................................219
  WAITUNTIL....................................219
  WHEN.........................................220
  WINDOW.......................................221
  WRITE........................................221
  WRITELN......................................222
  WRITEFILE....................................223
 Script Error Messages.........................223

Appendix A.....................................229
 Most Asked Questions & Answers................229















































viii The Forbin Project, Inc.





Preface

This document was revised for Qmodem 4.2.

Qmodem software and this document is (C) Copyright 1990 The Forbin Project, Inc.
All rights reserved World Wide.  Qmodem is a Trademark of The Forbin Project,
Inc.

Any specific hardware/software names used in this document are trademarks of
specific manufacturers.



Accolades
I would also like to take this opportunity to thank all of the Alpha and Beta
testers who helped find all the problems and solutions in Qmodem.  They have
made creating this new version a pure joy.  Many times we agreed and disagreed,
but we never lost sight of the goal; to make Qmodem the best darned
communications program!

Thank you!



Tools of the trade

I would also like to thank the various Software companies that helped bring
Qmodem 4.2 into reality.

           Borland  for Turbo Pascal 5.5 in which much of the actual code is
     International  written.  Also for their Turbo Assembler and Turbo
                    Debugger that I found so indispensable during the
                    debugging stages.

       Turbo Power  for the fine libraries of Turbo Professional and Object
          Software  Professional.  They made the difference between a so-so
                    program and a truly elegant one.

         Microsoft  for Word for Windows and Windows 3.0 which helped me get
                    this document together and formatted so nicely.

             ZSoft  for SoftType which made using Windows and Word  truly
                    enjoyable.

         Bitstream  for FontWare for Windows.  This allowed me to do what
                    everyone said was impossible.




System Requirements
Qmodem requires an IBM PC,XT,AT,PS/2 or IBM compatible computer with at least
384K RAM, a Color Graphics or Monochrome adapter and monitor, and a serial port
and modem.






                                                                Qmodem SST     1



How to Contact The Forbin Project

The best way to get hold of us, is to call the Forbin Project BBS.  We have 8
nodes running the PCBoard BBS software; 24 hours a day, 7 days a week.  From the
"Main Menu Command" prompt, use the (C)omment command.  Turn-around time for
answering BBS mail is usually within 24 hours.

We no longer respond to tech support through the US Mail.  It is too time
consuming and the delays are enormous.  If you must write a letter, you must be
able to FAX it to us.

You can send mail and packages to the following addresses:

       Mail Orders  The Forbin Project Inc.
                    Post office Box 702
                    Cedar Falls, IA  50613    (USA)

  Packages, UPS or  Please call before you ship to get the current address.
   Federal Express  (we're moving to larger facilities!)


Phone numbers for reaching us are:

      Voice Orders  (319) 232-4516   8am-5pm (CST)  Mon - Fri

      Tech Support  (319) 232-4516   1pm-5pm (CST)  Mon - Fri
                    (this time frame will expand when we finish relocating!)

       FAX Machine  (319) 233-1725   24 hours a day

     MultiTech V32  (319) 233-6006   24 hours a day
          (1 line)
   1200-38400 baud

    USRobotics HST  (319) 233-6157   24 hours a day
   Duals (7 lines)
   1200-38400 baud


Note: When calling our BBS system, set Qmodem up for 8 Data bits, No Parity
      and 1 Stop bit.

We also run a Qmodem Support Roundtable on the General Electric GEnie system.
Type "QMODEM" at any menu prompt to get to us!



Calling for Tech Support
Please have the following information handy before you call:

  o  Version of Qmodem you have
  o  Computer make and model number
  o  Modem make and model number
  o  Version of DOS
  o  Copies of your CONFIG.SYS and AUTOEXEC.BAT files





2    The Forbin Project, Inc.



License

Qmodem is not, and has never been in the Public Domain.  Qmodem is not free.

Non-registered users are granted a limited, 90-day  license to determine whether
or not the program meets their needs.  Continued use of Qmodem beyond the 90-day
evaluation time period  requires registration of the program.  Use of non-
registered copies of Qmodem beyond the original evaluation period is strictly
prohibited.

No one may modify Qmodem for any reason, in any way, including but not limited
to, decompiling-compiling, patching, disassembling, or reverse engineering the
program.

These restriction also applies to all Qmodem screen displays such as the opening
screen, help screen, and all other proprietary program output.  Only 'FORBIN
APPROVED' patches may be applied to the Qmodem program(s).

Qmodem may be copied and distributed to others, subject to the above
restrictions and the following:

  Qmodem must be copied in unmodified form, including the file containing this
  license information.

  Complete Qmodem documentation and Online Help must be included.

  No copying fee of any type may be assessed other than basic charges for the
  cost of the copying medium.

  Qmodem may not be distributed with any other software or hardware product(s)
  without the express written permission of The Forbin Project, Inc.

Sysops (bulletin board SYStem OPerators) may make Qmodem available for
downloading by their users as long as all above conditions are met.  If problems
are experienced due to the combined sizes of all Qmodem distribution files, the
QMODEM documentation must be bundled with the QMODEM.EXE file to insure that the
user gets it.

Commercial Distributors of Public Domain, ShareWare, or User-Supported software
may distribute Qmodem subject to the above conditions only after obtaining
specific written permission from the Forbin Project, Inc and filling out a
registration form for upgrade notifications.  This condition supersedes any and
all previous agreements.

No blanket authorization has been issued by the Forbin Project, Inc., for
commercial distribution of its products.



Ordering Information
When you register your copy of Qmodem, you are granted a license to use the
program as often as you wish.  There are several advantages to registering your
copy of Qmodem:

  1. The Forbin Project, Inc. has a large BBS in house for registered users.  As
     soon as your registration is received, you will receive 1 year of support
     at no additional charge on these BBS's.  After the first year, you may



                                                                Qmodem SST     3



     renew your subscription to the Forbin Project BBS.  Subscription renewals
     also include all Qmodem updates released during that year.

  2. Telephone support, also for a one-year period following your registration
     date.  No problem is too big or too small for us to tackle,   but you must
     be a registered user to get this kind of support.

  3. We run a "Round Table" (special interest group) on the General Electric
     GEnie system.  Now we are a local phone call away from 99% of you!

  4. Automatic notification of upcoming major new releases or enhancements
     through the mail and on the Forbin Project BBS.


  There are two methods for registering Qmodem:

  1. Send a completed Registration form and a check for $30.  We will assume
     that you have already obtained the program and documentation elsewhere.
     The $30 registration fee does not entitle you to diskettes or printed
     manuals.  Refer to the order form on the following page for pricing.

  2. If you have a valid Visa or Mastercard, we also accept phone orders.  Call
     us during normal business hours at (319) 232-4516.

Non U.S. residents: please send checks or money orders drawn on U.S. Banks in
U.S. Funds.  VISA and MasterCard credit cards are also acceptable.  All foreign
orders are subject to current U.S. foreign trade and technology exchange
restrictions.


NOTE: Pricing is subject to change without notice.  For current pricing,
      call us at the order number listed above.




























4    The Forbin Project, Inc.



INVOICE # 90-150842

        Remit To:       The Forbin Project, Inc.
                        Post Office Box 702
                        Cedar Falls, IA  50613

Qty. Description                             Amount

____ Qmodem Registration                     $30.00 ea __________

____ Qmodem Disk Set (specify 3.5 or 5.25)   $20.00 ea __________

____ Qmodem Printed Manual                   $29.95 ea __________

____ Qmodem Registration & New Disks         $50.00 ea __________

____ Qmodem Registration & Printed Manual    $59.95 ea __________

____ Qmodem Registration, Disks & Manual     $79.95 ea __________

                                             Shipping  __________

     (Iowa residents add 4% sales tax)       Tax       __________
                                    
                                             Total     __________
Payment:
Check [ ]     MasterCard [ ]    Visa [ ]     PO [ ] ________________________

Name:      _________________________________________________________________

Company:   _________________________________________________________________

Address:   _________________________________________________________________

           _________________________________________________________________

Work Phone: (____)  ________________     Home Phone: (____)  _______________

Card #:     __________________________________   Exp. Date: ________________

Signature of Cardholder:   _________________________________________________

Comments:   ________________________________________________________________

            ________________________________________________________________

            ________________________________________________________________

            ________________________________________________________________

Note: Shipping to 48 continental states is $5.00.  Alaska, Hawaii, and
      Canada is $10.00.  Other countries, please call before ordering.
      Second day and Next day air extra, please call.







                                                                Qmodem SST     5



Site License Information

If you plan on using Qmodem in a corporation, government office, or for any
business purpose whatsoever, registration is mandatory and the 90 day limited
license is strictly enforced.  Quantity discounts are available under a Site
License agreement, described below:

One MASTER copy of Qmodem and of its  documentation will be supplied on disk.
The site license customer is responsible for printing the documentation and
copying the disks for distribution.  Archival backups of the MASTER copy are not
counted toward the total copies of the license.

For all site licenses, the customer must appoint a single contact person with
whom all Qmodem related dealings will take place.  Should a problem occur, that
person -- and that person alone -- must  call to report the problem and arrange
for its resolution.  All Qmodem program updates will be forwarded to the contact
person.  When filling out the order form, please use the contact person's name
to prevent any later misunderstandings.

Site license discount rates are as follows:

               Total copiesDiscount
               11  -  20   5%
               21  -  30   10%
               31  -  40   15%
               41  -  50   20%
               51  -  100  25%
               101 -  200  30%
               201 -  300  35%
               301 -  500  40%
               501+        50%


NOTE: All prices and discounts are subject to change without notice.
      Discounts are not cumulative; they apply to separate orders only.

      Purchase Orders less than $100 must be pre-paid.























6    The Forbin Project, Inc.



Warranty (or lack of it)

The Forbin Project, Inc. makes no warranty of any kind, express or implied,
including without limitation, any warranties of merchantability and/or fitness
for a particular purpose.  The Forbin Project, Inc. shall not be liable for any
damages, whether direct, indirect, special or consequential arising from a
failure of this program to operate in the manner desired by the user.  The
Forbin Project, Inc. shall not be liable for any damage to data or property
which may be caused directly or indirectly by the use of this program.

IN NO EVENT WILL THE FORBIN PROJECT, INC. BE LIABLE TO YOU FOR ANY DAMAGES,
INCLUDING ANY LOST PROFITS, LOST SAVINGS OR OTHER INCIDENTAL OR CONSEQUENTIAL
DAMAGES ARISING OUT OF YOUR USE OR INABILITY TO USE THE PROGRAM, OR FOR ANY
CLAIM BY ANY OTHER PARTY.



Definitions
Throughout the documentation, you may run into technical terms or everyday
computer terminology with which you are not familiar.  Following are some text
examples you may come across:

ENTER      This represents the Return or Enter key on the keyboard.  If you see
           this in the text, press the Enter key rather than typing in the
           string.

ESC        This refers to the Esc key on the keyboard.

Alt-[char] Alt- is always followed by a character which means press and hold
           the Alt Key and hit the following letter.  Alt-A means hold the Alt
           key down and press 'A'.

Ctrl-[char]Is executed the same way the Alt- is handled. You press and hold the
           Ctrl key and then press the following letter.  Ctrl key combinations
           may also be specified by the ^ (carat) as in ^T (Ctrl-T).


The following bars represent an image on the screen.


               Sample text displayed on the screen.



















                                                                Qmodem SST     7



Operating Environments

Three multitasking environments are supported:

     DESQview from QuarterDeck Systems.

     TaskView/OmniView from Sunny Hill Software.

     Windows version 3.0 from Microsoft.

DESQview and Windows 3.0 allow Qmodem to run in a window and without requiring
the whole screen.

TaskView takes a slightly different approach and gives Qmodem an entire screen
when the partition is selected.  All of these multi-tasking programs let you be
more productive by running other software at the same time as Qmodem.

TIP: The Utilities Disk contains special configuration files for DESQview
     and Windows.

Qmodem may not operate properly when other background software is running.  By
other background software, we mean programs that are loaded in the CONFIG.SYS,
or by a BAT file and remain in memory.  Certain screen clock programs, for
example, are known to interfere with serial port operations.

If you experience loss of incoming data or other unpredictable problems, it is
possible that one of these programs is interfering with Qmodem.  Remove these
programs or device drivers from the AUTOEXEC.BAT or CONFIG.SYS file one at a
time until you find the offender.

Another method is to start DOS without any resident programs or device drivers
and add them back in, one at a time, until the culprit is identified.  Most
expanded memory drivers, mouse drivers, and hard-disk partitioning software
drivers do not interfere with Qmodem operation.

One program which is known to interfere seriously with serial port operations is
the clock driver supplied with some early memory and multi-function boards.

Conflicts with Qmodem may not be caused by a single program, but by a
combination of programs, which, taken singly, cause no problems.  Therefore, if
you suspect some conflict, you should boot your system with only absolutely
necessary device drivers and resident programs (i.e. a partitioned disk device
driver).

















8    The Forbin Project, Inc.



Installing Qmodem
Back up your diskettes!
The first thing you should do is back up your Qmodem distribution disks.  Always
backup your disks!  I can't stress this enough!  Please refer to your DOS manual
if you are not sure how to backup your disks.



Floppy Disk Installation
Qmodem diskettes have come pre-installed and you only need to make backups.  Be
aware that Qmodem does require one of the following floppy drive setups:

  2 - 360K floppy drives

     This allows you to use one of the floppy drives for downloading.  The drive
     with the QMODEM.OVR file must never be removed during operation.

  1 - 720K floppy & 1 - 360K floppy

     This allows all of the Qmodem files to remain on the 720K drive and allows
     the 360K to act as the data disk for downloading and uploading.  You should
     be able to split the files as if you have 2 360K drives and use the 720K as
     your data disk.  Again, the floppy with the QMODEM.OVR file must never be
     removed during operation.

Copy all of the files from the distribution diskette to a working diskette.  The
recommended files on each diskette are as follows:

     Disk #1   QMODEM.OVR     (overlay for main program)
               QMODEM.CNF     (configuration file)
               QMODEM.FON     (Alt-D phone book)
               QMODEM.PRE     (phone book prefixes)
               QMODEM.KEY     (function key text)
               QM.BAT         (startup BATCH file)
               COMMAND.COM    (to allow shelling to DOS)

     Disk #2   QMODEM.HLP     (online help)
               QMODEM.EXE     (main program)
               *.SCR          (optional script files)

NOTE: When using a single 720K or 1.2mb drive, disks #1 and #2 are combined
      on the single floppy.


















                                                                Qmodem SST     9



Starting Qmodem in a Floppy Setup
Follow these directions:

  1. Place a bootable DOS disk in drive A: and press Ctrl-Alt-Del.

  2. Place disk #1 in drive A: and disk #2 in drive B:.

  3. Type QM and press ENTER at the A> prompt.

  4. When the "Terminal mode" message appears on the screen, you can remove disk
     #2 from the B: drive and use it as a SCRATCH disk for uploads and download.

NOTE: Before running the Alt-N Setup or accessing the Online Help, make sure
      disk #2 is back in the B: drive.


The QM.BAT file should look something like this:

     PATH A:\;B:\
     B:QMODEM

The first line allows Qmodem to search both drives for files it may need to
allocate.  The second line tells DOS to load Qmodem from the B: drive and remain
logged to the A: drive.  This is important, because you may want to remove the
B: disk after Qmodem has loaded.


Hard Disk Installation
When installing Qmodem on a hard disk, all of the floppy disks should be copied
into the \QMODEM subdirectory.  You should also modify your AUTOEXEC.BAT file as
follows:

  1. Add the C:\QMODEM subdirectory to your existing PATH= statement.

  2. Add a SET QMODEM=C:\QMODEM (or the name of the subdirectory you create).
     This is an environment variable that Qmodem checks when it is loaded.  If
     it finds one, then it will also search the defined subdirectory for any of
     the Qmodem specific files it requires.

Making these two adjustments allows Qmodem to be started from any subdirectory
without needing a special BAT file.  You could start Qmodem from your word-
processor directory simply by typing QMODEM at the DOS prompt!


















10   The Forbin Project, Inc.



Subdirectory Structure
It is said that a picture is worth a thousand words...  Here is a picture of one
possible Qmodem subdirectory setup on a hard disk:

QMODEMÄÂÄDOWNLOAD
       ÃÄHOSTDIR
       ÀÄSCRIPTS


The QMODEM\DOWNLOAD directory will be used to store all uploaded and downloaded
file.  A separate directory is optional, but having it will make it easier for
you to see what you have transferred.

The QMODEM\HOSTDIR is similar to the QMODEM\DOWNLOAD directory, but is used by
the internal Host mode of Qmodem.  Callers to the HOST will be restricted to
this directory.

The QMODEM\SCRIPTS directory is used for script file storage.   Keeping scripts
in a dedicated directory makes script maintenance easier.  Copy all .SCR files
from the distribution disks to this directory.



Getting Help when you need it

Qmodem features context-sensitive help.  As the name suggests, relevant help
information is available for any command as you execute it, just by pressing the
F1 Help Key.

For example... You have the Alt-K window open and pressed F1.  The help window
would look like this:





























                                                               Qmodem SST     11




ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Change COM Port (Alt-K) ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³                                                                              ³
³ Qmodem can immediately switch between any one of eight communication ports   ³
³ on computers so equipped.  The standard COM1 and COM2 ports are Qmodem       ³
³ defaults; port definitions beyond COM2 must be specified with the Alt-N/M/P  ³
³ configuration menu.                                                          ³
³                                                                              ³
³ If you have defined additional COM ports, your menu may look something like  ³
³ this:                                                                        ³
³                                                                              ³
³                    ÕÍÍÍÍÍÍÍÍÍ Set COM Port ÍÍÍÍÍÍÍÍÍÍ¸                       ³
³                    ³ Active COM Port is COM1         ³                       ³
³                    ³                                 ³                       ³
³                    ³ 1  COM1  Base(03F8) Irq(04)     ³                       ³
³                    ³ 2  COM2  Base(02F8) Irq(03)     ³                       ³
³                    ³ 3  COM3  Base(03E8) Irq(04)     ³                       ³
³                    ³                                 ³                       ³
³                    ³ Your choice : _                 ³                       ³
³                    ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾                       ³
³                                                                              ³
³ To select a new serial port, type the desired number from the displayed      ³
³ list.                                                                        ³
³                                                                              ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
°°°°°°°°°°°°°°° F1-Topic Index    AltF1-Previous Topic   ESC-Exit °°°°°°°°°°°°°°


Now, if this isn't what you were looking for, or wanted to get a list of Help
Topics, you just press F1 again.  The Topic Index contains all of the major Alt-
commands, and some of the common procedures you might  need.  It may look
something link this:




























12   The Forbin Project, Inc.




ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Topics ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ þ Help with ONLINE HELP       þ        Function Keys (Alt-J)                 ³
³ þ Moving around in the INDEX  þ        Hang Up (Alt-H)                       ³
³ þ Dialing another System      þ        Host Mode (Alt-5)                     ³
³ ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ        Invoice for Ordering (Alt-I)          ³
³ 8th Bit Toggle (Alt-8)                 Log File Toggle (Alt-0)               ³
³ Adding Linefeeds (Shift-Tab)           Printer Echo Toggle (Alt-9)           ³
³ ANSI Music Toggle (Alt-M)              Screen Dump (Alt-T)                   ³
³ Backspace <> DEL Toggle (Alt-1)        Script File Execution (Alt-F)         ³
³ Batch Entry Window (BEW)               Script Parameters (Alt-F)             ³
³ Beeps & Bells Toggle (Alt-B)           Script QuickLearn (Alt-Q)             ³
³ Capture File Toggle (^Home)            Scroll Back (Ctrl-UpArrow)            ³
³ Change COM Port (Alt-K)                Scroll Back Toggle (Alt-U)            ³
³ Change Directory (Alt-O)               Send BREAK Signal (^End)              ³
³ Change Drive (Alt-L)                   Setup - The top menu (Alt-N)          ³
³ Clear Screen (Alt-C)                   Split Screen Mode (Alt-S)             ³
³ Communication Parameters (Alt-P)       Status Line Info Toggle (Alt-Enter)   ³
³ Delete a File (Alt-Y)                  Status Line Toggle (Alt-Minus)        ³
³ Dialing Directory (Alt-D)              Terminal Emulation (Alt-G)            ³
³ Directory Display (Alt-W)              Translate Tables (Alt-A)              ³
³ Doorway Keyboard Emulation (Alt-Equal) Upload Protocols (PgUp)               ³
³ Dos Shell (Alt-R)                      Video 25-Line Mode (Alt-2)            ³
³ Download Protocols (PgDn)              Video 43/50-Line mode (Alt-4)         ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ   for more Í¾
°°°°°°°°°°°°°°° F1-Topic Index    AltF1-Previous Topic   ESC-Exit °°°°°°°°°°°°°°


From here, you can jump over to help on other commands, or get more help on how
the Help System works.   Help remembers where you have been,  so you can retrace
your steps backwards by pressing Alt-F1 back to the original screen.

The online help is not all-inclusive, which is why you are reading this
paragraph.  Although the context-sensitive help is as detailed as possible, it
still is no substitute for this documentation.

Summary command help is available from the HOME window by pressing the F1 key,
followed by the desired command key combination.  When the F1 key is pressed,
the status line changes to the following display:


°°°°°°°°°° Select a Command    F1-Help    ESC-Return to TERMINAL Mode °°°°°°°°°°


For example, to get summary help for the Translate Table command (Alt-A), press
Alt-A, and the Translate Table summary help window will be displayed.

If you pressed F1 by mistake, press ESC to return to the previous Status Line.

NOTE: Pressing ESC will exit 99.9% of all windows and Qmodem functions
      without making any changes.



Upgrading from a previous release

Please refer to the file README.1ST on the first disk.  This contains specific
instructions for upgrading from previous releases of Qmodem.


                                                               Qmodem SST     13





Command Line Parameters

Certain Qmodem features are (out of necessity) implemented via command line
parameters and have no terminal mode or script command equivalents.  Command
line parameters are not case sensitive and may be specified in any order.

The following DOS command-line parameters are valid when starting Qmodem:

             /HOST  Will invoke the Host Mode immediately after startup.  This
                    option can be used to start an unattended Host system as
                    soon as the machine is booted, by adding the Qmodem start
                    command to your AUTOEXEC.BAT file.

     /S=SCRIPT.SCR  Autoexec Script: the Qmodem script file to be executed
                    immediately upon startup.  The script file must be located
                    in the script directory as specified in Alt-N/D/S or in
                    the current directory if the Alt-N/D/S field is blank.

            /STATS  Shows the technical information while Qmodem is loading.
                    Such things as: Number of Scroll-back lines, UART detected
                    and so on.

         /REGISTER  Can also be specified without the leading '/                                                               /                                                               /' character.
                    This invokes the internal Registration routine to make the
                    ShareWare version a Fully Registered version.

       /VGA=[mode]  Allows users of VGA and EGA cards to switch into a non-
                    standard video mode at start-up.  As long as your video
                    card allows setting the AL register to the desired mode,
                    this will do the trick.

   /VEGAVGA=[mode]  An Option Specific to the VEGA VGA cards from Video-7 Inc.
                    Allows setting an alternate text mode (like 132x43) from
                    the command line.  This is different from the normal /VGA=
                    command because the Video Seven boards have to load the
                    registers in a non-standard way.

                /R  This allows you to restart Qmodem without being prompted
                    to send the modem init string if you are already online.



The Status Line
While in terminal mode, Qmodem displays many of its operational settings in the
Status Line at the bottom of the screen:


   1        2         3          4       5    /-------- 6 --------\      7
  ANSI   Offline 38400 8N1  [Home]=Menu   FDX 8 LF X B M CP LG  PR  21:25:49


NOTE: Some of the special characters used in the status line are unprintable
      and may cause erratic printer behavior. These characters were changed
      to insure proper printing.

The status line is divided into the following areas:


14   The Forbin Project, Inc.




Area 1:The terminal emulation in effect.  In the above example, ANSI emulation
       is active.

Area 2:The Online/Offline indicator.  When connected to another computer, the
       word "Online"  will be displayed in this area.  When Qmodem is first
       started, this indicator should read "Offline".  It could also display
       either "DOORWAY" or "doorway" if the Alt-= toggle is set ON.  The upper
       case Doorway means you are Online, while lower case means you are
       Offline.

Area 3:The current communication parameters: Baud Rate, Data Bits, Parity, and
       Stop Bits.  These values will change to reflect changes made with the
       Alt-P command, or to reflect the values defined in the Dialing directory
       for each number.

Area 4:A short reminder to press the Home key to view the Main Help Menu, which
       shows all available commands.  Summary help on any Qmodem command may be
       obtained directly from the Main Menu as well.

Area 5:The current Duplex (a.k.a. Echo) state.  FDX stands for Full Duplex and
       HDX stands for Half Duplex.  Refer to the Alt-E command for a full
       explanation of Duplex mode.

Area 6:The current state of Qmodem Toggles.  There are 9 toggles, from left to
       right:

     8  Hi-bit strip toggle.  A "7" means that the high bits are stripped, and
        an "8" means all bits are used.

     LF Add Linefeed Toggle.  If "LF", a Linefeed will be added to all incoming
        Carriage Returns.  If disabled, this area will be blank.

     X  XON/XOFF toggle.  If "X", Xon/Xoff flow control is active.  If this
        area is blank, Xon/Xoff flow control is ignored by Qmodem.

     B  Beeps & Bells Toggle (Shown on-screen as a single musical note).  If
        present, indicates that Qmodem will generate sounds on the PC's speaker
        when specific conditions are met.  If this is blank, Qmodem produces no
        sounds.

     M  Music Toggle (Shown on-screen as a double musical note).  If present,
        indicates that Qmodem will play ANSI Music if found.  If blank, Qmodem
        will not play ANSI music.

     CP Capture Buffer Toggle.  If present, indicates that text is being
        captured to a file. If blank, incoming text is not captured.

     LG Session Log Toggle.  If present, indicates that the Session LOG is
        active.  If blank, the session LOG is not active.

     ^  Scroll-back Toggle (Shown on-screen by an up-arrow).  If present,
        Qmodem is capturing incoming data to the scroll-back buffer.  If blank,
        the scroll-back feature is not active.

     PR Printer Toggle.  If present, screen text is also sent to the printer.




                                                               Qmodem SST     15



Area 7:The last item on the Status Line is the System Clock.  When ONLINE, the
       clock displays Elapsed-Time (the duration of the call).  When OFFLINE,
       the clock displays the time-of-day.



The HOME Menu

Pressing the Home key displays the following screen which describes all
available commands :


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ COMMAND MENU ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ BEFORE ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ    ÄÄÄÄÄÄÄÄ TOGGLES ÄÄÄÄÄÄÄÄÄ ³
³ Alt-D  Phone Book        Alt-G  Term Emulation    Alt-0  Session Log         ³
³ ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ DURING ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ    Alt-1  Backspace DEL/^H    ³
³ Alt-C  Clear Screen      ^Home  Capture File      Alt-2  80x25 (EGA/VGA)     ³
³ Alt-F  Execute Script    ^End   Send BREAK        Alt-3  Debug Status Info   ³
³ Alt-Q  QuickLearn         PgUp  Upload Files      Alt-4  80x43/50 (EGA/VGA)  ³
³ Alt-S  Split Screen       PgDn  Download Files    Alt-5  Host Mode           ³
³ Alt-T  Screen Dump                                Alt-6  Batch Entry Window  ³
³       Scroll Back                                Alt-8  Hi-Bit Strip        ³
³ ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ AFTER ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ    Alt-9  Printer Echo        ³
³ Alt-H  Hangup Modem      Alt-X  Exit Qmodem       Alt-B  Beeps & Bells       ³
³                                                   Alt-E  Half/Full Duplex    ³
³ ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ SETUP ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ    Alt-I  Order Information   ³
³ Alt-A  Translate Table   Alt-N  Configuration     Alt-M  ANSI Music          ³
³ Alt-J  Function Keys     Alt-P  Change Baud Rate  Alt-U  Scroll-back Record  ³
³ Alt-K  Change COM Port                            Alt-Z  XON/XOFF Flow Ctrl  ³
³                                                   Alt-=  DoorWay Mode        ³
³ ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ DOS ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ    Alt--  Status Lines        ³
³ Alt-L  Change Drive      Alt-V  View/Edit File    ShTab  CR/CRLF Mode        ³
³ Alt-O  Change Directory  Alt-W  List Directory    AltÄÙ Status Line Info    ³
³ Alt-R  DOS Shell         Alt-Y  Delete File                                  ³
³                                                                              ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍ Qmodem SST Version 4.2 Production Compiled MM/DD/YY ÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
°°°°°°°°°° Select a Command    F1-Help    ESC-Return to TERMINAL Mode °°°°°°°°°°


The Home Menu is divided into the following areas:

  BEFORE  Commands you are likely to use before dialing a system
          such as setting terminal emulation and getting into the
          dialing directory itself.

  DURING  Commands you are likely to use while online.

   AFTER  Commands used to end your online session or exit.

   SETUP  Commands used to change operational parameters.

     DOS  Commands which interact with your computer, rather than
          with the computer you are calling.

 TOGGLES  Commands that activate or deactivate certain features.
          Operating these toggles is usually done by pressing the
          corresponding key combination.



16   The Forbin Project, Inc.



Notice that the Terminal Mode status line changes when the  Home Menu is
displayed (see above example)  As the Home status line indicates, you can get
summary help for any command by pressing [F1], then the desired command key
combination.  Pressing [ESC] returns you to terminal mode.

Qmodem updates or replaces the Status Line to reflect the current environment,
the function being performed, or the command being executed.  Check the Status
Line often, it may help you get out of trouble if and when you get stuck!




















































                                                               Qmodem SST     17



QINSTALL
Starting Qmodem for the First Time
If  this is your first time, you need to run the program QINSTALL before you can
run Qmodem.  This is the installation program that fine tunes Qmodem.
Qinstall is started by typing Qinstall and pressing the Enter key from the DOS
prompt.

After the Qinstall opening screen, you are presented with the Qmodem
Installation Part 1 screen:


                           QMODEM INSTALLATION PART 1

The file QMODEM.CNF was not found in the current directory or the directory
pointed to by the Environment variable "QMODEM=",  so it is assumed this is
a new installation.   A few questions will be asked to determine how Qmodem
should be setup for you.  Please follow the  directions and  this will only
take a few minutes.
_______________________________________________________________________________

Display adapter detected : VGA
Do you have a Color monitor connected ? [Y/N]


Qinstall then examines your hardware and tries to determine which video card you
are using.  In the previous example, a VGA card was detected.  Other
possibilities include Monochrome (which includes Hercules cards), CGA, EGA and
MCGA.  If Qinstall cannot figure out your type of adapter, we sure would like to
hear from you about it.

The next question asks if you have a color monitor attached to your video card.
Monochrome displays may be attached to some color adapters.  If this is your
case, reply no to this question.

Setup questions are based on the video adapter in your system.  The previous
example applied to EGA/VGA/MCGA adapters. If your system is equipped with a CGA
or Monochrome display, the prompts would have changed:


Display adapter detected : CGA

Press any key to test for video snow > _
Did your screen look fuzzy ? [Y/N] _

Do you have a Color monitor connected ? [Y/N] _


Early IBM CGA and cheap clones suffer from snow and flicker when display memory
is accessed.  When you to press a key, Qinstall will attempt to generate the
snow or flicker on your display.  If irregular, fuzzy patterns or dots appeared
on your screen, reply Y to the Did your screen look fuzzy question.

Monochrome setups are the easiest.   Qinstall  simply asks you to press any key
to continue.

NOTE: If this is an upgrade from a previous release, Qmodem will read the
      existing QMODEM.CNF and skip these questions.



18   The Forbin Project, Inc.





Configuration
Configuring Qmodem is simple, whether you are installing Qmodem for the first
time or upgrading from a previous release.  Seasoned Qmodem veterans should read
the section on Menu Navigation and Upgrading from a previous release.  First
time users should go through the Installation Section of the manual and ignore
the Upgrade section.



QINSTALL Menu Navigation
The Qinstall  Setup Menu will be automatically displayed the first time Qmodem
is started.


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Setup Menu ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Video      Modem    Dirs     Host     Protocols     Files    Options    Exit ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
                            QMODEM INSTALLATION PART 2

  The window above is the "Alt-N Setup Menu".  With it, you can customize
  almost every part of Qmodem.  Go through all of the options now to finish
  the installation procedure.  When you are through, select Exit/Save to
  write out the new configuration file.

        Press ENTER to Edit the selected option or open a SubMenu.
        Press ESC to abort the changes made or close the SubMenu.

  ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
  º Option A          º
  º Option B   ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ Selections that are followed by the
  º ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»        character have SubMenus below them.
  º º Sub Option B1       º
  ÈÍº Sub Option B2       º
    º Sub Menu Below     º
    ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
                          ÚÄ The Status Line will always give you help on
                          ³  the option you are changing.

 Change the way Qmodem looks to you


TIP: Qinstall can be started from inside of Qmodem with the Alt-N command.


The top window is the Alt-N Setup window, which we will refer to as Setup from
here on.  Since this is a new installation, it is invoked automatically.  The
accompanying text explains how to navigate through the Setup Menus.

NOTE: This text is only shown for first-time  installation.  Subsequent
      calls to Setup only display the Menu Window.  As with Qmodem, you have
      the complete Online Help system by pressing the F1 key!

Items may be selected with two different methods:

  1. By pressing the highlighted letter in the desired menu entry, or



                                                               Qmodem SST     19



  2. By moving the selection bar to the desired item and pressing ENTER.  To
     move the selection bar, use the cursor keys.

Menu entries followed by a down-pointing arrow have one or more additional menu
levels.  When such an entry is selected, another menu will be displayed from
which additional entries or parameters are configured.  Since all Main Setup
Window entries have associated menus, the arrows are omitted.

While in Setup, the status line always displays a brief description of the
currently selected item.  If additional information is needed, press the F1 key
for detailed online help.

While changing to an item, pressing ESC restores its original value.  To save
the change, press ENTER.  Changes to the Setup are not saved automatically; when
done you must use the Exit/Save Top Menu Option to save all changes in the
QMODEM.CNF file.



First Time Setup
Now that you can navigate through Setup menus, let's start with the various
setup tasks from left to right.  Colors are first...


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Setup Menu ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Video      Modem    Dirs     Host     Protocols     Files    Options    Exit ³
ÔÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
 ³ Custom colors    ³
 ³ Blue shades       ³
 ³ Purple shades     ³
 ³ Red shades        ³
 ³ Monochrome shades ³
 ³ LCD Laptop shades ³
 ³ Toggles          ³
 ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾




Alt-N/V  Video
The Video Setup option is used to configure Qmodem screen colors and toggles.
You may select one of 5 pre-defined color combinations, customize the colors to
your liking and set video related Toggles.

The Monochrome and LCD Laptop entries are intended for standard monochrome
displays and Laptop Liquid Crystal Displays (LCD) which can only display shades
of gray.

NOTE: Colors are a cosmetic feature and have no effect on Qmodem's
      operation. First-time users should select one of the predefined color
      combinations and concentrate on other sections of the Qmodem setup.
      Colors may be customized easily after all other operational
      parameters.




Alt-N/V/C Custom Colors
Selecting the Custom Colors options yields the following menu:

20   The Forbin Project, Inc.





ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Setup Menu ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Video      Modem    Dirs     Host     Protocols     Files    Options    Exit ³
ÔÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
 ³ Custom colors    ³
 ³ÕÍÍ Pick a Field to Color ÍÍÍ¸
 ³³ Pulldown normal text       ³
 ³³ Pulldown first letter      ³
 ³³ Pulldown selection bar     ³
 ³³ Pulldown window border     ³
 ³³ Pulldown edit field        ³
 Ô³ Window border              ³
  ³ Window primary text        ³
  ³ Window secondary text      ³
  ³ Window Scroll Bar          ³
  ³ Screen border              ³
  ³ Screen text                ³
  ³ Information text           ³
  ³ Status Line primary        ³
  ³ Status Line secondary      ³
  ³ Help border                ³
  ³ Help normal text           ³
  ³ Help selected xref         ³
  ³ Help unselected xref       ³
  ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍ   for more Í¾


This is a  Pick List of all the possible fields that can be customized.  You can
scroll through the list in several way with the Arrow keys being the easiest.
When one of the screen elements is selected, the Qmodem color selection screen
is displayed:




























                                                               Qmodem SST     21




ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Setup Menu ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Video      Modem    Dirs     Host     Protocols     Files    Options    Exit ³
ÔÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÕÍÍÍÍÍÍÍÍÍÍÍÍÍ Sample Screen ÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
 ³ Custom colors    ³              ³ Option 1    Option 2    Option 3         ³
 ³ BÕÍÍ Pulldown normal text ÍÍ¸    ³ ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸ÕÍÍÍ Help Window ÍÍÍÍ¸ ³
 ³ P³                          ³    ³ ³Field in Edit°°°³³ Normal text color  ³ ³
 ³ R³  þ  þ  þ  þ  þ  þ  þ  þ  ³    ³ ³Not in Edit°°°°°³³ Selected Xref      ³ ³
 ³ M³  þ  þ  þ  þ  þ  þ  þ  þ  ³    ³ ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾³ Unselected Xref    ³ ³
 ³ L³  þ  þ  þ  þ  þ  þ  þ  þ  ³    ³                   ³ Highlite text      ³ ³
 ³ T³  þ  þ  þ  þ  þ  þ  þ  þ  ³    ³                   ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾ ³
 ÔÍÍ³  þ  þ  þ  þ  þ  þ  þ  þ  ³    ³AT                                        ³
    ³  þ  þ  þ  þ  þ  þ  þ  þ  ³    ³OK            ÕÍÍÍÍ Frame Color ÍÍÍÍÍ¸    ³
    ³  þ  þ  þ  þ  þ  þ  þ  þ  ³    ³              ³Primary window text   ³    ³
    ³  þ  þ  þ  þ  þ  þ  þ  þ  ³    ³              ³Secondary text        ³    ³
    ³  þ  þ  þ  þ  þ  þ  þ  þ  ³    ³              ³Scroll Bar text       ³    ³
    ³ÚÄÄÄ¿þ  þ  þ  þ  þ  þ  þ  ³    ³              ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾    ³
    ³³ þ ³þ  þ  þ  þ  þ  þ  þ  ³    ³                                          ³
    ³ÀÄÄÄÙþ  þ  þ  þ  þ  þ  þ  ³    ³    ÕÍÍÍÍÍÍÍ Full Screen Edit ÍÍÍÍÍÍÍ¸    ³
    ³  þ  þ  þ  þ  þ  þ  þ  þ  ³    ³    ³ Normal Text                    ³    ³
    ³  þ  þ  þ  þ  þ  þ  þ  þ  ³    ³    ³ Marked Text                    ³    ³
    ³  þ  þ  þ  þ  þ  þ  þ  þ  ³    ³    ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾    ³
    ³  þ  þ  þ  þ  þ  þ  þ  þ  ³    ³Information message text                  ³
    ³                          ³    ³°°°° Status Line   Primary  Secondary °°°°³
    ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾    ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
 ARROWS - Move Indicator   ENTER-Accepts   ESC-Exit


At the left of the screen is a color chart showing all possible foreground and
background color combinations.  To the right is a sample of all the windows that
Qmodem and Qinstall will display.  The top of the left  window tells you which
selection you are changing.  In the example, the Pulldown Normal Text is being
modified.

To select a color, move the square color selector box in the left window with
the arrow keys.  The change is immediately reflected in the Qmodem mini-screen
on the right side of the display.

Pressing ESC restores the item's original color.  To confirm the color change,
press ENTER.   All color changes will take effect immediately.

NOTE: Color changes must be saved explicitly via the Alt-N Exit/Save menu
      option.  If the new color settings are not saved, the last color setup
      will be restored the next time Qmodem is started.




Alt-N/V/T  Toggles
The Toggles menu lets you set such things as how characters should be displayed,
how windows in Qmodem should be displayed, and how to handle certain types of
incoming data.    The menu looks like this:








22   The Forbin Project, Inc.




ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Setup Menu ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Video      Modem    Dirs     Host     Protocols     Files    Options    Exit ³
ÔÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
 ³ Custom colors    ³
 ³ Blue shades       ³
 ³ Purple shades     ³
 ³ Red shades        ³
 ³ Monochrome shades ³
 ³ LCD Laptop shades ³
 ³ Toggles          ³
 ÔÍÍÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
    ³ BIOS video         OFF ³
    ³ Linefeed after CR  OFF ³
    ³ Snow checking      OFF ³
    ³ Growing windows    OFF ³
    ³ STatus line        ON  ³
    ³ Destructive bksp   OFF ³
    ³ LIne Wrap          ON  ³
    ³ Video Restore      OFF ³
    ³ Jump Scroll        ON  ³
    ³ Emulation         ANSI ³
    ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


Alt-N/V/T/B      BIOS Video

  When OFF, Qmodem writes directly to screen memory, which results in extremely
  fast screen displays.  When ON, all screen displays are performed via calls
  to the system's ROM BIOS,  and screen displays are much slower.  BIOS Video
  mode must be ON when Qmodem operates under multi-tasking software such as
  DoubleDOS or Windows 3.0.

NOTE: This only applies to the text displayed that is received from the
      serial port.  Qinstall and most windows in Qmodem still write directly
      to video memory.


TIP: Qmodem is fully DESQview aware.  When running Qmodem under DESQview,
     set BIOS Video mode to NO.  With other multi-tasking programs, you
     should experiment with this setting to determine the best operating
     mode.


Alt-N/V/T/L      Linefeed after CR


  Setting this ON causes Qmodem to add a linefeed (LF) character after every
  carriage return (CR) character.  This may be needed if text lines seem to
  overwrite the previous line on the screen.   This toggle can be changed with
  the Shift-Tab command.


Alt-N/V/T/S      Snow Checking






                                                               Qmodem SST     23



  Older CGA display adapters (and some CGA clones)  may exhibit "snow" when
  video memory is accessed.  If this is the case, set this toggle to ON.
  Qmodem will use a different memory access method which may help alleviate the
  problem.  This toggle is not used if your system is equipped with an MDA,
  EGA, or VGA display.

TIP: While running under DESQview, you can set this to OFF for slightly
     improved display speed.



Alt-N/V/T/G      Growing Windows

  Controls the method used to display windows on screen.  When ON, windows will
  grow or explode onto the screen.  When OFF, windows will pop onto the screen
  instantly.


Alt-N/V/T/T      Status Line

  This toggle controls displaying of the status line  (the last line of the
  physical screen).  When OFF, the Qmodem status line is not displayed and the
  last screen line is available for incoming text display.  When ON (the
  default), the status line is used to display the status of the Terminal mode
  and options of various command windows.

NOTE: The Screen will clear when this is toggled ON and OFF.


Alt-N/V/T/D      Destructive Backspace

  This controls whether or not the character to the left of the cursor is
  erased when a Backspace character (^H or DEL) is received.  When ON, the
  character is erased before the cursor is moved to the left.  When OFF, the
  cursor moves leaving the character to the left untouched.


Alt-N/V/T/I      Line Wrap

  This controls how the cursor reacts when it writes a character in the last
  column on the screen (usually column 80).  When set ON, the cursor moves the
  next line down, performing a Line Feed if the cursor was on the last line on
  the screen.  When set OFF, the cursor writes the character in the last
  column, but does not advance to the next line.
















24   The Forbin Project, Inc.



Alt-N/V/T/V      Video Restore

  When set ON, Qmodem will attempt to restore the original mode of your video
  card to the settings prior to starting Qmodem.  If you want to leave the last
  video mode that Qmodem is using active upon exit, set this to OFF.


Alt-N/V/T/J      Jump Scroll

  This allow changing the method used to scroll the screen.  If you have a CGA
  card (the ones that cause snow), you may want to set this OFF to see if the
  screen scrolls more smoothly.  The default mode is ON to be compatible with
  the previous releases of Qmodem.


Alt-N/V/T/E      Emulation

  The default terminal emulation mode used by Qmodem.  When the cursor is
  located in this field, pressing ENTER presents a submenu with the list of
  available emulations.  Use the up and down arrow keys to select the emulation
  you need and press ENTER.



Alt-N/M  Modem
Modem-dependent  settings affect the interaction between Qmodem, your computer,
and your modem.  If you use a 2400bps Hayes Smartmodem (or compatible) attached
to COM1, most of Qmodem's default modem parameters are correct.  However, the
modem setup must be reviewed to insure that specific parameters are set
properly.

Selecting the Alt-N Modem option yields the following menu:


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Setup Menu ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Video      Modem    Dirs     Host     Protocols     Files    Options    Exit ³
ÔÍÍÍÍÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
     ³ Communication Parameters  ³
     ³ Modem Commands            ³
     ³ Port Addresses            ³
     ³ Quick Modem Config!       ³
     ³ Toggles                   ³
     ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

















                                                               Qmodem SST     25



Alt-N/M/C  Communications Parameters
These hardware parameters control the operation of the communication port and
its interaction with the modem.  When the Communication parameters option is
selected, the following menu is displayed:


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Setup Menu ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Video      Modem    Dirs     Host     Protocols     Files    Options    Exit ³
ÔÍÍÍÍÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
     ³ Communication Parameters  ³
     ³ MoÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
     ³ Po³ A - Default baud rate            2400           ³
     ³ Qu³ B - Default data bits            8              ³
     ³ To³ C - Default parity               None           ³
     ÔÍÍÍ³ D - Default stop bits            1              ³
         ³ E - Command before baud change   °°°°°°°°°°°°°° ³
         ³ F - Command after baud change    °°°°°°°°°°°°°° ³
         ³ G - Cycle delay                  10             ³
         ³ H - Timeout delay                60             ³
         ³ I - Modem command delay          10             ³
         ³ J - Serial port                  1              ³
         ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


Alt-N/M/C/A      Default Baud Rate

  The Baud Rate is the speed at which the COM port operates and should match
  the modem's speed.  Supported speeds are 110, 300, 1200, 2400, 4800, 9600,
  19200, 38400, 57600 and 115200.  The default baud rate is 2400.

NOTE: With many error-correcting and high-speed  modems, the COM speed can
      be set higher than the modem's nominal communications speed.  For
      example, the USR Courier HST modem, rated at 9600 baud, supports a COM
      speed of 38400 baud.  Consult your modem manual for additional
      information on supported COM speeds.



Alt-N/M/C/B      Default Data Bits

  Characters transmitted over phone lines are made up of data bits.  For
  systems which support text and binary program file transfers (IE., most PC-
  based BBS systems), 8 data bits are required.  When communicating with
  mainframe or minicomputer-based systems, 7 data bits is often used.
  Supported settings are 7 and 8.  This setting must match that of the software
  operating on the remote computer.


Alt-N/M/C/C      Default Parity

  Parity is used to insure the validity of the data being transmitted and
  received.  Parity values are None, Odd, Even, Mark and Space.  This value
  must match that used by the computer being called.  Most BBS's use  None (no
  parity), the default value.


Alt-N/M/C/D      Default Stop Bits



26   The Forbin Project, Inc.



  Stop bits are generated by the UART to isolate transmitted characters.  The
  majority of computer systems require 1 stop bit, the default value.
  Supported values include 1 and 2.  As with other parameters, this value must
  match the other computer's setting.


Alt-N/M/C/E      Command Before Baud Change

  This string is sent to the modem before the serial port speed is changed.
  The default value is blank.  Non-standard modems may require a different
  value.


Alt-N/M/C/F      Command After Baud Change

  This string is sent to the modem after the serial port speed is changed.  The
  default value is blank.  Non-standard modems may require a different value.


Alt-N/M/C/G      Cycle Delay

  The Cycle Delay is the number of seconds Qmodem waits after an unsuccessful
  dial (IE., a BUSY signal) before trying the next number in the dialing queue
  (or the same number again).   The default value is 10 seconds.


Alt-N/M/C/H      Timeout Delay

  The Timeout Delay is the number of seconds Qmodem waits for a connection
  after dialing a number.  When this period has expired, Qmodem will instruct
  the modem to hang up.  The default value is 60 seconds.

TIP: Most modems feature an internal timeout delay.  When dialing, the
     shortest delay will prevail.  Make sure that your modem's internal
     timeout value is at least equal to the Qmodem  setting.  In Hayes and
     compatible modems, the command ATS7=60 will set the modem's internal
     delay to 60 seconds.  Increasing the modem's own timeout value allows
     total control over the dialing process.






















                                                               Qmodem SST     27



Alt-N/M/C/I      Modem Command delay

  This is the delay, in milliseconds (1000 = 1 second) inserted between
  characters sent to the modem while it is OFFLINE.  The default value is 0.
  Some high-speed modems may require a non-zero value if commands are not
  recognized, or if the modem does not return an OK acknowledgment.  The most
  common symptoms are the modem's lack of an OK response when first
  initialized, or the modem's inability to dial.


Alt-N/M/C/J      Serial Port

  This is the port number (1-8) to which the modem is attached.  The default is
  port 1.  For port addresses higher than 2 be sure to configure the Base
  address and IRQ in the Alt-N/M/P menu.

TIP: The default Speed, Parity, Data bits and Stop bits values are not
     fixed.  Defaults can be overridden in each dialing directory entry to
     match the settings of the remote computer.




Alt-N/M/M  Modem Commands
Modem commands define the text of messages sent to the modem to cause a specific
action (IE., dial, hang up), or received from the modem to acknowledge a command
(IE., OK, ERROR), or reflect a specific condition (IE., BUSY, CONNECT, NO
CARRIER).
When the Modem Commands option is selected, the following menu is displayed:


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Setup Menu ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Video      Modem    Dirs     Host     Protocols     Files    Options    Exit ³
ÔÍÍÍÍÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
     ³ Communication Parameters  ³
     ³ Modem Commands            ³
     ³ PoÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
     ³ Qu³ Initialization Command    ATE1Q0X1V1S7=60^M°°°°°°° ³
     ³ To³ Prefix Dial Command       ATDT°°°°°°°°°°           ³
     ÔÍÍÍ³ Suffix Dial Command       ^M°°°°°°°°°°°°           ³
         ³ Connect Message           CONNECT°°°°°°°           ³
         ³ 1st Error Message         NO CARRIER°°°°           ³
         ³ 2nd Error Message         BUSY°°°°°°°°°°           ³
         ³ 3rd Error Message         NO DIAL TONE°°           ³
         ³ 4th Error Message         VOICE°°°°°°°°°           ³
         ³ Abort Dial Command        ^M°°°°°°°°°°°°           ³
         ³ Hangup Command            ^~^~^~+++^~^~^~ATH^M°°   ³
         ³ Redial Cancel Text        RING°°°°°°°°°°           ³
         ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾











28   The Forbin Project, Inc.



Alt-N/M/M/I      Initialization Command

  Default:     AT E1 Q0 M1 X1 V1 S7=60^M

  This command resets Hayes and compatible modems to their standard operating
  parameters.  This command may vary depending on the modem being used; consult
  the modem manual.


Alt-N/M/M/P      Prefix Dial Command

  Default:     ATDT

  This command is used to tone-dial a number on Hayes and compatible modems.
  It is sent to the modem immediately before the telephone number to be dialed.
  For pulse-dialing, change this to ATDP.

  The dialing commands may vary depending on your modem brand.  Consult the
  modem manual for additional information.  If your modem requires a 150
  millisecond BREAK signal for dialing,  change this command to the word BREAK.

TIP: Adding *70 after the ATDT dial command can be used to disable call-
     waiting on some tone-dialing phone systems. Adding 1170 after the ATDP
     dial command can be used to disable call-waiting on some pulse-dialing
     phone systems.  Check with your phone company to see if these features
     are supported.



Alt-N/M/M/S      Suffix Dial Command

  Default:     ^M

  This string immediately follows the number to be dialed.  Should your modem
  require a different End-of-Command character, you should place it here.


Alt-N/M/M/C      Connect Message

  Default:     CONNECT

  The message returned by the modem when a successful connection has been
  established.  Most modems will also return the connect speed as part of the
  message, IE: CONNECT 2400.  Do not include a speed value as part of this
  message.  Doing so will prevent a connection if the baud rate is different
  from the one you entered.
Alt-N/M/M/1      Error Message 1
Alt-N/M/M/2      Error Message 2
Alt-N/M/M/3      Error Message 3
Alt-N/M/M/4      Error Message 4

  Defaults:    BUSY
          NO CARRIER
          NO DIAL TONE
          NO CONNECT

  These error messages are returned by the modem when the connection could not
  be established.  Your modem may return different messages; refer to the
  manual for additional information.

                                                               Qmodem SST     29




NOTE: Many modems can be set to return Numeric result codes rather than
      Verbose result codes.  .  Although either can be used, you should use
      the more descriptive verbose messages.  If the modem is set to return
      numeric codes,  Qmodem will not be able to determine the connect
      speed.



Alt-N/M/M/A      Abort Dial Command

  Default:     ^M

  This string will be sent to the modem when a dial request is to be cancelled
  (IE: pressing ESC from the dialing directory screen while dialing is in
  progress).  Most modems accept  ^M.  If the modem supports dropping DTR as a
  disconnect method,  the word DTR (Data Terminal Ready)should be entered in
  this field.  Consult the modem manual for information on this feature.


Alt-N/M/M/H      Hangup Command

  Default:     ^~^~^~+++^~^~^~ATH0^M

  This command will cause Hayes and compatible modem to hang up.  Each ^~ pair
  causes a 1/2-second delay.  In the example above, the +++ modem escape
  sequence is preceded and followed by a 1.5 second delay.  This delay,
  referred to as  escape guard time is required for the modem to recognize the
  escape sequence and switch to command mode.  The ATH0^M command then
  instructs the modem to go on-hook (hang up).

  For modems which recognize dropping of the DTR signal as a disconnect method,
  specify the word DTR in this field.  To hang up, Qmodem disables the DTR
  signal, pauses, and then re-establishes it.  This hardware-only method, if
  supported by your modem,  is far more reliable than using a modem software
  command which could easily fail (IE., because of line noise).  The reason
  the DTR method is not the default is, unfortunately, not all modems support
  DTR disconnect control.

  Specifying BREAK will send the modem BREAK signal for 150 milliseconds.  Some
  modems attached to PBX (Public Board eXchange, a.k.a. switchboard) require a
  BREAK in order to disconnect a call.


Alt-N/M/M/R      Redial Hangup Text

  Default:     RING

  This message text, when received, will cause Qmodem to stop dialing
  immediately.  If you are sharing a voice line with your modem, this allows
  you to answer the phone personally.  If your modem is connected to its own
  dedicated phone line, this field can be left blank.



Alt-N/M/P Port Addresses




30   The Forbin Project, Inc.



Port addresses are hardware-dependent values which define the computer's
communications ports.  Qmodem allows you to define up to eight communication
ports (COM1 through COM8).  Two COM ports (COM1 and COM2) are standard for most
IBM PC, XT, AT, PS/2 and compatible machines.  This does not mean that all
machines have both ports.  These are optional.  You still have to verify which
ports you have available.

NOTE: An internal modem take up a COM port.  If you have two ports in your
      machine (COM1 and COM2), you CANNOT set the internal modem to either
      COM1 or COM2 and expect it to work.  You should set the internal modem
      to the first available port.  (in this example, it should be
      configured for COM3)

      Because it is possible to install an internal modem or additional
      serial port so that it shares an IRQ with another device, you should
      declare all the installed serial ports in Qmodem.  This allows Qmodem
      to disable other ports that may conflict with the port you are trying
      to use.  It a port is disabled, it will be enabled if you exit Qmodem
      or select another port with Alt-K.









































                                                               Qmodem SST     31



When the Port Address option is selected, the following menu will be displayed:


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Setup Menu ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Video      Modem    Dirs     Host     Protocols     Files    Options    Exit ³
ÔÍÍÍÍÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
     ³ Communication Parameters  ³
     ³ Modem Commands            ³
     ³ Port Addresses            ³
     ³ QuÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸  ³
     ³ To³ A - COM1 Base  03F8 ³  ³
     ÔÍÍÍ³ B - COM2 Base  02F8 ³ÍÍ¾
         ³ C - COM3 Base  0000 ³
         ³ D - COM4 Base  0000 ³
         ³ E - COM5 Base  0000 ³
         ³ F - COM6 Base  0000 ³
         ³ G - COM7 Base  0000 ³
         ³ H - COM8 Base  0000 ³
         ³ I - COM1 IRQ   4    ³
         ³ J - COM2 IRQ   3    ³
         ³ K - COM3 IRQ   0    ³
         ³ L - COM4 IRQ   0    ³
         ³ M - COM5 IRQ   0    ³
         ³ N - COM6 IRQ   0    ³
         ³ O - COM7 IRQ   0    ³
         ³ P - COM8 IRQ   0    ³
         ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾



Alt-N/M/P/ A-H      COMx Base Address

  These are the computer's COM port hardware addresses.  Qmodem supports
  default assignments for two serial ports, COM1: and COM2:.  For PC/XT/AT and
  compatibles equipped with IBM-standard adapters, the port address and IRQ
  assignments need not be changed.

  Non-PS/2 computers can address COM3: through COM8:.  Internal modems usually
  have the following Base Address assignments:

            Port       Base    IRQ
           Number    Address
            COM3       3E8      4
            COM4       2E8      3


  Be sure to read your manual that comes with your internal modem to verify
  these setting.

  CAUTION:     If you intend to install an internal modem as COM3 or COM4,
          and it is going in a computer that is not EISA or MC bussed, then
          try to set the IRQ to a value other than 4 or 3.  On an AT, try 5
          or 2.  Not all internal modems allow you to change the IRQ and
          this may not apply to you.  If you cannot set an IRQ other than 4
          or 3, then be aware that Qmodem will disable COM1 or COM2 while
          you are using the modem.  (IE: if you have a serial Mouse on COM1
          and your internal modem is set for COM3, then the mouse will be
          disabled while in Qmodem.


32   The Forbin Project, Inc.



  IBM PS/2 computers also support COM3: through COM8: with the following
  assignments:

             Port      Base    IRQ
            Number   Address
             COM3      3220     3
             COM4      3228     3

             COM5      4220     3
             COM6      4228     3
             COM7      5220     3
             COM8      5228     3


NOTE: On non-PS/2 machines, port assignments above COM2 are non-standard.
      Refer to the adapter or internal modem's documentation for specific
      hardware information.


Alt-N/M/P/ I-P   COMx IRQ

  The IRQ (Interrupt ReQuest) value must be known for the serial ports to be
  accessed.  When specifying Base addresses for non-standard COM ports, you
  must also set the correct IRQ values.

  Failure to set the IRQ will prevent Qmodem from accessing the COM port and
  will make communications impossible.  (You also stand a good chance of
  locking up your computer!  Trust me, I've done it several times!)

  Refer to the previous example for setting up a PS/2 COM3: or COM4: board.



Alt-N/M/Q Quick Modem Config
This is probably the single most wanted feature in a communication program...  A
method to quickly configure your new modem to work!  It's not like the old days
where we had just a handful of modem commands and everybody knew them by heart.

Now we have High-Speed modems with things like MNP and V.32 and V.42 and Speed
Buffering and on and on and so forth.  Each modem maker that enhanced upon the
Hayes standard had to come up with their own new commands.  To add to the
confusion, some have the same command(s), but mean different things to different
modems!

Enter Quick Modem Config!  It takes the worry and confusion out of setting up
your complex modem.  Everything in the modem and Qmodem is setup all at once
with a minimum of user intervention.  Like the commercial said, "Set it, and
forget it."

The heart of Quick Modem Config (herein called QMC) is the QMODEM.MDF file.
This is the Modem Definition File that QMC uses to configure your modem and
Qmodem.  As new modems are added to the MDF file, we post the new version on our
BBS.

The QMC window looks something like this:





                                                               Qmodem SST     33




ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Setup Menu ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Video      Modem    Dirs     Host     Protocols     Files    Options    Exit ³
ÔÍÍÍÍÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
     ³ Communication Parameters  ³
     ³ Modem Commands            ³
     ³ Port Addresses            ³
     ³ Quick Modem Config!       ³
   ÕÍÍÍÍÍÍÍÍÍÍ Pick a modem to install ÍÍÍÍÍÍÍÍÍÍ¸
   ³ Anchor 2400i Internal Half-card             ³
   ³ ATI 2400etc (non V.42)                      ³
   ³ Cermetek INFO-MATE 212A                     ³
   ³ Everex 12e External (EV-936)                ³
   ³ Everex 24e External (EV-945)                ³
   ³ Everex Evercom 24+ MNP                      ³
   ³ Fastcomm FDX 2424 (MNP Class-5)             ³
   ³ Fastcomm FDX 2496                           ³
   ³ Fastcomm FDX 9696 (V.32 & MNP-5)            ³
   ³ Generic 1200 Baud Hayes clone               ³
   ³ Generic 1200 Baud Hayes clone (switchless)  ³
   ³ Generic 2400 baud Hayes clone               ³
   ³ Generic 2400 Baud Hayes clone (switchless)  ³
   ³ Hayes SmartModem 1200 External              ³
   ³ Hayes SmartModem 1200B Full Card Internal   ³
   ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ   for more Í¾


NOTE: Your list of modems may differ if Qmodem was bundled with a modem or
      was added to since this manual went to print.


This is another Pick List.  You move the Scrollbar to highlight your modem from
the list and press ENTER.  If your modem does not appear in the list, call us.
We may have added it to the MDF file and have it posted for download.  In the
meantime, you can probably use one of the Generic entries to get you going.

Depending on the modem, there are up to 4 different windows that may pop up
during the process.

     1.Speed Detection.
     2.Hardware Notes.
     3.Modem Init Commands.
     4.Additional Notes.

Just follow the directions in each window as it is displayed.

Ok, your modem is in the list, and you want to get going!  Let's say you have a
MultiTech MT224 EH7 external and have selected it.

The screen will look something like this:










34   The Forbin Project, Inc.




ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Setup Menu ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Video      Modem    Dirs     Host     Protocols     Files    Options    Exit ³
ÔÍÍÍÍÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
     ³ Communication Parameters  ³
     ³ Modem Commands            ³
     ³ Port Addresses            ³
     ³ Quick Modem Config!       ³
    ÕÍÍÍÍ Hardware notes for MultiTech MultiModem MT224EH7 (MNP 7) ÍÍÍÍÍ¸
    ³ Switch Settings on the Bottom of the modem:                       ³
    ³         4 Switch Bank 1 2 3 4                                     ³
    ³                       D U D D                                     ³
    ³         8 Switch Bank 1 2 3 4 5 6 7 8                             ³
    ³                       U U D U D U U D                             ³
    ³                                                                   ³
    ³ Jumpers that need to be changed -inside- the modem:               ³
    ³   CTS/RTS: toward the back of the modem.                          ³
    ³                    ( Tap any key to continue )                    ³
    ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


If you get a Hardware Notes window (like above), follow the directions.  Do not
skip any steps!  There is always a reason for moving jumpers or switches.

After you have done what is asked, just tap any key to continue.

The MultiTech then gets the next window:


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Setup Menu ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Video      Modem    Dirs     Host     Protocols     Files    Options    Exit ³
ÔÍÍÍÍÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
     ³ Communication Parameters  ³
     ³ Modem Commands            ³
     ³ Port Addresses            ³
     ³ Quick Modem Config!       ³
    ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Modem Init Commands being sent ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
    ³AT$A0&B0&BS0&C1$D0&D2$F1^M                                         ³
    ³AT&G0#L0$MI0&M0$R1&R1&S1^M                                         ³
    ³ATB1E1M1Q0R0V1X4&Q0^M                                              ³
    ³AT&E1&E4&E8&E10&E13&E15^M                                          ³
    ³AT$MB2400$SB19200$BA0&W0^M                                         ³
    ³Send these commands to the modem [Y/N] ? _                         ³
    ³                                                                   ³
    ³                                                                   ³
    ³                                                                   ³
    ³                                                                   ³
    ³                                                                   ³
    ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


The Modem Init Commands window contains a list of modem commands that to be sent
to the modem.  Just in case, there is a prompt to confirm the sending of these
commands.  99.9% of all users should answer Y to this prompt.  Besides, failure
to do so will not guarantee correct operation in Qmodem.





                                                               Qmodem SST     35



You should verity that the modem responds OK to each line that is displayed.
Like this:


    ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Modem Init Commands being sent ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
    ³AT$A0&B0&BS0&C1$D0&D2$F1                                           ³
    ³OK                                                                 ³
    ³AT&G0#L0$MI0&M0$R1&R1&S1                                           ³
    ³OK                                                                 ³
    ³ATB1E1M1Q0R0V1X4&Q0                                                ³
    ³OK                                                                 ³
    ³AT&E1&E4&E8&E10&E13&E15                                            ³
    ³OK                                                                 ³
    ³AT$MB2400$SB19200$BA0&W0                                           ³
    ³OK                                                                 ³
    ³                    ( Tap any key to continue )                    ³
    ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


And finally, the Additional Notes window:


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Setup Menu ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Video      Modem    Dirs     Host     Protocols     Files    Options    Exit ³
ÔÍÍÍÍÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
     ³ Communication Parameters  ³
     ³ Modem Commands            ³
     ³ Port Addresses            ³
     ³ Quick Modem Config!       ³
    ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Additional notes ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
    ³ The 224EH7 is now configured for 19200 baud operation.  Be sure   ³
    ³ to set all your dialing directory entries to 19200 to get the     ³
    ³ best speed on all calls.  Note: Data compression was enabled with ³
    ³ the &E15 command.  Be sure to read your modem manual and double-  ³
    ³ check the setup.  Remember to Exit/Save to save these changes!    ³
    ³                    ( Tap any key to continue )                    ³
    ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


This is a list of parting comments that are specific to your particular modem.
You should at least read it.  TA-DA!  Your modem and Qmodem are now set!

Alt-N/M/T Toggles
These Toggles are specific to modem operations.  The menu looks like this:
















36   The Forbin Project, Inc.




ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Setup Menu ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Video      Modem    Dirs     Host     Protocols     Files    Options    Exit ³
ÔÍÍÍÍÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
     ³ Communication Parameters  ³
     ³ Modem Commands            ³
     ³ Port Addresses            ³
     ³ Quick Modem Config!       ³
     ³ Toggles                   ³
     ÔÍÍÍÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
         ³ Xon/Xoff flow        ON  ³
         ³ CTS/RTS flow         ON  ³
         ³ CTS when Writing     OFF ³
         ³ FIFO during Shell    OFF ³
         ³ Lock DTE Baud Rate   ON  ³
         ³ High Speed Xmit      ON  ³
         ³ 16550 UART Enable    ON  ³
         ³ Init ignores CD      OFF ³
         ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾









































                                                               Qmodem SST     37



Alt-N/M/T/X      Xon/Xoff Flow Control

  Xon/Xoff is a software flow control protocol used during normal text and
  ASCII transmissions.  This toggle can also be changed from terminal mode with
  the Alt-Z command.

  XOFF and XON are  ^S (Ctrl-S) and ^Q (Ctrl-Q) characters, respectively.  Most
  BBS and mainframe systems use XOFF and XON as a method of pacing text data
  transmissions.  If the XON/XOFF toggle is ON,  Qmodem will send the XOFF
  character when its receive buffer is almost full, and will display the
  following message on the Status line:


             Buffer FULL - Keyboard Input Suspended - Please Wait


  As text is displayed, the receive buffer empties and can accept more data.
  Qmodem then sends the XON character to resume transmission and restores the
  normal status line.

NOTE: The XON/XOFF software flow control is not used during Binary file
      transfer protocols.



Alt-N/M/T/C      CTS/RTS Flow Control

  When set to ON, Qmodem implements hardware handshaking between the modem and
  computer.  This is required for high-speed and error-correcting modems.
  Since additional signals are required to implement hardware handshaking, make
  sure that your external modem cable (if any) supports the CTS and RTS signal
  lines.


Alt-N/M/T/W      CTS when Writing

  This toggles controls CTS/RTS hardware flow control when writing to disk
  during a binary file download.  When this toggle is OFF, Qmodem drops the RTS
  signal while writing data to the disk, and raises RTS after the data has been
  written.

  When this toggle is ON, the RTS signal remains on during the disk writes.
  This allows Qmodem to overlap disk and serial port activity while downloading
  data on systems equipped with hardware-handshaking modems (IE, high-speed or
  MNP modems).  For this option to work properly, the Alt-N/M/T/C  flag must be
  ON.

  Normally, the RTS (Request To Send) signal line is dropped low (turned off)
  whenever a block of data is being written to disk.  This stops the modem from
  sending data to the computer during that time, which could cause data loss
  due to a missed interrupt.

TIP: If your computer and hard disk are fast enough, you can gain a small
     but measurable increase in download speed by using this option.

  CAUTION:     If you are downloading across a network to a file server
          drive, it is strongly recommended that you do NOT use this option.



38   The Forbin Project, Inc.




Alt-N/M/T/F      FIFO during Shell

  This toggle only applies to systems with serial adapters equipped with a
  16550 or 16550A UART, which feature a First-In, First-Out (FIFO) data buffer.
  When ON, Qmodem leaves the 16550/16550A UART in FIFO mode.  When OFF, Qmodem
  disables the FIFO buffer, and the 16550x UART runs in 16450 compatibility
  mode.

  Some external transfer protocols may require this toggle to be OFF for
  correct operation.  If your external transfer program aborts immediately upon
  startup, try setting this to OFF and execute the external again.

NOTE: This toggle only works if Qmodem detects the 16550/16550A UART in your
      system at startup.


TIP: In testing Qmodem 4.2, FIFO buffer operation improved performance in
     systems running under DesqView and equipped with high-speed modems.

  CAUTION:     Problems may occur when upgrading from an 8250 or 16450 UART
          to the newer 16550/16550A chips.  While they are pin-compatible,
          the 16550 series are a superset of the older chips and require
          additional connections not used in the older components.  Some
          serial adapters made specifically for the older chips may not be
          able to operate properly with the newer chips.



Alt-N/M/T/L      Lock DTE Baud Rate

  When set to OFF, Qmodem will set the serial port speed to the connect speed
  identified in the modem's CONNECT message. When ON, Qmodem maintains the
  serial port speed defined in the phone book entry being dialed.


























                                                               Qmodem SST     39



Alt-N/M/T/H      High Speed Xmit

  When set ON, Qmodem uses an interrupt driven transmit routine for better
  performance.  When set OFF, a "brute force" method of sending data is used
  (and as such, is a tad slower).  Some UART-CPU combinations may not be able
  to handle the faster ON mode and you should leave this set OFF.


Alt-N/M/T/1      16550 UART Enable

  When set ON, Qmodem enables the 16550 (and 16550A) FIFO Buffer for both
  transmit and receive.  We can't imagine why you would want to disable this
  feature if you have the 16550, but here is the toggle anyway.


Alt-N/M/T/I      Init Ignores CD

  When set ON, the Modem Init String (Alt-N/M/M/I) will be sent on startup
  regardless of the detection of a Carrier.  Some modems always default to
  reporting Carrier Detected (CD) until told to report the true state of
  carrier.  Unfortunately, this causes a catch-22.  Qmodem paused asking
  whether or not to send the Modem Init if Carrier was present, and the Modem
  Init String may have a command to override this.   If you have such a modem,
  you will surely appreciate this switch!



Alt-N/D  Directories
Qmodem directories are defined in the Directories Menu.  When selected, the
following window is displayed:


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Setup Menu ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Video      Modem    Dirs     Host     Protocols     Files    Options    Exit ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
               ³ Upload       D:\QMODEM\DL\°°°°°°°°°°°°°°°°° ³
               ³ Download     D:\QMODEM\DL\°°°°°°°°°°°°°°°°° ³
               ³ Scripts      D:\QMODEM\SCRIPTS\°°°°°°°°°°°° ³
               ³ SWAP         D:\°°°°°°°°°°°°°°°°°°°°°°°°°°° ³
               ³ 1st Batch    D:\QMODEM\DL\°°°°°°°°°°°°°°°°° ³
               ³ 2nd Batch    D:\°°°°°°°°°°°°°°°°°°°°°°°°°°° ³
               ³ 3rd Batch    D:\°°°°°°°°°°°°°°°°°°°°°°°°°°° ³
               ³ AltW Pick    D:\DL\*.*°°°°°°°°°°°°°°°°°°°°° ³
               ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾




Note that all the fields in this menu are added and edited manually, following
the procedures outlined earlier in this section.

Alt-N/D/U        Upload








40   The Forbin Project, Inc.



  The default drive:\directory which will be searched for files which are
  uploaded to the remote computer.  If this field is left blank, the current
  directory will be searched.  This directory will be displayed in the file
  allocation window following the PgUp upload command for non-batch protocols.
  If you exchange many files with remote computers, you may want to assign the
  same directory for uploads and downloads.


Alt-N/D/D Download

  The default drive:\directory into which downloaded files will be stored.  If
  this field is left blank, files will be stored into the current directory.
  This directory will be displayed in the file allocation window following the
  PgDn download command.  If you exchange many files with remote computers, you
  may want to assign the same directory for uploads and downloads.


Alt-N/D/S        Scripts

  The drive:\directory path which will be searched for all Qmodem script files.
  If this directory is not defined correctly, scripts files will not be
  accessible.


Alt-N/D/W        SWAP

  The drive:\directory path where the Shell to DOS will write a SWAP file if
  there is insufficient EMS memory, or EMS has been disabled (via Alt-N/O/R/E).
  If left blank, then the current drive:\directory will be used.

  The filename created is called QMODEM.$$$ and is marked Read-Only/Hidden.
  This is to remove temptation to delete the file while shelled to DOS.  Doing
  so will likely cause a lockup.


Alt-N/D/1 1st    Batch
Alt-N/D/2 2nd    Batch
Alt-N/D/3 3rd    Batch

  These three drive:\directories are the defaults for the Alt-6, Batch Entry
  Window.  This is to save time if you are always doing Batch Uploads from the
  same directory or directories.  For more information on how they are used,
  refer to the Alt-6 command.

















                                                               Qmodem SST     41



Alt-N/D/A        Alt-W Pick

  This is the default  drive:\directory\picture-mask for the Alt-W command.
  Earlier releases defaulted to *.* or blank.  Now you can set the default to
  your download directory, your word processor documents directory or even your
  spreadsheet WKS directory.

  An example might be:   C:\WORD\DOCS\*.DOC


NOTE: The above are all DEFAULT directories.  Uploads, downloads, and script
      commands all use the standard File Allocation Window (FAW) which
      allows directory specifications to be changed before the commands are
      executed.

      The Batch directories can also be overridden in the Batch Entry Window
      (BEW) at runtime.




Alt-N/H  Host
If you plan on using Qmodem's Host Mode, be sure to read the Host documentation
section completely.  When the Host option is selected, the following menu is
displayed:


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Setup Menu ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Video      Modem    Dirs     Host     Protocols     Files    Options    Exit ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸ÍÍÍÍÍÍÍÍÍÍÍÍ¾
              ³ Type of System     OPEN                           ³
              ³ Download Dir       °°°°°°°°°°°°°°°°°°°°°°°°°°°°°° ³
              ³ Upload Dir         °°°°°°°°°°°°°°°°°°°°°°°°°°°°°° ³
              ³ Maximum Time       60                             ³
              ³ DOS Password       PASSWORD                       ³
              ³ Shutdown Password  PASSWORD                       ³
              ³ Init Command       ATE1Q0V1M1H0S0=0^M°°°°°°°°°°°° ³
              ³ Answer Command     ATA^M°°°°°°°°°                 ³
              ³ OK Message         OK°°°°°°°°°°°°                 ³
              ³ Ring Detect        RING°°°°°°°°°°                 ³
              ³ Busy Command       ATM0H1^M°°°°°°                 ³
              ³ # Rings & Answer   1                              ³
              ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


The Qmodem Host mode operates as a mini Bulletin Board System, complete with
electronic messages, sysop chat, and file transfer capabilities.

Alt-N/H/T        Type of System

  Press ENTER to cycle through the 3 possible settings: OPEN, CLOSED and
  CALLBACK.

  An OPEN system is easiest to setup and get running.  As new callers log in,
  the Host Password (.PWD) file is automatically updated.  All new users are
  assigned a security level of 0.




42   The Forbin Project, Inc.



  In a CLOSED system, authorized callers' names and passwords must be defined
  in the Password file before callers are given access.  If the caller's name
  is not on file, the Host issues a polite "Sorry, this is a closed system"
  message and hangs up.

  CALLBACK mode is similar to a CLOSED system in that it requires the callers'
  name and passwords to be in the Password file.  In addition, CALLBACK
  requires that the callers' DATA Phone Number also be on file.  When callers
  log on successfully, they will be instructed to hang up and place their modem
  into Auto-Answer mode.  The Host will then hang up and immediately dial the
  caller's data phone number.  CALLBACK is a very secure system since it
  insures that all communications originate from known locations.


Alt-N/H/D        Download Dir

  This is the Host Mode equivalent of the Qmodem default download directory.
  Any valid DOS directory may be entered in this field.  All files available
  for download from the Host must be stored in this directory.  The Host "File
  List" command will produce a list of the files in this directory.

  Example:  C:\QMODEM\HOSTDIR\


Alt-N/H/U        Upload Dir

  This is the Host equivalent of the Qmodem default upload directory.  Any
  valid DOS directory may be entered in this field.  All uploaded files will be
  stored into this directory.  If the Upload and Download directories are the
  same, all uploaded files become public and are available for download.

  Example:     C:\QMODEM\HOSTDIR\UPLOADS\


Alt-N/H/M        Maximum Time

  This defines the maximum time allowed per call, in minutes.  The default
  value is 60 minutes, or 1 hour.  The maximum time allowed is 999 minutes (16
  hours 39 minutes).





















                                                               Qmodem SST     43



Alt-N/H/O        DOS Password

  The password required to  "Drop to DOS" from remote.  If this field is left
  blank, all callers may drop to DOS.


Alt-N/H/S        Shutdown Password

  Used to restrict access to the Host Shutdown command.  It is strongly
  recommended that the Shutdown Password be unique and given out only to your
  most trusted friends.  If the correct password is entered, the system hangs
  up immediately and Host mode is terminated.


Alt-N/H/I        Init Command

  This command string is sent to the modem each time Host mode is initialized
  and after each call.  The Host Initialization string should set Verbose
  result codes (Q0V1), no Auto-Answer (S0=0), and on hook waiting for call
  (H0).  The commands in parentheses are valid for Hayes and compatible modems.


Alt-N/H/A        Answer Command

  The Answer Command string is sent to the modem when an incoming call (RING)
  is detected.  For Hayes and compatible modems, use the  "ATA^M" command.


Alt-N/H/K        OK Message

  The modem returns an "OK" message when the last command was received and
  executed successfully.  For Hayes and compatible modems, use "OK".  For
  modems which do not return a response to the Initialization command, leave
  this field blank.


Alt-N/H/R        Ring Detect

  When an incoming call is detected by the modem, it returns  a special "Ring
  Detect" message.  For Hayes and compatible modems, this is the word "RING".
  When the ring detect message is received, the Host sends the Answer Command
  to the modem.


















44   The Forbin Project, Inc.



Alt-N/H/B        Busy Command

  This allows you to place the modem Off-hook when you log in as the local
  Sysop.  Your phone line will return a busy signal preventing callers from
  connecting to the host system.


Alt-N/H/#        # Rings and Answer

  This is exactly what it sounds like.  The Answer command is sent after it
  received this many  Ring Detect message.  In layman terms, it could the
  number of RINGS and then answers.



Alt-N/P  Protocols
When selecting the Protocols  option, the following menu is displayed:


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Setup Menu ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Video      Modem    Dirs     Host     Protocols     Files    Options    Exit ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
                                  ³ 0 -               ³
                                  ³ 1 -               ³
                                  ³ 2 -               ³
                                  ³ 3 -               ³
                                  ³ 4 -               ³
                                  ³ 5 -               ³
                                  ³ 6 -               ³
                                  ³ 7 -               ³
                                  ³ 8 -               ³
                                  ³ 9 -               ³
                                  ³ ASCII Options    ³
                                  ³ Toggles          ³
                                  ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


The Protocols section allows you to customize Qmodem by adding additional
external transfer protocols.  These protocols can then be called from an upload
or download and used as if it were built into Qmodem.  The ASCII Options are
used for customizing the built-in ASCII transfer protocol.   The Toggles menu
handles Internal transfer protocol specifics.


















                                                               Qmodem SST     45



Alt-N/P/0-9  Protocol Revisions
External protocols must be defined in numerical order; with no blanks between.
When selecting a number from 0 to 9, the Protocol Definition window will be
displayed:


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Setup Menu ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Video      Modem    Dirs     Host     Protocols     Files    Options    Exit ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
                                  ³ 0 -               ³
                             ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
                             ³  Select character  °            ³
                             ³  Protocol          °°°°°°°°°°°° ³
                             ³  Upload BAT        °°°°°°°°°°°° ³
                             ³  Download BAT      °°°°°°°°°°°° ³
                             ³  Filename Prompt               ³
                             ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
                                  ³ 8 -               ³
                                  ³ 9 -               ³
                                  ³ ASCII Options    ³
                                  ³ Toggles          ³
                                  ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


The following fields must be defined for each external protocol:

Alt-N/P/x/S      Select Character

  The letter or digit used to select this protocol for a file  transfer.

NOTE: Characters A,X,C,R,O,Y,F,G and Z are internal protocol definitions.
      If you define an external protocol with one of these letters, it will
      disable the internal protocol.



Alt-N/P/x/P      Protocol

  The written name of the protocol as it will appear in the upload/download
  Protocol Selection Window.


Alt-N/P/x/U      Upload BAT

  The name of the upload batch file for the external protocol.  In addition, be
  aware that four batch file parameters are passed as %1, %2, %3, and %4.

  %1 Serial Port speed.  (Computer to Modem)

  %2 Serial Port #       (Current COM Port number)

  %3 Connect MSG speed   (as reported by Modem,  CONNECT xxxxx)

  %4 Filename       (if required.  otherwise blank)


Alt-N/P/x/D      Download BAT



46   The Forbin Project, Inc.



  The name of the download batch file for the external protocol.  The same
  batch file parameters that are passed in the Upload Batch file are also
  passed to the Download Bat file.


Alt-N/P/x/F      Filename Prompt

  Specify "N" for external protocols which include filename as part of the
  transferred data (IE, Zmodem), and "Y" for protocols which must know the name
  of the file being received.  When "Y" is specified, Qmodem passes the
  filename to the download batch file as the 4th command-line parameter (%4).

TIP: Qmodem passes the COM Speed, Serial Port #, current DTE Baud rate and
     the optional Filename to the protocol batch file as parameters %1, %2,
     %3 and %4 respectively.




Installing an external protocol.
Because of their changing nature, and to insure that you use the latest
versions, external protocol drivers are no longer distributed with Qmodem.  We
will use Zmodem as an example to illustrate the various steps required in
installing an external protocol.

Files you will need:

  1. The DSZ.COM program.  Usually found on most BBS's as DSZmmdd.ARC.  "mmdd"
     represent the release date of the current release.

NOTE: in the case of DSZ, new releases can appear on a daily or weekly
      basis; the one you downloaded today may be obsolete tomorrow.

  2. The RZ.BAT (Receive Zmodem) batch file, used for Zmodem downloads.

  3. The SZ.BAT (Send Zmodem) batch file, used for Zmodem downloads.

  4. The DSZ.DOC documentation file without which you will be lost.

You may now select the first unassigned entry in the Alt-N/P menu.  The Revise
window will be displayed.  Edit the fields to make the above example.

Next, edit the RZ.BAT file as follows, using the Qmodem Internal Editor (or your
own favorite):


Echo OFF
DSZ port %2 handshake on rz c:\qmodem\download


The download directory specified in the DSZ command line should match the
download directory defined in the Alt-N/D/D setup menu.  If none is specified,
the file will be saved in the current directory.

Edit the SZ.BAT file as follows:





                                                               Qmodem SST     47




Echo OFF
DSZ port %2 handshake on sz %4


One last step...  Make sure the DSZ.COM program is in your Qmodem directory or
in a directory in the DOS PATH= so it is accessible by Qmodem.

Installation of other external protocols is similar.  Refer to the protocol
documentation to insure that upload and download batch file commands are coded
correctly.



Alt-N/P/A  ASCII Options
The ASCII Options are used to define the parameter which control ASCII (text)
file transfers.











































48   The Forbin Project, Inc.



Alt-N/P/A/R  ASCII Receive
When you select the ASCII Receive option, the following menu is displayed:


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Setup Menu ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Video      Modem    Dirs     Host     Protocols     Files    Options    Exit ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
                                  ³ 0 -               ³
                                  ³ 1 -               ³
                                  ³ 2 -               ³
                                  ³ 3 -               ³
                                  ³ 4 -               ³
                                  ³ 5 -               ³
                                  ³ 6 -               ³
                                  ³ 7 -            ÕÍÍÍÍÍÍÍÍÍÍÍÍ¸
                                  ³ 8 -            ³ Receive   ³
                                  ³ 9 -ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
                                  ³ ASC³ Use INPUT Translate Table   OFF    ³
                                  ³ Tog³ Carriage Return Handling    NONE   ³
                                  ÔÍÍÍÍ³ LineFeed Handling           NONE   ³
                                       ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


Alt-N/P/A/R/U    Use INPUT Translate Table

  When ON, all incoming data will be translated.  Translation criteria are
  defined in the  Alt-A INPUT Translate Table.  If this parameter is OFF, the
  data is not translated and is received exactly as it was sent.


Alt-N/P/A/R/C    Carriage Return Handling

  This option has three setting:

  NONE    No special treatment of the CR. (Decimal 13)
  STRIP   All CR's are removed from the file as it is saved.
  ADD LF  Adds a trailing LF (Decimal 10) after each CR.


Alt-N/P/A/R/L    LineFeed Handling

  This option also has three settings:

  NONE    No special treatment of LF. (Decimal 10)
  STRIP   All LF's are removed from the file as it is saved.
  ADD CR  Adds a CR (Decimal 13) before each LF.














                                                               Qmodem SST     49



  Example:  Lines of data sent by a Mainframe end with a single LF (linefeed).
  You wish to save the data to a file and edit it with an editor or word
  processor.  In this case, a carriage return character should be added in
  front of each trailing LF and the ASCII receive options should be set as
  follows:


                    ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
                    ³ Use INPUT Translate Table   OFF    ³
                    ³ Carriage Return Handling    NONE   ³
                    ³ LineFeed Handling           ADD CR ³
                    ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


  If the text lines ended with CR/CR/LF, you would set the following options:


                    ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
                    ³ Use INPUT Translate Table   OFF    ³
                    ³ Carriage Return Handling    STRIP  ³
                    ³ LineFeed Handling           ADD CR ³
                    ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


  The above options will remove (strip) both incoming CR, and add a leading CR
  to each LF (exactly what the doctor ordered!)



Alt-N/P/A/T  ASCII Transmit
When the ASCII Transmit options is selected, the following menu is displayed:


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Setup Menu ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Video      Modem    Dirs     Host     Protocols     Files    Options    Exit ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
                                  ³ 0 -               ³
                                  ³ 1 -               ³
                                  ³ 2 -               ³
                                  ³ 3 -               ³
                                  ³ 4 -               ³
                                  ³ 5 -               ³
                                  ³ 6 -               ³
                                  ³ 7 -            ÕÍÍÍÍÍÍÍÍÍÍÍÍ¸
                                  ³ 8 -            ³ Receive   ³
                                  ³ 9 -            ³ Transmit  ³
                                  ³ ASCÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
                                  ³ Tog³ Use OUTPUT Translate Table   OFF    ³
                                  ÔÍÍÍÍ³ Carriage Return Handling     NONE   ³
                                       ³ LineFeed Handling            NONE   ³
                                       ³ Pacing Speed                 0      ³
                                       ³ pAcing Character             NONE   ³
                                       ³ Blank Line Expansion         ON     ³
                                       ³ End of Line Character        10     ³
                                       ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


Alt-N/P/A/T/U    Use OUTPUT Translate Table


50   The Forbin Project, Inc.




  When set to ON, outgoing data is translated.  Translation criteria are
  defined in the Alt-A OUTPUT Translate table.  When OFF, the data is not
  translated and is sent "as is".

Alt-N/P/A/T/C    Carriage Return Handling

  This option has three setting:

  NONE    No special treatment of the CR. (Decimal 13)
  STRIP   All CR's are removed while the file is transmitted.
  ADD LF  Adds a trailing LF (Decimal 10) after each CR.


Alt-N/P/A/T/L    LineFeed Handling

  This option also has three settings:

  NONE    No special treatment of the LF. (Decimal 10)
  STRIP   All LF's are removed while the file is transmitted.
  ADD CR  Adds a leading CR (Decimal 13) before each LF.


Alt-N/P/A/T/P    Pacing Speed

  Pacing controls the speed of the data transfer to the remote computer.  If
  the remote computer is able to receive text data at high speed, this value
  should be zero, the default.  If you experience problems sending ASCII data
  without any pacing, insert a delay between each transmitted character by
  increasing the Pacing Speed value.  Pacing Speed is expressed in milliseconds
  (1000 = 1 second).  25 milliseconds (1/40 sec) is a good starting value.


Alt-N/P/A/T/A    Pacing Character

  If a pacing character is specified, Qmodem will wait until that character is
  received before it sends the next line of text.  If NONE is specified, the
  transfer will not pause between lines of text.  Use this only when you are
  sure that the remote system always prompts for each line of text with the
  same character.  To change the setting, use the Up and Down arrow keys to
  move through the ASCII character set and press ENTER when the desired
  character is displayed.

  In some cases, you may want to control transmission pacing yourself.  Qmodem
  allows you to do just that by setting the pacing character to ASCII 255 (or
  any other character which you know will not be received by the other system).
  When Qmodem pauses after sending each line, press any key to send the next
  line.  Repeat this procedure until the entire file has been transmitted.

  See also: End Of Line Character.

Alt-N/P/A/T/B    Blank Line Expansion

  This option controls whether or not blank lines (lines which only contain a
  CR and/or LF and no other text) should be expanded to include at least one
  SPACE as a leading character.




                                                               Qmodem SST     51



NOTE: Many online systems and BBS's interpret a blank line, as defined
      above, as an end-of-message indication.  If your text contains  blank
      lines, the first one will cause the other system to stop receiving
      message text, issue an end-of-message prompt, and wait for your input.
      Since additional message text is still being sent, unpredictable
      results can occur.  Setting Blank Line Expansion ON will eliminate
      this problem.



Alt-N/P/A/T/E    End Of Line Character

  Often referred to as EOL, this is the character that your text editor uses as
  the last character in a line.  Most often (IE., with the Qmodem Internal
  Editor), this is a LineFeed character (ASCII 10), which is usually preceded
  by a Carriage Return (ASCII 13).  If your text editor or word processor uses
  a different EOL character, you should define it here.

NOTE: Setting this value incorrectly results in a jerky or incomplete
      transmission.

  Example:

  You want to upload a message to your local PCBoard BBS system.  The message
  text was created with the Qmodem Internal Editor (a good combination).

  PCBoard starts each message line with a colon ":", which we can use as the
  pacing character.  PCBoard also terminates message entry when a blank line is
  received.  To successfully upload the message, the ASCII transmit options
  should be set as follows:


                      ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
                      ³ Use OUTPUT Translate Table   OFF    ³
                      ³ Carriage Return Handling     NONE   ³
                      ³ LineFeed Handling            NONE   ³
                      ³ Pacing Speed                 0      ³
                      ³ pAcing Character             : 58   ³
                      ³ Blank Line Expansion         ON     ³
                      ³ End of Line Character        10     ³
                      ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾



















52   The Forbin Project, Inc.



Alt-N/P/T Protocol Toggles
These are toggles specific to the file transfer protocols.   The menu looks like
this:


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Setup Menu ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Video      Modem    Dirs     Host     Protocols     Files    Options    Exit ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
                                  ³ 0 -               ³
                                  ³ 1 -               ³
                                  ³ 2 -               ³
                                  ³ 3 -               ³
                                  ³ 4 -               ³
                                  ³ 5 -               ³
                                  ³ 6 -               ³
                                  ³ 7 -               ³
                                  ³ 8 -               ³
                                  ³ 9 -               ³
                                  ³ ASCII Options    ³
                                  ³ Toggles          ³
                               ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
                               ³ Overwrite Files           OFF ³
                               ³ Auto-Increment Filename   OFF ³
                               ³ Save Partials             OFF ³
                               ³ Clear Batch Screen        ON  ³
                               ³ Zmodem Autostart          OFF ³
                               ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


Alt-N/P/T/O      Overwrite Files
Alt-N/P/T/A      Auto-Increment Filenames

  These two toggles work in tandem to control how downloaded files are treated.
  The rules are not that complicated and will be discussed in detail.  One of
  the combinations will be the right one for you.

NOTE: To keep confusion to a minimum, the exception to the rule is the
      Zmodem protocol and will be discussed in a moment.


  When you are prompted for a filename in one of the download protocols, a
  check is made to see if the file already exists.  If it does, the Auto-
  Increment flag is checked.  If it is set ON, then the filename entered gets
  incremented and the transfer begins.

  If the Auto-Increment flag is set OFF, then the Overwrite Files flag is
  checked.  If this is set ON, the existing file is deleted and the transfer
  begins.  If it is set OFF, then you will be prompted for a different filename
  before the transfer can begin.

  The Exception to the rule: Zmodem

  When downloading using any protocol except Zmodem (yes, there is always an
  exception to the rule), the Auto-Increment flag is checked first, and then
  the Overwrite flag.  With Zmodem, there is another possibility called Crash
  Recovery.  This will override the above mentioned flags under certain
  specific conditions.



                                                               Qmodem SST     53



  If the file you are downloading already exists and the file on disk is
  smaller than the one being downloaded, there is a possibility that the file
  on disk is a Partial (see below).  Zmodem then attempts to use Crash Recovery
  to pick up where the you left off.

  If it turns out that the two files are not the same, then the original rules
  apply.  IE. A check of the Auto-Increment flag, and then the Overwrite if
  Auto-Increment is OFF.  If Overwrite is also OFF, the file is SKIPPED by the
  Zmodem download.


Alt-N/P/T/S      Save Partials

  A Partial is created when the Save Partials flag is set ON and a download
  aborts. The portion that has been received successfully is not deleted.  If
  it is set OFF, then any partially downloaded file is erased when the transfer
  aborts.


Alt-N/P/T/C      Clear Batch Screen

  Clear Batch Screen  This is the only toggle that deals with Uploads.  All the
  others affect Downloads.  One of the new features in Qmodem is support for
  Batch Uploads.  The Batch Entry Window (BEW) has the ability to retain the
  entered information so you can do the same batch upload to several different
  systems without retyping the entire BEW screen.

  When a Batch upload completes, this flag is checked to see if the BEW
  information should be cleared.  The default is ON.  Even if you leave this
  set OFF, you can still clear the old information in the BEW with a press of
  the F4 key.


Alt-N/P/T/Z      Zmodem Auto-Start

  Zmodem Autostart When this parameter is ON, Zmodem file downloads are started
  automatically whenever a Zmodem download transfer header is received.  If
  this parameter is OFF, Zmodem downloads must be started manually with the
  PgDn command.





















54   The Forbin Project, Inc.



Alt-N/F  Files
Qmodem requires access to specific files and programs which must be defined in
the Files menu:


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Setup Menu ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Video      Modem    Dirs     Host     Protocols     Files    Options    Exit ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸Í¾
                           ³ Online Help      QMODEM.HLP°°°°°°°°°°°°°°°°°°°° ³
                           ³ Screen Dump      SCREEN.DMP°°°°°°°°°°°°°°°°°°°° ³
                           ³ Capture          CAPTURE.CAP°°°°°°°°°°°°°°°°°°° ³
                           ³ Log              QMODEM.LOG°°°°°°°°°°°°°°°°°°°° ³
                           ³ BackScroll       SCROLL.SAV°°°°°°°°°°°°°°°°°°°° ³
                           ³ View             °°°°°°°°°°°°°°°°°°°°°°°°°°°°°° ³
                           ³ Printer          °°°°°°°°°°°°°°°°°°°°°°°°°°°°°° ³
                           ³ Time/Date Stamp  ON                             ³
                           ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


Alt-N/F/O        Online Help

  This is the Qmodem online help file, distributed as part of the Qmodem
  program.  The default name for this file is QMODEM.HLP.

  If you use Qmodem from different subdirectories, then you should edit this
  and include the full drive:\directory where the HLP file is located.

  Example: C:\QMODEM\QMODEM.HLP


Alt-N/F/S        Screen Dump

  This is the file to which Qmodem screen dumps (Alt-T) are saved.  Qmodem
  automatically appends the .DMP suffix to the specified filename if one is not
  included.

  Example: C:\QMODEM\SCREEN.DMP


Alt-N/F/C        Capture

  This is the file where session data is recorded when  Capture (Ctrl-Home) is
  ON.  Qmodem automatically appends the .CAP suffix to the filename if one was
  not specified.

  Example: C:\QMODEM\CAPTURE.CAP














                                                               Qmodem SST     55



Alt-N/F/L        Log

  This is the file where Qmodem logs all activity.  The Qmodem Log can be
  started automatically (Alt-N/O/T/U  -- aUto Log Start) or explicitly with the
  Alt-0 command.  Qmodem automatically appends the .LOG suffix to the filename
  if one was not specified.

  Example: C:\QMODEM\QMODEM.LOG


Alt-N/F/B        Back-scroll

  This is the file to which the scroll-back buffer is copied.  Qmodem does not
  assign a default suffix to this file.

  Example: C:\QMODEM\SCROLL.SAV


Alt-N/F/V        View

  This is the path and filename of the program which is executed by the Alt-V
  command.  Any valid program can be executed by Alt-V, making this a powerful
  function.

  Example:


         ³ View          C:\UTIL\LIST °°°°°°°°°°°°°°°°° ³


  Two special keywords may also be specified as a View option: @FSE and
  @EDITOR.  If @FSE if specified, the Qmodem Internal Editor will be used for
  all file viewing and editing.

  Example:


         ³ View          @FSE °°°°°°°°°°°°°°°°°°°°°°°°° ³


  The @EDITOR keyword, if specified, causes the Qmodem Internal Editor to be
  replaced with an external program of your choice.

  Example:


         ³ View          @EDITOR QEDIT °°°°°°°°°°°°°°°° ³


  If "@EDITOR" is not specified, the Qmodem Internal Editor will be used for
  internal editing of scripts or note files attached to phone book entries.

NOTE: The @EDITOR and @FSE commands should always be followed by a space.
      (as shown in the above examples).



Alt-N/F/P        Printer


56   The Forbin Project, Inc.



  This is the default used when specifying a printer.  It can be a printer
  device such as PRN, LPT1, or LPT2.  Or, it can also be a drive:\path\filename
  like the others in this menu.  If left blank, it will default to PRN (the
  default DOS printer).

  Example: PRN

NOTE: Qmodem will append new data to the screen dump, capture, log, and
      back-scroll files if they exist.  If they do not, a prompt for their
      creation will be displayed when the corresponding command is issued.
      File names may be changed when these recording features are invoked.



Alt-N/F/T        Time/Date Stamp

  This toggle does not have a seperate sub-menu.  (what?  for only one toggle?
  nah..)  When set ON, the Screen Dump, Capture and Scroll back files will have
  Time and Date Stamp headers placed above the appended data.  This is appended
  each time the file is opened, not between each line added to the file.  When
  set OFF, no header is placed before the appended data.



Alt-N/O  Options
The Options Menus define run-time parameters which control the operation of
Qmodem.  These parameters fall into the following categories:


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Setup Menu ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Video      Modem    Dirs     Host     Protocols     Files    Options    Exit ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸Í¾
                                                      ³ Toggles             ³
                                                      ³ Runtime Parms       ³
                                                      ³ Memory              ³
                                                      ³ Sounds              ³
                                                      ³ Delays              ³
                                                      ³ Characters          ³
                                                      ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾




Alt-N/O/T  Options Toggles
Toggles is a list of feature switches which control  the remaining toggles that
do not fit under Video, Modem or Protocols.   The menu looks like this:














                                                               Qmodem SST     57



ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Setup Menu ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Video      Modem    Dirs     Host     Protocols     Files    Options    Exit ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸Í¾
                                                      ³ Toggles             ³
                                              ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸  ³
                                              ³ Beeps & Bells         ON  ³  ³
                                              ³ ANSI Music            OFF ³  ³
                                              ³ DEL/^H Backspace      OFF ³  ³
                                              ³ Auto-Start LOG        OFF ³  ³
                                              ³ Keypad emulation      OFF ³ÍÍ¾
                                              ³ ENQ response          OFF ³
                                              ³ Guard Alt-H           OFF ³
                                              ³ 0xE0 Doorway Codes    OFF ³
                                              ³ Alt-D FON Book           ³
                                              ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

Alt-N/O/T/B      Beeps & Bells

  Activates or deactivates the Qmodem audible signals produced when connecting
  to another computer, or at the completion of a file transfer.  This toggle
  can be changed with the Alt-B command.


Alt-N/O/T/A      ANSI Music

  Setting this ON will permit Qmodem to play ANSI music if found in the
  incoming data stream.  This toggle can be changed via the Alt-M command.


Alt-N/O/T/D      Del/^H Backspace

  This toggle defines the character which is generated when the [BACKSPACE] key
  is pressed.  When OFF, a ^H (standard backspace character) is generated.
  When ON, a DEL is generated.  This toggle can be changed via the Alt-1
  command.

TIP: Pressing [Ctrl-Backspace] will send the reverse  of this toggle.  For
     example, if ON, ^backspace will send a ^H character.



Alt-N/O/T/U      Auto Start Log

  When this toggle is ON, Qmodem will automatically record activity in the LOG
  file defined in Alt-N/F/L when first started.  If set to  OFF, activity
  logging must be started explicitly with the Alt-0 command.


Alt-N/O/T/K      Keypad emulation

  This toggle controls numeric keypad operation when the keyboard NumLock
  toggle is ON.  When Keypad emulation is ON, pressing a cursor key will send
  the correct cursor control sequence, as defined in the Terminal Emulation
  section of the manual.  When set to OFF, the keypad functions normally.

NOTE: Refer to the Alt-G Emulations sections for a complete description of
      the keypad.



58   The Forbin Project, Inc.




Alt-N/O/T/E      ENQ Response

  This toggle  controls the action taken when an ENQ ^E is received.  If set
  ON, then the contents of Function Key Alt-F12 is sent out the serial port.
  When set OFF, the ^E is processed as a normal incoming character.  Refer to
  the Alt-J command on editing the text for Alt-F12.

  This toggle can act as ENQ/ACK flow control.  If the characters ^F are stored
  in Alt-F12 and this is set ON, then every time the remote system sends the
  ENQ, an ACK (^F) will be sent back.


Alt-N/O/T/G      Guard Alt-H

  This toggle controls how the Alt-H Hangup command is processed.  If this is
  set ON and press Alt-H, a window will open confirming your wanting to hangup.
  When set OFF, the Hangup command is acted upon immediately.


Alt-N/O/T/0      0xE0 Doorway Codes

  This toggle controls whether or not the enhanced 101-key E0 (hex) codes are
  transmitted.  When set ON, the special 3-byte code is sent for any of the
  enhanced keys.  When set OFF, the E0 keys are converted to their 84-key
  keyboard equivalent.


































                                                               Qmodem SST     59



Alt-N/O/T/F  Alt-D FON Book
The Alt-D FON Book menu was created under Toggles to make it easy to find all
the toggles relating to the Alt-D command.  The menu looks like this:


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Setup Menu ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Video      Modem    Dirs     Host     Protocols     Files    Options    Exit ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸Í¾
                                                      ³ Toggles             ³
                                              ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸  ³
                                              ³ Beeps & Bells         ON  ³  ³
                                              ³ ANSI Music            OFF ³  ³
                                              ³ DEL/^H Backspace      OFF ³  ³
                                              ³ Auto-Start LOG        OFF ³  ³
                                              ³ Keypad emulation      OFF ³ÍÍ¾
                                              ³ ENQ response          OFF ³
                                              ³ Guard Alt-H           OFF ³
                                              ³ 0xE0 Doorway Codes    OFF ³
                                              ³ Alt-D FON Book           ³
                                              ÔÍÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
                                                ³ Tag Advance           ON  ³
                                                ³ AutoStart             OFF ³
                                                ³ Clear tags on FKey    ON  ³
                                                ³ Write FBK file        ON  ³
                                                ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


Alt-N/O/T/F/T    Tag Advance

  When set ON, tagging entries with the SPACBAR in Alt-D will make the
  Scrollbar move down to the next entry.  When set OFF, the Scrollbar does not
  move automatically.


Alt-N/O/T/F/A    Auto Start

  When set ON, Qmodem will come up in the Alt-D screen initially.  When set
  OFF, the TERMINAL mode is the default screen.

NOTE: If you start Qmodem with the /S= or /HOST command line options, the
      Auto Start toggle is ignored and defaults to OFF.



Alt-N/O/T/F/C    Clear tags on FKey

  When set ON, using one of the FKeys to tag and dial will do an implied U-
  Untag All command first.  When set OFF, pre-existing tags remain, and any new
  tags are added.











60   The Forbin Project, Inc.



Alt-N/O/T/F/W    Write FBK File

  Another popular addition.  When set ON, any changes to the FON book will
  result in writing an FBK Backup file to disk.  This Backup is the same size
  as the original.  When set OFF, no FBK file is written to disk.

  This could be very handy for floppy disk users where they do not want the
  extra FBK file written to disk.  It does take a lot longer to write this to
  floppy, not to mention the extra 23K (or so) disk space required.



Alt-N/O/R  Options Runtime Parms
Runtime Parms consist of 6 parameters which can be set ON or OFF to control
specific aspects of Qmodem operation.  These are similar to the TOGGLES menu and
replace previously used Command Like Parameters. To change the toggle setting,
type the toggle's highlighted letter or cursor to the entry and press <Enter>.

The menu looks like this:


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Setup Menu ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Video      Modem    Dirs     Host     Protocols     Files    Options    Exit ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸Í¾
                                                      ³ Toggles             ³
                                                      ³ Runtime Parms       ³
                                                  ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸³
                                                  ³ EMS for Overlays    ON  ³³
                                                  ³ Int16 Enable        ON  ³³
                                                  ³ Share IRQ's         OFF ³³
                                                  ³ Optimum Shell       ON  ³¾
                                                  ³ -- Disk Shell       ON  ³
                                                  ³ Calibrate DELAY     OFF ³
                                                  ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


Alt-N/O/R/E      EMS for Overlays

  This controls whether or not  to use EMS memory in Qmodem.  If set ON, the
  QMODEM.OVR file will be loaded into EMS memory.  Also, EMS memory will be
  used to store the SWAP file (see Alt-N/D/S) when shelling to DOS.

  Use of EMS memory will significantly improve performance by eliminating
  overlay-related disk activity.  The amount of EMS memory required to store
  the Overlay is slightly higher than the size of the QMODEM.OVR file.  Other
  aspects of Qmodem may draw on the available EMS memory as needed.














                                                               Qmodem SST     61



Alt-N/O/R/I      Int16 Enable

  When set ON, Qmodem uses an internal Interrupt 16 handler to access the 101-
  key enhanced keyboards.  This usually allows the F11 & F12 keys to be used if
  they are present.  When set OFF, the normal DOS interrupt handler is used and
  you will not be able to use the F11 & F12 keys.

  Some keystrokes in Qmodem do require this to be set ON to be used.  F11 & F12
  have already been mentioned.  Alt-Enter, to toggle the Status Line
  information is another.

NOTE: If you do not have an enhanced keyboard, or the BIOS does not support
      one, you cannot toggle this to the ON position.



Alt-N/O/R/S      Share IRQ's

  When ON, Qmodem will correctly share interrupts on PS/2 and EISA bus equipped
  computers.  When set OFF, Qmodem will not pass interrupts on to the previous
  interrupt handlers if any were present.  If you are running a PC, XT or AT
  based system, then this should be set OFF.


Alt-N/O/R/O      Optimum Shell

  When ON, Qmodem will attempt to remove all but 5K of itself from memory
  before all shell operations (external transfer protocols, Alt-R drop to DOS,
  etc.)  If the EMS USAGE is set ON, then it first tries to store the copy into
  EMS memory.  If there is not enough free EMS or the EMS USAGE is OFF, then it
  tries to swap to DISK.  If there is not enough DISK space, the Optimum Shell
  is disabled.


Alt-N/O/R/D      Disk Shell

  This toggle works only when the Optimum Shell toggle is set ON.  If OFF, this
  toggle has no effect.  Assuming the Optimum Shell is ON, this toggle controls
  whether or not the Swap file can be placed on Disk.

  If ON, then a Disk file will be attempted if you have insufficient EMS memory
  to hold the Swap file (or the Use EMS toggle is set OFF).  If OFF, and you
  have run out of EMS, then the Optimum Shell is disabled.

















62   The Forbin Project, Inc.



Alt-N/O/R/C      Calibrate Delay

  Calibrate DELAY  When set ON, the internal timer routine will automatically
  calibrate itself periodically.  This could be necessary if running under
  multitaskers or running on a network server. (the latter is strongly
  discouraged however).



Alt-N/O/M  Options Memory
Qmodem allows user-specified memory allocations for three storage areas: The
scroll-back buffer, the download buffers and the Overlay memory allocation.
These values can be changed to meet varying requirements.


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Setup Menu ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Video      Modem    Dirs     Host     Protocols     Files    Options    Exit ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸Í¾
                                                      ³ Toggles             ³
                                                      ³ Runtime Parms       ³
                                                      ³ Memory              ³
                                                 ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
                                                 ³ Lines of Scroll-back  1000 ³
                                                 ³ Download Buffer       8    ³
                                                 ³ Overlay Buffer (K)    40   ³
                                                 ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


Alt-N/O/M/L      Lines of Scroll-back

  Memory is allocated as the maximum number of lines which can be stored in the
  Scroll-back buffer.  Values from 0 to 1000 are valid.


Alt-N/O/M/D      Download Buffer

  Downloaded data is stored into the download buffer.  When the buffer is full,
  it is copied to disk.  Each buffer is 128 bytes, and from 8 to 240 buffers
  can be allocated.  When receiving to a fast hard disk or to a RAM disk, use
  the smallest allocation (8).  A low allocation when downloading to a diskette
  will reduce transmission efficiency.  Large allocation are at the expense of
  system RAM.


Alt-N/O/M/O      Overlay Buffer

  The default value is 30K.  Increasing this value will reduce disk activity
  during the loading of program overlay files at the expense of memory.
  Anything above around 64K is just wasting disk main memory.

TIP: If Qmodem seems slow, this value should be increased in 5-10K
     increments until execution speed is satisfactory.



NOTE: Memory available to Qmodem may vary greatly depending on the operating
      system's own requirements, and resident programs (TSRs) loaded. If
      Qmodem is unable to find sufficient memory, it will re-allocate it


                                                               Qmodem SST     63



      using a best-fit algorithm and will issue a warning message to that
      effect.


Alt-N/O/S  Options Sounds
Qmodem can generate various sounds to signal a successful connect or the
completion of a file transfer.  Whether or not sounds are generated is
controlled by the Alt-N/O/T/B toggle, or the  Alt-B command in terminal mode.
These sounds can be customized in the Options Sounds menu:


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Setup Menu ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Video      Modem    Dirs     Host     Protocols     Files    Options    Exit ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸Í¾
                                                      ³ Toggles             ³
                                                      ³ Runtime Parms       ³
                                                      ³ Memory              ³
                                                      ³ Sounds              ³
                                                      ³ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
                                                      ³³ Connect tones       ³
                                                      Ô³ Upload tone     1200 ³
                                                       ³ Download tone   1200 ³
                                                       ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


Alt-N/O/S/C      Connect Tones

  This multi-note jingle has its own custom menu.


Alt-N/O/S/U      Upload tone
Alt-N/O/S/D      Download tone

  This is the frequency in Hertz of the beeps that  are produced at the
  completion of each file transfer.  A sample will be heard as you change
  these.  The default frequency for the file transfer completion tones is 1200
  Hz























64   The Forbin Project, Inc.



Alt-N/O/S/C  Options Sounds Connect tones


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Setup Menu ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Video      Modem    Dirs     Host     Protocols     Files    Options    Exit ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸Í¾
                                                      ³ Toggles             ³
                                                      ³ Runtime Parms       ³
                                                      ³ Memory              ³
                                                      ³ Sounds              ³
                                                      ³ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
                                                      ³³ Connect tones       ³
                                                      Ô³ UploÕÍÍÍÍÍÍÍÍÍÍÍ¸200 ³
                                                       ³ Down³ 1 -  1200 ³200 ³
                                                       ÔÍÍÍÍÍ³ 2 -  1400 ³ÍÍÍÍ¾
                                                             ³ 3 -  1600 ³
                                                             ³ Max  3    ³
                                                             ÔÍÍÍÍÍÍÍÍÍÍÍ¾



Alt-N/O/S/C/1    Connect Tone 1
Alt-N/O/S/C/2    Connect Tone 2
Alt-N/O/S/C/3    Connect Tone 3

  Qmodem produces a 3-note jingle following a successful connection.  The
  default frequencies for the three notes are 1200, 1400, and 1600 cycles.

  These can be changed to suit your taste.  All 3 notes are played following
  each change.  To change a value, type the desired number, type in the new
  value, and press ENTER.


Alt-N/O/S/C/3    Max Repeats

  This entry is under the Connect Tones menu.  It controls the maximum number
  iterations of the Connect tones when you get connected via the Alt-D Phone
  Book.  Remember, this is the maximum number.  You can always cancel the tones
  with a press of any key.





















                                                               Qmodem SST     65



Alt-N/O/D  Options Delays
Delay values affect the timing of certain Qmodem operations:


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Setup Menu ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Video      Modem    Dirs     Host     Protocols     Files    Options    Exit ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸Í¾
                                                      ³ Toggles             ³
                                                      ³ Runtime Parms       ³
                                                      ³ Memory              ³
                                                      ³ Sounds              ³
                                                      ³ Delays              ³
                                                      ³ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
                                                      Ô³ Status window  100  ³
                                                       ³ File transfers 10   ³
                                                       ³ BREAK timing   500  ³
                                                       ³ DTR timing     500  ³
                                                       ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾



Alt-N/O/D/S      Status Windows

  Most toggles or immediate commands have an accompanying window showing the
  change in Qmodem's status.  The value in this field, expressed in hundredths
  of a second, controls the duration of time these status windows are
  displayed.

  The default is 300, for a 3 second duration.


Alt-N/O/D/F      File Transfers

  File transfer errors such as Short/Long blocks can occur on high-speed,
  buffered modems when the COM port rate is fixed at a high value.  Adding a
  file transfer delay of up to 20 seconds (or more, depending on the system you
  are communicating with) will correct this problem.

NOTE: This should be set to a non-zero value any time the serial port baud
      rate exceeds the actual connect baud rate.




Alt-N/O/D/B      BREAK Timing

  This is the number of milliseconds that Qmodem will hold the BREAK signal
  high when Ctrl-End is pressed or specified in the Dialing setup options.
  Values from 0 to 2000 (2 seconds) are valid.











66   The Forbin Project, Inc.



Alt-N/O/D/D      DTR Timing

  This is the number of milliseconds that Qmodem will hold the DTR signal low
  when specified in the Modem setup options.  Values from 0 to 2000 (2 seconds)
  are valid.



Alt-N/O/C  Options Characters
Special characters and field masks are used to change the way Qmodem looks and
acts.  The first four characters are more cosmetic than anything.  The picture
masks are cosmetic in addition to being functional.


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Setup Menu ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Video      Modem    Dirs     Host     Protocols     Files    Options    Exit ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸Í¾
                                                      ³ Toggles             ³
                                                      ³ Runtime Parms       ³
                                                      ³ Memory              ³
                                                      ³ Sounds              ³
                                                      ³ Delays              ³
                                                      ³ Characters          ³
                                                   ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
                                                   ³ Beeps & Bells         13  ³
                                                   ³ ANSI Music            14  ³
                                                   ³ Status Line Filler  ° 176 ³
                                                   ³ Phone Book Tag      û 251 ³
                                                   ³ Notes Tag           ð 240 ³
                                                   ³ Date Mask      mm-dd-yy°° ³
                                                   ³ Time Mask      hh:mm:ss°° ³
                                                   ³ Elapsed Mask   hh:mm:ss°° ³
                                                   ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


  To change a separator or indicator value, select the desired character and
  press the direction keys to select another character values.  When the
  desired character is highlighted, press Enter.  Press Esc to leave the
  character as it was.

  The Character Select Pick List looks like this:


                                                   ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
                                                   ³ Beeps & Bells         13  ³
                                                   ³ ANSI Music            14  ³
                                                   ³ Status Line Filler  ° 176 ³
          ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Character Select Window ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸1 ³
          ³   ¡ ¢ £ ¤ ¥ ¦ § ¨ © ª « ¬ ­ ® ¯ ° ± ² ³ ´ µ ¶ · ¸ ¹ º » ¼ ½ ¾ ¿ ³0 ³
          ³ À Á Â Ã Ä Å Æ Ç È É Ê Ë Ì Í Î Ï Ð Ñ Ò Ó Ô Õ Ö × Ø Ù Ú Û Ü Ý Þ ß ³y ³
          ³ à á â ã ä å æ ç è é ê ë ì í î ï ð ñ ò ó ô õ ö ÷ ø ù ú û ü ý þ   ³° ³
          ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ   for more Í¾° ³
                                                   ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


Alt-N/O/C/B      Beeps & Bells

  Default:     Single note  (ASCII 13)


                                                               Qmodem SST     67




  This also happens to be the Decimal representation of a carriage return so it
  cannot be accurately represented in this document.  This is the character
  used in the Status line to show that the Beeps & Bells is toggled ON.

TIP: You may want to change this to another character to prevent problems
     with the DOS Print Screen function if you like to use the PrtSc key!



Alt-N/O/C/A      ANSI Music

  Default:     Double note  (ASCII 14)

  This is the character used in the status line to show that ANSI Music is
  toggled ON.

TIP: You may want to change this to another character to prevent problems
     with the PrtSc function.  The double musical note character causes
     Epson and compatible printers to switch to compressed print mode.


Alt-N/O/C/S      Status Line Filler

  Default:     Hash block  (ASCII 176)

  This is the character used as an area separator in the Status line.


Alt-N/O/C/P      Phone Book Tag

  Default:     Check mark  (ASCII 251)

  This character is used in the Alt-D Phone Book to indicate that an entry has
  been tagged for dialing or other functions.


Alt-N/O/C/N      Notes Tag

  Default:     Triplet  (ASCII 240)

This character is used in the Alt-D Phone Book to indicate that an entry has an
attached Note file.

















68   The Forbin Project, Inc.



Alt-N/O/C/D      Date Mask
Alt-N/O/C/T      Time Mask
Alt-N/O/C/E      Elapsed Mask

  To allow the maximum amount of flexibility and to insure that the DATE, TIME
  and ELAPSED TIME routines can be used internationally, you can specify a
  picture mask to indicate how a given string should be formatted.

  For example, let's say that a date variable contains January 2, 1990 and you
  want to display it. There are several possible picture masks you could use:

     Picture        Result
     ---------------------------------------------
     mm/dd/yy  01/02/90
     MM/dd/yy   1/02/90     (note the Case difference)
     mm/dd/yyyy     01/02/1990
     mm-dd-yyyy     01-02-1990
     dd/mm/yyyy     02/01/1990
     DD-mm-yyyy      2-01-1990

  In Picture masks, the CASE of the letters is significant.  If the letter are
  Upper case, then any leading zeros are substituted for the SPACE character.
  If the letters are lower case, then leading zeros are left in place.  This
  applied for both DATE and TIME masks.

  Time strings are handled in a similar fashion, except that special formatting
  characters are available for working with times in am/pm (12-hour) format as
  well as military (24-hour) format.

  For example, lets say it is 1:02pm and you want to display this in a
  different format.  Here are some possible picture masks:

     Picture        Result
     ----------------------------------------------
     hh:mm:ss  13:02:00
     hh:mm          13:02
     hh:mm te  01:02 pm
     HH:mmt     1:02p
     HH:mm:ss  13:02:00  (note the Case difference)
     HH:mm:sste      1:02:00pm

  Note that string representations of time are always assumed to be in military
  format unless a 't' appears in the picture mask.  An 'e' (em) in the mask
  should always be accompanied by a corresponding 't' (time).

  Now that you have a general idea of what picture masks do, let's look at the
  characters that can appear in them.   The following special characters are
  meaningful in masks:

     Char      is replaced by
     ---------------------------------------------------------------------------
     -----------------------------------
     'm', 'M'  Month     (date fields only)
     'd', 'D'  Day       (date fields only)
     'y'       Year      (date, notice 'Y' is a literal)
     'h', 'H'  Hour      (time fields only)
     'm', 'M'  Minutes   (time fields only)
     's', 'S'  Seconds   (time fields only)


                                                               Qmodem SST     69



     't'       'p' or 'a'     (time dependant)
     'e'       'm'       (usually follows the 't')

  Any character other than shown above is treated as a literal and displayed
  without substitution.

  Elapsed  times use the same format as regular Time masks.  However, most of
  the elapsed times count from 00:00:00 as a base.  Therefore, it is
  recommended that you do not include the t or e codes to make it use 12-hour
  am/pm format.



Alt-N/E  Exit
You should always exit the Setup Menu with this option if you want changes to be
saved in the Qmodem configuration file.

The Configuration Exit Menu has two options:


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Setup Menu ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Video      Modem    Dirs     Host     Protocols     Files    Options    Exit ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
                                                                ³ Save Changes ³
                                                                ³ Abandon      ³
                                                                ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾



Alt-N/E/S        Save Changes

  Save the changes to the QMODEM.CNF file and exit.




























70   The Forbin Project, Inc.



Alt-N/E/A        Abandon

  Leave the configuration menu and do not save the changes.  Pressing ESC while
  at the main menu level has the same effect.  This allows changes to be tested
  before being saved with Alt-N/S.























































                                                               Qmodem SST     71



Qmodem Commands
Qmodem features a wealth of commands, many of them with multiple options, and
used for different purposes and under different circumstances.  This section of
the documentation describes all the commands in detail and -- mostly --  in
alphabetical order.


Alt-A  Strip/Replace Tables
Strip/Replace is more commonly known as character translation.  Translation may
be necessary when communicating with another computer whose ASCII codes  (the
computer's alphabet) do not match those used by your PC.  There are 256 ASCII
characters, ranging in value from 0 to 255.   "Stripping" a character causes
that character to be removed from all incoming text data.

The initial menu looks like this:


                        ÕÍÍÍÍÍÍ Table Selection ÍÍÍÍÍÍ¸
                        ³                             ³
                        ³    Select Table to Edit     ³
                        ³                             ³
                        ³         1 -  INPUT          ³
                        ³         2 -  OUTPUT         ³
                        ³                             ³
                        ³  Your Choice ?              ³
                        ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


Pressing either 1 or 2 displays a screen containing the ASCII values 0 through
127 and their respective translations.  Since character translation is not
performed by default, all values are the same the first time you use the Alt-A
command.

Above the translate table are the original and translated representations of the
current value.  Characters which have been translated will appear highlighted
until changed back to normal.  This is a quick visual cue showing what has been
changed.























72   The Forbin Project, Inc.




ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ INPUT Strip/Replace Table ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³                    In Character ||  Out Character ||                       ³
³  [  0-  0]  16- 16   32- 32   48- 48   64- 64   80- 80   96- 96  112-112     ³
³     1-  1   17- 17   33- 33   49- 49   65- 65   81- 81   97- 97  113-113     ³
³     2-  2   18- 18   34- 34   50- 50   66- 66   82- 82   98- 98  114-114     ³
³     3-  3   19- 19   35- 35   51- 51   67- 67   83- 83   99- 99  115-115     ³
³     4-  4   20- 20   36- 36   52- 52   68- 68   84- 84  100-100  116-116     ³
³     5-  5   21- 21   37- 37   53- 53   69- 69   85- 85  101-101  117-117     ³
³     6-  6   22- 22   38- 38   54- 54   70- 70   86- 86  102-102  118-118     ³
³     7-  7   23- 23   39- 39   55- 55   71- 71   87- 87  103-103  119-119     ³
³     8-  8   24- 24   40- 40   56- 56   72- 72   88- 88  104-104  120-120     ³
³     9-  9   25- 25   41- 41   57- 57   73- 73   89- 89  105-105  121-121     ³
³    10- 10   26- 26   42- 42   58- 58   74- 74   90- 90  106-106  122-122     ³
³    11- 11   27- 27   43- 43   59- 59   75- 75   91- 91  107-107  123-123     ³
³    12- 12   28- 28   44- 44   60- 60   76- 76   92- 92  108-108  124-124     ³
³    13- 13   29- 29   45- 45   61- 61   77- 77   93- 93  109-109  125-125     ³
³    14- 14   30- 30   46- 46   62- 62   78- 78   94- 94  110-110  126-126     ³
³    15- 15   31- 31   47- 47   63- 63   79- 79   95- 95  111-111  127-127     ³
³                                                                              ³
³                                                                              ³
³                                                                              ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
°°°°°°°° ARROWS-Movement   S-Swap   SPACEBAR-Change   F10-Save  ESC-Exit °°°°°°°


To change (translate) an incoming ASCII value:

  1. Move the half-box cursor to the desired ASCII value/character you want to
     strip or replace.  The number to the left of the dash is the original ASCII
     value; the number on the right  is the translated character which you will
     see when the original character is received.

  2. Press the Space Bar once.  A prompt will appear at the bottom of the screen
     asking for an number between 0 and 255.  To strip the character, replace
     the number on the right with a 0 (ZERO).

  3. Press [ENTER] to complete the change.

The original ASCII specification  was a 7-bit code allowing for 128 characters
(0-127).  All modern-day computers add an 8th bit in front of the original 7 to
allow another 128 characters.  This 8th bit is also referred to as the High Bit.
Pressing the [S] key will alternate the translate table display between the
lower 128  (0-127) and higher 128 (128-255) characters.

Note that although a standard exists for most "lower" ASCII characters, this is
not true of the "upper" 128 values.  These High-Bit values are assigned freely
by each computer manufacturer.  For example, Apple, IBM, and Commodore use
radically different standards in assigning characters to these higher values
(the IBM PC uses the high-bit values for the international character set,
symbols, and line/box-drawing characters).

When you are finished,  press [F10] to save the changes (if any) or [ESC] to
abort the changes and return to the terminal screen.

NOTE: If you do make a change, and press [ESC], you will be asked if you
      want to save your changes.  Respond  with [Y] if you do want to save
      the changes or [N] if you really don't.


                                                               Qmodem SST     73




Alt-B  Beeps and Bells Toggle
The speaker is used as an audible warning when certain events occur (i.e.,
successful connection, or completion of a file transfer).   Since the speaker
volume  cannot be adjusted,  you may wish to turn it off.  You can toggle the
noise on and off with Alt-B.


Alt-C  Clear Screen
This command clears the screen of all information and resets default colors; a
very useful feature.  For example, those ANSI color screens displayed on certain
Bulletin Boards can utterly mess up your screen colors, sometimes leaving your
screen black-on-black which is hard to read.  Using Alt-C will reset the color
on your screen back to your configuration selections;  a real lifesaver.

NOTE: If screen colors were changed while executing a Script command, the
      new screen colors will only remain in effect until the script
      terminates.  Once the Script has ended, default colors are restored
      (but may require an Alt-C to invoke them).


NOTE: In VT100 emulation mode, Alt-C only clears the active screen area
      between the top and bottom margins.  This area is referred to as the
      Scrolling Region.


Alt-D  Dialing Directory
The Dialing Directory can hold up to 200 entries, each containing information
such as:  name, number, communications parameters, auto-logon script name, date
of last connect, total connections, default transfer protocol, and duplex mode.

Each directory entry has the ability to have "Note Files" attached.   This file
is a standard ASCII text file intended to hold all information relating to that
entry: information about the System being called, hours of operation, Sysop
name, and so on.

The size of this text file is limited only by the amount of memory  not
allocated or 60K, which-ever comes first.  Entries with attached Notes are
identified in the Dialing Directory with a triple-bar symbol (or Alt-N/O/C/N if
you have changed the default) immediately following the entry's number.  Entry
#1 in the following snapshot has an attached Note File.



















74   The Forbin Project, Inc.




ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Phone Book ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Page  1 of C:\QMODEM\QMODEM.FON                                              ³
³ Total Tags > 0                        Prefixes > BC                          ³
³[D]   Name                             Number          Port       Script      ³
³1  ð  The Forbin Project BBS           1-319-233-6157  38400 8N1              ³
³2                                                      38400 8N1              ³
³3                                                      38400 8N1              ³
³4                                                      38400 8N1              ³
³5                                                      38400 8N1              ³
³6                                                      38400 8N1              ³
³7                                                      38400 8N1              ³
³8                                                      38400 8N1              ³
³9                                                      38400 8N1              ³
³10                                                     38400 8N1              ³
ÆÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Commands ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍµ
³            Entries                    Dial                   FON             ³
³   ^SP/SP - Tag-P/Tag-Untag        M - Manual Dial        F - Find Text       ³
³    I-Ins - Insert New Entry                              A - Find Again      ³
³ ^D/D-Del - Delete Tagged/Bar          Edit               L - Load            ³
³     ^R/R - Revise Tagged/Bar      E - Edit Prefixes      O - Other Info      ³
³        T - Tag Multiple           N - Attached Note   ^P/P - Print 132/80    ³
³        U - Untag All              V - Linked Script      S - Sort            ³
³        Q - QuickLearn                                   ^U - Undo            ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍF1 HelpÍÍÍ¾
°°°°°°°°°° ,PgUp/Dn,^PgUp/Dn-Move Scroll Bar   ENTER-Dial   ESC-Exit °°°°°°°°°


The Dialing Directory screen is divided into 2 sections:   The upper section
displays directory entries, the current page, the number of tagged entries (more
on this in a moment), the number of pre-defined Dialing Prefixes, and the actual
entries on the page.  The lower screen section displays all available Dialing
Directory commands.

TIP: If your PC has EGA or VGA display capabilities, or is able to display
     at least 43 lines on the screen, the directory will display an
     additional 10 lines entries per screen!


What this snapshot does not show is the scrollbar cursor,  a screen-wide
highlight identifying the current directory entry.  Instructions on moving the
scrollbar cursor are shown in the Alt-D status line.


MOVEMENT COMMANDS
Up/Down - PgUp/PgDn - ^PgUp/^PgDn
The Up and Down arrow keys move the scrollbar cursor one line at a time in the
corresponding direction.

Pressing [PgDn] displays the next directory page unless the last page is
displayed.  Pressing [PgDn] while in the last directory page causes wrap around
back to the first directory page.  The same principle applies to the [PgUp] key,
but in the opposite direction of course.

[^PgUp] will position the scrollbar cursor to the FIRST entry in the directory
(#1), while [^PgDn] positions the cursor at the LAST entry (#200).




                                                               Qmodem SST     75



Entries
^SP/SP  Spacebar Tagging entries
A number of Dialing Directory commands operate on tagged entries.  Therefore, it
is important to understand  what tagging is.  We will then be able to describe
how it is done.

Basic dialing directory commands such as Revise, Delete, and Dial,  act only on
entries that are tagged.  For example, to Delete one or more entries, you first
tag the entries to be deleted, then select the Delete option.  To build a
dialing queue, tag the desired entries, and press [ENTER].  As you will see,
there are many methods to accomplish the same things, each having its
advantages.  The rest of the commands are there to make Qmodem easier to use.

There are three methods used to tag entries; Pressing the [Spacebar] or
[^Spacebar], the [Q] key, and a third method called implied tagging.  The
Spacebar is the most commonly used tagging method.  "Q" tagging will be briefly
discussed here, but will be covered in more detail later on.  Implied tagging
will be discussed under the Deleting Entries heading.

Tagged entries are identified in two different ways:

  1. They are displayed in a different color (provided your color setup defines
     them as such), and

  2. They are preceded by the special check-mark character "û" ,"Q" or "P".

"What is the difference between the "û" , "P",and the "Q" tags? "

Good question.  If the Script field is blank or contains a Script name and the
Script exists, then the "û" tag is used.  If a Script name is specified for that
entry, but the script file does not exist, the letter "Q" is used as a tag
character instead.  If your phone entry uses Prefix modifiers, it is possible to
dial the entry without them by using the ^Spacebar.  This puts the letter P
where the Q would have been.

"So why the letter "Q", anyway?"

Another good question.  "Q" stands for "QuickLearn", the automatic script
building part of Qmodem.  As the connection is established, QuickLearn records
your interaction with the remote computer and creates a Script file which
exactly replicates these actions the next time you call.  As a result, the logon
process becomes automated.  A complete description of the QuickLearn facility is
included later on in this manual.  We think that QuickLearn sure beats a poke in
the eye with a sharp stick.  It is a neat feature, well worth paying for.

"I now have entries tagged...  now what?"

Now you can Dial them, Revise them, or Delete them!

TIP: Un-tagging an entry is as simple as tagging it; use the Spacebar
     again.  With the cursor on a tagged entry, pressing the Spacebar
     removes the tag.



I, Ins  Insert New Entry
Adding new entries has never been easier!  Simply move the Scrollbar to where
you want to place the new entry and press either [I] or [INS].  All entries from
the Scrollbar down are moved downward and a new blank entry is inserted.

76   The Forbin Project, Inc.




When you insert a new entry, another entry must be deleted.  The phone book is
searched from bottom to top to find the first blank entry, then deleted.  If
there are no blank entries, then the Insert command is aborted.  You have to
delete an entry before inserting another one.

After the entry has been inserted, you can then use the Revise command to modify
it.


^D/D, Del  Deleting Entries
Deleting multiple entries requires that they first be tagged.  Does this mean
that you must tag a single entry before you revise or clear it?   No, not quite.

If there are no tagged entries, it is assumed that the command applies to the
entry at the cursor.  Internally, the current entry is tagged,  then the
requested command is executed.  This is the implied tagging method mentioned
earlier, which requires no specific tagging action on your part.  Thus, to
perform operations against single entries,  you do nothing more than issue the
command; Qmodem does the rest.  To clear a single entry, move the scrollbar
cursor to it, and press either [D] or [Del].

Implied tagging cannot be used when multiple entries are tagged explicitly.  To
clear multiple entries, tag them first with the Space Bar, then press [^D].  The
scrollbar cursor will move to the first tagged entry and will display the Delete
Entry menu.

CAUTION:If multiple entries are already tagged as the result of a previous
        operation (i.e., dialing), and you wish to delete a single entry,
        REMOVE ALL TAGS FIRST by typing "U".  Since tagged entries may be
        elsewhere in the directory, and not visible in the current page, it
        is easy to assume that implied tagging will work, when in fact it
        will not.  It is advisable to check the Tag Count displayed at the
        top of the dialing directory screen before attempting any "implied-
        tag" commands.


Now that you understand the difference between explicit and  implicit tagging,
let's look at an example.  In the screen below, entry #5 was tagged, and [^D]
was pressed:




















                                                               Qmodem SST     77



ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Phone Book ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Page  1 of Z:\docsfon.FON                                                    ³
³ Total Tags > 1                        Prefixes > ABC                         ³
³[D]   Name                             Number          Port       Script      ³
³1  ð  Test Node at Forbin              1-319-555-1212  38400 8N1  TESTING.SCR ³
³2     Forbin Project BBS               1-319-233-6157  38400 8N1  FORBIN.SCR  ³
³3                                                      38400 8N1              ³
³4                                                      38400 8N1              ³
³5  ðû Old BBS to Delete                      555-1212   1200 8N1              ³
³6                                                      38400 8N1              ³
³7     GEnie Local 2400 access #            `B555-1212   2400 8N1  GENIE.SCR   ³
³8                                                      38400 8N1              ³
³9                      ÕÍ Delete Entries and/or Notes ÍÍ¸400 8N1              ³
³10                     ³                                ³400 8N1              ³
ÆÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ³      1.  Notes Only            ³ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍµ
³            Entries    ³      2.  Entries & Notes       ³     FON             ³
³   ^SP/SP - Tag-P/Tag-U³    ESC.  Return to Directory   ³ F - Find Text       ³
³    I-Ins - Insert New ³                                ³ A - Find Again      ³
³ ^D/D-Del - Delete Tagg³ Your Choice ?                  ³ L - Load            ³
³     ^R/R - Revise TaggÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾ O - Other Info      ³
³        T - Tag Multiple           N - Attached Note   ^P/P - Print 132/80    ³
³        U - Untag All              V - Linked Script      S - Sort            ³
³        Q - QuickLearn                                   ^U - Undo            ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍF1 HelpÍÍÍ¾
°°°°°°°°°° ,PgUp/Dn,^PgUp/Dn-Move Scroll Bar   ENTER-Dial   ESC-Exit °°°°°°°°°


The Delete Entry window serves a dual purpose.  It can delete Attached Notes
from an entry, or it can delete both the Notes and the entry itself.  Entries
cannot be deleted without Attached Notes being deleted as well.

In the example above, entry #5 has an attached Note. Selecting option #2 from
the menu would delete the Note file as well as the entry.  If entry #5 did not
have an attached Note and we selected Option #1, no action would be taken.

CAUTION:The menu option you select is applied to ALL tagged entries.  To
        clear "Notes only" from certain tagged entries cannot be done and
        requires a separate operation.


The complete Phone Book is backed up prior to deleting entries if you have the
Alt-N/O/T/F/W set ON.  In either case, the Note files are never backed up.  Once
Notes are cleared, they cannot be restored.


^R/R - Revise Tagged/BAR
The Revise command is used to edit directory entries.  Multiple entries can be
revised in a group.  Simply tag all the entries you want to revise and press
[^R].  If no entries are tagged, pressing [R] will revise the current entry
(implicit tagging).  If multiple entries are tagged and you press [R], only the
entry under the Scrollbar will be revised.









78   The Forbin Project, Inc.



The Revise Entry window looks like this:


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Phone Book ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Page  1 of D:\QMODEM\DOCSFON.FON                                             ³
³ Total Tags > 0                        Prefixes > ABCEF                       ³
³[D]   Name                             Number          Port       Script      ³
³1  ð  Test Node at Forbin                  EF555-1212  38400 8N1              ³
³2                ÕÍÍÍÍÍÍÍÍÍÍÍÍÍ Revise Entry ÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸ 8N1              ³
³3                ³ Name        Test Node at Forbin°°°°°°°° ³ 8N1              ³
³4  ð  Executive N³ Number      1-319-233-6157°°°°°         ³ 8N1              ³
³5                ³ Password    °°°°°°°°°°°°°°              ³ 8N1              ³
³6                ³ Script      °°°°°°°°°°°°                ³ 8N1              ³
³7     GEnie Local³ Baud Rate   38400°                      ³ 8N1              ³
³8                ³ Data Bits   8                           ³ 8N1              ³
³9                ³ Parity      N                           ³ 8N1              ³
³10               ³ Stop Bits   1                           ³ 8N1              ³
ÆÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ³ Duplex      F                           ³ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍµ
³            Entri³ Protocol    X                           ³  FON             ³
³   ^SP/SP - Tag-P³ Last Call   08-09-90                    ³- Find Text       ³
³    I-Ins - Inser³ Times On    0°°°°                       ³- Find Again      ³
³ ^D/D-Del - DeletÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍF1 HelpÍÍ¾- Load            ³
³     ^R/R - Revise Tagged/Bar      E - Edit Prefixes      O - Other Info      ³
³        T - Tag Multiple           N - Attached Note   ^P/P - Print 132/80    ³
³        U - Untag All              V - Linked Script      S - Sort            ³
³        Q - QuickLearn                                   ^U - Undo            ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍF1 HelpÍÍÍ¾
°°°° Change the NAME field                         [F10] Save   [ESC] Abort °°°°


This is one of the several  Mult-field Edit windows in Qmodem.  You simply move
the cursor to where you want and make the change.  Several fields in the menu
allow popping up a Pick List by pressing [F2] when the cursor is in the field.
Check the Status line as you cursor through the fields.

Once you have completed changing the information, press [F10] to save the
changes.  In the unlikely event you made a mistake, pressing [ESC] will restore
the entire entry.

When revising multiple tagged entries, the Revise Menu will display the entries
one at a time, in sequence.  As each entry is saved (or you exit the Revise Menu
via [ESC]), the next entry will be displayed, until all tagged entries have been
processed.


T - Tag Multiple
Tag Multiple is used to tag entries based on their entry number or the text
content of their Name, Number field, or Attached Note file.  In addition, Tag
Multiple can be used to add or delete Prefix codes from entry phone numbers.











                                                               Qmodem SST     79



Pressing [T] will display a small prompt window in the Command area:


ÆÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Commands ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍµ
³            Entries                    Dial                   FON             ³
³   ^SP/SP - Tag-P/Tag-Untag        M - Manual Dial        F - Find Text       ³
³    I-Ins - Insert New Entry                              A - Find Again      ³
³ ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Select Entries ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸    ³
³ ³ Numbers to TAG > °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°° ³    ³
³ ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾    ³
³        U - Untag All              V - Linked Script      S - Sort            ³
³        Q - QuickLearn                                   ^U - Undo            ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍF1 HelpÍÍÍ¾
°°°°°°°°°° Enter line #'s,  P[prefixes]#[suffixes],  T-Text  ESC-Exit °°°°°°°°°°


Let's review the options displayed on the status line.

Enter line #'s

  Used to tag entries based on their number in the directory.  To tag entries
  1, 22, 23 and 40, you would type:


³ ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Select Entries ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸    ³
³ ³ Numbers to TAG > 1 22 23 40°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°° ³    ³
³ ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾    ³


  This feature is reminiscent of earlier releases of Qmodem which prompted the
  user for the numbers to be dialed.

P[prefixes]#[suffixes]

  A prefix or suffix may be added to, changed, or deleted from an entry's phone
  number by preceding that entry's number with the letter 'P'.

  For example, to dial entry #1 and add the prefix modifier 'A' to the
  beginning and 'B' to the end of the number, you would type:


³ ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Select Entries ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸    ³
³ ³ Numbers to TAG > PA1B°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°° ³    ³
³ ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾    ³


The 'P' modifier means that one or more prefix codes will precede or follow the
entry number, and that these are to be added to the entry's phone number.  In
the example above, the prefix 'A' is added before the number, and 'B' following
it.










80   The Forbin Project, Inc.



To REMOVE  Suffix 'B' from entry #1, we would type:


³ ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Select Entries ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸    ³
³ ³ Numbers to TAG > PA1°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°° ³    ³
³ ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾    ³


Since the 'A' prefix is kept, it is typed.  'B' was not included, so the 'B'
suffix is removed.   Taking this one step further, to remove all
prefixes/suffixes from entry #1, we would type:


³ ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Select Entries ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸    ³
³ ³ Numbers to TAG > P1°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°° ³    ³
³ ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾    ³


T[text]

  Allows tagging of entries based on a text search:

     1.NAME field,
     2.NUMBER field, and
     3.Attached NOTE files

  Each text string to be searched is preceded by the letter 'T'.  Using the
  previous phone book example, let's tag all the entries in the 319 area code,
  as well as those using V9600 modems (we kept the modem information in the
  Attached Note Files):


³ ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Select Entries ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸    ³
³ ³ Numbers to TAG > T319 TV9600°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°° ³    ³
³ ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾    ³

_____________________________

NOTE: The leading 'T' is not case sensitive and text search arguments must
      be separated by at least one space.  Also, text search arguments may
      not contain imbedded spaces.  The space, the letter 'T', and the end
      of the prompt line are text search delimiters.


Tag Multiple is a powerful tool in the Alt-D arsenal.

U - Untag All
Pressing [U] will remove all tags in the directory.

TIP: When you are about to use an "Implied Tag" command on the current
     entry, make sure other entries are not tagged (the tag count is
     displayed at the top of the directory screen).  If entries are tagged,
     you may want to use Untag All to remove the tags before proceeding
     with the command.






                                                               Qmodem SST     81



Q - QuickLearn
Pressing [Q] toggles the QuickLearn  tag for the current entry if the Script
field is non-blank.  Connecting to a Q-tagged entry activates the QuickLearn
Script Recorder.

TIP: You can force QuickLearn by using the letter "Q" to tag the entry
     instead of the Spacebar.  When you connect, QuickLearn starts
     rewriting the Script for you!


The QuickLearn feature is described in detail under the Alt-Q command.


Dialing
ENTER - Start dialing
Pressing [ENTER] will begin dialing tagged entries in numerical order starting
from the current scrollbar position.  If no entries are tagged, the current
entry will be tagged and dialed immediately.  The Redialer will cycle through
the tagged entries until a connection is made or you press [ESC] to halt the
process.

NOTE: Qmodem will not dial entries with blank phone numbers.  Also, the
      information in the number field is not checked for validity.

Following is the Redialer window:


ÆÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Redialer ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍµ
³                                                                              ³
³     Name   : The Forbin Project PCBoard               Last On : 08-09-90     ³
³     Number : 233-6157                                 Total # : 10112        ³
³     Script : FORBIN.SCR                               Attempt : 1            ³
³                                                                              ³
³     Modem  : ATDT233-6157                             Start   : 22:49:34     ³
³     Status : 50  Seconds remain until Cycle           Current : 22:49:34     ³
³                                                                              ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
°°°°°°°°°°°°°°°°° C-Cycle   K-Kill   X-Extend Timer   ESC-Exit °°°°°°°°°°°°°°°°°


The Dialer screen is divided into four areas, each containing information
relating to the call in progress and to the entry being dialed:

The upper left identifies the dialed entry by name and phone number, and the
name of the attached Script, if any.  The lower left tracks the commands sent to
the modem and the responses received from it.  The status line displays timely
information on the call in progress.  The upper right displays the date of last
connect, the total number of successful connections to the entry being dialed,
and the number of dialing attempt during the current session.  The lower right
displays the time at which the dialing session was started, as well as the
current time of day.

While in the dialer window, the following commands are valid:

[C]ycle

  Pressing [C] cancels the current call and start dialing the next tagged
  entry.


82   The Forbin Project, Inc.




[K]ill

  Pressing [K] cancels the current call and untags it, effectively removing it
  from the dialing queue.

[X]tend Timer

  Pressing  [X] key increases the dial cycle delay by 5 seconds.  The cycle
  delay is the amount of time the Redialer waits for a connection before
  dialing the next entry (or the same entry if only one is being called). This
  delay is defined in the Alt-N/M/C/H setup menu.

[ESC]

  Pressing [ESC] cancels the current call and exits the dialer.  Explicitly
  tagged entries remain tagged.

The Status message area reports messages from the modem and the redialer.  Modem
messages are returned in response to dialing commands and may include codes such
as BUSY, NO CARRIER, VOICE, and so on.

NOTE: Extended responses such as BUSY, VOICE, and RINGING may not be
      implemented by your particular modem.  Check your modem manual to
      determine which return codes are available.  Modem responses are
      defined in the Alt-N/M/M setup menu.


The Dialer may return the following status messages:

  Manual Cycle

     You pressed [C] to Cycle.


  Number has been un-tagged

     [K] was pressed to remove the entry.


  [ESC] pressed, Dialing aborted

     [ESC] was pressed, and you are returned to Command mode.


  Dial timing period expired

     The cycle delay expired before a connection was made.


  Line busy or modem timed out

     One of the four modem Error messages (Alt-N/M/M) was returned and the call
     was cancelled.






                                                               Qmodem SST     83



  CONNECTED, press a key to continue

     The modem returned the Connect message (Alt-N/M/M/C) and is now on-line.
     If the entry has an attached script, this message will be immediately
     erased, you will exit the dialer, and control will be passed to the script.
     If no script is attached to the entry, press any key to return to the
     terminal screen to view the on-line session.


  Redial pausing XXX

     The previous attempt was unsuccessful and the dialer is waiting before
     placing the next call.


  Dialing halted. Incoming call detected

     The Redial Cancel message (Alt-N/M/M/R) was received between dial attempts,
     indicating that a call is being received at the same time dialing is
     attempted.


  XXX Seconds remain until Cycle

     The current call is in progress.  After XXX  seconds, the call will be
     cancelled if a connection is not established.  The original delay is
     specified in the Alt-N/M/C/H setup menu.

NOTE: Most modems have an internal timer which will cause the unit to hang
      up after waiting for a specific time for a connection to be made (most
      have a 60 second default).  If the modem hangs up before the delay
      expires, your modem's delay is shorter than the Alt-N/M/C/H setting.
      It is advised that you set the modem's delay to a value high enough
      not to conflict with the Qmodem setting.



Parameters passed to Scripts
Prior to passing control to a linked script, the redialer updates the values in
the following pre-assigned string variables:

     $BOARD    the name of field.
     $NUMBER   the number called.
     $SPEED    the current baud rate.
     $COM      the parity, data and stop bits.
     $PASSWORD the password field.
     $PROTOCOL the default transfer protocol.
     $SCRIPT   the name of the linked script.
     $NOTEFILE the name of the attached Note file.

These variables remain in effect for the duration of the script.  For more
information on scripts and string variables, refer to the Script Language
Section in this manual.


M - Manual Dial
When a number is not in the dialing directory, it can be dialed manually.
Pressing 'M' displays the Manual Dial window:


84   The Forbin Project, Inc.




ÆÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Commands ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍµ
³            Entries                    Dial                   FON             ³
³   ^SP/SP - Tag-P/Tag-Untag        M - Manual Dial        F - Find Text       ³
³    I-Ins - Insert New Entry                              A - Find Again      ³
³ ^D/D-Del -ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Manual Dial ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸ Load            ³
³     ^R/R -³ Phone number > °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°  ³ Other Info      ³
³        T -ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾ Print 132/80    ³
³        U - Untag All              V - Linked Script      S - Sort            ³
³        Q - QuickLearn                                   ^U - Undo            ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍF1 HelpÍÍÍ¾
°°°°°°°°°°°°°°°°°°° Enter the phone number to call   ESC-Exit °°°°°°°°°°°°°°°°°°


Manual dial commands may contain up to 30 characters and/or digits.  The number
is not checked for validity.  The data typed in the Phone Number field will be
passed to the modem  as if it was attached to a real entry.  Any Prefix modifier
will be substituted accordingly.


{F2}-{F12}  Speed Dialing
Another new feature is Function Key Speed Dialing.  Eleven function keys, [F2]
through [F12], can be added to the Name Field, or the Attached Notes to allow
for dialing 1 or a groups of numbers.   Alt-N/O/F/C , Clear on FKey, controls
whether or not the Untag All command is executed before tagging the entries
linked to the Fkey.

You use the left and right curly braces { } to surround the Fkey name.  Like
this:


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Phone Book ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Page  1 of Z:\QMODEM.FON                                                     ³
³ Total Tags > 0                        Prefixes > ABC                         ³
³[D]   Name                             Number          Port       Script      ³
³1     Sub Line 7            {F9}             233-6035  38400 8N1  FORBIN!     ³
³2     Home Qmodem Host                       235-0074  38400 8N1  QHOST!      ³
³3  ð  Sub Line 2            {F11}            233-6157  38400 8N1  SYSOP2      ³
³4     Sub Line 3            {F10}            233-6256  19200 8N1  SYSOP2      ³
³5     Sub Line 4            {F10}            233-6324  38400 8N1  SYSOP2      ³
³6     Sub Line 5            {F10}            233-6006   2400 8N1  SYSOP2      ³
³7     Sub Line 6            {F10}            233-9834  38400 8N1              ³
³8     Exec-Net               {F3}      1-914-667-4066  38400 8N1  EXECNET     ³
³9     Sub Line 1                             233-1453  38400 8N1  SYSOP2      ³
³10    GEnie_Local                            233-7623  38400 7E1  GENIE.F2    ³


In the above example, 4 FKeys are used as hot-keys.  {F3}, {F9} and {F11} each
dial a single entry in the FON book.  {F10} on the other hand, will tag 4
entries all at the same time!  Remember, the Fkey definition does not have to be
in the Name field.  It can be quietly tucked away in the attached Note file of
an entry too!








                                                               Qmodem SST     85



Edit
E - Edit Prefixes
Prefix characters are used at the beginning or end of phone numbers (or anywhere
between) to add standard and repetitive dialing information to the numbers as
they are dialed.   A prefix may be as simple as "Dial 9 to get out" or "Dial 1
for long distance", or it may hold a 7-digit SPRINT or MCI local access number.
When used at the end of a number, the prefix becomes a Suffix which may be used
to store a PBX access code, for example.  In special cases, prefixes may even be
used to store Alternate Dialing Commands.

Pressing [E] displays the Prefix edit window:


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Phone Book ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Page  1 of D:\QMODEM\DOCSFON.FON                                             ³
³ Total Tags > 0                        Prefixes > ABCEF                       ³
³[D]   Name                             Number          Port       Script      ³
³1  ð  Test Node atÕÍÍÍÍÍÍÍÍÍ Revise Prefixes ÍÍÍÍÍÍÍÍÍ¸38400 8N1              ³
³2                 ³ A  ATDT°°°°°°°°°°°°°°°°°°°°°°°°°° ³38400 8N1              ³
³3                 ³ B  AT&M0DT°°°°°°°°°°°°°°°°°°°°°°° ³38400 8N1              ³
³4  ð  Executive Ne³ C  AT&M4DT°°°°°°°°°°°°°°°°°°°°°°° ³38400 8N1              ³
³5                 ³ D  °°°°°°°°°°°°°°°°°°°°°°°°°°°°°° ³38400 8N1              ³
³6                 ³ E  555-1212,,°°°°°°°°°°°°°°°°°°°° ³38400 8N1              ³
³7     GEnie Local ³ F  1234567,°°°°°°°°°°°°°°°°°°°°°° ³ 2400 8N1              ³
³8                 ³ G  °°°°°°°°°°°°°°°°°°°°°°°°°°°°°° ³38400 8N1              ³
³9                 ³ H  °°°°°°°°°°°°°°°°°°°°°°°°°°°°°° ³38400 8N1              ³
³10                ³ I  °°°°°°°°°°°°°°°°°°°°°°°°°°°°°° ³38400 8N1              ³
ÆÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ³ J  °°°°°°°°°°°°°°°°°°°°°°°°°°°°°° ³ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍµ
³            EntrieÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍF1 HelpÍ¾       FON             ³
³   ^SP/SP - Tag-P/Tag-Untag        M - Manual Dial        F - Find Text       ³
³    I-Ins - Insert New Entry                              A - Find Again      ³
³ ^D/D-Del - Delete Tagged/Bar          Edit               L - Load            ³
³     ^R/R - Revise Tagged/Bar      E - Edit Prefixes      O - Other Info      ³
³        T - Tag Multiple           N - Attached Note   ^P/P - Print 132/80    ³
³        U - Untag All              V - Linked Script      S - Sort            ³
³        Q - QuickLearn                                   ^U - Undo            ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍF1 HelpÍÍÍ¾
°°°°°°°°° Edit Prefix Characters   F10-Save   ESC-Exit with no changes °°°°°°°°°


Qmodem allows up to 10 Prefix codes, assigned the letters  A through J.  Each
prefix code can store up to 30 characters.

In the example above, 5 Prefix codes have been defined.  Also note that the
phone number for entry #1 contains codes E and F.  You can use multiple Prefix
codes in any position of the Number field.

CAUTION:Do NOT define a phone number using its Alpha representation.
        Numbers such as "1-800-DECDEMO" may be a valid telephone number,
        but the Dialer will substitute the prefix values of letters A-J in
        any phone number.  For all we know, 1-800-DECDEMO might get you
        connected with Outer Mongolia ($98.55 a minute).


NOTE: Make sure that the total length of the dialed number AND prefix(es)
      does not exceed your modem's maximum command length.  This maximum
      should be listed in your modem's operation manual.  Most modems limit
      dialing input to 40 characters.


86   The Forbin Project, Inc.




If you have a Hayes-compatible modem, you will notice that Prefix codes A, B,
and C look amazingly similar to the Modem Dialing Command  defined in
Alt-N/M/M/P.  That's because these prefixes are dialing commands.

To use these alternate dialing commands, precede the desired prefix with the
special character ` (left tick mark or single end quote).  When it detects that
special character, it will use the prefix code which immediately follows instead
of the Alt-N default dialing command.

Example:


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Phone Book ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Page  1 of C:\QMODEM\QMODEM.FON                                              ³
³ Total Tags > 0                        Prefixes > BC                          ³
³[D]   Name                             Number          Port       Script      ³
³1  ð  The Forbin Project BBS               `A233-6157  38400 8N1              ³
³2     Test Node #2                   `C1-319-233-6157  38400 8N1              ³
³3     Test Node #3                         `B555-1212  38400 8N1              ³
³4                                                      38400 8N1              ³


The example above assumes a modem with an MNP error-correction mode that is
enabled with the AT&M4 command, and it is disabled with the AT&M0 command.   The
DT "Dial Tone" command tells the modem to tone-dial the number which follows.

In the example above, entry #2 will be dialed with an AT&M4DT command, which
enables MNP error-correction and dials the Forbin Project (which operates a few
HST modems). .  Entry #3 will be dialed with an AT&M0DT command, which disables
MNP error-correction and dials 555-1212.  Entry #1 will be dialed with a
standard ATDT command which will not affect the current state of MNP error
correction.

TIP: If you use the ` modifier to enable or disable one or more of your
     modem's features, be sure to set the default dialing prefix
     (Alt-N/M/M/P) to the mode which you use most often.  By doing this,
     you only need to override entries that do not conform to the default
     mode.  In the previous example, your default dialing prefix should be
     "AT&M4DT".  Prefix `B would  be used to dial non-MNP systems.



N - Attached Notes
Textual information can be "Attached" to each directory entry and retrieved with
a single keystroke.  The data is stored in special Note Files which can be
edited with the Internal Editor or any editor of your choice (as defined in
Alt-N/F/V).

To create a note file, update an existing note, or view one, move the Scrollbar
to the entry and press "N".  The Note command is an immediate command and does
not affect the tagging of other entries.  When you press "N", the current
entry's Note File will be edited.







                                                               Qmodem SST     87



The following example demonstrates the use of the Internal Editor:


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Notes for The Forbin Project PCBoard ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³      Line 1    Col 1          Indent     D:DOCSFON.1                         ³
³NAME: Forbin BBS                                                              ³
³DESC: Home of Qmodem                                                          ³
³BBS : PCBoard 14.5 (Alpha test site)                                          ³
³BAUD: 1200-38400                                                              ³
³MODM: HST Dual Standards                                                      ³
³HRS : 24 hrs/day                                                              ³
³NETS: InterLink, SmartNet, RIME                                               ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
°°°°°°°°°°°° F1-Help  F2-Save  F3-New  F9,ESC-Abort  F10-Save & Exit °°°°°°°°°°°


The internal editor screen overlays the command area at the bottom of the
screen.  The current entry's name is shown in the editor window's label.

TIP: In the example above, the note is used to store useful information
     which cannot be stored into the dialing directory itself.  Using this
     method to document directory entries allows the use of the Text Search
     function (or a text search argument in a Tag command) to locate
     entries based on BBS software, the type of modem in use, or supported
     baud rates.


The names assigned to Note Files are transparent to the user.  These names are
assigned permanently when the directory is created.  Note files have the same
file name as the directory to which they are attached, and their file extension
is a number in the range 1..200, corresponding to the entry to which that
specific note file is attached.  The name of each note file is stored in each
directory entry, which allows sorting of the directory without losing the Note
File linkage.

NOTE: If you use an external editor, make sure that is creates standard
      CR/LF-delimited ASCII files to insure that text search commands work
      properly.

If an entry has an attached Note, a special symbol will be displayed immediately
following the entry number in the directory.

TIP: The Attached Notes identifier can be changed via the Alt-N/O/C setup
     menu.




V - Linked Scripts
"Linked Scripts" are executed when a connection is established.  These are
commonly referred to as "Logon Scripts".  Pressing "V" allows editing of linked
scripts, much in the same way as the Revise Entry command.  The "V" command
operates the same way as the "N" command in that it is immediate and does not
affect the tagging of other entries.  When you press "V", the current entry's
linked script will be edited.

When editing a linked script, the Internal Editor uses the entire screen area.



88   The Forbin Project, Inc.



NOTE: The Script field cannot be blank for the editor to be invoked.


Following is a sample Linked Script Edit Screen (using the Internal Editor, of
course):


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Full Screen Edit ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³      Line 1    Col 1   Insert Indent     D:FORBIN.SCR                        ³
³;                                                                             ³
³;  QuickLearn Script generated at 12:16:09 on 02-20-89                        ³
³;  May require editing before use.                                            ³
³;                                                                             ³
³TurnON   8_BIT                                                                ³
³TurnOFF  LINEFEED                                                             ³
³TurnON   XON/XOFF                                                             ³
³TurnOFF  NOISE                                                                ³
³TurnOFF  MUSIC                                                                ³
³TurnON   SCROLL                                                               ³
³TurnOFF  PRINT                                                                ³
³TurnOFF  ECHO                                                                 ³
³TurnOFF  SPLIT                                                                ³
³TurnOFF  BS_DEL                                                               ³
³;                                                                             ³
³TimeOut  30     ; Set Waitfor timeout to 30 seconds                           ³
³Waitfor  "want ANSI Graphics (Enter)=no?"                                     ³
³Delay    100                                                                  ³
³Send     "n^M"                                                                ³
³                                                                              ³
³Waitfor  "What is your first name?"                                           ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
°°°°°°°°°°°° F1-Help  F2-Save  F3-New  F9,ESC-Abort  F10-Save & Exit °°°°°°°°°°°



FON
F - Find Text
The Find Text command is used to quickly scan the dialing directory for a
specific text string.  Entry Names, Phone Numbers and Attached Notes are
searched starting with entry #1.

Following the search, the Scrollbar will be positioned on the first matching
entry.  Unlike the Tag Multiple command, matching entries are not tagged  Also
unlike Tag Multiple, you may only specify one search argument.  With the Find
Text command, search arguments may contain imbedded spaces.















                                                               Qmodem SST     89



Pressing "F" displays the Find Text prompt:


ÆÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Commands ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍµ
³            Entries                    Dial                   FON             ³
³   ^SP/SP - Tag-P/Tag-Untag        M - Manual Dial        F - Find Text       ³
³    I-Ins - Insert New Entry                              A - Find Again      ³
³ ^D/D-Del - Delete ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Find Text ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸oad            ³
³     ^R/R - Revise ³ Search for > °°°°°°°°°°°°°°°°°°°°°°°°°°° ³ther Info      ³
³        T - Tag MulÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾rint 132/80    ³
³        U - Untag All              V - Linked Script      S - Sort            ³
³        Q - QuickLearn                                   ^U - Undo            ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍF1 HelpÍÍÍ¾
°°°°°°°°°°°°°°°°°°°° Enter the text to scan for   ESC- Exit °°°°°°°°°°°°°°°°°°°°


NOTE: Remember that the text search also scans Note Files.  As a result, if
      the text is not found, the search could take a few seconds.  In
      addition, it is possible that the matching text is in a Note File,
      rather than and in the entry's name or number.  If that is the case,
      press "N" to see the note file.  Don't go off the deep end thinking
      that the text search command is broken; it isn't.


If the last entry is reached before a match is found, the message "Text not
found" will be displayed.


A - Find Again
The Find Again command repeats the last Find Text command from the next entry
forward.  If no additional matches are found, the message "No more matches" will
be displayed.


L - LOAD
The "L" command is used to load an alternate phone book.  If the new phone book
does not exist, you will be prompted to create it.

Pressing "L" displays the following window:


ÆÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Commands ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍµ
³            Entries                    Dial                   FON             ³
³  ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ FON File Allocation ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸   ³
³  ³                                                                       ³   ³
³ ^³ > D:\QMODEM\°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°    ³   ³
³  ³                                                                       ³   ³
³  ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾   ³
³        U - Untag All              V - Linked Script      S - Sort            ³
³        Q - QuickLearn                                   ^U - Undo            ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍF1 HelpÍÍÍ¾
°°°°°°°°°°°°°°°°°°°°°°°°° Edit File/Pathname   ESC-Exit °°°°°°°°°°°°°°°°°°°°°°°°


To load a new phone book, type its name (with optional drive and path
information) in the prompt window and [ENTER].  The .FON extension is not
required and will be forced on if not entered.  If the file does not exist, a
new one will be created automatically using the default parameters defined in
the Alt-N/M/C Setup Menu.

90   The Forbin Project, Inc.




All phone book files must have a .FON extension.  Should you use pre Version 4.2
phone books with a different file extension, they must be renamed with the
mandatory .FON file type (the filename may have to be changed as well to prevent
duplication).   This was made necessary when Attached Notes were added.  Since
the Note Files are assigned the same name as the directory they are attached to,
duplicate phone book filenames would present conflicts.

This restriction can be circumvented if phone books reside in separate sub-
directories as long as the phone book file extension is .FON. (i.e., QMODEM.FON)


O - Other Info
Pressing "O" alternates the dialing directory display and allows viewing of the
"right half" of the directory. Following is a display after the "O" key was
pressed.  Note the new information shown:


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Phone Book ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Page  1 of D:\QMODEM\DOCSFON.FON                                             ³
³ Total Tags > 0                        Prefixes > ABCEF                       ³
³[D]   Name                            Password        LastCall    Total  P D  ³
³1  ð  The Forbin Project PCBoard                      08-09-90    10112  G F  ³
³2                                                       -  -      0        F  ³
³3                                                       -  -      0        F  ³
³4  ð  Executive Network-InterLink                     12-02-89    21     Z F  ³
³5                                                       -  -      0        F  ³
³6                                                       -  -      0        F  ³
³7     GEnie Local Access Number       test*anguish    08-12-90    321    Z H  ³
³8                                                       -  -      0        F  ³
³9                                                       -  -      0        F  ³
³10                                                      -  -      0        F  ³


The additional directory information displayed includes fields labeled LastCall,
Total, P, and E.  "LastCall" (last CONNECT date)  and "Total" (total CONNECTS)
are maintained by the Redialer, while the P(rotocol) and E(Cho, or Duplex
setting) fields are user-defined.

NOTE: Qmodem does not maintain "Last Dialed" and "Total Dialed" fields; the
      Last Call and Total fields shown only reflect successful connections
      to the entry.



^P/P - Print
The Print command produces a formatted ASCII copy of the Phone Book on a printer
or text file.   When pressing 'P', you are prompted for a valid DOS device or
filename.  The default is defined in Alt-N/F/P.











                                                               Qmodem SST     91




ÆÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Commands ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍµ
³            Entries                    Dial                   FON             ³
³   ^SP/SP - Tag-P/Tag-Untag        M - Manual Dial        F - Find Text       ³
³    I-Ins - Insert New Entry                              A - Find Again      ³
³ ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Print Phone Book ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸  ³
³ ³ Device or File >   PRN°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°   ³  ³
³ ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾  ³
³        U - Untag All              V - Linked Script      S - Sort            ³
³        Q - QuickLearn                                   ^U - Undo            ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍF1 HelpÍÍÍ¾
°°°°°°°°°°°°° Enter the destination device or filename.   ESC-Exit °°°°°°°°°°°°°
















































92   The Forbin Project, Inc.



Note the PRN default in the window.  To override it, backspace and type  the new
device or filename:


³ ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Print Phone Book ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸  ³
³ ³ Device or File >   C:\QMODEM\SAVEFON.TXT°°°°°°°°°°°°°°°°°°°°°°°°°°°°°   ³  ³
³ ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾  ³


The above example will create a phone book listing and store it in the file
SAVEFON.TXT in the C:\QMODEM directory.  Other valid devices include LPT1:,
LPT2:, LPT3:, COM1:, etc...

Following is a sample of the formatted phone book listing when the "P" 80 Column
mode is selected:


                     Qmodem Version 4.2 Phone Book
                     =============================

Page  1   File : Z:\QMODEM.FON

           Name                           Number          Com      Script
-----------------------------------------------------------------------------
1   Sub Line 7            {F9}              555-1212  38400-8-N-1  SYSOP2
2   ZSoft BBS                         1-404-427-1045  38400-8-N-1  ZSOFT
3   Home Qmodem Host                        555-1212  38400-8-N-1  QHOST!
4   Sub Line 2            {F11}             233-6157  38400-8-N-1  SYSOP2
5   Sub Line 3            {F10}             233-6256  19200-8-N-1  SYSOP2
6   Sub Line 4            {F10}             233-6324  38400-8-N-1  SYSOP2
7   Sub Line 5            {F10}             233-6006   2400-8-N-1  SYSOP2
8   Sub Line 6            {F10}             233-9834  38400-8-N-1
9   Sub Line 1                              555-1212  38400-8-N-1  SYSOP2
10  Exec-Net               {F3}       1-914-667-4066  38400-8-N-1  EXECNET

                Qmodem Copyright (C)  The Forbin Project, Inc.
























                                                               Qmodem SST     93



The "^P" 132 Column printout looks something like this:


                     Qmodem Version 4.2 Phone Book
                     =============================

Page  1   File : Z:\QMODEM.FON

           Name                           Number          Com      Script
Password        LastCall  Total  Prot  Dup
--------------------------------------------------------------------------------
----------------------------------------
1   Sub Line 7            {F9}              555-1212  38400-8-N-1  SYSOP2
08-07-1990  12353         F
2   ZSoft BBS                         1-404-427-1045  38400-8-N-1  ZSOFT
Deluxe        07-28-1990      1         F
3   Home Qmodem Host                        555-1212  38400-8-N-1  QHOST!
Hightension   06-11-1990   2029         F
4   Sub Line 2            {F11}             233-6157  38400-8-N-1  SYSOP2
05-16-1990   1817   F     F
5   Sub Line 3            {F10}             233-6256  19200-8-N-1  SYSOP2
10-15-1989   1788   F     F
6   Sub Line 4            {F10}             233-6324  38400-8-N-1  SYSOP2
12-02-1988   1774   F     F
7   Sub Line 5            {F10}             233-6006   2400-8-N-1  SYSOP2
04-23-1990   1765   F     F
8   Sub Line 6            {F10}             233-9834  38400-8-N-1
06-09-1990   1711         F
10  Exec-Net               {F3}       1-914-667-4066  38400-8-N-1  EXECNET
07-17-1990   1633   F     F

                Qmodem Copyright (C)  The Forbin Project, Inc.


The previous display is a sample printout merged into this document.  Your own
output will be different, of course.  Each page contains a standard header with
page numbers, the name of the Phone Book being printed, and the actual phone
book entries.

The entry numbers shown in the listing are assigned sequentially starting with
number 1.  Since the Print command does not process blank entries, these  number
are NOT the same as the entries' number shown in the Phone Book

NOTE: Entries and listing numbers will match only if blank entries appear at
      the end of the phone book -- i.e., no empty entries are imbedded
      between non-blank entries --.



S - Sort
The Sort command, as its name indicates, sorts the phone book in one of three
user-selected sequences:

  1. By Name field
  2. By Phone Number field
  3. By Total Connects




94   The Forbin Project, Inc.




ÆÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Commands ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍµ
³            Entries                    Dial                   FON             ³
³   ^SP/SP - Tag-P/Tag-UntagÕÍÍÍÍÍÍÍÍ Sort FON By: ÍÍÍÍÍÍÍÍ¸ - Find Text       ³
³    I-Ins - Insert New Entr³ 1 - Name (ascending)         ³ - Find Again      ³
³ ^D/D-Del - Delete Tagged/B³ 2 - Number (ascending)       ³ - Load            ³
³     ^R/R - Revise Tagged/B³ 3 - Total Calls (descending) ³ - Other Info      ³
³        T - Tag Multiple   ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾ - Print 132/80    ³
³        U - Untag All              V - Linked Script      S - Sort            ³
³        Q - QuickLearn                                   ^U - Undo            ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍF1 HelpÍÍÍ¾
°°°°°°°°°°°°°°°°°° NUMBER-Pick a method to Sort By   ESC-Exit °°°°°°°°°°°°°°°°°°


To select the sort field, press 1, 2, or 3 and then [ENTER] to Sort,   or press
[ESC] to cancel the operation.  Name and Number sorts are in Ascending ASCII
sequence (A), with  number being sorted before letters.  Sorts by Total Calls
are in Descending sequence.   As a result, the most-frequently called entries
will  move toward the top of the Phone Book (higher numbers being placed first).

NOTE: As a safety measure, the Phone Book is backed up prior to being
      sorted.  Should you change your mind, the previous unsorted copy of
      the Phone Book can be restored immediately via the Undo command,
      covered next.



^U - Undo
Prior to any changes, a snapshot of the Phone Book is taken, and the Phone Book
is saved in a backup file with the same name as the original and a file
extension of .FBK.  The last Phone Book backup can be restored immediately via
the Undo command.

When pressing ^U (Ctrl-U), Qmodem looks for a file with the same name as the
current phone book and an .FBK extension,  If found, that file will be loaded in
place of the current Phone Book.   If no .FBK file is found, an Information
Window will be displayed, stating that no backups were found.

NOTE: If Alt-N/O/T/F/W (Write FBK File) is set OFF , this command does not
      restore the backup.  There is no FBK file!


Alt-E  Duplex Toggle
Alt-E switches Qmodem operation between Full Duplex and Half Duplex modes.
"Duplex" describes the method used in echoing your keystrokes back to your
terminal screen.   In Full Duplex mode, the remote system you are connected to
echoes your keystrokes back to you.  In Half-Duplex Mode, the remote system does
not echo your keystrokes, and Qmodem must do it instead.

An incorrect Duplex setting will yield one of two results: either you will NOT
see any keystrokes displayed on your screen as you type, or your keystrokes will
be duplicated (i.e., HHEELLOO).  In the first case, you are operating in HALF
Duplex mode, and you should switch to FULL.  In the second case, you are
operating in FULL Duplex mode and you should switch to HALF.






                                                               Qmodem SST     95



NOTE: Most Hayes-compatible modems feature an internal Echo setting.  If set
      to ON, the modem itself will echo your keystrokes.  If your Qmodem
      settings are correct, but keystrokes are duplicated, the modem is
      likely to be the culprit.  Check your modem manual for switch settings
      or initialization parameters to turn the local echo off.


Pressing Alt-E will display a Status window on the screen when toggled.

TIP: Check the Status line for either FDX or HDX to see which modem you are
     in.


Alt-F  Script File Execution
"What is a Script?"

Scripts are internal Qmodem programs.  Qmodem features a command language to
automate and/or  time-schedule logons and interactions with remote computers.
Scripts can be used on commercial services such as CompuServe, Delphi, Dow Jones
News/Retrieval, GEnie, MCI-Mail, NewsNet and local BBS systems such as PCBoard,
Wildcat, Fido, and RBBS-PC.

With a script, you need only type a few keystrokes to set communication
parameters, dial the phone, connect to another computer, log on with your name
and account number or password, retrieve and save information, and log off.
Since everything is automated, there are no mistakes or wasted time spent on-
line.  When used properly, scripts can save you money.

Executing a script is a two step process.  Pressing Alt-F displays the script
File Allocation Window, in which you must type the desired script name.   You
will then get a prompt for any additional parameters which could be passed to
the script.

The following are samples of Script File Allocation and Execution windows:


   ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Script File Allocation ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
   ³                                                                       ³
   ³ > Z:\SCRIPTS\°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°    ³
   ³                                                                       ³
   ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾




   ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Script File Execution ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
   ³ Script to execute :                                                   ³
   ³ Z:\SCRIPTS\COLORS.SCR                                                 ³
   ³ Enter Script Parameters (if any)                                      ³
   ³ °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°      ³
   ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

°°°°°°°°° Enter optional script parameters, space separated   ESC-Exit °°°°°°°°°

Once you have entered any additional parameters, if any, the script will begin.





96   The Forbin Project, Inc.



NOTE: Scripts must be located in the Scripts Directory specified in the
      Alt-N/D/S Setup Menu.  If the default directory is blank, Qmodem will
      as look for the scripts in the current directory.


For more information on Scripts, refer to the Scripts Section of the Qmodem
manual.


Alt-G  Terminal Emulation
The Terminal Emulation feature allows Qmodem to behave like a terminal other
than a standard PC display, such as the popular VT100 from Digital Equipment
Corp.  While in terminal emulation mode, Qmodem interprets device-dependent
information so that it is displayed properly on the PC screen as if it were a
native terminal of the selected type.

Qmodem supports 7 different types of emulations:

  TTY   - No emulation at all.
  ANSI  - Emulates the ANSI.SYS of PC DOS.
  VT100 - Emulates the Digital VT100.
  TVI925- Emulates the Televideo 925.
  DBUG_A- Debug ASCII Mode
  DBUG_H- Debug HEX Mode
  AVATAR-  Superset of ANSI for OPUS BBS systems

When pressing Alt-G, the following window will be displayed:


                       ÕÍÍÍÍÍÍÍÍÍ Set Emulation ÍÍÍÍÍÍÍÍÍ¸
                       ³ Active Emulation is ANSI        ³
                       ³                                 ³
                       ³           1  TTY                ³
                       ³           2  ANSI               ³
                       ³           3  VT100              ³
                       ³           4  TVI925             ³
                       ³           5  DBUG_A             ³
                       ³           6  DBUG_H             ³
                       ³           7  AVATAR             ³
                       ³                                 ³
                       ³ Your choice : _                 ³
                       ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


To select the desired emulation mode, press the corresponding letter.  The
screen will be cleared and the Qmodem Status Line will reflect the new emulation
mode.

NOTE: If you are in Split-Screen mode (via Alt-S), you may not select a new
      terminal emulation mode.  In order to operate properly, Split-Screen
      mode forces TTY emulation.


TTY
  This has no specific character translations or function keys.  The full ASCII
  character set is supported with the IBM extended character set (codes 128-
  255).



                                                               Qmodem SST     97



  TTY does not include cursor control codes or enhanced video options.

TIP: When calling BBS systems, the ANSI emulation is recommended.



ANSI
  This emulation is recommended for BBS usage.  Complete IBM ANSI.SYS
  compatibility is built right in.  You do not need to load the ANSI.SYS driver
  in your CONFIG.SYS file.  Extensions include the VT100 mode Screen clear
  commands because CompuServe can't tell the difference between ANSI and VT100.


KEY             FUNCTION                XMITED CODE
Tab             Horizontal Tab                 0x09
Del             Character delete               0x7F
Home            Home the Cursor            0x1B5B48
Up Arrow        Cursor Up                  0x1B5B41
Down Arrow      Cursor Down                0x1B5B42
Left Arrow      Cursor Left                0x1B5B44
Right Arrow     Cursor Right               0x1B5B43
PgDn            Clear Screen             0x1B5B324A
End             Erase End of Line          0x1B5B4B
Enter           Carriage Return                0x0D
Ctrl-Enter      Linefeed                       0x0A


VT100
  Qmodem supports the standard VT100 functions; half/full duplex, set/reset
  modes, scrolling region, keypad application mode, special graphics character
  set, US & UK character sets, full display attributes including ANSI color
  extensions, programmable tabs and cursor control.

  To take advantage of larger screen dimensions other than 80x25, you must have
  an EGA or VGA card that supports more lines and columns in text mode.
  Assuming you have such a card, place the card in the desired mode (say,
  132x43) and then select the VT100 emulation.  Until changed manually (via
  Alt-2, Alt-4 or an external driver), the screen will lock in on the selected
  dimensions.

  Qmodem responds to the "Identify" command (0x1B5B63 or 0x1B5A) with
  "ESC[?1;2c" (0x1B5B3F313B3263).

KEY             FUNCTION                XMITED CODE
Tab             Horizontal Tab                 0x09
Del             Character delete               0x7F
Home            Home the Cursor            0x1B5B48
Up Arrow        Cursor Up                  0x1B5B41
Down Arrow      Cursor Down                0x1B5B42
Left Arrow      Cursor Left                0x1B5B44
Right Arrow     Cursor Right               0x1B5B43
PgDn            Clear Screen       0x1B5B481B5B324A
End             Erase End of Line          0x1B5B4B
Enter           Carriage Return                0x0D
Ctrl-Enter      Linefeed                       0x0A





98   The Forbin Project, Inc.



TVI925
  Qmodem supports a partial list of Televideo 925 functions; cursor
  positioning, inverse video, and custom Status lines.  Protected fields and
  multiple video pages are not supported, but will be in a future release.

KEY             FUNCTION                XMITED CODE
Tab             Horizontal Tab                 0x09
Del             Character delete               0x7F
Up Arrow        Cursor Up                      0x0B
Down Arrow      Cursor Down                    0x16
Left Arrow      Cursor Left                    0x08
Right Arrow     Cursor Right                   0x0C
Enter           Carriage Return                0x0D
Ctrl-Enter      Linefeed                       0x0A


DEBUG ASCII
  This is a custom Emulation for debugging connections.  It resembles the TTY
  emulation with the exception that ASCII codes 0-31 and 255 are displayed  in
  mnemonics surrounded by square brackets.

  The lists is as follows:

     Code Mnem.     Code Mnem.
     #0   [NUL]     #16  [DLE]
     #1   [SOH]     #17  [DC1]
     #2   [STX]     #18  [DC2]
     #3   [ETX]     #19  [DC3]
     #4   [EOT]     #20  [DC4]
     #5   [ENQ]     #21  [NAK]
     #6   [ACK]     #22  [SYN]
     #7   [BEL]     #23  [ETB]
     #8   [BS]      #24  [CAN]
     #9   [HT]      #25  [EN]
     #10  [LF]      #26  [SUB]
     #11  [VT]      #27  [ESC]
     #12  [FF]      #28  [FS]
     #13  [CR]      #29  [GS]
     #14  [SO]      #30  [RS]
     #15  [SI]      #31  [US]
                    #255 [0xFF]


DEBUG HEX
  This is also a custom Emulation for debugging connections.  It resembles
  nothing you've ever seen before...  All data received is displayed in HEX
  between square brackets.

  A sample looks like this:   [61][74][0D][0D][0A][4F][4B][0D][0A]

  This is the result of typing AT[ENTER] and the modem responding with "OK".


AVATAR
  This emulation is a superset of the ANSI emulation.  As such, all of the
  above information on ANSI applies to Avatar.  AVATAR control codes were
  designed to be lean and mean.  AVATAR includes provision for packing
  replicated characters which can cut transmission time significantly.


                                                               Qmodem SST     99




  Enhanced control codes are as follows:

  Codes     Type              ANSI Equivalent

  ^V^A<a>   Attribute         ESC[n;nm

     The "<a>" is a single byte.  The value of this attribute byte corresponds
     to the video attributes used by IBM on their Color Graphics adapters.
     (Intense video is supported, black-on-black is not.)


  ^V^B      Blinking On       ESC[5m

     Blinking is turned off by the next ^V^A command.


  ^V^C      Cursor Up         ESC[1A

     Move the cursor up one line.


  ^V^D      Cursor Down       ESC[1B

     Move the cursor down one line.

  ^V^E      Cursor Left       ESC[1D


  ^V^F      Cursor Right      ESC[1C


  ^V^G      Clear to end of line   ESC[K


  ^V^H<r><c>                  Set cursor position ESC[x;xf

     These are 1-based numbers with the row coordinate first.  The upper left of
     the display is "1,1."  The start of the second line would be "2,1."  In
     most cases, the lower right corner will be "24,80."  Values that fall
     outside of the user's declared screen size are clipped.



















100  The Forbin Project, Inc.



  ^L        Home & Clear Screen    ESC[H
                              ESC[0;30;36m
                              ESC[2J

     Note that the color will be reset to white on black, and not the default
     Text Color of Alt-N/V/C.


  ^Y<c><#>  Replicate Character    No matching ANSI command.

     This will replicate character <c> (or any byte 0-255) for <#> number of
     iterations.  <#> can be in the range 1-255.



Alt-H  Hang-up
The Hang-up command is used to force the modem to terminate a call.  In most
cases, you would not use this command to disconnect from the remote computer;
you would use the remote computer's standard LOG OFF procedure.  However, in
case you are experiencing problems (remote computer lockup, bad line noise) you
may use this command to disconnect the call.

What Alt-H does varies, depending on the information specified in the
Alt-N/M/M/H Setup Menu.  Usually, Qmodem will send the modem hang-up string
defined in your setup.  However, if you specified "DTR" as a modem hang-up
string, Qmodem will toggle the "DTR" signal and the connection will be dropped.
And if you specified "BREAK", the UART BREAK signal will be sent.

The recommended Hang-up string for Hayes_ and compatible modems is:

"^~^~^~+++^~^~^~ATH^M" where:

  ^~^~^~  =  1.5 seconds delay
  +++     =  go to Command Mode string
  ^~^~^~  =  another 1.5 seconds delay
  ATH     =  command to Hang-up
  ^M      =  the [ENTER] key

"DTR" stands for "Data Terminal Ready".  Most modems will automatically
disconnect from the phone line DTR signal is dropped for 1.5 seconds.  Having
the three characters "DTR" in the Hang-up string does exactly that.  If in
doubt, check your modem manual to see if "Dropping DTR" is an accepted method of
disconnecting.  If so, this should be the preferred method.

BREAK is a signal generated by the UART (Universal Asynchronous Receiver
Transmitter, the main chip on your serial adapter or modem).  Some PBX and Bell
type modems require a BREAK signal before they will take action.  Again, check
your modem manual before setting this option.


Alt-I  Information on Qmodem
The Qmodem information screen always displays the Qmodem release number, our
Voice, BBS, and Fax numbers.  You can also print out an official Invoice Form
which can be printed out and sent in to register your copy of the program.






                                                              Qmodem SST     101




ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
ÄÄÄÄÄÛßßßßßßßßßßßßßßÛÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÜÜÜÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
ÄÄÄÄÄÛ  ÜÜÜÜÜÜÜÜÜÜ  ÛÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÛ ÛÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
ÄÄÄÄÄÛ  ÛÄÄÄÄÄÄÄÄÛ  ÛÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÛ ÛÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
ÄÄÄÄÄÛ  ÛÄÄÄÄÄÄÄÄÛ  ÛÄÄÜÜÜÜÜÜÜÜÜÜÜÄÄÜÜÜÜÜÜÜÄÄÜÜÜÜÛ ÛÄÄÜÜÜÜÜÜÜÄÄÜÜÜÜÜÜÜÜÜÜÜÄÄÄÄÄÄ
ÄÄÄÄÄÛ  ÛÄÄÄÄÄÄÄÄÛ  ÛÄÄÛ ÜÜÜ ÜÜÜ ÛÄÄÛ ÜÜÜ ÛÄÄÛ ÜÜÜ ÛÄÄÛ ÜÜÜ ÛÄÄÛ ÜÜÜ ÜÜÜ ÛÄÄÄÄÄÄ
ÄÄÄÄÄÛ  ÛÄÄÄÄÄÄÄÄÛ  ÛÄÄÛ ÛÄÛ ÛÄÛ ÛÄÄÛ ÛÄÛ ÛÄÄÛ ÛÄÛ ÛÄÄÛ ÛÄÛ ÛÄÄÛ ÛÄÛ ÛÄÛ ÛÄÄÄÄÄÄ
ÄÄÄÄÄÛ  ÛÄÄÄÄÄÄÄÄÛ  ÛÄÄÛ ÛÄÛ ÛÄÛ ÛÄÄÛ ÛÄÛ ÛÄÄÛ ÛÄÛ ÛÄÄÛ ßßß ÛÄÄÛ ÛÄÛ ÛÄÛ ÛÄÄÄÄÄÄ
ÄÄÄÄÄÛ  ÛÄÄÄÄÄÄÄÄÛ  ÛÄÄÛ ÛÄÛ ÛÄÛ ÛÄÄÛ ÛÄÛ ÛÄÄÛ ÛÄÛ ÛÄÄÛ ÛßßßßÄÄÛ ÛÄÛ ÛÄÛ ÛÄÄÄÄÄÄ
ÄÄÄÄÄÛ  ßßßßßßßßßß  ßÄÄÛ ÛÄÛ ÛÄÛ ÛÄÄÛ ÛÜÛ ÛÄÄÛ ÛÜÛ ÛÄÄÛ ÛÜÜÜÜÄÄÛ ÛÄÛ ÛÄÛ ÛÄÄÄÄÄÄ
ÄÄÄÄÄÛÜÜÜÜÜÜÜÜÜÜÜ ÛßßÛÄÛÜÛÄÛÜÛÄÛÜÛÄÄÛÜÜÜÜÜÛÄÄÛÜÜÜÜÜÛÄÄÛÜÜÜÜÜÛÄÄÛÜÛÄÛÜÛÄÛÜÛÄÄÄÄÄÄ
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÛÜÜÛÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
ÄÄÄÄÄÄÄÄÄÄÄÜÜÜÜÜÜÜÜÄÄÜÜÜÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸ÄÄÄ
ÄÄÄÄÄÄÄÄÄÄÄÛ ÜÜÜÜÜÛÄÄÛ Ü³        Qmodem SST - Version 4.2 Production        ³ÄÄÄ
ÄÄÄÄÄÄÄÄÄÄÄÛ ÛÄÄÄÄÄÄÄÛ Û³ Copyright (C) 1983-1990, THE FORBIN PROJECT, INC. ³ÄÄÄ
ÄÄÕÍÍÍÍÍÍHow to reach usÍÍÍÍÍÍ¸          All Rights Reserved                ³ÄÄÄ
ÄÄ³  Voice : (319) 232-4516   ³ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾ÄÄÄ
ÄÄ³    BBS : (319) 233-6157   ³ÄÄÄÛ ÛÄÄÄÄÄÄÄÄÄÄÛÜÜÜÜÜ ÛÄÄÄÄÄÜß ÜßÄÜÄÄÄÄÄÄÄÄÄÄÄÄÄ
ÄÄ³    Fax : (319) 233-1725 ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍOrder FormÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸ÄÄÄ
ÄÄÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ³ Press Y to print an Order Form > _            ³ÄÄÄ
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾ÄÄÄ
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
ÄÄÄÄÄÄÄÄÄÄÄÄ  ¯¯ World Class Communications at a Shareware Price! ®®  ÄÄÄÄÄÄÄÄÄÄ
ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


The Forbin Project depends on your honesty to register the program if you use
it.  This allows us to keep on improving the software and supply you with top
quality technical support when you need it.


Alt-J  Function Key Macros
Function key (FKey for short) macros are used to store keystrokes which are sent
repetitively.  When pressing Alt-J, the following window is displayed:
























102  The Forbin Project, Inc.




 ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Function Key Assignment ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
 ³     Normal             Shift              Ctrl               Alt           ³
 ³F1  @Script Teleph F1                 F1                 F1  @Shellx MAKEH  ³
 ³F2  @Edit          F2                 F2                 F2                 ³
 ³F3                 F3                 F3                 F3  @Dial TSalt    ³
 ³F4                 F4                 F4                 F4                 ³
 ³F5                 F5                 F5                 F5                 ³
 ³F6                 F6                 F6                 F6  @Script TagDia ³
 ³F7                 F7  @edit \scripts F7                 F7                 ³
 ³F8                 F8  @Script test1. F8                 F8                 ³
 ³F9                 F9                 F9                 F9  @DIAL TGEnie_L ³
 ³F10 $Password^M    F10                F10                F10 @script test1. ³
 ³F11                F11 @Edit \qmhost. F11                F11                ³
 ³F12                F12                F12                F12 ^F             ³
 ³                                                                            ³
 ³ Key File is C:\QMODEM\ANSI.KEY                                             ³
 ³                                                                            ³
 ³ 1 - Normal   2 - Shift   3 - Ctrl   4 - Alt   L - Load    ESC - Exit       ³
 ³                                                                            ³
 ³ Your Choice ?                                                              ³
 ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

°°°°°°°°°°°°°°°°°°°°°°°° 1,2,3,4-Display/Edit   ESC-Exit °°°°°°°°°°°°°°°°°°°°°°°


Up to 48 FKey Macros may be programmed at one time.  FKey Macros are stored in
"Key Definition Files" with .KEY file extensions and user-assigned filenames.
Each key can store up to 4 separate macros, depending on the key's Shift state
(Fn, Shift-Fn, Ctrl-Fn and Alt-Fn).  To execute an FKey Macro, press the desired
Shift sate key, hold it down, and strike the Fn key.

The first 14 characters of each FKeys are displayed in 4 columns corresponding
to the shift states described earlier.  The status line at the bottom of the
window displays summary instructions on how to display and/or edit each series
of macros, load an alternate key definition file, or exit the Alt-J screen.

To view the complete key definitions for a given shift state, press the number
(1-4) corresponding to that state (1=Normal, 2=Shift, 3=Ctrl, 4=Alt).


Editing Key Macros
To edit an FKey macro, press the number (1-4) corresponding to the key's shift
state, as described above.  The following edit screen will then be displayed (in
the following example, the "3" key was pressed to display/edit Alt-Fn key
assignments):














                                                              Qmodem SST     103




 ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Function Key Assignment ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
 ³         Definitions for Alt F-keys                                         ³
 ³F1  @SHELL MAP°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°³
 ³F2  @SCRIPT SETCOLOR 7 1 "String passed to S2"°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°³
 ³F3  @DIAL TSalt°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°³
 ³F4  @EDIT°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°³
 ³F5  @STAMP This will be put in the LOG file.°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°³
 ³F6  @SHELLX DEL *.BAK°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°³
 ³F7  Be right back... Went to the kitchen...°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°³
 ³F8  I'm back.°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°³
 ³F9  @DIAL TGEnie_Local°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°³
 ³F10 @SCRIPT WHO°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°³
 ³F11 $PASSWORD^M°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°³
 ³F12 ^F°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°³
 ³                                                                            ³
 ³ Valid Edit Keys    :   INS - Insert mode Toggle      - Field Up           ³
 ³                        DEL - Delete Character        - Field Down         ³
 ³                           - Character Left         ^ - Word Left         ³
 ³                           - Character Right        ^ - Word Right        ³
 ³ Special Characters :    ^M = [ENTER]                ^~ = « second delay    ³
 ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

°°°°°°° Edit Function Key Entries    F10-Save    ESC-Exit with no changes°°°°°°°


The Alt-J edit screen features a scrollbar cursor.  Move the scrollbar with the
up/down arrow keys to select the key definition to edit.  The following section
describes available macro keywords and commands in detail.


DOS Shell Macros
Two macro commands, @SHELL and @SHELLX allow you to quickly access DOS with the
touch of a key.  Any program, with the exception of those that attach themselves
to DOS (TSR's) can be executed provided enough free memory is available.

Examples:


 @SHELL CHKDSK C:°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°


This will run the DOS Chkdsk program on drive C:.  When complete, it will stop
and prompt you to press a key before returning to Qmodem (and erasing the
screen).


 @SHELLX DEL *.BAK°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°


This will delete all the files with the extension of ".BAK" and immediately
return when completed.


 @SHELL ESU 43°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°





104  The Forbin Project, Inc.



If you have a Vega VGA, this is the program used to switch video modes on the
fly.  The @SHELL and @SHELLX macros will detect video mode changes and reset
Qmodem when returning from DOS.  A handy way to use those SuperEGA and SuperVGA
cards to get higher screen resolutions and larger viewing areas.


A Dial Macro
The @DIAL macro is just like invoking an Alt-D/T command.  Any text following
the @DIAL is parsed in the same way that Alt-D/T does.  For more information,
refer to the Alt-D/T section.

Examples:


 @DIAL TSALT-AIR°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°


This will search all entries for the text "SAlt-Air".  The search is not case
sensitive.  The Name, Number and attached Notes are searched.  All entries that
match are tagged and then dialing will start.


 @DIAL 1 2 23 155°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°


This will tag entries 1, 2, 23 and 155 to be dialed.


 @DIAL 1 TO 200°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°


This will tag entry 1, then all the entries with the letter "O", and finally
entry 200.  Did you think it would dial all the entries in the phone book?
Well, not yet anyway!

NOTE: @DIAL will do an implied "Untag-All" before applying the new tags.



An Edit Macro
The @EDIT macro allows you to quickly call up the internal editor to edit/view a
file.  If a filename follows @EDIT, that file will be brought up in edit
immediately.  If no filename has been specified, then you will be prompted for
one.

Examples:


 @EDIT°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°


This will prompt for the filename to edit.


 @EDIT QMHOST.PWD°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°


This will edit the Internal HOST database file.


                                                              Qmodem SST     105




A HELP Macro
The @HELP macro allows you to call up a Help Screen from TERMINAL mode.

Examples:


 @HELP°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°


Something like this will appear:


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Terminal Mode ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³                                                                              ³
³ You are now in what is called TERMINAL MODE.  This is where you can enter    ³
³ modem commands while Offline, and communicate with a remote computer while   ³
³ Online.                                                                      ³
³                                                                              ³
³ If you need a list of Commands that are available, press Esc to exit the     ³
³ Help System and then press the Home key.                                     ³
³                                                                              ³
³ If you would like to see the Index of Help Topics, press F1                  ³
³                                                                              ³
³ Hot Links:   Help Index         Dialing a number                             ³
³                                                                              ³
³              Qmodem Setup                                                    ³
³                                                                              ³
³                                                                              ³
³                                                                              ³
³                                                                              ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
°°°°°°°°°°°°°°° F1-Topic Index    AltF1-Previous Topic   ESC-Exit °°°°°°°°°°°°°°


From here, you could get more help on the three highlighted topics, press [F1]
for the Topic Index, or [ESC] to return back to terminal mode.  The most common
use of this will be to quickly get to the Topic Index.

NOTE: When new KEY files are created, the @HELP macro is not automatically
      placed in the F1 slot.  You still have to do this for yourself.



A Script Macro
In the example above, entries Alt-F2, Alt-F10 and Alt-F12 use the keyword
@SCRIPT.  The @SCRIPT macro command causes execution of the Script whose
filename follows (the .SCR script file extension is not required).  If the
script requires parameters, they must be included in the key definition
following the script name. The @SCRIPT macro, the script name, and script
parameters must be separated by at least one space.

Examples:


 @SCRIPT TEST1.SCR°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°




106  The Forbin Project, Inc.



This will call the script "TEST1.SCR".  Because ".SCR" was not included in the
filename, it is added by default.


 @SCRIPT TEST1.°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°


This will call the script "TEST1".  Because the "." is at the end of the script
name, the default extension is not included.


 @SCRIPT SETCOLOR 7 1 "String passed to S2"°°°°°°°°°°°°°°°°°°°°°°°°°°°°


This will call the Script SETCOLOR and pass it 3 parameters.  Parameter 1 is the
character "7", parameter 2 is "1" and parameter 3 is "String passed to S2".
Since the third parameter is text with imbedded spaces, it must be enclosed
within quotes.


A LOG Macro
The @STAMP macro causes the text following it to be recorded into the current
LOG file, preceded by the current time and date.  For more information on the
Qmodem LOG file, refer to the Alt-0 Command.

Example:


 @STAMP This will be put in the LOG file.°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°


The LOG file entry would look like this (except with the current time and date)
:


  16:26:54  11-20-90  This will be put in the LOG file.


NOTE: The special characters "^~" and "^M" have no meaning when @STAMP is
      used.



The $PASSWORD Variable
When used in a key macro definition, $PASSWORD variable is replaced by the
current entry's PASSWORD field (see Alt-D).  Whenever a connection is made, the
dialed entry's Password is automatically loaded into the $PASSWORD variable.
Unlike all the other special macro commands which must appear first in the
macro, $PASSWORD may be used anywhere within the macro text.

Example:

Let's assume that the word "QMODEM!" is the password for the entry we have just
connected to and the following was coded for Alt-F11:


 My password is $PASSWORD°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°



                                                              Qmodem SST     107



After the connection is made, pressing Alt-F11 would send the following:

     My password is QMODEM


Loading a new Key file
Pressing the "L" key while in the main Alt-J screen will load a new .KEY file,
if found.  If the specified .KEY file does not exist, Qmodem will issue a prompt
for its creation.  That's new key definition files are made.



Alt-K  Changing COM Port
The Alt-K commands is used to switch the active serial communications port.
After pressing Alt-K, the following window is displayed:


                       ÕÍÍÍÍÍÍÍÍÍ Set COM Port ÍÍÍÍÍÍÍÍÍÍ¸
                       ³ Active COM Port is COM1         ³
                       ³                                 ³
                       ³ 1  COM1  Base(03F8) Irq(04)     ³
                       ³ 2  COM2  Base(02F8) Irq(03)     ³
                       ³ 3  COM3  Base(03E8) Irq(04)     ³
                       ³                                 ³
                       ³ Your choice :                   ³
                       ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


°°°°°°°°°°°°°°°°°°°° NUMBER-Select a new COM Port   ESC-Exit °°°°°°°°°°°°°°°°°°°


Qmodem supports up to 8 serial communication ports (COM1 through COM8).   Only
the ports specifically defined in your setup will be identified in the Alt-K
menu.  In the above example, ports 1, 2 and 3 were defined during installation.

To select a new communication port, press the desired number (1-8).  Once the
new port is selected,  the current port will be closed and the new one opened.
Communication parameters (baud rate, parity, start/stop bits) will remain
unchanged.  To change the communication parameters, use the Alt-P command.



Alt-L  Changing the Logged Drive
"Logged Drive" refers to the default drive at the time Qmodem was started.  This
drive may be changed by using the Alt-L command.  Pressing Alt-L displays the
following prompt window:


                            ÕÍÍ Change Log Drive ÍÍ¸
                            ³ Logged Drive is  : C ³
                            ³ Enter new Drive  : _ ³
                            ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


°°°°°°°°°°°°°°°°°°°°° A thru Z-Select New Drive   ESC-Exit °°°°°°°°°°°°°°°°°°°°°


To select a new default drive, type its drive letter and [ENTER].


108  The Forbin Project, Inc.




The new drive will be verified before proceeding.  If the drive is invalid, a
message to that effect will be displayed and a new drive prompt will be issued.
Pressing [ESC] will cancel the drive change request.



Alt-M  Music Toggle
Music will be generated on the PC's speaker only if the following conditions are
met:

  1. ANSI terminal emulation is active (see Alt-G).
  2. The Music Toggle is ON (see Alt-M).
  3. Qmodem receives encoded music data.

If any of the above condition is not met, Qmodem will disregard encoded music
information.  To be recognized by Qmodem, encoded music data must conform to the
following format:

          ESC [ M  .....music codes.....  ^N

Music codes are those used in the BASIC language PLAY statement (please refer to
your BASIC language manual for further information on the PLAY statement).
Music strings must end with the Ctrl-N (^N) character.  If the ^N character is
missing, It is assumed that the following text, up to 255 characters, is
playable music.  It might not sound too good, however.



Alt-N  Invoking the Setup Menu
Almost all of Qmodem's operational parameters can be customized.  You may change
the colors, upload or download directory paths or even add an external protocol
without leaving Qmodem.

To use the Alt-N command requires that enough free memory be present.  If this
is not the case, you must exit Qmodem via the Alt-X command and run the Qinstall
program externally.

Refer to the SETUP section at the beginning of the manual for complete
installation instructions.



Alt-O  Changing Subdirectories
By definition, a directory listing request (see Alt-W) will display the current
subdirectory.  However, the default subdirectory is that which was active when
Qmodem was started.  In order to view the contents of other directories, the
current directory must be changed via the Alt-O command.












                                                              Qmodem SST     109



When pressing Alt-O, the following windows are displayed:

 ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Z:\*.* ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
 ³ ..\            HOSTDIR\       PRINTDOC\      RZSZ\          VCS\          ³
 ³ DL\            LOGO\          QMEDIT\        SCRIPTS\       YAK\          ³
 ³ GG\            NCI\           QPRO\          SHOW\                        ³
 ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


°°°°°°°°° ARROWS-Scroll   ENTER-Change Directory   F10-Save   ESC-Exit °°°°°°°°°

This is a Pick List window with 5 columns.  The top of the window  shows the
current subdirectory.  The entries in the pick list are possible subdirectories
that can be selected as the new current directory.

Move the scrollbar to the entry and press [ENTER] to make the change.  The top
of the window will also change to reflect this.  When the top of the window
shows where you want to be, press [F10] to save.  At any time, you can press
[ESC] to return to your original starting point.

Notice the upper left corner of the example, [..\].  This references the
previous subdirectory, if any.  Selecting this entry move you up the directory
tree.



Alt-P  Com Port Settings
The Alt-P command allows immediate changes to serial communications parameters.
Pressing Alt-P displays the following window:


           ÕÍÍÍÍÍÍÍÍÍÍÍÍ Communications Port Setup ÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
           ³              Port COM1:  38400,8,N,1               ³
           ³                                                    ³
           ³       Speed             Parity      Data     Stop  ³
           ³ A - 110   F - 9600     K - Even    P - 7    R - 1  ³
           ³ B - 300   G - 19200    L - Odd     Q - 8    S - 2  ³
           ³ C - 1200  H - 38400    M - Mark                    ³
           ³ D - 2400  I - 57600    N - None                    ³
           ³ E - 4800  J - 115200   O - Space                   ³
           ³                                                    ³
           ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


°°°°°°°°°°° LETTER-Select a Parameter   ENTER-Save Changes   ESC-Exit °°°°°°°°°°


Select the new parameters by pressing the corresponding option letter.  If an
error was made, pressing [ESC] restores the previous parameters and exits the
Alt-P window.  Pressing [ENTER] completes the parameter changes and exits the
window.

For example, say we want to set the port to 1200,7,E,1 and the current setting
is 19200,N,8,1.  You would press the letters C and K and press [ENTER].  You
might be wondering, why didn't you need to press P to set 7 data bits?  Because
when either K or L is selected, it forces P.




110  The Forbin Project, Inc.



Alt-Q  QuickLearn Script Recorder
The QuickLearn Script Recorder is much like a video camera.  As it records your
interactions, it creates a Script which can be replayed later to replicate the
session while QuickLearn was active.  Alt-Q is a toggle;  if the QuickLearn
recorder is not active, it is started.  If it is active, it terminates and the
Script is saved.

In a nutshell, QuickLearn stores incoming data internally until you type
information yourself.  QuickLearn assumes that your data was entered in response
to a prompt or question from the system you are connected to.  The last 32
characters received are assumed to be the prompt to which you are responding,
which will be reflected in the final script as a WAITFOR command.  In turn, the
entire contents of your response will be included in the script as a SEND
command.

The "Q" tag was mentioned in the Dialing Directory section (Alt-D command).  If
an entry is tagged by pressing "Q", the dialer will start QuickLearn
automatically -- but only if a Script file name is defined and the file itself
does not exist --.  As a result, script recording starts the instant the
connection is established.

What if you are already on-line and want to create a script to perform a
repetitive function?  You would invoke Alt-Q!

When pressing Alt-Q, Qmodem displays the following script file allocation
window:


   ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Script Learn Allocation ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
   ³                                                                       ³
   ³ > Z:\SCRIPTS\°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°    ³
   ³                                                                       ³
   ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


°°°°°°°°°°°°°°°°°°°°°°°°° Edit File/Pathname   ESC-Exit °°°°°°°°°°°°°°°°°°°°°°°°


Type the desired script file name and [ENTER].  If the script already exists, an
overwrite prompt will be displayed.  You may chose to overwrite the prompt, or
select a new name for the script.  If the script file is not found, it will be
created.

While QuickLearn is active, the status line is changed to the following:


°°°°°°°°°°°°°°° QuickLearn Recording Active!   AltQ-End Recording °°°°°°°°°°°°°°


When you are finished recording a script, press Alt-Q again.  Qmodem will
display the following status window, after which the standard Status Line will
be restored.








                                                              Qmodem SST     111




                         ÕÍÍÍÍÍÍÍÍÍ Status ÍÍÍÍÍÍÍÍÍÍ¸
                         ³ QuickLearn recording done ³
                         ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


QuickLearn saves the state of Qmodem environment variables at the beginning of
each Script.  These variable include toggles such as Split-screen mode (SPLIT),
Duplex setting (ECHO), as shown below:


;
;  QuickLearn Script generated at 14:41:51 on 08-13-1990
;  May require editing before use.
;
Graphics ANSI
TurnON   8_BIT
TurnOFF  LINEFEED
TurnON   XON/XOFF
TurnON   NOISE
TurnOFF  MUSIC
TurnON   SCROLL
TurnOFF  PRINT
TurnOFF  ECHO
TurnOFF  SPLIT
TurnOFF  BS_DEL


TimeOut  30     ; Set Waitfor for 30 seconds


This sample was created by pressing Alt-Q, entering a script filename, and then
pressing Alt-Q again to save the file.

The top of each Quicklearned script contains a time and date stamp, followed by
the commands needed to restore the environment at the time the script was
recorded.  Note the second line: the script may require editing before use.

QuickLearn also forces a default script TIMEOUT command of 30 seconds (the last
line of the sample script).  This default value is hard-coded in Qmodem and can
only be changed by manually editing the script.  The default value is probably
higher than necessary.  Set this value to the longest estimated time the script
will have to wait on data from the other system; if the delay exceed the TIMEOUT
value, the script will be cancelled automatically.

As QuickLearn records the session, it may capture text strings which contain
variable data, such as time and/or date information.  A good example  would be a
script created  while logging on to a Bulletin Board System (BBS).  Many BBS's
feature command line prompts which include time used and time remaining for the
current session.  The values recorded in the original script may never be
matched by the values received when the script is replayed.









112  The Forbin Project, Inc.



For example:


WaitFor  "56 min. left) Qmodem Conference Command?"
Delay    100
Send     "R S NS^M"


Needless to say, the script will ONLY work if there are EXACTLY 56 minutes left.
Likely, the WAITFOR command will wait forever for a prompt that will never come.
To eliminate this problem, edit the WAITFOR command and remove variable
information which is likely to cause problems:


WaitFor  "Conference Command?"
Delay    100
Send     "R S NS^M"


The " 56 min. left) Qmodem " was removed from the WAITFOR string, leaving a
generic prompt which will work at any time, and in any conference.


Commands that are recorded
QuickLearn also records certain Qmodem commands.  Following is a list of
supported Qmodem commands, and examples of the generated script commands which
replicate them:

  Alt-B   Beeps & Bells toggle

          TurnON   NOISE
          TurnOFF  NOISE


  Alt-C   Clears the screen

          ClrScr


  Alt-D   Dial an entry number

          Dial     "1"


  Alt-D/L Load a new FON book

          LoadFON  C:\QMODEM\QMODEM.FON


  Alt-E   Half/Full Duplex toggle

          TurnON   ECHO
          TurnOFF  ECHO


  Alt-G   Change current terminal emulation mode

          Graphics TTY


                                                              Qmodem SST     113



          Graphics ANSI
          Graphics VT100


  Alt-H   Terminate the connection

          HangUp


  Alt-J/L Load a new KEY file

          LoadKEY  C:\QMODEM\VT100.KEY


  Alt-K   Change current COM Port selection

          Port     1


  Alt-L   Change current Logged Drive

          Drive    C


  Alt-M   Toggle playing of MUSIC if detected

          TurnON   MUSIC
          TurnOFF  MUSIC


  Alt-O   Change current Subdirectory

          CHDIR    C:\QMODEM\SCRIPTS


  Alt-P   Change current Baud Rate

          SETCOMM 19200 8 NONE 1


  Alt-R   Execute the DOS shell

          DOS "Command"
          BIGDOS "Command"


  Alt-S   Toggle the Split Screen mode

          TurnON   SPLIT
          TurnOFF  SPLIT


  Alt-U   Toggle the Scroll-back capture

          TurnON   SCROLL
          TurnOFF  SCROLL




114  The Forbin Project, Inc.



  Alt-V   View a File with an external program

          DOS      "LIST filename"

  Alt-X   Exit the Script AND Qmodem

          SYSTEM X
          SYSTEM Y


  Alt-Y   Delete a File

          DOS      "DEL filename"


  Alt-Z   Toggle the Xon/Xoff flow control

          TurnON   XON/XOFF
          TurnOFF  XON/XOFF


  Alt-1   Toggle the Backspace/DEL key output

          TurnON   BS_DEL
          TurnOFF  BS_DEL


  Alt-2   Set 80x25 line mode for EGA/VGA

          EGA      25


  Alt-4   Set 80x43/50 line mode for EGA/VGA

          EGA      43


  Alt-8   Toggle the Hi-Bit filter

          TurnON   8_BIT
          TurnOFF  8_BIT


  Alt-9   Toggle the Printer Echo

          TurnON   PRINT
          TurnOFF  PRINT


  Alt-0   Toggle the LOG file on/off

          TurnOFF  LOG
          LOG      C:\QMODEM\QMODEM.LOG







                                                              Qmodem SST     115



  Sh-Tab  Toggle the Add Linefeeds

          TurnON   LINEFEED
          TurnOFF  LINEFEED


  ^Home   Toggle the Capture file on/off

          TurnOFF  CAPTURE
          CAPTURE  C:\QMODEM\CAPTURE.TXT


  ^End    Send the UART BREAK signal

          BREAK


  PgUp/   Upload (send) a file
  ^PgUp
          UPLOAD PROTOCOL [Filename]


  PgDn/   Download (receive) a file
  ^PgDn
          DOWNLOAD PROTOCOL [Filename]


  FKey xx Function Key macro execution

          FKey 13   [shift F1 key]


Putting it all together
Now that the basics have been covered, let's go over a sample QuickLearn
recording session. The scripts were recorded while calling the Forbin Project
PCBoard BBS, Home of Qmodem.

First, a little advance information:  we will call using the Alt-D directory
with an attached script name of "FORBIN".  The Password field in Alt-D for the
Forbin entry will be used to link to an FKey macro (F10 in this example).

In the Function Key setup (Alt-J), we must edit the F10 key to contain the
string "$PASSWORD^M".  Once this is done, we can press Alt-D and tag the Forbin
entry with a "Q" to invoke QuickLearn.
















116  The Forbin Project, Inc.



In this example, the Fkey assignments are blank.  Our F9 entry should look like:


 ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Function Key Assignment ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
 ³     Normal             Shift              Ctrl               Alt           ³
 ³F1                 F1                 F1                 F1                 ³
 ³F2                 F2                 F2                 F2                 ³
 ³F3                 F3                 F3                 F3                 ³
 ³F4                 F4                 F4                 F4                 ³
 ³F5                 F5                 F5                 F5                 ³
 ³F6                 F6                 F6                 F6                 ³
 ³F7                 F7                 F7                 F7                 ³
 ³F8                 F8                 F8                 F8                 ³
 ³F9                 F9                 F9                 F9                 ³
 ³F10 $Password^M    F10                F10                F10                ³
 ³F11                F11                F11                F11                ³
 ³F12                F12                F12                F12                ³
 ³                                                                            ³
 ³ Key File is C:\QMODEM\ANSI.KEY                                             ³
 ³                                                                            ³
 ³ 1 - Normal   2 - Shift   3 - Ctrl   4 - Alt   L - Load    ESC - Exit       ³
 ³                                                                            ³
 ³ Your Choice ?                                                              ³
 ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

°°°°°°°°°°°°°°°°°°°°°°°° 1,2,3,4-Display/Edit   ESC-Exit °°°°°°°°°°°°°°°°°°°°°°°


The Alt-D screen is also blank except for the first directory entry for the
Forbin Project BBS.  The second screen snapshot shows the "O"ther page of the
directory with the Password field "MyPassword!".


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Phone Book ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Page  1 of C:\QMODEM\QMODEM.FON                                              ³
³ Total Tags > 1                        Prefixes > BC                          ³
³[D]   Name                             Number          Port       Script      ³
³1   Q The Forbin Project BBS           1-319-233-6157  38400 8N1  FORBIN.SCR  ³
³2                                                      38400 8N1              ³
³3                                                      38400 8N1              ³


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Phone Book ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ Page  1 of D:\QMODEM\QMODEM.FON                                              ³
³ Total Tags > 1                        Prefixes > BC                          ³
³[D]   Name                            Password        LastCall    Total  P D  ³
³1  ð  The Forbin Project PCBoard      MyPassword!     08-09-90    10112  G F  ³













                                                              Qmodem SST     117



Calling Forbin...


CONNECT 9600/ARQ/HST
CONNECT 38400 / 08-13-90 (15:06)
(Error Correcting Modem Detected)

The Forbin Project - Home of Qmodem
PCBoard (R) v14.5/U (beta 08/10/90 16:17) - Node 7

Do you want ANSI Graphics (Enter)=no? n    <----- (1)

 ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
 ³                       Welcome to The Forbin Project!                       ³
 ³                                  Home of                                   ³
 ³                                Qmodem SST!                                 ³
 ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

What is your first name? John   <----- (2)
 What is your last name? Friel  <----- (3)

JOHN FRIEL
WATERLOO, IA

Is this correct? (Y)            <----- (4)

Password (Dots will echo)? ...........  <----- (5)

Scan Message Base Since 'Last Read' (Enter)=yes? n  <----- (6)

(254 min. left) Qmodem (1) Conference Command?

(998 min. left) Main Board Command?   <----- (7)


Wherever information was entered in response to a prompt, it is followed by a
"<--- (n]" tag.  Following is a review of the above session:

  1. N[ENTER]       ANSI graphics was not wanted.

  2. John[ENTER]         Entered my first name.

  3. Friel[ENTER]        Entered my last name.

  4. [ENTER]        Yes, this is me.

  5. [F10]               Pressed the F10 key to send the password.

  6. n[ENTER]       No, don't scan the message base.

  7. Alt-Q               Pressed Alt-Q to end QuickLearn!









118  The Forbin Project, Inc.



And QuickLearn generated the following script:

;
;  QuickLearn Script generated at 15:19:10 on 08-13-1990
;  May require editing before use.
;
Graphics TTY
TurnON   8_BIT
TurnOFF  LINEFEED
TurnOFF  XON/XOFF
TurnON   NOISE
TurnON   MUSIC
TurnON   SCROLL
TurnOFF  PRINT
TurnOFF  ECHO
TurnOFF  SPLIT
TurnOFF  BS_DEL

TimeOut  30     ; Set Waitfor for 30 seconds

Waitfor  "want ANSI Graphics (Enter)=no?"
Delay    100
Send     "n^M"

Waitfor  "What is your first name?"
Delay    100
Send     "John^M"

Waitfor  "What is your last name?"
Delay    100
Send     "Friel^M"

Waitfor  "Is this correct?"
Delay    100
Send     "^M"

Waitfor  "Password (Dots will echo)?"
Delay    100
FKey     10

Waitfor  "Since 'Last Read' (Enter)=yes?"
Delay    100
Send     "n^M"

Waitfor  "Qmodem (1) Conference Command?"
Delay    100
Exit


NOTE: The "<--- (n]" tags were added for reference purposes only.




Alt-R  DOS Shell
If enough system memory is available and a copy of your Command Shell (usually
called COMMAND.COM or 4DOS.COM) can be located via the COMSPEC= environment
variable or in the DOS PATH, you may Shell to DOS.  Pressing Alt-R yields the
following screen:

                                                              Qmodem SST     119





Qmodem ®--¯ DOS Shell
Swapping 442743 bytes to EMS
Type EXIT to return to Qmodem!


The COMPAQ Personal Computer MS-DOS
Version 3.31

(C) Copyright Compaq Computer Corp. 1982, 1989
(C) Copyright Microsoft Corp. 1981, 1987

C:\>_


NOTE: COMPAQ Dos 3.31 was being used on the machine that the snapshots were
      captured from.  Your version of DOS and messages may vary.


You may notice that just below the top line, that Qmodem swapped 442743 bytes to
EMS.  Your hardware is interrogated to see if EMS memory exists, and if so, how
much EMS is free.  If sufficient memory EMS is available, then most of Qmodem
and the memory it is using is swapped to EMS leaving a small 4K kernel resident.
The following screen snapshot using MAPMEM shows the amount resident:


 PSP  blks bytes owner    command line        hooked vectors
----- ---- ----- -------- ------------------- ------------------------------
0008   1   53888 config
1727   2    3760 command                      2E
1824   1   20048 N/A      /LB:C800 /LI:5      5C
1D0A   1    1024 N/A                          17 2A 2F
1D5A   2     896 N/A
1D96   4    6304 WIN386   N/A                 67
1F13   3    4128 
2019   2   77056 SKPLUS                       08 09 0B 0C 0D 10 13 15 16
                                              1A 1C 21 25 26 28 33 E0
32EA   2    4320 QMODEM <---  Kernel resident *
33FA   3    3840 N/A                          22 24
34ED   2  438576 free   <---  FREE MEMORY!!

block   bytes   (Expanded Memory)
-----   ------
    0   524288
    1   409600
    2   245760    <---- QMODEM used this much to store the OVR file
    3   458752    <---- Swapped to EMS during the Shell
 free   458752
total  2621440

C:\>


Now, if there hadn't been that much EMS available, Qmodem would have tried to
allocate a file on Disk to swap to.  The net effect would have been the same.
The only difference is that swapping to/from EMS is a lot faster.



120  The Forbin Project, Inc.



All standard DOS commands are available from within the DOS Shell.  For example,
you could copy files, format a disk, or run a separate program as long as there
is sufficient memory available to do so.

To return to Qmodem, type "EXIT" and press [ENTER] at the DOS prompt.  The
screen will be restored to its previous status.


Possible Error conditions
While in the DOS Shell, you may not execute programs which attach themselves to
DOS, terminate, and stay resident (IE. SideKick).  If such a program is loaded,
the following message will be displayed when you attempt to EXIT back to Qmodem:


A TSR was loaded while executing the DOS Shell and Qmodem cannot recover.
A Reboot (Ctrl-Alt-Del) is recommended at this time.
> Tap any key to continue <


At this point, you can return to Qmodem, but only long enough to save any open
files and re-boot the system.  Your on-line session will not be disturbed and
you can get right back on-line by executing Qmodem again.


FON File Protection
When returning from a DOS shell, a check is made on the Phone Directory (.FON
file) to see if it has been updated.  If it has, then it is automatically
reloaded.  This feature was implemented to allow execution of external phone
book editors such as QFE from Sunflower Systems.


Alternate Screen Sizes
The DOS Shell is also able to recognize a screen size change (feasible with EGA
and VGA displays), and will adjust accordingly.  If an external program changes
the size of the screen while in the DOS Shell, that change will be recognized
upon return.

Under normal circumstances, Qmodem restores the screen saved before the DOS
Shell was invoked.  If a size change is detected, you will see a Status window
displays that says:


                 ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Status ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
                 ³ Video mode changed.  Screen not restored. ³
                 ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾




Alt-S  Split Screen Mode
In split-screen mode, Qmodem divides the screen into two areas to separate
incoming and outgoing text:








                                                              Qmodem SST     121







ÍÍ[ Keystrokes Queued 0 ]ÍÍÍÍÍÍÍ[ Split Screen ]ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ



The larger section at the top of the screen is reserved for incoming text
received from the remote computer.  The smaller section at the bottom of the
screen echoes transmitted keystrokes.  Current keystrokes are displayed on the
screen's dividing line.

Qmodem implements a true split-screen mode,  complete with a 254 character input
buffer.  Pressing [ENTER] immediately transmits the buffer and clears it for
additional input.  Stored keystrokes are displayed on the screen's dividing
line.  The characters "^M" can be used to substitute an [ENTER] in the string.

If another terminal emulation other than TTY is in effect when Alt-S is pressed,
it is remembered so it can be restored when split screen is exited.  The split
screen mode requires TTY emulation to operate correctly.

NOTE: If you use FKey macros, ^M will not cause the contents of the
      character buffer to be sent;  the text stored in the FKey macro will
      be appended to the buffer.




Alt-T  Screen Dump
Screen contents can be copied to a disk file via the Alt-T command.  When
pressing Alt-T, the following window is displayed:


   ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Screen Dump File Allocation ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
   ³                                                                       ³
   ³ > SCREEN.DMP°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°    ³
   ³                                                                       ³
   ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


°°°°°°°°°°°°°°°°°°°°°°°°° Edit File/Pathname   ESC-Exit °°°°°°°°°°°°°°°°°°°°°°°°


The default file name is that defined in the configuration and may be changed at
the Alt-T prompt.  The screen contents are added to the end of the screen dump
file and are preceded with a Time and Date stamp (if Alt-N/F/T is set ON).  If
the dump was successful, a confirmation message in a status window will appear.



Alt-U  Scroll Back Toggle
The Alt-U Scroll-back command toggle use of the scroll-back capture buffer.  The
Scroll-back command is discussed under the heading "Up Arrow" later in the
documentation.

The default state is to have the Scroll-back capture active.  All data displayed
on the screen is stored in the scroll-back buffer for later recall.  When
pressing Alt-U, a Status window is displayed showing the new state.

122  The Forbin Project, Inc.






Alt-V  View a File
Pressing Alt-V invokes the file viewer/editor program.  When that command is
issued, the View/Edit file allocation window is displayed:


   ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ View File Allocation ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
   ³                                                                       ³
   ³ > LIST *.PAS°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°    ³
   ³                                                                       ³
   ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


°°°°°°°°°°°°°°°°°°°°°°°°° Edit File/Pathname   ESC-Exit °°°°°°°°°°°°°°°°°°°°°°°°


Alt-V can be thought of as a flexible gateway used to browse or edit a file.
The above example assumes use of Vern Buerg's popular LIST program, available on
most BBSs.  LIST is sophisticated replacement for the DOS TYPE command.

Although intended for file browsing or editing, the Alt-V gateway can be used to
invoke any program, even WordStar!  The program to be called by Alt-V can be
defined in Setup (Alt-N/F/V) or can be changed on the fly.  For example, you
could type "DEL *.BAK" and [ENTER] to delete all the files in the current
directory with an extension of ".BAK".

NOTE: If an external program is specified, a DOS Shell is used  and
      sufficient memory must be available.


Alt-V also accepts two special commands: @FSE and @EDITOR.  If you specify
either of these at the beginning of the command, the following actions will take
place:

@FSE uses the internal editor to edit/view the file.  This also assumes that the
text following is a valid DOS filename.  Following is an example of Alt-V use to
edit the AUTOEXEC.BAT file in the C:\ directory:


   ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ View File Allocation ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
   ³                                                                       ³
   ³ > @FSE C:\AUTOEXEC.BAT°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°    ³
   ³                                                                       ³
   ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


@EDITOR uses the user-defined editor rather than the internal editor in any
function where the internal editor would have been used, such as editing the
attached Note files in the dialing directory (Alt-D/N) or the attached Scripts
(Alt-D/V).



Alt-W  Disk Directory
The Alt-W command is Qmodem's internal version of the "DIR /p". DOS command.
This will produce a file listing of the current directory (see the Alt-W command
to change directory).

                                                              Qmodem SST     123




You are first prompted for the drive:\directory\FILE_MASK to use:


   ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ View Directory(s) Allocation ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
   ³                                                                       ³
   ³ > Z:\DL\*.*°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°    ³
   ³                                                                       ³
   ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


The default for this is stored in Setup, Alt-N/D/A.  As is the case with the DOS
prompt, you may change the directory listing argument, with all standard
wildcard "*?" characters being supported.

Then, you will get the Alt-W window:


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Z:\*.* ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³ ..              <dir>   3/26/90   1:47p ³
³ DL              <dir>   3/26/90   1:53p ³
³ GG              <dir>   7/12/90   2:39a ³
³ HOSTDIR         <dir>   3/26/90   1:57p ³
³ LOGO            <dir>   3/26/90   1:57p ³
³ NCI             <dir>   7/25/90   3:23p ³
³ PRINTDOC        <dir>   3/26/90   1:57p ³
³ QMEDIT          <dir>   3/26/90   1:57p ³
³ QPRO            <dir>   3/26/90   1:57p ³
³ RZSZ            <dir>   4/13/90  11:30a ³
³ SCRIPTS         <dir>   3/26/90   1:58p ³
³ SHOW            <dir>   7/25/90   2:54p ³
³ VCS             <dir>   4/18/90   6:00a ³
³ YAK             <dir>   3/26/90   1:58p ³
³ 08-13-19           57   8/13/90   1:21p ³
³ 3XMATE.INC        375   2/21/90  11:17a ³
³ 3XMATE.PAS       9821   7/11/90   9:05a ³
³ 42LOGO.PAS       7348   7/11/90   9:05a ³
³ ALLCHARS.DOC      256   8/09/90   9:52a ³
³ ANSI.KEY          251   8/13/90  11:39a ³
³ ASYINT.ASM      15447   3/13/89  11:04a ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ   for more Í¾

° <dir>-Change Directory  Arrows-Scroll  Alpha-Search  Enter-Selects  ESC-Exit °


This is yet another Pick List type window.

The <dir> entries show subdirectories that can be selected for viewing.  Simply
move the scrollbar to this type of entry and press [ENTER].  The window will
clear and show you the new subdirectory files that match the given mask.  In the
above example, *.* was used as the mask.

 You can scroll through the window with the standard direction keys.   Up, down,
PgUp, PgDn, Home and End all work the way you would expect them.






124  The Forbin Project, Inc.



You can also search lengthy entries by using  Alpha keys.  Just type the letters
of the file you are looking for.  As you type, the scrollbar moves to the first
entry that matches the list of characters.  If you type too many characters and
no match is found, the lower left will clear with the scrollbar on the last
entry that matched.  Typing again repeats the search sequence.  You can quickly
clear the search pattern by pressing the [Backspace] key.  This is one
intelligent Pick List!

You will also note, the status line mentions Enter-Selects.  This Pick List does
double duty, so in this case, the [ENTER] goes back to the FAW window so you can
enter a new Drive:\directory\Mask.



Alt-X  Exiting Qmodem
To exit Qmodem, press Alt-X.  The following prompt window will be displayed:


                         ÕÍÍÍÍÍÍÍÍ Exit Qmodem ÍÍÍÍÍÍÍÍ¸
                         ³  Are you sure? [Y/N/X]      ³
                         ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾



°°° Y-Drop DTR and Exit   N-Return to TERMINAL Mode   X-Leave DTR Up and Exit °°


Replying "Y" to the prompt will immediately terminate Qmodem, close the serial
port (and hang up the modem if a connection was active), and close the Capture
and LOG files if they were opened.

Entering an "X" will cause Qmodem to exit to DOS and leave the DTR line active,
which does NOT hang up the modem and retains the connection if one was active.
This allows you to perform any other process, such as run an external program
which requires more memory then is available via the Qmodem DOS Shell facility.

When the "X" option is used and you are on-line, the environment settings are
saved in a file called QMODEM.INI.  The next time Qmodem started, the values
stored in QMODEM.INI will override the default configuration, and QMODEM.INI is
deleted.  If Qmodem is NOT restarted, the QMODEM.INI file will remain and should
be deleted if not needed.

Replying "N" to the prompt or pressing [ESC] cancels the exit request and
returns to the Terminal mode screen.

CAUTION:Data received after you exit via Alt-X-X will be lost.   Use this
        exit option when you are sure no data will be sent by the remote
        computer.  Most modems and many remote computers will disconnect if
        the connection remains inactive for an extended period of time.  Be
        aware of these limitations when exiting.










                                                              Qmodem SST     125



Alt-Y  Delete a File
Alt-Y is a powerful command used to permanently delete a file.  When pressing
Alt-Y, the File Delete Allocation Window will be displayed:


   ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ File Delete Allocation ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
   ³                                                                       ³
   ³ > Z:\scripts\qqqq.scr°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°    ³
   ³                                                                       ³
   ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


°°°°°°°°°°°°°°°°°°°°°°°°° Edit File/Pathname   ESC-Exit °°°°°°°°°°°°°°°°°°°°°°°°


Type the desired file name in the space provided and [ENTER].  Qmodem will
verify that the file exists.  If it does, a second confirmation prompt will be
issued, just to be sure:


        ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ File Delete ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
        ³ You are about to delete the following file:                 ³
        ³ Z:\scripts\qqqq.scr                                         ³
        ³ Are you SURE ? [Y/N]                                        ³
        ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


°°°°°°°°°°°°°°°°°°°°°°°°°°° Y-Delete the File   N-Exit °°°°°°°°°°°°°°°°°°°°°°°°°


This is your last chance.  If you erase the wrong file, issue the Alt-R DOS
Shell command immediately and attempt to recover the lost file with a program
such as Norton's Undelete, PCTools, Mace Utilities etc.  There is no UNERASE
facility built into Qmodem.



Alt-Z  Xon/Xoff Toggle
Alt-Z toggles Xon/Xoff flow control. Xon/Xoff is a simple means of controlling
data flow, used mostly by mini and mainframe computers.  With Xon/Xoff in the
OFF mode, a buffer overrun may occur on long ASCII text transmissions (incoming
data will exceed the internal buffer capacity).

If Xon/Xoff is ON and Qmodem detects the Xoff (^S) code, the Status Line will
change to the following:


°°°°°°° XOFF(^S) Received, waiting for XON(^Q).  ^Q-Override and Continue °°°°°°


When the remote system is ready to receive more data, it will send the Xon (^Q)
code and the window will disappear.  If you believe there is a problem, you can
manually restart the data transfer by pressing ^Q.

TIP: If you have the Status line disabled via Alt-Minus, you will not see
     that you have received the XOFF.  If you think you are locked up, it
     is always a good idea to try pressing ^Q once or twice to see if this
     was the problem.


126  The Forbin Project, Inc.






PgUp/PGDN  Uploading & Downloading Files
Selecting a protocol
Selecting a protocol is the first step in a file transfer.  Pressing PgUp
(upload - send)  or PgDn (download - receive) will display the protocol
selection window:


                           ÕÍÍ Download Protocols ÍÍ¸
                           ³ Free Space 7622656     ³
                           ³ A - Ascii              ³
                           ³ X - Xmodem             ³
                           ³ C - Xmodem CRC         ³
                           ³ R - Xmodem Relaxed     ³
                           ³ O - Xmodem-1K          ³
                           ³ Y - Ymodem Batch       ³
                           ³ Z - Zmodem Batch       ³
                           ³ F - Xmodem-1K/G        ³
                           ³ G - Ymodem/G Batch     ³
                           ³ Your Choice ?          ³
                           ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


°°°°°°°°°°° LETTER-Select a Protocol for the File Transfer   ESC-Exit °°°°°°°°°°


The above window shows the PgDn protocol list.  The only difference between the
PgUp and PgDn window is the PgDn window includes a free space check at the top.
You will want to know how much free disk space you have when downloading files.

If external protocols have been defined in Alt-N/P, they will be displayed at
the bottom of the protocol selection window:


                           ÕÍÍ Download Protocols ÍÍ¸
                           ³ Free Space 7622656     ³
                           ³ A - Ascii              ³
                           ³ X - Xmodem             ³
                           ³ C - Xmodem CRC         ³
                           ³ R - Xmodem Relaxed     ³
                           ³ O - Xmodem-1K          ³
                           ³ Y - Ymodem Batch       ³
                           ³ Z - Zmodem Batch       ³
                           ³ F - Xmodem-1K/G        ³
                           ³ G - Ymodem/G Batch     ³
                           ÆÍÍÍÍÍÍÍ External ÍÍÍÍÍÍÍµ
                           ³ K - Kermit             ³
                           ³ P - Puma               ³
                           ³ Your Choice ?          ³
                           ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


°°°°°°°°°°° LETTER-Select a Protocol for the File Transfer   ESC-Exit °°°°°°°°°°





                                                              Qmodem SST     127



The protocol selection windows both feature the "F" and "G" protocols (Xmodem-
1K/G and Ymodem/G).  These are "Hardware-handshaking" protocols which can only
be used if your computer is equipped with an error-correcting modem (a modem
with supports MNP).

To activate these, CTS/RTS Flow Control must be specified in the Alt-N/M/T Setup
menu.  If CTS/RTS Flow is not specified, or if it is specified and your computer
is not equipped with an error-correcting modem, the F and G selections will not
be available.

When uploading or downloading files, both sending and receiving computers must
use the same communication protocol. Select the agreed-upon protocol by pressing
the corresponding letter.  "X", for example, would select Xmodem, which is
supported almost universally.

NOTE: Bulletin Board (BBS) programs each use a different method for
      selecting file transfer protocols.  When communicating with a BBS,
      make sure that you have selected the proper protocol on the BBS System
      before making the protocol selection in Qmodem.



Internal Protocols
ASCII
The ASCII protocol is used primarily for on-line text transfers.  It does not
support  the transferring of binary data such as programs or compressed files.
Attempting to do so is, well, crazy!

ASCII does not perform any error-checking, which makes it very sensitive to line
noise.  Bursts of phone line interference will introduce stray characters which
are not part of the data being transmitted.  For this reason, ASCII transfers
are not recommended unless they are used for specific purposes where that
protocol is needed.

NOTE: It is advisable to use XON/XOFF Software flow control with ASCII.
      Failure to do so may cause loss of data.


XMODEM
There are two XMODEM protocols currently in use.  The original Xmodem uses a
Checksum method to insure that the data received is the same as that which was
sent.  Checksum is a very simple error-detection method with an accuracy rate of
99.6%.  Xmodem Checksum transmits 128-byte data blocks.


XMODEM CRC
Xmodem-CRC (Cyclic Redundancy Checking) is similar to Xmodem-Checksum, but uses
a far more reliable error-detection algorithm (99.9969%.).  In the event that
the wrong Xmodem protocol was selected, Qmodem will correct itself
automatically, eliminating the need for aborting the transfer.


RELAXED XMODEM
Relaxed Xmodem is basically identical to Xmodem-Checksum, but error timing has
been relaxed by a factor of 10.  In other words, it takes ten times longer for
an error condition to be generated.  This protocol was designed specifically for
CompuServe communications,  due to the questionable implementation of Xmodem by
that On-line Information Service.


128  The Forbin Project, Inc.





XMODEM-1K
Xmodem-1K is a modified version of Xmodem CRC, which uses 1024-byte blocks as
opposed to Xmodem's 128 byte blocks.  In earlier releases of Qmodem, this
protocol was referred to as Ymodem.  The name has been changed to reflect the
addition of True Ymodem ((c) Omen Technology) to Qmodem.


YMODEM
Ymodem is the true implementation of the YMODEM batch protocol and is referred
to as YMODEM or YMODEM BATCH.  This protocol supports the transfer of multiple
files within a single session which does not require user intervention.

When using Ymodem, only one filename can be specified at a time.  To allow
multiple file transfers, wildcards must be used in the filename for uploads.
For downloads, Qmodem will automatically retrieve the names of the files being
sent from their respective header records.

True Ymodem and Ymodem/G batch protocols include "Header Records" in the
downloaded data.  These records contain file-dependent information such as name,
size, and date/time stamps.  As a result, file names need not be specified prior
to starting batch downloads.  As an added benefit, the moving Transfer
Completion Graph is updated during batch downloads since file sizes are known.

When the filename is extracted from the header block, it is checked to see if it
will create a valid DOS filename.  The Ymodem header was designed to be flexible
and allow for non MS-DOS file naming conventions.  Apple, Atari and Commodore
computers are more liberal in their file naming conventions and these need to be
converted when downloading these files.

Suppose you are calling a non-IBM BBS system and want to download one of their
foreign files and you are using Ymodem as the protocol.  Qmodem converts their
filename to one that is acceptable to MS-DOS on-the-fly.

The rules for the conversion are:

  1. The last ".", if any, in the Header filename is where the new DOS filename
     extension will begin.

  2. The first 8 character (or less, depending on the position of the "." in
     step 1) is converted.  Periods (".") are replaced with dollar-signs ("$"),
     and spaces (" ") are replaced with underscores ("_").


Examples:

     Foreign Filename              Converted Filename

     STARTER.ARC.STV1.2       STARTER$.2
     ST.DATAKIT.ARC.4         ST$DATAK.4
     ST.SOUND.ARC.1.2         ST$SOUND.2
     A LONG NAME.EXTENS       A_LONG_N.EXT







                                                              Qmodem SST     129



XMODEM-1K/G & YMODEM/G
These two protocols are identical to their non-/G counterparts. /G protocols do
not perform any error detection and rely on the error-correction features of the
modems.  Modems equipped with internal protocols such as like MNP, LAP-B, and
X.PC insure that communications are error-free.  Hardware handshaking via the
CTS/RTS signal lines must be enabled with such modems.

/G protocols will not be available unless the following is true:

     CTS checking is enabled in the Alt-N/O/T/C Setup menu option.

     The modem's CTS signal is enabled when the serial port is initialized.

CAUTION:Make sure that the modem does not force the CTS signal ON at all
        times.  This will cause a modem buffer overflow resulting in an
        aborted transfer.


NOTE: Xmodem-1K/G and Ymodem/G cannot retransmit bad data blocks.  In
      theory, there should be NO bad blocks of data in an error-free
      connection.  If errors occur, they are likely to be cause by an
      improper setup in either the modem or Qmodem.

High-speed or Error-Correcting modems communicate with Qmodem at the hardware
level via the CTS/RTS interface.  The modem cables used in conventional modems
(IE 1200/2400, non-MNP units) may not carry all the necessary signals (pins
could be missing).  The wrong cable could prevent Qmodem from detecting the CTS
signal, and ignore the modem's hardware-handshaking capabilities.

When in doubt, use a serial cable with all 25 pins connected (a flat ribbon, 25-
conductor cable).  AT Users may use a 9-pin to 25-pin adapter with all 9 lines
connected, attached to a 25-conductor cable as described above.


Zmodem
This is the popular streaming protocol put into the public domain by Telenet.
Zmodem uses a variable sized block to transfer date over even the noisiest phone
lines.  Zmodem was designed as a Batch transfer protocol.  As such, it shares
the same transfer windows and allocation methods that the Ymodem protocol uses.

Should errors occur, Zmodem can tell the sending end just exactly where to
restart.  The real bonus to Zmodem is that it does not require a high-speed or
error-correcting modem with MNP of V.42 to be effective.  While it is not as
fast as Ymodem/G or Xmodem-1K/G, it does perform well enough to have become a
'standard' in the industry.

One of the benefits of Zmodem is Crash Recovery.  This allows an aborted file
transfer to be restarted at a later time, without having to retransmit the
already received portion of the file.  A check is made to make sure the partial
file has not changed.  If it hasn't, then it picks up where it left off.  It it
has, then the file transfer is restarted from the beginning.


External Protocols
Due to their nature, external protocols do not have a seamless interface and
operate differently from built-in protocols.  When an external protocol is used,
Qmodem invokes the protocol's upload or download batch file which in turn
executes the external protocol's file transfer program.


130  The Forbin Project, Inc.




Since Qmodem has no control over external programs, screen displays will ba
handled entirely by the external program.  The screen will be cleared before
control is passed to the external protocol, and once the transfer is complete,
you will be returned to the standard Qmodem terminal display.

For more information on installing External protocols, refer to the Setup
(Alt-N/P) section.   For protocol-specific information, refer to the external
protocol's documentation.



Download File Allocation
After selecting your protocol, you have to tell Qmodem where to put the file and
what to call it.  If it is a Batch transfer protocol, then you only have to
decide where to put the file.  Batch transfers send the filename as part of the
file.

The non-batch window looks like this:


   ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Download File Allocation ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
   ³                                                                       ³
   ³ > C:\QMODEM\DL\°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°    ³
   ³                                                                       ³
   ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


°°°°°°°°°°°°°°°°°°°°°°°°° Edit File/Pathname   ESC-Exit °°°°°°°°°°°°°°°°°°°°°°°°


The batch window looks like this:


   ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Download Path Allocation ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
   ³                                                                       ³
   ³ > C:\QMODEM\DL\°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°    ³
   ³                                                                       ³
   ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


°°°°°°°°°°°°°°°°°°°°°°°°° Edit File/Pathname   ESC-Exit °°°°°°°°°°°°°°°°°°°°°°°°


Notice the Window titles.  Non-batch transfer want a complete
drive:\path\filename to be successful.  Batch transfer want only the
drive:\path.  Remember, the filename has already been decided and will
automatically be picked up as part of the file transfer.

Qmodem has the ability to "pick" file names directly from the screen.  A scan is
made on the screen, from right to left, bottom to top for a valid file name.
"Valid File Name" is defined as a 1- to 8-character text string followed by a
period and a 2- or 3-character suffix.  Spaces, semicolons, and the left and
right margins are valid file name delimiters.  Following are some examples of
valid and invalid file names:

  THISFILE.TXT      valid
  README.1          invalid (not enough chars in suffix)


                                                              Qmodem SST     131



  QMDMSST.ARC       valid
  PROGRAM.THIS      invalid (too many characters in suffix)
  MPROGRAM1.THIS    invalid (name too long)

If a suitable filename was not found, or if the one picked is not correct, the
filename must be added or edited manually.  Once the desired file name has been
specified, press [ENTER] to start the file transfer.



Upload File Allocation
Uploading files is similar to Downloading.  You still tell the remote host what
you are going to do before doing it.  You also have to make sure you use the
same protocol that you tell the host.

The PgUp protocol window is identical to the PgDn Down load window, with the
exception that the Free Disk Space is not at the top.  So, assuming you have
told the remote system what protocol you are going to use, and the filename if
necessary, you can begin your upload!

Once you have selected a protocol, you have to tell Qmodem the filename(s) to
use.  The possibilities can be simple if you selected a non-batch protocol, to
extensive for batch protocols.

Non-batch and External protocol windows look like this:


   ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Upload File Allocation ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
   ³                                                                       ³
   ³ > D:\QMODEM\qmodem.pas°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°    ³
   ³                                                                       ³
   ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


°°°°°°°°°°°°°°°°°°°°°°°°° Edit File/Pathname   ESC-Exit °°°°°°°°°°°°°°°°°°°°°°°°


You simply enter the complete drive:\path\filename of the file you are sending,
and press [ENTER].


Batch Entry Window (BEW)
Batch protocols are a different story.  You get a much enhanced screen called
the Batch Entry Window (BEW for short).  The BEW looks like this:
















132  The Forbin Project, Inc.




ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Batch Upload File Entry ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³PATH : D:\QMODEM\DL\°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°                ³
³                                                                           ³
³FILES: °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°³
³       °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°³
³       °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°³
³       °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°³
³                                                                           ³
³PATH : D:\°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°                ³
³                                                                           ³
³FILES: °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°³
³       °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°³
³       °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°³
³       °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°³
³                                                                           ³
³PATH : D:\°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°                ³
³                                                                           ³
³FILES: °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°³
³       °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°³
³       °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°³
³       °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°  °°°°°°°°°°°°³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍF1 HelpÍÍ¾


°°°°°°°° F2-Pick List   F3-Last Found   F4-Clear   F10-Upload   ESC-Exit °°°°°°°


The Batch Entry Window (BEW), used when uploading with a Batch Protocol, is
divided into three groups, each group comprising a PATH and 20 FILES cells.

The 3 different PATH fields are automatically initialized to the values defined
by the Alt-N/D/1, Alt-N/D/2 and Alt-N/D/3 in the Setup.  The FILES cells are
blank.  The three groups work independently of each other.  By this, we mean
that you could specify files in the 1st and 3rd groups without having to specify
any in the 2nd group.  Maybe you only want to send from the 2nd group only, and
that is fine too.

The PATH cells are like the FILES cells in that they can be changed within the
window before uploading.  You may decide to leave one of the 3 default paths
blank, just in case you frequently upload from several different directories
depending on who you call.  This would save time clearing a PATH field all the
time.

Each FILES cell can contain exactly one filename specification.  8 characters
for the NAME, the PERIOD, and 3 characters for the EXTENSION.  You do not have
to use all 12 characters, however.  Filenames such as YEAREND.WKS, REPORT.DOC,
and SOURCE.C are all valid.

To really make them functional, each cell could include multiple wildcard
characters.  The wildcard characters * and ? can allow each cell to specify a
group of files.  Filenames such as MONTH??.WKS, *.PAS, and even *.* are valid!
In these cases, all files matching the wildcard specification would be uploaded
in the batch transfer.






                                                              Qmodem SST     133



Caution should be used to avoid duplication when using wildcards within the same
group of cells.  There is no checking done to see if a file matches one or more
of the cells with wildcards.  You could be sending the same file more than once
in the same batch upload.  If the 3 examples were placed in the same cell group,
all the files matching the first two would be sent twice because the 3rd
example, *.*, will send them all again.

The status line at the bottom of the screen lists these options if you entered
the BEW with the PgUp key:

        F2-Pick List   F3-Last Found   F4-Clear   F10-Upload   ESC-Exit

If you used the Alt-6 Key, you will see this:

     F2-Pick List   F3-Last Found   F4-Clear   F10-Save to Disk   ESC-Exit

F2-Pick List

  When the cursor is in a FILES cell, you can press [F2] to open a Pick List.
  If the cell is blank, a default of *.* is used, showing all the available
  files in that PATH group.  If the cell contains a filename with wildcard
  characters, such as *.PAS, then all the files that end in .PAS are shown in
  the Pick List.  With the Pick List open, just move the scrollbar to the entry
  you want in that cell and press [ENTER].  The cell is then filled in with
  that filename.  You can only tag one filename at a time from the Pick List.


F3-Last Found

  This will scan the underlying screen for the last valid filename (right to
  left, bottom to top) and place it in the current cell.  You might use this
  when you have a file to upload, and you have just told the remote system
  about the file.  As long as it is on the underlying screen, you do not have
  to type the filename in again.


F4-Clear

  This clears all fields in the BEW and resets the three PATH cells to the
  defaults specified in Alt-N/D.


F10-Upload

  When you have pressed PgUp and selected either Y, G or Z, and you have 1 or
  more files defined, this will begin the upload.


F10-Save to Disk

  This will write out a file called QMODEM.BEW in the directory where the
  QMODEM.CNF file was found.  It contains all of the information in the BEW.
  The BEW window will then close.  The next time the BEW is opened, the
  QMODEM.BEW file is searched for and loaded back in if found.






134  The Forbin Project, Inc.



ESC-Exit

  Exits the BEW and aborts any changes made.


Download Transfer Window
The download window is common throughout all the internal protocols, except
ASCII.  Lets look at the others first:


 ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Download Status ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
 ³ File  BETA00.ZIP         Protocol Ymodem/G Batch                        ³
 ³ Path  Z:\DL                                                             ³
 ³                                                                         ³
 ³ Bytes Total 214572       Blocks Total 210        Time Elapsed 00:00:09  ³
 ³ Bytes Rcvd  14336        Blocks Rcvd  14         ++ Remaining 00:01:59  ³
 ³ Error Count 0            Block Size   1024       Efficiency   175.25%   ³
 ³                                                  Chars/Second 1682      ³
 ³ Status Msgs                                                             ³
 ³ Completion  6%   ²²²þþþþþþþþþþþþþþþþþþþþþþþþþþþþþþþþþþþþþþþþþþþþþþþ     ³
 ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


°°°°°°°°°°°°°°°°°° Download In Progress    ESC-Cancel Transfer °°°°°°°°°°°°°°°°°


You probably won't find a better file transfer status window anywhere!  Here is
a breakdown of each field.

FILE

  The name of the file being received.  If it is a Batch download (Ymodem or
  Zmodem), then this is filled in automatically.  Non-batch transfers allow you
  to enter the filename.

PATH

  This is the drive and subdirectory where the File is being saved to.

PROTOCOL

  The current transfer protocol being used.

BYTES TOTAL

  This is the number of bytes that is being received.  This field will say
  "N.A." if the protocol is non-batch.

BYTES RCVD

  This is the number of bytes received so far.

ERROR COUNT

  This is the number of errors recorded so far.





                                                              Qmodem SST     135



BLOCKS TOTAL

  This is the number of blocks expected to be received.  It is figured based on
  the Bytes Total  divided by the Block Size.  If it is a non-batch transfer,
  this will show "N.A.".

BLOCKS RCVD

  This is the number of blocks received so far.

BLOCK SIZE

  This is the current block size being used by the sending side.  It is
  included because protocols like Ymodem and Zmodem can change their data block
  sizes on the fly.

TIME ELAPSED

  This is the current elapsed time since the start of the download for the
  current file.  Current  is stressed because a batch transfer may have more
  than one file, and there is no global elapsed time kept.

++ REMAINING

  This is the estimated remaining time in the transfer for the current file.
  If this is a non-batch transfer, this field will be blank.

EFFICIENCY

  This shows you how efficient the protocol is.  It is based on the current DCE
  Baud Rate as reported by your modem, and the number of bytes received against
  the elapsed time.  Roll these all together, sprinkle with a little sugar, and
  out pops the efficiency!   Seriously, if the modem has features such as data
  compression, the efficiency can rise above the normal 100% DCE rate.
  Remember, this is based on the DCE speed, not the DTE rate that the serial
  port may be locked at.

CHARS/SECOND

  This is a by-product of figuring the Efficiency.  When you know how many
  bytes have been received in a set number of seconds, you can easily figure
  the Character per Second.  To convert this to a baud rate, multiply this by
  10.

STATUS MSGS

  Status messages keep you posted on the progression of the transfer.

COMPLETION

  Some people call this the gas gauge because it goes from Empty (0%) to Full
  (100%) as the transfer proceeds.  This is just a quick visual check of how
  much is complete and how much further you have to go.  Each block represents
  2% of the entire file.  If this is a non-batch transfer, this will not be
  available.





136  The Forbin Project, Inc.



Download ASCII Window
When downloading with ASCII, you do not get a fancy window.  Instead, the Status
Line switches to the following:


°°°°°°°°°°°°°°°° ASCII DOWNLOAD IN PROGRESS    ESC-Save and Exit °°°°°°°°°°°°°°°


The current terminal emulation stays in effect, and the screen  remains
unchanged.  Except, all data received now is saved to the file you specified.


Upload Transfer Window
The Upload Transfer window is identical to the Download window, with two
exception.  Wherever the word RCVD appears, it is changed to SENT.  Also,
because all the file sizes are known in advance, there are no "N.A." fields.


Upload ASCII Window
During an ASCII Upload, the Status Line changes to keep track of the upload.
Following is a sample of a QMODEM.LOG file being uploaded:


20:01:46  05-16-90  Connected With  : GEnie RealTime Conference
20:01:46  05-16-90  ++ Phone Number : 233-7623
20:01:46  05-16-90  ++ Comm Speed   : 2400-8-N-1
20:01:46  05-16-90  Online Timer Started.
20:20:41  05-16-90  Elapsed Online 00:18:54
20:21:56  05-16-90  Connected With  : GEnie RealTime Conference
20:21:56  05-16-90  ++ Phone Number : 233-7623
20:21:56  05-16-90  ++ Comm Speed   : 2400-8-N-1
20:21:56  05-16-90  Online Timer Started.
20:37:32  05-16-90  Hangup Command entered.
20:37:33  05-16-90  Elapsed Online 00:15:36
22:32:21  05-16-90  Connected With  : Sub Line 1              HST
22:32:21  05-16-90  ++ Phone Number : 233-1453

°°°°°° Uploading qmodem.log  Sent = 2313    Complete = 3%   ESC-Terminate °°°°°°


The screen uses whatever Terminal emulation was in effect at the time of the
Upload.  The Status line shows the Filename, the number of Bytes sent so far and
the Percent completed.



UP-ARROW  Scroll-back
As the on-line session proceeds, all displayed information is stored in a
special scroll-back buffer. Pressing the Up-Arrow selects Scroll-back mode.
While in this mode,  you can scroll backward and forward through previously
displayed text.

TIP: The size of the scroll-back buffer is defined in the Alt-N/O/M/L Setup
     menu.






                                                              Qmodem SST     137



Following is a sample scroll-back display:


CONNECT 38400 / 08-14-90 (16:51)
(Error Correcting Modem Detected)

The Forbin Project - Home of Qmodem
PCBoard (R) v14.5/U (beta 08/14/90 09:21) - Node 7

Do you want ANSI Graphics (Enter)=no? n

 ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
 ³                       Welcome to The Forbin Project!                       ³
 ³                                  Home of                                   ³
 ³                                Qmodem SST!                                 ³
 ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

 Everyone is waiting for 4.2 to be released.  You know it exists, and you might
 even have seen copies floating around where they shouldn't.  So, we're having
 a special in honor of the as-yet released 4.2!

 Register your Compete Package of 4.1B now for $60.00 and you will ALSO get the
 Complete 4.2 package when it ships!

     o  Registration for the best darned Comm Program out there!

     o  Complete Disks & Manual for version 4.1B!   (4.0 with readme files)
°° SCROLL-BACK   PgUp PgDn   F1-Help  S-Save  C-Clear  ESC-Exit  Queue 0    °°


While in scroll-back mode, the following cursor keys are active:

Up-Arrow/Down-Arrow      Move up or down one line.

PgUp/PgDn           Move up or down one page at a time.

Home/End            Move to the top and bottom of the buffer.

Pressing [ESC] exits scroll-back mode and returns to the terminal screen.

Pressing [S] will display a prompt for the name of the file to which the scroll-
back buffer is to be saved:


   ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Scroll Back Dump File Allocation ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
   ³                                                                       ³
   ³ > SCROLL.SAV°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°    ³
   ³                                                                       ³
   ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


°°°°°°°°°°°°°°°°°°°°°°°°° Edit File/Pathname   ESC-Exit °°°°°°°°°°°°°°°°°°°°°°°°


As with other Qmodem file prompts, you may override the default file name and
press [ENTER] to save the file.




138  The Forbin Project, Inc.



Pressing [C] clears the Scroll-back buffer and frees up the memory allocated to
it.

The QUEUE at the far right of the scroll-back status line tracks the amount of
incoming data while you are viewing Scroll-back information.



CTRL-HOME  Capture to Disk
Ctrl-Home is a toggle which starts or stops the Session Capture facility.  While
Session Capture is active, the data displayed on the screen is also saved to a
disk file.

When Session Capture is started, the following "Capture" file allocation window
will be displayed:


   ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Capture File Allocation ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
   ³                                                                       ³
   ³ > CAPTURE.CAP°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°    ³
   ³                                                                       ³
   ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾



°°°°°°°°°°°°°°°°°°°°°°°°° Edit File/Pathname   ESC-Exit °°°°°°°°°°°°°°°°°°°°°°°°


The file name may be changed by backspacing over the default name and typing a
new one.  If the capture file is new, you will be prompted for its creation.
Pressing [ESC] will cancel the session capture request and return to the
terminal screen.

Whenever session capture starts, a Status window will tell you that it has been
started successfully.  To end Session Capture, press Ctrl-Home again.  The
capture file will be closed and the Status window will be displayed telling you
so.



CTRL-END  Sending a BREAK
Pressing Ctrl-End generates a BREAK signal.  "BREAK" is a special signal
generated by the serial adapter,  used to notify the receiving computer of a
specific condition.  In most cases, BREAK is used to tell the other computer to
interrupt whatever it is doing.  For example, the GEnie On-line Service
interprets the BREAK signal in the same manner as your PC would interpret ^C or
Ctrl-Break.

In response to Ctrl-End, Qmodem displays the following message:


<<BREAK>>








                                                              Qmodem SST     139



NOTE: As is the case with PC programs which disable or ignore Ctrl-Break,
      the BREAK signal may not be recognized by the receiving computer.
      BREAK handling is a function of the communication software, and this
      feature may not be implemented in the computer you are communicating
      with.




SHIFT-TAB  Add Linefeeds
In some cases, text lines may be overwritten on the screen.  The most likely
reason is that the other computer is not sending Linefeed (LF) characters at the
end of each line.

Pressing Shift-Tab toggles the addition of a Linefeed (LF) character to each
incoming Carriage Return (CR).  To turn the Add Linefeed feature OFF, press
Shift-Tab again.

NOTE: If text lines are double-spaced, Linefeeds are being added when they
      shouldn't.  Press Shift-Tab again to disable Linefeed addition.

When Shift-Tab is pressed, a Status window will be displayed showing the new
state of the toggle.



Alt-1  Backspace / DEL Toggle
Alt-1 toggles the value generated by the Backspace key between the standard
backspace and the DEL character.

In normal operating mode, Backspace (BS) and Ctrl-H (^H) are treated in the same
fashion and both generate a Backspace (ASCII 8) character.  Certain terminals,
such as the DEC VT100 require that a DEL character be sent (ASCII 127) when the
backspace key is pressed.

When pressing Alt-1, a Status window will be displayed showing the new state of
the toggle.  The BS/DEL setting can be reversed on-the-fly by pressing Ctrl-
Backspace.  The current status of the BS/DEL toggle is displayed in the
Alt-N/O/T setup menu.

NOTE: If the BS/DEL setting is incorrect, pressing the Backspace key will
      not yield the desired result on the receiving computer.  If the toggle
      is active and the other computer expects a BS character, it will
      display the ASCII 127 instead (ASCII 127 on IBM PCs is displayed as a
      little house).




Alt-2 and Alt-4   EGA/VGA Modes
Qmodem supports 2 alternate screen modes with EGA/VGA adapter.  Alt-2 restores
the standard 80x25 video mode for both EGA and VGA adapters.  Alt-4 switches EGA
systems to 80x43 mode and VGA systems to 80x50 mode.  The screen will be cleared
following each video mode change.

TIP: Some "SuperEGA" or "SuperVGA" adapters also support extended screen
     modes beyond the standard 80x25 display.  These extended modes can be
     used if they are activated within Qmodem with a FKey macro which
     invokes the adapters' setup utility with a @SHELL command.

140  The Forbin Project, Inc.




     Example:

     The Video-7 VEGA VGA comes with a utility called ESU.COM used to
     switch video modes.  To run this utility within Qmodem, assign the
     command "@SHELL ESU 43" to a Qmodem function key via the Alt-J
     command.




Alt-3  Debugging Screen
This is used by Tech Support at Forbin should you have a problem.  The details
of this window are beyond the scope of this manual.  Suffice to say, it contains
important information about your particular setup, and you can count on being
asked about the contents should you call for help.  This is one more reason you
should be sitting in front of your computer, with Qmodem running, when you call
for help.  It is usually a waste of your time and ours if you are not.



Alt-6  Batch Entry Window
This is the same BEW window as discussed back on page 156.  Please refer back
for a complete discussion.



Alt-8  Hi-Bit Stripping Toggle
Some computer systems use the high bit of each 8-bit character for parity
checking , like CompuServe and GEnie.  If the high bit is not removed, the
screen display will consist of high-order ASCII characters (>ASCII 127) such as
foreign, graphic, or scientific characters.

Alt-8 toggles the stripping of the high-bit ON and OFF.  When pressing Alt-8,  a
Status window will be displayed showing the new state of this toggle.  Qmodem
starts in 8-bit mode by default.  This can be changed with a Script command to
automate high-bit stripping, for example when calling Compuserve.

The Status Line will display an "8" or "7" in the Toggles area to reflect the
current mode.

TIP: Some BBS's use fancy graphics characters and ANSI escape codes.  To
     display these properly, 8 bit mode must be in effect.



Alt-9  Copying to the Printer
The Alt-9 printer session toggle is similar to the DOS Ctrl-PrtSc command.  If
your system is equipped with a printer, pressing Alt-9 will replicate all screen
displays on the system printer.  To stop session printing, press Alt-9 again.

When pressing Alt-9,  a Status window will be displayed showing the new state of
the toggle.  The printer should be READY when the Alt-9 command is issued.  If
the system is not equipped with a printer, or the printer is not ready (IE.,
powered off or offline), Qmodem will display an "Abort ,Retry, Ignore or Fail"
Error window.




                                                              Qmodem SST     141




Alt-0  Log File Toggle
The Alt-0 command starts or stops Qmodem Session Log recording.  The session LOG
feature is used to keep track of major Qmodem activity.  When the session log is
active, Qmodem writes an entry in the session log file reflecting information
such as:

  Who was called
  The date and time of the call
  How long the on-line session

Each log entry is time- and date-stamped.

Alt-0 is a toggle.  If the Log File is closed, a filename prompt will be issued
and the file will be opened. If the Log File is already opened, it will be
closed.

Following is a sample Log File listing:

14:18:39  08-07-1990  Connected With  : Sub Line 7            {F9}
14:18:39  08-07-1990  ++ Phone Number : 233-6035
14:18:39  08-07-1990  ++ Comm Speed   : 38400-8-N-1
14:18:39  08-07-1990  Online Timer Started.
14:19:13  08-07-1990  ++ Protocol : Ymodem/G
14:19:13  08-07-1990  ++ File D:\TEMP1\UPLOAD\CHECKRIM.ASM
14:19:15  08-07-1990  ++ Chars Per Second    : 2363
14:19:15  08-07-1990  ++ Effective Percent   : 246.1
14:19:38  08-07-1990  ++ File D:\TEMP1\UPLOAD\COMMIO.ASM
14:19:47  08-07-1990  ++ Chars Per Second    : 2022
14:19:47  08-07-1990  ++ Effective Percent   : 210.6
14:19:47  08-07-1990  ++ File D:\TEMP1\UPLOAD\COMP-CRC.ASM
14:19:54  08-07-1990  ++ Chars Per Second    : 2448
14:19:54  08-07-1990  ++ Effective Percent   : 255.0

Some Log entries may take up more than one line in the file.  Any log entry
which starts with "++" is a continuation of the previous one.  For example,
download or upload log entries are made up of several records in order to record
all meaningful statistics.

Following is a complete list of all possible Log entries (the time and date
stamps are not shown):


Key       Log entry
-----     ------------------------------------------
[user]    STAMP [stamp message from Fkey or Script]

[auto]    On-line Timer Started.

[auto]    Elapsed On-line xx:xx:xx

Alt-D     Connected With  : [Board Name]
          ++ Phone Number : [Board Number]
          ++ COM Speed    : [Speed-Parity-Dbits-Sbits]

Alt-H     Hang-up Command entered.

Alt-K     COM Port [PortNumber] selected.


142  The Forbin Project, Inc.




Alt-J     New KEY file [KeyFileName].

Alt-L     Default Drive now [DriveLetter]:

Alt-O     Directory changed to [DirectoryPath]

Alt-R     Dropping to DOS.
          ++ Drop to DOS Failed.

Alt-X     Exiting QMODEM.

Alt-Y     File [Filename] DELETED.

PgDn      Download File [Filename]
          ++ Protocol : ASCII
          ++ Protocol : Xmodem
          ++ Protocol : Xmodem CRC
          ++ Protocol : Xmodem Relaxed
          ++ Protocol : Xmodem-1K
          ++ Protocol : Xmodem-1K/G
          ++ Protocol : Ymodem
          ++ Protocol : Ymodem/G
          ++ Long block errors   : [Number]
          ++ Short block errors  : [Number]
          ++ SOH errors          : [Number]
          ++ Complement errors   : [Number]
          ++ Block number errors : [Number]
          ++ Time Out errors     : [Number]
          ++ Resend Block errors : [Number]
          ++ Checksum errors     : [Number]
          ++ Chars Per Second    : [Number]
          ++ Effective Percent   : [Number]
          ++ Download Aborted.
          Download Executing [BatchFileName].
          ++ External Batch Failure.

PgUp      Upload File [Filename]
          ++ Chars Per Second    : [number]
          ++ Effective Percent   : [number]
          ++ Upload Aborted.
          ++ Using Ymodem-G protocol.
          ++ Using Xmodem CRC protocol.
          ++ Using Xmodem protocol.
          ++ Using Ymodem protocol.
          ++ Using ASCII protocol.
          ++ Transfer Successful.
          External Upload Batch [BatchFileName]
          ++ External Batch Failure.

^End      BREAK signal sent.


Entries starting with "[user]" vary depending on the STAMP command used in FKeys
and Script commands.  Both will begin with the word "STAMP" followed by user-
supplied text.




                                                              Qmodem SST     143



Entries starting with "[auto]" are recorded whenever Qmodem changes from offline
to on-line status and vice versa.

Remaining entries are related to the command listed in the left column.

Since Logging can be turned on automatically, you can now keep a perfect record
of all your long distance calls.  Many other important functions of operation
can also be tracked with the Session Log feature.



Alt-5  Host Mode
The Host mode is like a small BBS system.  It allows others to call your system
without a lot of hassles.  The Host Mode features the following:

  o  Open, Closed, and Callback operation to implement as little or as much
     security as needed.

  o  Support of all internal and external file transfer protocols (except ASCII)
     for both uploads and downloads.

  o  User-customizable menus.  Default menus are provided and can be modified or
     replaced altogether to meet users' requirements.

  o  Full-featured messaging system:  Enter/Read/Reply/Kill messages, and
     Private messaging facility.

  o  Shell to DOS from remote, with optional password protection.

  o  Shutdown from remote, also with optional password protection.

  o  Ability to call Scripts from the Host.  New Host features can be
     implemented via standard Qmodem scripts.

  o  Sysop CHAT mode which allows callers to converse with the SYStem OPerator
     while on-line..

  o  On-line listing of the HOST download file directory.

  o  Complete online help for each menu option.  These help files can be
     customized by you should you want.


Host Setup
Before it can be used, the Qmodem Host Mode must be configured via the Alt-N/H
Host Setup.


External Files Required
The Password File, QMHOST.PWD, is the only file required to run Host Mode.
QMHOST.PWD contains users' Names, Passwords, Security Levels, and optional
CallBack phone numbers.  If QMHOST.PWD does not exist, it will be created
automatically the first time Host Mode is started.

The file "QMHOST.PWD" is a CR/LF-delimited ASCII file.  It can be edited with
the Internal Editor or any standard text editor (IE. QEDIT, Norton Editor, or
word processors which can edit unformatted ASCII files).



144  The Forbin Project, Inc.



The QMHOST.PWD file layout is as follows:


   Firstname  Lastname  Password  Security-Level  Callback-#  ;Comments


Each field is separated by one or more spaces, and comments must be preceded by
a semicolon.  The Callback Number is required only if you have selected the
CALLBACK system type.  Information in the Password File is
case-insensitive("JANE", "Jane", and "jane" are interpreted identically).

Following is a sample QMHOST.PWD file:


John   Friel    Password  1  1-319-233-6157  ; Moi
Joe    Blow     Qmodem    0                  ; another example
Jane   Doe      Smegma    0  555-1212        ; yet another


Records may be in any order (the SYSOP record need not be first).  In the
example above, the first and last entries have a CALLBACK number and will work
in a CALLBACK system, while the second entry will not.

Security Levels may be "1" or "0".  Level 1 users may shut down the system from
remote (as long as they know the password).  Other security levels are
unassigned and are reserved for future use.


Files created by the Host
Two files are created by the Host the first time it is invoked:

     QMHOST.HDR     The Message Header file.

     QMHOST.MSG     The Message Text File.

These two files may not be edited or modified in any way.  If they are,
unpredictable results will occur while messaging.  The message base can be
packed (killed messages are deleted) by running the QMHOSTPK.EXE program
supplied on the Utilities disk.  (Refer to the Message Section for more
information on QMHOSTPK.EXE)


Optional Files
Host Menu files can be customized to meet your needs.  The following default
menu files are supplied:

     PRELOG.HST     The opening screen sent to all callers

     MENU.HST       The Host Main Menu

     PROTS.HST      The protocol list for Up/Download commands

     LOGOFF.HST     The logoff screen sent to all callers


Menu Files are all standard ASCII files and can be edited with the Internal
Editor.



                                                              Qmodem SST     145



NOTE: Host Mode supports ANSI color/graphic menus, but these cannot be
      selectively disabled.  If you use ANSI menus, all callers must have
      ANSI emulation active to correctly view the screens.


Included on the Utilities Disk, are sample menu files for you to experiment
with.   These files all end with the extension .HST .


Logging on Locally
While Host Mode is active, you may press [F1] to log on locally.  This feature
can be used to test menu and Script operation. All Host commands, except Page
the Sysop are available locally.  Attempting to do an Upload or Download will
allow you to verify that the protocols are installed correctly, but no transfers
will actually take place.

When you are finished, you should use the G command to log off.

To exit Host Mode, press [ESC] while the system is waiting for a call.  You will
be returned to TERMINAL mode and the Modem Initialization string (Alt-N/M/M/I)
will be sent to the modem.


Starting the Host while ONLINE
The HOST can be invoked while you are on-line.  The other person you are
connected to will be prompted for logon information as if the host had answered
the incoming call itself.

CAUTION:If the caller is unsuccessful in his logon, the host will drop the
        connection and cycle.  There is no method to return to normal
        terminal without dropping the connection once the host is started.


Sysop Commands while the Host is active
When a caller is on-line, the SYSOP may break into chat mode by pressing [F2],
Dropping to DOS locally by pressing [F5] or disconnect the caller by pressing
[F10].  At all times, Host Mode will accept input from the remote caller as well
as from the local keyboard.   The SYSOP, for example, may come to the rescue of
a caller by typing commands directly.  These will be processed as if they had
been typed by the remote caller.

Uploads and Downloads may be cancelled by pressing [ESC] key.  It is not
considered nice to cancel a download on the 244th block of a 245-block file.


F2  Chatting with the Caller
Pressing [F2] initiates an on-line chat between the caller and the sysop:


(60 min. left) Qmodem Host Command >

You are now Chatting with the Sysop

(a conversation may go here...

Returning you to Host Mode




146  The Forbin Project, Inc.



Both caller and Sysop may type at will; the display will be identical on both
computers.  End-of-Line wordwrap is also active in CHAT mode.

To exit CHAT mode, the SYSOP must press [F2] again.  The message "Returning you
to Host Mode" will be displayed and the caller will be returned to the Main
Menu.


F5  Dropping to DOS
When you drop to DOS, the caller will see the following message:


Sysop has dropped to DOS.  Please wait...


You then get the DOS prompt just as if you had pressed Alt-R from Terminal Mode.
When you type [EXIT]  and return to the Host, the caller will see:


Ok, you can continue...


and the main menu will be displayed.


F10  Disconnecting the Caller
This is a drastic measure, but one you should know how to use.  If your system
is suddenly beseeched by a gang of  Adolescent Deformed Kung-fu Crickets with
modems, you will want to be sure they get the message...  Pressing [F10] gives
them:


NO CARRIER


That's right, nothing!  The modem is hung up without a message.
























                                                              Qmodem SST     147



Host Functions
Here is a sample MENU.HST file bundled with Qmodem:


      ²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²
      ²²²²²²²²²²²²²²²²ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»²²²²²²²²²²²²²²²²
      ²²²²²²²²²²²²²²²²º         Board Commands        º°°²²²²²²²²²²²²²²
      ²²²²²²²²²²²²²²²²ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼°°²²²²²²²²²²²²²²
      ²²²²²²²²²²²²²²²²²²°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°²²²²²²²²²²²²²²
      ²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²
      ²²²²²ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸²²²²ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸²²²²²²
      ²²²²²³  <R>ead Messages      ³°°²²³  <F>iles Directory    ³°°²²²²
      ²²²²²³  <E>nter a Message    ³°°²²³  <D>ownload File(s)   ³°°²²²²
      ²²²²²³  <P>age the Sysop     ³°°²²³  <U>pload Files(s)    ³°°²²²²
      ²²²²²ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾°°²²ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾°°²²²²
      ²²²²²²²°°°°°°°°°°°°°°°°°°°°°°°°°²²²²°°°°°°°°°°°°°°°°°°°°°°°°°²²²²
      ²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²
      ²²²²²²²²²²²²²²²²²²²²ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸²²²²²²²²²²²²²²²²²²²²
      ²²²²²²²²²²²²²²²²²²²²³  <O>pen a Script      ³°°²²²²²²²²²²²²²²²²²²
      ²²²²²²²²²²²²²²²²²²²²³  <S>hell to DOS       ³°°²²²²²²²²²²²²²²²²²²
      ²²²²²²²²²²²²²²²²²²²²³  <G>oodbye (HangUp)   ³°°²²²²²²²²²²²²²²²²²²
      ²²²²²²²²²²²²²²²²²²²²ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾°°²²²²²²²²²²²²²²²²²²
      ²²²²²²²²²²²²²²²²²²²²²²°°°°°°°°°°°°°°°°°°°°°°°°°²²²²²²²²²²²²²²²²²²
      ²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²²


Let's look at each command in the Host:

R  READ MESSAGES
The "R" Read command is used to read messages.  Unlike sophisticated On-line
Services or Bulletin Board Systems, the Qmodem Host mode does not keep track of
each caller's "Last Message Read".  It is up to callers to remember the number
of the last message he/she read.

If the caller presses [ENTER] at the "Start with Msg" prompt, the READ command
is cancelled and the Main Menu is displayed.

If the number entered is lower than the number of the first available message,
reading will start with the first available message.  Likewise, if the number
entered is higher than the highest message number, the last valid message will
be read.



















148  The Forbin Project, Inc.



Following is a sample message-reading session:


     Msg# : 1
       To : JOHN FRIEL (private) (not read)
     From : JOE BLOW
  Subject : Testing the Host
Date/Time : 08-14-1990 21:32:03
---------------------------------------
This is just a test, John

Hope you get it ok!

Joe

(R)eply, (K)ill, (Q)uit, [ENTER] next msg >


Message headers contain Message Number, To, From, Subject, and Date & Time
information.  Message marked (private) or (killed) can only be viewed by callers
with SYSOP Security or the caller that left the message.

After reading a message, the caller is prompted for one of the following
actions:

  1. (R)eply to the message just read.

  2. (K)ill    the message.  A message can be killed if it was addressed to the
     caller or the caller has SYSOP privileges.

  3. (Q)uit and return to the Main Menu.

  4. [ENTER] to read the next message.


E  ENTER A MESSAGE
The "E" command is used to enter  a new message.  The caller will be prompted
for the name of the recipient, an appropriate subject for the message, and the
security status of the message (private or public).

The actual message is then entered.  Messages may have up to 20 lines of 72
characters each.  As text reaches the end of the line, it automatically wraps to
the next line.

















                                                              Qmodem SST     149



Following is a sample message entry session:


(53 min. left) Qmodem Host Command > E

To: The Sysop
Subject: Testing the Message Base
Private (y/n) ? N

Enter your message.  72 chars per line, 16 lines max.  Autowrap
Blank line ends message.
---------------------------------------------------------------------------
This is a test of the emergency broadcasting system...

This is ONLY a test!

Beeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeeep!


(C)ontinue, (S)ave or (A)bort >


At the end of the message, the caller presses [ENTER] twice to terminate message
entry.  The Host will then display the "(C)ontinue, (S)ave or (A)bort >" prompt.

  (C)     Continue with message entry - The last line with text is displayed
     with the cursor following the last non-blank character.  Use this option if
     you exited the message and wish to add to it.

  (S)     Save the Message.  The message is saved and the user is returned to
     the Main Menu.  If the message was entered as a reply, the next message, if
     any, will be displayed.

  (A)     Abort the Message.  The message is deleted and the user is returned to
     the Main Menu.  If the message was entered as a reply, then the next
     message, if any, will be displayed.

The end-of-message prompt will also be issued automatically when the messages
reaches the 20-line maximum.


P  PAGE THE SYSOP
When someone Pages the Sysop, you and the caller will  hear one beep
approximately every second, and see the following:


Paging Sysop.   Press any key to abort...


As the beeps go off, another dot is added to the line.  After 20 or so seconds,
the caller is told that you are not answering the Page and gives him the Menu
again.  While he is paging you, the Status line tells you that pressing [F2]
will answer the Page.  Then, it is identical to the Chat mode described earlier.







150  The Forbin Project, Inc.



F  FILES DIRECTORY
The "F" command lists the contents of the Host Download Directory:


(55 min. left) Qmodem Host Command > F

--- FILE LIST ---
OVERLOK.ZIP       4856  13:03  04-27-90
TESTFILE             0  20:35  08-14-90
------ END ------

Press any key to continue


If the directory exceeds one page, the caller is prompted to continue between
them.  These are the only files that can be downloaded from the Host.

Exception to Rule :
IF the caller has Sysop privileges, AND the Alt-N/H/D Download Directory is left
BLANK, the caller can then Download ANY file from the Host system provided
he/she knows the EXACT drive:\path\filename.  The Files command does not prompt
for the directory to display.  It will always show the CURRENT directory under
these conditions.

It is assumed that in this case, the caller has his/her Host set up securely.


D  DOWNLOAD FILES
When D is selected, the alternate Protocol directory file PROTS.HST is searched
for and displayed.  If this file is not found, then the default list of
protocols is displayed.  Download procedures are the same as uploads.  Prior to
a download, the Host verifies the existence of the file to be sent.  If the file
does not exist, the Download is cancelled.

The Host fully supports the Batch transfer protocols.  If a batch protocol is
selected, the user is prompted for up to 20 filenames to be downloaded.  Each
filename can also contain the wildcard characters * and ?.  This allows for even
greater flexibility!


U  UPLOAD FILES
When the Upload command is selected, the Host first looks for the alternate
protocol menu file PROTS.HST.  If it is found, it is displayed.  If not, the
list of default protocols is displayed.

The caller can then select the desired protocol.  A filename prompt will be
displayed next for the file transfer.  During the transfer, the standard Qmodem
Download window will be displayed.

NOTE: The meanings of Uploads and Downloads are reversed while in Host Mode
      -- an Upload by the caller is a Download to the Host, and vice-versa -
      -.



O  OPEN A SCRIPT
The Open Script command allows Qmodem script execution while in Host Mode; it is
the Host equivalent of the Alt-F command.  When the "O" command is selected, the
QMHOST.SCR script is executed.

                                                              Qmodem SST     151




NOTE: When logging on locally with the [F1] command, the "O" command invokes
      the QMHOSTL.SCR script rather than the QMHOST.SCR script.  This allows
      you to test the script offline.  Since QMHOSTL.SCR script is executed
      while offline, it should not test for an on-line condition.


If the Host script is found, it begins executing immediately.  If the Script is
not found, the following message is displayed:


Sorry, that function is not available.


Following is a sample QMHOST.SCR:


FirstNamePrompt:
DISPLAY "Enter your First Name > "  ; ask for a first name

GETR 0 20                           ; put it in $0

IF $Offline Exit1                   ; if we are offline, then exit
IF "$0" <> "" LastNamePrompt        ; If so, go to the next prompt.

DISPLAYLN "Hey, I want your Last name!  Try again...^M^J"
GOTO FirstNamePrompt

LastNamePrompt:
DISPLAY "Enter your Last name  > "  ; ask for a last name

GETR 1 20                           ; put it in $1

IF $Offline Exit1                   ; are we offline? if so, exit
IF "$1" <> "" NextStep              ; if a name was entered, go to next label

DISPLAYLN "Hey, I want your Last name!  Try again...^M^J"
GOTO LastNamePrompt

NextStep:                           ; continue here
DISPLAYLN " "
DISPLAYLN "Thank you, $0"
DISPLAYLN "You will now be returned to the Host...
DISPLAYLN " "
DISPLAYLN "Please wait $0 $1"

Exit1:
EXIT                                ; exit back to the Host












152  The Forbin Project, Inc.



The QMHOSTL.SCR version of the script would be modified as follows:


FirstNamePrompt:
DISPLAY "Enter your First Name > "  ; ask for a first name

GET 0 20                            ; put it in $0

IF "$0" <> "" LastNamePrompt        ; If so, go to the next prompt.

DISPLAYLN "Hey, I want your Last name!  Try again...^M^J"
GOTO FirstNamePrompt

LastNamePrompt:
DISPLAY "Enter your Last name  > "  ; ask for a last name

GET 1 20                            ; put it in $1

IF "$1" <> "" NextStep              ; if a name was entered, go to next label

DISPLAYLN "Hey, I want your Last name!  Try again...^M^J"
GOTO LastNamePrompt

NextStep:                           ; continue here
DISPLAYLN " "
DISPLAYLN "Thank you, $0"
DISPLAYLN "You will now be returned to the Host...
DISPLAYLN " "
DISPLAYLN "Please wait $0 $1"

EXIT                                ; exit back to the Host


NOTE: The GETR command was changed to GET, and the $OFFLINE tests were
      removed completely.


TIP: The callers First and Last name is passed to the script variables $0
     and $1 respectively.  For more information on Qmodem Scripts, refer to
     the Script Language section later in this manual.


S  SHELL TO DOS
The "S" Shell to DOS command allows access to the DOS prompt while Host Mode is
active.  This command is the Host equivalent of the Alt-R command, and similar
rules and restrictions apply.  There is, however, one major difference between
the local DOS Shell available with the Alt-R command, and the Host Shell.  In
the case of a remote logon, DOS must receive its input from the serial port,
rather than from the keyboard.

If there is a user on-line, the Host Shell command executes the QMHOST.BAT batch
file.  If you are logging on as the local Sysop, the Shell command operates in
the same manner as the Alt-R command.







                                                              Qmodem SST     153



The Host passes 4 parameters to the QMHOST.BAT file as follows:

     %1   The current COM port number
     %2   The current Baud rate
     %3   The current Port Base Address (in HEX)
     %4   The IRQ for the current port (in HEX)

Refer to the README file located on Disk 1 for further instructions on the
QMHOST.BAT file.

The default QMHOST.BAT file can be set up use the DOS CTTY function to do the
remote Drop to DOS functions.  This is not as clean a solution as running
Doorway, but it does work in a pinch.  The file would then contains the
following lines:


     ECHO OFF
     CTTY COM%1:
     COMMAND
     CTTY CON:


There is one limitation to the CTTY method you should be made aware of.  DOS
CTTY only supports COM1 and COM2.  If you need to use COM3 - COM8, you need to
look at the DOORWAY program described on page 156.


G  GOODBYE (HANG-UP)
The Goodbye command allows a clean exit from the Host mode.  The modem is put
back on-hook and returns to "Waiting for call...".


?  HELP WITH HOST
The ? command will cause the Host to search for the file called HELP.HST and
display it if found.  This is a generic Help file that should tell the caller
what all the commands are and briefly what they do.  It should also mention that
more help is available by typing in a ? followed by the command in question.
This will display a file by the name of HELP[character].HST where [character] is
the command letter they want more help with.

These help files are ASCII text and can be edited by you to customize your Host.
A default set of help files is included on the Utilities Disk.

HELP.HST  Generic Help about the Host and should include a brief command
          summary.

HELPD.HST Download command.  You should edit to include specific instructions on
          external protocols if any are installed.

HELPE.HST Enter Message command.  Instructions on entering a message.

HELPF.HST File List command.  Tells the caller about your downloadable files.

HELPG.HST Goodbye command.  Need I say more?

HELPO.HST Open Script  command.  This should describe any script systems you
          install.



154  The Forbin Project, Inc.



HELP.P.HST     Page Sysop command.  You might want to tell them the hours you
          are around for being paged.  If you are never around, you might want
          to tell them to always leave a message.

HELPR.HST Read Message command.  Instructions on reading messages.

HELPS.HST Shell to DOS command.  Most likely, you will not be allowing your
          callers to do this.  On the outside chance someone will, this is the
          help for for them.

HELPU.HST Upload command.  You might want to tell them about the protocols you
          have installed.  Similar to the Download help file.

HELPZ.HST Shutdown Host command.  Again, your users should not be doing this,
          but you never know!


Z  SHUT DOWN HOST
The Shutdown command can only be entered by users that have a security level of
1.  In addition, they must also know the shutdown password (Alt-N/H/S).  When
the correct password is entered, the Host hangs up and returns to Terminal mode
in Qmodem.

The "Z" does not appear in the default menu for security reasons.  Out of sight,
out of mind.


Packing the Message Base
There is a program called QMHOSTPK.EXE included on the Utilities Disk that will
pack the Message base.  The term PACK refers to removing 'killed' messages.

You execute QMHOSTPK from the DOS prompt.  It assumes the message base files
QMHOST.MSG and QMHOST.HDR are in the current directory.

CAUTION:Should the message base become corrupted, the files QMHOST.HDR and
        QMHOST.MSG files should be deleted and let the host re-create them.
























                                                              Qmodem SST     155



DOORWAY
Also on the Utilities Disk, you will find a subdirectory called DOORWAY.  This
contains the Shareware program DOORWAY written by Marshall Dudley.

DOORWAY is unique in that it will allow you to Drop to DOS from Remote and run
virtually  any program from remote!  Programs like Quattro, the Turbo Pascal
compiler, and almost any other program the writes directly to video memory
(which IBM calls "dirty" programs).

All of the necessary DOORWAY files and documentation are included.  To get the
full benefit of DOORWAY, it must be registered in addition to Qmodem.  To make
this even more appealing, Mr. Dudley is offering a special price to Registered
Qmodem users and is reducing the price by $5.

To make DOORWAY operational, just copy the QMHOST.BAT file in the DOORWAY
subdirectory over the one in the root directory.



Alt-MINUS  Status Line Toggle
The Alt-Minus command toggles ON and OFF the Status Line at the bottom of the
screen.  This is for normal Termal mode only.  When running the Host Mode, a
Script, or most other Alt commands, the appropriate status line(s) will be
displayed.

When turned OFF, it does give you one additional line for use in some terminal
emulations, and especially usefull when using the Doorway mode (Alt-Equal).



Alt-EQUAL  DOORWAY Mode
Doorway mode allows you to send the entire PC Keyboard Scan Codes across the
line to the remote system.  The exception to this is the Alt-Equal key, which is
the toggle to get you in and out of Doorway mode.

This is most often used with the bundled program DOORWAY.  Refer to the DOORWAY
documentation (on the Utilities Disk/Subdirectory).



Alt-ENTER  Alternate Status Line Toggle
A little feature that a lotof you requested.  The status line can now be toggled
between the Qmodem standard with all the toggles and junk, to one that shows you
the Name and Number of the last dialed system.  Yes, it will show you who you
are connected to!

The only restriction is that the number must have been dialed from the dialing
directory, Alt-D.

NOTE: Alt-N/O/R/I Int16 Enable must be set ON for this to function.










156  The Forbin Project, Inc.



The Internal Editor
The Internal Editor is a RAM-based editor and similar to the Turbo Pascal &
SideKick editors.  If you are familiar with either of these, you should need
little help in using the Internal Editor (perhaps no more than a look at the
Quick Command Reference); novices should read on.


Entering and Editing Text
You enter text into the Internal Editor the same way you would on a regular
typewriter.  Most keys behave in the same manner; pressing ENTER terminates a
text line, for example.  But there are some important differences too.

The cursor always indicates where new text will be entered, and you can move the
cursor in a number of ways.  You can correct mistakes easily using the Delete
commands.  You can copy or move blocks of text with the Block commands.  You can
quickly search the file for a particular text string with the Find commands.
And, most of the time, you can "undo" a change with the Line Restore command.

Each command (and there are many more) is described briefly in the following
section.



Quick Reference
Function                   Keystroke(s)

Character left             Ctrl-S or Left arrow
Character right            Ctrl-D or Right arrow
Word left                  Ctrl-A or Ctrl-left arrow
Word right                 Ctrl-F or Ctrl-right arrow
Line up                    Ctrl-E or Up arrow
Line down                  Ctrl-X or Down arrow
Scroll up                  Ctrl-W
Scroll down                Ctrl-Z
Page up                    Ctrl-R or PgUp
Page down                  Ctrl-C or PgDn
Beginning of file          Ctrl-QR or Ctrl-PgUp
End of file                Ctrl-QC or Ctrl-PgDn
Beginning of line          Ctrl-QS or Home
End of line                Ctrl-QD or End
Top of screen              Ctrl-QE or Ctrl-Home
Bottom of screen           Ctrl-QX or Ctrl-End
Top of block               Ctrl-QB
Bottom of block            Ctrl-QK
Jump to marker 0..3        Ctrl-Q0..Ctrl-Q3
Set marker 0..3            Ctrl-K0..Ctrl-K3
Previous cursor position   Ctrl-QP
New line                   Ctrl-M or ENTER
Insert line                Ctrl-N
Insert control character   Ctrl-P
Tab                        Ctrl-I or Tab
Delete current character   Ctrl-G or Del
Delete character left      Ctrl-H or Backspace
Delete word                Ctrl-T
Delete to end of line      Ctrl-QY
Delete line                Ctrl-Y
Find                       Ctrl-QF
Find-and-replace           Ctrl-QA


                                                              Qmodem SST     157



Find next                  Ctrl-L
Begin block                Ctrl-KB or F7
End block                  Ctrl-KK or F8
Copy block                 Ctrl-KC
Move block                 Ctrl-KV
Delete block               Ctrl-KY
Hide block                 Ctrl-KH
Mark current word as block Ctrl-KT
Read block from file       Ctrl-KR
Write block to file        Ctrl-KW
Print block                Ctrl-KP
Toggle insert mode         Ctrl-V or Ins
Toggle Autoindent mode     Ctrl-QI
Toggle fixed tabs          Ctrl-or
Restore line               Ctrl-QL
Exit editor                Ctrl-KD or F10 or Esc


NOTE: When the notation Ctrl- precedes another key, it means that you hold
      down the Ctrl key and press the second key.  In the case of commands
      that have a second letter (for example Ctrl-QP), you hold down the
      Ctrl only while pressing the first letter, not the second.




The Editing Screen
The top line in the Edit Window is called the Edit Status Line and should not be
confused with the global Status Line at the bottom of the screen.  The Edit
Status Line is inside the window and the global is not.






























158  The Forbin Project, Inc.



The editor screen:


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Full Screen Edit ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³      Line 18   Col 61  Insert Indent     E:SAMPLE.DOC                        ³
³                                                                              ³
³                                                                              ³
³                                                                              ³
³                                                                              ³
³                  This text was entered                                       ³
³                  with auto-indent ON                                         ³
³                                                                              ³
³                                                                              ³
³The x's mark the tab stops with fixed tabs ON:                                ³
³        x       x       x       x       x       x       x       x       x     ³
³COl:    9       17      25      33      41      49      57      65      73    ³
³                                                                              ³
³                                                                              ³
³The x's mark the tab stops with 'smart tabs' ON:                              ³
³    x   x    x   x   x     x    x      x     x                                ³
³                                                                              ³
³                                                                              ³
³To enter a ^B into the the text, you press ^P and then ^B...                  ³
³                                                                              ³
³                                                                              ³
³                                                                              ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
°°°°°°°°°°°° F1-Help  F2-Save  F3-New  F9,ESC-Abort  F10-Save & Exit °°°°°°°°°°°


Command echo

  When the first key of a command assigned to two keystrokes is pressed, or
  when the Insert control character command (Ctrl-P, like the example) is
  given, the keystroke is echoed in the upper left corner of the window on the
  status line.  For example, if you start to enter a command that begins with
  Ctrl-K (such as Ctrl-KK),  a ^K will appear until the second keystroke is
  entered.


Line n

  Shows the number of the line containing the cursor, counted from the start of
  the file.


Col n

  Shows the column number containing the cursor.


Insert

  Indicates that Insert mode is in effect.  Everything you type will be
  inserted as opposed to possibly overwriting existing text.





                                                              Qmodem SST     159



Indent

  Indicates that Autoindent mode is in effect.  Ctrl-QI toggles autoindent on
  and off.


Tab

  Indicates that fixed tabs (toggled with Ctrl-or) are in effect.


E:SAMPLE.DOC

  The Drive, name and extension of the file being edited.  Although the editor
  accepts path designations, the path name will not appear in the status line.



Basic Movement Commands
The basic movement commands are those that move the cursor without altering the
text.  The cursor can be moved in one of two ways; with a key on the numeric
keypad or with a control character.  For example, to move the cursor to the
right once character, you can press either the Right Arrow or Ctrl-D.

In the following listings, the key sequence on the left is the primary key
sequence and the one on the right, if any, is the secondary key sequence.
Either can be modified by running the EDINSTAL program included on the Utilities
Disk.

NOTE: The online help for the Internal Editor will not reflect any changes
      you make to the key sequences.  Only the default installation is
      shown.



Character left   Ctrl-S or Left arrow

  Moves the cursor one character to the left.  This command does not work
  across line breaks; when the cursor reaches column 1; it stops.


Character right  Ctrl-D or Right Arrow

  Moves the cursor one character to the right.  This command does not work
  across line breaks; when the cursor reaches the right-hand edge of the text
  window, the text starts scrolling horizontally until it reaches the extreme
  right edge of the line (column 248), where it stops.


Word left        Ctrl-A or Ctrl-Left arrow

  Moves the cursor to the beginning of the word to the left.  This command
  works across line breaks.


Word right       Ctrl-F or Ctrl-Right arrow

  Moves the cursor to the beginning of the word to the right.  This command
  works across line breaks.

160  The Forbin Project, Inc.





Line up          Ctrl-E or Up arrow

  Moves the cursor to the line above.  If the cursor is on the top line of the
  window, the window scrolls down one line.


Line down        Ctrl-X or Down arrow

  Moves the cursor to the line below.  If the cursor is on the next-to-last
  line of the window, the window scrolls up one line.


Scroll up        Ctrl-W

  Scrolls up toward the beginning of the file, one line at a time.  The cursor
  remains on its line until it reaches the bottom of the window.


Scroll down      Ctrl-Z

  Scrolls down towards the end of the file, one line at a time.  The cursor
  remains on its line until it reaches the top of the window.


Page up          Ctrl-R or PgUp

  Moves the cursor one page up with an overlap of one line.


Page down        Ctrl-C or PgDn

  Moves the cursor one page down with an overlap of one line.


Beginning of fileCtrl-QR or Ctrl-PgUp

  Moves the cursor to the first character in the file.


End of file      Ctrl-QC or Ctrl-PgDn

  Moves the cursor to the last character in the file.


Beginning of lineCtrl-QS or Home

  Moves the cursor to column 1 on the current line.


End of line      Ctrl-QD or End

  Moves the cursor to the end of the current line (the position following the
  last non-blank character on the line).  Trailing blanks are always removed
  from all lines to preserve space.




                                                              Qmodem SST     161



Top of screen    Ctrl-QE or Ctrl-Home

  Moves the cursor to the top line of the text window.


Bottom of screen Ctrl-QX or Ctrl-End

  Moves the cursor to the bottom line of the text window.


Top of block     Ctrl-QB

  Moves the cursor to the position of the block-begin marker set with Ctrl-KB.
  This command works even if the block is hidden with the Ctrl-KH command or
  the block-end marker is not set.


Bottom of block  Ctrl-QK

  Moves the cursor to the position of the block-end marker set with the Ctrl-QK
  command.  The command works even if the block is hidden or the block-begin
  marker is not set.


Previous cursor position Ctrl-QP

  Moves the cursor to the last position.  This command is useful to move back
  to the previous position after a Save, a Find, or a Find-and-replace
  operation.  (or in case you hit the wrong direction key!)


Jump to marker 0..3 Ctrl-Q0..Ctrl-Q3

  Moves the cursor to one of the four invisible text markers created with the
  Set marker command.  Ctrl-Q0 jumps to marker 0, Ctrl-Q1 jumps to marker 1,
  and so on.  If the specified marker has not been set, the cursor is not
  moved.


Set marker 0..3  Ctrl-K0..Ctrl-K3

  Sets one of the four invisible text markers at the current cursor position.
  Ctrl-K0 sets marker 0, Ctrl-K1 sets marker 1, and so on.



Insert and Delete Commands
These commands let you insert and delete characters, words, and lines.  Two
related commands are covered in later sections: Restore line (Ctrl-QL) and
Delete block (Ctrl-KY).

New line         Ctrl-M or Enter

  In insert mode, this command inserts a line break at the cursor's current
  position.  If Autoindent mode is in effect, the cursor moves to the next line
  and to the same column as the first non-blank character in the previous line;
  otherwise, it moves to column 1 of the new line.



162  The Forbin Project, Inc.



  In overwrite mode, this command moves the cursor to column 1 of the next line
  without inserting a new line, whether Autoindent mode is in effect or not.


Insert line      Ctrl-N

  Inserts a line break at the cursor's position.  The cursor does not move.


Insert control character Ctrl-P

  Allows control characters to be entered into the text.  For example, pressing
  Ctrl-P and then Ctrl-C would insert a Ctrl-C (^C) into the text.  Control
  characters are displayed as capital letters in the same color as the Status
  Line.


Tab              Ctrl-I or Tab

  Moves the cursor to the next tab stop.  In Insert mode, any text to the right
  of the cursor is moved along with it; in Overtype mode, only the cursor is
  moved.  The location of the next tab stop depends on whether fixed tabs or
  smart tabs are in effect.


Delete current character Ctrl-G or Del

  Deletes the character over the cursor and moves any characters to the right
  of the cursor one position to the left.  This command does not work across
  line breaks.


Delete character left    Ctrl-H or Backspace

  Moves the cursor one character to the left and deletes the character
  positioned there.  Any characters to the right of the cursor are moved one
  position to the left.  If the cursor is in column 1 at the time the command
  is given, the invisible end-of-line marker for the previous line is deleted
  instead, and the two lines are joined.


Delete word      Ctrl-T

  Deletes the word to the right of the cursor.  This command works across line
  breaks and thus may be used to remove line breaks.


Delete to end of line    Ctrl-QY

  Deletes all text from the position of the cursor to the end of the line.


Delete line      Ctrl-Y

  Deletes the line containing the cursor and moves any lines below it up one
  line.  The cursor moves to column 1 of the next line.  You cannot restore a
  deleted line, so use this with caution.



                                                              Qmodem SST     163



Block Commands
A block is any arbitrarily defined, contiguous unit of text; a block can be as
small as a single character or as large as the entire file.  Mark a block by
placing a begin-block marker at the first character in the desired block and an
end-block marker just beyond the last character.  Once marked, the block can be
copied, moved, deleted, or written to a file.

Although marked blocks are normally highlighted, the block may be "hidden" (or
made invisible) with the Hide block command.  Many of the block-manipulation
commands described here work only when the block is being displayed.  The block-
related cursor movement commands (Ctrl-QB and Ctrl-QK, described in the "Basic
Movement Commands") work whether the block is hidden or displayed.


Begin block      Ctrl-KB or F7

  Marks the beginning of a block.  The marker itself is not visible on the
  screen, and the block becomes visible only when the end-block marker is set.
  You can also use the  begin-block marker as an extra text marker and jump
  directly to it with Ctrl-QB.


End block        Ctrl-KK or F8

  Marks the end of a block.  Like the begin-block marker, the end-block marker
  is invisible, and the block itself will not be displayed unless both markers
  are set.  You can also use the end-block marker as an extra text marker and
  jump directly to it with Ctrl-QK.


Copy block       Ctrl-KC

  Creates a copy of a marked and displayed block at the current cursor
  position.  The original block is left unchanged, and the markers are placed
  around the new copy of the block.


Move block       Ctrl-KV

  Moves a marked and displayed block from its current position to the cursor's
  position.  The markers remain around the block at its new position.


Delete block     Ctrl-KY

  Deletes a marked and displayed block.  There is no command to restore a
  deleted block, so use caution with this command.


Hide block       Ctrl-KH

  Toggles on and off the visual marking of a block.  Block manipulation
  commands work only when the block is being displayed.







164  The Forbin Project, Inc.



Mark single word Ctrl-KT

  Marks a single word as a block, combining the functions of the Begin-block
  and End-block commands.  If the cursor is positioned within a word, that word
  will be marked.  If it is not within a word, then the word to the left of the
  cursor will be marked.  And if there is no word to the right of the cursor,
  then the word to the left will be marked.


Read block from file     Ctrl-KR

  Reads a file into the text at the cursor's current position exactly as if it
  were copied from another part of the text.  The file read in is marked as a
  block.  When you use this command, you are prompted for the name of the file
  to read.  If you have used this command earlier in the editing session, the
  last file name entered will be displayed.  You may enter a new file name,
  make minor changes to the one displayed using the Backspace key, or accept it
  by pressing ENTER.  The file specified may be any legal file name, including
  a drive and/or path identifier.  Cancel the command by pressing Ctrl-U.


Write block to file Ctrl-KW

  Writes the currently marked block to a file.  The block is left unchanged,
  and the block markers remain in place.  You are first prompted for a
  filename.  The file specified can be any legal file name, including a drive
  and/or path identifier.  You should avoid using file names with the extension
  .BAK, because this extension is used by the Internal Editor when creating
  backup files.  If the file specified already exists, you are asked if you
  want to overwrite it.  If you press "N" (for NO), you can enter a new file
  name, make minor changes, or cancel the command with the Ctrl-U command.  If
  no block is marked, this command is ignored.


Print            Ctrl-KP

  Prints the currently marked and displayed block on the default printer.  If
  no block is marked or the block is hidden, the entire file is printed.



Miscellaneous Commands
This section describes a number of commands that do not fall into any previous
category.

Toggle insert mode  Ctrl-V or Ins

  Selects Insert or Overwrite mode.  In Insert mode, text to the right of the
  cursor is moved to the right as new text is entered.  In Overwrite mode, any
  text to the right of the cursor is overwritten when new text is entered.


Toggle autoindentCtrl-QI

  When Autoindent mode is in effect, the New line command (Enter or Ctrl-M)
  will move the cursor to the next row and to the same column as the first non-
  blank character on the previous line.



                                                              Qmodem SST     165



Toggle fixed tabsCtrl-OT

  When fixed tabs are in effect, the tab stops (normally) start at column 9 and
  occur every 8 columns thereafter.  By default, fixed tabs are off, and smart
  tabs are on.  When smart tabs are in use, the tab stops are determined by the
  locations of the words on the previous line; the first character in each word
  represents a tab stop..  When fixed tabs are used, the Tab command inserts a
  single tab character at the cursor's position.  When smart tabs are used, the
  tab is stored as a series of blanks.


Restore line     Ctrl-QL

  Undoes any changes made to a line of text as long as you have not left the
  line.  The line is restored to its previous contents regardless of the
  changes made.  Since the Delete line command (Ctrl-Y) moves the cursor to
  what was previously another line, Restore line cannot recover lines deleted
  with it.


Find             Ctrl-QF

  Lets you search for a string of up to 30 characters.  When you enter this
  command, the status line is cleared and you will be asked for a search
  string.  The last search string entered (if any) will be displayed.  You can
  select it again by pressing Enter, edit it, or enter a new string.  When
  editing strings, Backspace deletes the previous character, Ctrl-R restores
  the previous string, Ctrl-S moves the cursor to the left, and Ctrl-D shows
  the next character to the right.  Esc or Ctrl-U will cancel a search command,
  and Ctrl-P can be used to enter control characters.

  After the search string is entered, you must specify your search options.
  The options you used last, if any, are displayed.  Editing works the same as
  the search string edit.  The following options are available:

  B  Searches backwards from the current cursor position toward the beginning of
     the file.

  L  Limits searches to the currently marked block.

  n  n may be any number.  Find the nth occurrence of the search string, counted
     from the current cursor position.

  U  Ignore case; treats all alphabetic characters as if they were uppercase.

  W  Searches for whole words only; skips matching patterns embedded in other
     words.

  If the text contains a target matching the search string, the cursor is
  positioned at the end of the target.










166  The Forbin Project, Inc.



Find and replace Ctrl-QA

  This operation works the same as the Find command, except that you can
  replace the "found" string with any other string of up to 30 characters.
  After entering the search string, you are asked to enter the replacement
  string.  The last replacement string, if any, will be displayed; you can
  accept it, edit it, or enter a new string.

  Finally, you are prompted for options.  The options you used last are
  displayed at first.  You can enter new options (cancelling the old ones),
  edit the current options, or select the same options by pressing Enter.  The
  options are the same as those for the Find command with the following
  exceptions:

  G  Searches globally.  The entire file is scanned for the search string,
     regardless of the current position of the cursor.  The search starts at the
     beginning of the file if searching forward; at the end if searching
     backwards.

  N  Replaces without asking.  Does not prompt for confirmation at each
     occurrence of the search string.

  If the text contains a target matching the search string, the cursor is
  positioned at the end of the target.  You are then asked if you wish to
  replace it.  Press "Y" to replace it, or "N" to ignore it.  You can abort the
  operation by pressing Ctrl-U.  If you selected the N (no prompting) option,
  this question will not be asked.

  You can speed up global search-and-replace operations by selecting the N
  option and then pressing a key (preferably for a nonprinting character, such
  as ESC or Ins).  The screen is then no longer updated when each replacement
  is made.


Find next        Ctrl-L

  Repeats the last search operation.  If the last search command called for a
  Find operation, the same search string and options will be repeated; for a
  Find-and-replace operation, the replacement string will be reused as well.

  Saves the file being edited and exits from the editor.  The original file, if
  any, is renamed to FILENAME.BAK.



EDINSTAL - Keyboard Installation Program
You can use the EDINSTAL program (on the Utilities Disk) to customize the
Internal Editor.  You can redefine the keystrokes (both primary and secondary)
used to invoke the predefined commands.  For example, the Toggle fixed tabs
command is by default assigned to Ctrl-OT using EDINSTAL, you could assign this
command to Shift-Tab.









                                                              Qmodem SST     167



Running EDINSTAL
Load EDINSTAL by typing EDINSTAL at the DOS command line.  The QMODEM.EXE file
must be in the current directory for this to run.  If it is, you will be asked


     Perform fast entry for fully reconfigured keyboard?


If you press "Y" for yes, you can install the keyboard using the fast-entry
method.  The default response, No, can be given by pressing "N" or Enter.  If
you answer No, the keyboard will be installed using the random access method.


Fast Entry
When you select the fast-entry option, you will see the following instructions:


   Press <Enter> to accept default
   Press keys followed by <Enter> for new key sequence
   Press <Bksp> to back up one keystroke, C to clear, R to restore
   Press <Scroll Lock> to toggle literal mode
   Press <Escape> to quit entering commands
   Random access editing is available when you are finished


You can then either enter a new key sequence for each command or accept the
current one by pressing Enter.  Both the command name and the current key
sequence are always displayed to the left of the cursor.  You specify a new key
sequence by pressing the keys you wish to use to invoke that command.  Pressing
Enter terminates your entry.

You can correct mistakes in the current entry by pressing the Backspace key
(delete last keystroke), C (Clear entry), or R (Restore previous entry).  To
specify either the Enter key or a Ctrl-M, you must first press the Scroll Lock
key, which indicates that keystrokes are to be interpreted literally; press it
again when you've finished entering the key sequence.  Pressing Esc stops the
fast-entry procedure and takes you to the random access entry screen.


Random Access
When you select the random access option or when you have finished using the
fast-entry procedure, you can alter any or all of the default key sequences.
The top line of the screen will give you some basic instructions.  The remainder
of the screen shows (from left to right) the name of the command, the primary
key sequence, and the secondary key sequence (if any).

Move the cursor to the key sequence you want to change and press Enter.  Use the
Left arrow and Right arrow keys to select the primary or secondary key
sequences, and scroll through the list of commands using the Up arrow, Down
arrow, PgUp, and PgDn keys.  Home takes you to the first command, and End to the
last.

You can correct mistakes the same way as the fast-entry edit.







168  The Forbin Project, Inc.



Quitting the Program
When you have finished making changes, press "Q" to quit or "W" to write your
changes to the QMODEM.EXE file.  If you choose the Write option, you will then
see the message "Checking for conflicts..."  If you have accidentally assigned
the same key sequence to two different commands, an error message will be
displayed.  You can correct your mistakes by searching for the highlighted
items.

You will also see an error message if the new list of keystrokes is too large
for the area set aside for it.  You can easily solve this problem by eliminating
a few secondary key sequences.

















































                                                              Qmodem SST     169



The Qmodem Script Language
What is a script?
A script is a Qmodem program, designed to perform specific and/or repetitive
functions much faster and more reliably than with manual methods.  Scripts can
be used to do just about anything that can be done at the keyboard; your
imagination is the only limit.  Common uses for scripts include:

  o  Automated logon
  o  File transfers
  o  Completely automated sessions
  o  Unattended Qmodem operations

The QuickLearn Script Recorder is an extremely convenient facility, but it has
its limitations.  Basically, QuickLearn can only record your interactions with a
remote computer and replicate them exactly.  It cannot add decision-making logic
to the scripts it creates, or account for unexpected or changing conditions.
When you run out of QuickLearn power, time has come to write or edit your own
scripts.

Scripts are similar to interpreted BASIC programs.  The syntax is somewhat
different, but the principles are almost identical.  The Qmodem Script
Interpreter (also referred to as the Script Parser) reads the script's code and
executes the instructions as it reads them.

Scripts can be very simple or extremely involved.  Logon scripts created by
QuickLearn are simple.  Some large and complex scripts have also been written to
turn Qmodem into a mini-Bulletin Board System.  With the advent of BBS Networks
such as InterLink, scripts have been written to automatically dial a BBS, log
on, open a mail transfer door, download a mail packet, and log off.  Many useful
Qmodem scripts are included on the Qmodem Utilities disk.  Many other scripts
can be found on bulletin boards, including the Forbin Project, Home of Qmodem.

You need not be a programmer to write scripts, but if you aren't, we recommend
that you start at the beginning until you have a good understanding of script
concepts, syntax rules, and common script commands.

As with all programming languages, The Qmodem script language has a few
idiosyncracies.  Here are some of the most obvious.


Physical vs. Logical Screen
The physical screen is the entire screen, which usually consists of 80 columns
and 25 lines (or more if you have an EGA or VGA and use one of the extended
display modes).

Smaller, logical screens can be defined with the script BOX or WINDOW commands.
All screen output commands except ATWRITE are limited to the logical screen
boundaries defined in the last BOX or WINDOW commands.


Input and Output Commands
The script language has a wealth of input and output commands, each with a
specific purpose.  For example, there are six commands available to read input
from the keyboard and/or COM port (GET, GETN, GETR, GETNR, GETX, and INKEY), and
seven commands available to display data on the screen and/or send it to the COM
port (ATWRITE, SEND, DISPLAY, DISPLAYLN, NOTE, WRITE, and WRITELN).  In
addition, the WHEN command can also be used to send data to the COM port when
specific COM input is received.


170  The Forbin Project, Inc.





Variable Handling
Variables used in scripts do not have explicitly declared types such as INTEGER
or STRING.  The string "100", for example, could be used as a numeric variable
as well as a text variable.  It is your responsibility to insure that the
variable contents are numeric when they need to be.

When a variable name is prefixed with a dollar sign, the Script Interpreter will
automatically substitute its value in the command.  When a value is assigned to
a string, the dollar sign is omitted.  It is important to understand this
concept to put it to good use.

Regardless of their contents, script variables cannot exceed 64 characters.


Running Scripts
Scripts may be invoked explicitly with the Alt-F command.  They may also be run
automatically by specifying a script name on the Qmodem command line, or if the
script name is defined in a directory entry (Linked Scripts), in which case the
script will start executing when the connection is made.


Script Commands
The Qmodem script language is very comprehensive.  Almost all terminal mode
manual commands are available as script commands (and then some).  Since
equivalent script commands perform the same functions as their manual
counterpart, we also recommend that you familiarize yourself with the manual
commands first; its documentation more thorough and we did not see the need to
duplicate it for the script command.  Commands that are unique to the script
environment are covered in detail, however.


Script Language
The script language is a programming language, and script files are special
Qmodem programs intended to perform specific functions.  If you are not a
programmer, do not let this intimidate you.  The script language is easy to
learn, and scripts are easy to read and modify.  Error messages are clear and
concise.  The built-in debugger and Qmodem Editor will help you along as you
develop your scripts, in the unlikely event you make a mistake.

Scripts can be very flexible.  They can be used in many ways that aren't
described here.  Scripts fall into one of four categories:

  1. Linked scripts, These scripts are physically named in entries in the Qmodem
     Phone Directory.  When connection is made, the script is executed
     automatically.  The same script can be linked to multiple entries.  These
     scripts are often referred to as "Logon Scripts", because they take control
     immediately after a connect and usually automate boring and repetitive
     logon processes.

     Examples:

     There are two local Tymnet phone numbers in your phone directory.  The
     script SOURCE-U.LOG can be linked to both numbers to automate the logon to
     The Source.




                                                            Qmodem SST       171



     A BBS system has three nodes with different phone numbers.  A single script
     like PCBOARD.LOG can be linked to all three numbers.


  2. Scripts started with the Alt-F command, which require execution-time
     parameters.  Qmodem allows up to ten variable parameters to be passed to a
     script.

  3. Scripts linked to Function Keys.  Because they are stored in a Function Key
     Macro, you do not have to re-enter the parameters each time you run the
     Script.

  4. Stand-alone Scripts, requiring no parameters.  These scripts can be
     executed automatically when Qmodem is started, by specifying their name in
     a command-line parameter.

     Example:

     To execute the script DOFIRST.SCR when starting Qmodem, use the command:


          C>QMODEM /S=DOFIRST.SCR<cr>


     Once initialization is complete, Qmodem  will load and execute the script
     whose name was specified in the /S= command-line parameter.  This command
     line could be contained in a BATCH file to automate the process even
     further.


How to Create and Name a Script
Any standard ASCII text editor or word processor can be used to create a script
file.  You may save scripts under any file name and extension, but using the
".SCR" file extension makes life much easier, as we'll see later.

The easiest way to write a script is to let Qmodem do it for you!  Refer to the
Alt-Q (QuickLearn) command for complete details.  But, if you insist on doing it
yourself with your favorite Word processor or Editor, remember these tips:

  1. Scripts must be saved as standard, CR/LF-delimited ASCII files.  Non-ASCII
     files like those produced by Wordstar Document mode won't work (for
     Wordstar, use N at the opening prompt to create scripts in the Non-Document
     mode).

  2. Each Script command must be on a separate line in the file.

TIP: We recommend the Internal Editor for creating and editing scripts.
     Refer to the Alt-V and Alt-J/@EDIT commands for information.



Starting a Script
There are 3 ways to start a Script:

  1. The command line switch /S= to "auto start" a script.  Refer to the Command
     Line Switches for a description.

  2. The explicit Alt-F command to call a script;.


172  The Forbin Project, Inc.



  3. Automatic execution of a Linked-Script attached to a Phone Directory entry.
     (See Alt-D for instructions on attaching a script to a dialing directory
     entry)


Stopping a Script
You can stop a script at any time by pressing the [ESC] key.  The Status line
will change to the following:


°°°°°°°°°°°°°°°°°°° S-Single Step   T-Trace   G-Go   A-Abort °°°°°°°°°°°°°°°°°°°


To cancel the script, press "A".  Pressing "G" resumes script execution at the
point where it was interrupted.  The "S" and "T" commands are used to start
Script Debug Mode (more on this later).


Debugging a Script
Qmodem includes a powerful script debugger, complete with single-step and
trace/animate features.  In addition, if a script fails, the Qmodem Internal
Editor can be automatically invoked with the cursor positioned at the exact
point where the error was detected.

Following is a simple script example to illustrate the debugger's operation:


;
; Script example
;
DISPLAYLN "this is the value of variable COUNTER : $COUNTER "
EXIT


The fourth line in the script refers to a variable called $COUNTER.  This
variable was not defined, and an error will result.  Executing the script will
cause the following window to be displayed:


  ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Script Error! ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
  ³Type : Invalid Substitute VARIABLE                                       ³
  ³File : Z:\SCRIPTS\TEST1.SCR                                              ³
  ³Line : DISPLAYLN "this is the variable COUNTER : $COUNTER "              ³
  ³Press any key to Edit file                                               ³
  ³                                                                         ³
  ³                                                                         ³
  ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾



°°°°°°°°°°°°° Script file "TEST1.SCR" at level  1.  [ESC] to ABORT °°°°°°°°°°°°°


The first line describes the error (explained in detail in the next section).
In this case,  we have used an invalid variable.

The second line shows the fully qualified script filename.



                                                            Qmodem SST       173



The third line is the actual script line in which the error occurred.

The bottom line displays an edit prompt.  Assuming that we are using the
internal editor, pressing a key yields the following display:


ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Full Screen Edit ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
³      Line 1    Col 43  Insert Indent     Z:TEST1.SCR                         ³
³DISPLAYLN "this is the variable COUNTER : $COUNTER "                          ³
³EXIT                                                                          ³
³                                                                              ³
³                                                                              ³
³                                                                              ³
³                                                                              ³
³                                                                              ³
ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
°°°°°°°°°°°° F1-Help  F2-Save  F3-New  F9,ESC-Abort  F10-Save & Exit °°°°°°°°°°°


When using the Qmodem Internal Editor, the cursor will be positioned under the $
in $COUNTER, which is the offending variable name.

Two additional error conditions yield different Script Error windows:


  ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Script Error! ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
  ³Type : LABEL not found                                                   ³
  ³       TIMEOUT LABEL    = WHOOPS                                         ³
  ³File : Z:\SCRIPTS\TEST1.SCR                                              ³
  ³Line : Waitfor "ever"                                                    ³
  ³Press any key to Edit file                                               ³
  ³                                                                         ³
  ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾

- or -

  ÕÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Script Error! ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¸
  ³Type : LABEL not found                                                   ³
  ³       GOTO/GOSUB LABEL = WHOOPS                                         ³
  ³File : Z:\SCRIPTS\TEST1.SCR                                              ³
  ³Line : goto Whoops                                                       ³
  ³Press any key to Edit file                                               ³
  ³                                                                         ³
  ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾


In both examples, identifying labels were not found in the script.

So far, we have seen the automated debugger at work.  An error occurs, and you
are immediately notified of it.  Qmodem also features an Interactive Debugging
mode, in which you are in control.  To start the interactive debugger, the
DEBUG ON command is used.








174  The Forbin Project, Inc.



Following is an example of interactive debugging:


;
; Script example
;

DEBUG ON                ; turn on the debugger

STRING ONE TWO THREE    ; define 3 new variables
ASSIGN ONE   "1"        ; give them numeric values
ASSIGN TWO   "2"
ASSIGN THREE "3"
DISPLAYLN " ONE = $ONE, TWO = $TWO, and THREE = $THREE"
EXIT


When the script is executed, the status line will change to:


 DEBUG << >>


In interactive debug mode, the next script line to be executed is displayed
between the << >> characters.  To execute the statement, press the Spacebar.  In
the example, the first line following  the DEBUG command is blank, and no text
appears between the << >>.

Pressing the Spacebar yields the following series of DEBUG status displays:


 DEBUG <<STRING ONE TWO THREE >>

 DEBUG <<ASSIGN ONE   "1" >>

 DEBUG <<ASSIGN TWO   "2" >>

 DEBUG <<ASSIGN THREE "3" >>

 DEBUG <<DISPLAYLN " ONE = $ONE, TWO = $TWO, and THREE = $THREE" >>


A number of useful debug commands are available while single-stepping through a
script.  Pressing the F1 key displays a summary of these commands on the status
line:


[SPACE] Next  [T] Trace  [G] Go  [S] Subst. Line  [O] Orig. Line  [U] Under


After the command summary line has been displayed for approximately 2 seconds,
the status line  reverts back to the standard DEBUG display.








                                                            Qmodem SST       175



Interactive Debug commands include:

  [SPACE] Next

     Pressing the Spacebar executes the line displayed between the << >>
     characters.


  [T] Trace

     Pressing "T" starts executing the script at the rate of 2 lines per second
     (Animate Mode).

  [G] Go

     Pressing "G" terminates interactive debug mode and resumes script executing
     with the next line.  The script will execute until it ends normally, an
     error occurs, or another DEBUG ON command is found.

  [S] Subst. Line

     Pressing "S" displays (substitutes) the values of all variables in the
     current script  line prior to execution.

  [O] Orig. Line

     Pressing "O" terminates variable substitution and re-displays current line
     in its Original form.

  [U] Under

     Pressing "U" temporarily suspends display of the Debug status line when
     running the script in full-screen mode and the normal status line itself is
     disabled (Alt-N/V/T/T OFF).


Going back to our script example, pressing "S" yields the following display:


 DEBUG <<DISPLAYLN " ONE = 1, TWO = 2, and THREE = 3" >>


pressing [Spacebar] again...


 DEBUG <<EXIT >>


pressing [Spacebar] again...

Returns us to the normal status line following the end of the script.









176  The Forbin Project, Inc.



Special Characters in Scripts
In scripts, the caret (^) is used as a modifier when combined with certain other
characters:

  ^~ A caret-tilde (~) combination generates a 1/2 second delay.

  ^^ A double-caret sequence yields a single-caret character.


To insert control characters in your scripts, prefix the letter with the  ^
(caret).

Following is a list of valid control characters and the corresponding caret
combinations:

     DecHex Ctrl         DecHex Ctrl
     ------ ----         ------ ----
     0  00  ^@           16 10  ^P
     1  01  ^A           17 11  ^Q
     2  02  ^B           18 12  ^R
     3  03  ^C           19 13  ^S
     4  04  ^D           20 14  ^T
     5  05  ^E           21 15  ^U
     6  06  ^F           22 16  ^V
     7  07  ^G           23 17  ^W
     8  08  ^H           24 18  ^X
     9  09  ^I           25 19  ^Y
     10 0A  ^J           26 1A  ^Z
     11 0B  ^K           27 1B  ^[
     12 0C  ^L           28 1C  ^\
     13 0D  ^M           29 1D  ^]
     14 0E  ^N           31 1F  ^_
     15 0F  ^O

TIP: Control characters are case-insensitive:  ^C is the same as a ^c.


NOTE: To generate the double-caret ^^  character in the internal editor,
      first type ^P, then type ^^.  The editor will display a "^" in the
      same colors as the header line rather then normal text colors.  This
      is normal and is used to represent an imbedded Ctrl character.

Comments may be added to scripts, and must be preceded by a semi-colon (;):


; A semicolon as the first character is always a comment

WAITFOR "Enter your password :"  ; This is a comment
SEND    "$Password^M"            ; another comment line
PASSWORD1:                       ; a comment after a label


Comments are not displayed during script execution.

TIP: Make it a habit to add comments to your scripts wherever and whenever
     possible. Comments are an invaluable help when debugging or making
     changes to scripts, especially older, long-forgotten ones.



                                                            Qmodem SST       177




Definitions and Parameters
Script statements usually consist of an operation code and one or more operands
or parameters.  Parameters shown in brackets [] are optional.  Parameters in
quotes (" " or ' ') are mandatory.

For example:


DIAL  "1"
DIAL  'TSAlt-Air'


Single- and double-quote characters should not be mixed except in special cases.
For example, to send the following message:


John said, "Qmodem is the BEST!"


you would code the following:


SEND 'John said, "Qmodem is the BEST!"'


Single- and double-quote characters are interchangeable, but must be used in
matched pairs.  As shown above, use of one set of quote characters allows you to
include the other as part of a text string.  To send the following string:


John's password is QMODEM


the script code would be:


SEND "John's password is QMODEM"



Labels
Labels define the targets of EXIST, GOTO, GOSUB, IF and WHEN commands.  All
labels must end with a colon.  Below are some examples of valid script labels:


EXIT_LABEL:
A:
A_LONG_LABEL:
A_much_longer_label_than_the_others:


Labels must appear on a line by themselves.  Comments are the only other
statements allowed on label lines.






178  The Forbin Project, Inc.



Pre-defined String Variables
The variables $0 through $9 are pre-defined and may be used anywhere in place of
user-defined string variable.  In addition, variables $0-$9 must be used if data
is to be passed to the script in the form of parameters in the Alt-F command or
F-key macros.

String variables may not exceed 64 characters in length.  The variables $0-$9
can be set with the ASSIGN, GET, GETR, GETN, GETNR and GETX commands.  For
example, the statement:


ASSIGN 0 "This is a test"


store the text string:

This is a test

into variable $0.

Since string variables are replaced with their actual values before script
commands are executed, the leading $ is omitted when one of the pre-defined
string variables is the first operand in an ASSIGN statement.   The following
examples further illustrate this principle:


ASSIGN; 0 "Qmodem is the Best!"   ;$0 becomes the quoted string
ASSIGN 1 $0                      ;$1 is set to $0

And the statement:

SEND "$1"                   ;the string $1 is sent


would send the following string to the modem:


Qmodem is the Best!


Script commands can actually be stored into string Variables with an ASSIGN
command, and used later in the script.  For example:


ASSIGN 0 "WAITFOR "   ;$0 = WAITFOR[space]
$0 "Password "


would be interpreted as:


WAITFOR "Password "








                                                            Qmodem SST       179



If a dollar sign ($) is required as part of a text string, that character must
be duplicated.  For example:


SEND "This is a dollar sign : $$"


will send the following:


This is a dollar sign : $


String variables are very powerful tools indeed!  With their flexible text and
command substitution features, what can be done with them is only limited by
your own imagination.

The next section of the manual describes Qmodem's script commands in detail.
Commands are listed in alphabetical order, and appropriate coding examples are
included for each command.


System Variables
Most of Qmodem's environment and operating parameters are stored in pre-defined,
read-only variables which are available during script execution.

NOTE: Pre-defined variables may not be the target of ASSIGN, GET or INKEY
      commands.



$DATE

The $DATE variable contains the current system date, based on the   internal
clock.  The date is returned as defined in Alt-N/O/C/D Date Mask.


$TIME

The $TIME variable is similar to the $DATE variable.  The time is returned in
the format as defined in the Alt-N/O/C/T Time Mask.


$LAST_ROW

The $LAST_ROW variable contains the number of the last line on the screen,  not
including the Status Line.   For example, on an 80x25 screen, this variable
contains the value 24.


$LAST_COL

The $LAST_COL variable contains the physical screen width, in columns.  On a
25x80 screen, this variable contains the value 80.






180  The Forbin Project, Inc.



$ATTR

The $ATTR variable contains the screen's current Color Attribute.  In a script
which changes the screen color, this value may be saved at the beginning of the
script, and restored before the script terminates to re-establish the normal
default screen color.


$DLPATH

This contains the Download Path as specified in the Alt-N/D/D Setup variable.
You could use this to point to the download directory when using the DOWNLOAD
script command.


$ULPATH

This contains the Upload Path as specified in the Alt-N/D/U Setup variable.  It
could be used in combination with the UPLOAD script command.


$SCPATH

This is the Script Directory Path as specified by the Alt-N/D/S Setup variable.
All temporary scripts should be stored in this directory.


Connect Information Variables
Qmodem stores information relating to the last successful connection (or the
current one, if ONLINE) in a series of variables.  For information to be valid,
the connection must have been established through a standard DIAL command or a
linked script.


$BOARD

The $BOARD variable contains the name field of the directory entry to which
Qmodem was last successfully connected.  This is a variable-length string which
does not exceed 34 characters.

If you use the default Qmodem Phone Directory, the commands:


DIAL "1"                    ;dial the first phone book entry
NOTE Connected to $BOARD!   ;display a connect msg


will display:


Connected to The Forbin Project PCBoard!



$NUMBER

The $NUMBER variable contains the phone number of the last connected entry, as
shown in the dialing directory.


                                                            Qmodem SST       181




Using the same example:


NOTE Connected to $BOARD at $NUMBER.


will display:


Connected to The Forbin Project PCBoard at 1-319-233-6157.



$PASSWORD

The $PASSWORD variable contains the password field for the last connected entry,
as stored in the dialing directory.  $PASSWORD can be used  in a generic logon
(linked) script for BBSs running the same software.  The following example will
operate with PCBoard systems:


NOTE Connected to $BOARD   ;display after connection
WAITFOR "Graphics"         ;wait for first prompt
SEND    "N^M"              ;send a "N[ENTER]"
WAITFOR "First name"       ;wait for the name prompt
SEND    "FIRST;LAST^M"     ;send your name
WAITFOR "Password"         ;wait for password prompt
SEND    "$PASSWORD^M"      ;send the linked password



$SCRIPT

The $SCRIPT variable contains the name of the linked script for the connected
entry, as stored in the dialing directory.  Using the above example, we could
add another line as follows:


NOTE This is script $SCRIPT


which would display:


This is script PCBOARD.SCR



$PROTOCOL

The $PROTOCOL variable contains the default file transfer protocol  assigned to
the connected entry.  It is used in SEND strings or script DOWNLOAD commands, as
illustrated in the following example, which sends a file download request to a
PCBoard BBS, waits for the start-of-transfer prompt, and starts the actual
download:




182  The Forbin Project, Inc.




  SEND     "D $PROTOCOL FILENAME.ARC^M"
  WAITFOR  "[ctrl-X] to abort"
  DOWNLOAD $PROTOCOL FILENAME.ARC



$SPEED

The $SPEED variable contains the current serial rate (i.e.., 300, 1200, 2400,
9600 etc...).  The serial baud rate is set by the by the redialer before each
number is dialed.  If you are connected at 2400, the following command:


NOTE Connected at $SPEED this time


will display:


Connected at 2400 this time


NOTE: The baud rate may not be reset, depending on the state of the "Lock
      DTE Baud Rate" toggle in the Alt-N/M/T Setup menu.



$COM

The $COM variable contains the remainder of the communication parameters, in the
form of Databits-Parity-Stopbits.  If your current settings are No parity, 8
data bits, and one stop bit, and your serial rate is 2400, the command:


NOTE Connected at $SPEED-$COM


will display:


Connected at 2400-8-N-1


$NOTEFILE

This is the full DOS filename for the Attached Note file.  Each entry has a
unique Note file that can store information.  Using this variable in combination
with the text IO Script commands (OPENFILE, READFILE, CLOSEFILE), you can store
remote computer specific information and load it every time you call that
system.









                                                            Qmodem SST       183



Example Script SHOWNOTE.SCR:


EXIST $NOTEFILE CONT           ;see if it exists
DISPLAYLN "No attached notes"  ;nope, say so
RETURN                         ;exit back to logon script
CONT:
DISPLAYLN "Contents of attached Note file:"
DISPLAYLN "-------------------------------"
OPENFILE $NOTEFILE READ        ;open the note file
READLOOP:
   READFILE 0                  ;read
   IF "$0" = "_EOF_" DONE      ;if end-of-file, jump to DONE
   DISPLAYLN "$0"              ;display the line
   GOTO READLOOP               ;go back and read some more
DONE:
CLOSEFILE                      ;close the note file
RETURN                         ;return back to the logon script


This script simply opens the attached Note file and displays the contents.  To
activate it, just use the SCRIPT command to call this as a subroutine:


;
;  QuickLearn Script generated at 02:35:18 on 08-22-88
;  May require editing before use.
;

NOTE Attached Note File is : $NOTEFILE  ;if you're curious
SCRIPT SHOWNOTE.SCR                     ;now show it

;rest of the auto-logon script




Script Commands
General Coding Information
Script commands usually consist of an Operation Code, often referred to as
OpCode, and one or more Operands, also referred to as arguments, targets, or
parameters.  Opcode and operands are separated with spaces.  In certain cases, a
relational operator may separate parameters.  For example, the script IF command
has two operands separated by a relational operator:


IF "$0" = "$1" ROUTINE


IF is the OpCode, "$1", "$2" and ROUTINE are the operands, and = is the
relational operator.  In the example, the command compares the contents of
variables 0 and 1, and branches to ROUTINE if they are equal.

Operands fall in one of the following categories:






184  The Forbin Project, Inc.



EXPNUM: explicit numeric values.  As with numeric variables, these values must
be integers in the range 0-32,767.  For example, in the command:


WINDOW 1 1 25 80


1 1 25 and 80 are explicit numeric values.


KEYWORD: keywords are reserved words defined internally in the script language.
For example, all modem system variables and TURNON/TURNOFF parameters are
keywords which may not be used as variable names for any other purpose.


LABEL: labels identify the beginning of a routine in a script.  They are normal
words followed by a colon.  They are used as parameters in explicit GOTO and
GOSUB statements, or implicitly in IF, WAITFOR and WHEN statements:


IF "$0" = "$1" ROUTINE
.
.
.
ROUTINE:
.
.


if variable 0 is equal to variable 1, branch to the label called ROUTINE.


GOTO MYPARTY
.
.
MYPARTY:
.
.


branches unconditionally to the label MYPARTY.


NUMVAR: numeric variable.  All numeric values and variables used in scripts must
be positive integers, and their value may not exceed 32,767.  Numeric variables
are not defined explicitly;  the same variable may be used for the storage of
text or numeric data.  It is the user's responsibility to insure that the
variable contains numeric data when required.


STRING: a string is an element of text delimited by quotes.  Strings may contain
imbedded blanks.  In the example:


ASSIGN 0 "This is text"


"This is text" is a string.


                                                            Qmodem SST       185





WORD: a self-delimiting alphanumeric value not bound by quotes, and not
containing imbedded blanks.  A word can also be defined as a string without
blanks and without quotes.  In the example:


ASSIGN 0 THISISAWORD


THISISAWORD is a word variable.  The command:


ASSIGN 0 "THISISAWORD"


is functionally identical to the previous one.


Script Command Reference
Following is a complete description of all available script commands.  Each
command is documented in an easy-to-understand format:

Script Command

Function       A brief description of the command.

Declaration    A brief description of the command's syntax.

Remarks        A more detailed description of the command, including parameters
               and their values, and how the command interacts with the rest of
               the script and the system in general.

Restrictions   limitations, or warnings that apply to the command or its
               parameters.  If the command has no restrictions, this section
               will be omitted.

See also       Related script commands.

Example        Limited Coding example.  For in-depth script examples, refer to
               the Utilities Disk.



















186  The Forbin Project, Inc.



ATWRITE

Function       Display a text string anywhere on the screen.

Declaration    ATWRITE  COL  ROW  ATTRIBUTE  STRING

Remarks        COL, ROW and ATTRIBUTE are explicit numeric values or variables.
               ROW and COL must be valid screen coordinates and are not
               restricted to the values set by the WINDOW and BOX commands.
               ATTRIBUTE must be  in the range 0-255.  The COLOR command gives
               a complete description of Color Attributes and how to compute
               them.

See also       COLOR

Example        ATWRITE 1,1,15,"This is a test"  ;put the msg in the
                                                ;upper left corner in
                                                ;high intensity white
                                                ;on a black background
               ATWRITE 1 24 30 "$0"    ;write the text in variable $0
                                       ;on the last line using yellow
                                       ;on a blue background


ASSIGN

Function       Store a value into a variable.

Declaration    ASSIGN  VARIABLE  WORD|STRING

Remarks        This command stores the contents of a word or string into
               VARIABLE.  The $ variable prefix is not used in order to prevent
               value substitution during script parsing.  If the string
               contains embedded quote characters, use the other quote
               character (IE., single ' and  double " quotes) to enclose the
               string.

See also       STRING

Example        ASSIGN 0 TEST            ;sets $0 to "TEST"
               ASSIGN 0 "Test string"   ;sets $0 to "Test string"
               ASSIGN 0 $1              ;sets $0 to equal $1
               ASSIGN THIS "John's Wife is Kathy"
               ASSIGN THAT "$THIS"      ;needs quotes because of
                                        ;spaces and quote embedded in
                                        ;$THIS














                                                            Qmodem SST       187



BEEP

Function       Produce a sound through the speaker.

Declaration    BEEP  TONE

Remarks        TONE is an explicit numeric value or variable and specifies the
               frequency in Hertz (cycles/sec)..  The sound lasts approximately
               1/5 sec.  Multiple BEEP commands may be grouped together to
               produce more meaningful sounds (IE., alarms).  If TONE is non-
               numeric, an error occurs.

Example        BEEP   1200      ;a 1200 Hz tone
               BEEP   1400      ;a 1400 Hz tone
               STRING TONE      ;define a new variable called TONE
               GET    TONE 4    ;prompt for the value of TONE
                                ;no check is made for invalid data
               BEEP   $TONE     ;beep at $tone Hz


BOX

Function       Draw a Box on the screen and set the logical screen dimensions.

Declaration    BOX  C1  R1  C2  R2

Remarks        This command is used to define an on-screen logical window.  The
               window is defined by its upper left corner at row R1, column C1,
               and its bottom right corner at row R2, column C2. Row and column
               values must be explicit numeric values or variables, separated
               by spaces or commas.

               After a BOX or WINDOW command, the output of screen display
               commands (except ATWRITE) is restricted to the area defined in
               the BOX command.

               Coordinates values are not verified; you must insure that C2>C1,
               R2>R1, and all four values are valid screen locations.

               The upper left corner of the screen is at coordinates 1,1.

See also       WINDOW;, GETSCR, PUTSCR

Example        BOX 1,1,80,24  ;opens a window the full size of the screen.
               BOX 20,4,60,8  ;opens a window 40 cols wide by 4 lines high.
               BOX 20 4 60 8  ;same as above without comma delimited.

TIP: If you have an EGA or VGA display, the lower right corner may vary
     with the screen dimensions (See Alt-2 or Alt-4).



BREAK

Function       Send the UART BREAK signal.

Declaration    BREAK



188  The Forbin Project, Inc.



Remarks        The BREAK command sends the UART Break signal for 1.5 seconds
               (or the timer value defined by Alt-N/D/B).  BREAK is the script
               equivalent of the Ctrl-End command.

Example        BREAK      ;Send the break signal


CAPTURE

Function       Open a File to capture all terminal I/O.

Declaration    CAPTURE  FILENAME

Remarks        The filename should be a fully qualified, valid DOS filename.
               FILENAME must be a word or string variable.  If the drive and
               path are omitted, the current drive:\path is assumed.  If the
               file exists, data will be added to the end of it (appended).  If
               the file does not exist, it will be created.

               To close the capture file, use the TURNOFF CAPTURE command.

               CAPTURE is the script equivalent of the Ctrl-Home command.

See also       TURNOFF

Example        CAPTURE C:\QMODEM\TEXT\CAPDATA.DAT
               CAPTURE THISFILE.DAT     ;in the current directory
               TURNOFF CAPTURE


CHDIR

Function       Change to a new Drive:\Directory.

Declaration    CHDIR  DIRECTORY

Remarks        This command is used to change the default DOS directory to that
               specified in the DIRECTORY variable.  DIRECTORY must be a word
               or string variable.  If a new drive specification is included in
               the DIRECTORY variable, the current drive will also be changed.

               CHDIR is the equivalent of the Alt-O command (and of the Alt-L
               command if the drive is changed).

See also       DRIVE

Example        CHDIR \           ;change to the root directory
               CHDIR C:\QMODEM   ;change to C:\QMODEM

               DISPLAY "Enter the new directory ? "  ;a prompt
               GET NEWDIR 64    ;get the new directory
               CHDIR $NEWDIR    ;and do the change








                                                            Qmodem SST       189



CLOSEFILE

Function       Closes the currently open TEXT file.

Declaration    CLOSEFILE

Remarks        The CLOSEFILE command closes the file opened by the OPENFILE
               command.  For a complete explanation, see the OPENFILE command.

See also       OPENFILE, READFILE, WRITEFILE

Example        OPENFILE TEXT.DOC READ  ;open text.doc for reading
               READFILE 0              ;read the first line into $0
               CLOSEFILE               ;close the file


CLRSCR

Function       Clear the logical screen.

Declaration    CLRSCR

Remarks        CLRSCR clears the current active window.  If a WINDOW or BOX
               command has not been issued, the entire screen is cleared.
               CLRSCR is the script equivalent of the Alt-C command.

See also       BOX, WINDOW

Example        CLRSCR             ;clear the screen
               BOX 1 1 80 14      ;open a window on the screen
               CLRSCR             ;clear the window
               WINDOW 1 1 80 24   ;define the "full screen"
               CLRSCR             ;clear the whole screen


COLOR

Function       Defines the color of displayed text.

Declaration    COLOR  ATTRIBUTE




















190  The Forbin Project, Inc.



Remarks        This command sets both foreground and background colors with a
               single attribute.  ATTRIBUTE is an explicit numeric value or
               variable.   The following values are needed to compute the color
               attribute:

               0  Black       8  Dark Gray        +128  Blink
               1  Blue        9  Light Blue
               2  Green       10 Light Green
               3  Cyan        11 Light Cyan
               4  Red         12 Light Red
               5  Magenta     13 Light Magenta
               6  Brown       14 Yellow
               7  Light Gray  15 White

               Foreground colors may be 0 thru 15; background colors may be 0
               thru 7.  To compute the correct attribute, use the following
               formula:

               ATTRIBUTE = Foreground + (16 * Background)

               For a blinking foreground, add 128 to the attribute.  To help
               you, we have included a Script called COLORS.SCR on the
               Utilities Disk.  Run this script to view all available color
               combinations and values.

See also       ATWRITE

Example        COLOR 30    ;Yellow on Blue
               COLOR 2     ;Green on Black
               COLOR 207   ;Blinking White on Red



COLORBG

Function       Changes just the background color of displayed text.

Declaration    COLORBG  ATTRIBUTE

Remarks        This command sets the background color with a single attribute.
               ATTRIBUTE is an explicit numeric value or variable.   The
               following are valid ATTRIBUTE values:

                    0  Black
                    1  Blue
                    2  Green
                    3  Cyan
                    4  Red
                    5  Magenta
                    6  Brown
                    7  Light Gray

See also       ATWRITE, COLOR, COLORFG

Example        COLORBG 1    ;Changes the background to Blue





                                                            Qmodem SST       191



COLORFG

Function       Changes just the foreground color of displayed text.

Declaration    COLORFG  ATTRIBUTE

Remarks        This command sets the foreground color with a single attribute.
               ATTRIBUTE is an explicit numeric value or variable.   The
               following values are valid color attributes:

                    0  Black         8  Dark Gray
                    1  Blue          9  Light Blue
                    2  Green         10 Light Green
                    3  Cyan          11 Light Cyan
                    4  Red           12 Light Red
                    5  Magenta       13 Light Magenta
                    6  Brown         14 Yellow
                    7  Light Gray    15 White

               For a blinking foreground, add 16 to the attribute.

See also       ATWRITE, COLOR, COLORBG

Example        COLORFG 7   ;change the foreground to white


DEBUG

Function       Enable or disable the Internal Script Debugger.

Declaration    DEBUG  ON|OFF

Remarks        The DEBUG command is useful in developing complex scripts since
               you can trace script execution on-screen and in real-time mode.
               DEBUG is OFF by default when a script starts.

Example        DEBUG ON   ;Turn it on
               - - - execute script commands - - -
               DEBUG OFF  ;Turn it back off


DECR

Function       Decrement the value stored in a variable.

Declaration    DECR  VARIABLE

Remarks        DECR decrements the value of a numeric variable by 1.  If the
               variable is non- numeric or not greater than zero, an error will
               occur.

See also       INCR, STRING, ASSIGN








192  The Forbin Project, Inc.



Example        ASSIGN  0 10              ;load $0 with 10
               LOOP:                     ;a place to loop to
               DISPLAY "$0"              ;display the value
               DECR    0                 ;decrement $0 by 1
               IF      "$0" = "0" DONE   ;if it is equal to 0
                                         ;goto DONE
               GOTO    LOOP              ;Branch back to LOOP
               DONE:                     ;Exit point


DELAY

Function       Pause a script for a certain amount of time.

Declaration    DELAY  DELAYVALUE

Remarks        DELAYVALUE is an explicit value or numeric variable containing
               the duration of the delay in milliseconds (1000 = 1 second).
               This is similar to the PAUSE command, but no characters are
               displayed during a DELAY.  You might want to use this command
               when building menus or displaying online help.

See also       PAUSE

Example        DELAY 1000    ;stops for 1 second
               DELAY 10000   ;stops for 10 seconds
               DELAY 100     ;stops for 1 tenth of a second


DIAL

Function       Used to tag and dial one or more entries.

Declaration    DIAL  DIALSTRING

Remarks        The DIAL command is used to call one or more entries stored in
               the phone directory. DIALSTRING is a string or string variable
               in the same format as the Tag Multiple entry in the Alt-D
               directory display.  Please refer to the Tag Multiple command
               under Alt-D for additional information.

Example        DIAL "1"         ;dial entry number 1.
               DIAL "TForbin"   ;dial all numbers that match
                                ;the text "FORBIN".
               DIAL "PA1B PA2"  ;dial 1 & 2 with Prefix
                                ;modifiers.

Restrictions   If a script is linked to the entry being dialed, it will not be
               executed.  All commands to be executed must be defined in the
               script file which contains the DIAL command.

Example        SEND "ATDT 1 319 233-6157^M" ;dial the number
               WAITFOR "CONNECT"            ;wait for connect
               - - -                        ;more commands

TIP: DIAL keeps dialing the same entry until a connection is established.
     To dial a number once without re-tries, use the SEND command with the
     appropriate modem dialing string.


                                                            Qmodem SST       193




TIP: If you sort the phone book and make explicit reference to entry
     numbers, be sure to reflect the changes in your script's DIAL
     commands.  To dial an entry regardless of its number, use the Text
     Match tagging method.



DISPLAY

Function       Display a line of text on the screen.

Declaration    DISPLAY  TEXT

Remarks        The TEXTSTRING string or string variable is displayed at the
               current cursor position and in the current color.  Following the
               DISPLAY, the cursor is located after the last character in
               TEXTSTRING.  The text is not sent to the serial port.  The
               cursor position is set by default following a DISPLAY,
               DISPLAYLN, NOTE or ATWRITE statement, or by the user with a
               GOTOXY statement.  The color is the screen's default, or is set
               by the user with a COLOR statement.

See also       ATWRITE, COLOR, DISPLAYLN, GOTOXY, NOTE

Example        GETSCR                ;save the screen
               BOX     1 1 20 9      ;draw a box
               COLOR   11            ;set color to Light Cyan
               GOTOXY  6 2           ;go to col 6, row 2
               DISPLAY "TEST MENU"   ;show heading
               COLOR   10            ;set Light Green color
               GOTOXY  3 4
               DISPLAY "A) Option one"
               GOTOXY  3 5
               DISPLAY "B) Option two"
               GOTOXY  3 6
               DISPLAY "C) Option three"
               GOTOXY  3 7
               DISPLAY "D) Option four"
               GOTOXY  3 7
               DISPLAY "Option # ? "
               COLOR   15            ;set color to White
               GET     0 1           ;read character into $0
               PUTSCR                ;restore the screen

Note: DISPLAY is similar to the basic statement PRINT "Text"; (note the
      semicolon) which does not automatically re-position the cursor to the
      next line and allows concatenation of displayed strings on the screen.


DISPLAYLN

Function       Display a line of text on the screen.

Declaration    DISPLAYLN  TEXT





194  The Forbin Project, Inc.



Remarks        The text defined by TEXT is displayed at the current cursor
               position and in the current color.  Following the display, the
               cursor is located on the first column of the next line in the
               logical screen.  The text is not sent to the serial port.
               Original cursor location and color is described under the
               DISPLAY command.

See also       DISPLAY, ATWRITE

Example        GETSCR                ;save the screen
               COLOR     11          ;set color to Light Cyan
               DISPLAYLN "TEST MENU" ;show heading
               COLOR     10          ;set Light Green color
               DISPLAYLN "A) Option one"
               DISPLAYLN "B) Option two"
               DISPLAYLN "C) Option three"
               DISPLAYLN "D) Option four"
               DISPLAY   "Option # ? "
               COLOR     15          ;set color to White
               GET       0 1         ;read character into $0
               PUTSCR                ;restore the screen


NOTE: DISPLAYLN is similar to the basic PRINT "Text" statement (note the
      lack of a trailing semicolon) which relocates the cursor to the
      beginning of the next line after printing.



DOS
BIGDOS

Function       Execute a DOS command.

Declaration    DOS  COMMAND
               BIGDOS  COMMAND

Remarks        DOS is the script equivalent of the Alt-R command; it invokes
               the Qmodem DOS Shell, and it is subjected to the same
               limitations.  Please refer to the Alt-R command for additional
               information on the DOS Shell .  COMMAND must be a word, string,
               or string variable.

               The DOS command disables the Optimum Shell (Alt-N/O/R/O) for the
               duration of the command.  The BIGDOS leaves this enabled if so
               set in the Setup.  Each has an advantage.

               DOS is faster if you do not have sufficient EMS memory because
               it will swap a large file to disk.  BIGDOS makes almost 220 more
               K available during the Shell.  If you have lots of EMS, then you
               most certainly will want to use BIGDOS.









                                                            Qmodem SST       195



Example        DOS "Copy text.doc PRN"    ;copy a doc file to
                                          ;the printer.

               BIGDOS "123"               ;run Lotus 123 with lots of free
               memory.

               DOS "type text.doc|more"   ;even pipes and
                                          ;redirection work!

               BIGDOS "COMMAND"  ;will invoke the command prompt
                                 ;until EXIT is entered, just
                                 ;like Alt-R


DOWNLOAD

Function       Receive a file.

Declaration    DOWNLOAD  PROTOCOL  FILENAME  [ASCII options]

Remarks        DOWNLOAD is the script equivalent of the PgDn command.  PROTOCOL
               must be one of the internal or external file transfer protocols
               defined to Qmodem.  FILENAME must be fully qualified (include
               the drive and path) or it will be saved in the download
               directory (Alt-N/D/D).  If the download directory is blank, then
               the file will be saved in the current directory.

               Status information is shown in a window while the transfer takes
               place.

               Internal Protocols:

                    A    ASCII
                    X    Xmodem
                    C    Xmodem CRC
                    R    Relaxed Xmodem
                    O    Xmodem-1K
                    F    Xmodem-1K/G
                    Y    Ymodem Batch
                    G    Ymodem/G Batch
                    Z    Zmodem

               ASCII downloads can have optional parameters to aid in
               conversion from one system to another.  They can be specified in
               any order and are not case sensitive.  The parameters are:

               XLATE=[ON|OFF]          Sets translate table usage.
               CR=[NONE|STRIP|ADDLF]   Sets CR handling options.
               LF=[NONE|STRIP|ADDCR]   Sets LF handling options.

See also       DOWNLD, UPLOAD, UPLD









196  The Forbin Project, Inc.



Example        DOWNLOAD Y C:\QMODEM\     ;Batch Ymodem download
               DOWNLOAD O THISFILE.TXT   ;saves to current directory

               CHDIR  C:\QMODEM          ;change directory
               DOWNLD C QMODEM30.ARC     ;put in current directory

               DOWNLOAD A Filename XLATE=on CR=addlf LF=strip
               ;This will filter the incoming data through the Input
               ;Translate Table, add one LF after each CR, and strip
               ;all LF's as it saves to FILENAME.

CAUTION:When using the ASCII protocol, Qmodem must receive a ^Z (EOF)
        character or the download will never terminate.



DRIVE

Function       Change the default drive.

Declaration    DRIVE  LETTER

Remarks        DRIVE changes the default logged drive, but does not switch
               directories as does the CHDIR command.  LETTER is any valid
               drive letter in your system (A-Z), including those defined with
               the DOS SUBST command.

               DRIVE is the equivalent of the Alt-L command.

See also       CHDIR

Example        DRIVE A   ; switch to the A: floppy drive
               DRIVE C   ; switch to the C: drive
               DRIVE Z   ; switch to the Z: drive


EGA

Function       Change screen size on systems equipped with EGA or VGA display
               adapters.

Declaration    EGA  25|43|50

Remarks        EGA changes the number of screen lines to the new value
               specified in the command (43 and 50 are interchangeable to
               remain compatible with previous releases of Qmodem).  If 43 or
               50 is specified, EGA systems will switch to an 80x43 screen
               size, while VGA cards will switch to 80x50.

               EGA is the equivalent of the Alt-2 and Alt-4 commands.

Restrictions   This command is ignored if no EGA or VGA is present.

Example        EGA 43  ;switch to 80x43 (EGA) or 80x50 (VGA).
               EGA 25  ;switch to 80x25 for both EGA and VGA.

NOTE: The screen will be cleared after each EGA command.



                                                            Qmodem SST       197



EXIST

Function       Conditional branch depending on the presence of a file.

Declaration    EXIST  FILENAME  LABEL

Remarks        If FILENAME is found, the script will  jump to the location in
               LABEL.  If a wildcard filename is passed, at least one match
               will set the $SUCCESS flag and a jump to LABEL occurs.  If there
               are no matches, the $FAIL flag is set and script execution will
               continue with the next sequential statement.

Example        EXIST C:\AUTOEXEC.BAT YES
                  ;if there is an autoexec.bat in the C:\ root
                  ;directory, jump to label YES:
               - - -
                  ;do other script commands if it does not exist.
               YES:  ;label

               ASSIGN 0 C:\AUTOEXEC.BAT   ;assign $0 the filename
               EXIST $0 YES               ;same as above


EXIT

Function       Terminates the script and returns to terminal mode.

Declaration    EXIT

Remarks        The script is unconditionally stopped, and control returns to
               Qmodem.

See also       RETURN

Example        EXIT        ;stop the scripts
               NOTE text   ;does NOT execute because of EXIT


FKEY

Function       Execute an F-Key macro.

Declaration    FKEY  KEYNO

Remarks        FKEY executes the command stored in the current function key
               file.  The function key and shift state are defined by the
               explicit numeric value or variable KEYNO, based on the following
               table:

                         1 - 12   Normal  F1 - F12
                        13 - 24   Shift   F1 - F12
                        25 - 36   Ctrl    F1 - F12
                        37 - 48   Alt     F1 - F12

See also       LOADKEY

Example        FKEY 27   ;send the string stored in Ctrl-F3.
               FKEY 1    ;send the string in F1.


198  The Forbin Project, Inc.




TIP: FKEY will execute commands stored in function keys 11 and 12, even if
     your keyboard has only 10 function keys rather than 12.  Refer to the
     Alt-J command for information on storing commands into function keys.



FLUSH

Function       Clear the Keyboard buffer, COM port buffer, or both.

Declaration    FLUSH  KBD|COM|ALL

Remarks        FLUSH clears data pending in the keyboard buffer (KBD option),
               the COM port buffer (COM option), or both (ALL).  Any pending
               input data stored in the buffers is lost.

Example        DISPLAY "What is your name? " ;ask for a name
               FLUSH   COM                   ;clear the com port
               GET     1 20                  ;read it into $1


GET

Function       Read data from the keyboard and store it into a variable.

Declaration    GET  KBDATA  COUNT

Remarks        Input:    KBD
               Output:   Screen and COM port

               The GET command only accepts data from the local keyboard.  The
               data is echoed to the screen AND to the COM port.

               KBDATA is any valid string variable; its name is not preceded
               with the "$" identifier.  COUNT is an explicit numeric value or
               variable which defines the maximum number of characters in the
               input string.  ENTER terminates the GET command.

See also       GETR, GETN, GETNR, GETX, INKEY

Example        DISPLAY   "Enter number ?" ;prompt for number.
               GET       0 2              ;read 2 chars max.
               DISPLAYLN "You entered $0" ;show it again.


GETR

Function       Read from both the local keyboard and COM port and store it in a
               variable.

Declaration    GETR  KBCOMDATA COUNT








                                                            Qmodem SST       199



Remarks        Input:    KBD and COM port
               Output:   Screen and COM port

               GETR is a superset of the GET command which also accepts data
               from the COM port.  Data is displayed on the screen and echoed
               back to the COM port.

               Parameters and coding syntax are identical to the GET command.

               If online checking is enabled with the TURNON ONLINE command,
               GETR will check the modem for an ONLINE condition.  If the
               connection is lost (IE., carrier drop), the variable will
               contain the string "_OFFLINE_", regardless of the value in
               COUNT.

See also       GET, GETN, GETNR, GETX, INKEY

Example        WRITE   "Enter number ?"  ;ask for number over COM port
               GETR    0 2               ;read 2 chars max
               WRITELN "You entered $0"  ;show again on both screens


               TURNON ONLINE                   ;online checking active
               WRITE  "Enter a number ? "      ;prompt for a number
               GETR   num 5                    ;read the number
               - - -                 - - -
               - - -  Carrier drops  - - -     ;the caller hung up...
               - - -                 - - -
               IF '$num' = '100' Label_100     ;if num=100,
                                               ;  goto Label_100.
               IF '$num' = '_OFFLINE_' Cycle   ;if caller hung up,
                                               ;  goto Cycle.


GETN

Function       Read from the local keyboard and store it in a variable.

Declaration    GETN  KBDATA COUNT

Remarks        Input:    KBD
               Output:   Screen

               The GETN command accepts data from the local keyboard.  The
               characters are displayed on the local screen only.

               GETN is syntactically identical to GET.

See also       GET, GETR, GETNR, GETX, INKEY

Example        DISPLAY   "Enter number ?"  ;ask for number
               GETN      0 2               ;read 2 chars max
               DISPLAYLN "You entered $0"  ;show again on local screen







200  The Forbin Project, Inc.



GETNR

Function       Read from both the local keyboard and COM port and store it in a
               variable.

Declaration    GETNR  KBCOMDATA  COUNT

Remarks        Input:    KBD and COM port
               Output:   Screen

               GETNR reads data from the local keyboard and from the COM port.
               The characters are displayed on the local screen only.

               GETNR is syntactically identical to GETR, and the GETR online
               dependency and restrictions also apply to GETNR.

See also       GET, GETN, GETNR, GETX, INKEY

Example        WRITE   "Enter number ?"    ;ask for number
               GETNR    0 2                ;read 2 chars max
               WRITELN "Caller entered $0" ;show again on local screen

               TURNON ONLINE                   ;online checking active
               WRITE  "Enter a number ? "      ;prompt for a number
               GETNR  num 5                    ;read the number
               - - -                 - - -
               - - -  Carrier drops  - - -     ;the caller hung up...
               - - -                 - - -
               IF '$num' = '100' Label_100     ;if num=100,
                                               ;  goto Label_100.
               IF '$num' = '_OFFLINE_' Cycle   ;if caller hung up,
                                               ;  goto Cycle.


GETSCR

Function       Save a copy of the current screen in memory.

Declaration    GETSCR

Remarks        GETSCR saves a snapshot of the current screen for later re-
               display with the PUTSCR command.

Restrictions   GETSCR may be nested up to three levels deep.  A "nesting level"
               is defined as a corresponding pair of GETSCR/PUTSCR commands.
               Beyond the third nesting level, an error condition occurs.

See also       PUTSCR, CLRSCR

Example        GETSCR  ;save screen level 1
               - - -   ;process
               GETSCR  ;save screen level 2
               - - -   ;process
               CLRSCR  ;clear the screen
               - - -   ;do more script commands
               PUTSCR  ;restore screen level 2
               - - -   ;process
               PUTSCR  ;restore screen level 1


                                                            Qmodem SST       201




NOTE: The above example demonstrate 2-deep GETSCR/PUTSCR nesting.



GETX

Function       Read data from both the local keyboard and the COM port and
               storing it in a variable.

Declaration    GETX  KBCOMDATA  COUNT  CHARACTER

Remarks        Input:    KBD and COM port
               Output:   Screen

               GETX captures incoming keyboard and COM data and stores it into
               the KBCOMDATA variable.  CHARACTER terminates the input in
               addition to ENTER.

               Unlike other GET commands which require a carriage return <CR>
               to indicate the end of the input, GETX his will terminate when
               one of the following conditions is met:

               CHARACTER is found in the input data,
               COUNT characters have been received, or
               ENTER has been received.

               If online checking is enabled with the TURNON ONLINE command,
               GETX will check the modem for an ONLINE condition.  If the
               connection is lost (IE., carrier drop), the variable will
               contain the string "_OFFLINE_", regardless of the value in
               COUNT.

See also       GET, GETR, GETN, GETNR, INKEY

Example        ;Let's assume that you are logging into an information
               ;service.  After logon, the service sends you a message
               ;that tells how many new messages there are to read.
               ;You want to capture just the number for later use in
               ;the script.  The message is in the following form:
               ;"NEW MESSAGES (xxx)" where xxx is the number.

               WAITFOR "MESSAGES ("  ;look for beginning of number
               GETX 0 4 )            ;grab up to 4 characters or
                                     ;until the ")" character.


GOSUB

Function       Call a subroutine at a specified LABEL.

Declaration    GOSUB  LABEL

Remarks        GOSUB passes control to a routine identified by its LABEL.  Upon
               completion, the routine must use a RETURN command, at which time
               script execution resumes with the statement immediately
               following the GOSUB. GOSUB/RETURN may be nested up to a maximum
               of 20 levels.


202  The Forbin Project, Inc.



Restrictions   SCRIPT commands and GOSUB/RETURN share a single nesting process.
               Together, they may not exceed 20 nesting levels in any
               combination.

See also       GOTO, RETURN, EXIT

Example        GOSUB SUB1    ;call the SUB1 subroutine
               EXIT          ;end the script

               SUB1:         ;the subroutine SUB1
               - - -         ;script commands
               RETURN        ;end of subroutine
                             ;will branch back to the EXIT statement


GOTO

Function       Unconditional branch to a LABEL in the script.

Declaration    GOTO  LABEL

Remarks        GOTO passes control to the routine identified by LABEL.  Control
               cannot be returned by the routine which was the target of the
               GOTO.

See also       GOSUB, RETURN, EXIT

Example        GOTO SUB1       ;jump to SUB1
               BACKHERE:       ;
               EXIT            ;end the script

               SUB1:           ;the subroutine SUB1
               - - -           ;script commands
               GOTO BACKHERE   ;end of subroutine.  go back up


GOTOXY

Function       Locate the cursor at a known screen position.

Declaration    GOTOXY  COL  ROW

Remarks        COL and ROW are explicit numeric values or variables and must
               contain valid logical screen coordinates.  If coordinates are
               invalid, the cursor will not be re-positioned.

See also       BOX, WINDOW

Example        GOTOXY 1 1        ;homes the cursor
               GOTOXY 80 24      ;puts cursor in lower right corner

               WINDOW 1 1 80 14  ;set a new window dimension
               GOTOXY 40 20      ;FAILS, not inside the window







                                                            Qmodem SST       203



GRAPHICS

Function       Change Terminal Emulation mode.

Declaration    GRAPHICS  EMULATION

Remarks        GRAPHICS changes the terminal protocol to the EMULATION
               variable.  It is the script equivalent of the Alt-G command.
               EMULATION must be one of the following:

               TTY     No Emulation
               ANSI    Internal ANSI driver
               VT100   DEC VT100 terminal
               VTI925  Televideo 925 terminal
               DEBUG_A Debug ASCII mode
               DEBUG_H Debug HEX mode
               AVATAR  Avatar Emulation

Example        GRAPHICS TTY     ;switch to TTY mode
               GRAPHICS VT100   ;switch to VT100 mode.

NOTE: The screen will clear when executing this command.



HANGUP

Function       Return the modem on Hook (Terminate the current online session).

Declaration    HANGUP

Remarks        HANGUP is the script equivalent of the Alt-H command.  The modem
               hangup command is sent and the connection, if any, is
               terminated.

Example        WAITFOR "COMMAND"  ;wait for the command prompt
               SEND    "G^M"      ;send the [G]oodbye command
               HANGUP             ;disconnect


IF

Function       Conditional branch based on the result of a test.

Declaration    IF  STRING1  OPCODE  STRING2  LABEL (type 1)
               IF  CONDITION  LABEL (type 2)














204  The Forbin Project, Inc.



Remarks        Type 1:

               If the result of the test defined by OPCODE is true, the script
               will branch to the routine called LABEL. Valid OPCODEs are:

               OPCODE    Test Performed

               =    If string1 equals string2, goto label
               <    If string1 less than string2, goto label
               >    If string1 greater than string2, goto label
               <=   If string1 less than  or equal to string2, goto label
               >=   If string1 greater than or equal string2, goto label
               <>   If string1 not equal to string2, goto label

               If STRING1 and STRING2 contain numeric values, a numeric
               comparison is performed.  If either is non-numeric, the two
               strings are compared based on their ASCII character values.

               Type 2:

               IF checks for a specific condition and branch to LABEL if true.
               Valid conditions are:

               $ONLINE    ;if Online, goto label
               $OFFLINE   ;if Offline, goto label
               $SUCCESS   ;if last operation was successful, goto label
               $FAIL      ;if last operation failed, goto label

               $ONLINE and $OFFLINE reflect the status of the carrier detect
               (CD) signal.  The ONLINE/OFFLINE indicator is also displayed on
               the Qmodem status line.

               The $SUCCESS and $FAIL indicators are set by the following
               commands:

               UPLOAD, UPLD, DOWNLOAD, DOWNLD, CHDIR, DRIVE and HANGUP.

               The state of $SUCCESS or $FAIL must be set by one of these
               commands before the indicators can be checked.  Once set, the
               state remains the same until it is changed again by the
               completion of another eligible command.  Referring to either
               variable before it is set yields unpredictable results.

Example of     IF '$0' = 'YES' Yes_Label  ;if $0 = YES, goto
(type 1)                                  ;  Yes_Label
               IF "$0" = ""    Nul_Label  ;if $0 is empty, goto
                                          ;  Nul_Label

Example of     IF $ONLINE Skip_Dial  ;go around dial if ONLINE
(type 2)       DIAL "1"              ;dial if offline.
               Skip_Dial:            ;continue...

               S1:                   ;a label
               DOWNLOAD X TEST.DOC   ;download a file
               IF $FAIL S1           ;if failed, go try again





                                                            Qmodem SST       205



INCR

Function       Increment a numeric variable.

Declaration    INCR  NUMVAR

Remarks        INCR adds 1 to the value of a numeric variable.  If the value
               before the INCR command was 32767, the variable will be set to
               zero.

Restrictions   If NUMVAR contains non-numeric data, a script error will occur.

See also       DECR

Example        ASSIGN 0 0             ;load $0 with 0
               LOOP:
               DISPLAY "$0"           ;show it.
               INCR 0                 ;now increment it.
               IF '$0' >= '10' DONE   ;loop until done
               GOTO LOOP
               DONE:


INKEY

Function       Reads a single character from the keyboard or COM port.

Declaration    INKEY  INDATA

Remarks        INKEY reads a single character from the COM port or keyboard
               (whichever is received first) and stores it into the INDATA
               variable.  Any keystroke or COM data is valid and ENTER does not
               have to be pressed for the script to continue.  This command is
               useful to select menu options, for example.

See also       GET, GETR, GETN, GETNR

Example        DISPLAYLN "MENU"
               DISPLAYLN " "
               DISPLAYLN "    A)  Call The Forbin BBS"
               DISPLAYLN "    B)  Call GEnie"
               DISPLAYLN "    C)  Call it a day"
               DISPLAYLN " "
               DISPLAY   "   ?"
               TOP:
               INKEY 0             ;Store result in $0
               IF "$0" < "A" TOP   ;Try again
               IF "$0" > "C" TOP   ;if not a valid choice
                                   ;Now $0 is either A, B or C.


LOADFON

Function       Load a new Phone Book into memory.

Declaration    LOADFON  FONFILE




206  The Forbin Project, Inc.



Remarks        LOADFON loads a new Qmodem phone book.  It is the script
               equivalent of the Alt-D/L command.  FONFILE should be a word,
               string, or variable containing a fully qualified DOS filename
               with the .FON extension.  If the drive and path are omitted, the
               current directory is searched.  Refer to the Alt-D command for
               additional information on Qmodem phone directories.

Restrictions   The FILENAME must end with the .FON extension or an error will
               occur.

See also       DIAL

Example        LOADFON  C:\QMODEM\PCP.FON     ;load a new FON file
               LOADFON  C:\QMODEM\QMODEM.FON  ;reload the original


LOADKEY

Function       Load a new Alt-J Macro KEY file.

Declaration    LOADKEY  KEYFILE

Remarks        LOADKEY loads a new Function Key Macro definition file, making
               48 new F-Key macros available to the script.  KEYFILE should be
               a word, string, or string variable containing a fully qualified
               DOS filename with the .KEY extension.  If the drive and path are
               omitted, the current directory is searched.

Restrictions   the FILENAME must end in a .KEY extension or an error occurs.

See also       FKEY

Example        FKEY 1                   ;send out the current F1 macro
               LOADKEY NEW.KEY          ;load a new KEY file
               FKEY 1                   ;send out a different F1 macro

               LOADKEY C:\QMODEM\1.KEY  ;load still another KEY file


LOG

Function       Open a LOG file to track Qmodem activity.

Declaration    LOG  LOGFILE

Remarks        LOG opens a Qmodem Log file to which activity is recorded.  LOG
               is the script equivalent of the Alt-0 command.  Please refer to
               the Alt-0 documentation for further information on the Qmodem
               Log file feature.

               LOGFILE is a word, string, or string variable containing any
               valid DOS filename.  If the file exists, data will be added to
               it.  If the file does not exist, the script will create it.

               To disable the Logging feature in a script, use the TURNOFF LOG
               command.




                                                            Qmodem SST       207



See also       STAMP, TURNOFF

Example        LOG  PHONELOG.DAT   ;start logging to file Phonelog.Dat
               - - -               ;more scripts commands, some of
                                   ;which will be logged
               TURNOFF LOG         ;close the log file


NOTE

Function       Display a message on the screen and log it in the Capture file
               if open.

Declaration    NOTE  TEXT

Remarks        NOTE displays the TEXT string on the screen. If Session Capture
               is active, TEXT is also recorded in the capture file.  If the
               cursor is not in column 1, then a CR/LF precedes the TEXT to be
               displayed, forcing the cursor to the first position of the next
               line.

               Unlike other text display commands, the TEXT string is NOT bound
               by quotes.  The string starts immediately after the first space
               following the NOTE command and ends with the last character on
               the line (or the semicolon which starts a comment field).

See also       CAPTURE, DISPLAY, DISPLAYLN

Example        NOTE This is a test of the note command    ;comment1


OPENFILE

Function       Open a sequential TEXT file for input or output.

Declaration    OPENFILE  FILENAME  READ|REWRITE|APPEND

Remarks        OPENFILE opens a standard ASCII text file for input or output.
               FILENAME must be a valid DOS filename.  Only one file may be
               open at a time.

               Parameters:

               READ
               Opens the file for INPUT with the READFILE command.

               REWRITE
               Opens the file for OUTPUT with the WRITEFILE command. If the
               file exists, its contents are erased and its length is reset to
               zero.  If the file does not exist, it is created.

               APPEND
               Opens the file for OUTPUT and positions the file pointer to the
               end of the file.  All data written will be added sequentially at
               the end of the file.

Restrictions   Only one file can be open at a time.



208  The Forbin Project, Inc.



See also       CLOSEFILE, READFILE, WRITEFILE

Example        CLRSCR
               NOTE       Testing FILE I/O
               NOTE       Clearing the file
               OPENFILE   testfile   rewrite     ;open the file
               ASSIGN     1 0                    ;set $1 = "0"
               NOTE Writing to the file

               T:
               WRITEFILE $1                  ;write $1 to the file
               IF        "$1" = "100" cl     ;is $1 = 100? jump to CL:
               DISPLAY   "$1 "               ;display the counter
               INCR 1                        ;increment $1
               GOTO t                        ;loop and write again

               CL:
               CLOSEFILE                     ;close the file
               OPENFILE  testfile   read     ;re-open for Reading
               NOTE Reading from the file

               READING:
               READFILE  0                    ;read first line into $0
               DISPLAY   "$0, "               ;show it
               IF        "$0" = "_EOF_" done  ;Is it EOF?  goto DONE
               GOTO      READING              ;loop and read another

               DONE:
               CLOSEFILE                      ;close the file and
               EXIT                           ;exit


PAUSE

Function       Pause a script for a specified amount of time.

Declaration    PAUSE  PAUSEVAL

Remarks        PAUSE is similar to DELAY, but normal screen and keyboard I/O
               are not suspended.  PAUSEVAL is an explicit numeric value or
               variable containing the length of the delay in milliseconds
               (1000 = 1 second).  This command is useful when building menus
               or displaying online help.

Restrictions   PAUSEVAL must be in the range 1-32767.

See also       DELAY

Example        PAUSE 100      ;stops for 1 tenth of a second
               PAUSE 1000     ;stops for 1 second
               PAUSE 10000    ;stops for 10 seconds









                                                            Qmodem SST       209



POP

Function       Remove the top entry from the stack and store it in a variable.

Declaration    POP  VARIABLE

Remarks        POP is used to retrieve a value which was PUSHed onto the
               "stack".  The stack is an area of memory which can store up to
               60 values  (IE, text, number, etc...).

               The stack operates in LIFO mode (Last-In, First-Out).  Thus, a
               POP command retrieves the item which was last PUSHed onto the
               stack.  Retrieving a value other than the top one requires
               multiple POP commands.

               POPping an empty stack returns a NULL string (zero length).
               PUSHing a full stack yields a script error.

See also       PUSH

Example        POP 0    ;POP stack into $0.  $0 will be NULL
                        ;because of no previous PUSH

               ASSIGN 0 0               ;set $0 to zero
               TOP:                     ;set a label TOP
               INCR 0                   ;increment $0
               NOTE This is $$0 [$0]    ;display the value of $0
               PUSH $0                  ;PUSH it on the stack
               IF "$0" = "10" POPSTACK  ;test for value of 10
               GOTO TOP                 ;loop back

               POPSTACK:                ;10 numbers on stack now
               POP 1                    ;POP the stack into $1
               NOTE This is $$1 [$1]    ;display the value of $1
               IF "$1" <> "" POPSTACK   ;If not NULL, get another

               NOTE Done.               ;now we're done
               EXIT


PORT

Function       Switch to a different COM port.

Declaration    PORT  PORTNUM

Remarks        PORT switches the active COM port.  PORTNUM is an explicit
               numeric value or variable in the range 1-8.  If the port
               selected is valid, the current port is closed, DTR is dropped,
               the new port is opened with the same COM parameters as the old
               port and DTR is raised.

               PORT is the script equivalent of the Alt-K command.

               This command can be used to detect the active COM port (the port
               to which the modem is connected).




210  The Forbin Project, Inc.



Restrictions   Valid COM ports must be defined in Setup (Alt-N/M/P).

Example        ;
               ; This assumes a Hayes or compatible modem
               ;
               TIMEOUT 2 TRY2      ;
               PORT    1           ; select COM1 first
               SEND    "AT^M"      ; send the ATtention command
               WAITFOR "OK"        ; look for the response
               GOTO    ON-LINE!   ; if successful, jump!

               TRY2:               ; next label
               TIMEOUT 2 ERROR
               PORT    2           ; select COM2
               SEND    "AT^M"      ; send the ATtention command
               WAITFOR "OK"        ; look for the response
               GOTO    ON-LINE!    ; if successful, jump!

               ERROR:              ; modem not found
               NOTE    No Modem
               EXIT

               ON-LINE!:           ; we found the modem so lets
                                   ; do something!


PUSH

Function       Place an item on the top of the stack.

Declaration    PUSH  TEXT

Remarks        PUSH stores an INTEGER, WORD, STRING or VARIABLE onto the top of
               the stack. TEXT can be retrieved later with the POP command.
               Please refer to the POP command for additional details,
               restrictions, and code example.

See also       POP

Example        See the POP command.


PUTSCR

Function       Restores a screen previously saved with GETSCR.

Declaration    PUTSCR

Remarks        PUTSCR works in conjunction with the GETSCR command, in a manner
               very similar to the PUSH and POP command pair.

               PUTSCR restores the screen which was saved by the GETSCR command
               at the same nesting level.  The entire physical screen is
               restored, as opposed to the logical screen defined with a BOX or
               WINDOW command.





                                                            Qmodem SST       211



Restrictions   Results are unpredictable if a previous GETSCR has not been
               executed prior to the PUTSCR command.  GETSCR/PUTSCR may be
               nested up to three levels.

See also       GETSCR

Example        GETSCR    ;save the current screen
               CLRSCR    ;clear the screen
               - - -     ;do more script commands
               PUTSCR    ;restore the previously saved screen


READFILE

Function       Read a record from a text file.

Declaration    READFILE  INDATA

Remarks        READFILE command reads one line of text from the file opened
               with the OPENFILE command and stores it into the INDATA
               variable.  See the OPENFILE command for an explanation and
               example.

Restrictions   The Text file must have been opened with the READ option or a
               script error occurs.

See also       CLOSEFILE, OPENFILE, WRITEFILE


RETURN

Function       Return from a GOSUB or SCRIPT command.

Declaration    RETURN

Remarks        RETURN returns control to the statement which immediately
               follows the GOSUB or SCRIPT command through which the routine
               received control.

               If there was no previous GOSUB or SCRIPT, RETURN behaves like an
               EXIT command. To unconditionally terminate a script, always use
               the EXIT command.

See also       GOSUB, SCRIPT

Example        GOSUB SUB1    ;call the SUB1 subroutine
               EXIT          ;end the script

               SUB1:         ;the subroutine SUB1
               - - -         ;script commands
               RETURN        ;end of subroutine
                             ;will branch back to the EXIT statement








212  The Forbin Project, Inc.



SCRIPT

Function       Call another script as a subroutine.

Declaration    SCRIPT  SCRFILE

Remarks        SCRIPT passes control to the script identified in SCRFILE and
               operates identically to the GOSUB command. If the script being
               called includes a RETURN command, execution of the calling
               script will resume with the statement following the SCRIPT
               command.  SCRFILE should be the name of a script file stored in
               the directory specified in Setup (Alt-N/D/S).

Restrictions   Up to 40 levels of SCRIPT and GOSUB commands may be nested.

See also       GOSUB, RETURN

Example        ; .....Script ONE.SCR.....      ;a comment line
               NOTE Executing Script ONE.SCR   ;display a note
               SCRIPT TWO.SCR                  ;call another script
               NOTE Back in ONE.SCR            ;display a note
               SCRIPT THREE.SCR                ;call another script
               NOTE Back in ONE.SCR            ;display a note
               EXIT                            ;halt execution

               ; .....Script TWO.SCR.....      ;comment line
               NOTE Executing Script TWO.SCR
               SCRIPT THREE.SCR                ;call another script
               NOTE Back in TWO.SCR
               RETURN                    ;return to previous script

               ; .....Script THREE.SCR.....    ;comment line
               NOTE Executing Script THREE.SCR
               RETURN                    ;return to previous script

               The output of these three scripts (provided ONE.SCR was executed
               first) will be:

               Executing Script ONE.SCR
               Executing Script TWO.SCR
               Executing Script THREE.SCR
               Back in TWO.SCR
               Back in ONE.SCR
               Executing Script THREE.SCR
               Back in ONE.SCR


SEND

Function       Send data to the COM port.

Declaration    SEND  STRING

Remarks        The text specified by STRING is sent to the COM port and
               displayed on the local screen.  The cursor will be positioned
               after the last character in STRING.




                                                            Qmodem SST       213



Example        SEND "^M"             ;send a carriage return (ENTER)
               SEND "^~^~ ^~ ^~ ^M"  ;pause one second followed by
                                     ;3 spaces at .5 second each and
                                     ;then ENTER

               ASSIGN 0 "^~^~ ^~ ^~ ^M"    ;put the above string in $0
               SEND $0                     ;send it

               SEND "$Password^M"   ;send Password stored in the
                                    ;dialing directory only after a
                                    ;valid connect.


SETCOMM

Function       Change the current COM port settings.

Declaration    SETCOMM  PARAMETER  [PARAMETER..]

Remarks        SETCOMM is the script equivalent of the Alt-P command.  At least
               one parameter is required; parameters may be specified in any
               order.

               Valid parameters are:

                        110     110 baud
                        300     300 baud
                       1200    1200 baud
                       2400    2400 baud
                       4800    4800 baud
                       9600    9600 baud
                      19200   19200 baud
                      38400   38400 baud
                      57600   57600 baud
                     115200  115200 baud
                       EVEN    Even parity
                        ODD     Odd parity
                       NONE      No parity
                       MARK    Mark parity
                      SPACE   Space parity
                          7       7 data bits
                          8       8 data bits
                          1       1 stop bit
                          2       2 stop bits

Example        SETCOMM 9600    ;change only the baud rate to 9600


STAMP

Function       Write a string to the LOG file.

Declaration    STAMP  TEXT

Remarks        STAMP is similar to NOTE, but the TEXT string is not displayed
               on the screen.  TEXT is stored into the LOG file (if open).  Any
               text following the STAMP keyword is "logged".



214  The Forbin Project, Inc.



See also       NOTE

Example        NAME_LABEL:
               WRITELN "                 [-------26-chars-max-------]"
               WRITE   "Enter your name ? "
               GETR    NAME 26
               IF      "$NAME" = "" NAME_LABEL       ;check for null
               IF      "$NAME" = "_OFFLINE_" CYCLE   ;check offline
               STAMP ****************************
               STAMP User [$NAME] Logged On

               could add the following two lines to the LOG file:

               10:37:33  04/10/87  STAMP ****************************
               10:37:33  04/10/87  STAMP User [Sysop] Logged On


STRING

Function       Define one or more variable(s)

Declaration    STRING  VARIABLE  [VARIABLE...]

Remarks        Up to 60 variables can be defined with the STRING command.  New
               variables are referenced by prefixing them with "$" (except
               where noted).

Restrictions   Variables are stored in the order in which they were defined.
               All user-defined variable names must start with a letter.

               If two or more variable names share the same beginning
               characters, define the longest name first.  Otherwise, only the
               shortest name will be recognized.

               For example, let's define three new variables called $A, $AA and
               $AAA.  To be able to reference all three, they must be defined
               as follows:

               STRING  AAA, AA, A

See also       ASSIGN

Example        STRING THIS THAT OTHER         ;create three variables
               ASSIGN THIS "NEW TEST"         ;put "NEW TEST" in $THIS
               NOTE [$THIS] [$THAT] [$OTHER]  ;display their values

               would display:

               [NEW TEST] [] []


SYSTEM

Function       Stop the script and exit Qmodem.

Declaration    SYSTEM  X|Y




                                                            Qmodem SST       215



Remarks        SYSTEM unconditionally halts script execution and exits Qmodem.
               It is the script equivalent of the Alt-X command.

See also       EXIT, RETURN

Example        SYSTEM X    ;exit Qmodem with DTR left High
               SYSTEM Y    ;exit Qmodem with DTR dropped


TIMEOUT

Function       Set a WAITFOR timeout value and optional routine label.

Declaration    TIMEOUT  TIMEVAL [LABEL]

Remarks        TIMEOUT controls the length of time WAITFOR commands will wait
               for a text string.  TIMEVAL is an explicit value or numeric
               variable containing the timeout delay (in seconds).  If LABEL is
               specified, the script will branch to that routine when the
               timeout delay expires.  If LABEL is omitted, the script will
               terminate with a timeout error.

See also       WAITFOR

Example        TIMEOUT 3 AGAIN    ;set timer to 3 seconds, label AGAIN
               AGAIN:             ;here's the label
               SEND "ATZ^M"       ;send modem reset command
               WAITFOR "OK"       ;if OK is not seen in 3 seconds,
                                  ;  goto the label AGAIN (try again)


TURNOFF
TURNON

Function       Change Qmodem operating parameters.

Declaration    TURNOFF  KEYWORD  [KEYWORD...]
               TURNON   KEYWORD  [KEYWORD...]






















216  The Forbin Project, Inc.



Remarks        TURNON and TURNOFF are ON/OFF switches for Qmodem functions or
               facilities which can affect the operation of Qmodem, even after
               the script has terminated.

               Following is the list of valid TURNON/TURNOFF keywords and the
               equivalent terminal mode command.  The third and fourth columns
               indicate whether the keyword can be used with TURNOFF and
               TURNON.  The fifth column provides a brief description of the
               keyword.

               Keyword Cmd   OFF ON Action
               ------- --------- -- -----------------------------------
               8_BIT   Alt-8 x   x  8 bit mode
               BS_DEL  Alt-1 x   x  Mode of the Backspace key,
                                    On: BS=DEL   Off: BS=^H
               CAPTURE ^Home x      Off only.  Closes Capture file if open
               CASE          x   x  Case sensitivity of WHEN and WAITFOR
               ECHO    Alt-E x   x  Local Echo mode (duplex)
               LINEFEEDShftTab   x  x  Controls adding LF's to incoming CR's
               LOG     Alt-0 x      Off only.  Closes the LOG file if open
               MUSIC   Alt-M x   x  ANSI Music mode
               NOISE   Alt-B x   x  Beeps & Bells (on or off)
               ONLINE        x   x  State of carrier detection
                                    for the GET Script commands
               PRINT   ^PrtScx   x  Local print echo mode
               SCROLL  Alt-U x   x  Scroll-back capture mode
               SPLIT   Alt-S x   x  Split screen mode on or off
               XON/XOFFAlt-Z x   x  XON/XOFF flow control mode

Example        TURNON  8_BIT NOISE XON/XOFF
               TURNOFF MUSIC ECHO LINEFEED
               CAPTURE C:\QMODEM\CAP.TXT   ;turn on the capture file
               TURNOFF CAPTURE             ;close the capture file
               TURNOFF LOG                 ;nothing happens, not open


UPLOAD

Function       Send a file to the other computer.

Declaration    UPLOAD  PROTOCOL  FILENAME  [ASCII OPTION...]



















                                                            Qmodem SST       217



Remarks        UPLOAD performs two basic types of file transfers; ASCII and
               non-ASCII.  FILENAME must be a fully qualified DOS filename,  or
               the file  must be located in the current directory.

               Valid protocols are:

                    A ASCII
                    X Xmodem
                    C Xmodem CRC
                    R Relaxed Xmodem
                    O Xmodem-1K
                    F Xmodem-1K/G
                    Y Ymodem Batch
                    G Ymodem/G Batch
                    Z Zmodem

               All external protocols (defined with Alt-N/P) are also valid.

               For ASCII uploads, additional parameters may be specified to
               override the Setup (Alt-N/P/A/T) defaults.

               Following are the valid ASCII upload options:

               PACECH=[NONE|character]
               Specifies a "pacing character" which must be received before the
               next ASCII record (IE,, text line) is sent.  The first line of
               the file is always sent regardless of this setting.

               PACESPEED=[nnnn]
               The delay, in milliseconds (1000 = 1 second) inserted between
               each character sent.

               XLATE=[ON/OFF]
               Specifies whether the outgoing file is (ON) or is not (OFF) to
               be translated with the output translate table (Alt-A-2) prior to
               being sent.

               CR=[NONE/STRIP/ADDLF]
               Defines carriage-return (CR) handling. This is normally not
               needed unless the receiving computer does not recognize the
               standard CR character (ASCII 13).

               LF=[NONE/STRIP/ADDCR]
               Defines LineFeed (LF) handling. Similar to CR, but affects the
               LF character (ASCII 10).

               EXPAND=[ON/OFF]
               If ON, adds a leading space to null lines (which contain only a
               CR/LF pair) so that there is a leading SPACE.  This is a useful
               feature when uploading messages to most BBS systems, which
               interpret a null line as and end-of-message indication.

               EOLCH=[nnn]
               Defines the ASCII value of the End-Of-Line character.  It is
               very important to set this parameter correctly.  Since most
               ASCII files end each line with a CR/LF sequence, the LF
               character should be defined as the EOLCH (LF is ASCII 10).



218  The Forbin Project, Inc.



See also       UPLD, DOWNLOAD, DNLD

Example non-   UPLOAD O QMODEM.ARC  ;send the file QMODEM.ARC using
ASCII                               ;Xmodem-1K.  The file must be in
                                    ;the current directory

               UPLOAD X C:\AUTOEXEC.BAT  ;upload the autoexec.bat file
                                         ;from the C: root directory
                                         ;using Xmodem

Example ASCII  SEND    "^M"                ;send a carriage return
               WAITFOR "Command"           ;look for the command line
               SEND    "E^M"               ;command to enter a message
               WAITFOR "To [Enter]=all?"
               SEND    "Sysop^M"           ;to the Sysop
               WAITFOR "Subject:?"
               SEND    "A Private msg^M"   ;the msg description
               WAITFOR "Security:"
               SEND    "R^M"               ;Receiver only

               UPLOAD A TEST.DOC PACECH=: EXPAND=ON EOLCH=10
                      ;upload a text file to a PCB BBS
                      ; and use the colon as the pace char
               SEND   "^M^~^~S^M"
                      ;tell the board to save the msg


WAITFOR

Function       Wait for a specific string to be received.

Declaration    WAITFOR  STRING

Remarks        WAITFOR waits for the defined text string to be received on the
               COM port.  WAITFOR will wait the amount of time specified in the
               last TIMEOUT command.  If no TIMEOUT command was issued, a
               default of 60 seconds is used.

               Each WAITFOR command may have a corresponding TIMEOUT value for
               explicit control of timing and error conditions.  If this method
               is selected,  all WAITFOR commands should have an associated
               TIMEOUT command  This will minimize unexpected errors (such as
               an incorrect branch).

See also       TIMEOUT

Example        TIMEOUT 3 AGAIN    ;set timer to 3 seconds, label AGAIN
               AGAIN:             ;here's the label
               SEND "ATZ^M"       ;send modem reset command
               WAITFOR "OK"       ;if OK is not seen in 3 seconds,
                                  ;  goto the label AGAIN (try again)


WAITUNTIL

Function       Wait for a specified time before continuing.




                                                            Qmodem SST       219



Declaration    WAITUNTIL  TIME

Remarks        WAITUNTIL suspends script execution until a specific time of
               day.  TIME must be in the same format as specified in the
               Alt-N/O/C/T Time Mask.

               While WAITUNTIL is in effect, the target TIME and the current
               system time are displayed side by side until they match, at
               which time the script resumes execution with the next command.

               If this command seems to fail, double-check the Time Mask and
               what you have coded in the script.

See also       DELAY, PAUSE

Example        WAITUNTIL 04:00:00   ;wait till 4 a.m.
               DIAL "1 2 3 4"       ;dial the numbers
               WAITUNTIL 24:00:00   ;will never get past this, because
                                    ;24hr time does not have 24:00:00


WHEN

Function       Allows searching for alternate text strings while WAITFOR is
               active.

Declaration    WHEN  STRING1 STRING2  (type 1)
               WHEN  STRING1 LABEL    (type 2)
               WHEN                   (type 3)

Remarks        WHEN may only be used while a WAITFOR is active.

               WHEN (Type 1) sends STRING2 when STRING1 is received

               WHEN (Type 2) branches to LABEL when STRING1 is received.

               WHEN (Type 3) immediately cancels all active WHEN commands.

               WHEN can be used in a logon (linked) script for systems which
               change certain prompts depending on when you last called.
               PCBoard, for example, changes prompts if you call more than once
               during the same day.

               A maximum of 10 WHEN statements can be active at one time.  WHEN
               statements remain active until they are explicitly canceled by a
               blank WHEN, and are not subjected to the TIMEOUT restrictions
               which affect WAITFOR commands.

See also       WAITFOR











220  The Forbin Project, Inc.



Example        WHEN
               WHEN "Press (Enter) to continue?"     "^M"
               WHEN "MUSIC? (Enter)=no?"             "N Q^M"
               WHEN "What is your first name?"       "John Friel PS^M"
               WHEN "MAILBOX for your mail?"         "N^M"
               WHEN "Conference members (Enter)=no?" "N^M"
               WHEN "More (Y), (N), (NS)"            "N^M"
               WHEN "Enter Language #"               "^M"
               WHEN "(H)elp, More?"                  "N^M"
               WHEN "ENTER to continue"              "N^M"

               WAITFOR  "Main Board Command?"
               DELAY    100
               WHEN

               The first WHEN (Type 3) clears any pending WHEN commands. The
               following WHEN (Type 1) commands identify all logon prompts and
               their respective responses.  With this method, only one WAITFOR
               is needed; WHEN commands handle all others prompts.


WINDOW

Function       Create a logical screen with user defined dimensions.

Declaration    WINDOW  C1  R1  C2  R2

Remarks        WINDOW creates a logical screen window. Unlike the BOX command,
               WINDOW does not cause a frame to be drawn on the screen.  For
               additional information, please refer to the BOX command.

Restrictions   See the BOX command.

See also       BOX, CLRSCR, GETSCR, PUTSCR

Example        WINDOW 1 1 80 24   ;window the full size of the screen
               WINDOW 20 4 60 8   ;window 40 cols wide by 4 lines high


WRITE

Function       Send text to the COM port without a CR/LF.

Declaration    WRITE  STRING

Remarks        WRITE sends text data to the COM port, but does not add a CR/LF
               at the end of the string. This is useful when sending prompts to
               insure that the cursor remains on the same line.  The WRITELN
               command is similar, but adds a CR/LF at the end of the string.

See also       WRITELN, DISPLAY, DISPLAYLN, SEND









                                                            Qmodem SST       221



Example        WRITELN "                       [------------]"
               WRITE   "Enter your first name ? "
               GETR    F_NAME 12
               WRITELN " "
               WRITELN "                       [--------------------]"
               WRITE   "Enter your last name  ? "
               GETR    L_NAME 20
               WRITELN " "
               WRITELN "                       [------------]"
               WRITE   "Enter your password   ? "
               GETR    P_WORD 12

               The following will be displayed on the receiving computer:

                                      [------------]
               Enter your first name ? JOHN
                                      [--------------------]
               Enter your last name  ? FRIEL III

                                      [------------]
               Enter your password   ? PASSWORD


WRITELN

Function       Send text out the COM port with a CR/LF.

Declaration    WRITELN  STRING

Remarks        WRITELN is the CR/LF version of the WRITE command.

See also       WRITE, DISPLAY, DISPLAYLN, SEND

Example        WRITELN "                       [------------]"
               WRITE   "Enter your first name ? "
               GETR    F_NAME 12
               WRITELN " "
               WRITELN "                       [--------------------]"
               WRITE   "Enter your last name  ? "
               GETR    L_NAME 20
               WRITELN " "
               WRITELN "                       [------------]"
               WRITE   "Enter your password   ? "
               GETR    P_WORD 12

               The following will be displayed on the receiving computer:


                                      [------------]
               Enter your first name ? JOHN

                                      [--------------------]
               Enter your last name  ? FRIEL III

                                      [------------]
               Enter your password   ? PASSWORD




222  The Forbin Project, Inc.



WRITEFILE

Function       Write a line to a text file.

Declaration    WRITEFILE  WORD|STRING|VARIABLE

Remarks        WRITEFILE writes a word, string, or string variable to the file
               opened by the OPENFILE command.

Restrictions   OPENFILE with the REWRITE or APPEND option must have been issued
               first.

See also       CLOSEFILE, OPENFILE, READFILE

Example        See the OPENFILE command for an explanation and example.




Script Error Messages
Error messages, while not a pretty thing to see, are important in fixing the
problems you may run across.


CAPTURE Filename not found

  The CAPTURE command expected a WORD parameter and it was either missing or a
  STRING was specified.


DOWNLOAD Filename expected

  The command was not followed by any text or the following text was not a
  WORD.


DRIVE Letter A..Z expected

  The DRIVE command did not receive a character between A and Z as a parameter.


EGA value must be 25, 43 or 50

  The value passed to the EGA command was not 24, 43 or 50.  Use a correct
  value.


ERROR opening FILE

  An error occurred in OPENFILE  Check the filename and correct.


ERROR Opening Script File

  The script file was found, but could not be opened.  Make sure the file is
  not locked in a network environment.




                                                            Qmodem SST       223



ERROR reading from FILE

  An error occurred in a READFILE command.  Make sure that the file contains
  valid data.


ERROR writing to FILE

  An error occurred in a WRITEFILE command.  Make sure the file is not locked
  by a network or multi-tasker, and that you are not running out of disk space,
  and try again.


File already open

  Two OPENFILE commands were issued without an intervening CLOSEFILE.  Only one
  file may be opened at a time.


FILE not open

  READFILE or WRITEFILE was issued before the file was opened with OPENFILE.
  Check the script logic.


FILE not open for READ

  READFILE was issued against a file opened for REWRITE or APPEND.   The file
  must be opened for READ.


FILE not open for WRITE/APPEND

  WRITEFILE was issued against a file opened for READ.  The file must be opened
  for WRITE or APPEND.


FKEY Filename does not exist

  The filename specified in the LOADKEY command does not exist.


FLUSH keyword not KBD, COM or ALL

  The FLUSH command requires the keyword KBD, COM or ALL.  Correct and re-try.


FON Filename does not exist

  The filename specified in the LOADFON command does not exist.


GETSCR Nested too deep

  GETSCR/PUTSCR commands can be nested 3-deep.  A 4th GETSCR was detected
  without a corresponding PUTSCR.




224  The Forbin Project, Inc.



GRAPHICS Keyword not found

  GRAPHICS was issued without a  parameter or with an invalid one.  Correct and
  re-try.


Insufficient space for String

  STRING memory  is exhausted.  You have exceeded the memory of your machine.


INTEGER expected

  The command expected an INTEGER value (-32768 to 32767).  The variable or
  string was null or contained non-integer data.


INTEGER value required for INCR or DECR

  The VARIABLE argument in an INCR or DECR command did not contain an integer
  value.  Check script logic and ASSIGN commands and insure that numeric data
  is stored into the variable.


Invalid IF Opcode

  The IF command requires one of 6 comparison Opcodes.  Make sure the Opcode is
  correct and that necessary quotes are used.


Invalid KEYWORD or TOKEN

  The first word in the line was not a valid KEYWORD, or the KEYWORD was passed
  the wrong type of data.


Invalid LABEL or misplaced Colon

  A colon ":" was found at the beginning of a line.  This may be an invalid
  LABEL or the colon needs to be changed to a semicolon if the line contains a
  comment.


INVALID OPENFILE mode

  An invalid parameter followed the OPENFILE command.  Valid OPENFILE
  parameters  are READ, REWRITE, or APPEND.


Invalid Substitute VARIABLE

  The specified VARIABLE name was not found.  Make sure the variable is defined
  with a STRING command before using it.







                                                            Qmodem SST       225



Invalid UPLOAD keyword or keyword option

  One of the ASCII UPLOAD keywords was misspelled or contains an invalid
  parameter.  Correct the keyword(s) and parameters and re-try.


LABEL not found

  A LABEL was not found.  Check the script for a possible omission or
  misspelling and try again.


Line too long

  A script line exceeds 254 character.  Edit the Script and make sure lines are
  less than 254 characters.


LOADFON Filename not found

  LOADFON expected a WORD parameter.  The parameter was missing or a STRING was
  specified instead.


LOADKEY Filename not found

  LOADKEY expected a WORD parameter.  The parameter was missing or a STRING was
  specified instead.


LOG Filename not found

  The LOG command expected a WORD parameter and it was either missing or a
  STRING was specified.


Off Screen Coordinates

  The Row and/or Column argument(s) of a GOTOXY command was (were) invalid.
  Since GOTOXY is limited by BOX/WINDOW boundaries, make sure you reset any
  WINDOW or BOX commands before assuming a full 80x25 screen.


ON or OFF parameter expected

  The DEBUG command can only be followed by the WORD ON or OFF.  Correct and
  re-try.


PORT selection invalid

  PORT expects a WORD in the range 1 to 8.  It was either missing out of range.








226  The Forbin Project, Inc.



RETURN SCRIPT Filename not found

  A Calling script was not found when a RETURN command was issued (IE, it was
  deleted or renamed).  Execution cannot continue.  Check to be sure you are
  not deleting/renaming the calling script by accident.


SCRIPT Filename not found

  A called SCRIPT file was not found.  THE script filename parameter was
  missing, or the file could not be located.


SCRIPT/GOSUB nested too deep

  SCRIPT and/or GOSUB commands were nested more than 40 levels.  Some serious
  thought needs to be put into the script(s) to reduce the levels of nesting.


SETCOMM Keyword or Letter expected

  An invalid parameter was used in a SETCOMM command.


STRING expected

  A command required a STRING, but it was either missing or a WORD was
  specified.


STRING length 0

  A null string was used.  The string must be at least 1 character.


STRING not defined

  The string variable used in a command was not defined.  Define the variable
  with the STRING command and try again.


STRING VARIABLE expected

  A string variable command parameter was missing, misspelled, or not defined.


Substitute Line too long

  String variable substitution yielded a line longer than 254 characters.  Use
  additional WRITE/DISPLAY/SEND commands to break up the line into shorter
  ones.


SYSTEM parameter not "Y" or "X"

  "X" or "Y" are the only valid arguments of the SYSTEM command.  Correct and
  try again.



                                                            Qmodem SST       227




Target LABEL cannot be a KEYWORD

  A reserved script keyword was used as a label.  Correct and try again.


Too many PUSHes

  More than 40 values were PUSHed onto the stack without any intervening POPs.


Too many WHEN's defined

  The maximum of 10 WHEN commands were active and an additional WHEN was
  issued.  Use a blank WHEN command to clear unused WHENs and try again.


TURNOFF Keywords(s) not found

  A TURNOFF keyword was missing or invalid.


TURNON Keyword(s) not found

  A TURNON keyword was missing or invalid.


UPLOAD Filename does not Exist

  The UPLOAD filename did not exist.  Verify the filename and try again.


UPLOAD Filename expected

  The FILENAME argument of the UPLOAD command was not a WORD or was missing.


WORD expected

  A WORD argument was expected, but it was missing or a STRING was used.


WORD or LABEL expected

  A WORD or LABEL argument was expected, but it was missing or a STRING was
  used.


WORD or STRING expected

  A WORD or string argument was expected, but was not found.  This is usually
  caused by a missing parameter.








228  The Forbin Project, Inc.



Appendix AAppendix AAppendix A

Most asked Questions or problems and their solutionsMost asked Questions or problems and their solutionsMost asked Questions or problems and their solutions

Question:Question:Question:   When I start up Qmodem, the Online/Offline indicator in the status
            line always says ONLINE?  Why?

Answer:Answer:Answer:     The modem is sending a signal back to Qmodem saying that it is
            connected to another computer.  On Hayes modems and clones that
            use the '&' (ampersand) extended commands, there is usually a
            command that controls the CD (carrier detect) signal.  The default
            mode (unfortunately) is for the CD to be on all the time.

            Check to see if your modem is supported in Quick Modem Config.  If
            so, then use that to configure your modem and Qmodem.  If it not
            listed in there, some of these hints may help...

            To make things right, send the following command to your modem from
            terminal mode:

                      AT&C1<cr>

            You will have to check your modem manual to verify this command in
            case it is not quite 100% Hayes compatible.


Question:Question:Question:   I make changes to the Dialing Directory but they are not saved.

Answer:Answer:Answer:     Changes made to the dialing directory are saved by pressing the
            [F10             F10             F10] key.  Please take a look at the status line on the bottom of
            your screen, which clearly indicates that F10 saves changes, while
            [ESC             ESC             ESC] aborts changes.

            As changes in operating procedures are made, explanatory displays
            are updated to reflect them.  Please look at the screen more
            closely when you encounter a problem; the solution may be a few
            lines away and will save you a telephone call to us in the process.


Question:Question:Question:   Why does Qmodem turn on HALF Duplex after I connect to a BBS?  What
            controls the Duplex mode?



















                                                              Qmodem SST     229



Answer:Answer:Answer:     There are four factors which affect Half and Full Duplex (echo):

            1. The modem itself is set to echo.  On most modems, ATE1 will
               cause commands sent to the modem to be echoed back to the system
               while offline only.  ATF0 will set local echo ON after the
               connection has been established.  Usually, ECHO OFF is the modem
               default.

            2. Doing ALT-E causes Qmodem itself to provide local echo.

            3. Local Qmodem echo can be set in the Qmodem phone directory.
               Alt-D, then O to see the alternate screen.  The last column on
               the right is the Duplex mode for that directory entry.  Once you
               connect, you will get echo if that column contains a "H".
               Change it to "F" and press F10 to save the changed directory
               entry.

            4. The Script commands TURNON ECHO and TURNOFF ECHO can also play a
               role in setting the local echo.  This is usually the one
               everyone overlooks!  Check those Linked Scripts in the dialing
               directory to see if these are set wrong.  This is the last place
               usually to look, but it will pay to be sure!


Question:Question:Question:   My HST modem does not connect with 1200 or 2400 non-MNP modems.
            Either nothing happens, even though the connection is made, or I
            get a VOICE return from the modem.

Answer:Answer:Answer:     The HST always tries to determine if it is talking to another HST
            first, then if it is talking to another MNP modem.  In some cases,
            this process takes longer than the other modem's carrier/training
            sequence (the high-pitch sound the modem makes when it first
            answers your call). As a result, the HST waits forever and
            eventually times out with a NO CARRIER condition.


            If you receive a VOICE return code, but the other modem has in fact
            answered the call, it is possible that background noise in the
            connection is being interpreted by the HST as voice rather than
            data.


            If you KNOW that the other modem is non-MNP, you may use the AT&M0
            command which effectively disables the HST's MNP capabilities and
            makes it act exactly like a standard 1200/2400 modem without MNP.
            The AT&M0 will eliminate many of the problems you may be
            experiencing connecting with slower non-MNP modems.

            To correct the VOICE problem, issue the ATX7 command (the previous
            setting was ATX6 which turns on the HST's voice- recognition
            circuitry). This will prevent the HST from becoming confused.
            However, it will also prevent the HST from recognizing legitimate
            voice answers.


Question:Question:Question:   When dialing out of the phone book, Qmodem does not switch baud
            rates to what was listed in the directory.



230  The Forbin Project, Inc.



Answer:Answer:Answer:     This is directly related to the first Question dealing with the
            Online / Offline indicator.  If the indicator is ONLINE when you go
            to dial from the phone book (Alt-D), the baud rate will not be
            switched because Qmodem assumes you are already online!  If you are
            Offline, then the baud rate is changed before placing the call.




Question:Question:Question:   My Hayes 2400B modem will not hang up reliably.

Answer:Answer:Answer:     The Hayes 2400B and many clones come from the factory with the DTR
            signal forced TRUE (always on) and Qmodem wants to control the DTR
            signal.  The most reliable method for hanging up, it to toggle the
            DTR signal going to the modem. On the Hayes 2400 (and 2400B) this
            is done by sending the following command:

                 AT&D2<cr>

            Then, go into Setup (Alt-N/M/M/H) and change it to the following:

                 DTR

            Make sure the letters are capitalized and there are no additional
            characters, just DTR.  Then make sure you exit and Save the
            Configuration (Alt/N/E/S).

            Now, when you press Alt-H, the modem will hang up!


Question:Question:Question:   What's Ymodem/G and 1K-Xmodem/G and why is it these protocols do
            not show up in the protocol window when I do an up/download.  What
            does it take?

Answer:Answer:Answer:     Ymodem/G and 1K-Xmodem/G are protocols which assume that all error
            corrections are performed by the modem hardware.  Many modems are
            now supporting the MNP (Microcom Networking Protocol) error
            detection/correction protocol, and most high-speed modems use
            proprietary error correction techniques at higher speeds.

            If you have such a modem, you should activate CTS/RTS Hardware Flow
            Control via Setup (Alt-N/M/T/C = ON).  This will enable the
            Ymodem/G and 1K-Xmodem/G protocols.


Question:Question:Question:   What is an Error-Correcting modem?

Answer:Answer:Answer:     Error-correcting modems perform error correction and recovery on
            incoming data by themselves.  This is a feature usually implemented
            in the modem's internal firmware (ROM, for example).  The accepted
            standard for internal modem error correction is MNP (Microcom
            Networking Protocol), names after the company (Microcom) who
            developed it.  MNP is not a "Fixed" standard, it is available in
            levels 1 thru 6, with MNP level 3 being the most commonly available
            implementation.





                                                              Qmodem SST     231



            For two modems to establish an error-free connection, they must
            both support the same MNP level.  Higher levels of MNP, however,
            are compatible with lower levels of the standard.  Two modems
            supporting MNP level 3 and communicating at 2400 (using the Bell
            2400 standard) should establish an error-free connection.  Error-
            free connections are usually indicated by the modem's verbal or
            numeric return code upon connect.

            A Multitech MNP-equipped modem may, for example, return a CONNECT
            2400/RELIABLE message, while a USRobotics HST modem would return a
            CONNECT 2400/ARQ message upon connect. Although many high-speed
            modems (IE, 9600bps and above) from different manufacturers may
            support the same level of MNP, they may use radically different
            encoding modulation schemes to yield high data transfer rates,
            which makes them incompatible at high speeds.

            For example, the Hayes, Microcom, and USR 9600 modems all support
            MNP level 3, but are unable to communicate with each other at
            speeds higher than 2400 due to the incompatibility of their
            proprietary modulation techniques.  Most of these modems will
            automatically "fall back" to the lower speed (IE, 2400) where a
            reliable error-correcting connection can be made.


Question:Question:Question:   How do I get my Qmodem Registration Number?

Answer:Answer:Answer:     This is going to be easy!  All you have to do is type "OPEN                                                                   OPEN                                                                   OPEN 1                                                                        1                                                                        1" at
            the Main Menu of the Forbin Project BBS and your NAME and NUMBER
            will be shown to you.  Copy these two down exactly                                                       exactly                                                       exactly as they are
            displayed by the BBS.  If you want to skip calling our BBS, you can
            call us during the day and get the same information quickly.

            Then, next time you are at the DOS prompt on your computer you can
            initiate the Qmodem registration process.

            1. (you are at the DOS prompt in the Qmodem directory)

            2. type "QMODEM REGISTER<enter>"  (without the quotes)

            3. type in the name exactly as displayed and press <enter>.

            4. type in the number exactly as displayed and press <enter>.

            5. enjoy your registered copy of Qmodem!

            If you have a problem or any question, please leave a comment to
            the Sysop or call us voice at 319-232-4516 during the days.



Question:Question:Question:   I press ENTER in the dialing directory, but it does not dial the
            current entry.  It dials another entry.  Why?








232  The Forbin Project, Inc.



Answer:Answer:Answer:     You have explicitly tagged entries in the directory, probably with
            the space bar, and you then moved to another directory location
            where no tagged entries show.  When you press ENTER, Qmodem dials
            tagged entries.  If NO entries are tagged, then it dials the
            current entry.  There is a tagged entry count displayed at the top
            of the Alt-D screen.  If it is greater than zero, some entries are
            tagged.


Question:Question:Question:   In Qmodem 3.1a I could start the program with any non-blank
            command-line parameter to bypass the opening screen delay. This no
            longer works in Qmodem 4.x.  What's wrong?

Answer:Answer:Answer:     The opening delay can no longer be defeated in Qmodem.  Although
            many have tried, the only known method to get around this is to
            REGISTER your program.  You will receive your own Qmodem
            registration number, and the opening delay will go away after the
            program has been registered to you.  Check the documentation for
            registration info.  We appreciate your support.


Question:Question:Question:   I inadvertently sorted my directory.  How do I get back to what it
            was before?

Answer:Answer:Answer:     Undo the sort by pressing Ctrl-U.  If you inadvertently sorted your
            directory TWICE, you're stuck with a sorted directory.  If you wish
            to experiment with the new directory functions, make a copy of your
            QMODEM.FON file before you start Qmodem.


Question:Question:Question:   I created a logon script with QuickLearn and it does not work.

Answer:Answer:Answer:     It is likely that you captured time- or environment-dependent
            information in the script.  For example, one of the prompts
            captured by QuickLearn contains the amount of time left during your
            online session.

            Edit the script manually to remove that part of the prompt.
            QuickLearn is quick and easy, but it is not intelligent.  It
            records everything that happens between you and the other computer
            and faithfully replicates it in the script, warts and all.

            This can cause problems if prompts change or if they contain
            information that's not likely to be there -- or that will change --
            the next time you call.


Question:Question:Question:   The Host mode seems to "run away" as soon as it's started!

Answer:Answer:Answer:     This is another common problem people are experiencing.  The cause
            is always that the modem is not reporting the true state of the CD
            (Carrier Detect) signal coming from the modem.

            For the Host to operate correctly, the CD signal is checked to see
            when a user is online or has disconnected.  Because the Host can be
            started when you are already online, this can be disastrous if the
            modem is not set up correctly!



                                                              Qmodem SST     233



            The usual symptom is that the Host takes right off, answering its
            own questions with the text it is displaying (or trying to
            display).  This is because the modem Echo (ATE1) is the default and
            the host thinks someone is really online.

            Check your status line before pressing Alt-5.  If it says ONLINE
            all the time, this is the culprit.

            To cure the problem:

            If your modem has DIP switches, look in the modem manual for the
            one that controls the CD signal and change it so that the modem
            reports the true state of the CD.

            If your modem does NOT have DIP switches, it must have what is
            called NRAM (Non-Volital RAM) to store it's configuration.  Most
            modems that have NRAM use the &C command to control the CD signal.
            From terminal mode, issue the following:

                      AT&C1&W

            If your modem comes back and says "OK", you are all set!  The
            status line should then show OFFLINE.  Once the online/offline
            problem is solved, 99% of your Host mode problems will go away.


Question:Question:Question:   When dialing out of the phone book, Qmodem does not switch baud
            rates to what was listed in the directory.

Answer:Answer:Answer:     This is directly related to the Online / Offline indicator.  If the
            indicator is ONLINE when you go to dial from the phone book
            (Alt-D), the baud rate will not be switched because Qmodem assumes
            you are already online!  If you are Offline, then the baud rate is
            changed before placing the call.


























234  The Forbin Project, Inc.


I N D E X

                                         @FSE, 56,123
        #                                @HELP, 106
                                         @SCRIPT, 106
# Rings and Answer, 45                   @SHELL, 104
                                         @SHELLX, 104
        $                                @STAMP, 107

$, 180                                           [
$$, 180
$ATTR, 181                               [ENTER], 7
$BOARD, 84,181                           [ESC], 13
$COM, 84,183                             [Home], 16
$DATE, 180
$DLPATH, 181                                     ^
$FAIL, 198,205
$LAST_COL, 180                           ^, 7
$LAST_ROW, 180                           ^^, 177
$NOTEFILE, 84,183                        ^~, 177
$NUMBER, 84,181                          ^~^~^~, 101
$OFFLINE, 205                            ^~^~^~+++^~^~^~ATH, 101
$ONLINE, 205                             ^End, 143
$PASSWORD, 84,107,182                    ^H, 58,140
$PROTOCOL, 84,182                        ^Home, 217
$SCPATH, 181                             ^M, 29,30,101,122
$SCRIPT, 84,182                          ^PrtSc, 217
$SPEED, 84,183                           ^Q, 38
$SUCCESS, 198,205                        ^S, 38
$TIME, 180
$ULPATH, 181                                     _
                                         _OFFLINE_, 200,202
        +
+++, 30,101
                                                 0
                                         0xE0 Doorway Codes, 59
        .
.CAP, 55                                         1
.DMP, 55
.FON, 121                                16450, 39
.KEY, 103,207                            16550, 39
.LOG, 56                                 16550 UART Enable, 40
                                         16550A, 39
        /                                1K-Xmodem/G, 231

/HOST, 14                                        8
/R, 14
/REGISTER, 14                            8-bit, 141
/S=, 172                                 8_BIT, 217
/S=SCRIPT.SCR, 14                        80x25, 140,180,226
/STATS, 14                               80x43, 140
/VEGAVGA=[mode], 14                      80x50, 140
/VGA=[mode], 14                          8250, 39

        @                                        A
                                         Abandon, 71
@DIAL, 105                               Abort Dial Command, 30
@EDIT, 105,172                           Alt-, 7
@EDITOR, 56,123




Alt-[character], 7                           Upload Dir, 43
Alt-0, 58,107,142,217                      Modem
Alt-1, 58,140,217                            Communication Parameters
Alt-2, 98,140,188,197                          CMD After Baud Change, 27
Alt-4, 98,140,188,197                          Cycle Delay, 27
Alt-5, 144                                     Default Parity, 26
Alt-8, 141,217                                 Default Stop Bits, 27
Alt-9, 141                                     MCD Before Baud Change, 27
Alt-A, 72                                      Modem Command Delay, 28
Alt-B, 58,64,74,217                            Serial Port, 28
Alt-C, 74,190                                  Timeout Delay, 27,83,84
Alt-D, 60,68,74,107,142,173,193,207          Communications Parameters, 90
Alt-D/L, 207                                   Default Baud Rate, 26
Alt-D/T, 105                                   Default Data Bits, 26
Alt-E, 15,217                                Modem Commands, 28,83
Alt-Enter, 62,156                              Abort Dial, 30
Alt-Equal, 156                                 Connect Message, 29,84
Alt-F, 96                                      Error Messages, 29
Alt-G, 58,97,204                               Hangup Command, 30,101
Alt-H, 59,142,204                              Initialization Command, 29,146
Alt-I, 101                                     Prefix Dial Command, 29,87
Alt-J, 143,172,199                             Redial Cancel Text, 30,84
Alt-K, 108,142,210                             Suffix Dial Command, 29
Alt-L, 143,189,197                           Port Addresses, 28,211
Alt-M, 58,217                                  Base and IRQ, 32,33
Alt-Minus, 156                               Toggles, 183
Alt-N, 87,109                                  16550 UART Enable, 40
  Dirs, 40                                     CTS when Writing, 38
    Alt-W Pick, 42                             CTS/RTS Flow Control, 38,231
    BEW Paths, 41                              FIFO during Shell, 39
    Download Path, 41,47,181,196               High Speed Xmit, 40
    Scripts Path, 14,41,97,181                 Init Ignores CD, 40
    Swap Path, 41                              Lock DTE Baud Rate, 39
    Upload Path, 40,181                        XON/XOFF Flow Control, 38
  Exit, 70                                 Options, 57
    Abandon, 71                              Characters, 67,88
    Save Changes, 70,71                        ANSI Music, 68
  Files, 55                                    Beeps & Bells, 67
    Back Scroll, 56                            Date Mask, 69
    Capture File, 55                           Elapsed Mask, 69
    Log File, 56,58                            Notes Tag, 68
    Online Help, 55                            Phone Book Tag, 68
    Printer, 57                                Status Line Filler, 68
    Screen Dump, 55                            Time Mask, 69
    Time/Date Stamp, 57                      Delays, 66
    View, 56,87                                BREAK Timing, 66
  Host, 42,144                                 DTR Timing, 67
    # Rings Answer, 45                         File Transfers, 66
    Answer Command, 44                         Status Window, 66
    Busy Command, 45                         Memory
    DOS Password, 44                           Download Buffer, 63
    Download Dir, 43                           Lines of Scroll Back, 63
    Init Command, 44                           Lines of Scroll back, 137
    Maximum Time, 43                           Overlay Buffer, 63
    OK Message, 44                           Runtime Parms
    Ring Detect, 44                            Calibrate Delay, 63
    Shutdown Password, 44                      EMS for Overlays, 61
    Type of System, 42                         Int16 Enable, 62






      Optimum Shell, 62                        Snow Checking, 23
        Disk, 62                               Status Line, 24,176
      Share IRQ's, 62                          Video Restore, 25
    Sounds                               Alt-O, 109,143,189
      Connect Tones, 64                  Alt-P, 15,108,110,214
        Max Repeats, 65                  Alt-Q, 82,111,172
      Download Tone, 64                  Alt-R, 119,143,153,195
      Upload Tone, 64                    Alt-S, 97,121,217
    Toggles, 57,61,140                   Alt-T, 122
      0xE0 Doorway Codes, 59             Alt-U, 122,217
      Alt-D FON Book, 60                 Alt-V, 56,123,172
        Auto Start, 60                   Alt-W, 123
        Clear Tags on FKey, 60           Alt-W Pick, 42
        Tag Advance, 60                  Alt-X, 125,143,216
        Write FBK File, 61               Alt-X;, 109
      ANSI Music, 58                     Alt-Y, 126,143
      Auto Start LOG, 56,58              Alt-Z, 38,126,217
      Beeps & Bells, 58,64               Alt-N
      DEL/Ctrl-H Backspace, 58             Files
      ENQ Response, 59                       Time/Date, 122
      Guard Alt-H, 59                    ANSI, 15,74,97,109,146,204
      Keypad Emulation, 58               ANSI emulation, 146
  Protocols, 47,131                      ANSI Music, 58,68
    ASCII Options, 48                    ANSI music, 15
      Receive, 49                        Answer Command, 44
        CR Handling, 49                  ASCII, 38,45,48,50,72,73,128,145,218
        LF Handling, 49                  ASSIGN, 179,180,187,192,225
        Use Input xlate table, 49        ASSIGN;, 179
      Transmit, 50                       ATDT, 29
        Blank Line Expansion, 51         ATH, 101
        CR Handling, 51                  ATH0, 30
        End of Line Character, 52        ATWRITE, 170,187,194,195
        LF Handling, 51                  Auto Start Log, 58
        Pacing Character, 51             Auto-Increment, 53
        Pacing Speed, 51                 auto-logon script, 74
        Use Output xlate table, 51       Autoexec Script, 14
    External Protocols, 46               AUTOEXEC.BAT, 8,10,14
      Download BAT, 47
      Filename Prompt, 47                        B
      Protocol Name, 46
      Select Character, 46               Backscroll, 56
      Upload BAT, 46                     BACKSPACE, 58
    Toggles, 53                          Backspace, 140
      Auto-Increment Filename, 53        Batch, 54
      Clear Batch Screen, 54             Batch Directories, 41
      Overwrite Files, 53                Baud Rate, 15,26
      Save Partials, 54                  BBS, 3,26,52,88,96,112,128,141,170,182
      Zmodem Auto-start, 54              BEEP, 188
  Video, 20                              Beeps & Bells, 15,58,67
    Custom Colors, 20                    BOX, 170,187,188,190,203,221,226
    Toggles, 22                          BREAK, 29,30,101,139,188
      Bios Video, 23                     BREAK Timing, 66
      Destructive Backspace, 24          browse, 123
      Emulation, 25                      BS, 140
      Growing Windows, 24                BS_DEL, 217
      Jump Scroll, 25                    BUSY, 27,28,29
      Line Wrap, 24                      Busy Command, 45
      Linefeed after CR, 23




        C                                        D

call-waiting, 29                         Data Bits, 15
CALLBACK, 42,43                          Data bits, 28
Callback, 144,145                        data bits, 26
CAPTURE, 208,217                         Data Terminal Ready, 30
Capture, 55,125,139                      Date Mask, 69
Capture Buffer, 15                       DEBUG, 174,175,192,226
caret, 177                               DECR, 192,206,225
Carriage Return, 15,52,140               Default Baud Rate, 26
carrier detect, 205                      Default Data Bits, 26
CASE, 217                                DEFAULT directories, 42
CGA, 24                                  Default Parity, 26
Characters, 67                           Default Stop Bits, 27
CHAT, 144                                DEL, 58,140
chat, 146                                Del/^H Backspace, 58
CHDIR, 197,205                           DELAY, 193,209,220
Checksum, 128                            Delay, 63
CLOSED, 42                               Delays, 66
CLOSED system, 43                        Delphi, 96
CLOSEFILE, 183,190,209,212,223,224       DESQview, 8,23,24
CLRSCR, 190,201,221                      DIAL, 194,207
COLOR, 187,190,191,194                   Dial Menu
Color, 181                                 Loading a new Phone Book, 90
Color Graphics, 1                          Other Info, 91
COLORBG, 191                               Printing the Phone Book, 91
COLORFG, 191,192                           Sorting the Phone Book, 94
Command After Baud Change, 27              Undo Changes, 95
Command Before Baud Change, 27           Dialing Directory, 74
Command line parameters, 14              dialing queue, 27
COMMAND.COM, 9,119                       DIR, 123
communication ports, 108                 DISPLAY, 170,194,195,208,221,222,227
CompuServe, 96,98,128,141                DISPLAYLN, 170,194,208,221,222
COMSPEC=, 119                            DNLD, 219
CONFIG.SYS, 8                            dollar sign, 180
CONNECT, 28,29,39                        Doorway, 15,59
Connect Message, 29                      DOS, 197
connect speed, 30                        DOS Password, 44
Connect Tone, 65                         DOS Shell, 125
Connect Tones, 64                        DOS/BIGDOS, 195
CONNECT/2400, 29                         double-spaced, 140
CONTROL, 177                             DoubleDOS, 23
Copyright, 1                             Dow Jones News/Retrieval, 96
CR, 140                                  DOWNLD, 196,205
Crash Recovery, 53                       DOWNLOAD, 181,182,196,205,219,223
Ctrl-End, 189                            Download, 41
Ctrl-Home, 189                           Download BAT, 47
Ctrl-[character], 7                      Download Buffer, 63
Ctrl-Backspace, 58                       Download Dir, 43
CTRL-END, 139                            Download tone, 64
Ctrl-H, 140                              DRIVE, 197,205,223
CTRL-HOME, 139                           DSZ, 47
Ctrl-Home, 55                            DSZ.COM, 47,48
Ctrl-PrtSc, 141                          DSZ.DOC, 47
CTS, 38,128,130,231                      DTR, 30,101,125,210
CTS/RTS Flow Control, 38                 DTR Timing, 67
Custom Colors, 20                        Duplex, 15,95
Cycle Delay, 27                          duplex, 74





                                         GETSCR, 188,201,212,221,224
        E                                GETX, 170,179,199,200,201,202
                                         GOSUB, 178,185,202,203,212,213,227
ECHO, 217                                GOTO, 178,185,203
EGA, 24,75,121,140,170,188,223           GOTOXY, 194,203,226
Elapsed Mask, 69                         GRAPHICS, 204,225
Elapsed-Time, 16                         Guard Alt-H, 59
EMS, 61,195
Emulation                                        H
  ANSI, 98
  AVATAR, 99                             Half Duplex, 15,95
  DEBUG_A, 99                            HANGUP, 204,205
  DEBUG_H, 99                            Hangup Command, 30
  TTY, 97                                hardware handshaking, 38
  TVI925, 99                             Hardware-handshaking, 128
  VT100, 98                              hardware-handshaking, 38
ENQ, 59                                  HDX, 15
ENQ Response, 59                         Help Key, 11
environment variable, 10                 high-speed, 38
EOL, 52                                  High Bit, 73
ERROR, 28                                High Speed Xmit, 40
error-correcting, 26                     high-speed, 26,38
error-correcting modem, 38,128           high-speed modems, 28
Error-Correcting modems, 130             Home, 15
error-correction, 130                    Home Menu, 17
ESC, 7                                   Host, 14
EXIST, 178,198                           Host Menu files, 145
EXIT, 198,203,212,216                    Host Mode, 144
Exit, 70                                 Host Password (.PWD) file, 42
EXPNUM, 185                              Host Setup, 144
External protocols, 46,130
external protocols, 127                          I

        F                                IBM compatible, 1
                                         IF, 178,185,204,225
FAW, 42                                  Implied tagging, 76
FDX, 15                                  implied tagging, 77
FIFO during Shell, 39                    inability to dial, 28
File Allocation Window, 42               INCR, 192,206,225
File Delete, 126                         Init Command, 44
File Transfers, 66                       Init Ignores CD, 40
Filename Prompt, 47                      Initialization Command, 29
Find Text, 89                            INKEY, 170,199,200,201,202,206
FKEY, 198,207                            Int16, 62
FKey, 102                                INTEGER, 171
flow control, 15,126                     Internal Editor, 52,56,87
FLUSH, 199,224                           internal editor, 88
FON Book, 60                             internal timeout, 27
Forbin Project, 182                      Invoice, 101
Full Duplex, 15,95                       IRQ, 28,32,62

        G                                        K
gateway, 123                             Key Definition Files, 103
GEnie, 4,96,139,141                      Keypad emulation, 58,59
GET, 170,179,199,200,201,202,206         KEYWORD, 185,225
GETN, 170,179,199,200,201,202,206
GETNR, 170,179,199,200,201,202,206
GETR, 170,179,199,200,202,206                    L



LABEL, 185,225,228                       NOTE, 170,194,208,215
Labels, 178                              Note Files, 74,88
LAP-B, 130                               Note files, 78
Laptop, 20                               Notes Tag, 68
LCD, 20                                  Numeric Result Codes, 30
LF, 140                                  NumLock, 58
LINEFEED, 217                            NUMVAR, 185
Linefeed, 15,140
LineFeed character, 52                           O
Linked Script Edit Screen, 89
Linked Scripts, 88                       OFFLINE, 28
Linked scripts, 171                      Offline, 15
LIST, 123                                OK, 28
LOADFON, 206,224,226                     OK Message, 44
LOADKEY, 198,207,224,226                 OmniView, 8
Lock DTE Baud Rate, 39                   on-hook, 30
LOG, 15,58,125,142,207,214,217,226       ONLINE, 217
Log, 56                                  Online, 15
LOG file, 107                            Online Help, 55
LOGOFF.HST, 145                          OPEN, 42
Logon Scripts, 88                        OPEN system, 42
                                         OPENFILE, 183,208,212,223,224,225
        M                                Overlay Buffer, 63
                                         Overwrite, 53
Macro, 172
macros, 102                                      P
mainframe, 26
mainframe computer, 141                  Pacing Speed, 51
margins, 74                              Parity, 15,26,28
MasterCard, 4                            PATH=, 10,48
Maximum Time, 43                         PAUSE, 193,209,220
MCI, 86                                  PBX, 30,86,101
MCI-Mail, 96                             PCBOARD, 182
MDA, 24                                  PCBoard, 52,96,181,182
Memory, 63                               PgDn, 143,196
MENU.HST, 145                            PgUp, 143
methods used to tag entries, 76          Phone Book Tag, 68
minicomputer, 26                         POP, 210,211
MNP, 38,87,128,130                       PORT, 210,226
modem cables, 130                        Prefix Dial Command, 29
Modem Command delay, 28                  Prefixes, 75
Monochrome, 1                            PRELOG.HST, 145
multi-tasking, 23                        PRINT, 217
multitaskers, 63                         Printer, 57
multitasking, 8                          printer, 141
MUSIC, 217                               Printer Toggle, 15
Music, 15,109                            Protocol, 46
music information, 109                   protocol, 46
Music Toggle, 15                         Protocol Definition window, 46
                                         Protocol Selection Window, 46
        N                                Protocols, 196
                                         PROTS.HST, 145
network, 38,63                           PS/2, 33
NO CARRIER, 28,29                        Public Board eXchange, 30
NO CONNECT, 29                           Public Domain, 3
NO DIAL TONE, 29                         pulse-dialing, 29
Nochange, 96                             PUSH, 210,211,228
NOISE, 217                               PUTSCR, 188,201,211,221,224
noise, 74





                                         Send Zmodem, 47
        Q                                Serial Port, 28
                                         serial port speed, 39
QFE, 121                                 Session Log, 15
QM.BAT, 9                                session log, 142
QMHOST.BAT, 153                          SET, 10
QMHOST.HDR, 145,155                      SETCOMM, 214,227
QMHOST.MSG, 145,155                      SETUP, 109
QMHOST.PWD, 144                          Shell, 62,195
QMHOST.SCR, 151,152                      Shell to DOS, 119,153
QMHOSTL.SCR, 152,153                     ShftTab, 217
QMHOSTPK.EXE, 145,155                    Shift state, 103
QMODEM.CNF, 9,70                         SHIFT-TAB, 140
QMODEM.EXE, 3,9                          Shift-Tab, 23
QMODEM.FON, 9                            Shutdown Password, 44
QMODEM.HLP, 9,55                         SideKick, 121
QMODEM.INI, 125                          Site License, 6
QMODEM.KEY, 9                            sounds, 15
QMODEM.LOG, 56                           speaker, 74
QMODEM.OVR, 9                            Speed, 28
QMODEM.PRE, 9                            SPLIT, 217
QuickLearn, 76,82,111,170,172            Split-Screen, 97
                                         split-screen, 121
        R                                SPRINT, 86
                                         STAMP, 143,208,214
RAM disk, 63                             Status Line, 14,17,141
RBBS-PC, 96                              status line, 24
READFILE, 183,190,209,212,223,224        Status Line Filler, 68
Receive Zmodem, 47                       Status Windows, 66
Redial Hangup Text, 30                   Stop Bits, 15
Registration, 4                          Stop bits, 27,28
Relaxed Xmodem, 128                      STRING, 171,185,187,192,215,225
RETURN, 198,203,212,213,216,227          Strip/Replace, 72
RING, 30,44                              Subscription, 4
Ring Detect, 44                          SUBST, 197
ROM BIOS, 23                             SuperEGA, 140
RTS, 38,130                              SuperVGA, 140
Runtime Parms, 61                        SWAP, 41
RZ.BAT, 47                               Sysops, 3
                                         SYSTEM, 215,227
        S                                System Clock, 16
Save Changes, 70                         SZ.BAT, 47
screen colors, 74
Screen Dump, 55                                  T
screen memory, 23
SCRIPT, 184,212,213,227                  Tag Multiple, 79
Script, 74,143,151                       tagged entries, 75
script files, 41                         TaskView, 8
script parameters, 106                   technical support, 102
Script Recorder, 82,111                  Telephone support, 4
Scripts, 41,96,144,171                   Televideo, 99
SCROLL, 217                              Terminal Emulation, 97
Scroll-back, 63,122,137                  terminal emulation, 15
scroll-back buffer, 15                   Terminal Mode, 17
Scroll-back Toggle, 15                   Text Search, 88
Scrolling Region, 74                     Time Mask, 69
Select Character, 46                     time-of-day, 16
SEND, 170,182,213,221,222,227            Time/Date Stamp, 57
                                         TIMEOUT, 219,220



Timeout Delay, 27                        X.PC, 130
timer, 63                                XMODEM, 128
TIP,                                     Xmodem-1K, 129
  38,47,82,87,88,140,153,172,177,188,19  Xmodem-1K/G, 128,130
  3,194,199                              Xmodem-CRC, 128
Toggles, 15                              XON/XOFF, 217
tone-dial, 29                            Xon/Xoff, 15,38,126
Translation, 49
translation, 72                                  Y
TSR, 63,104
TTY, 97,204                              Ymodem, 129
TURNOFF, 189,208,216,228                 YMODEM batch, 129
TURNON, 200,216,228                      Ymodem/G, 128,130,231

        U                                        Z

UART, 39,101                             Zmodem, 47,54
Un-tagging, 76
Untag All, 81
Up Arrow, 122
UP-ARROW, 137
UPLD, 196,205,219
UPLOAD, 181,196,205,217,226,228
Upload, 40
Upload BAT, 46
Upload Dir, 43
Upload tone, 64
USR Courier HST, 26

        V

Variables, 179
VEGA VGA, 14
Verbose Result Codes, 30
VGA, 24,75,121,140,141,170,188,197
Video, 20
Video-7, 14,141
View, 56
VISA, 4
VT100, 74,97,140,204

        W
WAITFOR, 111,185,216,219,220
WAITUNTIL, 219
Warranty, 7
WHEN, 170,178,185,220,228
Wildcat, 96
WINDOW, 170,187,190,203,221,226
Windows, 8
Windows 3.0, 8,23
WORD, 186
WordStar, 123
WRITE, 170,221,222,227
WRITEFILE, 190,209,212,223,224
WRITELN, 170,221,222


        X