+--------------------+
			| INT 14 H Extension |
			+--------------------+



	CDRV.COM is a "Terminate and Stay Resident" program. It provides
	several new functions for INT 14H.

	These functions use the same parameters as the usual BIOS ones :
	the function number is to be placed in AH, the COM port number
	(0 to 7) is to be placed in DX, whenever required.

	To install CDRV.COM, just type CDRV [Enter] at the DOS prompt,
	or insert this command into the AUTOEXEC.BAT file.

	The functions then available are :


=======
AH =  0	Init port using AL (same as BIOS)
=======
	AL bit meaning is :

	+---+---+---+
	| 7 | 6 | 5 |
	+---+---+---+
	  |   |   |
	  0   0   0  for  110 bps,
	  0   0   1  for  150 bps,
	  0   1   0  for  300 bps,
	  0   1   1  for  600 bps,
	  1   0   0  for 1200 bps,
	  1   0   1  for 2400 bps,
	  1   1   0  for 4800 bps,
	  1   1   1  for 9600 bps.

	+---+---+
	| 4 | 3 |
	+---+---+
	  |   |
	  0   0  for No Parity,
	  0   1  for Odd Parity,
	  1   1  for Even Parity.

	+---+
	| 2 |
	+---+
	  |
	  0  for 1 stop bit,
          1  for 2 stop bits.

	+---+---+
	| 1 | 0 |
	+---+---+
	  |   |
	  1   0  for 7 data bits,
	  1   1  for 8 data bits.

	Upon exit AH = LSR and AL = MSR (see function 3).


=======
AH =  1	Send character in AL (same as BIOS)
=======
	Upon exit AH = LSR with MSB is set in case of T.O.


=======
AH =  2	Recv character in AL (same as BIOS)
=======
	Upon exit AL = char and AH = LSR.
	In case of T.O., AL = MSR and AH = LSR with MSB set.


=======
AH =  3	Get port status (same as BIOS)
=======
	Upon exit AH = LSR and AL = MSR. The meaning of their bits is :

	+---+---+---+---+---+---+---+---+
	| 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | (for AH)
	+---+---+---+---+---+---+---+---+
	  |   |   |   |   |   |   |   |
	  |   |   |   |   |   |   |   +---> data ready (OK to read)
	  |   |   |   |   |   |   +-------> overrun
	  |   |   |   |   |   +-----------> parity error
	  |   |   |   |   +---------------> framing error
	  |   |   |   +-------------------> break detected
	  |   |   +-----------------------> THRE (OK to send)
	  |   +---------------------------> TSRE
	  +-------------------------------> always zero

	+---+---+---+---+---+---+---+---+
	| 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | (for AL)
	+---+---+---+---+---+---+---+---+
	  |   |   |   |   |   |   |   |
	  |   |   |   |   |   |   |   +---> delta clear to send
	  |   |   |   |   |   |   +-------> delta data set ready
	  |   |   |   |   |   +-----------> delta ring indicator
	  |   |   |   |   +---------------> delta carrier detect
	  |   |   |   +-------------------> CTS
	  |   |   +-----------------------> DSR
	  |   +---------------------------> RI
	  +-------------------------------> CD


=======
AH =  4	Write AL to MCR (bit 7 = 0) or LCR (bit 7 = 1)
=======
	+---+---+---+---+---+---+---+---+
	| 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | (for MCR)
	+---+---+---+---+---+---+---+---+
	  |   |   |   |   |   |   |   |
	  |   |   |   |   |   |   |   +---> DTR
	  |   |   |   |   |   |   +-------> RTS
	  |   |   |   |   |   +-----------> OUT1
	  |   |   |   |   +---------------> OUT2 (enable IRQ)
	  |   |   |   +-------------------> enable loopback (*)
	  |   |   +-----------------------> always zero
	  |   +---------------------------> always zero
	  +-------------------------------> 0 to select MCR

	In loopback mode : TXD ---> RXD
			   DTR ---> DSR
			   RTS ---> CTS
			   OUT1 ---> RI
			   OUT2 ---> CD

	+---+---+---+---+---+---+---+---+
	| 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0 | (for LCR)
	+---+---+---+---+---+---+---+---+
	  |   |   |   |   |   |   |   |
	  |   |   |   |   |   |   0   0	....... 5 data bits
	  |   |   |   |   |   |   0   1 ....... 6 data bits
	  |   |   |   |   |   |   1   0 ....... 7 data bits
	  |   |   |   |   |   |   1   1 ....... 8 data bits
	  |   |   |   |   |   |
	  |   |   |   |   |   0 ............... 1 stop bit
	  |   |   |   |   |   1 ............... 2 stop bits
	  |   |   |   |   |
	  |   |   |   |   0 ................... no parity
	  |   |   |   |   1 ................... parity
	  |   |   |   |
	  |   |   |   0 ....................... odd parity
	  |   |   |   1 ....................... even parity
	  |   |   |
	  |   |   0 ........................... no stick parity
	  |   |   1 ........................... stick parity
	  |   |
	  |   0 ............................... no break
	  |   1 ............................... send break
	  |
	  1 to select LCR


=======
AH =  5	Set baud rate according to CX (units are bits per second).
=======

=======
AH =  6	Set SEND TIME OUT, where CX = # of clock tics.
=======

=======
AH =  7	Set RECV TIME OUT, where CX = # of clock tics.
=======

=======
AH =  8	Set BREAK DURATION in clock tics (CX = duration).
=======

=======
AH =  9	Send BREAK on port DX.
=======

=======
AH = 10	Get version number in AH (major) and AL (minor).
=======

=======
AH = 11	Set I/O parms for asynch port (COM1: to COM8:)
=======
	DX = COM port number (0 to 7)
	CX = I/O base address (eg 03F8H)
	AL = IRQ mask (eg 00010000B for IRQ 4)


=======
AH = 12	Get I/O parms for asynch port (COM1: to COM8:)
=======
	DX = COM port number (0 to 7)
	CX and AL set upon exit (see function 11)


=======
AH = 13	Set IRQ mode for port number DX. 
=======
	Upon exit AX = 0 if OK, AX # 0 otherwise (*).

	(*) An error is returned if any com port is already IRQ driven,
	or if no IRQ line is specified for this port.

=======
AH = 14	Reset IRQ mode for current port.
=======

=======
AH = 15	Check for char in buffer.
=======
	CX returns # of chars in buffer, DX returns # of lost chars (if any)
	AH = number of port IRQ driven (0 for none, 1 for COM1:, etc...)
	AL holds the next char to be read from buffer (the char is not
	removed from buffer).

=======
AH = 16	Get char from ring buffer into AL.
=======
	CX returns # of chars still waiting in buffer,
	DX returns # of lost chars (if any),
	AH returns the IRQ driven port #, MSB is set in case of T.O.