HOW TO STUFF YOUR OWN BOARDS WITH CHIPS
              By Louis A. Warner, P. E.
              PEOPLE SYSTEMS LTD. -- SOFTWARE (C) 1983
 
              You have just purchased some of the finest devices 
              that have ever been produced. These chips need 
              special attention if you want to get the best out 
              of them, because they are very easily damaged by 
              static electricity, that you and I wouldn't even 
              notice. No snap, crackle or pop, but zowie, there 
              goes a good chip, destroyed by static electricity.
 
              There are ways to protect your investment against 
              such damage, if you're careful and take your time. 
              Before you unpack the chips think of a pettigree 
              puppy that you just purchased, and treat it 
              tenderly and you'll enjoy. Oh, yes, don't open up 
              the chips until you're ready to install them.
 
              Remember static electricity hates humidity, but it 
              loves nylon and synthetic clothing, soft rugs and 
              slippery shoes. Static is worse in the dry winter 
              weather, and least in the humid summer time. 
              Before you unpack your chips, have you read your 
              owners manuals for adding chips to the main memory 
              or an expansion board? Refresh your memory and 
              plan your project and you'll do it easily. It's 
              really not very hard to do and unless you get 
              rough with your equipment there is little you can 
              harm if you take precautions. You will need a big 
              sheet of aluminum foil, a spray bottle of water, a 
              boiling teakettle and some light hobby tools, 
              flashlight, magnifier, pad and pencil along with 
              the manuals etc.
 
              A clear, clean kitchen table on a linoleum floor 
              where the light is very good is a fine place to 
              operate on the patient. Take your computer cabinet 
              off to get at the board you're going to stuff. 
              Read your manuals or ask your buddy's help to get 
              it unbuttoned. On the IBM-PC there are two large 
              screws in the lower rear corners, near the curve 
              at the bottom of the back. Slide the cover forward 
              and put it aside. Vacuum the fan and inlet areas 
              carefully, but don't let the air from the vacuum 
              stir up any dust in the room. Wiping the fan 
              blades with a tiny brush will help it do its job.
 
              Remove the rear hold down screw from the expansion 
              board and gently raise the board from the bus 
              socket on the mother board. Place a large piece of 
              aluminum foil flat on the table to touch and 
              ground yourself on when you're working on the 
              chips. If you have a battery powered board (clock 
              etc) remove the battery. You are now ready to open 
              up your chips and set them into the open sockets. 
              Review your conditions again. Shoes off, tea 
              kettle boiling, dog and cat out of the house, kids 
              gone to the movies, you are ready to operate, 
              Doctor.
 
              What do you do in the winter or when the humidity 
              is real low? Wait for a rainy day or raise the 
              humidity with a vaporizer in the room. Don't wear 
              synthetic clothes. But use a spray bottle to keep 
              from getting too dry. Mist your clothes and the 
              floor and chair seat (usually plastic too) with 
              water to keep it from generating static. Don't 
              work on rugs, if possible, or else spray them with 
              static guard and water mist. Look-out for nylon 
              lingerie whether you are stuffing a board or 
              whatever. Don't get your computer wet.
 
              You have unwrapped your chips and the board is 
              sitting on the aluminum foil waiting for the 
              chips. Stand your chips, pins down on the foil and 
              examine one carefully, while touching the foil. 
              There may be a production number marked on the 
              underside, in case you need a reference mark. They 
              can also be marked with ordinary pencil lead if 
              you write small enough. Note the indentation at 
              one end that indicates the number one pin end. 
              Find out which way it should go in your board. The 
              pins taper outwards and need to be gently squeezed 
              together into two straight lines.
 
              Press the side of the pins (lengthwise) against 
              the table to align and narrow down the spacing 
              between the lines. Do it again for the pins on the 
              opposite side. Now set it on the socket gently, 
              check direction for the dimpled end (socket covers 
              have been removed, if they existed). Inspect it 
              carefully, with a magnifying glass, if available. 

              If the pins line up with the contact holes 
              properly, then use your two thumbs and steadily 
              press it into the socket. You will feel the socket 
              grab the pins, but dont try to test its holding 
              power. It's hard to get them in but much harder to 
              take chips out of the sockets. There are special 
              chip tools that are available and are well worth 
              the money, if you are going to do much pushing and 
              pulling. Or you can use a couple of small 
              screwdrivers as wedges. But gently! Now take your 
              glass and inspect the chip pins for one that might 
              have been folded under when you pressed it in and 
              it was not in line with the hole. Inspect each pin 
              carefully for a few chips and develop a secure 
              feeling that you are doing it right before you 
              proceed too far.
 
              When the board is stuffed with one full set of 
              eight or nine chips, (populated as they say) and 
              you have reset your switches properly, it is best 
              to test, doctor. But first, look around and read 
              the labels and signs so that the inside of your 
              computer isn't such a strange place next time you 
              have to dig under its covers. You probably feel 
              like the radio receiver owner, when he first 
              changed a tube, years ago. But it's just another 
              piece of hardware to get familiar with. Don't 
              touch but do look, ask questions, and read the 
              manuals. Take a photo or two.
 
              Now, doctor, lets plug it in and test each set 
              before we suture up the patient, and put on the 
              cabinet again. Install the operating cables and 
              put the boot disk in the A: drive and turn it on. 
              Remember that with more memory its going to take 
              more self- diagnostic time, so dont be surprised 
              if 256K takes over a minute before the CPU 
              beeps,"All present and accounted for, Sir". Then 
              your normal boot routine should begin. Watch 
              carefully for error messages on the screen and 
              write them down. If you have parity lights on the 
              board note them and shut the power off in case 
              there is not a normal boot sequence (except for 
              the longer memory check at the beginning.)
 
              DON'T PANIC -- SLOW AND EASY IS THE GAME -- THIS 
              HAS HAPPENED BEFORE AND PEOPLE LIVE THROUGH IT. 
              Here's a list of what could be causing a 
              malfunction, IF THERE IS ONE!  The switches on the 
              board and in the computer could be set wrong, 
              recheck them in writing. Have someone else double 
              check you. There could be a bad chip. (We'll tell 
              you how to look for it). You may have disturbed 
              something in your cleaning or reassembling the 
              cables and case. Make sure everything is properly 
              turned on for the test. There is also the remote 
              possibility that the expansion board is defective 
              or intermittant in the section you have just 
              stuffed. Examine the solder joints on the printed 
              circuit board in these areas. Retrace your steps 
              and restudy the manuals, check the switches and 
              then try it again after a short period. Shut it 
              down if it still doesn't boot properly and once 
              more check all possibilities. The chip failure 
              probability is less than any of the other 
              possibilities, especially wrong switch settings. 

              Remember there are totals of the PC mother board 
              chips, total of the expansion board's memory, 
              total of other boards like a C/PM adapter memory 
              and then the grand total of all RAM installed. 
              Check them by writing them down and see if the 
              switches are correctly set, one by one. Then if, 
              you find that everything is O.K. but it still 
              doesn't work the way it should, continue on.
 
              Let's see if there is a bad chip. This is usually 
              the first assumption, but most often it is switch 
              settings or bent pins or bad sockets that make 
              intermittant contact or some silly thing like 
              leaving the keyboard unplugged. Since taking the 
              chips out is a stubborn operation that doesn't 
              improve with brute force, let's plan our attack. 

              If we have a couple of spare chips we can try them 
              in another working circuit on the board and reset 
              the switches. Go back to where you started. Ground 
              Zero we shall call it. Usually, you dont have to 
              pull the chips just reset the switches and try out 
              the old chips under the original conditions 
              (before stuffing). Put the board in and test it 
              again. It's probably O.K. and you haven't done any 
              damage. But electronic gremlins aren't called 
              glitches for nothing.
 
              Now swap the new spares to determine if they work 
              in the working circuit. Yup, they work O.K. Now 
              let's start a planned procedure to reduce the 
              confusion and the number of times we have to push 
              and pull the same sockets and chips. We don't want 
              to damage our board or the chips with too much 
              handling or abuse. If you stuffed three sets of 
              chips without testing each set and the last one 
              shows the parity error then take those out to 
              test. Work your way backwards, one set at a time, 
              until you get to a working state. Remember to 
              reset the switches correctly each time you test 
              another full set of chips. You can not test 
              partial sets although they can usually remain in 
              the sockets if you know they are good. But, when 
              in doubt, take them out.
 
              Now test three chips at a time and mark them. Put 
              nine that tested good in the old circuit into the 
              next set of sockets. If you only have one extra 
              chip, borrow the parity chip, and turn off the 
              parity reporting until you locate the bad chip 
              (probably only one, IF ANY). By testing your chips 
              two or three at a time in the working circuit, you 
              can isolate the bad group then test them one by 
              one to find the culprit, if there is one.

              When you get through testing and stuffing, you'll 
              find there is nothing wrong with any of the chips 
              and they all work fine. There apparently was a 
              temporary glitche the first time around that 
              issued the parity error and it took a while to 
              discharge a condensor or change a flag or 
              something. That's why, when you buy a pocket 
              calculator, they tell you to turn it off and on 
              several times, if it doesn't work properly the 
              first time.
 
              Try to keep track of your tests and actions on 
              paper so that you can isolate a bad chip or 
              convince yourself that it's something else that's 
              wrong. Mark the chips with a pencil or note the 
              production marks that should identify them 
              uniquely. For your own piece of mind when you 
              think that you have found a faulty chip, after all 
              else is done, test it to prove it's bad in a 
              working circuit, one chip at a time.

              Don't be surprised if it tests good now. That's why 
              manufacturers call it "burning in". (Finding the 
              good and the bad actors). But usually the 
              percentage of bad chips is miniscule unless there 
              is a run that quality control didn't catch before 
              it left the plant, which is almost unheard of. If 
              it now works, burn it in. Leave a colored mark on 
              any suspicious ones, just in case you need to 
              locate an intermittent one in a couple of days or 
              so. Keep a written record of them also.
 
              If you are using the same set of sockets to test a 
              lot of chips, alternate the sockets so that the 
              same ones don't get all the wear. Be careful not 
              to pry against any of the small electronic 
              components and damage them.
 
              Good luck stuffing -- you'll find the experience 
              worth while and not hard at all once you get the 
              knack of it.