ÉÍÍÍÍÍÍÍÍÍÍÍÍÍ> S H A R E W A R E >ÍÍÍÍÍÍÍÍÍÍÍÍÍ»
          º                                               º
          º          DO  NOT  BREAK  THE  CIRCLE  !       º
          º                                               º
          ÈÍÍÍÍÍÍÍÍÍÍ< User-Supported Software <ÍÍÍÍÍÍÍÍÍÍ¼











    ÍÍÍ     ÍÍ   ÍÍ   ÍÍÍÍÍÍ   ÍÍ   ÍÍ    ÍÍÍÍ     ÍÍÍÍÍ      ÍÍÍ   (R)
   ÍÍ ÍÍ    ÍÍÍ  ÍÍ     ÍÍ     ÍÍ   ÍÍ   ÍÍ  ÍÍ   ÍÍ   ÍÍ    ÍÍ ÍÍ
  ÍÍ   ÍÍ   ÍÍÍÍ ÍÍ     ÍÍ     ÍÍ   ÍÍ   Í   ÍÍ   ÍÍ   ÍÍ   ÍÍ   ÍÍ
  ÍÍ   ÍÍ   ÍÍ ÍÍÍÍ     ÍÍ     ÍÍ   ÍÍ      ÍÍ     ÍÍÍÍÍ    ÍÍ   ÍÍ
  ÍÍÍÍÍÍÍ   ÍÍ  ÍÍÍ     ÍÍ     ÍÍ   ÍÍ     ÍÍ        ÍÍ     ÍÍÍÍÍÍÍ
  ÍÍ   ÍÍ   ÍÍ   ÍÍ     ÍÍ      ÍÍ ÍÍ     ÍÍ        ÍÍ      ÍÍ   ÍÍ
  ÍÍ   ÍÍ   ÍÍ   ÍÍ     ÍÍ       ÍÍÍ     ÍÍÍÍÍÍ    ÍÍ       ÍÍ   ÍÍ


            A N T i V i r u s 2 9 A   b y   H E X / 2 9 A

                         (C) Copyright 1988














        This is Version 2.0 and it is the first upgrade of ANTV29A.  The
program is written to be compatible with clone BIOSs and PC-DOS 3.xx. An
MS-DOS  version is also  available upon  your request.  I would  like to
thank  all the  people who  sent me money for version  1.0.  This  short
program is the first public domain  program I have ever released and has
proven to be far more useful than I ever expected. Enjoy it !

                                                                 HEX/29A



                             ANTiVirus29A
                             ÄÄÄÄÄÄÄÄÄÄÄÄ

PROGRAM
ÍÍÍÍÍÍÍ
     ANTV29A.EXE.


PROGRAMMER
ÍÍÍÍÍÍÍÍÍÍ
     Hex/29A.


DISTRIBUTION
ÍÍÍÍÍÍÍÍÍÍÍÍ
     ANTV29A.EXE is placed in the public domain under the user supported
shareware concept. It is now and will always remain the sole property of
the author. This  program  may  be  freely  distributed  as  long as the
following limitations are adheared to:

        1.  The program and documentation may not be modified.
        2.  The entire documentation file must be included with the
            program.
        3.  The author's copyright notice is not to be removed.
        4.  No fee for the program may be charged outside of a
            reasonable or customary charge for diskette media,
            and/or shipping.
        5.  It may not be packaged or sold in conjuction with any
            other product.



WARRANTY
ÍÍÍÍÍÍÍÍ
     The program  and  documentation  is supplied  as-is and  the author
disclaims  all  warranties,  expressed  or  implied,  including, without
limitation,  the  warranties  of merchantability  and the  warranties of
fitness for any  purpose. The author further  reserves the right to make
changes to the program or documentation without obligation to notify any
person or organization of such changes.



FORMAT
ÍÍÍÍÍÍ
     ANTV29A <Drive>  where drive is the drive letter  { A | B | C | D }
                      containing the PC-DOS to be checked.

     ANTV29A <0>.



TARGET FILES
ÍÍÍÍÍÍÍÍÍÍÍÍ
     IBMBIO.COM , IBMDOS.COM , COMMAND.COM , CONFIG.SYS and AUTOEXEC.BAT




                                                                  PAGE 1
                             ANTiVirus29A
                             ÄÄÄÄÄÄÄÄÄÄÄÄ

PURPOSE
ÍÍÍÍÍÍÍ
     ANTV29A <Drive>  will check  its five  target files  and detect any
alteration to their SIZE,  DATE/TIME of creation and  CHECKSUM since the
last time it ran. It was developed to verify that no virus has installed
itself in PC-DOS.

     ANTV29A <0> will set the attribute byte of its target files to NORM
This will  enable the user to list/edit all  the target files as some of
them are HIDDEN and/or READ ONLY.



HOW IT WORKS
ÍÍÍÍÍÍÍÍÍÍÍÍ
     ANTV29A <Drive>  will search  the root  directory of the designated
drive  for its  target files.  It will  detect their  SIZE, DATE/TIME of
creation and CHECKSUM  and compare those  values with the ones stored in
its data file  ANTV29A.OFI . When the comparisons end,  it will give its
report.  If there are  any mismatches between the two sets of data (data
in ANTV29A.OFI  and the values just detected) a warning  message will be
given: The filename and the set of data mismatched will be reported (e.g
®DATE/TIME¯  ®CHECKSUM¯  ®SIZE¯ error in file  x:\filename). A series of
recomended  actions  will  follow this  initial warning message.  At the
users  request,  the newly  detected values can  replace the ones in the
data file ANTV29A.OFI in case the user had made any changes to that file
An option  to just  abort the program  without saving  the new values is
also provided.  If the data file doesn't exist,  it will be automaticaly
created in  the root directory of  the designated  drive and  the values
just detected will be stored in it (first time run).

     ANTV29A <0>  will prompt the user for a drive.  It will then search
the root  directory of that drive for its target files and  change their
attribute byte to NORM.



FILE ATTRIBUTE
ÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
     When ANTV29A <Drive> is run, the attribute byte of its target files
will be set as follows regardless of their previous setting.

            IBMBIO.COM ÄÄ¿
                         ³=> Hidden, System, Read Only.
            IBMDOS.COM ÄÄÙ


            COMMAND.COM   => Read Only.


            CONFIG.SYS ÄÄ¿
                         ³=> Norm.
            AUTOEXEC.BAT Ù



                                                                  PAGE 2
                             ANTiVirus29A
                             ÄÄÄÄÄÄÄÄÄÄÄÄ
MISSING FILES
ÍÍÍÍÍÍÍÍÍÍÍÍÍ
     If any of the five  target files are missing  (e.g. CONFIG.SYS) the
ANTV29A <Drive>  will set the missing file's SIZE, DATE/TIME of creation
and CHECKSUM to zero and save those values in the data file. The name of
the missing file(s) will be reported.  If all five files are missing the
program will abort.  If a missing  file is later added  by the user or a
virus the program will produce a ®DATE/TIME¯ ®CHECKSUM¯ and ®SIZE¯ error
for that file.  This is perfectly normal since the missing file had zero
as a value  for all three checks.  When it was  added  those  values had
changed.

INSTALATION
ÍÍÍÍÍÍÍÍÍÍÍ
     I  would  recommend  putting  the  command  ANTV29A <DRIVE> in your
AUTOEXEC.BAT so it's data file ANTV29A.OFI is kept current.  If you have
some  kind  of LOGOFF.BAT,  it will also  be a good idea to put the same
command there too.  The program has an  average run time of 1.71 seconds
and it  will not increase  your  boot or logoff time much.  On the other
hand, if during your last session on your computer you had changed, lets
say, the AUTOEXEC.BAT or CONFIG.SYS file, the data file ANTV29A.OFI will
be updated when you logoff (ANTV29A will report the changes in the files
you changed)  and you will not panic the next  time you boot and receive
the error  message if  you have  forgotten  about the  changes you  made.
Believe me...I speak from experience.

WARNINGS & ERRORS
ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
     1. ROOT DIRECTORY OF x: DOES NOT CONTAIN THE TARGET FILES.
     2. FILE NOT FOUND: x:\filename. FILE DOES NOT EXIST.
     3. ®DATE/TIME¯ ®CHECKSUM¯ ®SIZE¯ ERROR IN FILE x:\FileName.
     4. POSSIBLE VIRUS DETECTION.
         .
         . (Recomended actions)
         .
        DO YOU WANT TO SAVE THE NEW VALUES (Y/N) ?
     5. EXISTING FILES ARE UNCHANGED SINCE THE LAST TIME ANTV29A RAN.
     6. ATTRIBUTE SUB-PROGRAM INVOKED.
     7. ALL TARGET FILES ATTRIBUTE BYTE IN DRIVE x: HAS BEEN SET TO NORM
     8. DRIVE x: NOT SUPPORTED.
     9. ANTV29A.OFI DATA FILE CREATED.
    10. ANTV29A.OFI DATA FILE UPDATED.
    11. CORRUPTED ANTV29A.OFI DATA FILE.
    12. WRITE PROTECTED DISK OR DISK NOT PRESENT IN DRIVE x:
    13. yy BYTES LEFT ON DRIVE x:. NOT ENOUGH  SPACE  TO WRITE DATA FILE
                                   ANTV29A.OFI

CONTRIBUTION
ÍÍÍÍÍÍÍÍÍÍÍÍ
      If you have received this program from another user or download it
from your local BBS and find it  of value, your  $ 5  contribution  will
be appreciated.

                         Ioannis Hadjiioannou
                             c/o Bonn Inc.
                           5-31 50th Avenue
                           L.I.C., NY 11101
                                                                  PAGE 3