Command QDR                                                Version 3.2b
 -----------                                                Oct 24, 1987


 Purpose
 -------
        Re-format a floppy  disk quickly,  optionally  with a new  volume
        label, thus deleting all files and sub-directories on a diskette.

 Format
 ------
                QDR [d:][label]  [/F] [/N] [/V] [/B] [/Q]
                                 [/1] [/2] [/3] [/4] [/8]

 Remarks
 -------
        The d: parameter is required and it  supplies  the drive letter.
        A fixed disk  can not  be re-formatted.

        You may supply a volume label (up to 11 characters)  immediately
        following the drive letter.  For example:

                QDR b:scratch

        Use the /F option to force a full format of all tracks.  The /1,
|       /2, /3, /4, and /8 options apply to a full format,  and  specify
|       the disk type.

        Bad clusters remain marked as bad unless a full format is
        used, then clusters are marked as unusable if they can not be
        formatted.  Use the /V (verbose) option to receive a display of
        the cluster numbers that are marked as not usable.

        The /N option suppresses  the "press ENTER to  continue" prompt.
        Otherwise, press  the enter  key to  reformat the  disk, or  the
        ESCape key to cancel.

        The DOS error level is set to 0 for successful completion, or to
        1 if any errors occur.















        QDR (c) Copyright Vernon D. Buerg 1986,87. All rights reserved.



 Command QDR                                                Version 3.2b
 -----------                                                Oct 24, 1987

                        Options
                        -------

        /F - forced format; uses DOS to format and verify each track

        /1 - forces single sided format, SSSD/8 or SSSD/9, on 360 kb drives
|       /2 - forces DSHD format on 1440 kb capacity drives
        /3 - forces DSQD format on 720 kb capacity drives
|       /4 - forces DSDD format on 1.2 mb capacity drives
        /8 - forces 8-sector format, SSSD/8 or DSDD/8, on 360 kb drives

        /N - no prompt; skips the "Press ENTER" message and reply

        /V - verbose messages; displays a message for each cluster
             that is marked as unusable

|       /B - use disk BIOS routines only for formatting; if omitted,
|            the DOS routines used for formatting are determined by the
|            version of DOS in use. This option is supplied as an
|            alternative to the default because QDR may not be able
|            to format a new diskette when certain device drivers or
|            versions of DOS are installed.

|       /Q - quick format without verification or bad track marking.
|            If the target disk has bad spots, write errors may result.
|            This option is NOT recommended for formatting new
|            diskettes.



                         Formatting
                         ----------

        To perform a full format of a disk sectors, use the /F  options.
        It is recommended that you use DOS FORMAT since QDR is not  much
        faster when doing a full format.  Both mark bad clusters.

        You may suppy /1 to force  SSSD format, /4 for DSQD (1.2mb),  or
        /3 for DSQD (720kb), or /8 for eight-sectors (SSSD or DSDD).

        Unless /F is used, the diskette must have been previously
        formatted.  The allowable diskette formats are:  DSQD (1.2mb or
        720kb), SSSD/8, SSSD/9, DSDD/8, DSDD/9, and DSHD (1.44 mb).
        When information is available for other drive types, they will
        be added to the data in the internal device table.  Your system
        hardware and software must support the device type.


 Command QDR                                                Version 3.2b
 -----------                                                Oct 24, 1987

                         Examples
                         --------

     o  Reformat a previously formatted and used diskette. Write a
        volume label of SCRATCH:

                QDR A:scratch

     o  Alternately format new diskettes in drives A and B.
        First, create a BAT file called TWOFOR.BAT with these commands:

                QDR A: /F/N
                QDR B: /F/N
                TWOFOR

        Then, issue the command TWOFOR. When the last diskette has been
        formatted, press ctrl-C to abort the program.


                         Version history
                         ---------------

        Version 1.0, 2/28/86
          -  initial release

        Version 2.7, 2/4/87
          -  update boot sector with device  constant when  using /f  to
             format, should correct problems  with 3.5  inch dsqd  drive
          -  correct  initialization of  fat (not marking  bad clusters)
             when using /f

        Version 2.8, 2/5/87
          -  correct marking of fat for side 2
          -  improve format verification, set retries to 2
          -  add operator action request for drive not ready  or if disk
             is write protected

        Version 2.9, 3/20/87
          -  minor correction for /3 (dsqd) formatting

|       Version 3.2, 10/24/87
|         - change meaning of /4; the default format is now the
|           highest density for the drive.
|         - allow formatting of drives under DOS 3.2 (and later?),
|           and new formats 3.5/720kb and 3.5/1440kb.


                         Restrictions
                         ------------

        QDR (c) Copyright Vernon D. Buerg 1986,87. All rights reserved.

        May be copied  and distributed in  its original form  only.  For
        private, personal use.  May  not  be  sold  or rented.  Use this
        program at your own risk. No warranty is given and no  liability
        is assumed.