PARK -- A new routine to park the heads of one or both fixed disks

The heads of fixed disks should be left in the parked position
whenever the drive is not in use, so that if the machine is jarred
or the power is dropped, the heads will land on an unused portion
of the platter.  IBM provides a way to do this, but only in
the DIAGNOSTICS diskette (under PREPARE SYSTEM FOR RELOCATION).

Several BBSs have had PARK routines available for download, but
universally they handle only one hard disk and universally the
cylinder number at which the disk heads should be parked is hard-coded
in the program.

This PARK.COM routine determines, for either or both hard disks,
where to park the heads (by trying ever-higher cylinders until it
finds a cylinder number to which the disk cannot move), and leaves
the heads there.  It does it separately for the first and second
drives, so that it is usable even in systems that have two dissimilar
hard disks.

The files are:  PARK.DOC       this DOC file
                PARK.COM       the executable module, obtained
                               by processing PARK.ASM with the
                               MASM, LINK, and EXE2BIN programs.

                Carl Hayes (SYSOP, NN5I BBS, 214-960-2730)