Kyoto Common Lisp Report

                      Taiichi Yuasa and Masami Hagiya

      Research Institute for Mathematical Sciences, Kyoto University

         Copyright (c) 1985 by the authors.  All rights reserved.




                                  Preface

Kyoto Common Lisp (KCL for short) is a full implementation of the Common
Lisp language described in the Common Lisp Reference Manual:


               Common Lisp: The Language.
               by Guy L. Steele et al.
               Digital Press, 1984

All Common Lisp functions, macros, and special forms are defined in KCL,
though a few of them have slightly different meanings from those described
in the Common Lisp Reference Manual.  All such differences are described in
this report:  If a Common Lisp function (or macro or special form) does not
work as described in the Common Lisp Reference Manual and if this report
does not describe the difference explicitly, then there must be a bug in
KCL.  All Common Lisp variables and constants are defined in KCL exactly as
described in the Common Lisp Reference Manual.

     Currently, there are four major versions of KCL:

        1. KCL/AOS, under the AOS/VS operating system for
           Data General's ECLIPSE MV series machines.

        2. KCL/VAX, under the Unix 4.2 bsd operating system for
           Digital Equipment Corporation's VAX 11 series machines.

        3. KCL/SUN, under the Unix 4.2 bsd operating system for
           Sun Microsystems' Sun Workstation.

        4. KCL/UST, under the Unix V (Uniplus' version)
           operating system for Sumitomo Electric Industries and
           Digital Computer Laboratory's Ustation E15.

KCL/AOS is the original version of KCL, which was developed at the Research
Institute for Mathematical Sciences (RIMS), Kyoto University, with the
cooperation of Nippon Data General Corporation.  The other three versions,
which are collectively called KCL on Unix, are transplanted versions of
KCL/AOS.

     This report is intended to complement the Common Lisp Reference
Manual.  This report describes deviations of KCL from Common Lisp, those
features specific to KCL, and the implementation-dependent functions of
Common Lisp.




                      Acknowledgements


The project of KCL was supported by many people affiliated with many
institutions.  We are very grateful especially to the following people for
their contributions to the KCL project.

     First of all, we are grateful to the contributors to the design of
Common Lisp.

     Prof. Reiji Nakajima at RIMS, Kyoto University, provided us with
considerable encouragement and moral support.

     Nippon Data General Corporation (NDG) helped us implement KCL/AOS.
Mr. Teruo Yabe and Mr. Toshiyasu Harada joined us during the first stage of
the KCL project and did a lot of coding.  Mr. Takashi Suzuki and Mr. Kibo
Kurokawa arranged the joint project.  NDG is now supporting the
distribution of KCL/AOS.

     Data General Corporation in the United States sent us materials
necessary to implement a Common Lisp system, such as the preliminary drafts
of the Common Lisp reference manual and benchmark tests for Common Lisp.

 For the benchmark tests we are indebted to Dr. Richard Gabriel at
Stanford University.

     Dr. Daniel Weinreb at Symbolics answered most of our questions about
the language specification.  He also sent us the definition of r a t i o n
a l i z e written by Dr. Skef Wholey at CMU.  We use this definition in KCL
without any change.

     Dr. Carl Hoffman at Symbolics checked the top-level of KCL and gave us
advice for improving KCL.  He also found some bugs in KCL and fixed them
for us.

     Mr. Naruhiko Kawamura at RIMS developed a Prolog system using the
earliest version of KCL/AOS.  That was one of the first big projects with
KCL and he found many bugs.

     Mr. Takashi Sakuragawa at RIMS hacked with KCL/AOS and gave us much
advice concerning those features specific to KCL.

     Mr. Tatsuya Hagino at Edinburgh University developed Micro EMACS on
which FeCl2, the full-screen editor embedded in KCL/AOS, is based.

     Mr. Kunihiko Nakamura at Kagawa University converted the assembly
language version of Micro EMACS into the C language, which happened to
become the prototype of FeCl2.

     Prof. Akinori Yonezawa at Tokyo Institute of Technology encouraged us
to port KCL/AOS to the VAX 11.

     Mr. Etsuya Shibayama at Tokyo Institute of Technology helped us while
we were working with the VAX 11 at the Institute.

     Hagiwara Laboratory at Kyoto University offered (and is offering)
their VAX 11 for finishing transplantation and maintaining KCL/VAX.  We got
also technical advice from people at Hagiwara Laboratory.

     Prof. Shuji Doshita at Kyoto University offered the SUN Workstation at
his Laboratory and gave us a lot of advice for transplantation to the SUN
Workstation.

     Mr. Takashi Hattori at RIMS gave us useful information about the
Motorola 68000, the CPU chip of SUN Workstation.

     NDG helped us build up the KROFF (K yoto ROFF) system, with which this
report was produced.  They offered the character font sets from which the
font sets used in KROFF were constructed.  We also received some technical
advice from NDG about the output device of KROFF, i.e., NDG's 5880 series
laser beam printers.  Incidentally, all the programs that constitute the
KROFF system, including tools to maintain KROFF font sets, are written in
the Common Lisp language and are running under KCL.





                            Table of Contents


 Preface
 Acknowledgements
 Table of Contents

 Chapter 1. How to Start and End a KCL Session

 Chapter 2. Data Types
          2.1. Numbers
          2.1.1. Integers
          2.1.2. Ratios
          2.1.3. Floating-point Numbers
          2.1.4. Complex Numbers
        2.2. Characters
          2.2.1. Standard Characters
          2.2.2. Line Divisions
          2.2.3. Non-standard Characters
          2.2.4. Character Attributes
          2.2.5. String Characters
        2.3. Symbols
        2.4. Lists and Conses
        2.5. Arrays
          2.5.1. Vectors
          2.5.2. Strings
          2.5.3. Bit-Vectors
        2.6. Hash Tables
        2.7. Readtables
        2.8. Packages
        2.9. Pathnames
        2.10. Streams
        2.11. Random-States
        2.12. Structures
        2.13. Functions
        2.14. Unreadable Data Objects
        2.15. Overlap, Inclusion, and Disjointness of Types

 Chapter 3. Input and Output
        3.1. Read Macros
        3.2. Input and Output Functions

 Chapter 4. Memory Management
        4.1. Implementation Types
        4.2. Heap and Relocatable Areas
        4.3. The Garbage Collector
        4.4. Allocation Functions
        4.5. Storage Information

 Chapter 5. Debugging Facilities
        5.1. The Tracer
        5.2. The Stepper
        5.3. Errors
        5.4. The Break Loop
        5.5. Describe and Inspect

 Chapter 6. The Compiler

 Chapter 7. Declarations
        7.1. Declaration Specifiers
        7.2. Significant Type Specifiers
        7.3. Treatment of Type Declarations
          7.3.1. Variable Allocations
          7.3.2. Built-in Functions that Operate on Raw Data Directly
          7.3.3. Arguments/Values Passing

 Chapter 8. Operating System Interface

 Chapter 9. Macros
        9.1. System Macros
        9.2. Defmacro Lambda-Lists

 Chapter 10. The C Language Interface

 Chapter 11. The Editor

 Appendix A. KCL Summary

 Appendix B. An Overview of Kyoto Common Lisp

 Appendix C. Kyoto Common Lisp Installation Guide
        C.1. Installation of KCL/AOS
        C.2. Installation of KCL/VAX
        C.3. Installation of KCL/SUN
        C.4. Installation of KCL/UST



 

             Chapter 1. How to Start and End a KCL Session


KCL on Unix is invoked by the Shell command  kcl.

        % kcl
        KCL (Kyoto Common Lisp)  July 1, 1987


---------------------- Note to KCL/AOS users ----------------------

KCL/AOS is invoked by the CLI command  KCL.

        ) KCL
        KCL (Kyoto Common Lisp)   July 1, 1987

--------------------------- End of Note ----------------------------


When invoked, KCL will print the banner and initialize the system.
The date in the KCL banner identifies the revision of KCL.  
"July 1, 1987" is the value of the
function   lisp-implementation-version.

     If there exists a file named init.lsp in the current working
directory, KCL successively evaluates the forms in the file, immediately
after the system initialization.  The user may set up his or her own KCL
environment (e.g., the memory configuration) with
init.lsp.

     After the initialization, KCL enters the top-level loop and prints the
prompt '>'.

        >

The prompt indicates that KCL is now ready to receive a form from the
terminal and to evaluate it.

     Usually, the current package (i.e., the value of *package*) is the
user package, and the prompt appears as above.  If, however, the current
package is other than the user package, then the prompt will be prefixed by
the package name.

        package-name>

     To exit from KCL,
call the function  bye (or by).

        >(bye)
        Bye.
        %


---------------------- Note to KCL/AOS users ----------------------

In this report, we sometimes assume that KCL is invoked from the Unix
Shell.  In particular, we use the standard prompt of the Unix Shell '%' in
most examples.

-------------------------- End of Note ----------------------------


Alternatively, you may type ^D (control-D), i.e., press the key D while
pressing down the CNTL key.

        >^DBye.
        %

     The top-level loop of KCL is almost the same as that defined in
Section 20.2 of the Common Lisp Reference Manual.  Since the input from the
terminal is in line mode, each top-level form should be followed by a
newline.  If more than one value is returned by the evaluation of the
top-level form, the values will be printed successively.  If no value is
returned, then nothing will be printed.

        >(values 1 2)
        1
        2

        >(values)
        
        >


     When an error is signalled, control will enter the break loop.

        >(defun foo (x) (bar x))
        foo

        >(defun bar (y) (bee y y))
        bar

        >(foo 'lish)
        Error: The function BEE is undefined.
        Error signalled by BAR.

        Broken at BAR.
        >>

'>>' in the last line is the prompt of the break loop.  Like in the
top-level loop, the prompt will be prefixed by the current package name, if
the current package is other than the user package.

     To go back to the top-level loop, type :q.

        >>:q

        Top level.
        >

See Section 5.4 for the details of the break loop.

     In KCL on Unix, the terminal interrupt (usually caused by typing ^C
(control-C) or by typing DELETE) is a kind of error.  It breaks the running
program and calls the break level loop.

     Example:

        >(defun foo () (do () (nil)))
        foo

        >(foo)
        ^C
        Correctable error: Console interrupt.
        Signalled by DO.

        Broken at FOO.
        >>


---------------------- Note to KCL/AOS users----------------------

In KCL/AOS, the console interrupt caused by typing ^C (control-C) followed
by ^A (control-A) is a kind of error.  Typing ^C and ^A breaks the running
program and calls the break loop.  On the other hand, the console interrupt
caused by ^C and ^B (control-B) will immediately terminate KCL. 

     Example:
        >(defun foo () (do () (nil)))
        foo

        >(foo)
        ^C^A
        Correctable error: Console interrupt.
        Signalled by DO.

        Broken at FOO.
        >>(foo)
        ^C^B
        *ABORT*
        CONSOLE INTERRUPT
        ERROR: FROM PROGRAM
        LEVEL 1
        x,kcl
        )

---------------------------End of Note----------------------------






                     Chapter 2. Data Types


KCL supports all Common Lisp data types exactly as defined in the
Common Lisp Reference Manual.  This chapter simply complements
Chapter 2 of the Common Lisp Reference Manual, by
describing implementation dependent features of Common Lisp data
types.  Each section in this chapter corresponds to the section in Chapter 2
of the Common Lisp Reference Manual, with the same section title.


2.1. Numbers

2.1.1. Integers

     Fixnums in KCL are those integers
in the range -(2 to the power of 31) to
(2 to the power of 31)-1, inclusive.  Other integers are bignums.  
Thus 25 factorial (25!)

    15511210043330985984000000

is certainly a bignum in KCL.

     Common Lisp constants related to integers have the following values
in KCL.

    most-positive-fixnum = 2147483647 = (2 to the power of 31)-1
    most-negative-fixnum = -2147483648 = -(2 to the power of 31)

    boole-1 = 3
    boole-2 = 5
    boole-and = 1
    boole-andc1 = 4
    boole-andc2 = 2
    boole-c1 = 12
    boole-c2 = 10
    boole-clr = 0
    boole-eqv = 9
    boole-ior = 7
    boole-nand = 14
    boole-nor = 8
    boole-orc1 = 13
    boole-orc2 = 11
    boole-set = 15
    boole-xor = 6

See Chapter 12 of the Common Lisp Reference Manual for their
meanings.


2.1.2. Ratios

There are no implementation-dependent features for ratios.


2.1.3. Floating-Point Numbers

KCL provides two distinct internal floating-point formats.  One format
is short; the other is single and serves also as double and
long.  The data types single-float, double-float, and long-float
are considered to be identical, but short-float is distinct. 
An expression such as (eql 1.0s0 1.0d0) is false, but
(eql 1.0f0 1.0d0) is true.  Similarly,
(typep 1.0L0 'short-float) is false, but
(typep 1.0L0 'single-float) is true.  For output purposes all
floating-point numbers are assumed to be of short
or single format.

     The floating-point precisions are:

    Format      KCL/AOS         KCL/VAX KCL/SUN         KCL/UST
    ----------------------------------------------------------------
    Short       24 bits         23 bits         24 bits         24 bits
    Single      56 bits         55 bits         53 bits         53 bits
    Double      56 bits         55 bits         53 bits         53 bits
    Long        56 bits         55 bits         53 bits         53 bits

The floating-point exponent sizes are:

    Format      KCL/AOS         KCL/VAX KCL/SUN         KCL/UST
    ----------------------------------------------------------------
    Short       7 bits          8 bits          8 bits          8 bits
    Single      7 bits          8 bits          11 bits         11 bits
    Double      7 bits          8 bits          11 bits         11 bits
    Long        7 bits          8 bits          11 bits         11 bits

There is no "minus zero."  (eql 0.0 -0.0) is true.

     Common Lisp constants related to floating-point numbers have the
following values in KCL.

    most-positive-short-float
      = - most-negative-short-float
      = 7.237005s75 (KCL/AOS)
        1.701412s38 (KCL/VAX)
        3.402823s38 (KCL/SUN and KCL/UST)

    least-positive-short-float
      = - least-negative-short-float
      = 5.397605s-79 (KCL/AOS)
        2.938736s-39 (KCL/VAX)
        1.401298s-45 (KCL/SUN and KCL/UST)

    most-positive-long-float
      = most-positive-double-float
      = most-positive-single-float
      = - most-negative-long-float
      = - most-negative-double-float
      = - most-negative-single-float
      = 7.237005577332264f75 (KCL/AOS)
        1.701411834604692f38 (KCL/VAX)
        1.797693134862315f308 (KCL/SUN and KCL/UST)

    least-positive-long-float
      = least-positive-double-float
      = least-positive-single-float
      = - least-negative-long-float
      = - least-negative-double-flo
      = - least-negative-single-float
      = 5.397605346934027f-79 (KCL/AOS)
        2.938735877055719f-39 (KCL/VAX)
        4.940656458412469f-324 (KCL/SUN and KCL/UST)

    short-float-epsilon
      = 4.468372s-7 (KCL/AOS)
        6.938894s-18 (KCL/VAX)
        2.980232s-8 (KCL/SUN and KCL/UST)

    short-float-negative-epsilon
      = 2.980232s-8 (KCL/AOS)
        6.938894s-18 (KCL/VAX)
        2.980232s-8 (KCL/SUN and KCL/UST)

    long-float-epsilon
      = double-float-epsilon
      = single-float-epsilon
      = 1.110223024625157f-16 (KCL/AOS)
        6.938893903907228f-18 (KCL/VAX)
        5.5511151231257827f-17 (KCL/SUN and KCL/UST)

    long-float-negative-epsilon
      = double-float-negative-epsilon
      = single-float-negative-epsilon
      = 6.938893903907228f-18 (KCL/AOS)
        6.938893903907228f-18 (KCL/VAX)
        5.5511151231257827f-17 (KCL/SUN and KCL/UST)

    pi = 3.141592653589793

See Chapter 12 of the Common Lisp Reference Manual for their meanings.


2.1.4. Complex Numbers

There are no implementation-dependent features for complex numbers.

2.2. Characters

2.2.1. Standard Characters

KCL supports all standard and semi-standard characters listed in Section
2.2.1 of the Common Lisp Reference Manual.  Non-printing characters have
the following character codes.

    Character           Code (in octal)
    --------------------------------
    #\Space             040
    #\Newline           012
    #\Backspace 010
    #\Tab               011
    #\Linefeed          012
    #\Page              014
    #\Return            015
    #\Rubout            177

Note that #\Linefeed is synonymous with #\Newline and
thus is a member of standard-char.  Other semi-standard characters
are not members of standard-char.


---------------------- Note to KCL/AOS users----------------------

KCL/AOS uses 025 (in octal) as the character code of #\Backspace.

---------------------------End of Note----------------------------



2.2.2. Line Divisions

Since KCL represents the #\Newline character by a single code 12, problems
with line divisions discussed in Section 2.2.2 of the Common Lisp Reference
Manual cause no problem in KCL.


2.2.3. Non-standard Characters

KCL supports no additional non-standard characters.

2.2.4. Character Attributes

The bit and font fields of KCL characters are always 0.

     Common Lisp constants related to characters
have the following values in KCL.

    char-bits-limit = 1 
    char-code-limit = 256 
    char-control-bit = 0 
    char-font-limit = 1 
    char-hyper-bit = 0 
    char-meta-bit = 0 
    char-super-bit = 0 

See Chapter 13 of the Common Lisp Reference Manual for their meanings.


2.2.5. String Characters

Since the bit and font fields of KCL characters are always 0, string-char
is considered to be identical to character.


2.3. Symbols

The print name of a symbol may consist of up to 16777216 (i.e., the value
of array-total-size-limit) characters.  However, when a symbol is read, the
number of characters (not counting escape characters) in the print name is
limited to 2048.


2.4. Lists and Conses

There are no implementation-dependent features for lists and conses.


2.5. Arrays

     KCL arrays can have up to 64 ranks.

     When the value of the Common Lisp variable *print-array* (see Section
22.1.6 of the Common Lisp Reference Manual) is nil, then bit-vectors are
printed as #<a bit-vector>, other vectors are printed as #<a vector>, and
other arrays are printed as #<an array>.

     Common Lisp constants related to arrays have the following values in
KCL.

    array-dimension-limit = 16777216
    array-rank-limit = 64 
    array-total-size-limit = 16777216 

See Section 17.1 of the Common Lisp Reference Manual for their meanings.


2.5.1. Vectors

In KCL, array elements are represented in one of six ways depending on the
type of the array.

Array Type                                      Element Representation

---------------------------------------------------------------
 (array t) and (vector t)                       a cell pointer
 (array fixnum) and (vector fixnum)             32 bit signed 
                                                integer
 (array string-char) and string                 8 bit code
 (array short-float) and (vector short-float)   32 bit
                                                floating point
 (array long-float) and (vector long-float)     64 bit floating point
 (array bit) and bit-vector                     1 bit bit


2.5.2. Strings

A string may consists of up to 16777216 (i.e., the value of
array-total-size-limit) characters.  However, when a string is read, the
number of characters (not counting escape characters) in the string is
limited to 2048.


2.5.3. Bit-Vectors

There are no implementation-dependent features for bit-vectors.


2.6. Hash Tables

All hash tables are printed as #<a hash-table>.


2.7. Readtables

All readtables are printed as #<a readtable>.


2.8. Packages

     The following packages are built into KCL.

    lisp  user  keyword  system  compiler

The compiler package contains symbols used by the KCL compiler.  Other
packages are described in Section 11.6 of the Common Lisp Reference Manual.
The system package has two nicknames sys and si; system:symbol may be
written as sys:symbol or si:symbol.  Other packages have no nicknames.

     Packages are printed as #<package-name package>.


2.9. Pathnames

     KCL provides a # macro #" that reads a pathname:  #"string" is
equivalent to (pathname "string").  For example,

        #"foo.lsp"

is equivalent to

        (pathname "foo.lsp").

The same format is used when a pathname is printed.

     The initial value of the Common Lisp variable 
*default-pathname-defaults* is #"" (or, equivalently, (pathname "")).

     A pathname in the file system of Common Lisp consists of the following
six elements:

        host  device  directory  name  type  version

Among these elements, KCL does not use host, device, and version.  That is,
when converting a namestring into a pathname, KCL turns these three
elements into nil.  Conversely, when converting a pathname into a
namestring, KCL ignores these three elements.

     In the sequel, we explain how KCL converts a namestring into
a pathname.

     If a namestring contains one or more periods '.', the last 
period separates the namestring into the file name and the filetype.

        "foo.lsp"
                name:           "foo"
                type:           "lsp"

        "a.b.c"
                name:           "a.b"
                type:           "c"

If a namestring ends with a period, the filetype becomes the null string.

        "foo."
                name:           "foo"
                type:           "" (null string)

If a namestring begins with a period, the file name becomes nil.

        ".lsp"
                name:           nil
                type:           "lsp"

If a namestring contains no period, the filetype is nil.

        "foo"
                name:           "foo"
                type:           nil

In a pathname, the file directory is represented as a list.

        "common/demo/foo.lsp"
                directory:      ("common" "demo")
                name:           "foo"
                type:           "lsp"

If a namestring does not contain a directory, the directory component of
the pathname is nil.

        "foo.lsp"
                directory:      nil
                name:           "foo"
                type:           "lsp"

In a pathname, the root directory is represented by the keyword :root.

        "/usr/common/foo.lsp"
                directory:       (:root "usr" "common")
                name:           "foo"
                type:           "lsp"

The abbreviation symbols '.' and '..' may be used in a namestring.

        "./demo/queen.lsp"
                directory:      (:current  "demo")
                name:           "queen"
                type:           "lsp"

        "../../demo/queen.lsp"
                directory:      (:parent :parent "demo")
                name:           "queen"
                type:           "lsp"

:current and :parent represent the current directory and the parent
directory, respectively.

    The part of a namestring after the last slash '/' is always regarded as
representing the file name and the filetype.  In order to represent a
pathname with both the name and the filetype nil, end the pathname with a
slash.

        "/usr/common/"
                directory:      (:root "usr" "common")
                name:           nil
                type:           nil

        "/usr/common/.lsp"
                directory:      (:root "usr" "common")
                name:           nil
                type:           "lsp"

'*' in the place of file name or filetype becomes :wild.

        "*.lsp"
                name:           :wild
                type:           "lsp"

        "foo.*"
                name:           "foo"
                type:           :wild


----------------------Note to KCL/AOS users----------------------

In KCL/AOS, all the lower-case letters are turned into upper-case letters
by pathname conversions.  Thus, for example,

        "foo.lsp"
                name:           "FOO"
                type:           "LSP"

KCL/AOS follows the convention of the AOS/VS file system:  The symbols
'/',  '.',  '..', and '*'  in the examples above should be replaced by
':',  '=',  '^', and '-', respectively, in KCL/AOS.

---------------------------End of Note----------------------------



2.10. Streams

Streams are printed in the following formats.

 #<input stream file-name>
     An input stream from the file file-name.

 #<output stream file-name>
     An output stream to the file file-name.

 #<string-input stream from string>
     An input stream generated by (make-string-input-stream 
string).


 #<a string-output stream>
     An output stream generated by the function
 make-string-output-stream

 #<a two-way stream>
     A stream generated by the function make-two-way-stream.

 #<an echo stream>
     A bidirectional stream generated by the function
 make-echo-stream.

 #<synonym stream to symbol>
     The stream generated by (make-synonym-stream symbol)

 #<a concatenated stream>
     An input stream generated by the function make-concatenated-stream.

 #<a broadcast stream>
     An output stream generated by the function
 make-broadcast-stream.


2.11. Random-States

KCL provides a # macro '#$' that reads a random state.  #$integer is
equivalent to (make-random-state integer).  The same format is used when a
random state is printed.


2.12. Structures

There are no implementation-dependent features for structures.


2.13. Functions

An interpreted function (including macro expansion functions) is
represented in one of the following formats.

(lambda lambda-list . body)

     A lambda-expression with null lexical environment and with no implicit
block around it.  This type of function typically appears when '(lambda
lambda-list . body) is evaluated.


(lambda-block block-name lambda-list . body)

     A lambda-expression with null lexical environment but with an implicit
block around it.  This type of function typically appears when (defun
function-name lambda-list . body) is evaluated.  In this case, block-name
is identical to function-name.


(lambda-closure env1 env2 env3 lambda-list . body)

     A lambda-expression with lexical environments but with no implicit
block around it.  This type of function typically appears when #'(lambda
lambda-list) . body) (or, equivalently, (function (lambda lambda-list .
body)) ) is evaluated.  env1, env2, and env3 represent the variable
bindings, the local function/macro definitions, and the tag/block-name
establishments, respectively, at the time the closure was created.


(lambda-block-closure env1 env2 env3 block-name lambda-list . body)

     A lambda-expression with lexical environments and with an implicit
block around it.  Local functions and local macros are represented in this
format.  env1, env2, and env3 represent the variable bindings, the local
function/macro bindings, and the tag/block-name establishments,
respectively, at the time the local function/macro was created by flet,
labels, or macrolet.  The block-name is identical to the local
function/macro name.

     Compiled functions (including compiled macro-expansion
functions) are printed in the following formats.

    #<compiled-function name>
 or
    #<compiled-closure nil>

Incidentally, the value of
 (symbol-function special-form-name) is a list,

    (special . address)

if special-form-name names a special form.

     Common Lisp constants related to functions have the following values
in KCL.

    call-arguments-limit = 64 
    lambda-list-keywords = (&optional &rest &key &allow-other-keys &aux
                            &whole &environment &body)
                            
    lambda-parameters-limit = 64 
    multiple-values-limit = 32 

Refer to the Common Lisp Reference Manual for their meanings.


2.14. Unreadable Data Objects

There are no implementation-dependent features for unreadable data objects.

2.15. Overlap, Inclusion, and Disjointness of Types

In KCL, the types number and array are certainly subtypes of common, since
KCL does not extend the set of objects of these types.





                    Chapter 3. Input and Output



3.1. Read Macros

     The following # macros are introduced in KCL.

        #"      #"string" reads a pathname.
                #"string" is equivalent to
                (pathname "string").

        #$      #$integer reads a random state.
                #$integer is equivalent to
                (make-random-state integer).

     The # macro '#,' works as described in the Common Lisp Reference
Manual, only if it is included in a constant object.  The forms immediately
after '#,' below will be evaluated when the compiled code is loaded.

        '#,x
        '(a b c (d #,e f) g)
        #(1 2 3 #,(+ a b c) 5 6)
        #C(0.0 #,(exp 1))

Otherwise, the effect of using '#,' is unpredictable.  Note that, when
interpreted code is loaded, '#,' has the same effect as the # macro '#.'.


3.2. Input and Output Functions

The input and output functions of KCL almost follow the definitions in
Chapter 22 of the Common Lisp Reference Manual.  Most of the differences
come from the fact that, in KCL, input from the terminal is always in line
mode and binary I/O is not supported.

     In KCL, *terminal-io* is a two-way stream from the standard input and
to the standard output.  The echoing to the terminal is performed by the
underlying operating system.  In particular, when a disk file is assigned
to the standard output, nothing will be echoed at the terminal.

     Those functions that deviate from the definitions in the Common Lisp
Reference Manual are listed below.


load pathname &key :print :verbose :if-does-not-exist [Function] 

If pathname does not specify the filetype of the input file, then load
first tries to load a file with the filetype .o, i.e., the fasl file (see
Chapter 6).  If it fails, then load tries to load a file with the filetype
.lsp.  KCL assumes that .lsp is the standard filetype for source files.  If
it fails again, then load will load the specified file with no filetype.

load recognizes a file as a fasl file if and only if the filetype of the
file is .o.  Other files are assumed to be source files.


----------------------Note to KCL/AOS users----------------------

In KCL/AOS, the filetype of fasl files is .fasl (see Chapter 6).
Therefore, if the pathname argument does not explicitly specify the
filetype, load first tries to load a file with the filetype
.fasl.  In addition, load recognizes a file as a fasl file if and
only if the filetype of the file is .fasl.

---------------------------End of Note----------------------------



open                                                        [Function]

  The argument to the keyword variable :element-type is ignored and
  :element-type is always bound to the value string-char.


close                                                        [Function]

  The keyword variable :abort is always ignored.


listen                                                       [Function]

  listen always returns t.


read-char-no-hang                                            [Function]

  read-char-no-hang is equivalent to read-char.


clear-input                                                  [Function]

clear-output                                                 [Function]

  clear-input and clear-output simply return nil without doing anything.


read-byte                                                    [Function]

write-byte                                                   [Function]

  These functions may operate on any stream.  They read or write a byte (8
  bits) at a time.


princ                                                        [Function]
write-char                                                   [Function]
write-byte                                                   [Function]

  These functions do not always flush the stream.  The stream is flushed when

  1. a newline character is written, or

  2. the input from the terminal is requested in the case that these
  functions operate on *terminal-io*.






                       Chapter 4. Memory Management



4.1. Implementation Types

Each KCL object belongs to one of the 22 implementation types.  The
implementation types are shown in Table 4-1 with the corresponding Common
Lisp data types.  In the table, the compiled functions are divided into two
implementation types; cfun is the type of compiled functions without
environment, and cclosure is the type of compiled functions with
environment (i.e., the type of compiled closures).  spice is the type of
internal data used by KCL, and does not correspond to any Common Lisp data
type.

                Table 4-1  Implementation Types

        Implementation Type     Common Lisp Data Type
        ----------------------------------------------------------------
        cons                    cons
        fixnum                  fixnum
        bignum                  bignum
        ratio                   ratio
        short-float             short-float
        long-float              long-float (= double-float = single-float)
        complex                 complex
        character               character
        symbol                  symbol
        package                 package
        hash-table              hash-table
        array                   (and array (not vector))
        vector                  (and vector (not string) (not bit-vector))
        string                  string
        bit-vector              bit-vector
        structure               structure
        stream                  stream
        random-state            random-state
        readtable               readtable
        cfun                    compiled-function without environment
        cclosure                compiled-function with environment
        spice                   none


     Each object is represented by a cell allocated in the heap area of the
interpreter.  The size of the cell is determined by the implementation type
of the object.

     The implementation types are classified according to the size of the
cells for the objects of the type, as shown in Table 4-2.  The size of the
cells in the same type class is the same.

                Table 4-2  Classification of Implementation Types

        Class   Implementation Types    
----------------------------------------------------------------
            1   cons bignum ratio long-float complex
            2   fixnum short-float character random-state readtable 
                 spice
            3   symbol package
            4   array hash-table vector bit-vector stream pathname 
                 cclosure
            5   string cfun
            6   structure


     For objects of the (implementation) types readtable, symbol, package,
array, hash-table, vector, bit-vector, stream, cclosure, string, cfun, and
structure, the cell is simply a header of the object.  The body of the
object is allocated separately from the cell and is managed in a different
manner.  The memory space occupied by the body of such an object is called
a block.  A block is either contiguous or relocatable depending on the area
in which it is allocated.  The difference between the two areas will be
explained below.  Table 4-3 lists these types, along with the contents of
the body and the kind of the block.

                Table 4-3  Types with Bodies

        Type            Body                    Block
        -----------------------------------------------------------
        readtable       read table              contiguous
        symbol          symbol name             relocatable
        package         hash table              contiguous
        array           array body              relocatable or 
                                                              contiguous
        hash-table      hash table              relocatable
        vector          vector body             relocatable or
                                                               contiguous
        bit-vector      bit-vector body         relocatable or 
                                                                contiguous
        stream          I/O buffer              contiguous
        cclosure        code                    contiguous
        string          string body             relocatable or
                                                              contiguous
        cfun            code                    contiguous
        structure       structure body          relocatable


     Usually, the body of an array, a vector, a bit-vector, or a string is
allocated as a relocatable block.  In KCL, the function make-array takes an
extra keyword argument :static.  If the :static argument is supplied with a
non-nil value, then the body of the array is allocated as a contiguous
block.


4.2. Heap and Relocatable Areas

    The memory space of KCL is divided into two parts:  the heap area and
the relocatable area.  Both areas occupy a contiguous space in the memory.

     Cells of KCL objects are allocated in the heap.  KCL divides the heap
into pages (1 page = 2048 bytes), and each page consists of cells in the
same type class (see Table 4-2).  Cells in different type classes are
allocated in different pages.  Some blocks are also allocated in the heap:
They are called contiguous blocks.  The pages for contiguous blocks contain
only contiguous blocks.  Thus each page in the heap is either a page for
cells in a particular type class, or a page for contiguous blocks.  Blocks
not in the heap are called relocatable blocks and are allocated in the
relocatable area.

     The user may specify the maximum number of pages that can be allocated
for each type class by calling the KCL specific function allocate.  There
is also a limit on the number of pages for contiguous blocks; the limit can
be altered by calling the KCL specific function allocate-contiguous-pages.
The size of the relocatable area is specified by the KCL specific function
allocate-relocatable-pages.  See Section 4.4 for these functions.

     In some installations of KCL, the total amount of memory that KCL can
use is limited.  In such cases, the entire memory may become exhausted
before the maximum number of pages for each type class, for contiguous
blocks, or for the relocatable area have been allocated.

     The heap lies in a part of memory with lower address than the
relocatable area and there is a "hole" between the two areas (see Figure
4-1).  On request for a new page of heap, the page with the lowest address
in the hole is used.  When the hole is exhausted, the relocatable area is
shifted toward the higher address space and a new hole of an appropriate
size is created between the two areas.

                Figure 1  Heap and Relocatable Area

     lower address                                  higher address
        ---------------------- - - - 2-------------------
        |        heap        | hole  | relocatable area |
        7--------------------- - - - 8------------------9



4.3. The Garbage Collector

The garbage collector of KCL has three levels according to what it
collects:

        1. cells
        2. cells and relocatable blocks
        3. cells, relocatable blocks and contiguous blocks.

In levels 2 and 3, the relocatable area is shifted to the higher address
space to reserve an appropriate number of pages in the hole.

     For each type class, KCL keeps a free list of unused cells, and when
the free list is exhausted, a new page is allocated, or the garbage
collector is invoked, depending on whether the maximum number of pages for
that class have been allocated or not.

     The garbage collector does not compactify the heap.  That is, cells
and contiguous blocks are never moved to another place.  Moreover, once a
page is allocated for a particular type class or for contiguous blocks,
that page will never be freed for other classes, even if the entire page
becomes garbage.

     On the other hand, the relocatable area is compactified during level 2
and level 3 of garbage collection.  A relocatable block is really
relocatable.

     The garbage collector is automatically invoked in one of the following
situations.  The number in the parentheses indicates the level of garbage
collection that is performed.

        * The free list of a certain type class is exhausted
after the maximum number of pages have been allocated for that
type class (1).

        * The hole is exhausted (2).

        * The relocatable area is exhausted after the maximum number of
pages have been allocated for the relocatable area (2).

        * The contiguous blocks are exhausted after the maximum number of
pages have been allocated for contiguous blocks (3).

     The garbage collector is also invoked by the following KCL specific
function.

gbc x                                               [Function]

The garbage collector is invoked with the level specified by x.  If x is
nil, the garbage collector is invoked for level 1 garbage collection.  If x
is t, it is invoked for level 3 garbage collection.  Otherwise, it is
invoked for level 2 garbage collection.

4.4. Allocation Functions

The following functions are used to set or inspect the (maximum) number of
pages for each type class, for contiguous blocks, or for relocatable
blocks.

allocate type number                                    [Function]

  Sets the maximum number of pages for the type class of the implementation
  type type to number.  If more than number pages have already been
  allocated, an error is signalled.


allocated-pages type                                    [Function]

  Returns the number of pages currently allocated for the type class of the
  implementation type type.


maximum-allocatable-pages type                          [Function]

  Returns the current maximum number of pages for type class of the
  implementation type type .


allocate-contiguous-pages number                         [Function]

  Sets the maximum number of pages for contiguous blocks to number.


allocated-contiguous-pages                               [Function]

  Returns the number of pages allocated for contiguous blocks.

  
maximum-contiguous-pages                                 [Function]

  Returns the current maximum number of pages for contiguous blocks.


allocate-relocatable-pages number                        [Function]

  Sets the maximum number of pages for relocatable blocks to number.  The
  relocatable area is expanded to number pages immediately.  Therefore, "the
  current maximum number" and "the number of pages allocated" have the same
  meanings for relocatable blocks.


allocated-relocatable-pages                              [Function]

  Returns the number of pages allocated for relocatable blocks.


     If the pages for a particular type class are exhausted after the
maximum number of pages for that class have been allocated, and if there
remain no free cells (actually, if there remain very few cells), KCL
behaves as directed by the value of the KCL specific variable
*ignore-maximum-pages*.  If the value is nil, then KCL signals a
correctable error and enters the break loop.  The user can reset the
maximum number by calling allocate and then continue the execution of the
program by typing :r.

     Example:

        >(make-list 100000)

        Correctable error: The storage for CONS is exhausted.
                           Currently, 531 pages are allocated.
                           Use ALLOCATE to expand the space.
        Signalled by MAKE-LIST.

        Broken at FUNCALL.
        >>(ALLOCATE 'CONS 1000)
        t

        >>:r

        (nil nil nil nil nil nil nil nil nil nil ............

The user can also reset the maximum number of pages for relocatable blocks
and for contiguous blocks in a similar manner.  On the other hand, if the
value of *ignore-maximum-pages* is non-nil, then KCL automatically
increments the maximum number of pages for the class by 50 percent.  The
initial value of *ignore-maximum-pages* is t.


4.5. Storage Information

room &optional x                                        [Function]

  The function room prints the storage information.  The argument x is simply
  ignored and the output of room is always in the same format.  room prints
  the following information:

        * for each type class
                * the number of pages so-far allocated for the type class
                * the maximum number of pages for the type class
                * the percentage of used cells to cells so-far 
                  allocated
                * the number of times the garbage collector has been 
                  called to collect cells of the type class
                * the implementation types that belong to the type class
        * the number of pages actually allocated for contiguous blocks
        * the maximum number of pages for contiguous blocks
        * the number of times the garbage collector has been called to 
          collect contiguous blocks
        * the number of pages in the hole
        * the maximum number of pages for relocatable blocks
        * the number of times the garbage collector has been called 
          to collect relocatable blocks
        * the total number of pages allocated for cells
        * the total number of pages allocated
        * the number of available pages
        * the number of pages KCL can use.

The number of times the garbage collector has been called is not shown, if
the number is zero.

     In the following example, the maximum of 531 pages have already been
allocated for the type class to which cons belongs, but only 16.9 percent
of the cells are actually used.  The garbage collector was once invoked to
collect cells in this type class.

 >(room)
  531/531   16.9%  1  cons bignum ratio long-float complex
    3/52    10.4%     fixnum short-float character random-state
                      readtable spice
   47/65    73.6%     symbol package
    3/71    32.4%     array hash-table vector bit-vector stream
                      pathname cclosure
   46/96    98.8%     string cfun
    1/32     2.3%     structure

   17/512             contiguous (3 blocks)
      14              hole
      50    47.4%  2  relocatable

   631 pages for cells
   712 total pages
 14840 pages available
 16384 maximum pages
 
 >



 



                       Chapter 5. Debugging Facilities



5.1. The Tracer

The Tracer causes selected functions to be traced.  When such a traced
function is invoked, it prints

        level > (name arg1...argn)

On return from a traced function, it prints

        < level (name value1... valuen)

name is the name of the traced function, args are the arguments, and values
are the return values.  level is a number which is incremented each time a
traced function is invoked and is decremented at the completion of the
invocation.  Trace print-outs are indented according to the level.

     In the current version of KCL, macros and special forms cannot be traced.


trace {function-name}*                               [Macro]

Causes one or more functions to be traced.  function-names must be symbols
and they are not evaluated.  If a function is called from a compiled
function, the call may not produce trace print-outs.  If this is the case,
the simplest way to get trace print-outs is to recompile the caller with a
notinline declaration for the called function (see Chapter 7).  trace
returns a name list of those functions that were traced by the call to
trace.  If no function-name is given, trace simply returnsa name list of
all the currently traced functions.


untrace {function-name}*                              [Macro]

Causes the specified functions to be not traced any more.  function-names
must be symbols and they are not evaluated.  untrace returns a name list of
those functions that were untraced by the call to untrace.  If no
function-name is given, untrace will untraceall the currently traced
functions and will return a list of their names.


5.2. The Stepper

step form                                              [Macro]

Starts evaluating the form in the single-step mode.  In this mode, before
any form is evaluated, the Stepper will print the form and prompt the user
for a Stepper command.  The Stepper binds the two variables *print-level*
and *print-length* both to 2, so that the current form may not occupy too
much space on the screen.  A Stepper command will be executed when the user
types the single character for the command followed by the required
arguments, if any, and presses the newline key.  If the user presses the
newline key without having typed any character, then the Stepper will
assume that the Stepper command n was abbreviated.

The Stepper commands are:

n       Next.  Evaluates the current form in the single-step
                            mode.

s       Skip.  Evaluates the current form in the ordinary mode.
                            The single-step mode will be resumed at completion
                            of the evaluation.

p       Print.  Pretty-prints the current form and
                             then prompts again.

f fn    Function.  Evaluates the current
              form in the ordinary mode until the specified
              function fn is invoked.  If the
              specified function
              is not invoked at all, then this command has
              the same effects as the q command
              below.

q       Quit.  Evaluates the current form and any
                            other forms in the ordinary mode.

e form  Eval.  Evaluates the specified
                                form in the ordinary mode and prints the
                                resulting values.  
                                Then prompts again with the same current
                                form.

?       Help.  Lists the Stepper commands.


5.3.  Errors

*break-enable*                                    [Variable]

This variable is used to determine whether to enter the break loop (see
Section 5.4) when an error occurs.  Even the function break checks this
variable.  Initially, this variable is set to t, and thus an error will
invoke the break loop.  If the value is nil, functions that cause fatal
errors, such as error, will just print an error message and control will
return to the top-level loop (or to the current break loop, if already in
the break loop).  Functions that cause correctable errors, such as cerror,
will print an error message and a "continue message", and control will
return to the next form.  In KCL, backtrace is not
 part of an error message, but a break loop command will print backtrace.
Therefore, if *break-enable* is nil, no backtrace appears on the screen.

When the break loop is entered, *break-enable*will be bound to nil.


5.4.  The Break Loop

The break loop is a read-eval-print loop similar to the top-level loop.  In
addition to ordinary Lisp forms, the break loop accepts various commands
with which the user can inspect and modify the state of the program
execution.  Each break loop command is identified with a keyword (i.e., a
symbol in the keyword package).  A break loop command is executed when the
user inputs a list whose first element is the keyword that identifies the
command.  The rest of the list is the arguments to the command.  They are
evaluated before being passed to the command.  If the command needs no
arguments, then the user may input only the keyword.  It is an error if the
given keyword does not identify any command.  Any other input to the break
loop is regarded as an ordinary Lisp form; the form will be evaluated and
the resulting values will be printed on the terminal.

     There can be several instances of the break loop at the same time, and
each such instance is identified by a level number.  When the break loop is
entered during execution in the top-level loop, the break loop instance is
given the level number 1.  The break loop instance that is entered from the
level n break loop is given the level number n+1.  The prompt of the level
n break loop is n+1 consecutive >'s, occasionally prefixed with the name of
the current package.

     The break loop keeps track of the invocation sequence of functions
(including special forms and macro expansion functions), which led up to
the break loop from the previous break loop (or from the top-level loop, if
the current break loop is level 1).  The invocation sequence is maintained
in a pushdown stack of events.  An event consists of an event function and
an event environment.  An event function is:

        1. an interpreted (i.e., not compiled) function (global 
           function, local function, lambda-expression, or closure),
        2. a special form within an interpreted function,
        3. a macro expansion function called from an 
           interpreted function,
        4. a compiled function called from an interpreted function, or
        5. a compiled function called from another compiled
           function which was compiled while the safety optimize
           level is 3 or with a notinline declaration for the called
           function (see Chapter 7).

     An event is pushed on the event stack when execution of its event
function begins, and is poped away at the completion of the execution.  An
event environment is the 'environment' of the event function at the time
the next event is pushed.  Actually, an event environment is a pointer to
the main stack of KCL.  For each interpreted event function (i.e., event
function in classes 1, 2, and 3), the pointer points to the first entry of
the three contiguous main stack entries that hold the lexical environment
of the event function.  For each compiled event function (i.e., event
function in classes 4 and 5), the pointer is set to the first entry of the
main stack area that is used locally by the compiled code.  In most cases,
the first argument to the compiled function is saved in the first entry,
the second argument in the second entry, and so on.  The local variables of
the function are allocated in the entries following the arguments.
However, this is not always the case.  Refer to Section 7.3 for variable
allocations in compiled functions.

     By break level commands, the user can choose one of the events as the
current event.  If the current event function is an interpreted event
function, then the break loop evaluates Lisp forms in the lexical
environment retrieved from the event environment.  In particular, local
variables may be referenced by the variable names, local functions and
local macros may be invoked as usual, established blocks may be exited
from, and tags may be used as the destination of go.  If the current
function is a compiled function, Lisp forms are evaluated in the null
environment.

     Within the break loop, each event is represented by the event symbol.
The :backtrace command, for example, lists events in terms of their event
symbols.  If the event function is a named function (global or local) or a
macro expansion function, then the function or macro name is used as the
event symbol.  If the event function is a special form, then the name of
the special form is used.  If the event function is a lambda-expression (or
a closure), then the symbol lambda (or lambda-closure) is used.

     To suppress unnecessary information, the user can hide (or make
invisible) some of the events.  Invisible events do not appear in the
backtrace, for example.  Initially, only those events are invisible whose
event symbols belong to the system internal package system.  When the break
loop is entered, the last visible event becomes the current event.

     The break loop commands are described below.  Some of the commands
allow abbreviation in the keywords that identify them.  For example, the
user may abbreviate :current as :c.  The break loop commands return no
values at all.


:current                                   [Break Loop Command]

:c                             [Abbreviated Break Loop Command]

  Prints the event symbol of the current event.

:previous &optional n                     [Break Loop Command]

:p &optional                  [Abbreviated Break Loop Command]

  Makes the n-th previous visible event the new current event.  Invisible
  events are not counted.  If there are less than n previous events, then the
  first visible event in the invocation sequence becomes the new current
  event.  n must be a positive integer and the default is 1.

:next &optional  n                         [Break Loop Command]

:n &optional n                 [Abbreviated Break Loop Command]

  Makes the n-th next visible event the new current event.  If there are less
  than n next events, then the last visible event in the invocation sequence
  becomes the new current event.  n must be a positive integer and the
  default is 1.


:backtrace                                 [Break Loop Command]

:b                             [Abbreviated Break Loop Command]

  Prints the event symbols of all visible events in order.  The symbol of the
  current event is printedin upper-case letters and the event symbols of
  other events are in lower-case.


:help                                        [Break Loop Command]

:h                               [Abbreviated Break Loop Command]

  Lists the break loop commands.


:quit &optional n                            [Break Loop Command]

:q &optional n                   [Abbreviated Break Loop Command]

  Returns control to the level n break loop.  If n is 0 or if n is omitted,
  then control will return to the top-level loop.  n must be a non-negative
  integer smaller than the current break level.


:resume                                       [Break Loop Command]

:r                                [Abbreviated Break Loop Command]

  Returns control to the caller of the break loop.  If the break loop has
  been entered from cerror, cerror returns nil as its value and control will
  resume at that point.  Otherwise, this command returns control to the
  previous break loop (or to the top-level loop, if the current break level
  is 1).


:variables                                  [Break Loop Command]

:v                              [Abbreviated Break Loop Command]

  Prints the names of the bound variables in the current environment.  To see
  the value of a bound variable, just type the variable name.


:functions                                  [Break Loop Command]

  Prints the names of the local functions and local macros in the current
  environment.  To see the definition of a local function or macro, use the
  function special form in the usual way.  That is, (function name) will
  return the definition of the local function or macro whose name is name.
  Local functions and local macros may be invoked as usual.


:blocks                                     [Break Loop Command]

  Prints the names of the blocks established in the current environment.  If
  a block block is established, then the return-from form (return-from block
  value) works as usual.  That is, the block form that established block will
  return value as its value and control will resume at that point.


:tags                                    [Break Loop Command]

  Prints the tags established in the current environment.  If a tag tag is
  established, then the go form (go tag) works as usual.  That is, control
  will resume at the position of tag in the surrounding tagbody.


:local &optional n                        [Break Loop Command]
:l &optional n                [Abbreviated Break Loop Command]

  If n is 0 or if it is omitted, then this command prints the value stored in
  the main stack entry that is pointed to by the current event environment.
  n is an offset from that entry.  If n is positive, then the value of the
  n-th next (i.e., toward the top of the main stack) entry is printed.  If n
  is negative, then the value of the | n |-th previous (i.e., toward the
  bottom of the main stack) entry is printed.  n must be an integer.  It is
  an error if the specified entry does not lie between the bottom and the top
  of the stack.


:hide symbol                             [Break Loop Command]

  Hides all events whose event symbol is symbol.  In particular, by (:hide
  'lambda) and (:hide 'lambda-closure), all events become invisible whose
  event functions are lambda-expressions and closures, respectively.  If the
  event symbol of the current event happens to be symbol, then the last
  previous visible event will become the new current event.  symbol must be a
  symbol.

  Events of eval and evalhook may never become invisible and attempts to hide
  them are simply ignored.  It is always the case that the first event
  function is either evalor evalhook.  Keeping both of them visible is the
  simplest way to avoid the silly attempts of the user to hide all events.


:hide-package package                      [Break Loop Command]

  Hides all events whose event symbol belongs to the package package.
  package may be any object that represents a package, i.e., a package
  object, a symbol, or a string.  If the event symbol of the current event
  happens to belong to the package package, then the last previous visible
  event will become the new current event.  Even if lisp package was
  specified as package, events of eval and evalhook do not become invisible.
  See the description of :hide above.


:unhide symbol                             [Break Loop Command]

  :unhide is the inverse command of :hide.  If, however, symbol belongs to
  one of the :hide-package'd packages, events of symbol become visible only
  after the package is :unhide-package'd.  symbol must be a symbol.


:unhide-package package[Break Loop Command]

  :unhide-package is the inverse command of :hide-package.  However, an event
  whose event symbol belongs to package becomes visible only after the symbol
  is :unhide'd, if the symbol was :hide'd before.  package may be any object
  that represents a package, i.e., a package object, a symbol, or a string.


     Example:

        >(defun fact (x) (if (= x 0) one (* x (fact (1- x)))))
        fact                    ;;; Wrong definition for fact, 
                                the factorial.
        
        >(fact 6)               ;;; Tries to calculate factorial 6.

        Error: The variable ONE is unbound.
        Error signalled by IF.
        
        Broken at IF.           ;;; Enters the break-loop.
        >>:h                    ;;; Help.
        :c(urrent)              Shows the current function.
        :p(revious)             To the previous function.
        :n(ext)                 To the next function.
        :b(acktrace)            Prints backtrace.
        :h(elp)                 Help.
        :q(uit)                 Returns to top-level.
        :r(esume)               Returns to the caller of break-level.
        :l(ocal)                Shows the n-th local value on the stack.
        :v(ariables)            Shows local variables.
        :functions              Shows local functions.
        :blocks                 Shows block names.
        :tags                   Shows tags.
        :(un)hide(-package)     (Un)hide a function (or a package).
        
        >>:b                    ;;; Backtrace.
        Backtrace: eval > fact > if > fact > if > fact > if > fact > if >
        fact > if > fact > if > fact > IF
        
        >>:p                    ;;; Moves to the previous event.
        Broken at FACT.
        
        >>:b                    ;;; Now inside of fact 
                                but outside of if.
        Backtrace: eval > fact > if > fact > if > fact > if > fact > if >
        fact > if > fact > if > FACT > if
        
        >>:v                    ;;; Shows local variables.
        Local variables: x.
        
        >>x                     ;;; The value of x 
                                is 0.
        0
        
        >>:blocks               ;;; Shows blocks.
        Block names: fact.
        
        >>(return-from fact 1)  ;;; Returns from the fact 
                                block with value 1.
        720                     ;;; Now the correct answer.

        >                       ;;; Top-level.


5.5. Describe and Inspect

describe object                                    [Function]

Prints the information about object to the stream that is the value of
*standard-output*.  The description of an object consists of several
fields, each of which is described in a recursive manner.  For example, a
symbol may have fields such as home package, variable documentation, value,
function documentation, function binding, type documentation, deftype
definition, properties.


inspect object                                     [Function]

Prints the information about object in an interactive manner.  The output
of inspect is similar to that of describe, but after printing the label and
the value of a field (the value itself is not describe'd), it prompts the
user to input a one-character command.  The input to inspect is taken from
the stream that is the value of *query-io*.  Normally, the inspection of
object terminates after all of its fields have been inspected.  The
following commands are supported:

n       Next.  Goes to the next level; the field is inspected
                            recursively.

s       Skip.  Skips the inspection of the field.
                            inspect proceeds to the next field.

p       Print.  Pretty-prints the field and prompts again.

u form  Update.  The form is evaluated 
                             and the field is replaced by the resulting 
                            value.  If the field cannot be updated,
                            the message Not updated. will
                            be printed.

a       Abort.  Aborts the inspection of the current object.
                     The field and the rest of the fields
                     are not inspected.

e form  Eval.  Evaluates the specified 
                             form in the null environment and prints 
                             the resulting values.  Then prompts again with 
                             the same field.

q       Quit.  Aborts the entire inspection.

?       Help.  Lists the inspect commands.






                     Chapter 6. The Compiler


The KCL compiler translates a Lisp program stored in a source file into a
C-language program, invokes the C-language compiler to compile the
C-language program, and then generates an object file, called fasl file (or
o-file because of the actual filetype).  The compiled program in a fasl
file is loaded by the function load.

     Ordinarily, the object program generated by the KCL compiler scarcely
does runtime error-checking for runtime efficiency.  In addition, Lisp
functions in the same source file are linked together and some system
functions are open-coded in-line.  To control runtime error checking,
supply appropriate optimize declarations (see Section 7.1).

     The KCL compiler processes the eval-when special form exactly as
specified in the Common Lisp Reference Manual.  However, all top-level
forms in the source file are normally processed in compile-time-too mode,
not in not-compile-time mode (see Section 5.3.3 of the Common Lisp
Reference Manual).  That is, each top-level form top-level-form is
processed as if it were surrounded by the eval-when special form with the
situations compile, load, and eval.

    (eval-when (compile load eval) top-level-form)

There is no exception for this rule.  Thus, for instance, in the example of
set-macro-character form in Section 5.3.3 of the Common Lisp Reference
Manual, the surrounding eval-when form is unnecessary in KCL.  If it is
desired that each top-level form be processed in not-compile-time mode,
change the value of the KCL specific variable *eval-when-compile* as
described below.

     The KCL compiler is invoked by the functions compile-file, compile,
and disassemble described below.  In addition, the KCL compiler may be
invoked directly by the Shell commands lc or lc1.  These commands require
the file name of the source file as their argument.  Both lc and lc1 simply
add ".lsp" to the file name argument to obtain the full name of the source
file.

        % lc filename

has the same effect as the compiler invocation (compile-file "filename")
from within KCL, and

        % lc1 filename

has the same effects as (compile-file "filename" :o-file t :c-file t
:h-file t :data-file t).


compile-file input-pathname                   [Function]
        &key :output-file :o-file :c-file :h-file :data-file

compile-file compiles the Lisp program stored in the file specified by
input-pathname, and generates a fasl file.  Also compile-file generates the
following temporary files.

        Temporary File  Contents
        ------------------------------------------------
        c-file          C version of the Lisp program
        h-file          The include file referenced 
                                         in the c-file
        data-file       The Lisp data to be used at load time

If files of these names already exist, the old files will be deleted first.
Usually, these intermediate files are automatically deleted after execution
of compile-file.

     The input-file is determined in the usual manner (see Section 2.9),
except that, if the filetype is not specified, then the default filetype
.lsp will be used.  The keyword parameter :output-file defines the default
directory and the default name to be applied to the output files (i.e., the
fasl file and the temporary files).  :output-file itself defaults to
input-pathname.  That is, if :output-file is not supplied, then the
directory and the name of the input file will be used as the default
directory and the default name for the output files.  The filetypes of the
output files are fixed as follows.

        Output File     Filetype
        ----------------------
        fasl file       .o
        c-file          .c
        h-file          .h
        data-file       .data

Each output file can be specified by the corresponding keyword parameter.
If the value of the keyword parameter is nil, then the output file will be
deleted after execution of compile-file.  If the value of the keyword
parameter is t, then the output file will be left in the default directory
under the default name.  Otherwise, the output file will be left in the
directory under the name specified by the keyword parameter.  The default
value of :o-file is t, and the default values of :c-file, :h-file, and
:data-file are all nil.

     Example:

        (compile-file 'foo)
                The source file is "FOO.lsp" and 
                  the fasl file is "FOO.o"
                both in the current directory.

        (compile-file 'foo.lish)
                The source file is "FOO.LISH" and 
                 the fasl file is "FOO.o".

        (compile-file "/usr/mas/foo" :output-file "/usr/tai/baa")
                The source file is "foo.lsp" in the 
                   directory "/usr/mas",
                and the fasl file is "baa.o" in the 
                 directory "/usr/tai".


----------------------Note to KCL/AOS users----------------------

The compiler of KCL/AOS generates the following output files.

        Output File     Filetype                Contents
        ------------------------------------------------------------
        fasl file       .fasl           The fasl file
        c-file          .c              C version of the Lisp program
        h-file          .h              The include file referenced 
                                        in the c-file 
        ob-file         .ob             The object file generated by 
                                         the C compiler
        data-file       .data           The Lisp data to be 
                                          used at load time

Note that the filetype of the fasl file is .fasl in KCL/AOS.  Also note
that the compiler of KCL/AOS generates an additional file ob-file.
Accordingly, the function compile-file has a slightly different definition:

compile-file input-pathname                       [Function] 
        &key :output-file :fasl-file :c-file :h-file :ob-file :data-file

The keyword parameter :fasl-file corresponds to the keyword parameter
:o-file in KCL on Unix.  In particular, the default value of :fasl-file is
t and the default values of :c-file, :h-file, :ob-file, and :data-file are
all nil.  In KCL/AOS,

        ) lc1 filename

has the same effects as (compile-file "filename" :fasl-file t :c-file t
:h-file t :ob-file t :data-file t).

     Because KCL/AOS follows the convention of the AOS/VS file system, the
last example above should be replaced as:

        (compile-file ":udd:mas:foo" :output-file ":udd:tai:baa")
                The source file is "FOO.LSP" in the 
                directory ":UDD:MAS",
                and the fasl file is "BAA.FASL" in the 
                directory ":UDD:TAI".

---------------------------End of Note----------------------------


compile name &optional definition                  [Function]

  If definition is not supplied, name should be the name of a
  not-yet-compiled function.  In this case, compile compiles the function,
  replaces the previous definition of name with the compiled function, and
  returns name.  If definition is supplied, it should be a lambda-expression
  to be compiled and name should be a symbol.  If name is a non-nil symbol,
  then compile installs the compiled function as the function definition of
  name and returns name.  If name is nil, then compile simply returns the
  compiled function.

       The KCL compiler is essentially a file compiler, and forms to be
  compiled are supposed to be stored in a file.  Thus compile actually
  creates a source file which contains the form designated by the arguments.
  Then compile calls compile-file to get a fasl file, which is then loaded
  into KCL.  The source file and the fasl file are given the names gazonk.lsp
  and gazonk.fasl, respectively.  These files are not deleted automatically
  after the execution of compile.


disassemble &optional thing &key :h-file :data-file     [Function]

  This function does not actually disassemble.  It always calls the KCL
  compiler and prints the contents of the c-file, i.e., the C-language code,
  generated by the KCL compiler.  If thing is not supplied, or if it is nil,
  then the previously compiled form by disassemble will be compiled again.
  If thing is a symbol other than nil, then it must be the name of a
  not-yet-compiled function, whose definition is to be compiled.  In this
  case, it is an error if the name is associated with a special form or a
  macro.  If thing is a lambda-expression (lambda lambda-list . body), then
  disassemble first creates a function definition (defun gazonk lambda-list .
  body) and this definition is compiled.  (The function name gazonk has no
  special meanings.  Indeed, the displayed code is essentially independent of
  the function name.)  Otherwise, thing itself will be compiled as a
  top-level form.  In any case, disassemble does not install the compiled
  function.  disassemble returns no value.

      No intermediate h-file is created if the keyword parameter :h-file is
  nil or if :h-file is not supplied.  Otherwise, an intermediate h-file is
  created under the name specified by :h-file.  Similarly, the intermediate
  data-file is specified by the keyword parameter :data-file.


*eval-when-compile*                           [Variable]

  The compiler processes each top-level form in not-compile-time mode if the
  value of this variable is nil, and in compile-time-too mode, otherwise.
  See Section 5.3.3 of Common Lisp Reference Manual for these two modes.  The
  initial value of this variable is t.





                          Chapter 7. Declarations


KCL supports all kinds of declarations described in the Common Lisp
Reference Manual.  Any valid declaration will affect the KCL environment in
some way or another, although information obtained by declarations, other
than special declarations, is mainly used by the KCL compiler.

     As described in the Common Lisp Reference Manual, Common Lisp
declarations are divided into two classes: proclamations and others.  A
proclamation is a global declaration given by the function proclaim, the
top-level macro defvar, or the top-level macro defparameter.  Once given, a
proclamation remains effective during the KCL session unless it is shadowed
by a local declaration or is canceled by another proclamation.  Any other
declaration is a local declaration and is given only by the special form
declare.  A local declaration remains in effect only within the body of the
construct that surrounds the declaration.  In the following nonsensical
example borrowed from Chapter 9 of the Common Lisp Reference Manual,

    (defun nonsense (k x z)
      (foo z x)
      (let ((j (foo k x))
            (x (* k k)))
           (declare (inline foo) (special x z))
        (foo x j z)))

the inline and the special declarations both remain in effect within the
surrounding let form.  In this case, we say that the let form is the
surrounding construct of these declarations.

proclamation decl-spec                           [Function]

This function is introduced to KCL so that the user can see currently
effective proclamations.  The argument decl-spec specifies the proclamation
to be checked.  It may be any declaration specification that can be a valid
argument to the function proclaim.  The function proclamation returns t if
the specified proclamation is still in effect.  Otherwise, it returns nil.
For example,

    >(proclaim '(special *x*))  ;;; The variable *x* is
    nil                         ;;; proclaimed to be globally special.

    >(proclamation '(special *x*))
    t

    >(defvar *y*)               ;;; Another way to proclaim a variable
    nil                         ;;; to be globally special.

    >(proclamation '(special *y*))
    t


the value-type form                          [Special Form]

The KCL interpreter does actually check whether the value of the form
conforms to the data type specified by value-type and signals an error if
the value does not.  The type checking is performed by the function typep.
For example,

    (the fixnum (foo))

is equivalent to

 (let ((values (multiple-value-list (foo))))
   (cond ((endp values) (error "Too few return values."))
         ((not (endp (cdr values)))
          (error "Too many return values."))
         ((typep (car values) 'fixnum) (car values))
         (t (error "~s is not of type fixnum." (car values)))))

On the other hand, the KCL compiler uses the the special form to obtain
type information for compiled code optimization.  No code for runtime
type-checking is embedded in the compiled code.


7.1. Declaration Specifiers

KCL recognizes all declaration specifiers defined in the Common Lisp
Reference Manual.  The syntax of each such declaration specifier is exactly
the same as defined in the Common Lisp Reference Manual.  In addition, KCL
recognizes the object declaration specifier which is specific to KCL.

special { variable-name }*                [Declaration Specifier]

The interpreter and the compiler of KCL both treat special declarations
exactly as described in the Common Lisp Reference Manual.


type type { variable-name }*              [Declaration Specifier]

A type proclamation (type type var1 var2 ...) specifies that the dynamic
values of the named variables are of the type type.  A local type
declaration specifies that the variables mentioned are bound by the
surrounding construct and have values of the type type during execution of
the surrounding construct.  The compiler issues a warning if one of the
named variables is not bound by the surrounding construct.  The information
given by type declarations is used by the compiler to optimize the compiled
code.  The behavior of the compiled code is unpredictable if a wrong type
declaration is supplied.  The compiler detects certain wrong type
declarations at compile time.  For example,

        >(defun foo (x y)
           (declare (fixnum x) (character y))
           (setq x y)
          ...))
        foo

        >(compile 'foo)

        ; (defun foo ...) is being compiled.
        ;; Warning: Type mismatches between x and y.

See Section 7.3 for further information on type declarations.


type { variable-name }*              [Declaration Specifier]

(type var1 var2 ...) is equivalent to (type type var1 var2 ...), provided
that type is one of the symbols in Table 4-1 of the Common Lisp Reference
Manual, other than function.  Declaration specifications that begin with
function are regarded as function declarations (see below).


function function-name argument-types . return-types [Declaration Specifier]

A function declaration is used to obtain type information for function call
forms.  That is, a function declaration specifies the argument and the
return types of each form that calls the named function.

    (defun foo ()
      (declare (function bar (character) fixnum))
      (+ (bar (atcholi1)) (bar (atcholi2))))

In this example, the function declaration specifies that the two functions
atcholi1 and atcholi2 both return character objects when called within the
body of foo, and that the function bar returns fixnum objects when called
within the body of foo.  The type information given by function
declarations is used by the compiler to optimize the compiled code.  The
behavior of the compiled code is unpredictable if a wrong function
declaration is supplied.  The compiler detects certain wrong function
declarations at compile time.  For example,

    >(defun foo (x)
       (declare (fixnum x)
                (function bar (character) fixnum))
       (bar x))
    foo

    >(compile 'foo)

    ; (defun foo ...) is being compiled.
    ;; Warning: The type of the form x is not character.

However, the compiler does not check the number of arguments, and thus,
the following function definition will be compiled successfully without
any warnings.

    (defun foo ()
      (declare (function bar (character character) fixnum))
      (+ (bar (atcholi1)) (bar (atcholi2) (atcholi3) (atcholi4))))

For this definition, the compiler assumes that the three functions
atcholi1, atcholi2, and atcholi3 will return fixnum objects.  The return
type of atcholi4 is unknown at compile time.

The complete syntax of a function declaration is:

    (function function-name
      ( { type }* [ { &optional | &rest | &key } { thing }* ] )
      { (values { type }* ) | { type }* }
     )

Although &optional, &rest, and &key markers may appear in the list of
argument types, only those types are recognized that appear before any such
markers and the rest of the list is simply ignored.  Note that functions
with &optional, &rest, or &key parameters may still be declared by function
declarations because of the use of function declarations mentioned above.

The values construct in the specification of return types is almost
useless:  (function function-name argument-types (values type1 type2 ...))
is equivalent to (function function-name argment-types type1 type2 ...).
We, the implementors of KCL wonder why the value construct was introduced
in Common Lisp.

See Section 7.3 for further information on function declarations.


ftype function-type { function-name }*     [Declaration Specifier]

function-type must be a list whose first element is the symbol function.
(ftype (function . rest) function-name-1 ... function-name-n) is equivalent
to n consecutive function declarations (function function-name-1 . rest)
...  (function function-name-n . rest).


notinline { function-name }*          [Declaration Specifier]

(notinline function1 function2 ...) specifies that the compiler should not
compile the named functions in-line.  Calls to the named functions can be
traced and an event (see Section 5.4) is pushed on the event stack when any
one of the named functions is invoked.


inline { function-name }*                 [Declaration Specifier]

An inline proclamation cancels currently effective notinline proclamations,
and a local inline declaration locally shadows currently effective
notinline declarations.

    >(defun foo (x)
       (cons (car x)
             (locally (declare (inline car)) (car x))))
    foo

    >(defun bar (x)
       (cons (car x)
             (locally (declare (inline car)) (car x))))
    foo

    >(proclaim '(notinline car))
    nil

    >(compile 'foo)
    ...

    >(proclaim '(inline car))
    nil

    >(compile 'bar)
    ...

Usually, primitive functions such as car are compiled in-line.  Therefore,
in this example, only the first call to car within foo is compiled not
in-line,

In general, the KCL compiler compiles functions in-line whenever possible.
Thus an inline declaration (inline function1 function2 ...) is worthless if
none of the named functions have previously been declared to be notinline.


ignore { variable-name }*             [Declaration Specifier]

Usually, the compiler issues a warning if a lexical variable is never
referred to.  (ignore var1 ... varn) causes the compiler not to issue a
warning even if the named variables are never referred to.  The compiler
issues a warning if one of the named variables is not bound by the
surrounding construct, or if a named variable is actually referred to.
ignore proclamations are simply ignored.


optimize { { (quality value) | quality } }*    [Declaration Specifier]

KCL supports the four optimize qualities listed in the Common Lisp
Reference Manual.  speed and compilation-speed are used to set up the
optimization switch of the C language compiler which is invoked to compile
the C-language code generated by the KCL compiler (see Chapter 6).
(optimize (speed n)) and (optimize (compilation-speed m)) are equivalent,
where n and m are integers between 0 and 3, and m is equal to 3-n.  When a
KCL session is started, the speed quality is set to 3.  That is, by
default, the compiler generates the fastest code in the longest compilation
time.  The space quality specifies whether the code size is important or
not:  The compiled code is a little bit larger and faster when compiled
with the space quality 0, than when compiled with the space quality 1, 2,
or 3.  When a KCL session is started, the space quality is set to 0.  The
safety quality determines how much runtime error checking code should be
embedded in the compiled code.  If the safety quality is 0, the compiled
code scarcely does runtime error checking.  If the safety quality is 1,
then the compiled code for a function will check the number of arguments to
the function at runtime.  If the safety quality is 2 or 3, then the
compiled code does full runtime error checking.  In addition, the highest
quality value 3 causes the compiler to treat all functions as if they were
declared to be notinline.  When a KCL session is started, the safety
quality is set to 0.


declaration ) { name }*                      [Declaration Specifier]

A declaration declaration is used exactly as specified in the
Common Lisp Reference Manual.


object { variable-name }*                    [Declaration Specifier]

This is the only declaration specifier that is specific to KCL.  (object
var1 ... varn) affects only variable bindings and specifies that the named
variables can be allocated in the C stack (see Section 7.3).  The compiler
issues a warning if one of the named variables is not bound by the
surrounding construct.  object proclamations are simply ignored.


7.2. Significant Type Specifiers

Whenever a declaration is encountered, each type specifier (if any) in the
declaration is converted to one of the following type specifiers, which are
collectively called the significant type specifiers.

          ------------  fixnum 
          |
          ------------  character 
          |
          ------------  short-float 
          |
          ------------  long-float 
          |
     t  ----  (array t)  ------------  (vector t) 
          |
          --  (array fixnum)  -------  (vector fixnum) 
          |
          --  (array string-char)  --  string  
          |
          --  (array short-float)  --  (vector short-float)
          |
          --  (array long-float)  ---  (vector long-float) 
          |
          --  (array bit)  ----------  bit-vector 

Here, the lines indicate subtype relations; the right type is a subtype of
the left type.  For instance, (vector t) is a subtype of (array t) and t,
and (array t) itself is a subtype of t.  However, (array t) and (array
string-char) are disjoint types.

     The function subtypep is used for the conversion to significant type
specifiers:  If the first value of (subtypep raw-type type) is t for one of
the significant type specifiers type, then the type specifier raw-type in
the declaration is converted to type.  If there are more than one such
significant type specifiers, then the type specifier that is a subtype of
other specifiers is selected.  For example, type specifiers fixnum, (mod
3), and (member 0 1) are all converted to fixnum, though they are also
subtypes of t.

     Because of this type specifier conversion, KCL may sometimes regard
two seemingly distinct declarations as the same.  For example, the
following type declarations are completely equivalent, internally in KCL.

    (declare (type fixnum x))

    (declare (type (mod 3) x))

    (declare (type (member 0 1) x))

Type specifiers in declaration specifications passed to the KCL specific
function proclamation are also converted to significant type specifiers.
Thus, for example,

    >(proclaim '(function foo (fixnum) fixnum))
    nil

    >(proclamation '(function foo ((mod 3)) (member 0 1)))
    t

    >(proclamation '(function foo (number) character))
    nil

The first call to proclamation returns t because both (mod 3) and (member 0
1) are converted to fixnum before the function type of foo is checked.


7.3. Treatment of Type Declarations

KCL has several runtime stacks.  One of them is called the value stack
which is the "main stack" of KCL:  Arguments to functions and resulting
values of functions are usually passed via the value stack, lexical
variables in compiled code are usually allocated on the value stack, and
temporary values during evaluation of nested expressions are usually saved
on the value stack.  However, if appropriate declarations are supplied to
the compiler, the compiled code will use another stack called the C stack,
which can be accessed more efficiently than the value stack.  In addition,
arguments and resulting values passed via the C stack, values of lexical
variables allocated on the C stack, and temporary values saved on the C
stack may sometimes be represented as raw data instead of pointers to
heap-allocated cells.  In KCL, even a fixnum object is usually represented
as a pointer to a fixnum cell in which the raw datum (i.e., the 32-bit
signed integer) for the fixnum is stored.  Accessing such raw data on the C
stack results in faster compiled code, partly because no pointer
deferencing operation is necessary, and partly because no cell is newly
allocated on the heap when a new object is created.  In contrast, any
object on the value stack is represented as a pointer to a heap-allocated
cell.

     One of the deficiencies of the use of the C stack is that raw data on
the C stack may sometimes need to be reallocated on the heap.  Suppose, in
the following example, that the lexical variable x is allocated on the C
stack and has always a fixnum raw datum as its value.  (The situations in
which this occurs will be explained later.)

    (defun foo ()
      (let ((x 0))
        ....
        (bar x)
        ....
        ))

Also suppose that the function bar expects its argument to be passed via
the value stack rather than via the C stack.  (This situation typically
occurs when foo and bar are defined in separate source files.  See below.)
On call to bar, the compiled code of foo will allocate a fixnum cell on the
heap and push the pointer to this cell on the value stack as the argument
to bar.

     Another deficiency is that it is sometimes dangerous to allocate a
cell pointer onto the C stack.  (This occurs when object) declarations are
supplied.  See below.)  The garbage collector of KCL never takes care of
cell pointers on the C stack and thus a heap-allocated cell pointed to only
from the C stack may be recycled for further use, while the data in the
cell is still in use.  This is why KCL usually uses the less efficient
value stack.  In contrast, objects on the value stack are automatically
protected against garbage collection.  Note that raw data on the C stack
need not be protected against garbage collection because they remain alive
until the C stack is popped.


7.3.1. Variable Allocations

If a lexical variable is declared to be of fixnum, character, short-float,
long-float, or their subtypes, then it is allocated on the C stack rather
than on the value stack.  In addition, the variable always has a raw datum
as its value: 32 bit signed integer for fixnums, 8 bit character code with
24 bit padding for characters (remember that the font and bit fields of KCL
characters are always 0), 32 bit floating point representation for
short-floats, and 64 bit floating point representation for long-floats.
Similarly, if a lexical variable is named in an object declaration (see
Section 7.1), then it is allocated on the C stack but, in this case, the
variable always has a cell pointer as its value.  The user is strongly
recommended to make sure that objects stored in such an object variable may
never be garbage collected unexpectedly.  For example,

    (do ((x (foo) (cdr x)))
        ((endp x))
        (let ((y (car x)))
             (declare (object y))
          (bar y)))

this object declaration is completely safe because the value of the
variable y is always a substructure of the value of x, which in turn is
protected against garbage collection.  Incidentally, loop variables of
dolist may always be declared as object variables, since the dolist form
has essentially the same control structure as the do form above.  On the
other hand, the result of evaluation of the following form is
unpredictable, because the cons cell pointed to from the object variable z
may be garbage collected before bar is called.

    (let ((z (cons x y)))
         (declare (object z))
      (foo (cons x y))
      (bar z))

     Lexical variables that are not declared to be of fixnum, character,
short-float, long-float, or their subtypes, and that are not named in
object declarations are usually allocated on the value stack, but may
possibly be allocated on the C stack automatically by the compiler.


7.3.2. Built-in Functions that Operate on Raw Data Directly 

Some built-in Common Lisp functions can directly operate on raw data, if
appropriate declarations are supplied.  The addition function + is
among such functions.

    (let ((x 1))
         (declare (fixnum x))
      ....
      (setq x (+ x 2))
      ....
      )

In the compiled code for this let form, the raw fixnum datum (i.e., the 32
bit signed integer) stored in x is simply incremented by 2 and the
resulting 32 bit signed integer is stored back into x.  The compiler is
sure that the addition for 32 bit signed integers will be performed on the
call to +, because the arguments are both fixnums and the return value must
be also a fixnum since the value is to be assigned to the fixnum variable.
The knowledge of both the argument types and the return type is necessary
for this decision:  Addition of two fixnums may possibly produce a bignum
and addition of two bignums may happen to produce a fixnum value.  If
either the argument type or the return type were not known to the compiler,
the general addition function would be called to handle the general case.
In the following form, for example, the compiler cannot be sure that the
return value of the multiplication is a fixnum or that the arguments of the
addition are fixnums.

    (setq x (+ (* x 3) 2))

In order to obtain the optimal code, a the special form should surround the
multiplication.

    (setq x (+ (the fixnum (* x 3)) 2))


     Built-in Common Lisp functions that can directly operate on raw data
are:

1. arithmetic functions such as +, -, 1+, 1-, *, floor, mod, /, and expt.

2. predicates such as eq, eql, equal, zerop, plusp, minusp, =, /=, <, <=,
>, >=, char=, char/, char<, char<=, char>, and char>=.

3. sequence processing functions that receive or return one or more fixnum
values, such as nth, nthcdr, length, and elt.

4. array access function such as svref, char, schar, and aref (see below).

5. system-internal functions for array update (see below).

6. type-specific functions such as char-code, code-char, and float.

     As mentioned in Section 2.5.1, array elements are represented in one
of the six ways depending on the type of the array.  By supplying
appropriate array type declarations, array access and update operations can
handle raw data stored in arrays.  For example,

     (let ((a (make-array n :element-type 'fixnum))
           (sum O))
          (declare (type (array fixnum) a)
                   (fixnum sum))
       (dotimes (i n)             ;;; Array initialization.      
                (declare (fixnum i))  
          (setf (aref a i) i))
....
(dotimes (i n)                    ;;;Summing up the elements.
         (declare (fixnum i))
  (setq sum (+ (aref a i) sum )))      
....
)

The setf form replaces the i-th element of the array a by the raw fixnum
value of i.  The aref form retrieves the raw fixnum datum stored in a.
This raw datum is then added to the raw fixnum value of the fixnum variable
sum, producing the raw fixnum datum to be stored in sum.  The similar raw
data handling is possible for arrays of types (array fixnum), (vector
fixnum), (array string-char), and (vector long-float).


7.3.3.Arguments/Values Passing

Function proclamations (function funtion-name (arg-type1 arg-type2...)
return-type ) or its equivalents give the compiler the chance to generate
the compiled code so that arguments to the named functions and resulted
values of the named function be passed via the C stack, thus increasing the
efficiency of calls to these functions.  Such arguments/values passing via
the C stack is possible only if the called function is also defined in the
same source file.  This is because the code for the called function must
have two entries:  One entry for arguments/values passing via the C stack
and another for arguments/values passing via the value stack.  (An ordinary
function has only the latter entry.)  When the latter entry is used, the
arguments on the value stack are pushed onto the C stack and then the
former entry is used to execute the body of the function.  On return from
the function, the resulted value on the C stack is pushed onto the value
stack.  This means that ordinary calls to these functions are slower than
calls to ordinary functions.

One of the merits of arguments/values passing via the C stack is that raw
data stored on C-stack-allocated variables can be passed directly to other
functions and raw data returned from functions may be directly saved in
C-stack-allocated variables or may directly be used as arguments to another
function.  A good example of this follows:

(eval-when (compile)
   (proclaim '(function tak (fixnum fixnum fixnum) fixnum)))

(defun tak (x y z)
   (declare (fixnum x y z))
   (if (not (< y x))
       z
       (tak (tak (1- x) y z)
            (tak (1- y) z x)
            (tak (1- z) x y))))

;;; Call (tak 18 12 6).

When tak is called with the arguments 18, 12, and 6, the raw fixnum data of
the arguments are set to the parameters x, y, z which are allocated on the
C stack.  After that, only raw data on the C stack are used to perform the
execution:  No cell pointers are newly allocated nor even referenced.
Arguments and resulted values for recursive calls to tak are passed via the
C stack, and the built-in functions < and 1- directly operate on the raw
data.  Only at the return from the top-level call of tak, the resulted raw
data value (which happens to be 7) is reallocated on the heap.  Note that
both the functions proclamation and the local fixnum declaration are
necessary to obtain the optimal code.  The function proclamation is
necessary for arguments/values passing via the C stack and the fixnum
declarations is necessary to allocate the parameters onto the C stack.





               Chapter 8. Operating System Interface

     KCL provides the following facilities that are not defined in the
Common Lisp Reference Manual.

save filename                                  [Function]

save saves the current memory image into a program file filename.  After
saving the memory image, the KCL process terminates immediately.  To
execute the saved program file, specify the full pathname of the file, as
indicated in the example below.


---------------------------Note to KCL/AOS Users-----------------------------

In KCL/AOS, if the filename does not contain the filetype .pr, then the
program file is given the name filename.pr.  Also save saves a symbol table
file with the filetype .st.  When the program file is executed, execution
begins at the top-level of KCL.  Even if there were streams that were open
at the call of save, these streams are not effective when the program file
is executed.  The function save of KCL/AOS does no terminate the KCL
process.

-------------------------End of Note------------------------------------


Example:

>(defun plus (x y) (+x y))
plus

>(save "savefile")
%

%pwd
/usr/hagiya/savefile

>(plus 2 3)
5
>(bye)
Bye.
%

-------------------Note to KCL/AOS users--------------------------

Here is the example of save in KCL/AOS.

  >(defun plus (x y) (+x y))
  plus

  >(save "savefile")
  t

  >(bye)
  Bye.
  )

  ) X SAVEFILE

  >(plus 2 3)
  5

  >(bye)
  Bye.
  )

----------------------------End of Note-------------------------------


system string                                          [Function]

Executes a Shell command as if string is an input to the Shell.  On return
from the Shell command, system returns the exit code of the command as an
integer.


----------------------Note to KCL/AOS Users-----------------------

This function is not suppported in KCL/AOS.  Use instead those functions
specific to KCL/AOS described below.

-------------------------End of Note--------------------------------


bye &optional exit-code                             [Function]
by  &optional exit-code                             [Function]

     Terminates KCL and returns the exit-code to the parent process.
exit-code must be an integer and its default value is O.


-----------------------Note to KCL/AOS Users--------------------------

The functions bye and by of KCL/AOS accept a string instead of an
exit-code.  If string is supplied, these functions return the string to the
father as the termination message.

---------------------------End of Note-----------------------------


The following functions process, termination-message, and
last-termination-message are specific to KCL/AOS and are not supported in
KCL on Unix.

process progname &optional ipc-message                 [Function]
                 &key :block :console :debug :dir
                 :input :output :username
                 :list :data :ioc

     This function is defined only in KCL/AOS.  process creates a 
process in the way as specified by its arguments.

     progname             The name of the process to create.  
                          Must be a string
     
     ipc-message          The IPC message passed to the process.  
                          Must be a string.  Arguments in the 
                          message must be separated with commas 
                          `,'.

     :block               If non-nil, Kcl blocks its execution 
                          while the son executes.  Defaults to t.

     :console             The name of the file to be associated 
                          to @console.  Must be a string.  No 
                          file is associated if :console is not 
                          specified and if the :ioc argument (see 
                          below) is specified with a non-nil 
                          value.  :console supercedes :ioc.

     :debug               If non-nil, the son runs in the debug 
                          mode.

     :input               The name of the file to be associated 
                          to @input.  Must be string.  No file is 
                          associated if :input is not specified 
                          and if the :ioc argument (see below) is 
                          specified with a non-nil value.  :input 
                          supercedes :ioc.

     :output              The name of the file to be associated 
                          to @output.  Must be a string.  No file 
                          is associated if :output is not 
                          specified and if the :ioc argument (see 
                          below) is specified with a non-nil 
                          value.  :output supercedes :ioc. 

     :username            The user-name of sub-process.  Must be 
                          a string.  If not specfied, the current 
                          user-name is used.

     :list                If a string, the name of the file to be 
                          associated to @list is used.  If t, the
                          file currently associated to @list is used.
                          If nil, or if not specified, no list file is 
                          passed to the son.

     :data                If a string, the name of the file to be 
                          associated to @data.  If t, the file 
                          currently associated to @list is used.  
                          If nil, or if not specified, no list
                          file is passed to the son.

     :ioc                 If non-nil, current @input, @output, 
                          and @console files are passed to the 
                          son.  If not specified, these files are 
                          not passed unless specified by the 
                          :console, :input, or :output arguments.

Example:

     >(process ":cli.pr")

    AOS/VS CLI  Rev 03f.03.00.00       01-July-87        12:00:00
    )by
    AOS/VS CLI TERMINATING             01-July-87        12:00:00
    t
  
    >


termination-message                                    [Function]

This function is defined only in KCL/AOS.  termination-message retruns a
string consisting of the termination message of a son.  Used in connection
with the function process.

last-termination-message                               [Function]

This function is defined only in KCL/AOS.  last-termination-message flushes
all the messages currently spooled and returns the last termination
message.





                       Chapter 9. Macros



9.1. System Macros

The KCL interpreter implements the following system macros as if they were
special forms.  That is, macro forms of the following macros are directly
evaluated without being macro-expanded.

    and       case      cond      decf      defmacro  defun
    do        do*       dolist    dotimes   incf      locally
    loop      multiple-value-bind           multiple-value-list
    multiple-value-setq           or        pop       prog
    prog*     prog1     prog2     psetq     push      return
    setf      unless    when

For these macro forms, the functions macro-function and special-form-p both
return non-nil values:  macro-function returns the macro expansion function
and special-form-p returns t.  Of course, functions such as macroexpand and
macroexpand-1 will successfully expand macro forms for these system macros.


9.2. Defmacro Lambda-Lists

A defmacro lambda-list is a lambda-list-like construct that is used as the
third element in the defmacro form,

    (defmacro name defmacro-lambda-list {declaration | doc-string}* {form}* )

The description of defmacro lambda-lists in the Common Lisp Reference
Manual is quite ambiguous.  KCL employs the following syntax.

The complete syntax of a defmacro lambda-list is:

( [ &whole var ]
  [ &environment var ]
  { pseudo-var }*
  [ &optional { var | ( pseudo-var [ initform [ pseudo-var ] ] ) }* ]
  {  [ { &rest | &body } pseudo-var ]
     [ &key { var | ( { var | ( keyword pseudo-var ) } [ initform 
[ pseudo-var ] ] ) }*
            [ &allow-other-keys ] ]
     [ &aux { var | ( pseudo-var [ initform ] ) }* ]
  |  . var }
 )

where pseudo-var is either a symbol or a list of the following form:

( { pseudo-var }*
  [ &optional { var | ( pseudo-var [ initform [ pseudo-var ] ] ) }* ]
  {  [ { &rest | &body } pseudo-var ]
     [ &key { var | ( { var | ( keyword pseudo-var ) } [ initform 
[ pseudo-var ] ] ) }*
            [ &allow-other-keys ] ]
     [ &aux { var | ( pseudo-var [ initform ] ) }* ]
  |  . var }
 )

The defmacro lambda-list keyword &whole may appear only at the top-level,
first in the defmacro lambda-list.  It is not allowed within pseudo-var.
Use of the &whole keyword does not affect the processing of the rest of the
defmacro lambda-list:

    (defmacro foo (&whole w x y) ... )


and

    (defmacro foo (x y) ... )

both bind the variables x and y to the second and the third elements,
respectively, of macro forms of foo.

     The defmacro lambda-list keyword &environment may appear only at the
top-level, first in the defmacro lambda-list if &whole is not supplied, or
immediately after the variable that follows &whole, if &whole is supplied.
&environment is not allowed within pseudo-var.  Like &whole, use of
&environment does not affect the processing of the rest of the defmacro
lambda-list.  If an &environment parameter is supplied and if this
parameter is not used at all, then the KCL compiler will issue a warning.
To suppress the warning, just remove the parameter from the defmacro
lambda-list, or add an ignore declaration.

     The defmacro lambda-list keyword &body is completely equivalent to the
&rest keyword.  KCL takes no special action for &body parameters.

     Although useless, KCL allows supplied-p parameters to be destructured.
This is useless because supplied-p parameters can never be bound to a
non-empty list.  Our intention is to stick to the specification in the
Common Lisp Reference Manual as far as possible, even if it is silly to do
so.

     Like for ordinary lambda-lists, the interpreter detects invalid
arguments to macro expansion functions.  When a parameter is destructured,
the structure of the corresponding argument is also checked.  Such runtime
argument checking may or may not be embedded in compiled code, depending on
the environment when the code was generated.  If the code was generated
while the safety optimize level is zero (that is, while the value of
(proclamation '(optimize (safety 0))) is t), then the generated code does
not perform argument checking at all.  Otherwise, the compiled code does
check the validity of arguments.





                    Chapter 10. The C Language Interface


This chapter describes the facility of KCL to interface the C language and
KCL.  With this facility, the user can arrange his or her C-language
programs so that they can be invoked from KCL.  In addition, the user can
write Lisp function definitions in the C language to increase runtime
efficiency.

     The basic idea of interfacing the C language is this:  As mentioned in
Chapter 6, the KCL compiler, given a Lisp source file, creates an
intermediate C-language program file, called c-file, which is then compiled
by the C-language compiler to obtain the final fasl-file.  Usually, the
c-file consists of C-language function definitions.  The first C-language
function in the c-file is the "initializer", which is executed when the
fasl file is loaded, and the other C-language functions are the C versions
of the Lisp functions (including macro expansion functions) defined in the
source file.  By using the top-level macros Clines and defCfun described
below, the user can direct the compiler to insert his or her own C-language
function definitions and/or C-language preprocessor macros such as #define
and #include into the c-file.  In order that such C-language functions be
invoked from KCL, another top-level macro defentry is used.  This macro
defines a Lisp function whose body consists of the calling sequence to the
specified C-language function.

     The C-language function definitions are placed in the c-file in the
order of the corresponding Lisp functions defined in the source file.  That
is, the C code for the first Lisp function comes first, the C code for the
second Lisp function comes second, and so on.  If a Clines or defCfun macro
form appears between two Lisp function definitions in the source file, then
the C code specified by the macro is placed in between the C code for the
Lisp functions.

     We define some terminology here which is used throughout this Chapter.
A C-id is either a Lisp string consisting of a valid C-language identifier,
or a Lisp symbol whose print-name, with all its alphabetic characters
turned into lower case, is a valid C identifier.  Thus the symbol foo is
equivalent to the string "foo" when used as a C-id.  Similarly, a C-expr is
a string or a symbol that may be regarded as a C-language expression.  A
C-type is one of the Lisp symbols int, char, float, double, and object.
Each corresponds to a data type in the C language; object is the type of
Lisp object and other C-types are primitive data types in the C language.


Clines {string}*                                            [Macro]

When the KCL compiler encounters a macro form (Clines string1 ... stringn),
it simply outputs the strings into the c-file.  The arguments are not
evaluated and each argument must be a string.  Each string may consist of
any number of lines, and separate lines in the string are placed in
separate lines in the c-file.  In addition, each string opens a fresh line
in the c-file, i.e., the first character in the string is placed at the
first column of a line.  Therefore, C-language preprocessor commands such
as #define and #include will be recognized as such by the C compiler, if
the '#' sign appears as the first character of the string or as the first
character of a line within the string.

     In order to clearly distinguish C code from other parts of Lisp programs,
we, the implementors of KCL, make it our rule to start each C code line
with a percent sign '%'.  We define % as a read macro
which returns the rest of the line as a string.  For example,
 
        ;;; C version of TAK.
        (Clines

        %       int tak(x, y, z)
        %       int x, y, z;
        %       {       if (y >= x) return(z);
        %               else return(tak(tak(x-1, y, z),
        %                               tak(y-1, z, x),
        %                               tak(z-1, x, y)));
        %       }

        )

Of course, the user may instead enclose each C code line or the whole C
code with double quotes, but we recommend the use of the percent sign read
macro.  Since the percent sign read macro is not a standard read macro, the
users must define this read macro by themselves.  We use the following
definition.

        (set-macro-character
            #\%
            #'(lambda (stream char) (values (read-line stream)))))

Here, the lambda-expression returns the first value of read-line by using
values as a filter.

     When interpreted, a Clines macro form expands to nil.


defentry function parameter-list C-function         [Macro]

defentry defines a Lisp function whose body consists of the calling
sequence to a C-language function.  function is the name of the Lisp
function to be defined, and C-function specifies the C function to be
invoked.  C-function must be either a list (type C-id) or C-id, where type
and C-id are the type and the name of the C function.  type must be a
C-type or the symbol void which means that the C function returns no value.
(object C-id) may be abbreviated as C-id.  parameter-list is a list of
C-types for the parameters of the C function.  For example, the following
defentry form defines a Lisp function tak from which the C function tak
above is called.

        (defentry tak (int int int) (int tak))

The Lisp function tak defined by this defentry form requires three
arguments.  The arguments are converted to int values before they are
passed to the C function.  On return from the C function, the returned int
value is converted to a Lisp integer (actually a fixnum) and this fixnum
will be returned as the value of the Lisp function.  See below for type
conversion between Lisp and the C language.

     A defentry form is treated in the above way only when it appears as a
top-level form of a Lisp source file.  Otherwise, a defentry form expands
to nil.


defla name lambda-list {declaration | doc-string}* {form}*       [Macro]

When interpreted, defla is exactly the same as defun.  That is, (defla name
lambda-list . body) expands to (defun name lambda-list . body).  However,
defla forms are completely ignored by the compiler; no C-language code will
be generated for defla forms.  The primary use of defla is to define a Lisp
function in two ways within a single Lisp source file; one in the C
language and the other in Lisp.  defla is short for DEFine Lisp
Alternative.

     Suppose you have a Lisp source file whose contents are:

        ;;; C version of TAK.
        (Clines

        %       int tak(x, y, z)
        %       int x, y, z;
        %       {       if (y >= x) return(z);
        %               else return(tak(tak(x-1, y, z),
        %                               tak(y-1, z, x),
        %                               tak(z-1, x, y)));
        %       }

        )

        ;;;  TAK calls the C function tak defined above.
        (defentry tak (int int int) (int tak))

        ;;; The alternative Lisp definition of TAK.
        (defla tak (x y z)
         (if (>= y x)
         z
         (tak (tak (1- x) y z)
         (tak (1- y) z x)
         (tak (1- z) x y))))

When this file is loaded into KCL, the interpreter uses the Lisp version of
the tak definition.  Once this file has been compiled, and when the
generated fasl file is loaded into KCL, a function call to tak is actually
the call to the C version of tak.


defCfun header n {element}*                            [Macro]

defCfun defines a C-language function which calls Lisp functions and/or
which handles Lisp objects.  header is a string consisting of the C code
for

        the optional type-specifier of the C function,
        the function-declarator of the C function, and
        the type-decl-list of the parameters to the C function.

(For the C-language terminology, refer to The C Programming Language by
Brian W.  Kernighan and Dennis M. Ritchie.)  The rest of the C function
definition, i.e., the function-statement, is given by elements.  Each
element may be a string, in which case the string is treated in the same
way as the arguments to the Clines macro.  Or else, the element is a list
((name arg1 ... argn) place1 ... placem).  The compiler translates this
list into a calling sequence to the Lisp function whose name is name.  As
will be mentioned later, name may be quote, but name may not be the name of
any other special form or a macro.  The args specify the arguments to the
function and the places specify where the values should go.  Thus the
list-formed element could be regarded as something like the Lisp form:

        (multiple-value-setq
            (place1 ... placem)
            (name arg1 ... argn)).

Each arg is a list (C-type C-expr), where C-expr is any C-language
expression of the  type C-type.  If type is object, then arg may be written
simply as C-expr.  Similarly, each place is a list (C-type C-expr), or it
may be abbreviated as C-expr if C-type is object.  The C-expr in this case
is any lvalue (in the terminology of the C language), i.e., it may be any
valid C-language code that can be written at the left side of an
assignment.

     The function call is performed as follows.  The args are evaluated,
and the values are sent to the specified Lisp function after type
conversion from C to Lisp.  On return from the called Lisp function, each
returned value is assigned to the corresponding place, i.e., the first
returned value goes to place1, the second to place2, and so on.  If there
are more places than the values returned, extra values of nil are assigned
to the remaining places.  If there are more values than places, the excess
values are simply discarded.  If necessary, Lisp-to-C type conversion may
take place before each returned value is assigned.

     If the Lisp function is called just for side-effects, then the
list-formed element may be abbreviated as a one-level list (name arg1 ...
argn).

     As a special case, if a list-formed element is of the form ((quote
value) place), the Lisp object value is assigned to place.  Here value may
be any Lisp object.

     The following defCfun form defines the C function silly which adds 100
to the value of the parameter x and prints the result in three different
ways.  The second argument to defCfun will be described later, and the user
may ignore it.

        (defCfun "silly(x) int x;" 0
        %       int y;
                ((+ (int x) (int "100")) (int y))
        %       printf("\\n%d", y);
        %       y = x+100;
                (print (int y))
                (print (int "x+100"))
        )

     When a C function handles Lisp objects (i.e., data of type object),
the user should be careful enough so that the objects may not be
garbage-collected.  This is because the garbage collector of KCL does not
take care of Lisp objects used in the C function.  See the following C
function which is assumed to return a two-element list consisting of its
two arguments.

        (defCfun "object list2(x,y) object x,y;" 0
        %       object z;
                ('nil z)
                ((cons y z) z)
                ((cons x z) z)
        %       return(z);
        )

When invoked, list2 first sets nil to the variable z, conses y to z, and
then conses x.  Each time cons is called, a new cons cell is allocated and
the pointer to this cell is stored in z.  However, there is no way to
inform the garbage collector that the cells are referenced from the C
variable z.  Suppose that the cons cell allocated by the first cons is the
last cons cell available at that time.  Then, during execution of the
second call to cons, the garbage collector begins to run and,
unfortunately, the cons cell in z will be destroyed so that the cell can be
recycled for further use.

     To prevent a Lisp object from being unexpectedly garbage 
collected, the user must save the object in some place that is 
recognized by the garbage collector.  The second parameter n 
to defCfun is used to reserve n such places for each call to the
C function.  In the body of the C function, these reserved places 
are referenced as vs[0], ..., vs[n-1].  The function list2 above, 
therefore, should be revised as follows.

        (defCfun "object list2(x,y) object x,y;" 1
                ('nil "vs[0]")
                ((cons y "vs[0]") "vs[0]")
                ((cons x "vs[0]") "vs[0]")
        %       Creturn(vs[0]);
        )

Notice that return is replaced by Creturn.  Creturn is similar to return
except that Creturn releases the reserved places on return from the
function.  In the C code within a defCfun form, write "Creturn(value);"
instead of "return(value);", and write "Cexit;" instead of "return;".

     Again, a defCfun form has the above meaning only when it appears as a
top-level form in a Lisp source file.  Otherwise, the form expands to nil.

     KCL converts a Lisp object into a C-language data by using the Common
Lisp function coerce: For the C-type int (or char), the object is first
coerced to a Lisp integer and the least significant 32-bit (or 8-bit) field
is used as the C int (or char).  For the C-type float (or double), the
object is coerced to a short-float (or a long-float) and this value is used
as the C float (or double).  Conversion from a C data into a Lisp object is
obvious: C char, int, float, and double become the equivalent Lisp
character, fixnum, short-float, and long-float, respectively.

     Here we list the complete syntax of Clines, defentry, 
and defCfun macro forms.

        Clines-form:
                (Clines { string }* )

        defentry-form:
                (defentry function-symbol
                        ( { C-type }* )
                 C-function-name | ( { C-type | void } C-function-name ) } )

        defCfun-form:
                (defCfun string  non-negative-integer
                        { string
                          | (function-symbol { value }* )
                          | ((function-symbol { value }* ) { place }* ) } )

        value:
        place:
                { C-expr | (C-type C-expr) }

        C-function-name:
        C-expr:
                { string | symbol }

        C-type:
                { object | int | char | float | double }

 



                              Chapter 11. The Editor



KCL/AOS is equipped with a screen editor FeCl2 (Full-screen Editor as a
Common Lisp TOOl).  FeCl2 is an EMACS-like editor with facilities for Lisp
coding.  FeCl2 is invoked from KCL by the function ed and the result of
editing can be passed to KCL directly.  For the details of FeCl2 refer to
The FeCl2 Editor Reference Manual.

ed &optional filename                                    [Function]

ed invokes FeCl2 and sets the edit file of FeCl2 to filename.  If the
filetype of the file is not explicitly specified, then the filename is
first merged into #".lsp".


The FeCl2 editor is not supported by other versions of KCL.  The function
ed of KCL/VAX, KCL/SUN, and KCL/UST calls the vi editor.  If you hate vi,
define your own ed function using the function system described in Chapter
8.






                           Appendix A. KCL Summary


The following table lists all symbols defined in KCL.  Each line has the
following form.

       symbol   [kind]   remark

where kind is Function, Macro, Special (i.e., Special form name), Variable,
Constant, Symbol, or Keyword.  In the table, some symbols are labeled both
as a macro and a special form name.  This means that, although these
symbols are defined to be a macro name in the Common Lisp Reference Manual,
KCL treats them as if they were special forms (see Section 9.1).  

*                               [Function]
*                               [Variable]
**                              [Variable]
***                             [Variable]
+                               [Function]
+                               [Variable]
++                              [Variable]
+++                             [Variable]
-                               [Function]
-                               [Variable]
/                               [Function]
/                               [Variable]
//                              [Variable]
///                             [Variable]
/=                              [Function]
1+                              [Function]
1-                              [Function]
<                               [Function]
<=                              [Function]
=                               [Function]
>                               [Function]
>=                              [Function]
:abort                          [Keyword]
abs                             [Function]
acons                           [Function]
acos                            [Function]
acosh                           [Function]
adjoin                          [Function]
adjust-array                    [Function]
:adjustable                     [Keyword]
adjustable-array-p              [Function]
allocate                        [Function] Added.
allocate-contiguous-pages       [Function] Added.
allocated-contiguous-pages      [Function] Added.
allocated-pages                 [Function] Added.
allocated-relocatable-pages     [Function] Added.
allocate-relocatable-pages      [Function] Added.
alpha-char-p                    [Function]
alphanumericp                   [Function]
and                             [Special, Macro]
append                          [Function]
:append                         [Keyword]
apply                           [Function]
applyhook                       [Function]
*applyhook*                     [Variable]
apropos                         [Function]
apropos-list                    [Function]
aref                            [Function]
:array                          [Keyword]
array-dimension                 [Function]
array-dimension-limit           [Constant]
array-dimensions                [Function]
array-element-type              [Function]
array-has-fill-pointer-p        [Function]
array-in-bounds-p               [Function]
array-rank                      [Function]
array-rank-limit                [Constant]
array-row-major-index           [Function]
array-total-size                [Function]
array-total-size-limit          [Constant]
arrayp                          [Function]
ash                             [Function]
asin                            [Function]
asinh                           [Function]
assert                          [Macro]
assoc                           [Function]
assoc-if                        [Function]
assoc-if-not                    [Function]
atan                            [Function]
atanh                           [Function]
atom                            [Function]
:b                              [Keyword] Abbreviate Break Loop Command.
:backtrace                      [Keyword] Break Loop Command.
:base                           [Keyword]
bit                             [Function]
bit-and                         [Function]
bit-andc1                       [Function]
bit-andc2                       [Function]
bit-eqv                         [Function]
bit-ior                         [Function]
bit-nand                        [Function]
bit-nor                         [Function]
bit-not                         [Function]
bit-orc1                        [Function]
bit-orc2                        [Function]
bit-vector-p                    [Function]
bit-xor                         [Function]
block                           [Special]
:block                          [Keyword] Added.
:blocks                         [Keyword] Break Loop Command.
boole                           [Function]
boole-1                         [Constant]
boole-2                         [Constant]
boole-and                       [Constant]
boole-andc1                     [Constant]
boole-andc2                     [Constant]
boole-c1                        [Constant]
boole-c2                        [Constant]
boole-clr                       [Constant]
boole-eqv                       [Constant]
boole-ior                       [Constant]
boole-nand                      [Constant]
boole-nor                       [Constant]
boole-orc1                      [Constant]
boole-orc2                      [Constant]
boole-set                       [Constant]
boole-xor                       [Constant]
both-case-p                     [Function]
boundp                          [Function]
break                           [Function]
*break-on-warnings*             [Variable]
*break-enable*                  [Variable] Added.
butlast                         [Function]
by                              [Function] Added.
bye                             [Function] Added.
byte                            [Function]
byte-position                   [Function]
byte-size                       [Function]
:c                              [Keyword] Abbreviated Break Loop Command.
caaaar                          [Function]
caaadr                          [Function]
caaar                           [Function]
caadar                          [Function]
caaddr                          [Function]
caadr                           [Function]
caar                            [Function]
cadaar                          [Function]
cadadr                          [Function]
cadar                           [Function]
caddar                          [Function]
cadddr                          [Function]
caddr                           [Function]
cadr                            [Function]
call-arguments-limit            [Constant]
car                             [Function]
:case                           [Keyword]
case                            [Special, Macro]
catch                           [Special]
ccase                           [Macro]
cdaaar                          [Function]
cdaadr                          [Function]
cdaar                           [Function]
cdadar                          [Function]
cdaddr                          [Function]
cdadr                           [Function]
cdar                            [Function]
cddaar                          [Function]
cddadr                          [Function]
cddar                           [Function]
cdddar                          [Function]
cddddr                          [Function]
cdddr                           [Function]
cddr                            [Function]
cdr                             [Function]
ceiling                         [Function]
cerror                          [Function]
:c-file                         [Keyword] Added.
char                            [Function]
char-bit                        [Function]
char-bits                       [Function]
char-bits-limit                 [Constant]
char-code                       [Function]
char-code-limit                 [Constant]
char-control-bit                [Constant]
char-downcase                   [Function]
char-equal                      [Function]
char-font                       [Function]
char-font-limit                 [Constant]
char-greaterp                   [Function]
char-hyper-bit                  [Constant]
char-int                        [Function]
char-lessp                      [Function]
char-meta-bit                   [Constant]
char-name                       [Function]
char-not-equal                  [Function]
char-not-greaterp               [Function]
char-not-lessp                  [Function]
char-super-bit                  [Constant]
char-upcase                     [Function]
char/=                          [Function]
char<                           [Function]
char<=                          [Function]
char=                           [Function]
char>                           [Function]
char>=                          [Function]
character                       [Function]
characterp                      [Function]
check-type                      [Macro]
:circle                         [Keyword]
cis                             [Function]
clear-input                     [Function] Different.
clear-output                    [Function] Different.
clines                          [Macro] Added.
close                           [Function] Different.
clrhash                         [Function]
code-char                       [Function]
coerce                          [Function]
commonp                         [Function]
compilation-speed               [Symbol] Optimize Quality.
compile                         [Function]
compile-file                    [Function]
compiled-function-p             [Function]
compiler-let                    [Special]
complex                         [Function]
complexp                        [Function]
:conc-name                      [Keyword]
concatenate                     [Function]
cond                            [Special, Macro]
conjugate                       [Function]
cons                            [Function]
:console                        [Keyword] Added.
consp                           [Function]
constantp                       [Function]
:constructor                    [Keyword]
:copier                         [Keyword]
copy-alist                      [Function]
copy-list                       [Function]
copy-readtable                  [Function]
copy-seq                        [Function]
copy-symbol                     [Function]
copy-tree                       [Function]
cos                             [Function]
cosh                            [Function]
count                           [Function]
:count                          [Keyword]
count-if                        [Function]
count-if-not                    [Function]
:create                         [Keyword]
ctypecase                       [Macro]
:current                        [Keyword] Break Loop Command.
:data                           [Keyword] Added.
:data-file                      [Keyword] Added.
:debug                          [Keyword] Added.
*debug-io*                      [Variable]
decf                            [Special, Macro]
declaration                     [Symbol] Declaration Specifier.
declare                         [Special]
decode-float                    [Function]
decode-universal-time           [Function]
:default                        [Keyword]
*default-pathname-defaults*     [Variable]
:defaults                       [Keyword]
defautoload                     [Macro] Added.
defcfun                         [Macro] Added.
defconstant                     [Macro]
defentry                        [Macro] Added.
define-modify-macro             [Macro]
define-setf-method              [Macro]
defla                           [Macro] Added.
defmacro                        [Special, Macro]
defparameter                    [Macro]
defsetf                         [Macro]
defstruct                       [Macro]
deftype                         [Macro]
defun                           [Special, Macro]
defvar                          [Macro]
delete                          [Function]
delete-duplicates               [Function]
delete-file                     [Function]
delete-if                       [Function]
delete-if-not                   [Function]
denominator                     [Function]
deposit-field                   [Function]
describe                        [Function]
:device                         [Keyword]
digit-char                      [Function]
digit-char-p                    [Function]
:dir                            [Keyword] Added.
:direction                      [Keyword]
directory                       [Function]
:directory                      [Keyword]
directory-namestring            [Function]
disassemble                     [Function] Different.
:displaced-index-offset         [Keyword]
:displaced-to                   [Keyword]
do                              [Special, Macro]
do*                             [Special, Macro]
do-all-symbols                  [Macro]
do-external-symbols             [Macro]
do-symbols                      [Macro]
documentation                   [Function]
dolist                          [Special, Macro]
dotimes                         [Special, Macro]
double-float-epsilon            [Constant]
double-float-negative-epsilon   [Constant]
dpb                             [Function]
dribble                         [Function]
ecase                           [Macro]
ed                              [Function] Different.
eighth                          [Function]
:element-type                   [Keyword]
elt                             [Function]
encode-universal-time           [Function]
:end                            [Keyword]
:end1                           [Keyword]
:end2                           [Keyword]
endp                            [Function]
enough-namestring               [Function]
&environment                    [Symbol] Defmacro-lambda Keyword.
eq                              [Function]
eql                             [Function]
equal                           [Function]
equalp                          [Function]
error                           [Function]
:error                          [Keyword]
*error-output*                  [Variable]
:escape                         [Keyword]
etypecase                       [Macro]
eval                            [Function]
evalhook                        [Function]
*evalhook*                      [Variable]
eval-when                       [Macro]
*eval-when-compile*             [Variable] Added.
evenp                           [Function]
every                           [Function]
exp                             [Function]
export                          [Function]
expt                            [Function]
:external                       [Keyword]
:fasl-file                      [Keyword] Added.
fboundp                         [Function]
fceiling                        [Function]
*features*                      [Variable]
ffloor                          [Function]
fifth                           [Function]
file-author                     [Function]
file-length                     [Function]
file-namestring                 [Function]
file-position                   [Function]
file-write-date                 [Function]
fill                            [Function]
fill-pointer                    [Function]
:fill-pointer                   [Keyword]
find                            [Function]
find-all-symbols                [Function]
find-if                         [Function]
find-if-not                     [Function]
find-package                    [Function]
find-symbol                     [Function]
finish-output                   [Function]
first                           [Function]
flet                            [Special]
float                           [Function]
float-digits                    [Function]
float-precision                 [Function]
float-radix                     [Function]
float-sign                      [Function]
floatp                          [Function]
floor                           [Function]
fmakunbound                     [Function]
force-output                    [Function]
format                          [Function]
fourth                          [Function]
fresh-line                      [Function]
:from-end                       [Keyword]
fround                          [Function]
ftruncate                       [Function]
ftype                           [Symbol] Declaration Specifier.
funcall                         [Function]
function                        [Special] Also Declaration Specifier.
functionp                       [Function]
:functions                      [Keyword] Break Loop Command.
gbc                             [Function] Added.
gcd                             [Function]
gensym                          [Function]
:gensym                         [Keyword]
gentemp                         [Function]
get                             [Function]
get-decoded-time                [Function]
get-dispatch-macro-character    [Function]
get-internal-real-time          [Function]
get-internal-run-time           [Function]
get-macro-character             [Function]
get-output-stream-string        [Function]
get-properties                  [Function]
get-setf-method                 [Function]
get-setf-method-multiple-value  [Function]
get-universal-time              [Function]
getf                            [Function]
gethash                         [Function]
go                              [Special]
graphic-char-p                  [Function]
hash-table-count                [Function]
hash-table-p                    [Function]
:h                              [Keyword] Abbreviated Break Loop Command.
:help                           [Keyword] Break Loop Command.
:h-file                         [Keyword] Added.
:hide                           [Keyword] Break Loop Command.
:hide-package                   [Keyword] Break Loop Command.
:host                           [Keyword]
host-namestring                 [Function]
identity                        [Function]
if                              [Special]
:if-does-not-exist              [Keyword]
:if-exists                      [Keyword]
ignore                          [Symbol] Declaration Specifier.
*ignore-maximum-pages*          [Variable] Added.
imagpart                        [Function]
import                          [Function]
in-package                      [Function]
incf                            [Special, Macro]
:include                        [Keyword]
:index                          [Keyword]
:inherited                      [Keyword]
:initial-contents               [Keyword]
:initial-element                [Keyword]
:initial-offset                 [Keyword]
:initial-value                  [Keyword]
inline                          [Symbol] Declaration Specifier.
:input                          [Keyword]
input-stream-p                  [Function]
inspect                         [Function]
int-char                        [Function]
integer-decode-float            [Function]
integer-length                  [Function]
integerp                        [Function]
intern                          [Function]
:intern                         [Keyword]
internal-time-units-per-second  [Constant]
intersection                    [Function]
:io                             [Keyword]
:ioc                            [Keyword] Added.
isqrt                           [Function]
:junk-allowed                   [Keyword]
:key                            [Keyword]
keywordp                        [Function]
:l                              [Keyword] Abbreviated Break Loop Command.
labels                          [Special]
lambda-list-keywords            [Constant]
lambda-parameters-limit         [Constant]
last                            [Function]
last-termination-message        [Function] Added.
lcm                             [Function]
ldb                             [Function]
ldb-test                        [Function]
ldiff                           [Function]
least-negative-double-float     [Constant]
least-negative-long-float       [Constant]
least-negative-short-float      [Constant]
least-negative-single-float     [Constant]
least-positive-double-float     [Constant]
least-positive-long-float       [Constant]
least-positive-short-float      [Constant]
least-positive-single-float     [Constant]
length                          [Function]
:length                         [Keyword]
let                             [Special]
let*                            [Special]
:level                          [Keyword]
lisp-implementation-type        [Function]
lisp-implementation-version     [Function]
list                            [Function]
:list                           [Keyword] Added.
list*                           [Function]
list-all-packages               [Function]
list-length                     [Function]
listen                          [Function] Different.
listp                           [Function]
load                            [Function]
*load-verbose*                  [Variable]
:local                          [Keyword] Break Loop Command.
locally                         [Special, Macro]
log                             [Function]
logand                          [Function]
logandc1                        [Function]
logandc2                        [Function]
logbitp                         [Function]
logcount                        [Function]
logeqv                          [Function]
logior                          [Function]
lognand                         [Function]
lognor                          [Function]
lognot                          [Function]
logorc1                         [Function]
logorc2                         [Function]
logtest                         [Function]
logxor                          [Function]
long-float-epsilon              [Constant]
long-float-negative-epsilon     [Constant]
long-site-name                  [Function]
loop                            [Special, Macro]
lower-case-p                    [Function]
machine-instance                [Function]
machine-type                    [Function]
machine-version                 [Function]
macro-function                  [Function]
macroexpand                     [Function]
macroexpand-1                   [Function]
*macroexpand-hook*              [Variable]
macrolet                        [Special]
make-array                      [Function]
make-broadcast-stream           [Function]
make-char                       [Function]
make-concatenated-stream        [Function]
make-dispatch-macro-character   [Function]
make-echo-stream                [Function]
make-hash-table                 [Function]
make-list                       [Function]
make-package                    [Function]
make-pathname                   [Function]
make-random-state               [Function]
make-sequence                   [Function]
make-string                     [Function]
make-string-input-stream        [Function]
make-string-output-stream       [Function]
make-symbol                     [Function]
make-synonym-stream             [Function]
make-two-way-stream             [Function]
makunbound                      [Function]
map                             [Function]
mapc                            [Function]
mapcan                          [Function]
mapcar                          [Function]
mapcon                          [Function]
maphash                         [Function]
mapl                            [Function]
maplist                         [Function]
mask-field                      [Function]
max                             [Function]
maximum-allocatable-pages       [Function] Added.
maximum-contiguous-pages        [Function] Added.
member                          [Function]
member-if                       [Function]
member-if-not                   [Function]
merge                           [Function]
merge-pathnames                 [Function]
min                             [Function]
minusp                          [Function]
mismatch                        [Function]
mod                             [Function]
*modules*                       [Variable]
most-negative-double-float      [Constant]
most-negative-fixnum            [Constant]
most-negative-long-float        [Constant]
most-negative-short-float       [Constant]
most-negative-single-float      [Constant]
most-positive-double-float      [Constant]
most-positive-fixnum            [Constant]
most-positive-long-float        [Constant]
most-positive-short-float       [Constant]
most-positive-single-float      [Constant]
multiple-value-bind             [Special, Macro]
multiple-value-call             [Special]
multiple-value-list             [Special, Macro]
multiple-value-prog1            [Special]
multiple-value-setq             [Special, Macro]
multiple-values-limit           [Constant]
:n                              [Keyword] Abbreviated Break Loop Command.
:name                           [Keyword]
name-char                       [Function]
:named                          [Keyword]
namestring                      [Function]
nbutlast                        [Function]
nconc                           [Function]
:new-version                    [Keyword]
:next                           [Keyword] Break Loop Command.
nil                             [Constant]
nintersection                   [Function]
ninth                           [Function]
not                             [Function]
notany                          [Function]
notevery                        [Function]
notinline                       [Symbol] Declaration Specifier.
nreconc                         [Function]
nreverse                        [Function]
nset-difference                 [Function]
nset-exclusive-or               [Function]
nstring-capitalize              [Function]
nstring-downcase                [Function]
nstring-upcase                  [Function]
nsublis                         [Function]
nsubst                          [Function]
nsubst-if                       [Function]
nsubst-if-not                   [Function]
nsubstitute                     [Function]
nsubstitute-if                  [Function]
nsubstitute-if-not              [Function]
nth                             [Function]
nthcdr                          [Function]
null                            [Function]
numberp                         [Function]
numerator                       [Function]
nunion                          [Function]
:ob-file                        [Keyword] Added.
object                          [Symbol] Declaration Specifier.  Added.
oddp                            [Function]
:o-file                         [Keyword] Added.
open                            [Function] Different.
optimize                        [Symbol] Declaration Specifier.
or                              [Special, Macro]
:output                         [Keyword]
:output-file                    [Keyword]
output-stream-p                 [Function]
:overwrite                      [Keyword]
*package*                       [Variable]
package-name                    [Function]
package-nicknames               [Function]
package-shadowing-symbols       [Function]
package-use-list                [Function]
package-used-by-list            [Function]
packagep                        [Function]
pairlis                         [Function]
:parent                         [Keyword] Added.
parse-integer                   [Function]
parse-namestring                [Function]
pathname                        [Function]
pathname-device                 [Function]
pathname-directory              [Function]
pathname-host                   [Function]
pathname-name                   [Function]
pathname-type                   [Function]
pathname-version                [Function]
pathnamep                       [Function]
peek-char                       [Function]
phase                           [Function]
pi                              [Constant]
plusp                           [Function]
pop                             [Macro]
position                        [Function]
position-if                     [Function]
position-if-not                 [Function]
pprint                          [Function]
:p                              [Keyword] Abbreviate Break Loop Command.
:predicate                      [Keyword]
:preserve-whitespace            [Keyword]
:pretty                         [Keyword]
:previous                       [Keyword] Break Loop Command.
prin1                           [Function]
prin1-to-string                 [Function]
princ                           [Function]
princ-to-string                 [Function]
print                           [Function]
:print                          [Keyword]
*print-array*                   [Variable]
*print-base*                    [Variable]
*print-case*                    [Variable]
*print-circle*                  [Variable]
*print-escape*                  [Variable]
:print-function                 [Keyword]
*print-gensym*                  [Variable]
*print-length*                  [Variable]
*print-level*                   [Variable]
*print-pretty*                  [Variable]
*print-radix*                   [Variable]
:probe                          [Keyword]
probe-file                      [Function]
process                         [Function] Added.
proclaim                        [Function]
proclamation                    [Function] Added.
prog                            [Special, Macro]
prog*                           [Special, Macro]
prog1                           [Special, Macro]
prog2                           [Special, Macro]
progn                           [Special]
progv                           [Special]
provide                         [Function]
psetf                           [Macro]
psetq                           [Special, Macro]
push                            [Special, Macro]
pushnew                         [Macro]
:q                              [Keyword] Abbreviated Break Loop Command.
*query-io*                      [Variable]
:quit                           [Keyword] Break Loop Command.
quote                           [Special]
:r                              [Keyword] Abbreviated Break Loop Command.
:radix                          [Keyword]
random                          [Function]
*random-state*                  [Variable]
random-state-p                  [Function]
rassoc                          [Function]
rassoc-if                       [Function]
rassoc-if-not                   [Function]
rational                        [Function]
rationalize                     [Function]
rationalp                       [Function]
read                            [Function]
*read-base*                     [Variable]
read-byte                       [Function] Different.
read-char                       [Function]
read-char-no-hang               [Function] Different.
*read-default-float-format*     [Variable]
read-delimited-list             [Function]
read-from-string                [Function]
read-line                       [Function]
:read-only                      [Keyword]
read-preserving-whitespace      [Function]
*read-suppress*                 [Variable]
*readtable*                     [Variable]
readtablep                      [Function]
realpart                        [Function]
reduce                          [Function]
:rehash-size                    [Keyword]
:rehash-threshold               [Keyword]
rem                             [Function]
remf                            [Macro]
remhash                         [Function]
remove                          [Function]
remove-duplicates               [Function]
remove-if                       [Function]
remove-if-not                   [Function]
remprop                         [Function]
:rename                         [Keyword]
:rename-and-delete              [Keyword]
rename-file                     [Function]
rename-package                  [Function]
replace                         [Function]
require                         [Function]
:resume                         [Keyword] Break Loop Command.
rest                            [Function]
return                          [Special, Macro]
return-from                     [Special]
revappend                       [Function]
reverse                         [Function]
room                            [Function]
:root                           [Function] Added.
rotatef                         [Macro]
round                           [Function]
rplaca                          [Function]
rplacd                          [Function]
safety                          [Symbol] Optimize Quality.
save                            [Function] Added.
sbit                            [Function]
scale-float                     [Function]
schar                           [Function]
search                          [Function]
second                          [Function]
set                             [Function]
set-char-bit                    [Function]
set-difference                  [Function]
set-dispatch-macro-character    [Function]
set-exclusive-or                [Function]
set-macro-character             [Function]
set-syntax-from-char            [Function]
setf                            [Special, Macro]
setq                            [Special]
seventh                         [Function]
shadow                          [Function]
shadowing-import                [Function]
shiftf                          [Macro]
short-float-epsilon             [Constant]
short-float-negative-epsilon    [Constant]
short-site-name                 [Function]
signum                          [Function]
simple-bit-vector-p             [Function]
simple-string-p                 [Function]
simple-vector-p                 [Function]
sin                             [Function]
single-float-epsilon            [Constant]
single-float-negative-epsilon   [Constant]
sinh                            [Function]
sixth                           [Function]
:size                           [Keyword]
sleep                           [Function]
software-type                   [Function]
software-version                [Function]
some                            [Function]
sort                            [Function]
space                           [Symbol] Optimize Quality.
special                         [Symbol] Declaration Specifier.
special-form-p                  [Function]
speed                           [Symbol] Optimize Quality.
sqrt                            [Function]
stable-sort                     [Function]
standard-char-p                 [Function]
*standard-input*                [Variable]
*standard-output*               [Variable]
:start                          [Keyword]
:start1                         [Keyword]
:start2                         [Keyword]
:static                         [Keyword] Added.
step                            [Macro]
:stream                         [Keyword]
stream-element-type             [Function]
streamp                         [Function]
string                          [Function]
string-capitalize               [Function]
string-char-p                   [Function]
string-downcase                 [Function]
string-equal                    [Function]
string-greaterp                 [Function]
string-left-trim                [Function]
string-lessp                    [Function]
string-not-equal                [Function]
string-not-greaterp             [Function]
string-not-lessp                [Function]
string-right-trim               [Function]
string-trim                     [Function]
string-upcase                   [Function]
string/=                        [Function]
string<                         [Function]
string<=                        [Function]
string=                         [Function]
string>                         [Function]
string>=                        [Function]
stringp                         [Function]
sublis                          [Function]
subseq                          [Function]
subsetp                         [Function]
subst                           [Function]
subst-if                        [Function]
subst-if-not                    [Function]
substitute                      [Function]
substitute-if                   [Function]
substitute-if-not               [Function]
subtypep                        [Function]
:supersede                      [Keyword]
svref                           [Function]
sxhash                          [Function]
symbol-function                 [Function]
symbol-name                     [Function]
symbol-package                  [Function]
symbol-plist                    [Function]
symbol-value                    [Function]
symbolp                         [Function]
system                          [Function] Added.
t                               [Constant]
:tags                           [Keyword] Break Loop Command.
tagbody                         [Special]
tailp                           [Function]
tan                             [Function]
tanh                            [Function]
tenth                           [Function]
*terminal-io*                   [Variable] Different.
termination-message             [Function] Added.
terpri                          [Function]
:test                           [Keyword]
:test-not                       [Keyword]
the                             [Special]
third                           [Function]
throw                           [Special]
time                            [Macro]
trace                           [Macro]
*trace-output*                  [Variable]
tree-equal                      [Function]
truename                        [Function]
truncate                        [Function]
type                            [Symbol] Declaration Specifier.
:type                           [Keyword]
type-of                         [Function]
typecase                        [Macro]
typep                           [Function]
unexport                        [Function]
unintern                        [Function]
union                           [Function]
:unhide                         [Keyword] Break Loop Command.
:unhide-package                 [Keyword] Break Loop Command.
unless                          [Special, Macro]
unread-char                     [Function]
untrace                         [Macro]
unuse-package                   [Function]
unwind-protect                  [Special]
upper-case-p                    [Function]
use-package                     [Function]
user-homedir-pathname           [Function]
:username                       [Keyword] Added.
:v                              [Keyword] Abbreviated Break Loop Command.
values                          [Function]
values-list                     [Function]
:variables                      [Keyword] Break Loop Command.
vector                          [Function]
vector-pop                      [Function]
vector-push                     [Function]
vector-push-extend              [Function]
vectorp                         [Function]
:verbose                        [Keyword]
:version                        [Keyword]
warn                            [Function]
when                            [Special, Macro]
&whole                          [Symbol] Defmacro-lambda Keyword.
:wild                           [Keyword] Added.
with-input-from-string          [Macro]
with-open-file                  [Macro]
with-open-stream                [Macro]
with-output-to-string           [Macro]
write                           [Function]
write-byte                      [Function] Different.
write-char                      [Function]
write-line                      [Function]
write-string                    [Function]
write-to-string                 [Function]
y-or-n-p                        [Function]
yes-or-no-p                     [Function]
zerop                           [Function]









                    Appendix B. An Overview of Kyoto Common Lisp


Kyoto Common Lisp (KCL for short) is a full implementation of the Common
Lisp language.  KCL is a highly portable Common Lisp system intended for
several classes of machines, from mini/micro to mainframe.  The key idea
behind the portability is the use of the C language and its standard
libraries as the interface with the underlying machines and operating
systems:  The kernel of the system is written in C and the rest of the
system is written in Common Lisp.  Even the compiler generates intermediate
code in C.  KCL is also an efficient and compact system:  KCL regards the
runtime efficiency of interpreted code as important as the efficiency of
compiled code.  The small size of the KCL system makes KCL suitable for the
current computer technology, such as the use of virtual memory and cache
memory.  This document reports the current status of KCL, its
implementation, and system performance.  This document is a draft:  the
description is still incomplete and informal, and some technical terms are
used without definition or explanation.  A full paper on the KCL
implementation is in preparation.


KCL is a full Common Lisp system.

KCL is a full implementation of the Common Lisp language described in
the Common Lisp Reference Manual:


                 Common Lisp: The Language.
                 by Guy L. Steele et al.
                 Digital Press, 1984

KCL supports all Common Lisp functions, macros, and special forms defined
in the Common Lisp Reference Manual.  All Common Lisp variables and
constants are defined in KCL exactly as described in the Common Lisp
Reference Manual.



KCL is available on several machines already.

Currently, there are four major versions of KCL:

        1. KCL/AOS 
           Machine: Data General's Eclipse MV series super-minicomputers 
           (MV10000, MV8000, MV6000, and MV4000)
           Operating System: Data General's original AOS/VS 
           (Advanced Operating System / Virtual Storage)

        2. KCL/VAX
           Machine: Digital Equipment Corporation's VAX 11 
           series machines (VAX 11/780 and VAX 11/750)
           Operating System: UNIX 4.2 bsd

        3. KCL/SUN
           Machine: Sun Microsystems' Sun Workstation (MC68000 base)
           Operating System: UNIX 4.2 bsd

        4. KCL/UST
           Machine: Sumitomo Electric Industries and Digital 
           Computer Laboratory's personal workstation Ustation E15 
           (MC68000 base) 
           Operating System: UNIX V (Uniplus' version)

KCL/AOS is the original version of KCL, which was developed at Research
Institute for Mathematical Sciences (RIMS), Kyoto University, with the
cooperation of Nippon Data General Corporation.  Other versions are ported
from KCL/AOS at RIMS.  All four versions share most of the source files of
KCL.  Improvements and error corrections are performed on the common source
files, and the most recent revisions are brought to each machine from time
to time.

Ports to other machines and other operating systems are being undertaken or
are in preparation at other organizations.  KCL is expected to become
available on the following machines in the near future.

        * IBM (and IBM-compatible) M series machines
        * Apollo Domain
        * Perkins Elmer
        * VAX 11 (running VMS)
        * VAX 11 (running Eunice, the Unix emulator)
        * Eclipse MV (running DGUX, Data General's native Unix)


KCL is written in C and Lisp

The kernel of KCL is written in C, including:

        * memory management and garbage collection
        * the evaluator (or interpreter)
        * Common Lisp special forms

The KCL compiler is entirely written in Common Lisp.

Each Common Lisp function or macro is written either in C or in Lisp.

        in C:
                418 Common Lisp functions
                11 Common Lisp macros

        in Lisp:
                133 Common Lisp functions
                59 Common Lisp macros

The size of the source code is:

        C code           705 Kbytes
        Common Lisp functions and macros written in Lisp
                         173 Kbytes
        The compiler     264 Kbytes
        -------------------------
                total   1142 Kbytes

Three routines in the kernel are partly written in assembly language.
These routines are:

        * bignum multiplication
        * bignum division
        * bit table manipulation of the garbage collector

The total size of assembly code is 20 to 30 lines, depending on the version
of KCL.



KCL/AOS is built up by old-fashioned bootstrapping

When KCL/AOS, the original version of KCL, was born, the following steps
were taken to build it up.

        1. Compile all C code with the C compiler and link them all.  A
subset of KCL is ready to run at this moment.

        2. Load all Lisp code into KCL.  Now the full system is ready to
run, although the compiler and some Common Lisp functions and macros run
interpretively.

        3. Compile the source files of the KCL compiler with the
(interpreted) KCL compiler itself.  Load each Fasl-file (i.e., the file
created by the KCL compiler) immediately after it is generated.  The
compilation process becomes faster toward the end of this step.  Finally,
the whole KCL compiler is ready to run by itself.

        4. Compile the Common Lisp functions and macros written in Lisp,
with the compiled KCL compiler.  Load the Fasl-files.  This completes the
generation of the full system.

The same steps are taken whenever drastic changes are made to the kernel.
On the other hand, the procedure to port KCL or to revise the ported
versions of KCL is much simpler, because all Lisp code has been
cross-compiled by the compiler of KCL/AOS beforehand.

Objects are represented by cells.

KCL does not support the so-called immediate data.  Any KCL object is
represented as (a pointer to) a cell that is allocated on the heap.  Each
cell consists of several words (1 word = 32 bit) whose first word is in the
format common to all data types: half of the word is the type indicator and
the other half is used as the mark by the garbage collector.  For instance,
a cons cell consists of three words:

                ------------------------
                |  'CONS'  |  mark-bit |
                ------------------------
                |      car-pointer     |
                ------------------------
                |      cdr-pointer     |
                ------------------------

and a fixnum cell consists of two words:

                ------------------------
                | 'FIXNUM' |  mark-bit |
                ------------------------
                |    fixnum-value      |
                ------------------------

Array headers and compiled-function headers are represented in this way, and
array elements and compiled code are placed elsewhere.

Internally in compiled functions, certain Lisp objects may be represented
simply by their values.  For example, a fixnum object may be represented by
its fixnum value, and a character object may be represented by its
character code.

Cells of small fixnums ranging from -1024 to 1023 and cells of characters
are pre-allocated in fixed locations.  Thus, for example,

        (eq 1023 1023)

yields t, whereas

        (eq 1024 1024)

yields nil.



The heap is divided into pages.

The whole heap of KCL is divided into pages (1 page = 2048 bytes).  Each page
falls in one of the following classes:

        * pages that contain cells consisting of the same number of words
        * pages that contain binary data such as compiled function code
        * pages that contain relocatable data such as array elements

Free cells (i.e., those cells that are not used any more) consisting of the
same number of words are linked together to form a free list.  When a new
cell is requested, the first cell in the free list (if it is not empty) is
used and is removed from the list.  If the free list is empty, then the
garbage collector begins to run to collect unused cells.  If the new free
list is too short after the garbage collection, then new pages are
allocated dynamically.  Free binary data are also linked together in the
order of the size so that, when a binary datum is being allocated on the
heap, the smallest free area that is large enough to hold the binary datum
will be used.  Cell pages are never compactified.  Once a page is allocated
for cells with n words, the page is used for cells with n words only, even
after all the cells in the page become garbage.  The same rule holds for
binary pages.  In contrast, relocatable pages are sometimes compactified.
That is, each relocatable datum may be moved to another place.

The actual configuration of the KCL heap is:

  lower address                                             higher address
        ----------------------------------------------------------------
        |  cell pages and binary pages  |  hole  |  relocatable pages  |
        ----------------------------------------------------------------

There is a "hole" between the area for cell/binary pages and the area for
relocatable pages.  New pages are allocated in the hole for cell/binary
pages, whereas new relocatable pages are allocated by expanding the heap to
the higher address, i.e., to the right in this figure.  When the hole
becomes empty, the area for relocatable pages are shifted to the right to
reserve a certain number of pages as the hole.  During this process, the
relocatable data in the relocatable pages are compactified.  No free list
is maintained for relocatable data.

Symbol print names and string bodies are usually allocated in relocatable
pages.  However, when the KCL system is created, i.e., when the object
module of KCL is created, such relocatable data are moved towards the area
for cell/binary pages and then the pages for relocatable data are marked
"static".  The garbage collector never tries to sweep static pages.  Thus,
within the object module of KCL, the heap looks like:

  lower address                        higher address
        ----------------------------------------
        |  cell/binary pages and static pages  |
        ----------------------------------------

Notice that the hole is not included in the object module; it is allocated
only when the KCL system is started.  This saves secondary storage
a little bit.  The maximum size of the hole is about
100 pages (= 200 Kbytes).



KCL uses five stacks.

KCL uses the following stacks.

        * Value Stack, for
             arguments/values passing
             lexical variables allocation
             temporary values saving

        * Frame Stack, consisting of
             catch, block, tagbody frames

        * Bind Stack, for
             shallow binding of dynamic variables

        * Invocation History Stack, maintaining
             information for debugging

        * C Language Control Stack, sometimes used in compiled functions for:
             arguments/values passing
             typed lexical variables allocation
             temporary values saving,
          in addition to the obvious use such as function invocation


Arguments/values are passed via the value stack.

To show the argument/value passing mechanism, here we list the actual code
for the Common Lisp function cons.

        Lcons()
        {
                object x;
                check_arg(2);
                x = alloc_object(t_cons);
                x->c.c_car = vs_base[0];
                x->c.c_cdr = vs_base[1];
                vs_base[0] = x;
                vs_pop;
        }

We adopted the convention that the name of a function that implements a
Common Lisp function begins with 'L', followed by the name of the Common
Lisp function.  (Strictly speaking, '-' and '*' in the Common Lisp function
name are replaced by '_' and 'A', respectively, to obey the syntax of C.)
Arguments to functions are pushed on the value stack.  The stack pointer
vs_base (value stack base) points to the first argument and another pointer
vs_top points to the stack location next to the last argument.  Thus, for
example, when cons is called with the first argument 1 and the second
argument 2, the value stack looks like:

                  4---------6
         vs_top ->|         |
                  -----------
                  |    2    |
                  -----------
        vs_base ->|    1    |
                  -----------
                  |         |
                  :         :
                  |         |
          bottom  -----------
                  value stack

check_arg(2) in the code of Lcons checks if exactly two arguments are
supplied to cons.  That is, it checks whether the difference of vs_top and
vs_base is 2, and if not, it causes an error.  allocate_object(t_cons)
allocates a cons cell in the heap and returns the pointer to the cell.
After the car and the cdr fields of the cell are set, the cell pointer is
put onto the value stack.  The two stack pointers are used also on return
from a function call.  vs_base points to the first returned value and
vs_top points to the stack location next to the last returned value.
vs_pop in the code above decrements vs_top by one.

                  4---------6
                  |         |
                  -----------
         vs_top ->|         |
                  -----------
        vs_base ->| (1 . 2) |
                  -----------
                  |         |
                  :         :
                  |         |
          bottom  -----------
                  value stack

Because the same stack pointers are used both for argument passing and for
return value passing, the Common Lisp function values does almost nothing.

        On the call of (values 1 2)    On return from (values 1 2)

                  -----------                -----------
         vs_top ->|         |       vs_top ->|         |
                  -----------                -----------
                  |    2    |                |    2    |
                  -----------                -----------
        vs_base ->|    1    |      vs_base ->|    1    |
                  -----------                -----------
                  |         |                |         |
                  :         :                :         :
                  |         |                |         |
          bottom  -----------        bottom  -----------
                  value stack                 value stack

In most cases, the caller of a function uses only the first returned value
which is pointed to by vs_base.  This is not the case, however, when the
called function returns no value at all.  In order to avoid the check
whether this is the case, each KCL function, on return from its call, sets
nil to the stack entry which is pointed to by vs_base, whenever it returns
no value at all.  Thus, for instance, the actual code for the Common Lisp
function values is:

        Lvalues()
        {
                vs_top[0] = Cnil;
        }

where Cnil is a global variable that always contains the pointer to nil.
See why this works.



The interpreter uses A-lists.

The KCL interpreter uses three A-lists (Association lists) to represent
lexical environments.

        * One for variable bindings
        * One for local function/macro definitions
        * One for tag/block bindings

When a function closure is created, the current three A-lists are saved in
the closure along with the lambda expression.  Later, when the closure is
invoked, the saved A-lists are used to recover the lexical environment.



The invocation history stack is used for debugging.

The invocation history stack consists of two kinds of elements.  Each
element may be either a pair of a Lisp form and a pointer to lexical
environment:

        ---------------------------------------------
        |        form         | environment-pointer |
        ---------------------------------------------

or a pair of a function name and a pointer to the value stack:

        ---------------------------------------------
        |    function-name    | value-stack-pointer |
        ---------------------------------------------

The former is pushed on the invocation history stack when an interpreted
code is evaluated.  The form is the interpreted code itself and the
environment-pointer points to the three consecutive memory words each of
which holds the A-list that represents the lexical environment.  The latter
is pushed when a compiled function is invoked.  The function-name is the
name of the called function and the value-stack-pointer points to the value
stack location which is pointed to by vs_base when the function is called.
For both kinds, the element on the invocation history stack is poped at the
end of the evaluation.

Let us see how the invocation history stack is used for debugging.

        >(defun fact (x)                ;;; Wrong definition of the
           (if (= x 0)                  ;;; factorial function.
               one                      ;;; one should be 1.
               (* x (fact (1- x)))))
        fact
        
        >(fact 3)                       ;;; Tries 3!
        
        Error: The variable ONE is unbound.
        Error signalled by IF.
        
        Broken at IF.
        >>:b                            ;;; Backtrace.
        Backtrace: eval > fact > if > fact > if > fact > if > fact > IF
                                        ;;; Currently at the last if.
        >>:h                            ;;; Help.

        :c(urrent)      Show current function.
        :p(revious)     Move to previous function.
        :n(ext)         Move to next function.
        :b(acktrace)    Backtrace.
        :h(elp)         Help.
        :q(uit)         Return to top-level.
        :r(esume)       Return to the caller
        :l(ocal)        Show n-th local value.
        :v(ariables)    Show local variables.
        :functions      Show local functions.
        :blocks         Show block names.
        :tags           Show tags.
        :hide           Hide a function
        :hide-package   Hide a package.
        :unhide         Unhide a function
        :unhide-package Unhide a package.

        >>:p                            ;;; Move to the last call of fact.
        Broken at FACT.
        
        >>:b
        Backtrace: eval > fact > if > fact > if > fact > if > FACT > if
                                        ;;; Now at the last fact.
        >>:v                            ;;; The environment at the last call
        Local variables: x.             ;;; to fact is recovered.
                                        ;;; x is the only bound variable.
        >>x
        0                               ;;; The value of x is 0.
        
        >>:blocks
        Block names: fact.              ;;; The block fact is established.
        
        >>(return-from fact 1)          ;;; Return from the last call of
        6                               ;;; fact with value of 0.
                                        ;;; The execution is resumed and
        >                               ;;; the value 6 is returned.
                                        ;;; Again at the top-level loop.

The KCL compiler generates intermediate code in C.

The KCL compiler is essentially a translator from Common Lisp to C.  Given
a Lisp source file, the compiler first generates three intermediate files:

        * a C-file which consists of the C version of the Lisp program
        * an H-file which consists of declarations referenced in the C-file
        * a Data-file which consists of Lisp data to be used at load time

The KCL compiler then invokes the C compiler to compile the C-file into an
object file.  Finally, the contents of the Data-file is appended to the
object file to make a Fasl-file.  The generated Fasl-file can be loaded
into the KCL system by the Common Lisp function load.  By default, the
three intermediate files are deleted after the compilation, but, if asked,
the compiler leaves them.

The merits of the use of C as the intermediate language are:

        * The KCL compiler is highly portable.  Indeed the four versions of
KCL share the same compiler.  Only the calling sequence of the C compiler
and the handling of the intermediate files are different in these versions.

        * Cross compilation is possible, because the contents of the
intermediate files are common to all versions of KCL.  For example, one can
compile his or her Lisp program by the KCL compiler on Eclipse, bring the
intermediate files to SUN, compile the C-file with the C compiler on SUN,
and then append the Data-file to the object file.  This procedure generates
the Fasl-file for the KCL system on SUN.  This kind of cross compilation
makes it easier to port KCL.

        * Hardware-dependent optimizations such as register allocations are
done by the C compiler.

The demerits are:

        * At those sites where no C compiler is available, the users cannot
compile their Lisp programs.

        * The compilation time is long.  70% to 80% of the compilation time
is used by the C compiler.  The KCL compiler is perhaps the slowest
compiler in the Lisp world.

The compiler mimics human C programmer.

The format of the intermediate C code generated by the KCL compiler is the
same as the hand-coded C code of the KCL source programs.  For example,
supposing that the Lisp source file contains the following function
definition:

        (defun add1 (x) (1+ x))

The compiler generates the following intermediate C code.

        init_code(start,size,data)char *start;int size;object data;
        {       register object *base=vs_top;
                register object *sup=base+VM2;
                vs_check;
                Cstart=start;Csize=size;Cdata=data;
                set_VV(VV,VM1,data);
                MF(VV[0],L1,start,size,data);
                vs_top=vs_base=base;
        }
        /*      function definition for ADD1    */
        
        static L1()
        {       register object *base=vs_base;
                register object *sup=base+VM3;
                vs_reserve(VM3);
                check_arg(1);
                vs_top=sup;
                base[1]=one_plus(base[0]);
                vs_top=(vs_base=base+1)+1;
                return;
        }

The C function L1 implements the Lisp function add1.  This relation is
established by MF in the initialization function init_code, which is
invoked at load time.  There, the vector VV consists of Lisp objects; VV[0]
in this example holds the Lisp symbol add1.  VM3 in the definition of L1 is
a C macro declared in the corresponding H-file.  The actual value of VM3 is
the number of value stack locations used by L1, i.e., 2 in this example.
Thus the following macro definition is found in the H-file.

        #define VM3 2

When the compiled add1 is called, the value stack looks like:

        On the call of (add1 1)    On return from (add1 1)

                  -----------                -----------
                  |         |       vs_top ->|         |
                  -----------                -----------
         vs_top ->|         |      vs_base ->|    2    |
                  -----------                -----------
        vs_base ->|    1    |                |    1    |
                  -----------                -----------
                  |         |                |         |
                  :         :                :         :
                  |         |                |         |
          bottom  -----------        bottom  -----------
                  value stack                 value stack

Note that the two value stack pointers need not be moved
in this example.  This shows that the KCL compiler still has room
for improvement.

Lexical environment of compiled closures is represented by a list.

The KCL compiler takes two passes before it invokes the C compiler.  The
major role of the first pass is to detect function closures and to detect,
for each function closure, those lexical objects (i.e., lexical variable,
local function definitions, tas, and block-names) to be enclosed within the
closure.  This check must be done before the C code generation in the
second pass, because lexical objects to be enclosed in function closures
are treated in a different way from those not enclosed.

Ordinarily, lexical variables in a compiled function f are allocated on the
value stack.  However, if a lexical variable is to be enclosed in function
closures, it is allocated on a list, called the "environment list", which
is local to f.  In addition, one entity is reserved on the value stack, in
which the pointer to the variable's location (within the environment list)
is stored, so that the variable may be accessed by indexing rather than by
list traversal.  The environment list is a pushdown list:  It is empty when
f is called.  An element is pushed on the environment list when a variable
to be enclosed in closures is bound, and is popped when the binding is no
more in effect.  That is, at any moment during execution of f, the
environment list contains those lexical variables whose binding is still in
effect and which should be enclosed in closures.  When a compiled closure
is created during execution of f, the compiled code for the closure is
coupled with the environment list at that moment to form the compiled
closure.  Later, when the compiled closure is invoked, as many entities as
the elements in the environment list is reserved on the value stack, each
of which points to a lexical object in the environment list, so that,
again, each object may be referenced by indexing.

Let us see an example.  Suppose the following function has been compiled.

        (defun foo (x)
          (let ((a #'(lambda () (incf x)))
                (y x))
            (values a #'(lambda () (incf x y)))))

foo returns two compiled closures.  The first closure increments x by one,
whereas the second closure increments x by the initial value of x.  Both
closures return the incremented value of x.

        >(multiple-value-setq (f g) (foo 10))
        #<compiled-closure nil>

        >(funcall f)
        11

        >(funcall g)
        21

        >

After this, the two compiled closures look like:

        second closure        y:                    x:
        ----------------      ----------------      ---------------
        |  **   |    -------->|  10   |    -------->|  21  | nil  |
        ----------------      ----------------      ---------------
                                                        ^
                              first closure             |
                              ----------------          |
                              |   *   |    --------------
                              ----------------

   * : address of the compiled code for #'(lambda () (incf x))
  ** : address of the compiled code for #'(lambda () (incf x y))

Declarations increase code efficiency.

Declarations, especially type and function declarations, increase the
efficiency of the compiled code.  For example, for the following Lisp
source file, with two Common Lisp declarations added,

        (eval-when (compile)
          (proclaim '(function tak (fixnum fixnum fixnum) fixnum)))

        (defun tak (x y z)
          (declare (fixnum x y z))
          (if (not (< y x))
              z
              (tak (tak (1- x) y z)
                   (tak (1- y) z x)
                   (tak (1- z) x y))))

the compiler generates the following C code.

        /*  local entry for function TAK  */
        static int LI2(V4,V5,V6)
        int V4,V5,V6;
        {       VMB3 VMS3 VMV3
                if((V5)<(V4)){
                goto T4;}
                VMR3(V6)
        T4:;
                {int V7=LI2((V4)-1,V5,V6);
                {int V8=LI2((V5)-1,V6,V4);
                VMR3(LI2(V7,V8,LI2((V6)-1,V4,V5)))}}
        }
        /*  global entry for the function TAK  */
        static L2()
        {       register object *base=vs_base;
                base[0]=make_fixnum(LI2(fix(base[0]),
                                        fix(base[1]),
                                        fix(base[2])));
                vs_base=base; vs_top=base+1;
        }

The main part of the tak function is LI2.  If redundant parentheses are
removed, macros are expanded, and identifiers are renamed, we obtain the
following code equivalent to LI2.

        /*  local entry for function TAK  */
        static int tak(x,y,z)
        int x,y,z;
        {
                if(y<x) goto L;
                return(z);
        L:
                {       int t1=tak(x-1,y,z);
                        int t2=tak(y-1,z,x);
                        return(tak(t1,t2,tak(z-1,x,y)));
                }
        }

This is almost hand-written tak code in C.  The only overhead is the use of
the temporary variables t1 and t2.  This is necessary to make sure that the
arguments are evaluated in the correct order (i.e., from left to right),
since the C language does not specify the order of argument evaluation.  If
the compiler generated the following code,

        return(tak(tak(x-1,y,z),tak(y-1,z,x),tak(z-1,x,y)));

the C compiler of Eclipse AOS/VS evaluates the three inner calls to tak
from left to right (this is all right), whereas the C compiler of Unix
evaluates from right to left (this is bad).  In this example of tak, the
order of evaluation does not matter actually, because tak causes no side
effects.  But the KCL compiler does not know that.  The KCL compiler still
has room for improvements.

KCL does not have "disassembler".

Common Lisp defines a function disassemble, which is supposed to
disassemble a compiled function and to display the assembler code.
According to the Common Lisp Reference Manual,

        This is primary useful for debugging the compiler, ..

This is, however, useless in our case, because we are not concerned with
assembly language.  Rather, we are interested in the C code generated by
the KCL compiler.  Thus the disassemble function in KCL accepts
not-yet-compiled functions only and displays the translated C code.

        >(defun add1 (x) (1+ x))
        add1
        
        >(disassemble 'add1)
        init_code(start,size,data)char *start;int size;object data;
        {       register object *base=vs_top;
                register object *sup=base+VM2;
                vs_check;
                Cstart=start;Csize=size;Cdata=data;set_VV(VV,VM1,data);
                MF(VV[0],L1,start,size,data);
                vs_top=vs_base=base;
        }
        /*      function definition for ADD1    */
        
        static L1()
        {       register object *base=vs_base;
                register object *sup=base+VM3;
                vs_check;
                vs_top=sup;
                base[1]=one_plus(base[0]);
                vs_top=(vs_base=base+1)+1;
                return;
        }
        
        >

KCL/AOS has its own screen editor.

KCL/AOS has an embedded full-screen editor which resembles EMACS.  The
editor is called FeCl2 as the acronym of Full-screen Editor as a Common
Lisp TOOl.  It is invoked by the Common Lisp function ed.  Unfortunately,
FeCl2 is not supported by other versions of KCL, simply because we are too
lazy to port it (it is written in C).  For these versions, ed invokes the
vi editor of Unix.

KCL has C language interface.

The user can embed his or her own C code into Lisp source code.  The idea
is very simple:  The specified C code is inserted in the intermediate C
code that is generated by the KCL compiler.  In the following example,
Clines and defentry are top-level macros specific to KCL.  The Clines macro
form specifies the C code to be embedded, in terms of strings, and the
defentry form defines an entry of the specified C function from KCL.

        (Clines
        "   int tak(x, y, z)                       "
        "   int x, y, z;                           "
        "   {   if (y >= x) return(z);             "
        "       else return(tak(tak(x-1, y, z),    "
        "                       tak(y-1, z, x),    "
        "                       tak(z-1, x, y)));  "
        "   }                                      "
        )

        (defentry tak (int int int) (int "tak"))

Port to VAX took three days.

Although KCL is made to be highly portable, certain minor changes had to
be done, when it was ported to VAX Unix 4.2 bsd.  These changes include:

        1. The compiler top-level was slightly changed, because of
the differences of the calling sequence of the C compiler and of the handling
of object files.

        2. File system interface was changed to fit Unix 4.2 bsd.

        3. The following system parameters were redefined because
Vax's representation of floating point numbers differs from that of Eclipse.

                most-positive-short-float
                most-negative-short-float
                least-positive-short-float
                least-negative-short-float
                most-positive-long-float
                most-positive-double-float
                most-positive-single-float
                most-negative-long-float
                most-negative-double-float
                most-negative-single-float
                least-positive-long-float
                least-positive-double-float
                least-positive-single-float
                least-negative-long-float
                least-negative-double-float
                least-negative-single-float
                short-float-epsilon
                short-float-negative-epsilon
                long-float-epsilon
                double-float-epsilon
                single-float-epsilon
                long-float-negative-epsilon
                double-float-negative-epsilon
                single-float-negative-epsilon

        4. For the same reason as above, the following machine-dependent
Common Lisp functions were rewritten.

                decode-float
                scale-float
                float-radix
                float-digits
                float-precision
                integer-decode-float

        5. The three assembler routines were rewritten.

        6. The in-core loader that loads Fasl-files into the KCL memory was
changed.  This was a simple job because we used the standard linkage editor
ld of Unix.

        7. The memory dump routine was rewritten.

The whole job of poring KCL to VAX Unix 4.2 bsd took three days.  Later, we
spent some more days, to fix bugs in the ported version of KCL.

Port to SUN took three evenings.

The port to the SUN Workstation was much easier than the port to the VAX,
mainly because the operating system is the same for both VAX and SUN.

        1. The compiler top-level of KCL/VAX was used without changes.

        2. The file system of KCL/VAX was used without changes.

        3. The system parameters that depend on the representation of
floating point numbers were rewritten.

        4. The Common Lisp functions that depend on the representation of
floating point numbers were redefined.

        5. The three assembler routines were rewritten.

        6. The in-core loader of KCL/VAX was used without changes.

        7. The memory dump routines of KCL/VAX was used without changes.

The whole job of poring KCL to SUN took three evenings.  Most of
the time was spent for the three assembler routines, because we did not know
anything about the MC68000 assembler at first.



Port to Ustation took one week.

The port to the Ustation was relatively a hard job.  It took almost a week.
The major difficulity was that the C compiler of Unix V on the Ustation
recognized identifiers only by the first seven characters.  As already
mentioned, we used the convention that the C function that implements the
Common Lisp function function-name is given the name Lfunction-name.  Thus,
for example, the Common Lisp functions on packages such as

                package-name
                package-nickname
                package-shadowing-symbols
                package-use-list
                package-used-by-list
                packagep

are implemented by the C functions whose names all begin with Lpackage.
These C functions are regarded as having the same name by the C compiler.
This problem was solved by preparing a preprocessor program which maps long
identifiers into smaller ones.  This program is now used by the KCL
compiler on Ustation before the C compiler is called.

KCL is relatively compact.

The size of the object module of the whole KCL system (including the Compiler)
is:

                KCL/AOS         1.78 Mbytes
                KCL/VAX         1.45 Mbytes
                KCL/SUN         1.56 Mbytes
                KCL/UST         1.56 Mbytes

Since all system initialization (such as loading the database of the KCL
compiler) has been done when the object module is created, the object
module size roughly corresponds to the initial size of the KCL process when
a KCL session is started, minus the initial size of the hole in the heap
(about 200 Kbytes).

Gabriel's benchmark.

The following table shows the results of Richard Gabriel's Lisp benchmark
tests with the four versions of KCL.  The results with five other Common
Lisp systems are also listed for comparison.  Each number represents the
CPU time (in seconds) for the compiled program.  '*' indicates that the
time includes garbage-collection time.  The data of S-1 Lisp and Spice Lisp
are found in:


                  Performance and Evaluation of Lisp Systems
                                    by
                            Richard  P. Gabriel
                    Computer Systems Ser. Research Reports,
                             MIT Press, 1985

We received the data of Symbolics, DEC Common Lisp, and DG Common Lisp
directly from Dr. Richard Gabriel in April 1985.  We measured the
data for KCL in July 1985.  For the details of the benchmark
tests, refer to the book above.



 Benchmark |   Boyer  |  Browse  | Destruct | Traverse | Traverse |
   Test    |          |          |          |Initialize|    Run   |
 -------------------------------------------------------------------
           |          |          |          |          |          |
  Kyoto CL |   11.02  |   18.09  |    3.15  |    5.75  |   44.16  |
   MV10000 |          |          |          |          |          |
           |          |          |          |          |          |
  Kyoto CL |   43.73  |   68.15* |    8.00  |   14.42  |  151.20  |
   VAX 780 |          |          |          |          |          |
           |          |          |          |          |          |
  Kyoto CL |   43.60* |   73.08* |   10.23  |   20.38  |  118.60  |
    E15    |          |          |          |          |          |
           |          |          |          |          |          |
  Kyoto CL |   47.00  |   81.37  |   14.10  |   26.30  |  160.58  |
    SUN    |          |          |          |          |          |
           |          |          |          |          |          |
 Symbolics |   11.99  |   30.8   |    3.03  |    8.62  |   49.95  |
   3600    |          |          |          |          |          |
           |          |          |          |          |          |
  S-1 CL   |   10.03  |   10.2   |    0.91  |    1.93  |   30.1   |
  Mark IIA |          |          |          |          |          |
           |          |          |          |          |          |
   Spice   |  134.79  |  359.63  |   17.78  |   41.75  |  490.6   |
    Perq   |          |          |          |          |          |
           |          |          |          |          |          |
   DEC CL  |   46.79  |  118.51  |    6.38  |   20.76  |  161.68  |
  VAX 780  |          |          |          |          |          |
           |          |          |          |          |          |
    DG CL  |   29.3   |   59.91  |    6.95  |   27.77  |   45.86  |
   MV10000 |          |          |          |          |          |
 
 
 
 Benchmark |    Tak   |   Stak   |   Ctak   |   Takl   |   Takr   |
   Test    |          |          |          |          |          |
 -------------------------------------------------------------------
           |          |          |          |          |          |
  Kyoto CL |    0.42  |    1.90  |    4.35  |    5.13  |    0.54  |
   MV10000 |          |          |          |          |          |
           |          |          |          |          |          |
  Kyoto CL |    1.45  |    6.03  |   14.02  |   19.97  |    1.75  |
   VAX 780 |          |          |          |          |          |
           |          |          |          |          |          |
  Kyoto CL |    1.17  |    7.63  |    9.58  |   16.10  |    1.38  |
    E15    |          |          |          |          |          |
           |          |          |          |          |          |
  Kyoto CL |    1.48  |   11.02  |   16.88  |   23.35  |    1.67  |
   SUN     |          |          |          |          |          |
           |          |          |          |          |          |
 Symbolics |    0.6   |    2.58  |    7.65  |    6.44  |    0.6   |
    3600   |          |          |          |          |          |
           |          |          |          |          |          |
   S-1 CL  |    0.29  |    4.31  |    0.82  |    2.92  |    0.58  |
  Mark IIA |          |          |          |          |          |
           |          |          |          |          |          |
   Spice   |    4.7   |   13.5   |    8.4   |   24.0   |    7.7   |
    Perq   |          |          |          |          |          |
           |          |          |          |          |          |
   DEC CL  |    1.83  |    4.11  |    8.09  |    7.34  |    3.42  |
   VAX 780 |          |          |          |          |          |
           |          |          |          |          |          |
    DG CL  |    0.89  |    3.09  |    1.79  |    5.52  |    1.21  |
   MV10000 |          |          |          |          |          |
 

 
 Benchmark |   Deriv  |  DDeriv  |   Div2   |   Div2   |    FFT   |
   Test    |          |          | Iterative| Recursive|          |
 -------------------------------------------------------------------
           |          |          |          |          |          |
  Kyoto CL |    4.85  |    5.93  |    1.99  |    2.73  |    1.55  |
   MV10000 |          |          |          |          |          |
           |          |          |          |          |          |
  Kyoto CL |   18.98  |   23.07  |    7.48  |   11.25  |    9.07  |
   VAX 780 |          |          |          |          |          |
           |          |          |          |          |          |
  Kyoto CL |   22.07* |   25.38* |    9.95* |   12.60* |   74.62  |
    E15    |          |          |          |          |          |
           |          |          |          |          |          |
  Kyoto CL |   20.72  |   24.77  |    9.32  |   12.30  |   94.07  |
    SUN    |          |          |          |          |          |
           |          |          |          |          |          |
 Symbolics |    5.12  |    5.24  |    1.85  |    2.89  |    4.75  |
    3600   |          |          |          |          |          |
           |          |          |          |          |          |
   S-1 CL  |    4.99  |    3.27  |    0.82  |    1.49  |    1.44  |
  Mark IIA |          |          |          |          |          |
           |          |          |          |          |          |
   Spice   |   71.8   |   77.7   |   28.15  |   40.69  |   59.0   |
    Perq   |          |          |          |          |          |
           |          |          |          |          |          |
   DEC CL  |   13.76  |   ---    |    5.0   |    9.84  |   32.69  |
   VAX 780 |          |          |          |          |          |
           |          |          |          |          |          |
    DG CL  |    5.6   |    8.11  |    2.86  |    4.48  |   62.78  |
   MV10000 |          |          |          |          |          |
 
 
 
 Benchmark |   Puzzle |  Triang  |  Fprint  |   Fread  |  Tprint  |
   Test    |          |          |          |          |          |
 -------------------------------------------------------------------
           |          |          |          |          |          |
  Kyoto CL |    6.76  |  104.85  |    1.98  |    2.45  |    1.74  |
   MV10000 |          |          |          |          |          |
           |          |          |          |          |          |
  Kyoto CL |   20.57  |  366.12  |    5.73  |    5.77  |    6.55  |
   VAX 780 |          |          |          |          |          |
           |          |          |          |          |          |
  Kyoto CL |   41.30  |  341.23* |    9.83  |    6.07  |   11.58  |
    E15    |          |          |          |          |          |
           |          |          |          |          |          |
  Kyoto CL |   49.13  |  499.68  |   10.05  |    7.62  |    8.50  |
    SUN    |          |          |          |          |          |
           |          |          |          |          |          |
 Symbolics |   13.89  |  151.7   |    2.6   |    4.6   |    4.9   |
    3600   |          |          |          |          |          |
           |          |          |          |          |          |
   S-1 CL  |    1.82  |   62.06  |   ---    |   ---    |   ---    |
  Mark IIA |          |          |          |          |          |
           |          |          |          |          |          |
   Spice   |   75.14  | 1488.85  |   20.0   |   26.0   |   22.6   |
    Perq   |          |          |          |          |          |
           |          |          |          |          |          |
   DEC CL  |   47.48  |  360.85  |    3.94  |    7.24  |    2.85  |
   VAX 780 |          |          |          |          |          |
           |          |          |          |          |          |
    DG CL  |  138.2   |  151.2   |    2.35  |    4.65  |    2.83  |
   MV10000 |          |          |          |          |          |



            Appendix C. Kyoto Common Lisp Installation Guide

This appendix explains how to install the KCL system, separately for each
version of KCL.

C.1. Installation of KCL/AOS

1. Prepare a directory (hereafter called KCL directory) for Kyoto Common
Lisp.  In the following examples, we suppose that the KCL directory is
:UDD:KCL.


2. Load the distribution tape to the KCL directory.

        ) DIR
        :UDD:KCL
        ) LOAD

You will find that the subdirectory PORT has been created.  The PORT
subdirectory contains everything that is needed to run KCL.  Files in this
directory are:

    Documents:
        README                  this file

    Executable files:
        KCL.PR                  the KCL interpreter and compiler
        KCL.ST
        BUILD_FASL.PR           the fasl-file builder
        FECL2.PR                the FeCl2 editor

    Command files:
        KCL.CLI                 to invoke KCL
        LC.CLI                  to invoke the KCL compiler
        LC1.CLI                 to invoke the KCL compiler
        FECL2.CLI               to invoke the FeCl2 editor

     Header file:
        CMPINCLUDE.H            the header file for the KCL compiler

     Miscellaneous:
        FECL2.CMD               FeCl2 editor command table

3. Customize the command files.

The command file KCL.CLI consists of the following command lines to invoke
the KCL interpreter.

        push;prom pop
        sea :usr:dgc [!sea]
        x :udd:[!user]:port:%0-% :udd:[!user]:port:
        pop

Replace the two occurrences of "[!user]" with the name of the KCL directory
(i.e., KCL in our example).

        push;prom pop
        sea :usr:dgc [!sea]
        x :udd:KCL:port:%0-% :udd:KCL:port:
        pop

And move this file to an appropriate command directory, say :UTIL, so that
all KCL users can access it.

If the name of the directory that includes DG's C compiler is not :USR:DGC,
you should replace it with the appropriate directory name, so that the KCL
compiler can access the C compiler by CC.PR.

You can use the commands LC.CLI and LC1.CLI to invoke the compiler directly
from the CLI.  The content of LC.CLI is:

        push
         prompt pop level
         sea :usr:dgc [!sea]
         WRITE Compiling %1%.LSP.
          proc/def/ioc/block/pri=3 &
          :udd:[!user]:port:kcl :udd:[!user]:port: %1% %1% U10000
        pop

Customize these command files in the same way as for the KCL.CLI command
file above.

4. Install the header file

Copy the header file CMPINCLUDE.H to the standard directory for C include
files, say :USR:DGC.

C.2. Installation of KCL/VAX

1. Prepare a directory (hereafter called KCL directory) for Kyoto Common
Lisp.  In the following examples, we suppose that the KCL directory is
/usr/kcl.

2. Load the distribution tape to the KCL directory.

        % pwd
        /usr/kcl
        % tar x

You will find that the subdirectory unixport has been created.  The
unixport subdirectory contains everything that is needed to run KCL and the
KCL compiler.  Files in this directory are:

    Documents:
        readme                  this file

    Executable files:
        saved_kcl               the KCL interpreter and compiler

    Command files:
        kcl                     to invoke KCL
        lc                      to invoke the KCL compiler
        lc1                     to invoke the KCL compiler

     Header file:
        cmpinclude.h            the header file for the KCL compiler

3. Customize the command files.

The command file kcl consists of a single line command to invoke the KCL
interpreter.

        #
        ~/unixport/saved_kcl ~/unixport/

Replace two '~'s with the pathname of the KCL directory (i.e., 
/usr/kcl in our example).

        #
        /usr/kcl/unixport/saved_kcl /usr/kcl/unixport/

And move this file to an appropriate command directory, say /usr/bin, so
that all KCL users can access it.

You can use the commands lc and lc1 to invoke the compiler directly from
the shell.  The content of lc is:

        #
        echo Compiling $1.lsp
        ~/unixport/saved_kcl ~/unixport/ $1 $1 U1000

Customize these command files in the same way as for the kcl command file
above.

4. Install the header file

Copy the header file cmpinclude.h to the standard directory for C include
files, say /usr/include.

C.3. Installation of KCL/SUN

1. Prepare a directory (hereafter called KCL directory) for Kyoto Common
Lisp.  In the following examples, we suppose that the KCL directory is
/usr/kcl.

2. Load the distribution tape to the KCL directory.

        % pwd
        /usr/kcl
        % tar x

You will find that the subdirectory unixport has been created.  The
unixport subdirectory contains everything that is needed to run KCL and the
KCL compiler.  Files in this directory are:

    Documents:
        readme                  this file

    Executable files:
        saved_kcl               the KCL interpreter and compiler

    Command files:
        kcl                     to invoke KCL
        lc                      to invoke the KCL compiler
        lc1                     to invoke the KCL compiler

     Header file:
        cmpinclude.h            the header file for the KCL compiler


3. Customize the command files.

The command file kcl consists of a single line command to invoke the KCL
interpreter.

        #
        ~/unixport/saved_kcl ~/unixport/

Replace two '~'s with the pathname of the KCL directory (i.e., /usr/kcl in
our example).

        #
        /usr/kcl/unixport/saved_kcl /usr/kcl/unixport/

And move this file to an appropriate command directory, say /usr/bin, so
that all KCL users can access it.

You can use the commands lc and lc1 to invoke the compiler directly from the
shell.  The content of lc is:

        #
        echo Compiling $1.lsp
        ~/unixport/saved_kcl ~/unixport/ $1 $1 U1000

Customize these command files in the same way as for the kcl command file
above.


4. Install the header file

Copy the header file cmpinclude.h to the standard directory for C include
files, say /usr/include.



C.4. Installation of KCL/UST


1. Prepare a directory (hereafter called KCL directory) for Kyoto Common
Lisp.  In the following examples, we suppose that the KCL directory is
/usr/kcl.

2. Three floppy disks are used for the distribution.  Load the floppy disks
to the KCL directory by the multi-volume option of the tar command.  (Insert
the first disk to the drive and issue the tar command.  Then, you will be
prompted to change the disks.)

        % pwd
        /usr/kcl
        % tar xvfBM /dev/rdy0g 1976

You will find that the subdirectory unixport has been created.  The unixport
subdirectory contains everything that is needed to run KCL and
the KCL compiler.  Files in this directory are:

    Documents:
        readme                  this file

    Executable files:
        saved_kcl               the KCL interpreter and compiler
        ild                     incremental loader
        trans                   translator from Unix 4.2 to Unix V

    Command Source files:
        kcl.c                   to invoke KCL
        lc.c                    to invoke the KCL compiler
        lc1.c                   to invoke the KCL compiler

     Header file:
        cmpinclude.h            the header file for the KCL compiler


3. Customize the command files.

The source file kcl.c consists of a C-language program to invoke the KCL
interpreter.  Replace all /usr/ukcl in this file with the pathname of the
KCL directory (i.e., /usr/kcl in our example), and compile this file.

        % cc -o kcl kcl.c

And move the object file to an appropriate command directory, say /usr/bin,
so that all KCL users can access it.

You can use the source files lc.c and lc1.c to invoke the compiler directly
from the shell.  Customize these source files in the same way as for the
kcl command file above.


4. Install the header file

Copy the header file cmpinclude.h to the standard directory for C include
files, say /usr/include.





                         Addendum, 1986


        KCL on UNIX: Problems and Future Improvement


* Core Dump

We can consider several situations in which KCL dumps core.

1. The KCL compiler, by default, produces efficient but very dangerous
code.  The code seldom detects erraneous situations such as extracting the
car of a fixnum, which, in bad cases, cause "Segmentation violation" or
"Bus error" on UNIX.  I think this is the reason for most of the complaints
you have been reported so far.  To avoid this, one should tell the compiler
to produce rather inefficient but safe code using the appropriate
proclamation such as

        (proclaim '(optimize (safety 2))).

The safety level greater than or equal to 2 guarantees that the
code detects every runtime error.

2. KCL keeps several stacks.  Whenever an item is pushed on a stack, KCL
checks whether the stack limit is violated or not, except for the value
stack and the C stack.  The limit for the value stack is not checked if the
code was compiled with the safety level 0; i.e., the limit is always
checked in the code compiled with the safety level greater than 0, and in
the interpreted code.

3. The limit for the C stack is not checked in the compiled code.  We can
insert the code to check the C stack limit at the beginning of each
compiled function.  However, we don't think it is feasible.

4. GC of KCL uses the C stack in the marking phase.  Currently, the C stack
overflow in the marking phase is not detected.  We will insert the code to
check the stack limit in the next revision.  However, we can't signal a
Lisp error in GC.  The C stack overflow in GC will result in a fatal error.

Note: Big lists extending to the direction of car consume more stack
area than those extending to cdr. 


* C Stack Limit

The C stack limit used by KCL is smaller than the actual limit.  Currently,
its value is fixed and independent of the actual limit.  On BSD, as you may
know, the actual limit for the C stack can be changed by the limit command
of csh.  In the next revision, we will set the C stack limit of KCL from
the value obtained by the getrlimit system call.  Therefore, for those
applications that use much stack area, one can invoke KCL in the following
way:

        % limit stacksize 1024          # 1024K bytes = 1M bytes
        % kcl

We can even change KCL so that it dynamically increments its C stack limit
by the setrlimit system call.  But we don't think it's feasible, either.

Note: Currently, the C stack limit of KCL is set 15000 words = 60K bytes
for all the versions of KCL.  Its value is defined as the C macro CSSIZE in
"h/eval.h".

Note: The actual stack limit is 512K by default on SUN-III.

Note: In the revision of KCL you have, the C stack overflow will never
signal a Lisp error; it always results in a fatal error and KCL terminates
immediately.  This is a BUG.  I found it while I was checking the behavior
of KCL for the C stack overflow.  I've already fixed it, so in the next
revision, the C stack overflow will signal a Lisp error except in GC.


* Process Size

Since KCL keeps a table which records the type of each page in the process
space, the process size of KCL is limited by the size of the table.  Its
size is determined by the MAXPAGE macro defined on the cc command line used
for compiling each C source file of KCL.  Currently, MAXPAGE = 16384 = 32M
bytes.  I think the size is reasonable now.

On BSD, the size of the KCL process is also limited by the resource limit
set by the limit command.  KCL doesn't change the limit by the setrlimit
system call.

Note: Even if the resource limit is 1G, you can't use that much unless
MAXPAGE is large enough.

Note: For SUN-III, the limit is nearly 256M bytes by default.

Note: Even if the resource limit is bigger than MAXPAGE, you can't use
MAXPAGE pages because of the limitation of the swap space of the operating
system.  In SUN3/75M, which I am using now, I can't allocate more than 16M.
If there are many other processes running, I can only allocate far less
than 16M.

* Explicit Expansion of Process Space

Usually, KCL expands its process space incrementally, i.e., it only
allocates memory after it has failed in collecting enough space by GC.  In
order to expands the process space of KCL explicitly, we changed the
function ALLOCATE and ALLOCATE-CONTIGUOUS-PAGES so that they take one
optional argument.  When a non-NIL value is supplied for the optional
argument, these functions acutally allocate the maximum number of pages for
the specified type or for the contiguous blocks.  Therefore, one can begin
with 1M bytes for conses (500 pages = 1M bytes) as follows:

        % kcl
        KCL (Kyoto Common Lisp) ...

        >(allocate 'cons 500 t)
        t

        >

If one extends the hole size by SI:SET-HOLE-SIZE and allocates memory as
above, while consuming the current hole, KCL will surely make the hole of
the specified size.  Therefore, if one begins KCL in the following way, one
will never invoke GC.

        % kcl
        KCL (Kyoto Common Lisp) ...

        >(si:set-hole-size 8000)        ; 16M
        8000

        >(allocate 'cons 500 t)         ; Actually allocates 1M.
                                        ; The hole will be 16M.
        t

        >(allocate 'cons 8000)          ; Set the maximum.
        t

        ...
        ...

        >(allocate 'fixnum 8000)
        t

        >(allocate-contiguous-pages 8000)
        t

        >(allocate-relocatable-pages 3000)      ; 6M
        t

Note: In the above example, KCL allocates 16M for cells and 6M for
relocatable blocks.  Since KCL uses two spaces for the relocatable area,
16M + 2*6M < 32M.  We are not prepared for the critical case, say 16M+2*8M
= 32M.

Note: The above example will not work on SUN-III in general, unless you
reinstall the operating system so that it has MUCH swap space.  Please make
a test with smaller parameters than above, after you have recieved the next
revision of KCL.

Note: One should first check the size of the swap space before
complaining about KCL.

* Notification of GC

We defined a new system-internal variable SI:*NOTIFY-GBC*.  When
its value is non-NIL, GC will print

        GBC invoked

when it is invoked, and will print

        GBC finished

when it returns.  It's much neater than SI:*GBC-MESSAGE*.

Note: The message is directly written on the standard output of the C
library and is not written on a Lisp stream.  Therefore, when one DRIBBLEs
the KCL session, the message from GC won't be written out on the specified
file.  This is because writing on a stream has the danger of consuming
memory.


* Faslink

We made the loader which can load the object file while linking
other object files and/or libraries.  It is defined as a function
SI:FASLINK and used as follows:

        (si:faslink "foo.o" "bar.o boo.o -lpixrect")

"foo.o" should be an object file produced by compiling a Lisp source file.
The Lisp file, in general, consists of DEFENTRY definitions that call
functions in the object files and/or the libraries specified in the second
argument.  The first argument should be a pathname, a string or a symbol,
and the second argument should be a string that can be accpted by the UNIX
linkage editor.  If there are more than one arguments, they should be
separated by a space as above.

Note: The second argument is passed to "ld" as it is.

Note: SI:FASLINK is only defined in the BSD versions of KCL.


* valloc

The SunView library uses the "valloc" function of C.  To use the SunView
library with KCL, one should redefine "valloc" as follows:

        #define PAGSIZ  ...

        char *
        valloc(size)
        {
                int p;

                p = (int)malloc(size+PAGSIZ);
                return((p+PAGSIZ-1)&(~PAGSIZ));
                return((char *)p);
        }

Note: In my SunView interface, all the libraries are linked with KCL from
the beginning.  I haven't checked that SI:FASLINK will work for SunView.
But, it is necessary (perhaps, not sufficient) to redefine "valloc" as
above.


* init.lsp

If there exists a file with the name "init.lsp" in the current directory,
KCL loads the file before entering into the top-level loop.  The user of
KCL is expected to make his own environment using this facility.  It is
similar to ".chsrc" for csh, ".profile" for sh, ".newsrc" for readnews,
although the name doesn't begin with ".".

If you want to invoke your favorate editor from KCL, please define the
interface in "init.lsp".


* Big C Code

The C compiler sometimes complains that the code produced by KCL is too big
and cannot compute jump addresses.  I bet this is a bug of the UNIX
assembler.  To avoid this, one should supply the assembler with the -J
option.  I'm not sure that the cc command will pass the -J option to the
assembler, since it passes those arguments it can't interpret to the
linkage editor in general.

To avoid the problem, you should compile the Lisp file by

        >(compile-file "foo.lsp" :c-file t :h-file t :data-file t
                       :o-file nil)

and compile the C file with the -S option

        % cc -S foo.c

and then assemble it with the -J option.

        % as -J foo.s -o foo.o

Finally, on BSD, concatenate the data file at the end.

        % cat foo.data >> foo.o

Note: The above recipe is totally dependent on the version of UNIX.  I hope
you will report what C compilers (and assemblers) have failed in compiling
the C code produced by the KCL compiler.