Copyright (c) 1990, PC RESOURCES, Hudson, Mass: All Rights Reserved



                                ACKNOWLEDGMENTS

      We would like to thank the following vendors, whose data is used in
      this database with their permission:

                            Fair Rite Products Corp.
                             Ferrite International
                                   Ferronics
                                 Magnetics Inc
                                  MicroMetals
                      Phillips Discrete Products Division
                                    Siemens







                             HARDWARE REQUIREMENTS

      CoreDBMS will run on PC, XT, and AT class machines and close-
      compatibles running DOS 2.0 or above, with at least 320k of free
      memory, and one disk drive.

                    A hard-disc drive is highly recommended.

      A CGA or EGA monitor is required to view or print graphics.  Print-
      ing graphics requires an Epson or Pro-Printer compatible printer.
      But without graphic-capable devices, the database and all of its'
      searching tools are still available.


                                   LEGALEASE

      Purchase of this program allows installation on one system OR for
      use by one person on any number of systems.  For multiple-copies at
      a single site, contact us for prices.

      The data used by this program is subject to change without notice.

      This program and database does not warrant or guarantee the suit-
      ability of any given core, material, or vendor for any given
      application.  In all cases, the user is responsible for verifying
      the suitability of a core in his application.

      The information in this database is believed to be correct and the
      program is believed to display this information properly. PC
      Resources will correct errors in material or core specifications
      when found; but will not be liable for consequential damages from
      use of this database or data within.

      We offer a money-back guarantee to all users of our software.  If
      you are not completely satisfied, write us and your purchase price
      will be refunded.





                                  INTRODUCTION

      CoreDBMS is a program for the IBM-PC which simplifies working with
      ferrite cores by replacing stacks of vendors' databooks with one
      simple-to-use tool.

      CoreDBMS can be used as a computerized databook, with smart sort
      and selection routines allowing you to organize and view data in
      ways never before possible.

      But, CoreDBMS is designed as a searching tool to cross-reference
      cores from different vendors as an aid in finding second-sources.

      CoreDBMS allows you to:
           Search for cores by part number, vendor, material, size, form-
           factor, magnetic path-length, area, volume, inductance factor,
           or dimension.

           Sort cores by any of the above fields for easy comparisons.

           Display data in summary form - BROWSE - for quick viewing, in
           DETAIL mode with outline drawings and full dimensions, or in
           COMPARE mode for easy comparisons between cores.

           Print or file data in a number of formats, including comma-
           delimited format for use in other programs.

           View material specifications including graphs of; loss factor
           vs frequency and temperature, permeability vs frequency and
           temperature, permeability vs ac flux, dc bias, and temperature,
           loss vs frequency and temperature, and static magetization
           curves.

      CoreDBMS is menu-driven, allowing a novice user to start using the
      program immediately.  Help screens are available in most menus.


                                    The Data

      CoreDBMS provides data on both cores and materials.

      One advantages of CoreDBMS is that data from all vendors is given
      in a common format.  You, the user, need not translate cgs, mks,
      and english units while searching.

      Information in the database is as complete as we can make it, with-
      in the limitation of disk size and searching speed; we don't want
      to fill your hard disk with the database, and we don't want to take
      too long to find information.

      Vendors - especially in the materials section - differ in what in-
      formation they provide.  Where a vendor does not provide data it is
      left blank.




                                  The Cores

      CoreDBMS lists standard cores which are in each vendor's databook.
      Special order cores and any non-standard cores are not listed.  For
      each core the following data is available:

      part number                       effective magnetic volume 
      vendor                            weight  
      form factor                       inductance factor and tolerance 
      material type                     8 dimensions with tolerances 
      material code, or name            a reference to a figure 
      effective magnetic path length    a reference to available bobbins 
      effective magnetic area           a notes field 

      Fields may blank or zero if the vendor does not give the inform-
      ation, or if for dimensional tolerances the value is 'nominal'.

      The above data is sufficient for most design with magnetic cores,
      BUT, the vendor's databook is a valuable source of information
      which should be consulted.  Vendors often include design nomo-
      graphs, Q-factor curves, and other information which will not fit
      in this program.


                                  The Figures

      Figures are outline drawings or sketches which are intended to
      clearly indicate the core shape and mounting features.

      Eight dimensions are available - assigned letters A through H in
      the core data fields.  If more than eight features are present on a
      core, the eight most important are given.

      If the vendor does not dimension a feature, the feature is usually
      not drawn.  For this reason, few wiring channels are shown in pot
      figures.  Similarly, wire break-outs in pots are usually drawn as
      rectangles, although a variety of - un-dimensioned - shapes are
      shown in vendor databooks.

      Channels for mounting hardware - where the user may wish to use his
      own hardware - are generally shown: slots for specialty hardware
      such as for RM core clips are generally not shown.  A core avail-
      able both with and without a center-hole usually has figures drawn
      both with and without the center hole(In some figures a center-
      hole-dimension of zero implies that there is no center-hole.)

      As with dimensions and other data, this program provides sufficient
      information to make a valid comparison between cores - but the
      vendor's databook should be consulted for exact dimensions where
      dimensions may be critical, including dimensions which we cannot
      fit within the database.





                                 The Materials

      The materials section provides quick access to information on
      vendors' materials, such as:

      initial permeability                 specific gravity, or density 
      maximum permeability                 Curie temperature 
      saturation flux density              volume resistivity 
      residual flux density                loss factor 
      coercivity or coercive force 
      recommended min and max frequencies of operation 

      plus, up to 10 graphs of functions versus frequency and temperature:

      1-loss factor vs frequency           6-permeability vs frequency 
      2-loss factor vs temperature         7-static magetization curves 
      3-permeability vs temperature        8-core loss vs flux density 
      4-permeability vs ac flux            9-core loss vs temperature 
      5-permeability vs dc bias           10-Flux Density vs temperature

      Vendors vary widely in the amount of information provided on their
      materials, and blank fields are quite common.


                                  The Bobbins

      One field of the core database is a bobbin cross-reference.  At
      present this indicates that the vendor does or does not have a
      bobbin available.

      In the future, we hope to also catalog bobbins and allow selection
      and viewing bobbins as in the cores and materials sections.



      To get started, we suggest you read the sections, 'Installing the
      program' and 'Running the program'.  After that a brief reading of
      the 'Using CoreDBMS' and the 'Examples' section might be helpful.

      CoreDBMS is designed to be a 'bullet-proof' program - experiment!

      The program is menu driven with most of the options always listed
      on the screen, and help is available by using the F1 key.




                      Chapter 1  - Installing the Program

      If you have a floppy-based system, copy the distribution disk(s),
      place the original in a safe place, and use the copy for all work.

                     DO NOT USE THE DISTRIBUTION DISKETTE!

      With a two-disk copy of CoreDBMS: Insert the PROGRAM floppy in one
      drive, make that drive the active drive with the DOS command 'A:'
      (or 'B:') and type the command line as given in Chapter 2.

      Then; remove the program floppy, insert the DATA floppy, and hit
      ENTER.

      The speed of the floppy drive limits the speed of searching and
      displaying data.  With a 5-1/4 inch drive and a large database the
      speed is about acceptable for occasional use.

      If you have sufficient memory, a RAM-disk is faster.  Move all
      files ending in .db1, .db2, .db3, and .hlp to the RAM-disk and make
      the RAM-disk your active disk before running the program.  The
      program itself need not be on the RAM-disk.


      If you have a hard disk drive create a directory and load all of
      the files from the distribution disks to that directory.   For
      example, to place the files in a new directory, c:\cores, a set of
      commands to do this would be:

                               C:
                               mkdir \CORES
                               A:
                               copy *.* C:\cores


      Before running the program, add the following line to your
      config.sys file :
                                    files=10

      and re-boot your system.

      If files is already greater than 10, you may skip this step.  Coredbms
      keeps a number of files open simultaneously - files=10 (or more)
      notifies DOS to make provision for these files.



                        Chapter 2  - Running the Program

      To execute CoreDBMS make its' directory the default with the DOS
      cd command, and type:

                               COREDBMS {options}


      Options configure the program for your monitor, printer, and
      personal preferences; they may be in any order, and need not be
      separated by spaces.

      Options are usually not required.  HOWEVER, you should read the
      following section to insure this is true for your system.


      MONITOR OPTIONS 
      CoreDBMS can recognize most EGA adapters, CGA adapters, and mono-
      chrome monitors and configure the program properly.  CoreDBMS can-
      not recognize MDA and HGA (Hercules) monitors, and may not success-
      fully configure for VGA adapters.

      Options over-ride the recognition functions of the program, so that
      if you are using an EGA monitor and specify the /CGA option, graph-
      ics will in CGA mode.  This may be required to use image capture
      programs or the DOS graphics.com program.

      You can control the monitor settings using the following switches:

      /EGA  specifies your monitor is an Enhanced-Graphics-Adapter type.
            Use this switch if you have a VGA monitor or if CoreDBMS does
            not properly configure to your system. 

      /CGA  specifies your monitor has CGA-graphics capabilities. 

      /NGT  tells the program that the monitor cannot display graphics.
            This will disable all attempts to write graphics to the
            screen - attempting to draw graphics to a non-graphics
            terminal will usually cause a run-time error and halt the
            program.

      /BW   specifies that the monitor is monochrome - black and white.
            This will cause the program to output white text or graphics
            on a black back-ground.  High-lighted text will be in bright-
            white.  If you have a mono-chrome monitor you should use this
            option.


      COLOR OPTIONS
      /FG=n, /BG=n, and /HL=n  sets the colors used for text screens. The
              default - FG=3/BG=7/HL=4 - is a good selection for most
              monitors in most lighting conditions.  For use in brightly
              lit areas, try /FG=1/BG=7/HL=5.

      Not all monitors follow the standard color definitions. If your
      monitor appears to be missing data or the colors appear to be a bad
      choice, adjust the above values.

      In graphics mode the background color defaults to zero, or black
      and the line-drawing color to white.  The fore-ground and high-
      light color options affect text drawn on the graphics screen.
      Specifying a fore-ground or high-light color of zero will render
      text invisible in graphics mode.

      A utility program - colors.exe - is included on the distribution
      diskette to show the color options on your monitor.


      PRINTER OPTIONS 
      /LPT1, /LPT2, /LPT3 tell Coredbms where your printer is attached.
              If you have a printer connected to a serial port, you will
              have to either use re-direction - see your DOS manual - or
              FILE the output and use COM1 or COM2 as the file name.

      /IBMPRO  tells CoreDBMS that your printer is a ProPrinter or
              compatible.  The graphics format of IBM ProPrinters and
              Epson-compatible printers is slightly different.  Most
              printers will accept graphics in one of these two formats.

      /NGP   (No-Graphics-Printer) disables all attempts to print graphics.
              Attempting to print graphics to a printer without graphics
              capability will result in a confused jumble as output,
              usually taking up many pages.


      If you require any of the above options to run CoreDBMS, you might
      consider creating a batch file to simplify running the program.

      A batch file is identified by a file name ending in .BAT .  When
      the name of the batch file is typed the contents of the batch file
      is executed as DOS commands.  Batch files can be useful to estab-
      lish initial conditions for a program and save typing.

      For example, if CoreDBMS is placed in a directory named CORES, a
      batch file with the following lines could be used to move to the
      proper directory, set the colors, set the monitor for CGA-mode, and
      the line printer for port 2:

                        cd c:\CORES
                        Coredbms /hl=3/fg=1/bg=7/lpt2/cga



                  Chapter 3  - Using  CoreDBMS - The Main-Menu

      When CoreDBMS is run, the main menu is displayed.  From the main
      menu a function-key-stroke will take you to any program option.

      The function keys F1 through F10 perform the following actions:

               F1 - shows a general help screen 
               F2 - displays material characteristics 
               F3 - enter the core-selection and viewing routine 
               F4 - find alternate sources
               F5 - displays core outline drawings 
               F6 - displays vendor information 
               F9 - shows statistics 
               F10- Quits the program.


      The Materials Menu - F2 - is described in detail in Chapter 4.

      The Core Selection and Viewing Menu - F3 - is described in detail
      in Chapter 5.

      The "Find alternate sources" selection - F4 - opens a help window
      with basic information on using CoreDBMS to find an alternate
      source for a known core.

      The "Display Core Outline Drawings" selection opens a graphics
      window to display the core figures.  At the start, a help screen
      with a listing of figures is given, then figure 1 is shown.  Page-
      Down, Page-up, Up-Arrow, Down-Arrow, and ENTER move forward and back
      through the cores, and 'R' will prompt you for a figure number and
      then jump to that figure.

      Typing P will print the displayed figure.  F1 re-displays the help
      screen, and F10 exits the routine.


      The Display Vendor Information Option - F6 - will show several
      screens of information, giving the address and phone number for the
      vendors in the database and of some major distributors.


      The Statistics option - F9 - provides two pages of statistics on
      the cores.  The first page is a breakdown of cores by vendor, form-
      factor, and material type.  The second page is a breakdown of cores
      by figure.



               Chapter 4  - F2 - Selecting and Viewing Materials

      The Materials and Cores menus are similar with keys performing
      roughly the same functions; as there are far fewer materials than
      cores, the materials section is slightly simpler.

      When you enter the materials selection menu the screen shows two
      boxes: on the right a Status box shows total number of materials
      and the number presently selected for viewing.  On the left a box
      presents the selection options with one option highlighted.

      At the bottom of the screen, a help line displays additional
      options.

      You may view the selected materials using the F3 or F4 keys, or you
      may reduce the number of materials through selections.

      The selection routine is similar to that used in library services.
      You start with ALL records 'selected' or available.  You then set
      selection guidelines to reduce the number of records to a usable
      number.

      The selection process is a 'forward-only' one; you can not reverse
      a selection once made.  If the result of a search matches no mat-
      erials, you must reset to all materials via the F9 key - RESET.

      Unlike the selection process with many databases, selections may be
      made in steps.  To find all nickel-zinc ferrites torroids made by
      vendor 'A' you can first request all cores made by vendor 'A' then
      all torroids then all nickel-zinc cores - the order of searching is
      not important.

      To start the selection process, move the high-lighted bar in the
      selection options box using the cursor keys, then hit the ENTER key
      to choose a selection option.  Or type the number of the selection
      option.


                             0 - Selection by Name

      Selection by Name is the fastest way to view a material when you
      know a name or part of a name.

      This selection pops up a small box, prompting for a search-string.
      Enter a string, ending with the ENTER key.  The backspace key
      allows limited editing.  If you decide not to perform a search,
      strike the ENTER key on a blank search-string.

      The program then checks all records in the database for materials
      with names containing the search-string.


                            1 - Selection by Vendor

      This selection pops up a list of vendors with an arrow to the left
      of the vendors selected.  At the start, ALL vendors are selected.


      Move the cursor using the cursor keys or the first letter of the
      vendor name.  If more than one vendor's name starts with the same
      letter the cursor stops at the first and repeated strikes of that
      key proceeds down the list.

      To select a vendor, use the following function keys:

      F5-drop this - removes the highlighted vendor from the searchlist.
      F3-add this  - adds the highlighted vendor to the searchlist. 
      F7-Only this - makes the highlighted vendor the only vendor on the
                     searchlist. 
      F9-reset ALL - selects ALL vendors. 
      F10          - will begin a search, if a new selection has been
                     made, or abort the operation if no selection has
                     been made.

      esc  will abort the operation and return to the selection menu.

      Operations can be combined in a single search - to find all mat-
      erials made by vendor 'A' or 'B', move the cursor to 'A' and type
      F7, then 'B' and F3.  F10 starts the search.

      The F9-Reset key is an editing key; it allows quickly clearing your
      selection if you make a mistake and wish to start over, BEFORE a
      search.  After a search, F9 does not UNDO the search; although the
      arrows will re-appear indicating that the search-criterion has been
      reset, the selected materials will not change.


                         2- Selection by Material Type

      This selection pops up a list of materials types, or classes, with
      a small arrow to the left of the materials selected.  At the start,
      ALL materials are selected, and thus marked.

      The materials listed are:

               MnZn Ferrite      - Manganese or Manganese-Zinc Ferrites
               NiZn Ferrite      - Nickel-Zinc Ferrites
               Powdered-Iron
               Moly-Permalloy
               Met-Glass
               Steel
               Tape-Wound

      The following commands allow forming a searchlist:

      F5-drop this - removes the highlighted material from the searchlist.
      F3-add this  - adds the highlighted material to the searchlist.
      F7-Only this - makes the highlighted material the only material on the
                     searchlist.
      F9-reset ALL - selects ALL materials.

      F10 or ENTER will begin a search, if a new selection has been made, or
           abort the operation if no selection has been made.

      esc  will abort the operation and return to the selection menu.


      Use the cursor keys or the first letter of an option to highlight a
      selection, then one of the above function keys.


                         3- Selection by Material Code

      This selection pops up two boxes; the first, a list of vendors,
      with the first vendor high-lighted and the second, the materials
      that the high-lighted vendor makes.

      A prompt at the screen bottom indicates that you may now start a
      Search or an eXclude searchlist.

      A Search will find only those materials on your list; an eXclude
      will find those materials NOT on your list.

      To begin a Search list, use the cursor keys to highlight a vendor,
      then type F3; to begin an exclude list type F4.  You will be
      prompted for a material name, which you should enter as given in
      the vendor's box.  A new command now becomes available; typing 'F4'
      allows you to add another material to the list.

      To select another vendor move the cursor to the next vendor and hit
      F4.  To begin the search hit the F10 key from the vendor menu; the
      ESC key will abort the search.

      This selection is very useful in the Cores Menu.  In the Material
      menu it is mostly useful to show a one page summary of all mat-
      erials made by any vendor.


                             Selection by Parameter

      This set of options allows choosing materials by any of the
      following:

      4- Initial Permeability                9- loss factor 
      5- Maximum Permeability                A- disaccommodation 
      6- Saturation Flux Density             B- Hysteresis Constant 
      7- Residual Flux Density               C- Curie Temperature 
      8- Coercive Force                      D- Frequency Range 

      When you make one of these selections, a small box opens showing:

                       the parameter, 
                       the minimum search value, 
                       the maximum search value, 
                       and the units of measurement used.

      The cursor keys move the highlighted bar between the Min and Max
      fields.  When the proper field is highlighted, press ENTER to
      change the field.  A second box opens prompting you for a numerical
      value.  Enter a number and press the ENTER key.  For scientific
      notation, the proper format is, 1.5E-9: no spaces are allowed.

      You may enter search limits for either min or max or for both.  The
      ESC key exits the procedure without starting a search. F10 begins a
      search if a search limit has been changed.

      The Min field must always be less than the Max field; attempting to
      enter values which would make the Min field greater than the Max
      field or the Max field less than the Min field sounds a tone and
      aborts the operation.


                             E - Selection by Notes

      This selection allows selecting materials by the contents of their
      note-field.  One possible use would be to find a material if you
      remember a warning was in the note-field.

      This selection will pop up a small box, prompting for a search-
      string.  Enter a string, ending with the ENTER key.  The backspace
      key allows limited editing.  If you decide not to perform a search,
      strike the ENTER key on a blank search-string.

      The program then checks all records in the database for materials
      with note-fields containing the search-string.



                        F - Selecting by Cores Selected

      This selection will scan the cores selected in the Core Menu and
      select those materials used in one or more cores.  If you have not
      used the Core Menu to select cores, this option will display all
      materials which are used by any cores.  As vendors often list
      materials which they do not produce in stock cores, this will drop
      some materials from the material selection list.

      This is a quick way to generate reports on alternate sources: use
      the Core Selection Menu to find cores, move to the Materials Menu,
      and select all the alternate materials with one keystroke.



                              F2 - Viewing Graphs

      Much of the information about materials is given in graphs in the
      vendors' databooks: CoreDBMS allows viewing the same information in
      a similar graphical format.

      Up to 10 graphs may be retrieved for each material:

      1-loss factor vs frequency           6-permeability vs frequency 
      2-loss factor vs temperature         7-static magetization curves 
      3-permeability vs temperature        8-core loss vs flux density 
      4-permeability vs ac flux            9-core loss vs temperature 
      5-permeability vs dc bias           10-Flux Density vs temperature

      Not all graphs are available for every material.

      The graphs menu is called up by hitting the F2 key from any Mat-
      rials menu.

      The graphs menu displays the current selected-material on the top
      line and several help lines at the screen bottom.  In the screen
      center a menu lists the ten graphs.  To the left of each graph a
      star indicates that the graph is available: if the star is missing,
      the graph is not available for the current material.

      To display a material, type the number to the left of the graph or
      high-light the graph using the cursor keys and hit ENTER.  You can-
      not select a graph which is not starred.  The Pg-Up, Pg-Dn, and up-
      and down-cursor keys allow changing the current material.

      When displaying a graph, the right- and left-cursor keys display
      the other graphs available for the current material.  The P key
      will dump the graph to the printer.  Note that the printer must be
      capable of printing graphics.

      The current material is set by where the graphs menu is called
      from.  If called from the main material menu, the current material
      is the first on the selection list.  If called from the Detail
      menu, the current material is the material displayed.  If called
      from the Browse menu the current material is the material at the
      top of the Browse screen, or the high-lighted material if the
      cursor is active on the Browse screen.



             F3 - Browse - and F4 - Detail - Viewing the Materials

      Two display modes are provided in the Materials Menu.

      BROWSE mode displays the materials across the screen, twenty mat-
      erials to a page.  The TAB, shift-TAB, and 1,2,3 keys move sideways
      through the screens.

      Screen 1 shows; the Vendor, Material Type, Material name, initial
      Permeability, maximum Permeability, Saturation Flux density in
      Gauss and Oersteads for the measurement, the residual flux density
      in Gauss, the Coercive force in Oersteads, and the minimum and
      maximum recommended operating frequency in Hertz.

      Screen 2 shows; loss factor, the frequency at which it was measur-
      ed, dissipation factor, the specific gravity, and the Curie temp-
      erature.

      Screen 3 gives the notefield for the material.

      BROWSE mode is a fast way to compare materials.  Enter the BROWSE
      screen by hitting F3, either from the Materials menu or the DETAIL
      screen.


      DETAIL mode uses the entire screen to show all of the data on one
      material.  From the Material Menu, F4 will display the first
      material on the selection list.  From the BROWSE screen, F4 will
      display the top record on the screen.

      DETAIL and BROWSE are designed to be highly integrated.  When in
      the BROWSE screen, hitting F3 enables a cursor which high-lights a
      material.  With the cursor on, hitting F4 will enter the DETAIL
      screen showing the material high-lighted by the cursor.  Hitting F3
      returns to the BROWSE screen.

      While in either display mode, F7 will jump to the print routine and
      F8 will jump to the SORT routine.  F10 will return to the Material
      Menu.

      F5 will delete the displayed record when in Detail mode or the
      high-lighted record when in Browse mode with the cursor on.

      When in Browse mode, with cursor on, or in Detail mode, the cross-
      reference feature - activated by typing X - will select cores from
      the core selection list which use the high-lighted material.  This
      is useful, but can be confusing - it should be used with caution.

                       F7 - Printing and Filing Materials

      The Print menu allows you to print or file the results of your
      searches.

      You can print a list of materials for review away from the comput-
      er, put results in a file for inclusion in word-processing doc-
      uments or allow for post-processing of your results by importing
      into a spreadsheet or other program.

      The Print menu may be called from the select menu or any viewing
      menu by hitting the F7 key.  A series of prompts then appears on
      the screen, guiding you through the selections.

      When the Print menu is called, the first sub-menu selects file or
      print and the data format:

           Print in Browse format - this mode puts your printer in com-
              pressed-mode and prints material data on two lines; the
              first line contains the vendor name, material type, and
              material name, the second contains material data.
               
           Print in Detail format - prints a report in detail format.

           Print in Detail format, with Graphics presently defaults to
              the prior selection. 

           File in Browse format - files the data in the Browse format.
              The first line contains control characters to set the
              printer into compressed-mode, and the last line contains
              control characters to reset the printer. This may be used
              to file the data for later printing at a remote printer.

           File in Detail format - files the data in the Detail format. 

           File in Comma-delimited format - files the data for import
              into other programs.  All text data is enclosed in double-
              quotes, and all data is separated by commas. 

              The file output consists of three lines as follows: On line
              1; vendor name, material type, and material, initial perm-
              eability, max permeability, saturation flux density and
              Oersteds at the reading point, residual flux, Coecive
              Force, Relative Loss, and Disaccomodation factor, resis-
              tivity, density, Curie temperature, minimum frequency, and
              maximum frequency.

      If you select a file-operation, you are prompted for a file name.
      The file name should be a legal DOS name.  The program will check
      if this file exists, and give the option of over-writing the file
      or appending new data to the file.

      Where in the Cores menu you are prompted for printing a single core
      or all cores, in the material menu the choice defaults.

      If called from the Selection Menu, or the BROWSE display with
      cursor off, the default is to print all materials.  In Browse with
      the cursor on, and in Detail the default is to print only the high-
      lighted material.

      There are two cautions to bear in mind when using file and print.

      First since CoreDBMS is a LARGE database, attempting to print or
      file a large number of records will take up a considerable amount
      of time - and paper or disk space.  The program will warn you if
      the number of records selected seems excessive, but if you answer
      'YES' to the 'Are you Sure?' prompt, the program will dutifully
      attempt to print however many records are selected.

      TO TERMINATE A PRINTING SESSION hit any key, and respond to the
      "terminate printing?" question with Y.

      Second, CoreDBMS relies on DOS BIOS calls for checking printer
      status.  This is fast for detecting no-printer and printer-not-
      ready states, but extremely slow for detecting when a printer is
      attached but turned off.  Average time appears to be 30 seconds in
      this case, but will vary - widely! - depending on the author of the
      BIOS firmware.  Turn your printer ON before running CoreDBMS.

      The print routine assumes that your printer is connected to LPT1 -
      or printer port 1.  If your printer is connected to another port
      you should use the /LPTn switch when running the program to
      identify the port, or file the data and print the file later.

      An alternative to this is to use the FILE options rather than the
      PRINT options, and when prompted for a file name to use one of the
      DOS default files; LPT1, LPT2, LPT3, COM1, COM2.

      This allows using changing printers from within the program and
      using printers connected to serial ports.



                             F8 - Sorting Materials 

      Sorting materials is a powerful tool for quicker and easier
      comparisons.

      When you enter the sort routine, a menu is displayed with all of
      the sorting criterion.  All sorts are in made in ascending order,
      and may be made by:

              Vendor                      residual flux density 
              Material Type               coercive force 
              initial permeability        loss factor 
              maximum permeability        Curie temperature 
              saturation flux density     max frequency  

      To select a sort criterion, type the number or letter which precedes
      the selection in the menu.  A repeat of the first menu will appear.
      You may use up to two sort criterions.

      The sort commences when you strike the F10 key; you may abort the
      sort - BEFORE execution ! - by hitting the ESC key.

      The sort takes place in two steps; first the database is read and the
      sort fields indexed, then the sort process itself is performed.  A
      brief "Indexing" and "Sorting" message is displayed in each section.


                     F9 - Reseting the Materials Searchlist

      From the Material Menu, F9 will reset any selections you have made so
      that all materials are available.




                 Chapter 5  - F3 - Selecting and Viewing Cores

      When you enter the core selection and viewing routine the screen
      shows two boxes: on the right a status box shows the database, re-
      vision, number of cores in the database, and number of cores
      selected and tagged.  On the left a box presents the selection
      options, with one option highlighted.

      At the bottom of the screen, a help line displays additional
      options, which will be described later in this chapter.

      You may view the selected cores using the F3, F4, or F6 keys, or
      you may reduce the number of cores by making selections.

      The search routine is similar to that used in library services.
      You start with ALL records 'selected' or available.  You then set
      selection guidelines to reduce the number of records to a usable
      number.

      The selection process is a 'forward-only' one; you can not reverse
      a selection once made.  If the result of a search matches no cores,
      you must reset to all cores selected via the F9 key - RESET.

      Unlike the selection process with many other databases, this
      selection process may be done in steps.  To find all nickel-zinc
      ferrite torroids made by vendor 'A' you can first request all cores
      made by vendor 'A' then all torroids then all nickel-zinc cores -
      the order of searching is not important.

      Move the highlighted-bar in the selection options box using the
      cursor keys, then hit the ENTER key to choose a selection option.
      Or type the number of the selection option.



      The selection options will now be given in detail, followed by the
      function-key options within the Core Selection menu.


                          0 - Selection by Part Number

      This selection pops-up a box, prompting for a search-string.  Enter
      a string, ending with the ENTER key.  The backspace key allows
      limited editing.  If you decide not to perform a search, strike the
      ENTER key on a blank search-string.

      The program checks all records in the database for part numbers
      containing the search-string.

      Common errors made in this type of search are to provide too many
      characters, or too few.

      An example of too many characters: some cores have prefixes or suf-
      fixes which describe options.  These options are not included in
      the database part number, but intead are described in the note
      field.  If you enter such an option in your search-string, the
      search will fail.  It's always safest to use the minimum root for a
      search ( "4525" and not A4525-23 ) and risk selecting more than one
      record.

      An example of a string with too few characters is, "1", which will
      retrieve most of the records in the database.


                            1 - Selection by Vendor

      This selection pops up a list of vendors with an arrow to the left
      of the vendors selected.  At the start, ALL vendors are selected.

      Move the cursor using the cursor keys or the first letter of the
      vendor name.  If more than one vendor's name starts with the same
      letter the cursor stops at the first, and repeated strikes of that
      key proceeds down the list.

      To select a vendor, use the following function keys:

      F5-drop this - removes the highlighted vendor from the searchlist.
      F3-add this  - adds the highlighted vendor to the searchlist.
      F7-Only this - makes the highlighted vendor the only vendor on the
                     searchlist. 
      F9-reset ALL - selects ALL vendors. 
      F10          - will begin a search, if a new selection has been
                     made, or abort the operation if no selection has
                     been made. 
      esc          - will abort the operation.

      Function keys can be combined in a single search.  For example, to
      find all cores made by either vendor 'A' or 'B', move the cursor to
      'A' and type F7, then 'B' and F3.  Finally, F10 - or the ENTER key
      - starts the search.

      The F9-Reset key is an editing key which allows clearing your
      selection if you make a mistake and wish to start over, BEFORE a
      search.  After a search, F9 does not UNDO the search; although the
      arrows will re-appear indicating that the search-criterion has been
      reset, the selected cores will not change.


                         2- Selection by Material Type

      This selection pops up a list of materials types, or classes, with
      a small arrow to the left of the materials selected.  At the start,
      ALL materials are selected, and thus marked.

      The materials listed are:

             MnZn Ferrite   - Manganese or Manganese-Zinc based Ferrites
             NiZn Ferrite   - Nickel-Zinc Ferrites
             Powdered-Iron
             Moly-Permalloy
             Met-Glass
             Steel
             Tape-Wound

      From the above list, the following commands allow forming a search-
      list:

      F5-drop this - removes the highlighted material from the searchlist.
      F3-add this  - adds the highlighted material to the searchlist.
      F7-Only this - makes the highlighted material the only material on 
                     the searchlist. 
      F9-reset ALL - selects ALL materials.

      F10 or ENTER will begin a search, if a new selection has been made, or
           abort the operation if no selection has been made.

      esc  will abort the operation and return to the selection menu.

      Use the cursor keys or the first letter of an option to highlight a
      selection, then one of the above function keys.


                         3- Selection by Material Code

      Material Code selection is a complicated - but powerful - option.

      This selection pops up two boxes; the first, a list of vendors with
      a vendor high-lighted and the second, the materials that the high-
      lighted vendor makes.

      A prompt at the screen bottom indicates that you may now start a
      Search or an eXclude searchlist.

      A Search will find only those cores matching a material on your
      list; an eXclude will find all cores NOT matching a material on
      your list.

      To begin a Search list, use the cursor keys to highlight a vendor
      then hit F3; to begin an eXclude list type F4.  You will be prompt-
      ed for a material name, which you should enter as given in the
      vendor's box.  Typing 'F4' then allows you to add additional mat-
      erials to the list.

      To select another vendor move the cursor to the next vendor and hit
      the F4 key again.  To begin a search hit the F10 key; the ESC key
      will abort the search.

      This search is useful in finding alternate sources; if you know
      that material A from one vendor and material B from a second vendor
      will both work in your application, this option will allow select-
      ing all cores with either material.

      Or, if you know that your application cannot use a material, this
      option allows quickly dropping all cores with that material from
      consideration.

                          4- Selection by Form Factor

      Selection by form-factor pops up a list of the various form-factors
      with an arrow to the left of the form-factors selected.  At the
      start, ALL forms are selected, and marked.

      From this list, the following commands allow forming a searchlist:

      F5-drop this - removes the highlighted form from the searchlist.
      F3-add this  - adds the highlighted form to the searchlist.
      F7-Only this - makes the highlighted form the only form on the
                     searchlist.
      F9-reset ALL - selects ALL form-factors.

      F10 or ENTER will begin a search, if a new selection has been made, or
           abort the operation if no selection has been made.

      esc  will abort the operation and return to the selection menu.

      Use the cursor keys or the first letter of an option to highlight
      your selection, then one of the above function keys.  Searching for
      several forms is possible by combining the above keys.  For
      example, to search for either EC or EE cores, type E and F7, and
      then E and F3.  Type F10 to begin the search.


                           5- Selection by Dimensions

      The eight core dimensions are indicated by the letters A through G.
      Selecting by core dimension requires some care; although an effort
      was made to keep dimensions consistent for all core form-factors,
      this was not always possible.  Dimension G is quite different in an
      EC core and an EP core.

      Before attempting a selection by dimension you may wish to make a
      selection by form factor or figure, or re-view the core outlines.
      As an aid in this process, function-key F2 will display core
      outlines.

      When you make a selection by dimension, a menu appears with the
      letters; choose a dimension by typing a letter or by moving the
      high-light bar and typing ENTER.  A small box is opened showing:

                       the dimension, 
                       the minimum search value, 
                       the maximum search value, 
                       and the unit of measurement used.

      The cursor keys move the highlighted bar between the Min and Max
      fields.  When the proper field is highlighted, press ENTER to
      change the field.  A second box opens prompting you for a numerical
      value.  Enter a number and press the ENTER key.  For scientific
      notation, the proper format is, as example,  1.5E-9    .

      You may enter search limits for both min and max or for either.
      The ESC key exits the procedure without starting a search. F10 will
      begin a search if a search limit has been changed.

      The Min field must always be less than the Max field; attempting to
      enter values which would make the Min field greater than the Max
      field or the Max field less than the Min field sounds a tone and
      aborts the operation.



                             6- Selection by Notes

      Selection by Notes opens a box prompting you for a search-string.

      Type a string, ending with the ENTER key.  The backspace key allows
      limited editing of the string.  If you decide not to perform a
      search, strike the ENTER key on a blank search-string.

      The program will check all records in the database for notes which
      contain the search-string.  Partial strings are okay - any record
      which contains the search string will be found.

      There are several abbreviations used in the note field which are
      helpful in searching:

      *G  indicates that this core is gapped. 
      *T  indicates that a center-hole tuner is available. 
      *GS indicates a core with a stepped-gap center leg, often called a
          type-3 pot. Rotation of the two core halves changes the
          inductance over a range of values. 
      *P  indicates a 'preferred' core for that vendor.

      Selection by Notes takes a long time when searching the entire
      database.  If possible try limiting the number of cores with any
      other search before searching the note-field.



                 7 through 9, A, and B - Selection by Parameter

      The above selections set search limits for various core parameters:

             effective path length          inductance factor, Al 
             effective area                 weight 
             effective volume 

      When you choose one of these selections, a small box is opened
      showing:
                       the parameter, 
                       the minimum search value, 
                       the maximum search value, 
                       and the unit of measurement used.

      The cursor keys move the highlighted bar between the Min and Max
      fields.  When the proper field is highlighted, press ENTER to
      change the field.  A second box opens prompting you for a numerical
      value.  Enter a number and press the ENTER key.  For scientific
      notation, the proper format is, 1.5E-9.

      You may enter search limits for both min and max or for either.
      This allows, for example, finding all cores with effective area -
      Ae - between two limits.  The ESC key exits the procedure without
      starting a search. F10 will begin a search if a search limit has
      been changed.


      The Min field must always be less than the Max field; attempting to
      enter values which would make the Min field greater than the Max
      field or the Max field less than the Min field sounds a tone and
      aborts the operation.


                           C - Miscellaneous Searches

      Selection by figure groups cores which look the same.  Form factor
      does this to an extent, but there are variations of design within
      each form factor.  For example, the CC/UU core is available with:

                             two rectangular legs;
                         two rectangular legs, notched;
                     one rectangular and one octogonal leg;
                     one rectangular and one circular leg;
                               two circular legs,
                      two circular legs with center-holes,
           circular legs with mounting-hardware channels in each leg,
                          and with two octagonal legs.

      When you make this selection you have the option to select a figure
      or exclude a figure.  Choose either option and a prompt box appears
      for you to enter the figure number.

      Selection-by-Unique-Size quickly reduces the number of cores when
      you are interested only in size.  This selection scans the list of
      selected cores and deletes all but the first of identically sized
      cores.  This eliminates cores in different materials and with
      different gapping.  The selection process insures that cores of the
      same size from different vendors are kept.

      Selection by Window Area is handy when you have an idea of how much
      winding area you require.  Selection by Ae*Aw product is an option
      that allows use of this figure of merit during searches.

      Selection or Exclusion of gapped cores is similar to the figures
      option, and allows quick searches according to gaps.

      Cross-Reference to Materials - or search by selected materials -
      will read the Material Selection list set from the Material
      Selection Menu and select those cores with materials on the list.
      This is faster than manually entering the materials in the Select
      by Material Code option.


                                    D - Tags

      Tagged cores cannot fail a selection and are not cleared by the F9-
      Reset key; this allows performing 'ORing' searches.  Perform a
      search, tag the result, reset with the F9 key, and perform a second
      search.  The resulting selection list is the cores matching either
      the first search OR the second.

      Tagged cores may be cleared using shift-F9 which also resets the
      selection list.

      The Tag Menu allows tagging all selected cores, selecting all tagged
      cores, and clearing - or resetting - all tagged cores.

      Tagging all selected cores is the second step in an ORing search as
      mentioned above.  This may also be done by hitting the F2 function
      key.  Note that Tag-all-selected cores will not work if the selected
      cores is equal to the total cores - that is, if you have not made
      any selections.

      Selecting all tagged cores is a fast way to recall tagged cores for
      viewing.

      Clear all tagged cores will un-tagged cores.  This does not affect
      selected cores, unlike shift-F9 which clears tagged cores and re-
      sets the selection list.



                  M - Match a Core - Finding Alternate Sources

      This option provides a fast way to find all cores of the same form-
      factor and dimensions as a core you specify.  It is therefore very
      useful when you have to find an alternate or secondary supplier for
      a core.

      You must first select a single core, either by limiting the
      selection list to a single core(perhaps by searching for a known
      part number), or by pointing to a core in the BROWSE or DETAIL
      viewing modes and tagging it with the F2 key.

      After selecting a core you may enter a tolerance for matching
      dimensions or accept the default of +/-10% .  You may also limit
      the search to the same material type as your selected core, or
      search through all materials.

      The result is a selection list of all cores which are of the same
      form-factor, material type(optional), and with dimensions matching
      your selected core.

      This search does not check figures, so if you want a core EXACTLY
      like the selected core you may have to do a further selection by
      figure.


                  Other Options within the Core Selection Menu

                                 S - Statistics

      While in the Selection Menu, the 'S' key will display the stat-
      istics page for all selected cores.

      This can be a useful tool during searches.  Selecting a vendor and
      then requesting statistics will show you the number of all forms
      the vendor produces, the number of cores in each form, and the
      number of cores in each material.

      Alternately, selecting a form will show you which vendors produce
      it, and in what materials it is available.


                         F2 - Tag the Selected Records

      Usually you will search, find a core, clear the search, and stop;
      or perform another search.  But there may be times when you want to
      keep the results of the first search and add it to the second.

      The Tag feature allows this: by hitting the F2 key, all selected
      records are made permanent.  Tagged records always pass any test,
      and so stay in the selection list.

      Tagged records are not reset by the F9 key.  Tagged records are
      removed from the selection list by hitting, shift-F9, which resets
      all records including Tagged ones; or may be deleted by the delete-
      record function in BROWSE or DETAIL mode.

      Alternately, the Tag option in the selection menu allows control of
      Tagged records.


                   F3 - Browse, F4 - Detail, and F6 - Compare
                              Viewing the Database

      Once you have selected a list of cores, CoreDBMS has three ways of
      viewing the list.


      BROWSE shows 20 records at a time, each record written across the
      screen on a single line.

      There are four screens in Browse - you could think of the core
      record written across all four screens placed side-by-side.  The
      TAB and shift-TAB keys and 1,2,3,4 move sideways through the
      screens.

      The first screen shows part number, vendor, material, form-factor,
      and magnetic data.

      The second screen shows the core dimensions, figure and bobbin
      number, and a tagged field.  The third screen shows the minimum
      area, weight, window area and Ae*Aw product.  The fourth screen
      shows the note field.


      The cursor keys, Page-up, Page-down, HOME, and END move you up and
      down through the list of cores, and 'J' prompt you for a relative
      record number and then 'Jumps' the screen to show that record( if
      the record has been eliminated in a selection JUMP will move to the
      nextrecord; if the list has been sorted JUMP moves to the relative
      record number in the sorted series.)

      One field of each Browse screen is a record number.  This number
      from 1 to 9999 is the relative position of the core in the data-
      base.  If the database is sorted the record number moves with the
      cores.

      The record number allows fast and easy movement through the cores
      by providing a simple way of identifying a core.

      The BROWSE format makes extensive use of abbreviations to get the
      maximum information on a screen.  For example, "FORM" for form-
      factor shows "Tor" for torroid; the vendor field is truncated, and
      in some cases the part-number field may be truncated as well.  To
      see all the data, you can use DETAIL mode, discussed below.

      The bottom line of the Browse screen displays the major options:

      F1 - displays the help screen. 
      F2 - tags all selected records, or the high-lighted record if the
           cursor is active 
      F3 - toggles the cursor on and off. 
      F4 - jumps to DETAIL mode. With the cursor off you are prompted for
           a record; with the cursor on, the high-lighted record is used. 
      F5 - deletes a record from the select list. With the cursor off you
           are prompted for a record; with the cursor on, the high-
           lighted record is used. 
      F6 - jumps to COMPARE mode. 
      F7 - opens the FILE/PRINT menu. 
      F8 - opens the sort menu. 
      F10- exits the display mode.


      The F3 key enters the BROWSE screen.

      Tapping the F3 key while in BROWSE activates a cursor which may be
      moved using the arrow keys. All of the options available in the
      normal mode are available with the cursor on, but now affecting
      only the record high-lighted by the cursor.  Tap the F3 key again
      to turn the cursor off.

      In Browse Mode with the cursor ON a cross-reference function to the
      Materials menu is available.  By typing  X  the Detail-Material
      screen for the material used in the high-lighted core will be
      shown.  The F10 key, ENTER, or X will return to the Core Browse
      Mode.


      DETAIL shows one record at a time, using an entire screen -  this
      is a convenient way to see all of the data on the core at a glance.

      If you have a graphics terminal the detail screen also shows an
      outline drawing of the core.

      You can enter the DETAIL screen with the F4 key - which will prompt
      you for the record number to display - or by holding the shift key
      and pressing F4, which if you are in the Main Menu will jump to the
      first record in the selection list, or if you are in the Browse
      display will jump to the first record on the present Browse screen.

      The first method is most useful from the BROWSE screen when you
      have records on the screen and can see the record number, or when
      you want to see a core for which you have memorized or recorded the
      number.

      As with BROWSE, DETAIL displays the major options on the bottom
      line of the screen:

      F1 - displays the help screen. 
      F2 - tags the displayed record. 
      F3 - jumps to BROWSE mode.
      F4 - prompts for a new record to display in DETAIL mode. 
      F5 - deletes the displayed record. 
      F6 - jumps to COMPARE mode. 
      F7 - opens the FILE/PRINT menu. 
      F8 - opens the sort menu. 
      F10- exits the display mode.


      In Detail Mode, X - the Cross-Reference function - will display the
      Detail-Material screen for the material used in the displayed core.
      The F10 key, ENTER, or X will return to the Core Detail Mode.


      BROWSE and DETAIL are useful for quickly scanning records.  But for
      making detailed comparisons between cores, each have draw-backs.

      Consider comparing a list of torroids from several vendors in an
      attempt to find the closest match in both size and inductance, with
      an Ae value exceeding a given value.  BROWSE will easily show the
      list, but the core dimensions and the Al values are on different
      screens.  This forces you to jump between screens in the com-
      parison.  DETAIL presents all the information on one screen, but
      for a single core - comparing cores requires jumping screens for-
      ward and back and relying on memory.

      You could PRINT the selection list in Browse-format and compare the
      printed list, but COMPARE allows doing this at your terminal.

      COMPARE shows seven records at a time on one screen, and shows the
      majority of information about the cores.

      To display this amount of data on one screen, COMPARE makes use of
      fore-ground and back-ground colors in text mode.  On a monochrome -
      Black-and-White - monitor, you will find that COMPARE makes little
      sense.

      At the top of the COMPARE screen a status line shows the number of
      cores in the database, the number of cores selected, and the number
      of pages required to list the selected cores.

      Each record consists of three lines.  The first line is a header in
      black on a light-blue background giving record number, part number,
      vendor, material, and form-factor.  The second line shows lm, Ae,
      Ae-min, Ve, Al, and weight in alternating fields of blue and green.
      The third line gives mechanical dimensions, figure, and bobbin data
      in alternating fields of red and white.

      To compare records, scan down the screen at alike-colored fields.
      To compare the A-dimension of all the records, scan down the screen
      at the first red field.

      This sounds difficult, and perhaps a bit odd, but you'll find that
      a bit of practice allows for very quick use.

      At the bottom of the screen is a prompt line in white, showing the
      major options from this mode, and a multi-color key to identify the
      data on the screen.



                         F7 - Printing and Filing Cores

      F7 allows you to print or file the results of your searches.

      You can print a list of cores for review away from the terminal,
      put results in a file for inclusion in word-processing documents,
      print a core specification-sheet, or allow for post-processing of
      your results by importing into a spreadsheet or other program.

      The Print menu may be called from the select menu or any viewing
      menu by hitting the F7 key.  A series of prompts then appears,
      guiding you through the selections.

      When the Print menu is called, the first sub-menu selects file or
      print and the data format:

           Print in Browse format - this mode puts your printer in com-
              pressed-mode and print data on two lines; the first line
              contains the vendor name and the part number, the second
              contains electrical information and dimensions. 

           Print in Detail format - prints a report similar to the detail
              screen, without figure.

           Print in Detail format, with Graphics - as above, plus the
              core outline figure is printed.

           File in Browse format - files the data in Browse format. The
              first line contains control characters to set the printer
              into compressed-mode, and the last line contains control
              characters to reset the printer. This may be used to file
              the data for printing later.

           File in Detail format - files the data in Detail format. 

           File in Comma-delimited format - files the data for import
              into other programs.  All text data is enclosed in double-
              quotes(""), and all data is separated by commas. 

              The data filed is:  the part number, the vendor, the
              material type, the material, the form-factor, the figure
              number, the effective area, the minimum area, the effective
              magnetic length, the inductance factor, the weight, and the
              eight dimensions, from A through H.

      If you select a file-operation, you are prompted for a file name.
      The file name should be a legal DOS name.  The program will check
      if this file exists, and give the option of over-writing the file
      or appending new data to the file.

      When called from the Selection Menu, BROWSE, or COMPARE you are
      prompted for printing all selected records or one single record.
      If called from DETAIL, the print routine assumes you wish to print
      the record you are currently viewing.

      Graphics output to a printer takes approximately one minute per
      figure and requires a CGA, EGA, or VGA graphics terminal and a
      graphics printer.


      There are two cautions to bear in mind when using file and print.

      First since CoreDBMS is a LARGE database, attempting to print or
      file a large number of records will take up a considerable amount
      of time - and paper or disk space.  The program will warn you if
      the number of records selected seems excessive, but if you answer
      'YES' to the 'Are you Sure?' prompt, the program will dutifully
      attempt to print however many records are selected.

      TO TERMINATE A PRINTING SESSION hit any key, and respond to the
      "terminate printing?" question with Y.

      Second, CoreDBMS relies on DOS BIOS calls for checking printer
      status.  This is fast for detecting no-printer and printer-not-
      ready states, but extremely slow for detecting when a printer is
      attached but turned off.  Average time appears to be 30 seconds in
      this case, but will vary - widely - depending on the author of the
      BIOS firmware.

      The print routine assumes that your printer is connected to LPT1 -
      or printer port 1.  If your printer is connected to another port
      you must use the /LPTn switch when running the program to identify
      the port, or file the data and print the file later.

      An alternative to this is to use the FILE options rather than the
      PRINT options, and when prompted for a file name to use one of the
      DOS default files; LPT1, LPT2, LPT3, COM1, COM2.

      This allows using changing printers from within the program and
      using printers connected to serial ports.


                          F8 - Sort: Sorting the Cores

      Sorting your selected cores is a powerful tool for quicker and
      easier comparisons.

      When you enter the sort routine, a menu is displayed with all of
      the sorting criterion.  All sorts are in made in ascending order,
      and may be made by:

              Part Number             Magnetic path length, Lm 
              Vendor                  Material Type           
              Material                Effective Area, Ae
              Form Factor             Al 
              Weight                  Figure 
                                      and by dimensions A through H.

      To select a sort criterion, type the number or letter which precedes
      the selection in the menu.  A repeat of the first menu will appear.
      You may use up to four sort criterions; the sorting order is set by
      the order you make your selections, e.g., if you select dimension A,
      then B, and then C, the cores will be placed in order of ascending A
      dimension; if two or more cores have the same A dimension those cores
      will be further sorted by ascending B dimension, etc.

      The sort commences when you strike the F10 key; you may abort the
      sort - BEFORE execution ! - by hitting the ESC key.

      The sort takes place in two steps; first the database is read and the
      sort fields indexed, then the sort process itself is performed.  A
      brief "Indexing" and "Sorting" message is displayed in each section.

      Sorting a large number of records can take a large amount of time.
      To achieve a fast sort, the sort is performed in one 64k block of
      memory - this limits the maximum number of records which can be
      sorted to about 1500.  A limit of 1000 cores has been set for all
      sorts.  However, for fast sorting you should consider 200 to 500
      records as a reasonable maximum.

      To further speed sorts, sort on the minimum number of fields.
      Sorting by four criterion will take longer than sorting by one.


                         F9 - Reset the Selection List

      Use this key to 'reset' your search criterions so that all cores are
      displayed.

      The F9-Reset key will not change the status of tagged records -
      holding down the Shift key while striking F9 will also reset any
      Tagged records.


                              Chapter 6  - Examples

      Let's begin with a general browse through the core selection menus.

      When you execute CoreDBMS you begin in the Main Menu.  Press the F9
      key and the program will index the database and print two screens of
      statistics about the cores.

      Hit any key to clear the statistics screen, then the F3 key to enter
      the Core Selection & Viewing Menu.


      First let's make CoreDBMS act as an on-line vendor's catalog by view-
      ing the cores from Magnetics Inc.

      Hit 1, for select-by-vendor; then M to jump to the first 'M'-vendor,
      then F7 to select-only-this vendor, then F10 to search.

      The program quickly comes back to report that xxxx cores have been
      selected.

      Hit S, and the statistics screen is called, now presenting statistics
      for only the selected cores: showing the material-types the vendor
      makes, the form-factors, and finally the figures that apply to this
      vendor.

      Hit any key to return to the Core Selection Menu and then F3 to enter
      the Browse display.

      At the upper right of the screen the number of pages available in
      Browse is displayed; at present about 52 pages.

      To reduce this number hit F10 to return to the Selection Menu, then
      C, for Miscellaneous Selections and 1, for Select-by-Unique sizes.
      This option selects unique cores by size, resulting in a single core
      of each size with no repeats due to different materials or gapping.

      Hit S, and the statistics screen will now show the number of unique
      core sizes from the vendor.

      Now hit F3 and the number of pages is only 8; a comfortable number to
      quickly browse through.  At present the cores are roughly sorted by
      form-factor.  Let's sort by effective-Area.

      Hit F8, to enter the Sort Menu; 7, to select Ae, and F10 to start the
      sort.  The screen is redrawn with the cores sorted by effective-Area.
      Hit 3, to display window 3 of the Browse screen, then F8 for the Sort
      Menu, J for window area, and F10 to begin the sort.  When the screen
      is redrawn the cores are now sorted by window area.  Hit the END key
      to show the end of the list, giving the largest window areas.

      Hit F10 to return to the Selection Menu and F9 to reset the selection
      list.

      Now let's find all torroids from all vendors: hit 4, for select by
      form-factor, T for torroid, F7 for only-torroids, and F10 to perform
      the search.

      The program comes back to report that xxxx cores have been selected.

      Hit C, for Miscellaneous Selections and 1, for Select-by-Unique
      sizes.  Then F8 for the Sort Menu, A for dimension A and H for
      dimension H, and F10 to perform the sort.  You now have a list of
      torroids from all vendors, sorted by outer-diameter and by height.


      Hit F9 to reset the list, 1 for vendors, M, and ENTER to select
      Magnetic Inc's.  Hit C for Miscellaneous Selections and 1 for Select-
      by-Unique sizes.

      Hold down the SHIFT key and hit F4.  You enter the DETAIL display
      with the first selected core, the screen now showing the core data
      and an outline drawing of the core.

      The material displayed is Magnetic's A ferrite.  Hit the X key and
      you jump to the Materials Display section with a full screen of
      information on Magnetic's A material.  Hit X, ENTER, or F10 to return
      to the DETAIL core display.


      With these tools powerful searches can be performed.

      Example; find a torroid core for a pulse transformer, with outer
      diameter under 0.5 inch and Ae between 0.1 and 0.3 cm^2.

              Hit 4 for select by form-factor, T for torroid, F7 for
              only-torroids, and F10 to perform the search.

              Hit 5 for select by dimensions, then A.  Use the cursor
              keys to high-light MAX and hit ENTER.  Type in 12.5 (mm)
              and ENTER.  Hit F10 to perform the search.

              Hit 8 to select-by Ae; hit ENTER type 0.1 and ENTER; move
              the cursor to MAX and hit ENTER; type 0.3 and ENTER; then
              type F10.

      You have reduced a list of over 4000 cores to less than 200 torroids
      which meet your requirements. For further reductions you may wish to
      limit the selection to ferrites or moly-Permalloy cores.


      Example; you have wound a transformer on a core you found but do not
      know the part number, or vendor.  You measure the Al value as 24 nH
      per turn^2, and the outer diameter as 0.2 inches.  How can you find
      the core?

              Hit 4 for select by form-factor, T for torroid, F7 for
              only-torroids, and F10.

              Hit A to select-by Al; ENTER; type 18E-09 and ENTER; move
              the cursor to MAX and hit ENTER; type 33E-09 and ENTER;
              F10.

              Hit 5 for select by dimensions, then A.  Use the cursor
              keys to high-light MIN and hit ENTER.  Type in 3 (mm) and

              ENTER.  High-light MAX and hit ENTER.  Type in 6 (mm) and
              ENTER.  Hit F10 to perform the search.

      Over 4000 cores are reduced to under 10; by comparing the remaining
      dimensions the number can be reduced to one or two.  If you know what
      the material type is or can eliminate several vendors the number of
      possibilities can be reduced further.

      Note that selection by dimensions is done after selection by Al.
      This is because selection by Al is faster that selection by
      dimensions, and thus performing selection by dimensions last - with
      fewer cores to now search - takes less time.

      For this type of search you must enter search values.  Some practice
      is needed to make search values wide enough to bracket the nominal
      value and its' tolerance, yet tight enough to limit the number of
      cores selected.


      Example; you have designed a transformer which requires an Ae of .1
      square-cm.  You have several ideas of what cores to use, but as a
      blue-sky problem, what is the smallest possible core?

              Hit C for Miscellaneous Selections and 1 for Select-by-
              Unique sizes.

              Hit 8 to select-by Ae; hit ENTER type 0.09 and ENTER; move
              the cursor to MAX and hit ENTER; type 0.2 and ENTER; then
              type F10.

              Hit F8 for sort and A for dimension-A, then F10.

      The result is a list of several hundred cores with the proper area
      sorted by increasing size.  By entering search values for Al or lm
      the number of cores could be reduced.

      Sorting by dimension A is a good way to roughly sort cores of differ-
      ent form factors by size.  An alternate way is to sort by volume.


                           Searching for Second Sources

      From the previous examples it can be seen that CoreDBMS provides the
      searching capabilities needed to find a second - or alternate -
      source.  This section considers some of the problems in finding
      second sources and how the program can simplify the process.

      CoreDBMS is intended as a tool to help find second sources.  As with
      and tool, the way it is used affects how useful it is.


      The Match-a-Core option in the Selection menu will quickly find all
      cores of a single form-factor which are the same size as a target
      core you select.  This generally means that all of the cores have
      very similar lm and Ae values.

      The Match-a-Core option deliberately does not attempt a search by
      figure or magnetic parameters.  That is because only the designer can
      determine whether these parameters are of importance.

      As a rough example, if the final application of the core is in a
      pulse transformer or forward-mode DC-to-DC converter then the Al
      parameter is not critical - any core with Al exceeding some value is
      usable.

      However, if the application is for an inductor where inductance is
      critical then the Al value is important.

      The program does not match figures because different figures some-
      times display subtle differences which may not affect using either
      figure as a second source.  For example, torroid figures 1 and 25
      show different rounding on corners and EE figures 2, 50, and 51 show
      different mounting options.

      However, figures can also be extremely different within the same
      family of form-factors.  When searching for pots, EE, EI, CC/UU, or
      CI/UI cores it is a good idea to perform a search by figure number
      after the Match-a-Core search.

      If mounting features of the core are important then you may wish to
      perform a search by figure number.

      When matching dimensions, a dimension of zero always matches.  This
      insures that if a vendor does not dimension a feature the core will
      still match.  However, if you have a core with a center-hole and one
      without then they will match as well.



                         Chapter 7  - CoreDBMS in Detail

      This chapter need not be read to experiment with the program, but
      should be read after the user has some experience, as the contents
      can speed searching and help avoid errors.


                                   The Cores

      CoreDBMS allows for long part numbers, so when two parts with dif-
      ferent part numbers are required for a core set, both part numbers
      are listed separated by a '/'.

      But when displayed in BROWSE format, part numbers are truncated at 20
      characters.  DETAIL mode will display all of a long part number.

      When a vendor has several suffixes - perhaps to identify coatings -
      only one will be given in the database, often with a note in the note
      field mentioning the other suffixes.  It is important during searches
      to avoid suffixes when possible.  Including a suffix on a part-number
      can cause a search to fail.


      Vendor names and note-fields are subject to truncation in the Browse
      display also.  A list of vendors can be obtained by using the stat-
      istics option from the main menu or core select menu.  Full fields
      can be seen in detail-mode.


      Form factors and figures may be used in searches and sorts, but the
      objectives must be considered carefully.

      Some form-factors have more than one figure, which can be a source of
      confusion as you select a form-factor and find several cores with
      figures you may not recognize and may not want.

      Equally confusing can be the names used with form-factors.  Pot cores
      and Double-slab cores are interchangeable in many applications, but
      in this database as well as in many vendors' catalogs the two are
      kept separate.

      Similarly, ER cores are listed separately by some vendors, but in
      this database ER and EE cores are combined.

      And there are the cores which don't fall neatly in any single form-
      factor.  For example, the pot core with only one slab cut: or the
      elongated-torroid shape which is not quit a torroid.

      These shapes are either kept in the category of the shape they are
      derived from, or are placed in the 'Misc' category of form-factor.

      The best way to make careful use of form factors is to become fam-
      iliar with the different form-factors and figures - browsing through
      the outline drawings and the selection routine.

      Any number field - dimensions or magnetic data - can be missing if
      the vendor does not provide it.  Most display routines blank such
      fields rather than display a zero, but in the sorting routine a blank
      field sorts as a value of zero.

      This can give misleading results; if two cores from different vendors
      are identical but one vendor provides a value for a parameter while
      the other does not, a sort on that parameter will place one core at
      the beginning of the list - where you may not find it - and the other
      will take its' proper place in the sorted list.

      Since most selection parameter use zero for the minimum selection
      value, if you change the minimum selection value you will drop any
      core having zero for that parameter.

      These are not major problems.  The best defense is to be aware that
      it can happen, and to check the list of selected cores for blank
      fields which you may be working with.


      When entering search values for minimums and maximums, any format
      will suffice.  The precision used by the program follows the default
      minimum and maximum values, i.e. if no decimal place is shown and you
      enter data with a decimal place, data after the decimal is truncated.

      Data may in entered in scientific notation in the format;  1.3E-06 
      No spaces are allowed within the number.


      Window Area - Aw - and window area times effective area - Ae*Aw - are
      calculated numbers, i.e. they are not stored in the database.  If
      either the effective area or the dimensions required to calculate the
      window area are zero then Aw or Ae*Aw will be zero.


                                   The Figures

      Figures are sketches and are not drawn to scale.  A figure may be
      drawn with the width and length approximately equal, but a core using
      this figure could have the width twice the length, or vice-versa.
      When selecting cores check the dimensions.

      Due to variations in printers and terminals, circles - as in the
      torroid figures - may not be displayed as true.

      Figures are intended to aid in the selection process and new figures
      are drawn to display differences in core shapes.  Figures may be used
      as a selection criterion when you need a core which looks EXACTLY
      like a figure, but using figures as a selection criterion has risks -
      in many cases the differences between figures may be slight.  Note as
      example figures 2, 11, 50, and 51.

      Figure 2 is an EE-core with squared-corners.  Figure 11 is an EE-core
      with rounded corners, used if the vendor's figure indicates rounded
      corners but does not provide dimensions.  Figures 50 and 51 are
      squared-corner cores with mounting channels.  In most cases cores of
      figure 2, 11, 50, or 51 are interchangeable.

      Figures are not grouped by form-factor; the original order was set by
      the order cores were entered and new figures were required.  As ven-
      dors and cores are added and deleted figure numbers are not changed,
      to avoid confusion( such as a core being figure 12 in one revision of
      CoreDBMS and figure 14 in the next).

      Finally, figures may not be drawn to drafting standards.  As mention-
      ed, figures are intended to be a an aid to the selection process: if
      hidden-lines make it difficult to understand the figure - especially
      in low-resolution CGA-mode - then hidden lines are not drawn.  The
      result is a core drawing which primarily shows the outline and little
      internal detail.  Some cores with arcs are rotated between views
      because CGA-mode does not have sufficient resolution vertically to
      show a small arc.


                                  The Materials

      Vendor names, material names, and the note-fields are subject to
      truncation in Browse displays.  Full fields can be seen in detail-
      mode.

      As with cores, any field may be missing if the vendor does not
      provide it.  Where most display routines will blank such fields
      rather than display a zero, for the sorting routine, a blank field
      sorts as a value of zero.

      Most parameter use zero for the minimum selection value.  If you
      change the minimum selection value you will drop any material with
      zero for that parameter.

      These are seldom major problems.  Be aware that they can happen and
      check the list of selected materials for blank fields.


                               The Material Graphs

      Graphical data given in the Materials section has been obtained from
      similar graphs in the vendors databooks.  In the process of reading
      the data, scaling, encoding it for the program, and drawing it to the
      screen an un-avoidable loss of resolution occurs.

      The graphs are a valuable source of data, and useful for making com-
      parisons.  However, do not attempt to interpolate data too exactly
      from the graphs; for that purpose use the original graphs in the
      vendors' databook.

      Graphical data is very dependent on the measuring conditions.  Again,
      check the vendors' databook for this information.



                                   Sorting Data

      Sorts on materials - in either the material or cores menus - are not
      alphabetical.  The sort routine is actually sorting materials by the
      order they appear in the database, first by vendor, then by material.

      This order can be seen in the Select-By-Material menu.


                             Making Searches Faster

      With a large number of cores, a long time can be used in searching.
      Here are some tricks to reduce search time.


      The biggest improvements in search time can be made by varying the
      order in which you make searches; performing searches that your
      computer can do quickest first.  After the first search additional
      searches are faster because fewer records are read.

      Vendor, Form-factor, and Material Type are indexed fields and are
      searched very rapidly.  Where possible search on one of these three
      fields first.

      Searches by figure, material, and magnetic data are the next fastest
      searches, requiring access to only one of the database files.

      Searches by dimension require reading two of the three database files
      and are much slower than the above searches.  Searches by window area
      and Ae*Aw product require performing calculations on dimensions which
      further slows searching.

      Finally, searches by part number and notes are the slowest of search-
      es, requiring reading two of three database files then scanning long
      note fields.  It is often faster to make two searches - search by
      vendor and then search for part number - than it is to simply search
      the entire database for a part number.

      Simple searches are faster than complex searches.  Searching for one
      vendor is quicker than searching for two vendors, etc.


      Coredbms is disk-based - the entire database is maintained on disk
      and the disk is read for every access to the data.  The alternative
      to this system, of reading data into memory once and then reading
      memory when data is required uses a lot of memory with a database of
      this size.  A memory-based database is faster, but a disk-based
      database will run on nearly any machine, regardless of the amount of
      memory installed.

      You can speed searches with a RAM-disk, which uses system memory to
      pretend to be a disk drive.  Load the *.db? files and CoreDBMS.hlp to
      the RAM-disk and execute CoreDBMS from there; searches take place at
      the speed of the memory rather than the much slower speed of a disk.

      The problem with a RAM-disk is if - for example - the database re-
      quires a 360 k RAM-disk and the program requires 300 k of memory then
      you need more than the 640k of memory found on many PC's.

      A disk caching program can speed searches.  A cache is a portion of
      memory which retains information read from a disk, assuming that you
      may need it again.  A cache program notes when the database requests
      data which is already in memory and supplys it without accessing the
      disk drive.

      An important step for fast searches is to avoid fragmentation of the
      data files.  DOS starts writing files at the first free disk block;
      if the entire file will not fit in the space, DOS splits the file and
      continues writing at the next free disk block.  If your disk has been
      very active, then you've deleted files and enlarged files, creating
      empty disk blocks.  When you copy the database to your disk, DOS
      'fills the holes', and when you try to read the data your disk drive
      is forced to jump around, slowing your search.

      To avoid this, consider using a disk de-fragmenter to rewrite the
      files on your hard disk so that they are all in one piece.  Such
      programs are available from several vendors.


      With all steps to improve the speed of searching, the time required
      for a search is still proportional to the number of records searched.
      It takes a considerable period of time to scan a large database.

      To speed searches make smart searches.  Eliminate the maximum number
      of cores each time so that your next search has far fewer cores to
      scan.


                                    Caveats

      There are many things that the user or person specifying cores must
      be aware of.  We present some of them here.

      First, vendors specify that their data is subject to change without
      notice.  We - of course - pass this warning on.  When a vendor makes
      a change we update our data as quickly as possible.

      Second, typographical errors abound.  We find several in each re-
      vision of a catalog.  When we identify a typo, we try to confirm the
      problem with the vendor and correct it in this database.

      Third, all core data has tolerances.  The designer must note and
      compensate for such tolerances.

      Fourth, the existence of a core in this database - or in the vendor's
      catalog - does not guarantee that you can quickly obtain the core.
      Vendors usually keep a reasonable stock on hand, but may run out.
      Check on availability.  Also check for possible distributors who
      might have the core in stock.

      Fifth, there are aspects of magnetics design which are not an exact
      science.  IEC Publication 401 states:

          "It should be recognized that there is no direct relation
           between material characteristics as measured on test pieces
           and corresponding parameters measured on other cores, made
           of the same material, because of difference in geometry,
           etc.  Also the extrapolation of material characteristics to
           other flux densities and other frequencies will not permit
           a valid comparison of cores of different materials under
           these new conditions of operation."

      In brief, always TRY a core in your application before specifying it.

      Other points to consider:

      Does a part number indicate a set of two cores or a single core?
      Generally, we note if the part number is a set.  If a vendor lists
      cores both as sets and singles, then both are noted.  When two dif-
      ferent parts are required to achieve a form, both part numbers are
      given separated by a slash (/).


      When a vendor lists gapped cores, is the gap in one core of the set
      or in both cores?  If the gap is in one core half, you probably must
      buy the cores by two different part numbers - if the gap is in both
      cores then one part number suffices.

      Note that cores need not have the same gap.  Two cores with different
      gaps can be used for inductances between the two listed values.


      What are the conditions for which the magnetic characteristics of the
      core were measured?  This can make a difference in Al values, when
      vendors give Al at different magnetic field strengths. Field strength
      will often vary with material. Check the vendors databooks for
      measurement conditions.


      With a vendor's databook there are areas of confusion, due to missing
      information(which may simply be elsewhere in the databook), or due to
      assumptions that you - or the vendor - make.

      With CoreDBMS these points of confusion may not go away, but by being
      familiar with different vendors formats, converting them into our own
      format, and explaining our assumptions, we try to clear up the areas
      of confusion.



                                    Glossary

      Al                Inductance Factor, or the inductance, L, per square
                        turn.  Al = L / N^2.  In this database Al is in
                        Henries per square-turn.

      Ampere-Turn       The product of the current flowing in a winding in
                        amperes, times the number of turns.

      Amplitude         The permeability of a core when excited by an AC
      Permeability      flux with no DC flux present, given in graphical
                        form as graph 4 - permeability vs ac flux.

      Coercive Force    The magnetizing field strength required to reduce
                        the magnetic field in a material to zero.

      CC Core           In this database CC and UU are used interchangeably
                        for a core-half shaped like the letter 'C' or 'U'.
                        An alternate use for the term "CC" is for a deep
                        pot form with no wire break-outs, which this
                        database refers to as a cup core( CC for Cup, Cap?)

      Core-Loss         The power absorbed by a core and dissipated as heat
                        when the core is subjected to a time-varying mag-
                        netic field

      Cube-Core         alternate name for Q-core.

      Cup Core          A pot core shape typically very deep and with no
                        slots, designed to be used alone or with a simple
                        slab as a cap.  Lead breakout is through slots or
                        holes in the cap or holes in the pot bottom.

      Curie             The temperature at which a magnetic core changes
      Temperature       from the ferro-magnetic to para-magnetic state,
                        i.e. shows a sudden and rapid drop in permeability.
                        The change is reversible.

      Cut-Core          alternate name for RS, DS, or touch-tone pot core.

      Disaccommodation  The time rate of change of initial permeability of
                        a core which has just been demagnetised.

      Disaccommodation   The disaccommodation of a material per unit of
      Factor            permeability.

      Double-slab Core  A pot core with a section cut off on either side of
      DS Core           the center post: provides a large opening for wire
                        breakout and allows use of larger wire sizes and PC
                        Bobbins.

      EC Cores          EC cores provide the wide breakout of EE cores with
                        a round center leg for a short winding-path length.

      EE Cores          EE cores are less expensive than pot cores(being a
                        less complex form), allow simple bobbin winding and
                        easy assembly, and provide a large area for wire
                        breakout; allowing the use of larger wire sizes.
                        But EE cores lack the shielding of pot cores.

      Effective Area    or, Effective Magnetic Cross-Sectional Area. The
                        cross-sectional area of an ideal torroid that
                        yields the equivalent magnetic properties of a
                        core. There is no guaranteed correlation between
                        effective area and any mechanical dimension of a
                        core.

      Effective         The magnetic path length of an ideal torroid
      Magnetic          that yields the equivalent magnetic properties of a
      Path Length       core. There is no guaranteed correlation between
                        path length and any mechanical dimension of a core.

      Effective         The volume of an ideal torroid that yields the
      Magnetic          equivalent magnetic properties of a core. There is
      Volume            no guaranteed correlation between effective
                        magnetic volume and geometrical volume.

      Effective         For a component made up of different materials,
      Permeability      e.g. a magnetic material with an airgap, the perm-
                        ability of a hypothetical homogeneous material with
                        the same shape, dimensions, and total reluctance.

      Effective Retentivity   See Retentivity.

      EP Cores          EP cores have a round center-post and a cubical
                        shape which encloses the coil except for the print-
                        ed-circuit terminals. EP cores provide a large
                        volume-to-mounting-space ratio, minimize air gaps
                        at the mounting surface, and provide excellent
                        shielding. Mating surfaces are polished and should
                        be cleaned before assembly.

      ETD Cores         ETD cores are optimized for off-line, forward-mode
                        switching converters; are designed for low-loss in
                        the 20 to 200kHz range, and features a near-uniform
                        cross-sectional area with a round center-post.

      Ferrite           A class of ceramic materials with a spinel crystal-
                        line structure; a combination of iron oxide with
                        one or more divalent metal oxides, such as man-
                        ganese (Mn), nickel(Ni), magnesium(Mg), zinc(Zn),
                        and Copper (Cu), of which the most popular are MnZn
                        and NiZn.

                        Ferrite features high magnetic permeability and
                        high resistivity.  The high resistivity limits
                        eddy-current losses, permitting the use of ferrite
                        at frequencies into the mega-Hertz range.

                        Ferrite cores are produced by mixing ingredients,
                        forming into pellets, and pre-firing at a temp-
                        erature of 850 to 1100 deg-C; milling the pellets
                        to a uniform particle size, and pressing to shape
                        at high-pressure. Finally the core is sintered -
                        fired - in a 1000 to 1500 deg-C kiln.

                        Sintering results in a reduction in volume, to
                        almost 63% of original. Due to this, tolerances of
                        parts are typically 2 percent or more, unless
                        machining is performed.

      Incremental       The permeability of a core at a given DC magnetic
      Permeability      field, in Oersteds. Provided in graphical form as
                        graph 5 - permeability vs dc bias.

      Inductance Factor   the inductance, L, per unit turn. Al = L / N^2

      Initial           the limiting value of permeability at the origin
      Permeability      of the magnetization curve, i.e. at very low field
                        strengths

      Iron Powder       A material of finely divided iron powder, insulat-
                        ed, mixed with a binder, formed in high-pressure
                        presses, and baked to set the binder and form the
                        finished core.  The resulting core provides the
                        magnetic properties of iron with much lower losses
                        than iron laminations - as the insulated particles
                        limit eddy losses - and at lower cost.  Usually
                        available only as torroids and EE cores.

      Loss Factor       the quotient of the tangent of the loss angle and
      theta             the permeability.

      Magnetic Path Length    see Effective Magnetic Path Length

      Magnetostriction  Relative change in length of a magnetic core under
                        the influence of a magnetic field.  Magneto-
                        strictive effects can produce audible whistling in
                        ferrite power transformers.

      Molypermalloy     A magnetic material similar to powdered iron in
                        composition and manufacturing, but with addition of
                        nickel and molybdenum.  More expensive than iron
                        powder, with greater flux density and better
                        stability.

      Parylene C        An insulating material for cores, generally vapor-
                        deposited as a film approximately .0005 inches
                        thick. 
                                        Properties: 
                        Dielectric Strength: 4700 volts per mil 
                        Surface Resistivity: 1e14 Ohms
                        Dielectric Constant: 3 
                        Dissipation Factor:  0.02
                        Coefficient of Friction: 0.29 
                        Operating Temperature:  -55 to 130 degrees Celcius

                        Trademark of Union Carbide.

      Permeability      By definition, B/H, where B is the flux density in
                        Gauss and H is the magnetizing force in oersteds.

      Post              Center leg of pot core, RS, DS, etc. also called
                        Slug by some vendors.

      Pot Core          Pot cores surround the wound bobbin when assembled,
                        aiding in shielding. The pot core is not readily
                        available in large sizes, and is often more
                        expensive than other shapes of comparable size.

      PQ Core           PQ cores are designed for switching power supplies
                        from 20 to 100kHz, and provide an optimized ratio
                        of volume to winding area and to surface area;
                        providing maximum power output with minimum weight
                        and volume. Cross-sectional area is very uniform,
                        eliminating hot spots.

      Residual Flux     The amount of magnetic flux density retained by a
      Density,          core after a magnetic field of effective saturation
      Retentivity       flux density is removed.

      Ring Core         alternate name for torroid, primarily European. 

      RM Core           RM or Square cores offer the shielding advantage
                        and round center post of pot cores but; provide a
                        more compact package, save on mounting area, and
                        offer larger windows for bobbins.

      Rod Core          Typically a single-piece cylindrical core with
                        length much greater than the diameter.

      RS Core           'Round-slab' cores are modified pot cores with
                        sides removed from one core-half. RS core offer the
                        shielding, high Q, and compact design of pot cores
                        plus the easy wire breakout and use of bobbins of
                        EE cores. Touch-Tone cores are in this class.

      Slug              1) Center leg of pot core, RS, DS, etc. 
                        2) A short, cylindrical core

      Square Core       alternate name for RM-core; due because the core
                        plus bobbin forms a square footprint.

      Teflon S          An insulating material for cores, generally sprayed

                                        Properties: 
                        Dielectric Strength: 2000 volts per mil 
                        Surface Resistivity: 6e12 Ohms 
                        Dielectric Constant: 3.35 
                        Coefficient of Friction: 0.095 
                        Operating Temperature:  -45 to 145 degrees Celcius

                        Trademark of DuPont.

      Torroids          Torroids are economical to produce, thus low in
                        cost. Bobbins are not required and machines are
                        available for winding. Torroids may be gapped,
                        although this can significantly increase cost.
                        Shielding is good.  To allow automatic winding, the
                        amount of window area used for the windings must be
                        limited, usually to around 70%. This can require
                        hand labor and increase costs for complicated
                        windings.

      Touch-Tone Core   a double-slab core half and a pot core half with-
                        out openings, as in figure 28. Called an RS core in
                        this database, and identified as 'Touch-Tone' in
                        the note field.  Named for its' use in touch-tone
                        phone dial-ing systems.

      Turns Factor, c   defined as number of turns divided by the square
                        root of the inductance, c=N/Sqrt(L). c is sometimes
                        given as K or alpha. See also Inductance factor.

      Type 1 Pot Core   a pot core with no air gap. 
      Type 2 Pot Core   a pot core with a uniform air gap in the center
                        leg.
      Type 3 Pot Core   a pot core with a stepped-gap in the center leg. By
                        rotating the two core halves a range of inductance
                        values can be acheived.
      Type 5 Pot Core   a pot core allowing adjustment of inductance via a
                        tuner assembly in the center hole.  May be provided
                        with or without an air gap. 



                  Appendix 1. - Conversions & Miscellaneous Data

                                   Conversions

                 1 Tesla = 1Vs/m^2 = 10^-4 Vs/cm^2 = 10^4 Gauss 
                 1 mT = 10 Gauss 
                 1 A/m = 10^-2 A/cm = 1.257E-2 Oersteds 
                 1 Oersted = 79.6 A/m = .796 A/cm


                             Ferrite Characteristics

             Tensile strength                  20 N/mm^2 
             Resistance to compression        100 
             Vickers Hardness                8000 N/mm^2 
             Modulus of elasticity         150000 
             Heat Conductivity               4 x10^-3 J/mm/s/K 
             Linear Expansion coefficient    7x10^-6 / K 
             Specific Heat                 0.7 J / gram/ deg-Kelvin 
             Radiation Resistance
               Gamma Quanta        10E9  rad
               Quick Neutrons       2E20 neutrons/m^2
               Thermal Neutrons     2E22 neutrons/m^2


                            Applicable Core Standards

      Din 41280(1983) Soft magnetic Cores; Material properties
      Din 41290(1972) Calculation of Effective Parameters

      IEC 205(1966)   Calculation of Effective Parameters of Magnetic Piece
                      Parts

      IEC 367-1(1962) Cores for inductors and transformers for
                      Communications

      JIS C2560       Japan Industrial Standards,  General Rules for Cores
                      made of ferro-magnetic oxides




                 Appendix 2. - Error Messages and Problem Solving

            There are only a few errors which CoreDBMS is subject to:

      Error 6  at pgm-ctr: nnnnn      
              This is an 'Insufficient Memory' error, and occurs when there
              is not enough memory to load the error-checking code.

              CoreDBMS requires 320k of free memory to load and run. This
              error may be caused by running the program from a shell or from
              within another program - terminate your first program and try
              again.  Possibly you are using memory running 'Terminate-and-
              stay-resident' programs. Eliminating some TSRs and re-run.

      Error 5  at pgm-ctr: nnnnn 
              Error 5 is a 'catch-all' error message, but one common cause is
              attempting to run in graphics-mode on a non-graphics terminal.
              Try running with the /NGT switch.

      Any error other than 5 or 6 typically involves a corrupted database
      that the error-checking code could not detect. Try reloading the
      program and all files from the distribution diskette.

      "File Core.db1 Not Found"
      "File Core.db2 Not Found"
      "File Core.db3 Not Found" 
      "File Index.db Not Found" 
              These errors usually occur when you are not in the same direc-
              tory as CoreDBMS.exe. The DOS path command may allow you to
              find and run the exe file but does not find the support files.
              Before running the program, use the dos cd command to move to
              the directory containing the DBMS files.

      "File Figures.db1 Not Found"
      "File Mats.db1 Not Found"
      "Help File Not Available" 
              These errors result in a warning message when the program
              attempts to access the files. The cause is usually the same as
              in the previous error. If using a RAM-disk the above six files
              should be on the RAM-disk when running the program.

      "File Core.db1 Found Damaged"
      "File Core.db2 Found Damaged" 
      "Data file does not match expected format" 
              These are fatal errors and indicate that the database files
              have been corrupted OR are of a different revision than the
              program file. Try copying the data files and CoreDBMS.exe from
              the distribution diskette to your working diskette or direct-
              ory. Make sure to use your latest distribution diskette if you
              have received an update.

      "No Printer or Printer not Ready" 
              This is a non-fatal error. Make sure your printer is on-line
              with paper loaded and retry. CoreDBMS assumes your printer is
              LPT1; if your printer uses another printer port use the /LPTn
              switch to print to another port.  You may have to file the
              output and then use the DOS print command to print the file.


                                 Problem Solving

      As with error messages, there are only a few problems that you might
      encounter with CoresDBMS; most quickly solved.

      You can't find a core you know exists. 
              The database only contains standard, catalog cores.  If the
              core you're searching for is a custom core it will not be in
              the database.

              If searching by part number use caution to search for the
              base part number; prefixes and suffixes which identify coat-
              ing options may not be present in the database.

      Figures do not agree with description. 
              Figure 1 - the torroid - may draw as an EE core. This is
              caused by a mismatch in revision of figure database and
              program or by a corrupted file.  Reload the Figure.db1 file
              and the program file from the latest database.

      The screens flash past the screen you want.
              If you type slower than the program can read data the program
              waits for you; if you type faster, extra keystrokes are kept
              by DOS in a buffer until the program 'catches-up.'

              If you type a key while CoreDBMS is searching or sorting, the
              key is stored in the buffer and CoreDBMS acts on it as soon
              as the search or sort ends.  This can seem as if the program
              is skipping steps or screens.

              Also, most keyboard keys will repeat if held down.  The
              period that the key must be held down varies with different
              machines.  Perhaps when you strike a key you are holding it
              long enough to generate two characters, instead of one. As
              CoreDBMS executes the second character it again looks like
              the program is skipping screens.


      The Printer does not respond after or while running the program. 
              If you terminate a printing session the printer may not be
              properly reset.  This usually results in characters printing
              in compressed mode.  If you take the printer off-line while
              printing graphics or if you print graphics with the mode set
              incorrectly (i.e. EPSON vs IBM PROPRINTER) the printer may
              remain in graphics mode.  Manually set the printer paper to
              the top-of-form and reset the printer, either by a reset
              switch or by turning the printer off.


      If your problem is not solved with the suggestions in this chapter,
      please get in touch with us.  We want our program to work for you and
      will make every effort to solve your problem.




                               Appendix 3. - KeyMap

      Main Menu 
         F1 - Help 
         F2 - Materials menu 
         F3 - Core-selection menu 
         F4 - Display Help page on finding alternate sources 
         F5 - display core outline drawings 
         F6 - display vendor information 
         F9 - show system statistics 
         F10- To Quit this program.

      Core Selection Menu 
         F1 - Help 
         F2 - Tag; make all selected cores permanent 
         F3 - Display in BROWSE mode 
         F4 - Display in DETAIL Mode 
         F6 - Display in COMPARE mode 
         F7 - File or print one core or all selected cores 
         F8 - Sort Cores 
         F9 - Reset Selection list  
         shift-F9 - Reset selection list including Tagged cores 
         F10-Exit 
         P - File or print one core or all selected cores 
         S - shows statistics for selected cores

      Core Selection Menu - Browse Display Mode 
         F1 - Help  
         F2 - Tag all records (if cursor on, tag only highlighted record) 
         F3 - Toggle cursor on/off 
         F4 - Switch to DETAIL Display mode 
         F5 - Delete Record (if cursor on, delete highlighted record) 
         F6 - Switch to COMPARE Display mode 
         F7 - File or Print one core or all selected cores 
         F8 - Sort 
         F10- Exit 
         sh-F4 show first selected record in DETAIL 

         1,2,3,4 - moves sideways to display additional screens 
         J - 'jump' to prompted record 
         P - File or Print one core or all selected cores 
         R - Detail 
         X - with cursor active will display the material used in the high-
             lighted core. 
         TAB, sh-TAB  cycles through data screens 
         HOME  move detail screen to display first record in database  
         END move detail screen to include last record in database 
         UP Arrow  scroll screen up(decreases record number) one record. 
         DOWN Arrow  scroll screen down one record. 


      Core Selection Menu - Detail Display Mode 
         F1 - Help        
         F2 - Make displayed core permanent. 
         F3 - Jump to BROWSE mode 
         F4 - Display new record  
         F5 - Delete displayed record 
         F6 - Jump to COMPARE mode 
         F7 - File or Print the Displayed core 
         F10- Exit P  - File or Print the displayed core 
         R,J - Display new record X - Display the material used in this core 
         ENTER, Page-Down, Down-arrow - display next record in list Page-Up,
         Up-arrow - display previous record in list

      Core Selection Menu - COMPARE Display Mode 
         F1 - Help        
         F2 - Make all selected records permanent 
         F3 - Switch to DETAIL mode 
         F4 - Switch to BROWSE Mode 
         F5 - Delete a record   
         F7 - File or Print one core or all cores 
         F10- Exit            
         J - 'Jump' display to begin at new record. 
         P - File or Print one core or all cores 
         R  - Browse Mode 
         D  - Drop this record

      Materials Selection Menu F1 - Help 
         F3 - Display in BROWSE mode 
         F4 - Display in DETAIL Mode 
         F7 - File or print all selected materials 
         F8 - Sort Materials 
         F9 - Reset Selection list  
         F10-Exit 

      Materials Selection Menu - Browse Display Mode 
         F1 - Help 
         F4 - Display in DETAIL Mode 
         F5 - Delete - Drop - the high-lighted material (Cursor mode only) 
         F7 - File or print all selected materials 
         F8 - Sort Materials 
         F10-Exit 

         TAB, shift TAB - jump right/left through screens 
         1,2,3 - jump sideways to indicated screen 
         D - if cursor is active, will delete the high-lighted material 
         X - if cursor is active, will select cores with the high-lighted
             material

      Materials Selection Menu - Detail Display Mode 
         F1 - Help 
         F3 - Display in Browse Mode 
         F5 - Delete - Drop - this material 
         F7 - File or print displayed material 
         F8 - Sort Materials 
         F10-Exit 
         D - delete the displayed material 
         X - will select cores with the displayed material.





                              Appendix 4. - Figures

                                 Figures by Number

      1 Torroid, squared-wall 
      2 EE, squared-wall 
      3 EI, squared-wall 
      4 CI,UI, squared-wall 
      5 CC,UU, squared-wall 
      6 DS - Double-Slab - with center-hole 
      7 Pot, 2-slot, with center hole 
      8 EC 
      9 ETD 
     10 ETD, alternate
     11 EE, with rounded outer corners 
     12 EI, with rounded outer corners 
     13 EE, with octogon center leg    
     14 CC,UU, half-round wall    
     15 CI,UI, half-round wall    
     16 DS, no center hole        
     17 Pot, 2-slot no center hole       
     18 Pot, 4-slot, with center hole         
     19 CC,UU, half-round; alternate    
     20 CI,UI, half-round; alternate    
     21 CC,UU, with one rectangular, one octal leg   
     22 CC,UU, round wall         
     23 CC,UU, squared corners, notched   
     24 X                        
     25 Torroid, rounded-wall    
     26 Pot 2-slot no hole;   
     27 Pot 2-slot, with hole; alt    
     28 RS core                  
     29 RS core; touch-tone core 
     30 RM core                  
     31 1-opening Q core         
     32 2-opening Q core 
     33 PQ core                         
     34 EP core                         
     35 PM core                         
     36 CC, UU, one rectangular, one round leg 
     37 1-opening Pot core              
     38 1-opening Pot core, alt         
     39 CC,UU, with octagonal legs           
     40 Pot 2 slots in one half, no slots in other 
     41 Pot 4 slot & none, alt          
     42 Pot 4 slot & none, step-gap     
     43 Pot 2 slot & none, step-gap     
     44 FQ Core                         
     45 EPC Core                        
     46 Oval Bead                       
     47 Rectangular Bead 
     48 'Single-Slab' Core 
     49 CC, UU with circular legs, alt
     50 EE core with semi-circular notch in base 
     51 EE core with rectangular notch in base
     52 CC, UU core with rounded outer corners 
     53 CC, UU core; one round, one rectangular leg, mounting slot 3 sides 
     54 CC, UU core; one round, one rectangular leg, alternate
     55 CC, UU core; one round, one rectangular leg, alternate
     56 CC, UU core; one round with slab cut, one rectangular, mounting
            channel in two sides 
     57 CC, UU core; one round, one rectangular leg, mounting slot in two
            sides 
     58 ETD-style core with rounded outer-legs 
     59 CC, UU core, rounded; cut-core


                        Breakdown of Figures by Form-Factor

    Beads:    46, 47 
    Bobbins: 
    CC-Cores: 5, 14, 19, 21, 22, 23, 36, 39, 49, 52, 53, 54, 55, 56, 57, 59 
    CI-Cores: 4, 15, 20 
    Cup-Cores:
    Double-Slab Cores: 6, 16 
    EC-Core:  8 
    EE-Cores: 2, 11, 13, 50, 51 
    EI-Cores: 3, 12 
    EPC-Core: 45
    ETD-Core: 9, 10, (58)
    FQ-Core:  44 
    PM-Core:  35 
    Pot Cores: 7, 17, 18, 26, 27, 28, 29, 37, 38, 40, 41, 42, 43, (48) 
    PQ-Core:  33 
    Q-Cores:  31, 32 
    RM-Core:  30 
    Torroids: 1, 25 
    X-Core:   24

    Figures in () represent cores which are similar to the form-factor 
    listed but which may not qualify as a member of that form-factor.