SYSHELP DOCUMENT


     Have you ever wondered how to make a ramdisk?  Have you ever 
wondered what the CONFIG.SYS file was for?  Well, in this brief 
document, I plan to tell you.  First, contained within this ARC 
file should be the following:

                           RAMDISK.SYS
                           CONFIG.BAK
                           SYSHELP.DOC

     RAMDISK.SYS is the actual ramdisk system file.  The reason 
that I included this is because a lot of people with PC-DOS don't 
have this file.  When I installed PC-DOS on my hard disk, it 
wasn't on there, so I am assuming that PC-DOS doesn't include it.  

     CONFIG.BAK is a renamed config.sys file.  This file is to be 
used as a sample of what a config.sys file could look like.

     SYSHELP.DOC is the file you are currently reading.  


     First, a RAMDISK is a virtual disk drive that uses RAM as 
opposed to media (floppy disk, hard disk, cassette tape, ect.).  
Anything copied or put into a RAMDISK will be erased when the 
computer is turned off or re-booted.  The RAMDISK is useful for 
copying things from drive A: to drive A:, uploading/downloading 
programs at a higher speed, arcing/unarcing files, highspeed 
access time usefull for oft used programs, and other things you 
want to do quickly.  Your RAMDISK may be of any size, in K 
increments, but it cannot exceed the total K memory of your 
computer.  IE- if your computer has 640k, then the total K memory 
for your RAMDISK would be 576k (it keeps 64k for your computer to 
run on).  

     To create a RAMDISK, copy the RAMDISK.SYS file included in 
this arc file to your root directory.  Then, using a text editor 
(ASCII) create the file CONFIG.SYS in NON-DOCUMENT mode.  Using 
the text editor, type in the following line (if the file 
CONFIG.SYS already exists, then edit it and add this line 
somewhere within it.  See the CONFIG.BAK file for an example.):

                    DEVICE = RAMDISK.SYS nnn

     The nnn stands for a variable K length.  I would suggest 
100, but you can choose whatever size you desire.  When finished 
editing, save the file, and copy it to your root directory.  Then 
re-boot your system and the RAMDISK should be installed.  Usually 
the RAMDISK is drive D: and can be accessed by typing D: [RETURN].
           




                 Created by:  Asbrand of Norway
                        For:  Pirate's Cove, Inc.