User Documentation                 EZDIAG.EXE                        Page no.  1


                             USER DOCUMENTATION
    
                      WESTERN DIGITAL USER DIAGNOSTICS
    
       This document is intended to accompany the utility EASYDIAG.EXE
       placed on this bulletin board for your convenience.
    
       The utility is a safe, non-destructive way for your customer
       (or your self) to verify the configuration of your AT
       compatible computer, and to specifically test the hard drive/
       controller subsystem.
    
       Upon loading the program, the low-order ram pointer bytes are
       presented to the screen. The machine's power-on self tests
       test installed peripherals, and if valid ones exsist, the
       tables are updated.
    
       NOTE : THIS UTILITY DOES NOT PERFORM THE SETUP OR FORMAT
              FUNCTIONS. THESE FUNCTIONS MUST BE PERFORMED BY
              THE MACHINE'S MANUFACTURER-SUPPLIED SETUP AND
              FORMAT UTILITIES. IN THE EVENT A FORMATTER IS
              REQUIRED, WE SUGGEST THE OBTAINING OF THE WD
              UTILITY WDFMT.
    
       A sample of the start-up screen follows:



































User Documentation                 EZDIAG.EXE                        Page no.  2


    System contains the following :
    
     640K bytes of RAM
     2 Floppy disk drive(s)
     1 Parallel printer port(s)
     2 Asynchronous serial port(s)
     1 Hard disk drive(s) of the following configuration(s) ...
    
    Drive    Cylinders    Heads    Precomp cyl    Landing zone    Sectors/track
    
     0          820        10         65535           820              17
    
    Total formatted capacity of drive  0  is  71,372,800 bytes
    
    If the above information is not correct, run your system's setup utility
    
    The following diagnostic will use the configuration information above 
    
    Do you want to do a hard drive / controller diagnostic ( y / n) ??
    
       Note that the total count for all devices, as well as the
       physical capacity of the hard drive is indicated. The useable
       capacity is somewhat less, due to the partitioning method
       that DOS uses.
    
       You can proceed to the controller/drive diagnostic by typing
       'y' now. No return is necessary. The following menu appears:

































User Documentation                 EZDIAG.EXE                        Page no.  3


                  Select the diagnostic mode desired


                  (A)utomatic Quick Test ..........


                  (U)ser Selected Advanced Test ...


                  (E)xit to DOS / END TEST ........


                  ...  ENTER YOUR OPTION  ...  ==>




       Explanation of options on following page :










































User Documentation                 EZDIAG.EXE                        Page no.  4


                (A)utomatic Quick Test ... Operation

        A really fast and thorough test of the controller/drive subsystem.
        The following repetitive commands are issued :

                1) Rezero (recalibrate) command is issued to the
                   controller. The purpose of this command is to
                   simply move the hard drives' data heads over
                   the very first cylinder. The drive must then
                   respond with  DRIVE READY, SEEK COMPLETE, and
                   TRACK ZERO signals all present. The following
                   errors can occur :

                        REZERO (RECALIBRATE) COMMAND ERROR LIST

                   NO SEEK COMPLETE FROM DRIVE ...... --- OR ---
                   DRIVE NOT READY ERROR  ........... The drive never
                   reported that it was ready, or that the requested
                   seek (to track zero) was complete. This is usually
                   a drive select jumper or termination option (see the
                   drive's installation manual for more details) if the
                   drive activity lamp never lit when the controller was
                   trying to access the drive. Can also be a wrong, mis-
                   installed, or a defective cable. If the drive never
                   came to full speed (due to mechanical or power supply
                   limitations) this is also the error you will see.

                   TRACK ZERO ERROR  ................ The drive reported
                   that it was READY, and failed for some reason to reach
                   the first cylinder. This is usually either a termination
                   option problem, or a defective hard drive.

                   CONTROLLER STAYED BUSY  .......... This error can be
                   caused by failure of the controller to receive INDEX
                   (revolution) pulses from the hard drive. This input
                   is necessary for the timeout mechanism to function
                   properly on the controller. Try a known, good drive
                   and cable set. If the error persists, the controller
                   is probably bad.





















User Documentation                 EZDIAG.EXE                        Page no.  5


                2) 256 RANDOM SEEKS are issued all over the drive.
                   The drive does not have to be formatted to pass
                   this test. This is a thorough test of the
                   mechanics of the hard drive. A failure here will
                   probably be reported as a NO SEEK COMPLETE or
                   a NO DRIVE READY error. If the power supply in
                   the system under test is not capable of supplying
                   sufficient current to operate the drive, it will
                   usually show up as a drive error. If the wrong
                   number of cylinders or are selected in the
                   SETUP program (supplied with the machine), an
                   error listed above or a WRITE FAULT error will
                   be displayed. The errors possible follow :

                     a) NO SEEK COMPLETE  .......... Covered above

                     b) DRIVE NOT READY  ........... Covered above

                     c) WRITE FAULT ................ Beyond maximum
                     cylinder number seek was attempted. Check your
                     drives' parameters and your machine's SETUP.
                     Could also be a defective drive.






































User Documentation                 EZDIAG.EXE                        Page no.  6


                3) Now to the meat of it. 256 RANDOM TWO SECTOR
                   READ commands are issued to the drive. The
                   randomness of the location selected combined
                   with the deliberate selection of 2 sectors
                   (blocks) of data requested was carefully chosen
                   to bring out the elusive "random" failures.
                   The controller is told to NOT RETRY any operation
                   that resulted in an error. The possible errors
                   that could be reported are :

                       RANDOM READ POSSIBLE ERROR DESCRIPTION

                    a) DRIVE NOT READY ............. Covered above

                    b) WRITE FAULT ................. Covered above

                    c) DATA REQUEST FAILURE ........ A severe and
                       total controller failure. The card either
                       never transferred data, or won't quit
                       transferring data.

                    d) BAD BLOCK ON DRIVE .......... This area was
                       previously marked on drive. This location
                       should appear on the drive's error log. This
                       error is displayed solely for confirmation.
                       No automatic or combination tests are aborted
                       if this error is encountered.

                    e) ID FIELD (address) NOT FOUND . The controller
                       was unable to find any understandable data
                       on the hard drive. Check to ensure the drive
                       has been FORMATTED, the SETUP is correct, and
                       the ERROR MAP on the drive does not have this
                       location listed as a BAD TRACK.

                    f) UNCORRECTABLE or CORRECTABLE DATA ERROR
                       Indicates this location should be marked as
                       a BAD TRACK with a LOW-LEVEL FORMAT utility.
                       Such a utility can be found on this BBS. It is
                       called WDFMT.EXE and will format, verify, and
                       perform an intensive surface scan of the drive.
                       Unless you format out marginal areas, the data
                       you store on the drive could eventually be
                       corrupted THE NEXT TIME IT IS READ. Play it
                       safe. THERE ARE VERY FEW DEFECT FREE DRIVES !!!















User Documentation                 EZDIAG.EXE                        Page no.  7


                4) NOW WE REALLY GET TOUGH ! A random data pattern
                   WRITTEN / READ / and VERIFIED on the LAST PHYSICAL
                   SECTOR of the drive as defined in SETUP. This
                   location was chosen because operating systems
                   (and hence application programs) RARELY access the
                   last sector on the drive. Even if this sector was
                   able to be addressed in the machine's operating
                   system, you would have to be using EVERY BYTE on
                   the drive (within 512 bytes of full). This is rare.
                   Some errors that can exsist :

                RANDOM DATA WRITE/READ/COMPARE ERROR DESCRIPTION

                        a) WRITE FAULT FROM DRIVE ...... Covered before

                        b) DATA REQUEST FAILURE ........ Covered before

                        c) DATA COMPARE ERROR .......... A difference
                           between the WRITE data and the READ data
                           was discovered. You need to replace this
                           controller.

                        d) ID FIELD (address) NOT FOUND . Covered above

                        e) UNCORRECTABLE/CORRECTABLE DATA ERROR
                           Covered above.

                        f) DRIVE NOT READY ..............   --- OR ---
                           NO SEEK COMPLETE ............. Covered above

                        g) BAD BLOCK on drive ........... Covered above

                Sample screen follows ...



























User Documentation                 EZDIAG.EXE                        Page no.  8


         (A)utomatic quick test in progress ... please stand by ...



Now issuing the rezero (recal) command ......... command successful !

Now issuing 256 random seeks ................... command successful !

Now issuing 256 two sector random reads ........ command successful !

Now issuing 50 random data write/read verifies . data compared O.K. !



             Automatic quick test completed flawlessly !


           CONGRATULATIONS on a successful installation !



          (U)ser Defined Advanced Test ... Next Section ...






































User Documentation                 EZDIAG.EXE                        Page no.  9


          (U)ser Defined Advanced Test ... Operation

       This disk diagnostic is useful for a problem installation,
       or to verify absolute disk addresses in the event of a disk
       error later.
    
       The user can directly enter any cylinder, sector, or head
       he desires to test. The drive number can also be selected
       if TWO drives are present. The amount of sectors to test
       (sector count) is valid only for a (R)ead operation. If
       no value is entered for any parameter, the program
       automatically chooses:
    
               drive        =   0
               cylinder     =   0
               head         =   0
               sector no.   =   1
               sector count =   1
               command      =   re(Z)ero

       The currently supported commands are :
    
               re(Z)ero ....... recalibrates drive to cylinder 0
    
               (S)eek   ....... positions drive to any cylinder
    
               (R)ead   ....... transfers data from drive starting
                                at location chosen, and continues
                                for duration of sector count
    
               (W)rite / read . transfers a random pattern of
                                data to the drive, then reads
                                it back, and checks for errors.
                                THIS IS DONE ONLY AT THE LAST
                                SECTOR OF THE DRIVE. YOU CANNOT
                                CHANGE THE LOCATION.
    
               (A)ll .......... each of the preceeding commands
                                done in order. Any error will
                                terminate the sequence, and you
                                have the option of trying a
                                single command.


















User Documentation                 EZDIAG.EXE                       Page no.  10


       As you may notice, the sector number, sector count, and
       head number have no bearing on re(Z)ero and (S)eek
       commands.
    
       IMPORTANT NOTE : Illegal disk addresses have been screened
                        for, and the following is how the program
                        handles them.
    
       ILLEGAL SECTOR NUMBER : results when sector 0 or a sector number
                               greater than the actual sector per track
                               count is selected. Sector 0 is fixed
                               to 1, and the sector per track value
                               from the system BIOS is the maximum.
    
       ILLEGAL HEAD NUMBER   : results when a head number greater
                               than ONE LESS THAN THE BIOS VALUE
                               is selected. Head numbers are truncated
                               at one less than the BIOS value.

       ILLEGAL CYLINDER NO.  : results when a cylinder number less
                               than zero or greater than ONE LESS
                               than the BIOS table. Handled exactly
                               like the heads, above. Can also
                               result when a read operation will
                               span many cylinders. The actual
                               cylinder entered is tested against
                               the selected value PLUS the sector
                               count divided by the number of sectors
                               in a cylinder PLUS 1. If the result
                               would be greater, than the max cylinder
                               count of the drive, the difference is
                               truncated.
    
       ILLEGAL SECTOR COUNT .. results when less than zero or
                               greater than 256 is entered. The
                               program makes >256 equal the value
                               entered AND 255, and makes 0 equal 1.
    
       A sample session follows:





















User Documentation                 EZDIAG.EXE                       Page no.  11


          (U)ser Defined Advanced Test ... Sample Screen

     Drive 0 selected automatically
     Select a cylinder between           0  and     819   ? 819
     Select a head (surface) between     0  and       9   ? 9
     Select a starting sector between    1  and      17   ? 1
     Select a number of sectors between  1  and     256   ? 17
     The following commands are available :

      re(Z)ero,  (S)eek,  (R)ead,  (W)rite/read verify,  (A)ll

            ENTER YOUR OPTION      :      ? a

     Now issuing the rezero (recal) command ......... command successful !
     Now issuing the seek command ................... command successful !
     Now issuing the read command ................... command successful !

     For your protection, this part of our show will only do the LAST SECTOR
     That will be ... cylinder   819  , head   9  , sector   17

     Now issuing the write command .................. command successful !
     Now issuing the read command to compare data ... command successful !
     Now comparing data ............................. data compared O.K. !

     Want another test  ( y / n )          ?

    
    
       IMPORTANT NOTE : In the event of an error, the status and
                        error registers are presented to the screen.
                        An English interpretation of the HIGHEST
                        PRIORITY ERROR will follow. If there is a
                        real problem, such as an XT controller
                        installed in the system, or a timeout error
                        that "hangs" the controller, the status
                        and error register values may be the same.
                        The sector count, head number, and cylinder
                        number are also displayed.
    
         ERROR CODE SUMMARY FOR ALL TESTS SAME AS IN PRECEEDING SECTION

     IF PROBLEMS PERSIST ... 24 hour Technical Support number 1-800-777-4787
                                                              ==============