LU  is  a utility to manipulate "LBR" files generated  by 
the CP/M utility of the same name, or any of the MSDOS compatible 
ones.  The  most common use is to pack a group of  related  files 
into a single LBR file, for modem transfers or for archiving.

	LU  or  an  equivelant  program is  usually  required  to 
"unpack"  the  larger  software  packages  available  on   public 
Bulletin Board Systems.

	LBR  files  are  a  special  file  generated  by  LU  (or 
whatever)  that  contain  one or more DOS  files,  and  a  simple 
directory. Whenever an existing library is changed (files changed 
or  deleted)  the library requires "reorganizing".  More on  this 
below.

	LU  operation  is  quite simple.  Ther  are  only  a  few 
commands.  Each  is described below,  and a quick summary can  be 
obtained by running LU like so:

		LU <cr>

OPERATING LU

	LU  commands,  etc are entered on the command line  after 
the program name.  You must ALWAYS enter a command letter, below, 
and the name of an LBR file, followed by file names, if needed:

		LU <command> <lbr file name> { <optional filenames> }

	For example,

		LU T FILE.LBR

	Lists  all  the  files  contained  within  the  LBR  file 
FILE.LBR.

                     L U    C O M M A N D S

	All LU commands are a single letter. Only one can be entered
at a time.

A 	Unpack all files from the library.  This is the same  as 
the E (extract) command,  followed by all the file names. Thi sis 
much easier if all you want to do is remove all the files.


T 	List all files contained in the LBR file.  Each filename 
is  listed,  along with the size of the file in  bytes,  and  its 
starting  offset  within  the LBR file.  (The  offset  is  pretty 
useless information, but there it is.)

L	Same as T.

E 	Extract  a  file from the library.  The  file(s)  to  be 
extracted are entered after the LBR file name.  Each file will be 
extracted, and copied to a disk file of the same name.

U 	Update  a  library.  This  is also used  to  create  new 
libraries.  File name(s) are entered after the LBR file name, and 
each  file  is added to the library.  Any file of the  sam  ename 
already  in  the library will be deleted  first,  otherwise  just 
added. Pleas read about reorganizing, below.

	If  the library file does not exist (creating a new  one) 
then  you are asked for the number of new slots for the  library. 
"Slots"  means the maximum number of files that the LBR file  can 
contain.  The number you enter is rounded up to the next  highest 
multiple  of  four;  this is just a peculiarity of the  LBR  file 
structure.  It  does not hurt anything.  After the new library is 
created, any specified files are added to it.

D	Delete a file. The just marks the file within the library 
as "deleted".  The library file will NOT change in size;  it does 
not remove the data contained by the file.  See "reorganization", 
below.

R 	Reorganize  the library.  All free space  (from  deleted 
files,  or existing files that were Updated) is freed up, and the 
LBR file generally becomes smaller. Should be used after a Delete 
or Update command.  Creates a temporary file called LU$$$$$$.TMP, 
therfore you should not use this file name elsewhere.

                     R E O R G A N I Z I N G

	The structure of an LBR file (described in detail  below) 
is very simple. Because of its simplicity, files that are deleted 
or changed still consume space within the LBR file, which must be 
"squeezed" whenever the library is changed.

	Deleteing  a file merely marks the file as "deleted";  it 
does not remove the data contained in the LBR file. Updated files 
are deleted first, and also consume space. Therefore, the library 
must be reorganized. This consists of creating a new library, and 
copying the active files to it,  dropping out all the deleted  or 
changed data.

	The  rule  is:  reorganize  after  deleting  a  file,  or 
updating a file that already existed.  If the library runs out of 
slots,  and you want to add more files,  reorganize and specify a 
larger number of slots. You can then add to the library.

	Reorganizing never does any harm, in any case.


              L B R    F I L E    S T R U C T U R E

	The  LBR  file  is  a disk file that  contains  a  simple 
directory,  followed by all the data contained in the files.  New 
files  are added to the end of the LBR file,  and  the  directory 
entry for each file points to the data,  and contains its length. 
Each directory entry is:

	00:	file status (0= active, FF= deleted, FE= unused)
	01:	11 character filename (FCB format)
	12:	16 bit offset to start of data (in sectors)
	14:	16 bit data length (in sectors)
	16:	16 bytes of filler

	Since  the  original program was written in  BDS  C,  all 
offsets  and  lengths  are in multiples of 128  bytes,  the  CP/M 
"sector  size".  LU multiplies these values by 128 before  using. 
(Also, all file sizes are rounded up to the nearest 128 bytes.)

	The  offset  is the location of the data  for  the  file, 
relative to the start of the LBR file.

	The  first directory entry is the directory  itself.  The 
filename  is always blank, the offset is not used, and the length 
is the length of the directory. Since the length is a multiple of 
128,  LU  rounds  up the number of slots when creating a new  LBR 
file to a multiple of four. (32 bytes per entry * 4 == 128).

                    P E C U L I A R I T I E S

	There  are  only two peculiarities (nice  way  of  saying 
"bugs") that I know of: Filenames without extentions, like "FILE" 
instead  of "FILE.EXT" should be entered without a dot.  Entering 
with  a dot wil cause "NOT FOUND" errors to be  generated.  (I.e. 
use "FILE" not "FILE.".  Two, not really a bug, but a side effect 
of the original design:  all files are rounded up to the  nearest 
128 bytes.  This does not matter for most files,  but some,  like 
spreadsheet  files,  will  not  work unless the size  is  exactly 
right.  LU (or equivalent) cannot be used with such files. Try it 
and see what happens.