1        
        
        
                                         GEOD
        
                                    USER'S MANUAL
        
                                     version 1.1
        
                               (c) Copyright 1992-1993
                                     H. S. Aurand
                                 All rights reserved
        
                                     4 June 1993
        
        
        
        
        
        
                                   GETTING STARTED
        
        If you are viewing this document on the screen of a personal computer, 
        you have already decompressed GEODLHA.EXE to obtain the GEOD.DOC which 
        contains this manual.  You probably have done this by executing the 
        installation file, INSTGEOD.EXE.  In any event you should have the 
        following files in a single directory.
        
                     INSTGEOD.EXE  Installation file
                     GEODLHA.EXE   Self-extracting compressed file containing:
                     GEOD.EXE      
                     GEOD.MSG
                     GEOD.MIX
                     GEOD.DOC      User's Manual (this file)
                     README.DOC    Shareware information
                     VENDOR.DOC    Vendor Information
                     FILE_ID.DIZ   BBS Information
        
        If these files are not present in a desired directory, you should 
        install them in such a directory as follows:
        
        Place the GEOD distribution disk containing INSTGEOD.EXE and 
        GEODLHA.EXE in a floppy drive.  If the letter for that drive is n, 
        type n:instgeod <Enter>.  Answer the questions (there may be only 
        one), and you will be at the initial GEOD screen.  Please read the 
        information there.  Then press any key, and you will be at a screen 
        that permits input and execution as described in this document.  At 
        any menu the different help screens and the background and explanation 
        screens that make up this document can be viewed by pressing F1 or F8 
        respectively.  If want to save disk space you may delete all but 
        GEOD.EXE, GEOD.MSG and GEOD.MIX, but be sure to have INSTGEOD.EXE and 
        GEODLHA.EXE saved on a backup floppy disk. 
        



	2



                          GEOD - BACKGROUND AND EXPLANATION
        
        GEOD is a program to solve shortest-distance (geodetic) lines on an 
        ellipsoidal earth.  It also compares these results with three 
        different spherical earth solutions.
        
        Standard ellipsoids stored and used in the program are the Bessel-
        Encke(1852), International or Hayforth (1910) and Clarke (1866).  
        Other ellipsoids may be entered and used.  Also several different ways 
        are provided to calculate the earth's mean radius for these 
        ellipsoids.
        
        Different units may be specified for length and are changed 
        automatically throughout the program.  Those available are meters, 
        kilometers, feet, statute miles and nautical miles.  Nautical miles 
        have no standard definition.  A value of 10800 feet is used in this 
        program.
        
        There are seven variables that are defined by a line between two 
        points on the earth's surface - the latitude and longitude of one 
        point, the latitude and longitude of the other, the distance between 
        them and the azimuths of the two points from each other.  Four of 
        these variables must be specified in order to solve for the other 
        three.
        
        Of the several cases that ensue, the two most interesting, and the 
        ones solved by this program, are the vector, wherein a point and the 
        distance and azimuth to the other are specified, and the inverse, 
        wherein the two points are specified and the azimuths and distance 
        between them determined.
        
        In addition to single solutions for each of these two cases, there is 
        another mode in which multiple solutions are provided for the vector 
        case only.  In this mode the distance or the azimuth can be varied 
        between two values in specified increments.  Output to a printer can 
        also be provided.
        
        Comparisons with three different spherical solutions are made in the 
        single solution case.  In the first, the geodetic latitudes are used 
        as they are specified.  This is called the geographical solution.  In 
        the other two, the specified geodetic latitudes are altered before 
        calculation.  After calculation the inverse alteration is performed on 
        a calculated latitude.  These two cases are called the geocentric and 
        reduced respectively.
        
        In the geocentric spherical solution a latitude is changed to one 
        specified by a line running from the center of the meridional ellipse 
        to the point.  In the reduced spherical solution a latitude is altered 
        by reducing it in accordance with a geometrical construction used in 
        calculating the meridional ellipse.
        



	3



        It is beyond the scope of this brief note to explain and justify these 
        methods of calculation, but the user can run the program and see that 
        by altering the latitudes in the geocentric and reduced spherical 
        calculations a closer approximation to the geodetic line can often be 
        achieved.  To understand this and other aspects of geodetic 
        calculations, the user is referred to a general text on geodesy such 
        as "Geodesy", G. Bomford, Oxford, 1971.
        
        The author is not schooled in geodesy, but is an engineer.  On 
        occasion I have had the need to calculate geodetic lines.  In 
        reviewing the literature, I found that the several formulas were 
        predominately special purpose approximations that minimized 
        computational effort, but could be used only for limited ranges of 
        distance.  Before the advent of computers this is understandable.  
        However, I also noticed references to Helmert's method.  These 
        references stated that his solutions could be made as exact as desired 
        for any distance, albeit at the expense of computational effort.  I 
        found this to be so in his book, "Die Mathematischen und 
        Physikalischen Theorieen der H”heren Geod„sie", F. R.  Helmert, 
        B. G. Teubner Verlagsgesellschaft, Leipzig, 1880, republished by 
        Minerva GMBH Frankfurt/Main, 1962.
        
        This book contains an elegant solution for the vector case which 
        relies on strongly convergent series and is ideally suited for use on 
        small computers.  Helmert's solution for the inverse case not only has 
        this feature, but uses a strongly convergent iteration.  The 
        algorithms looks like they were developed with computer solutions in 
        mind!  Helmert's methods are used in this program.
        
        Helmert also addresses the case where the two points are antipodal or 
        near antipodal.  The results are counter-intuitive.  In the vector 
        case the locus of points having a constant geodetic distance is not a 
        continuous curve around the antipodal point, but has four well-defined 
        cusps.  This can be clearly seen by using the multiple solution case 
        varying the azimuth from 0ø to 90ø with a value of eta of .5.  In the 
        inverse case there are two solutions for the geodetic line for the 
        near antipodal case.  In this program only the shorter is calculated 
        and displayed.
        
        There is another counter-intuitive aspect of the geodetic line on an 
        ellipsoid that should be mentioned.  In general the geodetic line is 
        not contained in a plane containing the vertical at one end point and 
        the other end point.  Such a plane does not even contain the vertical 
        at the other end point (as does a great circle on a sphere).  In fact 
        the geodetic line is not contained in a plane at all.  Beware, there 
        are other counter-intuitive aspects of geodetic lines.  For further 
        explanation consult a geodesy text such as Bomford's.
        
        In this program there are two levels of accuracy that can be selected.  
        The first, labeled Helmert, follows Helmert's book closely except that 
        fifteen significant figures instead of seven are used.  The second, 
        labeled Helmert extended, in addition to this greater number of 
        significant figures, adds to the number of terms in his series,
	



	4



        decreases the epsilon at which iteration terminates in the inverse 
        case and adds an additional iteration to this case in which Newton's 
        Method is used to adjust for greater accuracy.   
        
        This program has been tested for accuracy in two ways.  First it has 
        been checked against the examples given in Helmert's book.  Second it 
        has been checked by running the vector and inverse cases sequentially 
        and observing the change from the initial values.  In this particular 
        attention has been paid to singular cases such as polar and antipodal 
        ones.  Nevertheless, bugs and mistakes are bound to slip through.  
        This version, 1.1, is a considerable improvement in this regard to 
        version 1.0 which saw only limited release.  The first registered user 
        who reports a non-trivial bug or error will be provided with a free 
        upgrade.
        
        This program is written in Microsoft C, version 6.0.  Double precision 
        is used for all calculations.  These have been encapsulated in a few 
        functions separate from the user interface.  Copies of the source code 
        can be licensed along with a mathematical explanation of the methods 
        used to extend the accuracy of the calculations beyond that given by 
        Helmert.  For information please contact the author at the address 
        listed below. 
        
        Your comments, critique and suggestions would be appreciated.
        
        
        
                               Henry S.Aurand
                               734 Camino Catalina
                               Solana Beach, CA 92075
        
                               Telephone:  619-481-0781
        



	5



                                 EXPLANATION OF MENUS
        
                                      MAIN MENU
        
        Provides access to all other menus.
        
        Use the highlighted and capitalized letter key or move the pointer 
        using the up and down arrow keys to the selection of your choice, then 
        press ENTER.
        
        The selections are:
        
        Quit -              Exits the program
        
        Spheroid -          Permits the selection of ellipsoids
        
        Radius of sphere -  Permits choice of several means for determining 
                            the radius of an approximating sphere used in 
                            calculating spherical solutions
        
        Units -             Permits the selection of the units used for the 
                            ellipsoid axes, distance and spherical radius
        
        Accuracy -          Permits the selection of Helmert or Helmert
                            extended accuracy along with selection of the
                            epsilon for error termination and maximum number 
                            of iterations
        
        sIngle execute -    Goes to Single/Input Output Menu where data can be
                            entered and a solution obtained for either vector
                            or inverse cases
        
        muLtiple execute -  Goes to Multiple Input/Output Menu where data can 
                            be entered and solutions obtained for the vector 
                            case.  Azimuth or distance can be varied in steps. 
                            Output is to the screen and may be sent to a 
                            printer
        
        Zero variables -    Zeros all seven input/output variables.  Does not
                            affect ellipsoid parameters
        
        View descriptive information - Displays several pages of background
        



	6



                   Keys which operate at all menus are as follows:
        
        
        F1 and H - Help
        
        F2 -       Go to single execution input/output menu
        
        F3 -       Go to multiple execution input/output menu
        
        F4 -       Go to spheroid menu
        
        F5 -       Go to radius of approximating sphere menu
        
        F6 -       Go to units menu
        
        F7 and Z - Zeros variables.  Zeros all seven input/output variables.
                   Does not affect ellipsoid parameters.  Z is only effective
                   in the two Input/Output menus.
        
        F8 -       View descriptive information.  Displays five pages of 
                   background
        
        F9 -       Go to Accuracy menu
        



	7



                                    SPHEROID MENU
        
        Permits the selection of different spheroids.
        
        Use the highlighted and capitalized letter key or move the pointer 
        using the up and down arrow keys to the selection of your choice, then 
        press ENTER.
        
        Quit -             Quits program
        
        Main -             Return to Main Menu
        
        Radius of sphere - Goes to Radius of Sphere Menu
        
        Units Menu -       Goes to Units Menu
        
        Single Execute -   Goes to Single/Input Output Menu where data can be
                           entered and a solution obtained for either vector 
                           or inverse cases.
        
        muLtiple execute - Goes to Multiple Input/Output Menu where data can 
                           be entered and solutions obtained for the vector 
                           case.  Azimuth or distance can be varied in steps.
                           Output is to the screen and may be sent to a 
                           printer 
        
        Bessel -           Changes to the Bessel standard ellipsoid
        
        haYforth -         Changes to the Hayforth standard ellipsoid
        
        Clarke -           Changes the Clarke standard ellipsoid
        
        Other -            Permits direct entry of semimajor and semiminor 
                           axes of any ellipsoid
        



	8



                                RADIUS OF SPHERE MENU
        
        Permits the selection of the radius for the approximating sphere.
        
        Use the highlighted and capitalized letter key or move the pointer 
        using the up and down arrow keys to the selection of your choice, then 
        press ENTER.
        
        Quit -                Quits program
        
        Main menu -           Return to Main Menu
        
        Spheroid menu -       Goes to Spheroid Menu
        
        Units Menu -          Goes to Units Menu
        
        Single execute -      Goes to Single/Input Output Menu where data can 
                              be entered and a solution obtained for either 
                              vector or inverse cases
        
        muLtiple execute -    Goes to the Multiple Input/Output Menu where 
                              data can be entered and solutions obtained for 
                              the vector case.  Azimuth or distance can be 
                              varied in steps.  Output is to the screen and 
                              may be sent to a printer
        
        Geometric mean -      Sets the radius of the approximating sphere 
                              equal to the geometric mean of the axes of the 
                              ellipsoid used 
        
        Equal volume -        Sets the radius of the approximating sphere 
                              equal to that of a sphere having the same volume
                              as the ellipsoid used
        
        Equal area -          Sets the radius of the approximating sphere 
                              equal to that of a sphere having the same 
                              surface area as the ellipsoid used
        
        Other proportional -  Sets the radius of the approximating sphere 
                              equal to c * a0 ^ rho  *  b0 ^ (1-rho).  c and 
                              rho must be entered.  a0 and b0 are the 
                              semimajor and semiminor axes respectively of the
                              ellipsoid used
        
        Enter -               The radius of the approximating sphere is 
                              entered by the user
        



	9



                                      UNITS MENU
        
        Permits the selection of units for all distance variables and 
        parameters.
        
        Use the highlighted and capitalized letter key or move the pointer 
        using the up and down arrow keys to the selection of your choice, then 
        press ENTER.
        
        Quit -             Quits program
        
        Main menu -        Return to Main Menu
        
        sPheroid -         Goes to Spheroid Menu
        
        Radius of sphere - Goes to Radius of Sphere Menu
        
        Single Execute -   Goes to Single/Input Output Menu where data can be
                           entered and a solution obtained for either vector 
                           or inverse cases.
        
        muLtiple execute - Goes to Multiple Input/Output Menu where data can 
                           be entered and solutions obtained for the vector 
                           case.  Azimuth or distance can be varied in steps.
                           Output is to the screen and may be sent to a 
                           printer
        
        
        When one of the following is selected, the units for all variables and 
        parameters are changed to the value selected.
        
        Kilometers 
        
        Nautical miles
        
        Statute miles
        
        mEters
        
        Feet
        



	10



                               SINGLE INPUT/OUTPUT MENU
        
        Permits the entry of input and displays output for a single solution.
        The display indicates whether the calculation is vector or inverse as 
        well as the spheroid, the units, the radius approximation and the 
        accuracy used.  In the inverse case the number of iterations required 
        is also shown and if extended accuracy is used the number of 
        iterations for this purpose is also shown.
        
        Use the highlighted and capitalized letter key or move the pointer 
        using the up and down arrow keys to the selection of your choice, then 
        press ENTER.  When you make a selection requiring input of an angle, 
        you must press ENTER after each entry to the "deg?", "min?" and "sec?" 
        prompts.  For latitude an "n" or "s" and for longitude a "w" or "s" 
        are required to complete the entry.  If out of range entries are made, 
        the display so indicates.  To return to inputting press any key.
        
        Quit -                       Quit the program
        Main menu -                  Return to Main Menu
        mUltiple execute -           Goes to MULTIPLE INPUT/OUTPUT MENU
        Type of calculation toggle - Toggles between vector and inverse
                                     calculations
        Go -                         Performs calculation after input data 
                                     has been entered.  The  results are 
                                     displayed alongside the selections and at
                                     the bottom of the screen.  The computed 
                                     results of the three spherical 
                                     approximations are compared with the 
                                     ellipsoidal results.  See the Main Menu 
                                     selection, "View descriptive 
                                     information" or press F8, to see an 
                                     explanation of these approximations. 
        
        In the following you are permitted to enter only the variables needed. 
        
        1 Enter Lat1 -        Enter the latitude of the first point
        2 Enter Long1 -       Enter the longitude of the first point
        3 Enter Lat2 -        Enter the latitude of the second point
        4 Enter Long2 -       Enter the longitude of the second point
        5 Enter Az1,2 -       Enter the azimuth, clockwise from north, of the
                              second point from the first
        6 Az2,1 -             Azimuth, clockwise from north, of the first 
                              point from the second.  Never can be entered, 
                              results of calculation only are displayed.
        7 Enter distance, s - Enter the distance between two points in the 
                              units shown
        



	11



                              MULTIPLE INPUT/OUTPUT MENU
        
        Permits the entry of input and displays output for a range of 
        solutions.
        
        Use the highlighted and capitalized letter key or move the pointer 
        using the up and down arrow keys to the selection of your choice, then 
        press ENTER.  When you make a selection requiring input of an angle, 
        you must press ENTER after each entry to the "deg?", "min?" and "sec?" 
        prompt.  For latitude an "n" or "s" and for longitude a "w" or "s" 
        only are required to complete the entry.  If out of range entries are 
        made, the display so indicates.  To return to inputting press any key.
        
        Quit -            Quit the program
        
        Main menu -       Return to Main Menu
        
        Units -           Goes to Units Menu
        
        Single execute -  Goes to SINGLE INPUT/OUTPUT MENU
        
        Variable toggle - Successively selects Az1,2, distance and distance
                          parameter, eta, to be varied
        
        Go -              Calculates vector case in accordance with beginning,
                          ending and difference variables entered.  Outputs 
                          the results below these and scrolls the display up 
                          as required.  Outputting can be stopped for viewing 
                          by pressing any key except ESC.  Pressing any key 
                          except ESC will resume outputting.  Pressing ESC 
                          will return to the menu
        


	12




        In the following you are permitted to enter only the variables needed.
        
        If selected,
        
        1 Enter Lat1 -        Enter the latitude of the first point
        2 Enter Long1 -       Enter the longitude of the first point
        3 Lat2 -              Latitude of the second point
        4 Long2 -             Longitude of the second point
        5 Enter Az1,2 -       Enter the azimuth, clockwise from north, of the
                              second point from the first.  No entry permitted
                              if you are varying this azimuth
        6 Az2,1 -             Azimuth, clockwise from north, of the first 
                              point from the second.  Cannot be entered, 
                              results of calculation only are displayed
        7 Enter distance, s - Enter the distance between two points in the 
                              units shown.  s and eta cannot be entered if you 
                              are varying either.
        8 Enter eta -         Enter this dimensionless parameter, called 
                              offset ratio, that sets distance.  Used 
                              primarily for antipodal or near antipodal cases.
                              When eta is 0, the distance, s, is set at pi 
                              times the semiminor axis, b0.  When 1, s is set
                              at pi times the semimajor axis, a0.  When .5, s
                              is set to the average of these two values. This
                              is just slightly smaller than the meridional 
                              distance from equator to equator.  The correct
                              value for this distance can be determined using
                              the inverse case of the single input/output case
        9 Print toggle -      When "on" outputs to standard printer in the 
                              same format as the output to the screen.
        
        In the following, input is made to a variable determined by the 
        Variable toggle set above.  The three types are: Az1,2, distance and 
        offset ratio.
        
        A Enter starting (variable name)
        B Enter ending (variable name)
        C Enter delta (variable name)
        
        
        Pressing F7 or 'Z' zeros the seven variables, but not the ellipsoid 
        parameters
        



	13



                                    ACCURACY MENU
        
        Permits the selection of variables that affect the accuracy of 
        calculations.
        
        Use the highlighted and capitalized letter key or move the pointer 
        using the up and down arrow keys to the selection of your choice, then 
        press ENTER.
        
        Quit -             Quits program
        
        Main menu -        Return to Main Menu
        
        sPheroid -         Goes to Spheroid Menu
        
        Radius of sphere - Goes to Radius of Sphere Menu
        
        Units menu -       Goes to Units Menu
        
        sIngle Execute -   Goes to Single/Input Output Menu where data can be
                           entered and a solution obtained for either vector 
                           or inverse cases.
        
        muLtiple execute - Goes to Multiple Input/Output Menu where data can 
                           be entered and solutions obtained for the vector 
                           case.  Azimuth or distance can be varied in steps.
                           Output is to the screen and may be sent to a 
                           printer
        
        Accuracy toggle -  Toggles between Helmert's method and extended 
                           accuracy achieved by extending his series and 
                           adding a Newton's Method approximation in the
                           inverse case.  Resets the epsilon used in 
                           terminating iterations in the inverse case. Uses 
                           1.0e-9 for Helmert and 1.0e-15 for Helmert extended
                           accuracies.
         
        enter Epsilon -    Permits the user to select the epsilon used in 
                           terminating iterations.  Note that this value is 
                           overwritten by the Accuracy toggle.
        
        enter max inVerse iterations -  Permits the user to select the 
                           maximum number of iterations used in the inverse 
                           case.  Default value is 100
        
        enter max inverse iterations for Newton's method -  Permits the user 
                           to select the maximum number of iterations used in 
                           the inverse case when Helmert extended accuracy 
                           is used.  Default value is 100.