GRAPHICS.DOC -- Graphic Plotting Procedures
===========================================

  From `BLUEBOOK of ASSEMBLY ROUTINES for the IBM PC & XT'
        by Christopher L. Morgan
        Copyright (C) 1984 by The Waite Group, Inc.

  Purpose: GRAPHICS.ASM contains routines to perform fundamental plotting jobs
    on the IBM PC. These include point plotting, line drawing, character
    drawing, and filling of areas.  GRAPHICS.DOC describes the routines.

   Contents:
   ---------
   CLS		--  Clear the screen
   GET_COLOR	--  Get the color of a point on the med res color screen
   GMSG_OUT	--  Plot a string
   PAINT	--  Fill an area with specified color
   RCHAR	--  Plot a raster character
   SCHAR	--  Plot a stroke character
   SET_BOX	--  Fill a rectangular box with specified color
   SET_LIN	--  Draw a line
   SET_PT	--  Plot a point
   XOR_BOX	--  Fill a rectangular box using XOR
   XOR_PT	--  Plot a point using XOR
 _____________________________________________________________________________

Primitive Functions
-------------------

CLS -- Clear the graphics screen.

  Function: This routine clears the color graphics screen.

  Input: None.

  Output: Just to the screen.

  Registers used: Unmodified; AX & CX are saved, then restored.

  Segments referenced: Upon entry, ES must point to screen RAM at B8000H.

  Routines called: None.
 -----------------------------------------------------------------------------
SET_PT -- Plot a point on the medium resolution color screen.

  Function: This routine plots a point on the medium resolution color graphics
    screen. The pixel at the specified location is given a specified color,
    over-writing the old color.

  Input: Upon entry:
   		     X-coordinate (0-319) of the point is in SI
		     Y-coordinate (0-199) of the point is in DI
		     color (0-3) is in DX.	

  Output: Just to the screen.

  Registers used: Unmodified; SI,DI, & DX are used for input.

  Segments referenced: Upon entry, ES must point to video RAM at B8000, and
    DS must point to a data segment containing the following look-up table
    of rotated color masks:

	CTABLE	DW	0003FH,0403FH,0803FH,0C03FH
		DW	000CFH,010CFH,020CFH,030CFH
		DW	000F3H,004F3H,008F3H,00CF3H
		DW	000FCH,001FCH,002FCH,003FCH

  Routines called: None.

  Note: No bounds checking is performed.  Programmer must ensure the 
    coordinates and color are in their proper ranges.
 -----------------------------------------------------------------------------
XOR_PT -- Plot a point using XOR onto the med res color screen.

  Function: This routine plots a point on the med res screen using the 
    `exclusive or' operation. The pixel at the specified location is colored
     with a color obtained by `exclusive oring' its original color with a
     specified color.  This function is useful for making cursors.

  Input: Upon entry:
   		     X-coordinate (0-319) of the point is in SI
		     Y-coordinate (0-199) of the point is in DI
		     color (0-3) is in DX.	

  Output: Just to the screen.

  Registers used: Unmodified; SI,DI, & DX are used for input.

  Segments referenced: Upon entry, ES must point to video RAM at B8000, and
    DS must point to a data segment containing the following look-up table
    of rotated color masks:

	CTABLE	DW	0003FH,0403FH,0803FH,0C03FH
		DW	000CFH,010CFH,020CFH,030CFH
		DW	000F3H,004F3H,008F3H,00CF3H
		DW	000FCH,001FCH,002FCH,003FCH

  Routines called: None.

  Note: No bounds checking is performed.  Programmer must ensure the 
    coordinates and color are in their proper ranges.

 -----------------------------------------------------------------------------
GET_COLOR  -- Get color of a point on med res screen.

  Function: This routine returns the color of a specified point on the med
    res color screen.  The color is returned in AL.

  Input: Upon entry:
   		     X-coordinate (0-319) of the specified point is in SI
		     Y-coordinate (0-199) of the specified point is in DI.

  Output: Upon exit, AL contains the color (0-3) of the pixel at the 
    specified location.

  Registers used: Only AX is modified.  SI & DI are used for input and AL is
    used for output.

  Segments referenced: Upon entry, ES must point to the video RAM at B8000H.

  Routines called: None.

  Note: No bounds checking is performed.  Programmer must ensure the 
    coordinates and color are in their proper ranges.
 -----------------------------------------------------------------------------
SET_BOX -- Fill a rectangular box.

  Function: This routine fills a rectangular box on the color graphics screen
    with a specified color.

  Input: Upon entry:
		     X-coordinate of upper left corner is in X1
		     Y-coordinate of upper left corner is in Y1
		     X-coordinate of lower right corner is in X2
		     Y-coordinate of lower right corner is in Y2
		     Color of the rectangle is in bits 0 & 1 of COLOR.

  Output: Just to the screen.

  Registers used: Unmodified; SI, DI, DX, BX, CX, & AX are save & restored.

  Segments referenced: Upon entry, ES must point to video RAM at B8000, and
    DS must point to a data segment containing the following look-up table
    for color masks:

	XTABLE	DW	0FFC0H,0FFF0H,0FFFCH,0FFFFH
		DW	03FC0H,03FF0H,03FFCH,03FFFH
		DW	00FC0H,00FF0H,00FFCH,00FFFH
		DW	003C0H,003F0H,003FCH,003FFH

  Routines called: None.

  Note: No bounds checking is performed.  Programmer must ensure the 
    coordinates are in their proper range and order; i.e., the following
    must be true:
		 0 <= X1 <= X2 <= 319
		 0 <= Y1 <= Y2 <= 199.
 -----------------------------------------------------------------------------
XOR_BOX -- Fill a rectangular box using XOR.

  Function: This routine fills a rectangular box in the color graphics screen
    with a given color using the `exclusive or' operation. Each pixel in the
    rectangle is colored with a color obtained by `exclusive oring' its 
    original color with a specified color.  This function is useful for 
    making cursors.

  Input: Upon entry:
		     X-coordinate of upper left corner is in X1
		     Y-coordinate of upper left corner is in Y1
		     X-coordinate of lower right corner is in X2
		     Y-coordinate of lower right corner is in Y2
		     Color of the rectangle is in bits 0 & 1 of COLOR.

  Output: Just to the screen.

  Registers used: Unmodified; SI, DI, DX, BX, CX, & AX are saved & restored.

  Segments referenced: Upon entry, ES must point to video RAM at B8000, and
    DS must point to a data segment containing the following look-up table
    for color masks:

	XTABLE	DW	0FFC0H,0FFF0H,0FFFCH,0FFFFH
		DW	03FC0H,03FF0H,03FFCH,03FFFH
		DW	00FC0H,00FF0H,00FFCH,00FFFH
		DW	003C0H,003F0H,003FCH,003FFH

  Routines called: None.

  Note: No bounds checking is performed.  Programmer must ensure the 
    coordinates are in their proper range and order; i.e., the following
    must be true:
		 0 <= X1 <= X2 <= 319
		 0 <= Y1 <= Y2 <= 199.
 -----------------------------------------------------------------------------
	
Second Level Functions (use Primitive Functions)
----------------------

SET_LIN -- Draw a line.

  Function: This routine draws a line from (X1,Y1) to (X2,Y2) in the specified
    color.  It uses Bresenham's algorithm.

  Input: Upon entry:
		     X-coordinate of starting point is in X1
		     Y-coordinate of starting point is in Y1
		     X-coordinate of ending point is in X2
		     Y-coordinate of ending point is in Y2
		     Color of line is in COLOR.

  Output: Just to the screen.

  Registers used: Unmodified; BX, CX, DX, SI, DI, & AX are saved & restored.

  Segments referenced: Upon entry, ES must point to video RAM at B8000H, and
    DS must point to a data segment used by the SET_PT plotting routine.

  Routines called: SET_PT.

  Note: No bounds checking is performed.  Programmer must ensure the 
    coordinates are in their proper range; i.e., the following
    must be true:
		 0 <= X1 & X2 <= 319
		 0 <= Y1 & Y2 <= 199
                 0 <= COLOR <= 3.
 -----------------------------------------------------------------------------
SCHAR -- Plot a stroke character.

  Function: This routine plots a stroke character. It uses a stroke character
    table in which each character is stored as a series of strokes.  The
    programmer must create this stroke character table according to specific
    rules. Each stroke is stored as three bytes.  The first byte contains a
    code as follows:
		     1AH = end of strokes
		     `U' = pen Up, move to new current position,
			     but don't draw
		     `D' = pen Down, draw a stroke from old to
			     new current position.

    The second byte contains the local X-coordinate of the new current
    position, and the third byte contains the local Y-coordinate of the new
    current position. These local coordinates are relative to the upper left
    corner of the character cell. At the beginning of the stroke table is an
    address table for the locations of the strokes for each of the characters.

  Input: Upon entry:
                     ASCII code character is in AL
		     X-coord of upper left corner of char cell is in X0
		     Y-coord of upper left corner of char cell is in Y0
		     Horizontal magnitude is in XMAGN
		     Vertical magnitude is in YMAGN
		     Color of character is in COLOR.

  Output: Just to the screen.

  Registers used: Unmodified; SI, CX, & AX are saved & restored.

  Segments referenced: Upon entry, ES must point to video RAM at B8000H, and
    DS must point to the data segment used by the point and line-drawing
    routines. This data segment must also contain the table of stroke chars.

  Routines called: SET_LIN.

  Note: No bounds checking is performed. Unpredictable results happen if the
    horizontal or vertical magnitude is too large. A string of raster 
    characters can be printed using the GMSG_OUT routine.
 -----------------------------------------------------------------------------
RCHAR  -- Plot a raster character.
 
  Function: This routine plots a raster character. It uses the raster
    character table in the IBM BIOS ROM. Only ASCII codes 0 through 127
    are supported.

  Input: Upon entry:
                     ASCII code character is in AL
		     X-coord of upper left corner of char cell is in X0
		     Y-coord of upper left corner of char cell is in Y0
		     Horizontal magnitude is in XMAGN
		     Vertical magnitude is in YMAGN
		     Color of character is in COLOR.

  Output: Just to the screen

  Registers used: Unmodified; SI, DX, CX, & AX are saved & restored.

  Segments referenced: Upon entry, ES must point to video RAM at B8000H, and
    DS must point to the data segment used by the box-fill routine.

  Routines called: SET_BOX.

  Note: No bounds checking is performed. Unpredictable results happen if the
    horizontal or vertical magnitude is too large. A string of raster 
    characters can be printed using the GMSG_OUT routine.
 -----------------------------------------------------------------------------
GMSG_OUT  -- Print a string on the graphics screen.

  Function: This routine prints a message on the graphics screen, using the
    SCHAR or RCHAR routines. The message terminates in a zero. 

  Input: Upon entry:
                     Address of message is in SI
		     X-coord of upper left corner of string is in XMSG
		     Y-coord of upper left corner of string is in YMSG
		     Horizontal magnitude of characters is in XMAGN
		     Vertical magnitude of characters is in YMAGN
		     Color of characters is in COLOR
		     Choice of fonts (0=stroke,1=raster) is in FONT.

  Output: Just to the screen

  Registers used: Unmodified.

  Segments referenced: Upon entry, ES must point to video RAM at B8000H, and
    DS must point to the data segment used by the point-plotting, box-filling,
    line-drawing, and stroke character routines.

  Routines called: RCHAR & SCHAR

  Note: No bounds checking is performed. Unpredictable results happen if the
    horizontal or vertical magnitude is too large.
 -----------------------------------------------------------------------------
PAINT -- Fill an area on the screen with color.

  Function: This routine fills an area on the graphics screen with a specified
    color. It begins `painting' at a `seed' position, filling a region bounded
    by a `boundary' color.

  Input: Upon entry:
		     X-coordinate of seed is in SI
		     Y-coordinate of seed is in DI
		     Paint color is in the low byte of COLOR
		     Boundary color is in the high byte of COLOR.

  Output: Just to the screen.

  Registers used: Unmodified.

  Segments referenced: Upon entry, ES must point to video RAM at B8000H, and
    DS must point to the data segment used by the point-plotting & get-color
    routines.

  Routines called: SET_PT & GET_COLOR

  Note: The region must be completely surrounded by a boundary drawn in the
    boundary color. Any paint color in the region can obstruct the filling
    process, acting just like a boundary. This algorithm uses its own stack.
    If the region is too complex, this stack will overflow.  There is no
    check for stack overflow, but one could easily be added.
 -----------------------------------------------------------------------------
 _____________________________________________________________________________
>>>>> Physical EOF GRAPHICS.DOC <<<<<