READ
                                        THIS
                                       BEFORE
                                      PRINTING!!!!



      This document has been formatted in a special way. Virtually all dot
      matrix printers have a condensed mode which prints 132 characters
      across a standard 8 1/2 inch page.  When this file is printed out in
      condensed mode, the resulting printed pages can be cut down to 5 1/2 X
      8 1/2 inches.  The cut pages will fit nicely in the back of your
      DOS manual for storage.

      Typically, you can turn on this mode by sending a special control
      sequence to the printer from BASIC.  For example, you can turn on the
      condensed mode of the IBM/Epson printer with the BASIC statement:
      LPRINT chr$(15).  If your printer has such a condensed mode, turn it
      on now, before printing the rest of this document.






















































                                         (tm)
                                    CHASM

                               Cheap Assembler
                        for the IBM Personal Computer

                                User's Manual
                          (c) 1983 by David Whitman
                                Version 4.00



















      David Whitman
      136 Wellington Terrace
      Lansdale, PA 19446

      (215) 641-7114 (days)
      (215) 362-8526 (evenings)






















                        Table of Contents




      Why CHASM?..................................................1
      What can CHASM do?..........................................2
      What WON'T it do?...........................................3
      System Requirements.........................................4
      Advanced and Subset CHASM...................................5
      Modifying CHASM's I/O Defaults..............................6
      Syntax.....................................................10
      Labels.....................................................12
      Operands...................................................15
      Operand Expressions........................................20
      Resolution of Ambiguities..................................23
      Pseudo-Operations..........................................26
      Macros.....................................................33
      Structures.................................................41
      Outside the Program Segment................................45
      Running CHASM..............................................46
      Error and Diagnostic Messages..............................50
      Execution of Assembled Programs............................54
      Notes for Those Upgrading to This Version of CHASM.........62
      Miscellaneous and A Word From Our Sponsor..................65
      =============================================================
      Appendix A: Mnemonic List..................................70
      Appendix B: Differences Between CHASM and TOA..............72
      Appendix C: Description of Files...........................77
      Appendix D: Bug Reporting Procedure........................78
      Appendix E: Using CHASM on "Compatable" Systems............79
      Compiled Version Order Form................................80
































                                                                      1

      >>Why CHASM?<<

      Why go to the trouble to write an assembler, when one already
      exists?  The IBM Macro Assembler is a very powerful software tool
      available off the shelf.  It supports features such as macros,
      multiple segments, and linking to external procedures.

      Unfortunately, the cost of all this power is complexity. The
      Macro Assembler is so complicated that IBM warns beginners it is
      only suitable for "experienced assembly language programmers".

      For most users, this sophistication is more of a hindrance than
      an aid.  Even when writing short, simple programs, the user is
      saddled with a set of confusing pseudo-ops only appropriate for
      large, multi-segment programs.  Producing a fast loading
      executable file requires running three separate programs (MASM,
      LINK and EXE2BIN) before you can get down to testing.

      The macro assembler is totally unsuitable for use with BASIC.
      Although it is *possible* to produce machine language subroutines
      for BASIC with the Macro Assembler, the process is incredibly
      convoluted and confusing.

      To top it all off, the Macro Assembler costs an overpriced $125.

      CHASM is, I hope, a more reasonable compromise between power and
      accessibility.  CHASM is simple to use and understand.  Unlike
      the Macro Assembler, CHASM doesn't require a second LINK step to
      produce a working program.  CHASM also produces fast loading
      programs without the use of the utility EXE2BIN.

      CHASM supports two different, simple mechanisms for getting
      machine language routines into BASIC, the most popular language
      for the IBM Personal Computer.

      Finally, the suggested payment for CHASM is a modest $40.

      A Note for Beginners:

      Before going on, you might find it useful to print and read the
      file PRIMER.DOC, included on your CHASM disk.  PRIMER is a gentle
      introduction to assembly language, which will teach you some of
      the vocabulary and key concepts you will need to start out with.





















                                                                      2

      >>What can CHASM do?<<

      CHASM is a tool for translating assembly language into the native
      machine language of the 8088 microprocessor.  Using CHASM, you
      can write down easy to remember "mnemonics" which are then
      converted into the relatively incomprehensible series of ones and
      zeros that your PC prefers to work with.

      In addition to simple mnemonic translation (such as provided by
      the mini-assembler in DEBUG), CHASM provides a great many
      "convenience" features which make writing machine language much
      easier.

      CHASM allows you to define labels for branching, rather than
      requiring you to figure out offsets or addresses to jump to.
      CHASM also lets you give symbolic names to any constants or
      memory locations you use, to make your program easier to
      understand.

      You can instruct CHASM to make your file "BLOADable" so that
      BASIC can load it as a subroutine.   A utility is also provided
      to convert machine language into BASIC "DATA" statements, so that
      BASIC can "POKE" routines into memory.

      CHASM has intelligent error and diagnostic messages which guide
      you in correcting mistakes and ambiguities in your program.  A
      nicely formatted listing is produced during assembly, to help
      during debugging.

      In general, CHASM is designed to eliminate much of the confusion
      and dirty work involved in writing machine language for the IBM
      PC.

      Using CHASM, you can produce:

         1. Lightning fast "stand-alone" programs.

         2. Machine language subroutines for BASIC programs, both
            interpreted and compiled.

         3. External procedures for Turbo Pascal (*)



      * Turbo Pascal is a product of Borland International. 



















                                                                      3


      >>What WON'T it do?<<

      In the interest of simplicity, CHASM has the following
      restrictions:

      1. Multiple segment definitions are not allowed. CHASM assumes
         that your entire program fits in one segment, that the cs, ds,
         and es registers all point to this same segment, and that the
         ss register points to a valid stack area.  An equivalent
         statement is that CHASM produces COM files, not EXE files.

      2. Linking to Microsoft languages is not supported.  You can't
         use CHASM to produce object modules for use with IBM/Microsoft
         Pascal or FORTRAN.

















































                                                                      4

      >>System Requirements<<

      Minimum system requirements to use CHASM are:

           IBM PC or true compatible (must emulate IBM BIOS)
           128K of memory
           1 disk drive
           80 column display
           DOS 2.0 or later.

      Note the DOS 2.0 requirement.  To provide *true* DOS 2 support,
      it was necessary to give up DOS 1 compatibility.  If you're still
      using DOS 1, you'll need to upgrade to DOS 2.0 or later to use
      CHASM.

      Adding more memory will allow you to assemble larger programs.
      CHASM can take advantage of all available memory, up to a
      megabyte.

      CHASM will run faster if your source files and object files are
      on a hard disk or RAM disk.











































                                                                      5

      >>Advanced and Subset CHASM<<

      CHASM is available in two flavors, Advanced and Subset.
      The two versions vary in their capabilities and method of
      distribution.

      The subset version is the budget release.  It may be freely
      copied by individuals as "user-supported" software, and is
      available from user groups and bulletin boards across the
      country.  Every time the subset runs, it prints a banner page
      suggesting a payment of $40 to the author.  As its name
      suggests, Subset CHASM does not support all the features of
      Advanced CHASM.

      Advanced CHASM is the deluxe release.  It runs twice as fast, and
      has a number of features not supported by the subset:

            macros
            conditional assembly
            include files
            operand expressions
            structures

      Advanced CHASM is only available directly from Whitman Software.
      Users who make the suggested $40 payment receive an upgrade to
      Advanced CHASM.  Details, and an order blank are given at the
      end of this document.

      Throughout this document, features supported only by the
      advanced version will be marked as follows:

        ==>Advanced version only.

      Attempts to use these features in the subset version will
      generally result in error messages, with the advanced feature
      otherwise being ignored; however, unpredictable behavior could
      result in some instances.



























                                                                      6

      >>MODIFYING CHASM'S I/O DEFAULTS<<

      CHASM supports the use of a configuration file, which can be used
      to override some of CHASM's I/O defaults.  If you are willing to
      accept CHASM's defaults, you may skip this section - CHASM will
      work perfectly well without the file described below.

      The configuration process involves supplying a text file named
      CHASM.CFG on your default drive.  You can create this file with
      any text editor or word processor.

      You have some freedom in where you put the configuration file.
      If CHASM.CFG is not found in the current directory, CHASM will
      also try the following paths:

            \CHASM\CHASM.CFG
            \CHASM.CFG

      The file should contain a series of text "switches" of the
      following form:

      /SWITCH, xx [, yy, zz,...]

      Where "/SWITCH" is a reserved word, listed below, and xx, yy, zz
      are numbers.  The brackets around yy and zz indicate that these
      numbers are optional - don't put brackets in CHASM.CFG.

      Each switch should start a new line, and the switch and each of
      the numbers should separated by one or more blanks or commas.

      The following switches are implemented:

      /132        Printer 132 column mode.  The numbers following this
                  switch are the ASCII codes for the characters which
                  cause your printer to go into condensed mode.  You
                  may specify as many characters as you like.  If you
                  don't provide this switch, CHASM will truncate source
                  lines in listings to avoid going over 80 columns. You
                  can also include characters to activate any special
                  features of your printer you want CHASM to use during
                  printing.  Example: (for IBM printer)

                  /132, 15





















                                                                      7

      /80         Printer 80 column mode.  Similar to /132, but the
                  numbers represent the characters to return your
                  printer to normal.  Include the codes for any
                  characters you want CHASM to send to your printer
                  before returning you to DOS.  The following example
                  turns off condensed mode and causes a Form Feed on
                  the IBM printer:

                  /80, 18, 12

      /FF         Formfeed.  A value of zero tells CHASM that your
                  printer doesn't recognize ASCII 12 as a formfeed
                  command.  Any other value, and CHASM assumes that
                  formfeeds will be recognized.  The default is no
                  formfeed character.

                  If /FF is off, CHASM will simulate formfeeds with a
                  series of linefeeds.  However, most printers respond
                  quicker to a formfeed than to multiple line feeds, so
                  set /FF on if possible.  Example: (on)

                  /FF, 1

      /PAGELEN    CHASM assumes that there are 66 lines to each printed
                  page.  If you use different sized paper, enter the
                  number of lines per page after this switch.
                  Example: (European standard)

                  /PAGELEN, 72

      /LINES      By default, CHASM will print 58 lines on each printed
                  page, then skip over the perforation to the next
                  page.  You can change this number to suit your paper
                  and personal taste.  Example:

                  /LINES, 50

      /BEEP       Enables/Disables audible warning when errors are
                  discovered in your source program.  A value of zero
                  turns off beeping, anything else turns it on. The
                  default is on.  Example: (off)

                  /BEEP, 0





















                                                                      8

      /FG         Foreground color.  Users with color monitors may
                  select a foreground color from the following list:

                  0    Black               8    Gray
                  1    Blue                9    Light Blue
                  2    Green              10    Light Green
                  3    Cyan               11    Light Cyan
                  4    Red                12    Light Red
                  5    Magenta            13    Light Magenta
                  6    Brown              14    Yellow
                  7    White              15    High Intensity White

                  Example: (Magenta)

                  /FG, 5

      /BG         Background color.  Selections 0-7 above are
                  available. Example: (Cyan)

                  /BG, 3

       /DWIDTH    When listing to a disk file, CHASM normally truncates
                  listing lines to 80 columns to prevent wrap-around
                  when viewing the file.  In some instances, such as
                  disk-based print spooling with DOS's PRINT utility,
                  you may wish to override this truncation.  You can
                  enter a new truncation limit after this switch. 
                  Example: (128 column lines)

                  /DWIDTH, 128

        /PATH     Path Stratagy.  Affects the way CHASM constructs the
                  default file names for list and object files.  If
                  /PATH is set to 0 (the default), any drive or path
                  specified on the source file name will be included in
                  the default file names.  If /PATH is set to anything
                  else, path and drive info are removed, thus putting
                  the default list and object files in the current
                  directory of the logged drive.  The following table
                  shows how this works:

                  /PATH | Source filename   | Default object file
                  ------|-------------------|-------------------------
                     0  | a:\chasm\test.asm |   a:\chasm\test.com
                     1  | a:\chasm\test.asm |   test.com



















                                                                      9


                  /PATH only affects how the default file names are
                  constructed - CHASM won't edit filenames that you
                  explicitly type in.

       /TIMER     Enables/Disables reporting of total assembly time. A
                  value of 0 turns off timing, anything else turns it
                  on.  The default is off.  This switch is used
                  internally at Whitman Software to benchmark new
                  versions of CHASM.

      A sample CHASM.CFG file, suitable for use with the IBM dot matrix
      printer, is included on your CHASM distribution disk.



















































                                                                     10

      >>Syntax<<

      CHASM accepts a standard DOS text file for input.  Lines may be
      any combination of upper and lower case characters.  CHASM does
      not distinguish between the two cases: everything except single
      quoted strings are automatically converted to upper case during
      the parsing process.  Thus, BUFFER, Buffer, buffer, and bUFFer
      all refer to the same symbol.

      The characters  blank ( ), comma (,), single quote (')
      semi-colon (;) and TAB are reserved, and have special meaning to
      CHASM (see below).

      Each line must be no more than 80 characters long and have the
      following format:

         Label Operation Operand(s) ;comment

      The different fields of an input line are separated by the
      delimiters blank ( ), comma (,) or TAB.  Any number of any
      delimiter may be used to separate fields.

      Explanation of Fields:

      Label: A label is a string of characters, beginning in column 1.
         Depending on the operation field, the label might represent a
         program location for branching, a memory location, or a
         numeric constant (see the section titled "Labels" for more on
         this topic). To ensure that CHASM can distinguish between
         labels and numeric constants, the first character of a label
         must *not* be a number (0-9), plus sign (+) or minus sign(-).
         Anything beginning in column 1, except a comment, is
         considered a label.

      Operation: Either a pseudo-op (see the section with the same
         name) or an instruction mnemonic as defined in "The 8086
         Book" by Rector and Alexy.  A list of acceptable mnemonics is
         given in Appendix A.

         Note 1: Except as modified below,"The 8086 Book" is the
            definitive reference for use with CHASM.

         Note 2: There are several ways to resolve some ambiguities in
            8086 assembly language.  Please read page 3-285 of The 8086
            Book, and "Resolution of Ambiguities" in this document.



















                                                                     11


      Operand(s): A list of one or more operands, as defined in
         the section titled "Operands", separated by delimiters.

      Comment: Any string of characters, beginning with a semicolon
         (;). Anything to the right of a semicolon will be ignored by
         CHASM.

      Note that except for the case of an operation which requires
      operands, or the EQU pseudo-op which requires a label, all of the
      fields are optional.  The fields MUST appear in the order shown.





















































                                                                     12

      >>Labels<<

      The symbol in the label field of an input line can be interpreted
      in four different ways by CHASM:

        1. A program location which may be branched to.

        2. A memory location for data storage.

        3. An equated symbol, which takes the place of a numeric
           constant.

        4. A macro name, which takes the place of a series of
           frequently used source code lines.

      The default interpretation of a symbol is a program location for
      branching.  This default is modified by the presence of one of
      the following pseudo-ops in the instruction field:

      DB, DM, DS, or DW:

            Normal:  The symbol is a memory location.

            In a Structure: The symbol is a numeric constant.

      EQU:

            Normal:  The symbol is a numeric constant.

            Memory Option:  The symbol is a memory location.

      MACRO: 
           The symbol is a macro name.

      A given symbol may have only ONE of the above interpretations!
      Attempts to branch into a memory location or an equated symbol
      will result in error messages.  Similarly, CHASM will not allow
      you to treat program code as a data area.  Examples:

      TEXT DB  'Hit any key when ready'  ;memory location
           MOV  AL,TEXT                  ;ok
           JMP  TEXT                     ;wrong!
      LOOP MOV  AX,CX                    ;program location
           JMP  LOOP                     ;ok
           MOV  AX, LOOP                 ;wrong!



















                                                                     13


      If for some arcane reason you *need* to branch into a data area,
      you can fool CHASM by placing a label on an otherwise blank line,
      immediately before the data area.  Example:

            JNZ NPU
            RET
      NPU                                ;dummy label for jump
            DB  D8H, 00H                 ;an 8087 instruction

      If you have a masochistic urge to crash your system by writing
      self-modifying code, there are at least two ways you can defeat
      CHASM's injunction against using program code as a data area.

      The first way is to use DS to declare zero bytes of storage
      immediately before the code you want to access.  A label on the
      null DS will have the same offset as the immediately following
      code.  Example:

             MOV   JUNK1, 9090         ;change endless loop to NOP
      JUNK1  DS    0
      JUNK   JMP  JUNK

      A sneakier approach is to load the OFFSET of a program
      location into a register, then use the register for indirect
      addressing. Using the optional displacement field, you can even
      address the middle of an instruction.  Examples:

             MOV   BX, OFFSET(CALL)
             MOVB  1[BX], 00H          ;change interrupt number in code
      CALL   INT   0

      In general, I cannot recommend trying to get around CHASM's type
      restrictions.  If you find yourself in a situation where it
      seems necessary to fool CHASM, there's probably a safer, more
      direct way to legally program what you're trying to accomplish.

      Labels can be up to 80 characters long, but only the first 15
      characters are significant.  For example, CHASM considers the
      following labels identical:

         VERYLONGLABELOVER15CHARACTERS
         VERYLONGLABELOVER





















                                                                     14

      To avoid ambiguity, a given string can legally appear in the
      label field of only ONE statement.  If the same string appears on
      more than one instruction, all instances after the first will
      receive an error message.  Remember that labels are only
      significant to 15 characters, and if the first 15 characters are
      identical, an error will occur.

      TWO   EQU  '2'      ;first use is ok
      TWO   PROC FAR      ;wrong! symbol already defined

      CHASM has a number of reserved strings which are "predefined" in
      the symbol table, and will generate an error message if used as
      labels.  All the two letter register names are reserved, as are
      the indirect address mode combinations.  The only other reserved
      strings are the words "NEAR" and "FAR", and the symbol "$".
      Examples:

      AX   MOV  AX, DX      ;wrong! (register name)
      [DI] ADD  AX, BX      ;wrong! (indirect address)
      FAR  CALL GETINPUT    ;wrong! (reserved word)
      $    SUB  AX, DX      ;wrong! (reserved word)











































                                                                     15

      >>Operands<<

      The following operand types are allowed.

      1. Immediate data: A number, stored as part of the program's
         object code.  Immediate data are classified as either byte,
         expressible as an 8 bit binary integer; or word, expressible
         as a 16 bit binary integer.  If context requires it, CHASM
         will left-pad byte values with zeroes to convert them to word
         values.  Attempts to use a word value where only a byte will
         fit will cause an error message to be printed.

         Immediate data may be represented in 9 ways:

            A. An optionally signed decimal number in the range -32768
               to 32767.  Examples:

               MOV AL,21
               MOV BX,-6300

            B. A series of up to 4 hex digits, followed by the letter
               H.  The first digit must be non-alphabetic, i.e. in the
               range 0-9, to allow CHASM to distinguish between numbers
               and symbols. If necessary, a leading zero, which does
               not count in the four allowed digits, may be added to
               fulfill the non-alphabetic condition. Examples:

               ADD CX, 0B123H
               ADD DL, 12H

           C.  A series of up to 16 binary digits, followed by the
               letter B.  Examples:

               MASK   EQU   00000111B
                      MOV   AL, 10000000B


            D. A symbol representing types A, B or C above,
               defined using the EQU pseudo-op.  Examples:

               MASK EQU 10H
               MAX  EQU 1000
                    AND  CL,MASK
                    SUB  AX,MAX




















                                                                     16

            E. The offset of a label or storage location returned by
               the OFFSET operator.  OFFSET always returns a word
               value. OFFSET is used to get the address of a named
               memory location, rather than its contents.  Example:

                      MOV DI,OFFSET(BUFFER)
               BUFFER DS  0FFH

            F. The ASCII value of a printable character, represented by
               the character enclosed in single quotes (').  Thus, the
               following lines will generate the same object code:

                  MOV AL,41H  ;ascii code for 'A'
                  MOV AL,'A'

            G. ==>Advanced version only:
               Labels within structures become immediate operands whose
               values equal their offset within the structure.  See the
               section titled "Structures" for more detail and
               examples.

            H. ==>Advanced version only:
               The length of a structure, returned either by the LENGTH
               operator, or simply the structure's name.  See the
               section titled "Structures" for more detail and
               examples.

            I. The number of bytes counted by the COUNT pseudo-op,
               returned by the LENGTH operator on the COUNT's label.
               Example:

               HLP_MSG   COUNT
               HLP_TXT   DB 'Hit F10 for Help...' cr lf
                         ENDC
                         MOV CX, LENGTH(HLP_MSG)  ;length of message

            J. ==>Advanced version only:
               An expression that evaluates out to type Immediate.
               Examples:

                      MOV AX, (3+2)*5 
                      MOV DX, MEMLOC1-MEMLOC2

               See the "Operand Expressions" section for more details.




















                                                                     17

      2. Register Operands: One of the 8088's internal registers.

         A. An 8 bit register from the following list:
            AH    AL
            BH    BL
            CH    CL
            DH    DL

         B. A 16 bit register from the following list:
            AX   BX   CX   DX   SP   BP   SI   DI

         C. A segment register from the following list:
            CS   SS   DS   ES

      3. Memory Operands: The contents of a memory location addressed
         by one of the following methods.  Note that none of the memory
         addressing options specifies whether a byte or word operand
         is being referenced.  See the section titled "Resolution of
         Ambiguities" for more on this topic.

         All memory operands can optionally be proceded with a segment
         overide to specify the segment register to be used in
         accessing memory.  The overide takes the form of a segment
         register, followed by a colon, followed by the memory operand.
         No intervening delimiters are allowed.  Examples:

              MOV AX, ES:[80H]    ;80H into the extra segment
              MOV CS:[DI], SI     ;indirect with DI in the code segment

         Segment overides are also discussed in the section titled
         "Resolution of Ambiguities".

         A. Direct address.

            1. A number, or other immediate operand, enclosed in
               brackets, indicating an offset into the data segment.
               Example:

               BUFFER EQU 5A5AH
                      MOV BH,[BUFFER]
                      MOV [80H],DI























                                                                     18

            2. A symbol, defined to be a variable (i.e. a named memory
               location) using the EQU pseudo-op.  Example:

               FCB EQU [80H]
                   MOV DI,FCB

            3. A symbol, defined to be a variable by its use on a
               storage defining pseudo-op.  Examples:

                    MOV AX,FLAG
                    MOV DATE,BX
               FLAG DS 1
               DATE DB 31

            4. The special symbol '$'.  $ returns an address of value
               equal to the current setting of CHASM's location
               counter.  This address can be used as either a memory
               location, or a program location for branching.  Used by
               itself, $ has little utility, but it is a very powerful
               tool when used in expressions.  Example:

                    MOV AX, $+4    ;get the byte after this instruction

            5. ===> Advanced version only:
               An expression that evaluates out to type address.
               Example:

                      MOV AX, buffer+3
               BUFFER DS 20

               See the "Operand Expressions" section for more details.

         B. Indirect Address:  The address of the operand is the
            sum of the contents of the indicated register(s) and a
            displacement.  The register, or sum of registers, are
            enclosed in square brackets: []

            The displacement is optional, and takes the form of an
            immediate operand, placed without intervening delimiters to
            the left of the first bracket.

            Immediate data written as decimal numbers, with values
            between 127 and -128 generate a signed 8 bit offset.
            Values outside this range, or those expressed in some
            other manner generate 16 bit offsets.



















                                                                     19


            The following indirect modes are provided:

            1. Indirect through a base register (BX or BP).  Examples:

               ENTRYLENGTH EQU 6
                           MOV AX, ENTRYLENGTH[BP]
                           MOV DL, -2[BX]
                           MOV CX, [BP]
                           MOV 9A9AH[BX], AX

            2. Indirect through an index register (DI or SI).
               Examples:

               MOV [DI], CX
               MOV CX, -5[SI]

            3. Indirect through the sum of one base register and one
               index register.  Examples:

               MOV [BP+DI], SP      ;note that no spaces are
               MOV BX, 10H[BX+SI]   ;allowed within the
               MOV CL, [BP+SI]      ;brackets.
               MOV DH, -2[BX+DI]

      4. Labels

         A label on most instructions may be used as an operand for
         call and jump instructions.  See the section titled "Labels"
         for more information.  Examples:

         START    PROC NEAR
                  CALL GETINPUT
                  JMPS START
                  ENDP
         GETINPUT PROC NEAR

      5. Strings

         A string is any sequence of characters (including delimiters)
         surrounded by single quotes (').  Example:

         DB 'Copyright May 15,1982'





















                                                                     20

      >>Operand Expressions<<

      ===> Advanced version only.

      Advanced CHASM can perform arithmetic calculations at assemble
      time, to help you generate memory addresses and immediate data
      constants.

      The following operand types can participate in operand
      expressions: 

           immediate data
           program locations
           data storage locations

      Actually, for the purpose of expression evaluation, CHASM treats
      both program locations and data storage locations identically.
      Thus, really only two types of operands are allowed in
      expressions: immediate and address.

      Symbols standing for immediate operands must have been defined
      prior to use in an expression, or you may get Phase Errors (see
      the error message section for a discussion on this topic).  You
      should put all your EQU and STRUC pseudo-ops at the beginning of
      your program, before any machine instructions.

      The following arithmetic operators are available:

           +  addition
           -  subtraction
           *  multiplication
           /  integer division

      Note that / performs *integer* division.  5/2 evaluates to 2.

      The normal rules of precedence apply.  To force evaluation
      contrary to normal precedence, you can use parenthesis: ().

           MOV AX  2+5*3   ;means mov ax, 17 because * outranks +
           MOV AX, (2+5)*3 ;means mov ax, 21
























                                                                     21

      No delimiters can appear within an expression.  If you separate
      the parts of an expression with delimiters, CHASM will try to
      interpret each part as a separate operand.

           MOV [BX], BUFFER + 3    ;WRONG!!
           MOV [BX], BUFFER+3      ;ok

      The type of an operand expression is determined by the individual
      operand types that are combined within it.  In evaluating each
      operation in an expression, the result type follows this rule:

           If the two operand types are the same, the result type is
           IMMEDIATE.

           If the two operand types are different, the result type is
           an ADDRESS.

      In expressions, both program locations and data storage locations
      are considered identical.  An expression which evaluates to type
      address can be used in either a MOV or a JMP.

      The result type of a complicated expression is determined by
      replacing individual binary operations with their result, and
      evaluating the (simpler) expression thus formed, following the
      above rules.

      Here's a program fragment with some expressions, and a discussion
      of their types and significance:

      EXPSAMPLE PROC  NEAR
                MOV   AX, 3+5         ;immediate, calculated value
                MOV   DX, STRING-END  ;immediate, length of string
                MOV   STRING+5, 'A'   ;address, third byte of string
                JMP   EXPSAMPLE+100H  ;address, used as program loc.
                JMP   STRING+100H     ;valid address syntax, but silly
      STRING    DB    'MESSaGE'       ;data area
      END                             ;marks position of end of string


      The special symbol '$' returns the current value of CHASM's
      location counter for use in expressions.  $ is of type address.
      Thus, $-1 is the address of the byte immediately prior to the
      instruction currently being assembled.





















                                                                     22

      The rules for typing expressions were set up to produce the
      "most useful" result type, taking a guess as to why one would
      want to do a given calculation.  If the type isn't what you have
      in mind, you can coerce CHASM using square brackets or the
      OFFSET function:

            MOV AX, 3+5              ;immediate
            MOV AX, [3+5]            ;coerced to address
            MOV DX, $+4              ;address
            MOV DX, OFFSET($+4)      ;coerced to immediate

      Under certain circumstances, CHASM can get confused when you use
      OFFSET or LENGTH functions in expressions.  The problem occurs if
      the expression starts with a function, and ends with a close
      parenthesis:

            MOV AX, OFFSET(BUFFER)*(3+2)    ;will be misinterpreted

      CHASM will try to interpret this as the offset of "BUFFER)*(3+2",
      and you'll get the error message "Illegal or undefined argument
      for OFFSET".  The solution is to enclose the whole works in
      parenthesis, to force CHASM to recognise it as an expression:

            MOV AX, (OFFSET(BUFFER)*(3+2))  ;correct








































                                                                     23

      >>Resolution of Ambiguities<<

      The language defined in "The 8086 Book" contains a number of
      ambiguities which must be resolved by an assembler.  This is
      discussed throughout the book, but pages 3-285 and 3-286
      specifically cover this topic.  CHASM's solutions of these
      problems are discussed in this section.

      A. Memory references:

      When one specifies the address of a memory location, it is
      unclear how large an operand is being referenced.  An operand
      might be a byte, or a word.

         1. If a register is present as an operand, it is assumed that
            the memory operand matches the register in size.  An
            exception to this rule are the shift and rotate
            instructions, where the CL register is used as a counter,
            and has nothing to do with the size of the other operand.
            Examples:

            MOV MASK,AX   ;mask is a word
            MOV DH,[BX]   ;BX points to a byte
            NEG [SI]      ;error, operand of unknown size
            SHR FLAG,CL   ;error, flag is of unknown size

         2. If no register is present, (or if the only register is CL
            being used as a counter) the size of the memory operand is
            specified by adding the suffix "B" or "W" to the
            instruction mnemonic.  Examples:

            NEGB [SI]       ;SI points to a byte
            SHRW FLAG,CL    ;flag is a word
            MOVW MASK,0AH   ;mask is a word
            MOVB MASK,0AH   ;mask is a byte
            MOVW MASK,9A9AH ;must specify size even though
                            ;immediate operand implies word
            MOVB DH,[BX]    ;error(!), register already
                            ;specifies size

























                                                                     24

      B. Indirect Branching.

      The 8088 supports two flavors of indirect branching: intra, and
      intersegment.  A register is set to point at a memory location
      which contains a new value for the program counter, and in the
      case of intersegment branching, a new value for the CS register
      as well.

      The syntax of "The 8086 Book" does not specify which flavor of
      branch is being invoked.  CHASM adds the suffixes "N" (for near,
      or intrasegment) and "F" (for far, or intersegment) to the
      indirect CALL and JMP mnemonics.  Examples:

         CALLN [BX]    ;intrasegment call
         JMPF  [DI]    ;intersegment jump
         JMP   [BP]    ;error, unspecified flavor

      C. Long and Short Jumps

      Two types of relative jumps are supported by the 8088: short
      (specified by a signed 8 bit displacement) and long (specified by
      a 16 bit displacement).  Both are implemented in CHASM as a jump
      to a label.

      The short jump is specified by mnemonic JMPS, in accord with the
      IBM disassembler, but not with The 8086 Book, which uses JMP.
      Since one of the displacement bits is used to indicate direction,
      only seven are left to express the magnitude of jump.  JMPS (and
      similarly, all the jump on condition instructions) is thus
      limited to branching to labels within a range of -128 to +127
      bytes.

      CHASM reserves mnemonic JMP for the long jump.  JMP may be used
      to jump anywhere within the program segment, but the object code
      generated is less compact than that from JMPS.

      Examples:

         START PROC NEAR
               JMPS END     ;short jump
               JMP  START   ;long jump
         END   ENDP






















                                                                     25

      D. Instruction Prefixes.

      The 8088 supports three instruction prefixes:

         1. SEG: segment override. An alternate segment register is
            specified for a reference to memory

         2. REP, REPE,REPNE,REPZ,REPNZ: repeat. A string primitive is
            repeated until a condition is met.

         3. LOCK: Turns on the LOCK signal. Only useful in
            multi-processor situations.

      SEG is implemented as a modifier attached to a memory operand.
      If you want to overide the default segment register for a memory
      access, precede the memory operand with the segment register
      followed by a colon.  Examples:

         MOV AX, ES:FLAG     ;flag is in the extra segment
         MOV CS:[100H], DX   ;offset 100H in the code segment

      The other prefixes are implemented as separate instructions. They
      appear on a separate line, immediately before the instruction
      which they modify.  For compatability with earlier versions of
      CHASM, you can also specify segment overides on a separate line,
      using the mnemonic SEG. Examples:

         REP
         MOVSB           ;move bytes until CX decremented to 0
         SEG SS
         MOV AX,BUFFER   ;buffer is in the stack segment
         LOCK
         MOV [8FFH], AX  ;lock bus to ensure data is transferred
                         ;before other processors try to access it

      Note for 8087 users:  You may get unexpected results using the
         separate instruction form of SEG on 8087 instructions.  Use
         the operand modifier form for segment overides on 8087
         instructions.

      (CHASM version 4.01 will have 8087 support)























                                                                     26

      >>Pseudo-Operations<<

      The following pseudo-ops are implemented:

      A. BSAVE: Generate object code in BSAVE format.

         Instructs CHASM to build a header in the format of BASIC's
         BSAVE command.  The resulting object code file may be BLOADed
         by BASIC programs.  No operands are required, and the
         pseudo-op may appear anywhere within the source code.
         Example: 

               ORG    0     ;no psp
         SUBRT PROC   FAR   ;subroutine for BASIC program
               BSAVE        ;make BLOADable object file

      B. COUNT ...ENDC:  Count bytes.

         Instructs CHASM to count the number of object code bytes
         generated between COUNT and ENDC.  Both machine instructions
         and pseudo-ops can appear within the COUNT block. If a label
         appears on the COUNT, it becomes an immediate operand of value
         equal to the number of bytes counted.  Neither COUNT or ENDC
         require any operands.  COUNTs cannot be nested.

         (COUNT and ENDC are supported mainly for compatibility for
         earlier releases.  Now that expressions are available, you can
         get exactly the same result by subtracting two labels, one on
         either side of the area to be COUNTed.)

         It is *strongly* recommended that the immediate operands
         generated by COUNT be accessed via the LENGTH function, which
         unambiguously forces the "immediate" type on CHASM's first
         pass.  If you do not use the LENGTH function, forward
         references to a COUNT may cause phase errors.  (See Phase
         Error in the Error Message section.)

         Example: (next page)


























                                                                     27

         MESSAGE    COUNT
         MSG_TXT    DB   'This utility requires DOS 2.0!' beep cr lf
                    ENDC

                    MOV SI, OFFSET(MSG_TXT)
                    MOV DI, OFFSET(BUFFER)
                    MOV CX, LENGTH(MESSAGE)
                    REP
                    MOVSB                   ;move message into buffer

      C. DB: Declare Bytes

         Memory locations are filled with values from the operand list.
         Any number of operands may appear, but all must fit on one
         line. Acceptable operands are immediate data, or strings
         enclosed in single quotes (').  DB interprets strings as a
         series of ASCII bytes.

         If a label appears, it is redefined as a memory location, and
         the data area may be referred to using the label, rather than
         an address. Examples:

               MOV AX,MASK
         MASK  DB  00H,01H
         STG   DB  'A string operand'

         CHASM generates an error message ("Data too large") if word
         operands (such as OFFSETs, or numbers greater than 255) are
         found in the DB operand list. DW should be used for declaring
         words.

      D. DM: Declare Multiple Bytes

         Used to declare blocks of storage, the number of bytes
         declared being the product of two immediate operands.  If only
         one operand is present, the other operand is assumed to equal
         one.

         (DM is supported mainly for compatibility with earlier
         releases.  Now that expressions are available, you can
         accomplish the thing by using DS with an expression for the
         immediate operand.)






















                                                                     28

         As with DB, any label is redefined as a memory location.  To
         save space, the object code does not appear on the listing.
         It is anticipated that this pseudo-op will be used in
         conjunction with STRUC, to declare structured storage.
         Example:

            DM  LENGTH(MAILIST) 500   ;mailing list with 500 entries

      E. DS: Declare Storage

         Used to declare large blocks of identically initialized
         storage.  The first operand is required, a number specifying
         how many bytes are declared.  If a second operand in the form
         of a number 0-FFH appears, the locations will all be
         initialized to this value.  If the second operand is not
         present, locations are initialized to 0.   As with DB, any
         label is redefined as a memory location.  To save space, the
         object code does not appear on the listing.  Examples:

            DS 10         ;10 locs initialized to 0
            DS 100H,1AH   ;256 locs initialized to 1AH

      F. DW: Declare Words

         Used to unambiguously assign a word of storage for each item
         in the operand list.  Any number of immediate operands may
         appear, but all must fit on one line.  As with DB, any label
         is redefined as a memory location. Example:

             DW 0012H, FFFFH       ;four bytes declared

      G. EJECT: Begin New Print Page

         When listing is enabled, causes CHASM to move to the top of
         the next page in printed listings.  Has no effect on listings
         sent to the screen or to disk.




























                                                                     29

      H. EJECTIF: Conditional Page Break

         Requires one immediate operand.  If listing is enabled
         and fewer than that many lines are left on the current page of
         a printed listing, CHASM will move to the top of the next
         page.

         If you put an appropriate EJECTIF at the beginning of each
         procedure or section of your programs, CHASM will keep them in
         one piece.  Like EJECT, EJECTIF has no effect on listings to
         the screen or disk.  Example:

             EJECTIF 20    ;following procedure is 20 lines long

      I. ENDC: End of Count

         See COUNT (above) for details.

      J. ENDP: End of Procedure

         See PROC (below) for details.

      K. ENDSTRUC: End of Structure

         ==>Advanced version only.  See STRUC (below) for details.

      L. EQU: Equate

         Used to equate a symbolic name with a number. The symbol may
         then be used anywhere the number would be used.  Use of
         symbols makes programs more understandable, and simplifies
         modification.

         An alternate form of EQU encloses the number in square
         brackets: []. The symbol is then interpreted as a memory
         location, and may be used as an address for memory access.
         This version is provided to allow symbolic reference to
         locations outside the program segment. Examples:

            MOFFSET    EQU 0B000H
            MONOCHROME EQU [0000H]























                                                                     30

         Warning: Difficult to debug errors may result from using a
         ======>  symbol prior to its being defined by EQU.  You are
                  strongly urged to group all your equates together at
                  the beginning of programs, before any other
                  instructions. See "Phase Error" in the Error Message
                  section.

      M. IFXX... [ELSE]... ENDIF: Conditional Assembly

         ===> Advanced version only.

         CHASM's conditional assembly pseudo-ops can be used to cause
         macros to expand differently according to the parameters
         supplied on the invocation.  Eight different IF pseudo-ops are
         provided, to allow testing for (in)equality, relative size,
         and (non)existence of parameters.

         For more details and examples, see the Macro section of this
         document.

      N. INCLUDE: Include file

         ==>Advanced version only.

         INCLUDE requires one string operand, a filename enclosed in
         single quotes.  If desired, you can specify a drive and/or a
         path as part of the filename.

         The contents of the specified file are logically inserted into
         the source file at the point where the INCLUDE appears.
         INCLUDEs cannot be nested: an error message will be printed if
         the specified file itself contains an INCLUDE.  Example:

             INCLUDE '\ASM\STDIO.HDR'    ;bring in standard library

      O. LIST: Enable listing output

         Output to the list device is enabled, presumably after a
         NOLIST was encountered.  No operands required.

























                                                                     31

      P. MACRO ...ENDM: Macro Definition

         ==> Advanced version only.

         Declares a macro.  MACRO requires no operands, and signals
         CHASM that the following lines constitute a macro definition,
         and are to be stored for later use, rather than assembled in
         place.  A label is required on the MACRO statement to name the
         defined macro.

         ENDM terminates the macro definition, and requires no
         operands.

         For more information and examples, see the section titled
         "Macros".

      Q. NOLIST: Disable listing output

         Normal output to the list device is disabled.  Error messages
         are listed as usual.  No operands required.

      R. ORG: Origin

         Allows direct manipulation of the location counter during
         assembly.  By default, CHASM assembles code to start at offset
         100H, thus leaving room for the program segment prefix
         normally built by COMMAND or DEBUG.  In situations where no
         PSP is provided, such as routines to be called from BASIC, you
         should override this default with ORG, or incorrect assembly
         may result.

         ORG requires one operand, a number between 0 and FFFFH, which
         represents the new setting of CHASM's location counter.
         Although the location counter may be reset anywhere within a
         program, generally this pseudo-op should be used before any
         machine executable instructions for meaningful results.

         Example:

           ORG 0   ;Code will be assembled for starting
                   ;offset of 0























                                                                     32

      S. PROC ...ENDP: Procedure Definition

         Declares a procedure.  One operand is required on PROC, either
         the word NEAR, or the word FAR.  This pseudo-op warns CHASM
         whether to assemble returns as intra (near) or intersegment
         (far).  Procedures called from within the program being
         assembled should be declared NEAR.  Generally, all others
         should be FAR.  ENDP terminates the procedure, and requires no
         operands.  If a RET is encountered outside of a declared
         procedure, an error occurs.  Procedures may be nested, up to
         10 deep.  Example:

         MAIN  PROC  FAR
               ...
               ...      ;body of procedure
               ENDP

      T. STRUC ...ENDSTRUC: Structure Definition

         ==> Advanced version only.

         Declares a structure.  STRUC requires no operands, and signals
         CHASM that the following lines constitute a structure
         template, and not actual storage declaration.  If a label
         appears on the STRUC, the label is equated with the length of
         the structure.

         ENDSTRUC terminates the structure definition, and requires no
         operands.

         Inside the structure, storage defining pseudo-ops behave
         somewhat differently.  See the section titled "Structures" for
         more information. Example:

             DIRENTRY STRUC      ;disk directory entry
             NAME     DS    8
             EXT      DS    3
             ATRIB    DS    1
             RESERVED DS   10
             TIME     DS    2
             DATE     DS    2
             START    DS    2
             SIZE     DS    4
                      ENDSTRUC




















                                                                     33

      >>Macros<<

      ==>Advanced version only.

      Macros are an advanced feature.  Beginners may wish to skip this
      section until they become more experienced with CHASM and
      assembly language programming.

      A. Introduction

         Macros are a shorthand way of writing frequently used
         sections of code.  Using macros, you can write a code fragment
         once, then any time you want to use it, just reference it by
         name.  Once you define a macro and give it a name, anywhere
         CHASM sees the name will be automatically "expanded" into the
         previously defined code.

         For example, suppose you were writing a large program, and at
         the beginning of each subroutine you pushed all the general
         purpose registers onto the stack to save their contents.
         Every subroutine would start out something like this:

               push ax       ;save register contents
               push bx
               push cx
               push dx

         Before long, you'd get pretty sick of writing the same thing
         for each subroutine.  Macros are a way to put some of the
         boring, repetitive nature of assembly language into the hands
         of the assembler, freeing you up for the more creative
         aspects.  Here's how you define a CHASM macro to take the
         place of this code fragment:

         savestate  macro
                    push ax           ;save general purpose registers
                    push bx
                    push cx
                    push dx
                    endm
























                                                                     34

         Note the MACRO and ENDM statements.  These signal to CHASM
         that the enclosed code is a macro definition to be saved for
         later use, rather than code to be assembled at this point in
         your program.  The MACRO statement also gives a name
         (SAVESTATE) to the macro, which will take the place of the
         stored code.

         Now, at the beginning of each subroutine you can just write
         "SAVESTATE" when you want to push the general purpose
         registers. Here's an example:

         get_input  proc  near
                    savestate
                    ...
                    ...
                    endp

         Given the previous macro definition, the above example is
         *exactly* equivalent to:

         get_input  proc  near
                    push ax
                    push bx
                    push cx
                    push dx
                    ...
                    ...
                    endp

         The only difference is that less busy work is required on your
         part.

         Macros are NOT subroutines!  Subroutines are coded once, then
         called within your program at run time.  Macros are expanded
         in-line at assembly time, and the code is inserted into your
         program at the invocation point.  If you invoke the macro 20
         times in your program, you'll end up with 20 copies of the
         macro code. 


























                                                                     35

         Although this does waste some memory space, you save execution
         time by eliminating the subroutine call and return process.
         At a minimum, it takes 32 machine cycles to call a subroutine.
         The four instruction macro given above requires 40 cycles to
         execute.  If it were coded as a subroutine, the time to
         execute it would almost *double*.  Macros trade off space for
         speed.

      B. Macro Parameters

         CHASM's macros allow 9 user defined parameters, which are
         evaluated at expansion time.  The parameters work just like
         those in DOS batch files.  Here's an example of a macro with
         one parameter.  PRINT calls DOS function 9 to print a string
         on the console.  A parameter is used to specify the name of
         the string to be printed:

         print    macro
                  mov  ah, 09H          ;specify print string function
                  mov  dx, offset(%1)   ;point to string
                  int  21H              ;call DOS
                  endm

         Given this definition, when CHASM sees a line like:

               print title

         The following code gets inserted in its place:

               mov  ah, 09H
               mov  dx, offset(title)
               int  21H

         Note how the "%1" in the macro definition got replaced by
         "title" which was put as an operand on the invocation of the
         macro.  You can put up to 9 operands onto a macro invocation,
         and they will be substituted for the dummy parameters %1
         through %9.


























                                                                     36

         If you put a label on a macro invocation, two things happen.
         As usual, the label represents a program location for
         branching, with offset equal to the beginning of the expanded
         macro.  You can branch into the expanded macro by using the
         label as an operand on a jump or call instruction.  In
         addition, if the special dummy parameter "%0" is used in the
         macro definition, it is replaced with the label text when the
         macro is expanded.  This feature is provided to facilitate
         writing loops within macros.

         If you fail to provide an operand for any dummy parameter used
         in the macro definition, CHASM substitutes a null string of
         length zero.  To leave one parameter blank, but provide
         replacements for parameters with higher numbers, use the
         special operand "%B" for the one you want blank.  For example:

              def_mem  macro
              %1       db  %2, %3
                       endm

                       def_mem twobytes, 128, FFH
                       def_mem %B, 'Hit any key when ready...'

         Expands to:

              twobytes  db 128, FFH
                        db 'Hit any key when ready...'

      C. Macro Nesting

         Macro invocations can be nested, up to 10 deep.  Invocations
         are maintained on a stack, and each invocation has it's own
         set of parameters.

         CHASM does not check for recursive macro calls.  If you call a
         macro from within itself, it's quite possible to get caught in
         an endless loop.  This can also happen indirectly, where a
         macro invokes another macro, which ends up calling the first.
         If you get caught, you can escape by hitting Ctrl-Break.

         Experienced programmers can use macro recursion, along with
         expressions and conditional assembly, to create some really
         elegant macros.  However, this is definitely not for beginners
         or the faint of heart.  Enter at your own risk.




















                                                                     37

      D. Conditional Macro Expansion

         This advanced feature allows you to write general purpose
         macros which expand in different ways based on the parameters
         used on the invocation.

         For example, suppose you wanted to write a macro to do
         operating system calls.  Many of the DOS functions just load
         the function number into AH, then call DOS with an interrupt.
         Here's a macro to do this:

         doscall  macro
                  mov ah, %1
                  int 21H
                  endm

         Given the above definition, "DOSCALL 1" will expand into a
         call to DOS function #1, keyboard input.

         Unfortunately, not all DOS calls are quite so simple.  For
         example, the call for printing a string to the console
         requires that the offset of the string be loaded into DX.
         Different system calls are going to require somewhat different
         handling.  One approach would be to write separate macros for
         each function.  However, with 87 different functions in DOS 2,
         this starts to get unwieldy.

         A more general approach is to incorporate some "intelligence"
         into the macro, and let it expand differently for different
         DOS functions.  Here's a slightly more general macro, which
         loads DX whenever the "print string" function is requested:

         doscall  macro
                  mov ah, %1
                  ife %1 9
                     mov dx, offset(%2)
                  endif
                  int 21H
                  endm

























                                                                     38

         "IFE" is short for "If Equal".  The "IFE" and "ENDIF" bracket
         a line of macro code which will be included during expansion
         only if the "IFE" statement is satisfied.  In this example,
         the MOV DX statement will be included only if the first
         parameter is equal to 9.  The enclosed line is indented in
         this example to help show the structure of the macro, but
         indentation is not required.

         Given the above definition, "DOSCALL 1" expands to only two
         lines:

            mov ah, 1
            int 21H

        However, "DOSCALL 9, STRING" expands to three lines:

            mov ah, 9
            mov dx, offset(string)
            int 21H

         CHASM supports eight different conditional test statements.
         They are:

              IFE     "if equal"
              IFNE    "if not equal"
              IFGT    "if greater than"
              IFGE    "if greater than or equal"
              IFLE    "if less than or equal"
              IFLT    "if less than"
              IFB     "if blank"
              IFNB    "if not blank"

         Most of the conditionals take two operands, and perform a
         comparison.  The operands are evaluated, and their values are
         compared according to the condition being tested.  Strings are
         compared in the normal alphabetical order sense.  Examples:

              IFE   15, 0FH       ;is true
              IFGT  'ABCD' 'EFGH' ;is false
              IFLE  20H, 128      ;is true

         IFB and IFNB require only one operand, which should be a dummy
         parameter.  These conditionals test whether the parameter was
         left "blank" or if a replacement was provided on the
         invocation.



















                                                                     39


         You can place as many lines as you like between an IF
         statement and the ENDIF.  All will be included if the
         condition tested is true, and none will be included if it's
         false.

         An optional "ELSE" construct is also provided.  Statements
         after the ELSE get included only if the tested condition is
         false. CHASM's conditional assembly syntax can be summarized
         as follows:

             IF.....            ;if statement with parameter(s)
               s1                  ;statements included if true
               s2                  ;    "         "      "   " 
             ELSE               ;end of "true" option, begin "false"
               s3                  ;statements included if false
               s4                  ;    "         "      "   "
             ENDIF              ;end of conditional assembly

         IF statements can be nested, up to 10 deep.  During
         nesting, CHASM assumes that ELSEs are paired with the
         latest unfinished IF statement.  For example:

         example macro
                 ife %1, 1
                    db 'Outer IF is true'
                    ifb %2
                       'Inner IF is true'
                    else
                       'Where do I belong?'
                    endif
                 endif

         "EXAMPLE 1, 5" expands to:

                db 'Outer IF is true'
                db 'Where do I belong?'

         But "EXAMPLE 2" produces no expansion at all.

         This is easiest to follow if you use "structured" indenting
         when writing the macro, as in the example above. Remember,
         however, that CHASM ignores indenting and follows the
         "latest unfinished" rule in figuring out which IF gets the
         ELSE.  Don't fool yourself with improper indentation.



















                                                                     40


      E. Final Notes:

         The conditional assembly pseudo-ops are not restricted to use
         only in macros, although there aren't that many useful
         non-macro applications.

         CHASM won't recursively expand parameters.  If you use a dummy
         parameter symbol as an operand on a macro invocation, the
         expanded macro contains the dummy parameter symbol, NOT the
         indirectly referenced replacement text.

         Like equates and structures, macro definitions should all be
         placed at the beginning of your programs, before the macro
         gets invoked.  If you invoke a macro before it's defined, a
         phase error will occur.

         Macro definitions are stored and expanded blindly by CHASM,
         with no syntax checking.  Dummy parameter symbols can appear
         in any of the input line fields.  Any errors in a macro
         definition will only become evident when CHASM expands the
         macro and attempts to assemble the result.

         In keeping with the "shorthand" philosophy of macros, the
         results of macro expansion don't normally appear on the
         listing.  If you want to see the expansion for debugging
         purposes, insert a LIST pseudo-op as the first line of the
         macro definition.

         Once you start writing macros, you might find it useful to
         gather them together into a single file.  You can then pull
         this file into the beginning of all your programs with an
         INCLUDE pseudo-op.  Macros which don't get invoked won't add
         anything to the object code produced, and you'll save yourself
         the trouble of typing in the ones you *do* need.  If you put a
         NOLIST at the beginning and a LIST at the end of your INCLUDE
         file, you don't even have to look at the definitions on your
         listings.


























                                                                     41

      >>Structures<<

      ==>Advanced version only.

      Structures are an advanced feature.  Beginners may wish to skip
      this section until they become more experienced with CHASM and
      assembly language programming.

      CHASM's structure capability allows you to generate a "template"
      with which to organize repetitive data structures.  As an example
      of a repetitive data structure, consider a phone list.  Each
      entry in the list has three components:

           Name    - 20 characters
           Address - 50 characters
           Phone   - 10 characters

      Each entry thus uses a total of 80 bytes of storage.  To declare
      a list with 500 entries, you would declare 80 x 500 = 4000 bytes:

           PHONELIST  DS  4000   ;500 entries @ 80 bytes/entry

      That's easy enough, but now what's the offset of the 346th
      address field?  This is starting to get confusing, and time
      consuming to figure out.

      Furthermore, hard-coding numbers (like that 4000, above) into a
      program is never a good idea.  What's going to happen when you
      decide to add a zip code field, or make more room in the name
      field because you just met Alexandria Zbrievskivich?  You'd have
      to go through and change by hand each number which depended on
      the actual layout of your data.  Murphy's law guarantees that
      it'll take somewhere between "several" and "too many" assemblies
      to find them all.

      Structures allow you to set up a symbolic template which makes it
      much easier to manage structured data like this phone list.  By
      using symbols defined in the structure, rather than bare numbers,
      a change in data structure doesn't mean a frantic search
      throughout your entire program to make corrections.  If you
      change the structure definition, the symbols take on new values
      automatically.






















                                                                     42

      Here's what the phone list structure looks like:

           LISTENTRY  STRUC
           NAME       DS 20
           ADDRESS    DS 50
           PHONE      DS 10
                      ENDSTRUC

      Note the STRUC and ENDSTRUC statements.  They mark the beginning
      and end of the structure, and give it a name (LISTENTRY).

      Within the structure are storage defining pseudo-ops.  DS is used
      in this example, but DB, DW, and DM could also be used.  ORG can
      be used within a structure, but any 8088 instruction will result
      in an diagnostic message and termination of the structure
      definition.

      Inside a structure, the storage defining pseudo-ops
      behave somewhat differently than normal.  No actual storage is
      set aside, but CHASM keeps track of how much space would normally
      be declared.

      Labels on pseudo-ops get assigned values equal to their offset
      within the *structure*, not within the program as a whole.  Also,
      CHASM will treat the labels as immediate operands, rather than
      memory locations.  The result of the structure given above is to
      generate three immediate operands, with the following values:

           NAME    =  0
           ADDRESS = 20
           PHONE   = 70

      CHASM does one other piece of useful book-keeping during
      structure definitions.  If a label appears on the STRUC
      pseudo-op, it gets treated as an immediate operand, whose value
      is equal to the total length of the structure.

      You can either use the STRUC label directly as an operand, or if
      you like "pretty" code, use the LENGTH operator on it.  In this
      example, both LISTENTRY and LENGTH(LISTENTRY) are immediate
      operands of value 80.

      (Inside note: LENGTH is a null operator, provided mainly for
      aesthetic reasons.  Using LENGTH will often make your code more
      readable, but is equivalent to using just the label itself.)



















                                                                     43


      Like equates and macros, structures should be placed at the
      beginning of your programs before any machine instructions,
      otherwise phase errors can occur.  If you *do* embed structures
      inside your program, you can eliminate any phase errors by using
      the LENGTH function to reference any of the immediate operands
      generated by the embedded structure.

      The immediate operands generated during a structure definition
      can be very useful in writing your program.  Following the phone
      list example, here's a better way to declare storage for the
      list:

         NUMENTRYS  EQU 500
         PHONELIST  DM  LISTENTRY*NUMENTRYS ;500 entries of length
                                            ;defined by the structure.

      Now if you add another field to the structure, PHONELIST will
      automatically increase in size.

      The 8088's indirect addressing modes, coupled with structures,
      make a very powerful combination for accessing structured data in
      memory.  Suppose AX contains the number of the entry you want to
      work on.  You can calculate the address of the entry as follows:

          MOV BX, LENGTH(LISTENTRY)    ;length per entry
          MUL AX,BX                    ;times entry number
          ADD AX, OFFSET(PHONELIST)    ;plus the starting offset
          MOV BX,AX                    ;BX <== frame pointer

      BX is now a "frame pointer" - it points to the beginning of the
      desired entry.  You can access the various parts of the entry
      using the optional displacement field in the indirect address.
      For example, here's how you would store the letter 'A' into the
      first byte of the address field:

           MOV  ADDRESS[BX], 'A'

      As another example, the following line reads the third letter of
      the name into the AL register:

           MOV  AL, NAME+3[BX]






















                                                                     44

      The more complicated indirect modes can be used to scan through
      or point within the fields.  The following program fragment gets
      the fourth digit in the phone number:

           MOV DI, 4             ;specify 4th digit
           MOV AL, PHONE[BX+DI]  ;read it into AL

      Often times, you'll want to process entries sequentially.  To
      move to the next entry, you just add the length of the entry to
      the frame pointer:

           ADD   BX, LENGTH(LISTENTRY)    ;point to next entry

      The preceding examples should give you a feel for what you can
      do with structures, but do not exhaust all the possibilities.
      Experiment with this feature, and many of your programs will be
      both more readable and more easily modified.















































                                                                     45

      >>Outside the Program Segment<<

      As mentioned previously, CHASM does not support multiple segment
      definitions.  Provision is made for limited access outside of the
      program segment, however.

      A. Memory References:
         To access memory outside the program segment, you move a new
         segment address into the DS register, then address using
         offsets in the new segment.  The memory option of the EQU
         pseudo-op allows you to give a variable name to offsets in
         other segments. For example, to access DOS's equipment flag:

            BIOS_DATA   EQU  40H
            EQUIP_FLAG  EQU  [0010H]
                        MOV  AX,BIOS_DATA  ;can't move immed. to DS
                        MOV  DS,AX
                        MOV  AX,EQUIP_FLAG ;get bios equipment flag

      B. Code Branching:
         CHASM supports 4 instructions for branching outside the
         program segment.

         1. Direct CALL and JMP

            New values for the PC and CS registers are included in the
            instruction as two immediate operands.  Example:

            BIOS         EQU  0F000H            ;RAM bios segment
            DISKETTE_IO  EQU  0EC59H            ;disk handler
                         JMP  DISKETTE_IO,BIOS

         2. Indirect CALLF and JMPF

            Four consecutive bytes in memory are initialized with new
            values for the PC and CS registers.  The CALLF or JMPF then
            references the address of the new values.  Example:

            BIOS        EQU   0F000H           ;RAM bios segment
            PRINTER_IO  EQU   0EFD2H           ;printer routine
                        MOV   [DI],PRINTER_IO
                        MOV   2[DI],BIOS
                        CALLF [DI]





















                                                                     46

      >>Running CHASM<<

      A. Prompt Mode

         From DOS, type:

           CHASM

         If you're using the Subset version, a hello screen is printed,
         followed by the message:

           Hit Esc to exit, anything else to continue...

         Advanced CHASM skips the commercial message.

         You're now presented with a series of prompts:

            Source code file name? [.asm]

         Type in the name of the file which contains your program.  If
         you don't include an extension for the filename, CHASM
         assumes it to be .ASM.  If CHASM is unable to find the file,
         it will give you the option of naming another file, or
         returning to DOS.  Note that anywhere CHASM expects a
         filename, you can optionally include a drive and/or path.

         Assuming your file is present, CHASM prompts:

            Direct listing to Printer (P), Screen (S), or Disk (D)?
            [nul:]

         Respond with either an upper or lower case letter.  If you
         just press enter, no listing will be produced.  If you select
         "D", CHASM will prompt:

            Name for listing file? [fname.lst]

         Type in a name for the listing file.  If you just press ENTER,
         the name defaults to that of your source file, with an
         extension of .LST.
























                                                                     47

         Listing Notes:

            1. The setting of the /PATH configuration switch controls
               the exact form of the default list file name.

            2. Regardless of where the listing is sent, error messages
               are always echoed to the screen.

            3. Suppressing the listing will result in faster assembly.

         The final prompt is:

            Name for object file? [fname.com]

         Type in a name for the assembled program.  If you just press
         ENTER, the name defaults to that of your source file, with an
         extension of .COM.

         Note: The setting of the /PATH configuration switch controls
               the exact form of the default object file name.

         CHASM now assembles your program.  A status line is maintained
         on the screen, showing how many lines have been processed,
         along with how many errors have been discovered.  CHASM makes
         two passes over your source file, outputting the listing and
         object code on the second pass.  You may abort assembly and
         return to DOS at any time by hitting Ctrl-C or Ctrl-Break.

         At the end of the second pass, a final summary of the assembly
         process is printed.  It will look something like:

            0 Error(s) detected
            0 Diagnostic(s) offered

         954 (3BAH) Bytes of object code generated

         This information should be self-explanatory.  The number of
         bytes is given in both decimal and hex format.


























                                                                     48

         If labels appeared in your program, a dump of the symbol table
         will follow.  This lists each user-defined symbol, along with
         its value (in hex). The symbols are printed in alphabetical
         order.  Each value is preceded by a one-letter code, which
         tells the symbol's type:

                  P: a program location
                  M: a memory location for data
                  I: immediate data

         Upon exit, CHASM sets the system variable ERRORLEVEL to
         (surprise!) the total number of errors discovered in your
         source file. If you run CHASM from a batch file, you can use
         this feature to automatically invoke your text editor if
         errors were discovered.

      B. Expert Mode:

         This mode allows you to specify all i/o information on the
         command line which invokes CHASM.  The syntax is:

            CHASM sourcefile [p|s|d|/] [listfile|/] [objectfile]

         Items within brackets ([]) are optional. You may select *one*
         of any list of items separated by a bar (|).

         Basically, you just include on the command line all your
         responses to the normal prompts.  Each response must be
         separated from the others by either a space or comma.

         If you don't specify the list device/file or the object file,
         they default to NUL: and sourcename.COM respectively.  To
         represent a carriage return (to specify a default choice, but
         allow modifying a later response) use the character slash (/).






























                                                                     49

         Expert mode examples:

            1. Source file is EXAMPLE.ASM, no listing, object file
               EXAMPLE.COM:

                  CHASM example

            2. Source file is SDIR.ASM, list to printer, object file
               SDIR.COM:

                  CHASM sdir p

            3. Source file is MYFILE.PRG, list to disk file MYFILE.LST,
               object file SUBR.COM:

                  CHASM myfile.prg d / subr.com
















































                                                                     50

      >>Error and Diagnostic Messages<<

      Error messages generated on pass one appear on the listing before
      any source code is printed, and mention the line number to which
      they refer.  The majority of messages occur during pass two, and
      will appear in the listing immediately prior to the line which
      caused the message.  Unless the listing itself is going to the
      screen, messages and the source line which generated them will be
      echoed there.

      Add Leading Zero to Hex Constant: Diagnostic.  The unknown
         symbol could be interpreted as a hexadecimal number if a
         leading zero was added.

      CHASM Internal Error: XX PC: YYYY or
      CHASM I/O Error: XX PC: YYYY 
         Sigh. You just discovered a problem in CHASM itself.  Please
         contact Whitman Software, following the procedure in the
         appendix on Bug Reporting.

      Could Use JMPS: Diagnostic.  The specified label requires an
         offset of less than 128 bytes; specifying the short jump would
         result in more compact code.  The assembled code is correct,
         however.

      Conditional Nested Too Deeply:  IF statements can only be nested
         10 deep.

      Data too Large: XXX   XXX was found in DB operand list, but is a
         word value.  Use DW to declare words.

      DM out of range:  The product of the DM's operands is either
         negative, or greater than 32767.

      Duplicate Definition of XXX in (linenum): Pass 1 error.  An
         attempt was made to define a symbol already present in the
         symbol table.

      ELSE without IF: An ELSE was encountered, but no corresponding
         conditional pseudo-op was found.

      ENDC without COUNT: An ENDC was encountered, but no corresponding
         COUNT was found.





















                                                                     51

      ENDIF without IF: An ENDIF was encountered, but no corresponding
         conditional pseudo-op was found.

      ENDM without MACRO:  An ENDM was encountered, but no
         corresponding MACRO was found.

      ENDP without PROC: An ENDP was encountered, but no corresponding
         PROC was found.

      ENDSTRUC without STRUC: An ENDSTRUC was encountered, but no
         corresponding STRUC was found.

      EQU Without Label: No symbol was found to equate with the
         operand.

      File not found: XXX in (linenum).  Pass one error.  CHASM was
         unable to find the file XXX, specified in the INCLUDE
         pseudo-op.

      Heap Full: Too many XXX.  Usually a Pass one error.
         You've run out of memory for the symbol and macro tables.  You
         shouldn't see this message unless you have only 128K and are
         assembling a very large program.

      Illegal Label: XXX in (linenum). Pass one error.  The symbol
         XXX begins in column one and has as its first character a
         number, or a plus or minus sign.  Alternatively, you tryed to
         use the reserved symbol '$' as a label.

      Illegal Operation for Structure - ENDSTRUC Implied: Diagnostic.
         The current line is within a structure, and is not a storage
         defining pseudo-op.  CHASM generates an ENDSTRUC, which
         terminates the structure definition, then assembles the line
         normally.

      Illegal or Undefined Argument for LENGTH:  The argument for the
         LENGTH  function was not present in the symbol table as an
         immediate operand on pass 2.

      Illegal or Undefined Argument for OFFSET: The argument for the
         OFFSET function was not present in the symbol table as a near
         label or memory location on pass 2.

      Missing ENDC: The end of the input file was encountered, and at
         least one COUNT had not been terminated by an ENDC.



















                                                                     52


      Missing ENDM:  The end of the input file was encountered, and
         at least one MACRO had not been terminated by an ENDM.

      Missing ENDP: The end of the input file was encountered, and at
         least one PROC had not been terminated by an ENDP.

      Missing ENDSTRUC: The end of the input file was encountered, and
         at least one STRUC had not been terminated by an ENDSTRUC.

      Multiple Segment Overides are Illegal:  Diagnostic.  You have
         specified more than one segment overide on this instruction.
         The first overide is used, and the other(s) ignored.

      Nested COUNT:  A COUNT was encountered while CHASM was already
         COUNTing.  COUNTs cannot be nested.

      Nested INCLUDE: An INCLUDE was encountered in an INCLUDEd file.
         The INCLUDE pseudo-op cannot be nested.

      Nested Structure: A STRUC was encountered inside a structure.
         Structures cannot be nested.

      No Name For Macro:  Diagnostic.  The macro statement did not have
         a label.  CHASM is unable to give a name to the macro, and you
         will be unable to reference it.

      Phase Error: A label or memory location is found to have
         different values on pass 1 and pass 2.  A difficult to debug
         error: generally the problem is not caused by the statement
         which received the error message.

         There are four documented ways to generate this error.

         1. A previous instruction used a symbolic immediate operand
            prior to the symbol's definition.

         2. A previous instruction made improper use of a forward
            referenced label, either an attempt to branch into a data
            area, or to access a code area as if it was data.

         3. The label on the flagged statement is defined more than
            once in the program.





















                                                                     53

         4. A previous instruction invoked a macro prior to its
            definition.

         Whitman Software would appreciate hearing about any other
         situations which cause the Phase Error message to appear.

      Procedures Nested Too Deeply: Procedures may be nested no more
         than 10 deep.

      Source Line Truncated:  The length of the input line exceeded 80
         characters.

      Specify Word or Byte Operation: Diagnostic.  CHASM suggests that
         the Syntax Error might be resolved by adding the suffix "B" or
         "W" to the instruction mnemonic.  Most, but not all, ambiguous
         memory references are flagged with this diagnostic.

      Syntax Error: (OP) (DEST) (SOURCE).  CHASM was unable to find a
        version of the instruction (OP) which allows the operands
        (DEST) and (SOURCE).  Either the instruction doesn't exist, or
        it is an inappropriate choice for the given operands.

        Syntax Error messages are followed by two diagnostics which
        spell out in words CHASM's best guess about the operands.

      Too Far For Short Jump: The displacement to the specified label
         is not in the range -128 to +127.

      Undefined Operand for EQU: Any operands on an EQU statement must
         have been previously defined.

      Undefined Symbol XXX: The symbol XXX was used as an operand, but
         never appeared as a label, and is not a predefined symbol.

      Unrecognized Operand XXX: XXX is used in the DB or DW operand
         list, but is not a valid immediate operand. (or string, in the
         case of DB).



























                                                                     54

      >>Execution of Assembled Programs<<

      A. Object code format

         The object code file produced by CHASM is in the form of a
         memory image, exactly as will be present in your computer at
         run time.  No link step is required.  Provided that the segment
         registers are set correctly, the architecture of the 8088
         guarantees that code is self-relocating, and will run correctly
         loaded anywhere in memory.  Storing a program as an exact image
         of memory at run time is called the COM format by IBM.

         This COM format is *not* that produced by the IBM assembler.
         The output of the IBM assembler is in the form of an "object
         module" suitable for input to the linker.  The object module
         is not directly executable, but must first be "filtered"
         through the linker.  This adds an extra step to the process of
         producing a working program, but gives you the option of
         combining multiple object modules into one program.  The
         resulting linked program is *still* not a memory image, but
         has a header which is used to perform relocation during
         loading.  This linked program plus header is called the EXE
         format by IBM.

      B. Running Assembled Programs From DOS

         DOS provides a loader for running machine language programs.
         To run a program, you merely type its name, without the
         extension.  This is what you're doing every time you use a DOS
         external command such as FORMAT or CHKDSK.  In fact, the COM
         format is named after "external COMmand".

         When DOS loads a program, it examines the file extension to
         determine what format the file is in, either COM or EXE.  This
         is why CHASM defaults to using the extension .com for your
         object file.  If you plan to run the program from DOS, don't
         change the extension.

         For COM programs, DOS builds a 255 byte long "program segment
         prefix" and sets the segment registers to point to this PSP.
         The contents of the file are then loaded verbatim right after
         the PSP, at offset hex 100 in the segment defined by the
         segment registers.  As soon as loading is complete, your
         program is executed starting with the instruction at hex 100.




















                                                                     55

         Although you can totally ignore the PSP, you should read pages
         E-3 through E-11 of the DOS manual to see what DOS puts there
         for you.  It turns out there are some real goodies which your
         program might want to use.

         When your program is done, it must transfer control back to
         DOS, otherwise the 8088 will continue to fetch what it
         believes are instructions from whatever garbage or bit-hash
         happens to follow your program in memory.  The easiest way to
         return to DOS is to execute the instruction:

           INT 20H

         This is the vectored interrupt reserved by DOS for program
         termination.

         While we're on the topic of vectored interrupts, you would be
         well rewarded to study both the DOS manual and Technical
         Reference to find out what happens when you execute some of
         the other interrupts.  Some very useful functions, such as
         file handling and screen i/o, are available at the machine
         language level through this mechanism.

         Looking at things the other way, by changing the interrupt
         vector for a given function to point to your own code, you can
         override the way DOS or the BIOS does something, and do it
         your way.  DOS even provides a method (via interrupt 27H) by
         which your new code can be grafted onto DOS, and not be
         overwritten by other programs.

      C. Debugging Assembled Programs

         IBM provides an excellent utility with DOS, called DEBUG.COM.
         By specifying your program's name as a parameter when invoking
         DEBUG, you can observe your program execute with DEBUG's trace
         and other functions.  To debug your program, from DOS type:

            DEBUG progname.COM

         DEBUG builds a PSP and loads your program just like DOS does,
         but you have the added power of the debugging commands to
         monitor your program while it runs.  See chapter 6 of the DOS
         manual for more details about using DEBUG.





















                                                                     56

         On the topic of debugging, I can recommend most highly a
         program called TRACE86, from Morgan Computing (10400 N.
         Central Expressway, Suite 210, Dallas, TX 75231).  The program
         replaces DEBUG, and although a little steeply priced at $125,
         makes the IBM debugger look silly.  I've been using TRACE86
         for some time now, and wouldn't be without it.

      D. Using Assembled Programs in BASIC

         To incorporate a machine language subroutine in a BASIC
         program, write it in assembly language, then assemble it with
         CHASM.  You should read page C-7 of the BASIC manual for some
         conventions to use in writing your subroutine.  In particular,
         note that you must declare the routine to CHASM as a FAR
         procedure using the PROC pseudo-op, and that the last
         instruction of the routine should be a RET.

         Unlike programs which are run directly from DOS, your routine
         will not be preceded by a program segment prefix.  You should
         prevent CHASM from leaving room for a PSP by putting an ORG 0
         pseudo-op at the beginning of your routine. If you don't
         include the ORG, memory references will not be assembled
         correctly.  Example:

              ORG  0    ;no psp
         SUBR PROC FAR  ;far procedure
              ...       ;body of subroutine
              RET
              ENDP

         CHASM supports two methods for getting assembled routines into
         BASIC programs.  The methods differ in whether the routine is
         included in the BASIC program file, or in a separate file.

         A utility program called COM2DATA is provided for including
         machine language within BASIC program files.  The program is
         distributed in source code form (file COM2DATA.ASM) and must
         be assembled with CHASM prior to use.  The program functions
         as a DOS 2 filter, reading a COM file in from the standard
         input, and writing a series of BASIC DATA statements to the
         standard output.























                                                                     57

         COM2DATA's syntax is as follows:

           COM2DATA [<infile] [>outfile] [linenum]

         You specify the input and output files as with any DOS 2
         filter.  The linenum parameter sets the starting line number
         used on the BASIC code produced.  If you don't specify
         linenum, it defaults to 1000.

         If you MERGE the file of DATA statements into your BASIC
         program, the program can then READ the data and POKE it into
         memory.  An example program to do this is given on page C-6 of
         the BASIC manual.  An alternative approach would be to store
         the routine in a string variable, which could later be located
         with the VARPTR function. 

         If you would prefer to keep your machine language subroutine
         in a separate file, include a BSAVE pseudo-op somewhere within
         your assembly language source code.  CHASM will build a header
         on the object code produced, which will mimic that built by
         BASIC's BSAVE command.  The resulting file may be BLOADed by
         BASIC to any location in memory.

         You transfer control to your routine with either the USR
         function, or the CALL statement.  Syntax for these statements
         can be found in the BASIC manual.






































                                                                     58

      E. Using Assembled Programs with Turbo Pascal:

         CHASM and Turbo Pascal work splendidly together, complementing
         each other's strong points.  You can use CHASM to provide new
         functions you wish Turbo had, or to fine tune a critical
         procedure for optimum speed.

         Turbo loads external procedures and functions within the same
         segment as the rest of your Pascal program.  You have no
         control of the exact load location (more on this later), but
         on the other hand, you don't have to worry about setting aside
         a special location for your procedures (as in BASIC).  Since
         your external procedure is loaded in the same segment as the
         Pascal code, it should be declared NEAR to CHASM:

           EXTERNAL PROC NEAR
                    ...           ;body of procedure
                    ...
                    ENDP

         Turbo passes parameters to your procedure/function via the
         stack.  To work effectively, a good grasp of the stack
         structure is critical.  Read the Turbo manual for information
         on internal data formats and parameter passing, to see just
         what to expect on the stack.  Also, remember that the stack
         grows down from the top of memory.

         If you're going to access the stack in your procedure, the
         first thing you should do is set up BP as a stack pointer.
         Since Turbo also uses BP, you have to save the current value
         first.  The obvious place to save it is on the stack...

            PUSH BP            ;save old BP
            MOV  BP, SP        ;and set up to indirectly address stack

         You can now access the parameters on the stack using offsets
         off the BP register.  Note that since you PUSHed BP,
         everything is 2 bytes deeper onto the stack than what Turbo
         originally sent you.

























                                                                     59

         Here's an example.  Suppose you declare the following external
         function in Turbo:

            function Sum(x,y: int): int;
               external 'sum.com';

         After you've pushed BP, here's how the stack looks:

             stack contents           indirect address
          ----------------------------------------------
             <value of parameter y>        6[BP]
             <value of parameter x>        4[BP]
             <return address to Turbo>     2[BP]
             <old BP value>                 [BP]

         The indirect addresses go up two at a time, since each item on
         the stack is a word (two bytes) long. You can access the
         parameters using their indirect addresses. Here's the code for
         an external function to add two integer parameters:

         SUM  PROC NEAR
              PUSH BP          ;save old BP
              MOV  BP, SP      ;set up stack pointer

              MOV  AX,  4[BP]  ;get parameter x
              MOV  ADD, 6[BP]  ;add parameter y
                               ;leave sum in AX to return to Turbo

              POP  BP          ;restore old BP for Turbo
              RET  4           ;clear params off stack
              ENDP

         Functions return scalar results by having the value in AX upon
         return.  This function saves some time by calculating the
         value in AX in the first place.  Upon exit, the function POPs
         BP, to restore the value Turbo was using.

         Note the RET 4.  This returns to Turbo, while simultaneously
         POPing (and discarding) 4 bytes off the stack.  This clears
         off the two parameters which Turbo passed.  If there were
         three parameters, you'd use a RET 6; if none, a simple RET
         would do. When Turbo receives control, it assumes that you've
         cleaned up the stack by removing all parameters.  If you don't
         do this properly, a run-time error, or even a system crash
         will result.



















                                                                     60


         (Typical scenario:  Turbo tries to return from one of its own
         subroutines, thinking the top of the stack has the return
         address.  Unfortunately, the top is really an integer
         parameter, left over from your external function.  Turbo's
         RET sends control into some random area of memory, and boom -
         the system crashes.)

         It's easy to get confused about the exact contents of the
         stack.  If your procedure doesn't seem to be working right,
         the first thing to suspect is Turbo and you have different
         ideas about what's where on the stack.  A DEBUG session can
         usually straighten things out.

         A problem of addressability can crop up if your external
         procedure tries to maintain its own local variables and/or
         constants.  The problem is that you have no way of knowing
         just where Turbo is going to load your procedure within the
         shared segment.  As such, the address CHASM calculates for any
         memory locations are going to be offset from their real values
         by some unknown constant, the offset of the procedure within
         the shared segment.  This is called a relocation problem.

         Fortunately, there's a way around this problem, but it
         requires using a trick.  Your program has to figure out, *at
         run time*, just where it's located in memory.  If you could
         find out the offset of any known point in your procedure,
         you'd "have your bearings" so to speak, and could go on.

         The trick is as follows.  The 8088 CALL instruction pushes the
         address of the next instruction onto the stack, then branches
         to the location given in the CALL.  By performing a dummy
         CALL, then stealing the value off the stack, we have the
         location of a known spot in the procedure.   By subtracting
         the offset within the procedure of that known location, we get
         a pointer to the beginning of the procedure which can be used
         to access everything else.  Here's an example:



























                                                                     61

         LOCAL  PROC NEAR
                PUSH BP                     ;set up to access stack
                MOV  BP, SP                 ; ditto

                CALL DUMMY                  ;establish addressability
         DUMMY  POP  BX                     ;  "           "
                SUB  BX, OFFSET(DUMMY)

                MOV  AX, 4[BP]                ;get parameter
                SEG  CS                       ;offset relative to CS
                ADD  OFFSET(TOTAL)[BX], AX    ;maintain running total

                POP  BP
                RET  2
         TOTAL  DW   0000H
                ENDP

         We use indirect addressing here.  After the funny business
         with the CALL, POP, SUB sequence, BX has a pointer to the
         beginning of the procedure.  Using indirect addressing, we
         take that pointer and we add in the offset of the memory
         location we want to access.  In this example we're using a
         local variable to maintain a running total of the parameter
         which gets passed.

         Note the SEG CS just before the ADD which accesses the
         location TOTAL.  Since we found our bearings by stealing the
         address of a program instruction, our offset is known relative
         to the CS register, NOT the DS which is normally used to
         access data.  The SEG CS forces the 8088 to calculate the
         address using CS rather than the default DS register.  Every
         time you access a memory location within your procedure, you
         *MUST* do it relative to CS by using a segment overide.

         Turbo is very forgiving about what values you leave in the
         registers upon return.  If you modify their contents, you do
         have to restore BP, SP and SS before returning to Turbo.
         However, as far as I can tell, you can safely trash the
         contents of all the general purpose registers, plus DI, SI, DS
         and ES.
























                                                                     62

      >>Notes for Those Upgrading to This Version of CHASM<<

      CHASM is not yet carved in stone - improvements and corrections
      are made fairly frequently, based on both my own experience in
      using the program, and the comments of outside users.  This
      section summarizes the changes which have been made since version
      1.2 was released.  Changes followed with an asterisk (*) denote
      modifications which could invalidate programs written under
      earlier versions of CHASM.

      Version     Notes

      4.00        Total rewrite in Turbo Pascal.  Subset replaces
                  interpreted version as free distribution release.
                  Faster assembly.  Symbol and macro tables can now use
                  all available memory.  Nested macros now permitted.
                  Operand expressions.  $ now returns location counter
                  value.  New syntax for segment overides.  Conditional
                  pseudo-ops now evaluate operands.  Improved error and
                  diagnostic messages.  DOS 2 or later now required
                  (*). DOS 2 path support for files. Setting of DOS 2
                  ERRORLEVEL. EJECTIF pseudo-op added. New
                  configuration switches: /FF, /DWIDTH, /TIMER, /PATH.
                  CHASM.CFG must now have only one switch per line (*).

      3.15        Macros added. New pseudo-ops: MACRO, ENDM, IFE, IFNE,
                  IFB, IFNB, ELSE, ENDIF.

      3.14        Interpreted version frozen at version 2.13, further
                  changes apply only to compiled version.  Memory
                  requirement raised to 128K.  INCLUDE, STRUC,
                  ENDSTRUC, DM, DW, LIST, NOLIST, COUNT and ENDC
                  pseudo-ops added.  Alternate mnemonics for the jump
                  on condition instructions, and alternate syntax for
                  the DIV and MUL instructions.  Binary numbers added.

      2.13        Assembly can now be aborted with the Esc key.
                  Negative decimal numbers are working again.  Input
                  lines now limited to 80 characters, and labels must
                  begin with a non-numeral. (*) 

      2.12        Listings can now be suppressed.  Error messages are
                  echoed to the console on non-screen listings.
                  Expert mode added.




















                                                                     63

      2.11        Pagination improved.  Listings now time stamped.
                  OFFSETs and word values now allowed in DB operand
                  list.

      2.10        Equated symbols allowed in the DB operand
                  list.  Status line improved.

      2.09        The first digit of hexadecimal constants must now be
                  in the range 0-9. A leading zero is permitted on four
                  digit hex constants, to allow fulfilling this
                  condition. (*)

      2.08        Configuration process expanded.  CHASM now skips over
                  perforations on printed listings.  EJECT pseudo-op
                  added.

      2.07        Oops.  Configuration file now works as advertised.

      2.06        CHASM now supports reverse long jumps.

      2.05        Compiled version released.  BSAVE pseudo-op.
                  Configuration process simplified.

      2.04        TABs are now expanded and replaced with blanks, for
                  compatibility with IBM text editors.

      2.03        Two bugs corrected.  The first bug involved incorrect
                  assembly of indirect memory references which used a
                  displacement in the range 128-255.  The second caused
                  a program crash if a hex number longer than 4 digits
                  was in found in the input file.

      2.01        COM2DATA utility added.

      2.00        Corrected a bug in the DS and DB pseudo-ops which
                  caused the last label in a program to be redefined as
                  a memory location.  Also, the TAB character was added
                  as a new delimiter, and PRIMER.DOC was added to the
                  CHASM package.

      1.9         The short jump is now represented with mnemonic JMPS,
                  for compatibility with DEBUG version 1.1. (*)

      1.8         The operand type "character" was added as a new way
                  to represent immediate data.



















                                                                     64


      1.7         The DS operator now works for blocks larger than 255
                  bytes.  Also, the OFFSET function now works properly
                  in the displacement field of an indirect memory
                  reference.

      1.6         A revision of this document.  Some sections were
                  improved slightly, and in response to user requests,
                  a section on execution of assembled programs was
                  added.

      1.5         Corrected an error which generated the message "Data
                  too Long" if the value FFH was used as 8 bit
                  immediate data.

      1.4         User interface improved.  CHASM now traps some common
                  input errors such as misspelling a file name, or
                  forgetting to turn on your printer.

      1.3         A speed enhancement.  Version 1.3 benchmarks about 5
                  times faster than version 1.2.











































                                                                     65

      >>Miscellaneous and A Word From Our Sponsor...<<

      A. Programming Notes:

         1. CHASM is written in Turbo Pascal.  The source code is
            available to registered users by sending a formatted disk
            and stamped return mailer.  If you make any improvements,
            I'd like to hear about them for possible inclusion in
            future releases.

            Please note that although you can modify CHASM for your own
            use, under NO CIRCUMSTANCES may you distribute modified or
            translated versions, either in the public domain or for
            profit.

      B. Red Tape and Legal Nonsense:

         1. Disclaimer:

            CHASM is distributed as is, with no guarantee that it will
            work correctly in all situations.  In no event will the
            Author be liable for any damages, including lost profits,
            lost savings or other incidental or consequential damages
            arising out of the use of or inability to use these
            programs, even if the Author has been advised of the
            possibility of such damages, or for any claim by any other
            party.

            Despite the somewhat imposing statement above, it *is* my
            intention to fix any bugs which are brought to my
            attention.  See the appendix on Bug Reporting for more
            details.

         2. Copyright Information:

            The entire CHASM distribution package, consisting of the
            main program, documentation files, and various data and
            utility files, is copyright (c) 1983, 1984 and 1985 by
            David Whitman.  The author reserves the exclusive right to
            distribute this package, or any part thereof, for profit.
            The name "CHASM (tm)", applied to a microcomputer assembler
            program, is a trade mark of David Whitman.






















                                                                     66

            CHASM's Subset version and various subsidiary files may be
            copied freely by individuals for evaluation purposes.  It
            is expected that those who find the package useful will
            make a contribution directly to the author of the program.
            The Subset version identifies itself by displaying a banner
            page giving the author's address and inviting free copying.
            ONLY VERSIONS DISPLAYING THIS BANNER PAGE MAY BE COPIED.

            CHASM's Advanced version is only available to registered
            users who have made the $40 suggested payment.  Registered
            users may copy the program for backup purposes, but must
            restrict use of the program to either one user or one CPU,
            at their option.

            CHASM's source code is made available for educational
            purposes and to allow users to customize for their own
            personal use.  Under NO CIRCUMSTANCES may modified versions
            or translations into other computer languages be
            distributed, either in the public domain or for profit.

            User groups and clubs are authorized to distribute CHASM's
            Subset version under the following conditions:

            1.  No charge is made for the software or documentation.  A
                nominal distribution fee may be charged, provided that
                it is no more than $8 total.

            2.  Recipients are to be informed of the user-supported
                software concept, and encouraged to support it with
                their donations.

            3.  The program and documentation are not modified in ANY
                way, and are distributed together.

            Interested manufacturers are invited to contact Whitman
            Software to discuss licensing CHASM for bundling with
            MS-DOS based computer systems. 

            Distribution of CHASM outside the United States is through
            licensed distributors, on a royalty basis.  Interested
            distributors are invited to contact Whitman Software. 























                                                                     67

         3. Royalty Information: 

            No royalties are required to distribute programs produced
            using CHASM.  However, if you send me a copy of any major
            program you have produced using CHASM, I'll give you a free
            page of advertising in this document. 

         4. Educational Discount:

            Substantial discounts are available for multi-CPU licenses
            of CHASM's Advanced version to educational institutions.
            Contact Whitman Software for details.

      C. An Offer You Can't Refuse. 

         CHASM is User-Supported software, distributed under a
         modification of the FREEWARE (tm) marketing scheme developed
         by Andrew Fluegelman, whose efforts are gratefully
         acknowledged. 

         Anyone may obtain a free copy of CHASM's Subset version by
         sending a blank, formatted diskette to the author. An
         addressed, postage-paid return mailer must accompany the disk
         (no exceptions, please). 

         A copy of the program, with documentation, will be sent by
         return mail.  The program will carry a notice suggesting a
         payment to the program's author.  Making the payment
         is totally voluntary on the part of the user.  Regardless of
         whether a payment is made, the user is encouraged to
         share the program with others.  Payment for use is
         discretionary on the part of each subsequent user. 
































                                                                     68

         The underlying philosophy here is based on three principles: 

         First, that the value and utility of software is best assessed
            by the user on his/her own system.  Only after using a
            program can one really determine whether it serves personal
            applications, needs, and tastes. 

         Second, that the creation of independent personal computer
            software can and should be supported by those who benefit
            from its use.  Remember the Tanstaafl principal:  There
            Ain't No Such Thing as a Free Lunch.

         Finally, that copying and networking of programs should be
            encouraged, rather than restricted.  The ease with which
            software can be distributed outside traditional commercial
            channels reflects the strength, rather than the weakness,
            of electronic information. 

        If you like this software, please help support it.  Your
        support can take three forms: 

        1. Become a registered user.  The suggested payment for
           registration is $40.

        2. Suggestions, comments, and bug reports.  Your comments will
           be taken seriously - user feedback was responsible for most
           of the changes listed in CHASM's revision history. 

        3. Spread the word.  Make copies of the Subset for friends.
           Write the editor of your favorite computer magazine.
           Astronomical advertising costs are one big reason that
           commercial software is so overpriced.  To continue offering
           CHASM this way, I need your help in letting other people
           know about CHASM. 






























                                                                     69

        Those who make the $40 payment to become registered users
        receive the following benefits:

        1. An upgrade to the Advanced version of the program. The
           Advanced version executes twice as fast as the Subset and
           supports macros, operand expressions and other features.  An
           order form for the Advanced version is given at the end of
           this manual. 

        2. User support, by phone or mail.  Support is only
           available to registered users.  Phone numbers and the
           address for help are given below.

        3. Notices announcing the release of significant upgrades.

      CHASM is copyrighted, and users are requested NOT to make copies
      of the Advanced version other than for their own use.  I am
      strongly opposed to copy protection, and would regret being
      forced to protect CHASM.  Please recognize the amount of time and
      money which went into producing CHASM, and respect the wishes of
      the author. 

            David Whitman
            136 Wellington Terrace
            Lansdale, PA 19446

            (215) 641-7114 (days)
            (215) 362-8526 (evenings)




































                                                                     70

      Appendix A: Mnemonic List

      This appendix lists the mnemonics which CHASM will recognize,
      grouped roughly by function.  Consult "The 8086 Book" for
      definitions of these instructions, and for the operands each will
      accept.  Mnemonics marked with an asterisk (*) will accept a 'B'
      or 'W' suffix for ambiguous memory references.

      Arithmetic:

      AAA      AAD       AAM       AAS       ADC*      ADD*      CBW
      CWD      CMP*      CMPS*     DAA       DAS       DEC*      DIV*
      IDIV*    IMUL*     INC*      MUL*      NEG*      SBB*      SUB* 

      Data Movement:

      LAHF     LDS       LEA       LES       LODS*     MOV*     MOVS*
      POP      POPF      PUSH      PUSHF     SAHF      STOS*    XCHG
      XLAT

      Logical:

      AND*     NOT*      OR*       TEST*     XOR* 

      String Primitives:

      CMPS*    LODS*     MOVS*     SCAS*     STOS*

      Instruction Prefixes:

      LOCK     REP       REPE      REPNE     REPNZ     REPZ      SEG

      Program Counter Control: (unconditional)

      CALL     CALLN     CALLF     JMP       JMPF      JMPN      JMPS
      RET

      Program Counter Control: (conditional)

      JA       JAE      JB      JBE      JC        JCXZ       JE
      JG       JGE      JL      JLE      JNA       JNAE       JNB
      JNBE     JNC      JNE     JNG      JNGE      JNL        JNLE
      JNO      JNO      JNP     JNS      JNZ       JO         JP
      JPE      JPO      JS      JZ       LOOP      LOOPE      LOOPNE
      LOOPNZ   LOOPZ



















                                                                     71


      Processor Control:

      CLC      CLD       CLI       CMC       HLT       NOP       STC
      STD      STI       WAIT

      I/O:

      IN       OUT

      Interrupt:

      INT      INTO      IRET

      Rotate and Shift:

      RCL*     RCR*      ROL*      ROR*      SAL*      SAR*      SHL*
      SHR*














































                                                                     72

      Appendix B: Differences Between CHASM and That Other Assembler

      Virtually all magazine articles about assembly language
      programming on the IBM PC assume that the reader is using That
      Other Assembler - you know, the one that costs $150.  This
      appendix will try to summarize the differences between the two
      programs.  Please note that I do not own a copy of That Other
      Assembler, and therefore this section is not complete, nor even
      guaranteed to be correct.  Anyone with more experience is
      invited to make additions or corrections.

      A. General Differences

      The biggest difference is philosophical.  The IBM assembler was
      designed for use by professional assembly language programmers,
      to write operating systems and other huge projects.  This is
      reflected in the large size and relative complexity of the macro
      assembler.

      On the other hand, CHASM was designed for use by beginners, to
      write relatively short programs.  This was done by leaving out a
      some of the power offered by IBM's assembler, in exchange for
      simplicity and small size.  The main simplification involved
      producing object code in the COM format, rather than the EXE
      format chosen by IBM. There are two main consequences of this
      choice:

         1. You can't link routines assembled by CHASM to
            Microsoft languages. (Although you *can* include them in
            Turbo Pascal or BASIC programs.)

         2. Your program has to fit in one 64K segment.  If (shudder!)
            you want to write a 256K assembly language program, you're
            out of luck.

      Like Pascal, the IBM assembler is a strongly typed language.  By
      requiring you to specify the *type* of each memory location you
      will access in your program, the IBM assembler generally knows
      what size of memory operand you want.  If you don't like the
      declared size, you have to overide the default with the PTR
      operator.  Thus, to loading the AL register from a location
      declared word is a syntax error, unless you specify BYTE PTR
      before the address.





















                                                                     73

      In analogy to the C language, CHASM is weakly typed. CHASM is
      perfectly happy extracting a byte from where you originally set
      aside a word - CHASM can't tell the difference. In most cases,
      CHASM can tell what size you want from context:  if you're using
      a word register, it's a word memory access. On the other hand,
      for any access to memory which doesn't have a register as the
      other operand, you must add either a 'B' or a 'W' to the
      instruction mnemonic used by IBM.

      B. Miscellaneous Differences:

         1. Short Jumps:

            IBM uses the SHORT keyword, CHASM uses an 'S' suffix.
            Example:

            JMP   SHORT label    ;ibm
            JMPS  label          ;chasm

         2. Offset Function:

            Where IBM precedes an operand with the keyword OFFSET,
            CHASM has a *function* called OFFSET. CHASM requires
            parentheses around the operand. Example:

            MOV   AX, OFFSET FCB  ;ibm
            MOV   AX, OFFSET(FCB) ;chasm

         3. Declaring Storage:

            A.  If you don't care what value a memory location is
                initialized to, the IBM assembler allows you to specify
                '?' as its contents.  In CHASM, if you don't care what
                value the variable is initialized to, just put down a
                zero.  Example:

                   DB   ?      ;ibm
                   DB   0      ;chasm


























                                                                     74

            B.  The IBM assembler allows the keyword DUP as an operand
                in storage declaring pseudo-ops.  This means to repeat
                the definition as many times as the number just before
                the DUP.  Example:

                DW   3 DUP(?)  ;ibm
                DW   0, 0, 0   ;chasm

      4. ASSUME Pseudo-op:

         IBM's ASSUME pseudo-op tells the assembler where the segment
         registers will be pointing.  CHASM always assumes that the CS,
         DS and SS registers point to the beginning of the code
         segment, and that the SS register has been set up to point to
         a valid stack area.  If you find an ASSUME pseudo-op where the
         CS, DS and ES registers point to different locations, you will
         have to figure out the addresses for memory references in the
         DS or ES segments yourself.

      5. Segment Pseudo-op:

         This pseudo-op is used to set up multiple segments in the IBM
         assembler.  Since CHASM only allows one segment, there is no
         equivalent pseudo-op.  If there is only one segment definition
         in an IBM assembler program, everything is fine, just leave
         the pseudo-op out for CHASM.

         Often times the SEGMENT pseudo-op is used to provide
         addressing of an area in the BIOS, or perhaps the interrupt
         vector table at the beginning of memory.  For example, if a
         program needed to get at the BIOS data area, in the IBM
         assembler you would define a dummy segment with the same
         structure as that in the BIOS listing in Technical Reference:

           DATA          SEGMENT AT 40H
           RS232_BASE    DW    4 DUP(?)
           PRINTER_BASE  DW    4 DUP(?)
           EQUIP_FLAG    DW    ?
           MFG_TST       DB    ?
           MEMORY_SIZE   DW    ?
           IO_RAM_SIZE   DW    ?

         All this is really accomplishing is giving a name to some
         memory locations which are outside the actual program being
         written.



















                                                                     75


         In CHASM, you can simulate the dummy segment using a
         structure.  This will generate a series of immediate operands
         whose values correspond to the offsets of the labels in the
         dummy segment.  You can then reference the locations by
         enclosing the label names in square brackets, to coerce from
         type immediate to type address.

           DUMMY         STRUC            ;simulate dummy segment
           RS232_BASE    DW    0, 0, 0, 0
           PRINTER_BASE  DW    0, 0, 0, 0
           EQUIP_FLAG    DW    0
           MFG_TST       DB    0
           MEMORY_SIZE   DW    0
           IO_RAM_SIZE   DW    0
                         ENDSTRUC
                         MOV AX, [EQUIP_FLAG]

      6. Labels:

         The macro assembler indicates a local label by appending a
         colon (:).  The colon does not become part of the label, and
         is not included when referencing the label.  CHASM's labels
         are all global, and although they may end with a colon, the
         colon will become part of the label itself, and must then be
         used when referencing the label.  Example:

         a2:   mov ax,cx      ;ibm
               jmp a2         ; "

         a2:   mov ax,cx      ;chasm
               jmp a2:        ;  "

      7. Entry Point:

         The macro assembler allows you to specify the point within
         your program where execution will begin.  A label is put
         on the entry point, then to indicate entry, the same label is
         placed on the "END" pseudo-op.  Since COM programs must always
         start at offset 100H, CHASM doesn't allow setting an entry
         point.























                                                                     76

      Appendix C: Description of Files

      Your CHASM distribution disk contains a number of files.  This
      appendix will give a brief statement of the purpose of each.

      FILE           DESCRIPTION
      ----------------------------------------------------------------
      CHASM.CFG       Sample configuration file, for IBM printer.

      CHASM.COM       The CHASM program (either subset or advanced)

      CHASMS.COM      This file may appear on the disk of advanced
                      version users.  It is the current subset version,
                      that can be shared with others.  Please rename it
                      CHASM.COM on their disk, to avoid confusion.

      CHASM.DOC       This document.

      EXAMPLE.ASM     Sample source file.

      COM2DATA.ASM    Source code for COM2DATA filter.

      COM2DATA.DOC    Documentation for COM2DATA.

      FREEWARE.DOC    References to other User Supported programs.

      PRIMER.DOC      Simple introduction to assembly language.

      Occasionally, various other sample source files for CHASM will be
      distributed.  These files will have extension ASM, and will be
      accompanied by a corresponding DOC file.

































                                                                     77

      Appendix D: Bug Reporting Procedure

      Although each version of CHASM is tested extensively prior to
      release, any program of this magnitude is bound to contain a few
      bugs.  It is the intention of Whitman Software to correct any
      genuine problem which is reported.

      If you think you have found a bug in CHASM, please take the time
      to report it for correction.  Although any report is helpful,
      correction of the problem will be easiest if you provide the
      following:

         1. The version of CHASM you are using.  Your problem may have
            been fixed already!

         2. A brief description of what you believe the problem to be.

         3. A printed listing of a source file which manifests the
            problem.

            * DON'T send a 5,000 line program which has one
              manifestation of the bug!  Isolate the problem area, or
              write a short sample routine that demonstrates the bug.

      Unlike normal commercial software, where corrections are saved up
      for major a revision, bugs in CHASM are fixed as soon as
      reported, with a new version released almost immediately (which
      is why there are so many versions in CHASM's revision history).

                     =====> BONUS <======

      If you send a copy of your problem source file on disk, it will
      be returned with either a new, corrected version of CHASM, or
      with an explanation of what you were doing wrong to *think* you'd
      found a bug.





























                                                                     78

      Appendix E: Using CHASM on "Compatible" Systems

      CHASM was written specifically for the IBM PC, but should
      function normally on true "compatibles".  This appendix is a new
      section to summarize compatibility data for various systems.

      Since CHASM version 4.00 is a totally new program, little
      compatibility data is currently available.  If you are using (or
      are unable to use...) CHASM on a non-IBM computer, please write
      with your experiences.  Does CHASM work correctly on your system?
      Are there specific problem areas?  Can they be worked around?

      The following systems are known to run CHASM version 4.00
      successfully:

             IBM PC
             IBM XT
             IBM 3270 PC and 3270 PC/G
             Zenith 150

      The following systems have one or more problems:

      ================================================================
      Tandy 1200HD - version 4.00 seems to crash this system.  The
      problem has not yet been isolated.  Input from others with access
      to a Tandy 1200HD would be appreciated.
      ================================================================





































                                                                     79

            ********ADVANCED VERSION ORDER FORM********

      Please add me to the list of registered CHASM users, and send me
      an upgrade to Advanced CHASM.  I understand that CHASM is
      copyrighted, and agree not to distribute any unauthorized copies
      of this Advanced version.

      Note that version 4.00 requires DOS 2 (or later) and 128K

      Computer Model: ____________________________________

      Diskette format:            Total Memory: _______K
                                     (128K required)
         __ single sided/DOS 2

         __ doubled sided/DOS 2

      Check one:

             ___ I enclose a check for $40

             ___ I am a past customer.  The enclosed check brings my
                 total payment up to $40.


      Where did you hear about CHASM? ________________________________

      Name:    _______________________________________________________

      Address: _______________________________________________________

      City, State, Zip: ______________________________________________


      ================================================================
           Send order form and check to:

                Whitman Software
                136 Wellington Terrace
                Lansdale, PA 19446
























                                                                     80

        ==============PRINTER ENHANCEMENT===================


      Michael Hoyt, of Soft and Friendly Software, has produced a set
      of printer enhancement programs using CHASM, which is sold under
      the name Prowriter Utilities.  The package supports the following
      printers:

          NEC 8023A-C
          Prowriter I  (C. Itoh 8510)
          Prowriter II (C. Itoh 1550)

      The package contains three programs:

          PRINT_CHARACTERS
          PRINT_SCREEN
          PRINT_SET

      Once PRINT_CHARACTERS is run, it attaches itself to DOS, and
      makes your printer have exactly the same character set as your
      video monitor.  The conversion is very professionally done.
      Particularly impressive are the line drawing characters, which
      actually form connected lines, both horizontally and vertically.

      As if this wasn't enough, PRINT_CHARACTERS adds italics
      capability as well.  The italics make very effective emphasis in
      documents and letters, and look really good.

      PRINT_SCREEN is a graphics screen dump, activated by the normal
      Shift/PrtSc sequence.  Several options are available which trade
      off speed and print quality.  Since I have the mono card, I
      haven't tried PRINT_SCREEN, but Michael sent me a sample printout
      which looked quite nice.

      PRINT_SET is a menu-driven program to turn on and off the various
      special printing modes supported by these printers.  A simple but
      effective program.

      I've been using this package with my NEC 8023 for a few months
      now, and I like them quite a bit.  To get a copy, send $35 to:

          Soft and Friendly
          RR 2 Box 65
          Solsberry, IN 47459




















                                                                     81



           ================= NEW PRODUCT ==================

      If you use the IBM/Microsoft BASIC compiler, chances are your
      programs are bigger and slower than they have to be.  If all
      unreferenced line numbers are removed from your source program,
      and the /N switch is used, BASCOM will "optimize" your program.
      The result is tighter, more efficient code.

      NUMZAP is a utility which carefully scans your source file, and
      deletes all the non-essential line numbers.  Performing this task
      by hand would be prohibitively time consuming and you'd probably
      introduce errors into your program in the process.  NUMZAP will
      do the job in minutes, 100% error free.

      The old BASIC version of CHASM was passed through NUMZAP, and the
      resulting compiled code shrank by a factor of 10% (!).  That 10%
      reduction could make the difference between your program running
      in 64K, or having users with minimal systems get "Out of Memory"
      messages just before your program crashes.

      An added advantage to using NUMZAP is that bigger programs can be
      compiled.  You may not be aware that there is a limit on the size
      of program which the compiler can handle.  BASCOM uses up space
      remembering the offset of each line number in your program. If
      you have too many numbered lines, BASCOM will run out of room and
      you'll get a unending series of "TC" (Too Complex) error
      messages.  By eliminating the unneeded line numbers, you give
      BASCOM more elbow room.  The free space available to compile
      CHASM increased 27% (!) after using NUMZAP.

      NUMZAP is available under the standard FREEWARE deal - just send
      a formatted disk and self-addressed, stamped return mailer to:

                  David Whitman
                  136 Wellington Terrace
                  Lansdale, PA 19446

      Be sure to specify that you are interested in NUMZAP.  If you
      like the program, a donation of $15 is suggested.