PROBLEMS.DOC

			    Matthew Dillon
			    891 Regal Rd.
			    Berkeley, Ca. 94708
			    USA

			    uunet.uu.net!overload!dillon    or
			    dillon@overload.Berkeley.CA.US

				CED

    Those of you using the CED editor need to use the sticky option.
    Unfortunately, CED requires that STICKY be the last argument so
    what you really need to do is set the editor command in UULIB:Config
    to execute a script file that runs CED with the filename and STICKY
    option.

    The format for CED is:	CED file -sticky

    A script file can be found in UUCP:SC/UUCed

			  MODEMS AND GETTY

    There are several possible sources of problems in setting up
    UUCP.  The major problem areas in order of likelyhood are
    listed below:

    (1) The modem is expecting a protocol that Getty has not
	been told to use (XON/XOFF, 7WIRE, none)

	If the modem uses 7-wire use the -7 option for Getty, else it is
	assumed the modem uses no protocol.  Normally you specify -7 but
	the modem will probably work just fine whether you specify it or
	not.

    (2) The modem does not hangup when DTR is dropped

	All modern modems hangup when DTR is dropped.  Usually a dip switch
	enables/disables the option.  If it is impossible to drop a
	connection by dropping DTR you can use the -d0 option to make Getty
	use the +++ sequence.  This only works if you do not specify a dumb
	modem in the -M option.

	NOTE: older versions of the A2232 multi-port serial.device do not
	drop DTR when the device is closed.  There is no way to drop DTR
	with these devices.

	When you cannot use DTR to drop a connection you must use the -d0
	option so Getty will use +++ ATH0 instead.

    (3) The modem does not understand simple AT commands or does
	not generate a CONNECT message.

	If the modem does understand dropping DTR but does not understand
	simple AT commands or generate a CONNECT message use -c0 -Md (no
	connect msg and dumb modem). In this case the baud rate must be
	known and specified with one or more -B options.  When no CONNECT
	message is available Getty does not know what the connect baud rate
	actually is.  It will begin by trying the first -B option and
	switch to the next whenever a line-break is received.

    (4) Baud rate problems

	The default modem type when no -M option is specified for Getty is
	a hays modem.  If you have a multimodem you can use -Mm and the
	baud adjust options for Getty.	Normally you specify a -B option
	for each baud rate the modem is capable of connecting at.  If the
	modem generates a CONNECT message you need only specify one -B
	option that is used to reset the modem and Getty will automatically
	handle the CONNECT messages.

	If your modem always talks to your Amiga at a given baud rate no
	matter what the CONNECT message says then use a single -B option to
	specify that baud rate then the -A option which tells getty to
	ignore any baud rate specified in the CONNECT message.

    (5) GETTY CRASHES or FREEZES, TERMINAL PROGRAMS or UUCICO FREEZES

	Due to bugs in the serial.device, it is possible that Getty
	and/or another program using the serial.device while Getty is
	active will crash or freeze.

	To get around these problems you MUST use the -d0 option to
	disconnect (+++ sequence), both for Getty and for UUCico.

				  OUTGOING CALLS

    Unfortunately Getty handles only incomming calls.  UUCico deals without
    outgoing calls itself.  Currently you must specify the proper baud rate
    in the L.Sys file for uucico to work properly. UUCico currently ignores
    any connect message.

    Disconnecting will work the same way Getty handles it.  If there is no
    Getty running disconnecting works by dropping DTR.


				NEWS

    RNews supposedly takes less memory now.  It still takes quite a
    hunk and you may run out, which will cause queue files to be
    left in your spool directory and possible temporary files in
    your news directory.

				 MAIL ADDRESSES

    If you have problems queuing mail check your L.sys file.  Try emailing
    to the adjacent node directly. E.G. if you can connect to 'foo' try
    emailing a test message to 'foo!postmaster'.  If you do not wind
    up with three queue files in UUSPOOL: then your L.sys file
    probably has a corrupted entry for foo.  Whenever you email to somebody
    three files should end up being added to UUSPOOL: and whenever you
    UUCico to a given machine the spool files in question should be deleted
    as they are sent.  When UUCico receives mail from the remote machine it
    will download the remote queue files to UUSPOOL: then uuxqt them. That
    is, the remote queue files should will be placed temporarily in
    UUSPOOL:, unpacked with rmail and placed in UUMAIL:, then deleted.

    The most common of all problems is an address like this:

    a!b!c!d!e!user%g

    In UUCP land this means:	a->b->c->d->e->g->user

    In ARPA land this means:	g->a->b->c->d->user

    To get around the problem you must determine the proper sequence
    and convert the address to SOLELY bang-paths (!).  DMail has a
    special variable ('help set' from dmail) that specifies fields to
    find the return address in which may be helpful.  For especially
    strange addresses you may have to look at the mail headers with
    the 'h' command from dmail.

			       REMOTE SHELL STARTUP

    You can cause Getty to start up a remote CLI with the following entry:

<login>,<password>,<gid-dummy>,0,(AuxShell),ram:,execute uucp:sc/UUShell

    where uucp:sc/UUShell is a simple script file.