SLOWSETUP.DOC

			    Matthew Dillon
			    891 Regal Rd.
			    Berkeley, Ca. 94708
			    USA

			    uunet.uu.net!overload!dillon


		    GETTING UUCP UP AND RUNNING FOR REAL


    This UUCP distribution in general is not for the uninitiated.  That is,
    it is not user friendly.  This particular document outlines a general
    installation procedure.  Be warned that there are a LOT of things you
    will have to do to bring up UUCP on your machine.

    This document shows a TYPICAL setup.  You will most likely want to
    modify the example to fit your own needs.  I cover all the points
    though.

    (1) You made backups of the distribution floppies, right?  DO NOT
	MODIFY THE DISTRIBUTION FLOPPIES.  The instructions below are
	long and some are complex and you may wish to refer to the
	original distribution diskettes if you accidently mess something
	up.


    (2A) Installing UUCP on a single floppy system.

	Well, it *is* possible, but difficult.	you need to make as much
	space as possible available on the main floppy.

	The second distribution disk contains only the source and manual
	pages.	I suggest you shuffle things around a bit.  You already
	have a copy of the first distribution diskette. I suggest you
	format a new disk and put the MAN directory of the second
	distribution disk on it.  Note that there is a MAN directory
	on the boot disk as well but this one contains only dmail.help
	which you need to gain online help from dmail.

	The following executables are required on the boot floppy and
	should not be moved off.  You should move as many of the remaining
	executables somewhere else as you can.

	    Required Executables in C

	    c/dmail
	    c/getty
	    c/rmail
	    c/uucico
	    c/rnews
	    c/uucp
	    c/unbatcher
	    c/dme	    (unless you configure your own editor)
	    c/sendmail
	    c/uux
	    c/uuxqt

	You will want to change the ASSIGNments in s/startup-sequence
	as follows:

	    Assign UUSPOOL:	UUCP:SPOOL
	    Assign UUMAIL:	UUCP:MAIL
	    Assign UUNEWS:	UUCP:NEWS

	These directories MUST be in nonvoltile storage or your USENET
	node will be unreliable.

    (2B) Installing UUCP on a duel floppy system.

	In this case very little shuffling is required.  I suggest
	the second floppy be used for UUSPOOL:, UULIB:, UUMAIL:, UUNEWS:,
	GETTY:, and UUPUB:.

	Format a new floppy (this will be your second floppy) and create
	directories as follows:

	    MakeDir df1:spool
	    MakeDir df1:mail
	    MakeDir df1:mail
	    MakeDir df1:news
	    MakeDir df1:pub
	    MakeDir df1:lib

	Modify the Assignments in s/startup-sequence of the boot floppy
	as follows:

	    Assign UUSPOOL:	df1:spool
	    Assign UULIB:	df1:lib
	    Assign UUMAIL:	df1:mail
	    Assign UUNEWS:	df1:news
	    Assign GETTY:	UULIB:
	    Assign UUPUB:	df1:pub

	Copy df0:lib to df1:lib and either delete or rename df0:lib to
	prevent confusion.  What we have done is move all dynamic storage
	to df1: .. files that will change a lot or require a lot of disk
	space.	Specifically, UULIB: was moved to DF1: because the
	sequence number file is kept in UULIB: and this is updated for
	each mail message sent.

    (2B) Installing UUCP on a Hard Drive

	Make a directory called UUCP on your hard drive somewhere.  And
	Assign UUCP: to it.   Copy the contents of both distribution
	floppies to your harddrive:

	    (put first disk in DF0:)
	    1> Copy df0: UUCP: ALL CLONE
	    (put second disk in DF0:)
	    1> Copy df0: UUCP: ALL CLONE

	It is easiest to keep all the directories in one place.  Note
	that a MAN directory exists on both distribution floppies, simply
	merge them together.

	Merge the startup-sequence on the boot floppy into your master
	startup-sequence.  Make sure you get all the Assigns and that
	they are properly reassigned to the appropriate directory on
	the harddisk.  Most people normally make a master UUCP: assign
	as a reference point to other assigns.


	Be sure that UUSPOOL:, UUMAIL:, UUNEWS: and UUPUB: are assigned
	to your hard disk instead of ram.

	You will most likely want to run DCron and Getty from your
	startup-sequence.  Be sure that UUCP:C is assigned *before*
	these programs are run so they pick up the appropriate path.

	If Getty interferes with any terminal program you might use
	you may be forced to BREAK it.	Remember to restart it to
	enable incomming UUCP calls again.

DCron
	DCron is an extremely useful utility to run, especially in
	systems with hard disks.  The only thing you have to watch out
	for is to be sure to BREAK it (kill it) before shutting off your
	machine.  DCron writes to its log file and runs other programs
	based on the date and you don't want to accidently turn off your
	machine when DCron has just started up some other program that
	may write to your hard disk.

	In the context of UUCP, DCron is normally used to automatically
	poll systems in the wee hours while you are asleep, to trim
	log files automagically, and maybe disable the modem's speaker
	while you are asleep (at least, that is what I use it for).

	Most people running UUCP leave their Amiga's on 24 hours a day.

			    Other System Directories

	Merge the mountlist into your master mountlist and copy any
	devices from l that you do not already have into your
	master l directory.

	merge or copy uucp:s/crontab to s:crontab and uucp:s/.edrc to
	s:.edrc .

	You can ignore files in uucp:system, they are standard system
	files.

		----	--  -	-   -	-   -	-  --	----

    (3)     Other startup-sequence efficiency considerations

	UUCP relies heavily on the Amiga's multitasking capabilities.
	Most programs execute other programs.  Many programs in UUCP:C
	may be made resident as shown by the pure bit being set.  You
	will probably at least want to make C:RUN resident if you haven't
	already.

	Depending on available RAM you may want to make certain other
	progams resident.  Here are some suggestions:

		uucp:c/dme	    ; run by dmail to edit mail
		uucp:c/uuxqt	    ; run by uucico to handle received files
		uucp:c/rmail	    ; run by uuxqt to handle received mail
		uucp:c/sendmail     ; run by dmail to handle outgoing mail

		(note that uucp:c/sendmail and uucp:c/rmail are the same
		 executable just renamed)

	STACK:	All programs should run with a stack of 8192.  This
	has been tested for all programs except RNews and ANews which
	may require more.

	RNEWS:	RNews currently takes a huge amount of memory and may run
	reliably only on machines with at least 1.5MB of ram.  Even with
	1.5MB you may need to run rnews manually instead of having it
	automatically run by uuxqt.  In this case rename the rnews
	executable to something else and create a dummy script file in its
	place (named as 'rnews') with the script bit set.

    (4)     System requirements

	Be sure you are running at least version 1.3 of the operating
	system.  The main consideration is that you are using at least
	the 1.3 serial device which fixes some bugs that existed in the
	1.2 serial device.

	The NULL: device is required, this is in the l directory of
	the boot floppy as already discussed.

	The UUSER: device is not required unless you want to start
	getting fancy with the Getty.  This is mainly a programmer's
	tool.

    (5)     Getty

	Normally one runs a Getty in his startup-sequence on the internal
	serial port (from which you wish to receive calls).  Currently
	only one Getty may be run PER SERIAL DEVICE NAME, and using other
	units of a given serial device will interfere with Getty's operation.
	This is due to the difficulty of implementation in Getty and will
	eventually be fixed (to fix the problem I have to patch into
	the OpenDevice and CloseDevice vectors).

	So for now you can really only run Getty on the internal serial
	device.

	Getty does its best to not interfere with comm programs and
	the like, but if a comm program refuses to run because it
	can't get exclusive access to the serial port you may have
	to kill the Getty by BREAKing it from a CLI.

	Refer to the manual page MAN:Getty for more information (for
	floppy based systems all manual pages are on the second
	distribution diskette).

    (6)     SHELL-STARTUP

	Assuming you are using the 1.3 Shell, the S:Shell-Startup file
	normally contains at least a Path command and Stack command to
	properly setup a newshell's path and stack.  Be sure the stack is
	at least 8192 for this distribution of UUCP and add the UUCP:C (or
	wherever you have placed the distribution executables) to your path
	list.  Older UUCP distributions (<1.03) required a huge stack, this has
	been fixed.

    (7)                   SITE-SETUP CONTROL FILES

	The following is a description of control and log files required
	for UUCP and how you must modify them to install your system.

	(GETTY: is normally Assign'd to UULIB:)

	GETTY:Getty-Header

	    This file contains the header line that is printed before a
	    login: prompt and is typically only two or three lines long.
	    The header usually contains your node name and the version of
	    the OS you are running under so people calling from term
	    programs know who you are.

	    (Getty can be used to run things other than uucico)

	    Modify accordingly.

	GETTY:Passwd

	    The password file is used by Getty to authenticate login
	    requests.  In the context of UUCP, remote UUCICOs that call
	    your machine up will provide a login and password.	Getty
	    handles this and if the login is valid and the password matches
	    will run the appropriate program found in the password file.

	    This is also where the directory corresponding to a ~user
	    specification is looked up.

	    Getty also deals with such features as automatic disconnect on
	    timeout and logs times for all incomming and outgoing calls.

	    In a serious system you should first remove all the junk
	    entries that come with the distribution.   You need an entry
	    for each remote machine you want to be able to call you.  You
	    do not necessarily need to give them logins that corrospond to
	    their machine names though this is how it is usually done.

	    In the future other programs will be able to be run from
	    a Getty.

	    Later versions of UUCP will implement MAILER-DAEMON type
	    stuff like 'unknown user', in which case the password file
	    will be used to define which user names are valid on the
	    system.

	GETTY:LOGFILE

	    The logfile is appended to by Getty whenever an incomming
	    call occurs or somebody takes over the serial port.  It
	    logs connect and disconnect times for incomming calls and
	    usage for external programs.

	UULIB:Domain

	    In nearly every case you will not need this file.

	    Those of you who wish to do domain routing through
	    their machine or have more than one default for
	    unknown destinations should refer to the manual
	    page MAN:Domains.

	UULIB:.Signature

	    .Signature is used by the Mail program and normally appended
	    to outgoing mail and news.

	    Modify accordingly.  DMail can be setup to use an alternate
	    file.  ANews will check <user>.signature before falling back
	    on .Signature.

	UULIB:Seq

	    The Seq file should exist but otherwise not be modified by
	    the user (except for setting it to a "1" once a year).  This
	    file is atomically updated and used to provide unique filenames
	    and mail IDs for outgoing mail.

	UULIB:Security

	    This file contains a list of allowed directories remote UUCP
	    transfers may read and write to.  Refer to the Security manual
	    page.  This file never contains the UUSPOOL: directory which
	    is implicitly read-write.

	    You need not modify this file now but should keep it in mind.
	    It protects your system in as much as I have been able to
	    close the loopholes.  Loopholes might still exist.

	UULIB:news.distribution

	    This file contains a list of news distribution idents for
	    various areas and must normally be modified according to
	    where you are.. you need to be a UUCP guru to do this.  Most
	    people can just leave it alone.

	UULIB:Config

	    This file contains configuration information for many
	    executables in UUCP:C and should be modified accordingly.

	    Be sure you modify at least the following entries.	REFER TO
	    THE 'Assigns' MANUAL PAGE.

		NodeName
		UserName
		RealName
		NewsFeed    (not required if you don't care about news)
		Organization
		TimeZone
		DefaultNode
		Editor

	    **** Take some time to pick a node name for yourself.  It
		 should be no more than 8 characters long.  Some UUCP sites
		 barf at node names longer than 6 chars so if you are not
		 sure of your neighbors pick one no more than 6 characters
		 long.	Your site name should be in lower case.

		 In anycase, the first 6 characters MUST be unique.

	UULIB:L.Sys

	    This file contains site information for sites that may call
	    you up or you may call up.

	    You must modify this file appropriately before you can run
	    UUCico and other UUCP related programs.  Refer to the 'L.Sys'
	    manual page.

	UULIB:Aliases

	    This is a mail aliases file with aproximately the same
	    power as /usr/lib/aliases on UNIX systems.	You should
	    refer to the 'Aliases' manual page and modify this file as
	    appropriate for various defaults like 'postmaster'... to
	    whatever user name you pick for yourself.

	UUCP:S/Crontab

	    This is a functional Crontab file for use with the DCron program.
	    This file is normally moved to S: (it is useless in UUCP:S).

	UUSPOOL:LOGFILE

	    UUCICO and other programs log errors and other things to
	    this file.	Normally you use DCron to clean up this and
	    other log files once daily to keep them from getting to large.


    (8)     TESTING / DMAIL

	You will next want to test your UUCP configuration.  If testing
	with a friend's Amiga running the same distribution simply
	email to him, then one of you run uucico -s<remotesystem>
	just like in QuickSetup.DOC, except this time you are using
	the system name he picked instead of 'test1' or 'test2'.

	If the initial tests in QuickSetup.DOC worked and the system
	is not working now check the following (common problems):

	    (a) the login and password in your L.Sys file (that uucico uses
		to login to the remote machine) matches the login and
		password in the remote machine's Getty:Passwd file.

	    (b) There is an entry for your node in the remote machine's
		L.Sys file and vise versa

	    (c) The telephone number is correct

	    (d) the node names are all in lower case

	    (e) you constructed the email address correctly (nodename!user)

	I suggest you get UUCP running with a friend before getting it
	running with a UNIX system as it is easier to test it with a
	friend.

	Assuming you email to the user name he picked for his UULIB:Config
	'UserName' entry and he did the same thing to you, entering
	'dmail' without any arguments will bring up the mail shell
	and allow you to read the message after transfer via UUCico
	is complete.  You can check that the email actually arrived
	into the right mail box in UUMAIL: by simply getting a directory
	of UUMAIL:

	READ the manual page for DMail for information on the
	construction of mail paths to other systems and users.