SetCPU V1.4
                         by Dave Haynie 
                  (released to the public domain)


          This program is designed to allow the user to detect and modify
  various parameters related to 32 bit CPUs in Amiga computers.  This program
  began life as "WhatCPU", which did little more than read the proper place
  in ExecBase and report what kind of CPU/FPU was in the system.  The first
  version of SetCPU added the capability to identify a 68030 and to change the 
  cache parameters of the 68020 and 68030 systems.  The recently released
  SetCPU V1.3 also did tests for 68882 vs. 68881, and for the presence of an
  MMU.  It was supposed to allow for checking of a particular thing in a
  startup sequence, but unfortunately the CHECK code in V1.3 was broken.

          That brings us up to V1.4.  As well as fixing and extending the CHECK
  code, SetCPU V1.4 also has some simple MMU code to allow 32 bit systems with
  MMUs to copy ROM into RAM and then relocate this RAM as ROM, thus greatly
  enhancing the speed of ROM based operations.  This "FASTROM" code isn't
  extremely sophisticated, and could possibly run into trouble on other 32 bit
  systems, but it has been tested on the A2620.  It will certainly have to be
  rethought to work properly with memory outside of the 68000 compatible 24 bit
  address space.

          In any case, the syntax of the program is given as follows:

                  SetCPU [INST|DATA] [[NO]CACHE|[NO]BURST]
                         [[NO]FASTROM [TRAP]] [NOMMUTEST]
                         [CHECK 680x0|68851|6888x|MMU|FPU]

  where "[]" indicates an optional parameter, "|" indicates a choice of
  parameters.  Typing "SetCPU ?" will retrieve this same syntax diagram.
  Typing SetCPU alone will result in the SYSTEM configuration being
  send to the console, my current system returns this:

          SYSTEM: 68020 68881 68851 FASTROM (INST: CACHE)

  This indicates I have a 68020/68881/68851 system (eg, standard A2620), I've
  previously installed the FASTROM translation, and my instruction cache is
  turned on (done by AmigaOS V1.2 or V1.3).  Note that any parameters that
  don't make sense to the real system configuration, such as asking to modify
  the data cache on a 68020 system or install the FASTROM translation on a
  68000 system are just ignored.

          The individual commands are given below in detail:


  [NO]CACHE
          This command will switch on or off 68020 and 68030 caches.  If
          not qualified, it'll act on both instruction and data caches of
          the 68030.

  [NO]BURST
          This command will switch on or off the burst cache line fill
          request of the 68030.  If not qualified, it'll act on both
          instruction and data caches.

  INST
          This preceeds a CACHE or BURST operation to restrict it's application
          to the instruction cache only.

  DATA
          This preceeds a CACHE or BURST operation to restrict it's application
          to the data cache only.

  [NO]FASTROM [TRAP]
          This activates the FASTROM translation on or off an MMU equipped 
          system.  When switching on, it first allocates 256K of memory for
          the ROM image, then currenly 512 bytes of memory for the MMU table.
          It copies the ROM into the image area, then applies the translation
          by pointing the MMU at the table and activating it.  The TRAP option
          causes the MMU to look at all 32 bits of address; access to any
          memory outside of the 24 bit space will result in an exception, which
          if unhandled, results in a GURU 2.  When TRAP is not specified, the
          MMU is only looking at 24 bits of address space.  This is the mode
          you'd normally run in.  Under V1.3 and earlier releases, a DOS bug
          can cause invalid accesses, which cause the exception, when running
          the EndCLI or NewCLI/NewShell programs; running untrapped will avoid
          gurus with these commands.  It's still possible to run into an
          exception when running without the TRAP option.  One easy way is
          writing to the ROM image, which is write protected by the MMU.  The 
          NOFASTROM option will switch off the MMU and reclaim the memory used
          for the ROM image and MMU table.  Note that this is achieved by
          locating these items via the appropriate MMU registers.  If any other
          program set up the MMU for something, this could be a very bad thing
          to do.  In general, until there's some level of OS support for the
          MMU in Amiga systems, you're really safe using only one MMU tool at
          a time.

  NOMMUTEST
          This option won't normally be necessary.  However, some 68020 boards
          out there apparently have hardware bugs of some sort that make
          testing for the MMU impossible, at least as near as I can tell.  If
          your 68020 board freezes, or crashes with some kind of coprocessor
          protocol violation GURU (probably numbers $0D or $0E), you have a
          problem with your 68020 board.  The most common bug is the 68020
          board hardware failing to fully decode CPU space, such that the FPU
          in the system also responds to the MMU's address space.

  CHECK 
          This option lets you check for the existence of a particular
          CPU system component in a script.  It works like this:

                  SetCPU CHECK 68020
                  If WARN
                          echo "No 68020 here!"
                  Else
                          echo "Sho nuff got a 68020 here!"
                  Endif

          The arguments to CHECK can be any of:

                  68000   Matches the obvious
                  68010   "
                  68020   "
                  68030   "
                  68851   "
                  68881   "
                  68882   "
                  FPU     Matches 68881 or 68882
                  MMU     Matches 68851 or 68030

  That's about it.  As mentioned, this code is public domain, and you're
  free to do anything with it you like.  Even make it better!  For any real
  MMU programming, I'd recommend both "MC68030 Enhanced 32-Bit Microprocessor
  User's Manual" and "MC68881 Paged Memory Management Unit User's Manual",
  both from Motorola.  There are some differences between the two, please make
  sure, if you're writing any MMU code, that you either write code that works
  on both, or you specifically check for each MMU and act accordingly.

  Also note that much of what SetCPU does may be wrong in a future release of
  the OS, so it's a very bad idea to put any of this stuff in a commercial
  program.  Things like identifying the MMU, CPU, or FPU that aren't fully
  done in 1.3 may still work in a future OS release, but if that OS is
  correctly identifying the MMU, CPU (eg, 68020 vs. 68030), or FPU (eg,
  68881 vs. 68882), SetCPU should be using the OS's opinion of these items,
  not testing itself.  On a more drastic note, if an OS ever starts using
  the MMU, the FASTROM code will certainly break.  It's the job of the OS to
  arbitrate the MMU, and if the OS is doing that, no legal program would be
  able to come along and muck with the MMU registers without reeking havoc
  on the operating system.

  One final note, if you have a 68020 board that locks up without the
  NOMMUTEST option, you'd be wise to express your concerns to the vendor
  of that board.  There's an awful good chance that if, in the future,
  Amiga releases an operating system that knows about the MMU, it'll test
  for it in some way, probably similar to what I do here.  If your board
  locks up on MMU operations, you may not be able to run this future OS
  on your 68020 board.  Maybe the vendors can fix these now, instead of
  later when you really need this fixed.

                          -Dave Haynie
                           PLINK:         D-Dave H
                           bix:           hazy
                           usenet:        {uunet,rutgers}!cbmvax!daveh