PostScript shared library interface (post.library, with Post V1.3)
==================================================================

Copyright Adrian Aylward 1990.

Free use and non-commercial reproduction of the binaries of the interpreter
library (post.library) is permitted, providing that the copyright notices
are not removed.  Distribution by disk libraries is permitted provided only
a nominal copying fee is charged.

All other rights are reserved.

Introduction
============

The file "post.library" is an Exec library containing the PostScript
interpreter.  It is designed to be shareable between different processes,
supporting arbitrarily many PostScript activations - at least until you
run out of memory.

This file should be read in conjunction with the header file "postlib.h".

The standard user interface source files are distributed with Post.  Read
them as examples.

Activation Records
==================

Simultaneous multiple activations of PostScript are allowed.  Before using
post.library you must first open it by a call to OpenLibrary.  To create
an activation you then call PScreateact which returns a pointer to the
activation record.  You can then make calls to the interpreter library,
passing the activation record pointer as an argument.  You can create
several activations, possibly from different processes and intermingle
the interpreter calls if you wish.  When you have finished with an
activation, call PSdeleteact to delete it and free the memory it used.
When you have finished with the library call CloseLibrary; if no other
processes have it open, then Exec can remove it from memory if the space
is needed.  (N.B. if the space is not needed, the library will remain in
memory in case it is opened again.)

N.B. the library can only be called from a process, as it calls various
AmigaDOS functions.  It should be possible to pass activation records
between processes (I think) but I have not tested it.

The Parameter Block
===================

The parameter block is the argument to PScreateact.  It is specifies the
addresses of the bitmap planes, size of the page, and the amount of memory
to be allocated for the activation etc..  Its format is defined in the
header file.

N.B. all ints are 32 bits, shorts are 16 bits.

The page size is limited to 30000 pixels.  The densities (pixels per inch)
may be any strictly positive integer value.  The y direction may be set
to +1 - if the bitmap rows are in PostScript order (bottom row first) or
-1 - Amiga order (top row first).

    page.buf[24]        Bitplane pointers, up to 24
    page.len            Size in bytes of each plane
    page.depth          Number of planes (must be 1,3,4)
    page.reserved       Reserved, must be zero
    page.xbytes         Number of bytes in each row
    page.xsize          Number of pixels in each row
    page.ysize          Number of rows
    page.ybase          Base of current band
    page.yheight        Total height of full page, for band rendering
    page.xden           X density
    page.yden           Y density
    page.ydir           Y direction

As a starting point for memory sizes try the values following.  If you load
many fonts you will need to increase the size of the VM.  The other sizes
should prove adequate for even the more complex programs.

    memvlen    280000   VM
    memflen     60000   Font cache
    memllen     60000   Path lines
    memhlen     20000   Halftones

The user data pointer is intended to be used to identify multiple
activations.  You can set it to any value you like.  The function pointers
are described below.

    userdata            User data pointer
    flushfunc           Flush page function pointer
    copyfunc            Copy page function pointer

The standard input and output streams are the DOS file handles to be used
by the interpreter for %stdin, %stdout, %stderr.  Also the standard output
is used for prompts and the error output for error messages.

    infh                Standard Input file handle
    outfh               Standard Output file handle
    errfh               Standard Error file handle

The rest of the block is reserved and must be set to zero.

Function Pointers
=================

There are two function pointers within the parameter block, which are used
when the interpreter needs to call routines supplied by its client.  If
the pointers are zero the calls are skipped.

To help identify calls from multiple activations, the activation record
address is also passed in a0 and the userdata pointer in a1.

      flushfunc(d0: int y1, d1: int y2)

Flush the bitmap to the screen.  The interpreter calls this function after
a painting operation has updated the bitmap.  Then if the output is being
viewed interactively the client can update the screen or window.  The
arguments are the range of bitmap rows (y1 ... y2-1) that may have been
updated.

      copyfunc(d0: int num)

Copy the page to the output device.  The argument is the value of #copies,
which should be taken into account if the output is to a printer, but is
not meaningful for screen output.

Library Entry points
====================

Prototypes and pragmas for the entry points are defined in the header file.

  Create a PostScript activation

          d0:int arec = PScreateact(a1:struct PSparm *parm)

The result is the address of the new activation record.  If the activation
fails an error code is returned instead - zero if the interpreter failed
to start at all because there was insufficient free memory, or an
interpreter error code if there was an error during initialisation.
Otherwise the result is the address of the activation record.  The result
is always returned as an int.  If is is greater than errmax then the
activation was successful, and the value is an address; otherwise the
activation failed, and the result is zero or an error code.

  Delete a PostScript activation

          PSdeleteact(a0:APTR arec)

The activation record is deleted and the associated memory is freed.

  Interpret a string or file

          d0:int errnum = PSintstring(a0:APTR arec, a1:char *string,
                                      d0:int length, d1:int flags)

If the flag PSFLAGSTRING is set, the contents of the string are interpreted
as PostScript source.  If the flag PSFLAGFILE is set, the string is a file
name, whose contents are interpreted.  If neither of these flag bits are set
the string is ignored, but the other flag bits still have their effects; if
both are set the result is undefined.

If PSFLAGINTER is set (when interpreting a file), the file is considered to
be interactive.  The banner is printed, and the interpreter prompts for each
line of input from the file.

If PSFLAGCLEAR is set, then after interpretation the operand stack is
cleared and the dictionary stack is popped until only the system and user
dictionaries remain.

If PSFLAGESAVE is set, the vm is saved before interpretation begins and
restored afterwards.  You would normally use PSFLAGCLEAR with this option,
to prevent invalidrestore errors.

If PSFLAGERASE is set, then the page is erased.  This happens right at the
end, after any vm restore, so the page is erased taking into account the
restored transfer function(s).

  Signal an interrupt
 
          PSsignalint(a0:APTR arec, d0:int flag)

This routine may be called to set (flag = 1) or clear (flag =0) the
interrupt signal flag.  The interpreter tests this flag at the head of its
main loop, and also within certain potentially length operators (=, ==,
stack and pstack).  If the flag is set it generates an interrupt error.
You may safely call this routine at any time during the like of the
activation.  It is intended to be called from within your task's
exception handler, if the CTRL/C break signal is set.

  Signal a floating point error

          PSsignalfpe(a0:APTR arec)

This routine is intended to be called whenever a floating point trap is
generated by the interpreter.  It generates an immediate undefinedresult
error.  You must not call it at any other time; if you do you will crash
the machine.  It is only useful if you are using the version of the library
compiled for the 68881 FPU or compatible chips.  (The software floating
point routines do not generate traps).  Before calling the library you
should set up a trap handler and set the bits in the fpcr register to
enable the traps.  (If you do not set up the traps, the FPU will substitute
the special value not-a-number for the result and continue.  The
undefinedresult error will not be triggered, and results of your program
may be incorrect.)  If you application does not use the FPU you can simply
direct all traps to the library, otherwise it is essential that you
ensure that you only call this routine if the trap derived from the library
and not your own code.

  Error

          PSerror(a0:APTR arec, d0:int errnum)

This routine is intended to be called from within your own flush or copy
page functions, to signal that an error ocurred.  You must not call it at
any other time; if you do you will crash the machine.  The values for the
error number are defined in the header file.

Versions
========

The version distributed with Post V1.3 has version number 1, revision 3.