===========================================================================
================================= Lh v1.8 =================================
===========================================================================
        A data compression system for the Commodore Amiga computer
           written by Holger P. Krekel and Olaf 'Olsen' Barthel
                  © Copyright 1990, all rights reserved.

============================== What is `Lh'? ==============================
===========================================================================
Do  you  know LhArc?  If you do, you will probably remember the compression
ratio  (astonishing!)  and  the  time  required  for  data  compression and
decompression (a lot!).
   It  took  us  more than three months to create an MC680x0 version of the
data compression / decompression routines (we have `baptized' the resulting
package  "Lh").   Special  stress  has been put on two features:  speed and
efficiency.   Lh  is much faster than any other implementation of the LhArc
data  compression  /  decompression routines and generates about 2% smaller
data files.  Unfortunately, the data files are incompatible with the output
produced  by  the  standard  LhArc  routines,  i.e.   data  files cannot be
exchanged between both implementations.

============================ Performance of Lh ============================
===========================================================================
The  following  tables  give a brief overview on the performance of Lh.  We
compared  Lh  to  the following popular data compression programs:  LhArcA,
The  Imploder  & PowerPacker.  `Compression' and `Decompression' denote the
time  required  to execute the approriate action.  The duration is given in
minutes.

1. Picture, 320x256, (32 colours), hand-drawn, 1 pixel = 1 byte
---------------------------------------------------------------
Input length in bytes: 81920

             Output Compression Decompression
Lh           11838  01:56       00:01
LhArcA       11849  02:04       00:10
The Imploder 13076  01:41       00:01
PowerPacker  14868  00:30       00:01

2. Picture, 320x256, (32 colours), hand-drawn, bitplanes
--------------------------------------------------------
Input length in bytes: 51200

             Output Compression Decompression
Lh           13870  01:27       00:02
LhArcA       14041  02:40       00:10
The Imploder 15342  02:40       00:01
PowerPacker  15840  00:27       00:01

3. Picture, 640x400, (16 colours), sampled, 1 pixel = 1 byte
------------------------------------------------------------
Input length in bytes: 256000

             Output Compression Decompression
Lh           76428  03:01       00:06
LhArcA       77970  04:05       00:38
The Imploder 93152  09:12       00:08
PowerPacker  90728  02:20       00:08

4. Picture, 640x400, (16 colours), sampled, bitplanes
-----------------------------------------------------
Input length in bytes: 128000

             Output Compression Decompression
Lh           81886  01:02       00:09
LhArcA       81580  01:42       00:44
The Imploder 93152  09:12       00:02
PowerPacker  86956  01:52       00:06

5. Executable file, Amiga-hunk format
-------------------------------------
Input length in bytes: 130964

             Output Compression Decompression
Lh           71330  01:07       00:08
LhArcA       77970  01:48       00:34
The Imploder 73172  08:23       00:03
PowerPacker  74208  01:40       00:06

6. ASCII file
-------------
Input length in bytes: 81627

             Output Compression Decompression
Lh           32596  00:35       00:04
LhArcA       33091  00:54       00:17
The Imploder 37166  03:50       00:02
PowerPacker  38700  00:39       00:03

============================ Supplied material ============================
===========================================================================
                This package includes the following files:

      Lh.doc ......... The file you are currently reading.

      lh.library ..... Amiga shared-reentrant runtime library containing
                       compression / decompression and auxilary routines.
      lhglue.lib ..... Library glue routines (blink/ln format).
      LhGlue.LZH ..... Library glue source codes.
      lhlib.h ........ Library support header file.
      lh_lib.fd ...... Library function definitions.

      Decode.bin ..... Decompression routines in raw binary format.

      LhDecode ....... Demonstration data decompression tool.
      LhDecode.c ..... Source code for the above.
      LhEncode ....... Demonstration data compression tool.
      LhEncode.c ..... Source code for the above.
      MakeFile ....... Script file to create the demonstration tools.
      PreInclude.c ... Global definitions and includes (to be precompiled).

================================== Usage ==================================
===========================================================================
As  shown above, Lh is based on two files:  the library which contains both
the  compression  and  the  decompression  routines  as  well  as  auxilary
routines.   Decode.bin  has been included for assembly language programmers
who  want  to take advantage of Lh in standalone applications which are not
to require the library.
   In order to use the routines, your application has to open lh.library by
calling  OpenLibrary.   The current library revision supports four standard
functions which are described below:

                                     *

CreateBuffer - Allocate auxilary buffers required by the compression and
               decompression routines.

Usage: LhBuffer = CreateBuffer(OnlyDecode)
          D0                       D0

   This function call allocates and initializes an LhBuffer structure to be
passed to the data compression / decompression routines.  In respect to the
library  routine to call with the buffer structure, `OnlyDecode' can be set
to  TRUE  if  a  small  buffer  (4500  bytes  in  the  current  revision of
lh.library) is required for data decompression.  Pass FALSE to CreateBuffer
to  allocate  a  larger  buffer  (40000  bytes  in  the  current release of
lh.library)  suitable both for data compression and decompression.  A value
of NULL (= 0) is returned if the memory allocation fails.

                                     *

DeleteBuffer - Free auxilary buffers allocate by CreateBuffer

Usage: DeleteBuffer(LhBuffer)
                       A0

   Passing  an  LhBuffer  structure previously allocated by CreateBuffer to
this routine will free all associated resources.

                                     *

LhEncode - Perform adaptive Lempel-Ziv-Huffman data compression

Usage: Size = LhEncode(LhBuffer)
        D0                A0

   The  real  data  compression  is  handled  by this routine.  The calling
parameter  is an LhBuffer structure as initialized by CreateBuffer.  It has
the following format:

        struct LhBuffer
        {
        /* 0*/  APTR  lh_Src;
        /* 4*/  ULONG lh_SrcSize;

        /* 8*/  APTR  lh_Dst;
        /*12*/  ULONG lh_DstSize;

        /*16*/  APTR  lh_Aux;
        /*20*/  APTR  lh_AuxSize;

        /*24*/  ULONG lh_Reserved;
        };

lh_Src ........ Points to the beginning of the memory region to compress.
lh_SrcSize .... Denotes the size of the source memory region.

lh_Dst ........ Points to the beginning of the memory region  to  send  the
                compressed data to.

                NOTE: 1) lh_Src and lh_Dst _M_U_S_T_ _N_O_T_ overlap!

                      2) The size of the memory region pointed to by lh_Dst
                         MUST  be  1/8  larger  than  the  size  stored  in
                         lh_SrcSize!

lh_DstSize .... Size of the memory region to send the compressed data to.

lh_Aux,
lh_AuxSize .... Private data, DO NOT TOUCH!

lh_Reserved ... Currently unused, leave it zero.

   The  size  of  the compressed data will both be stored in lh_DstSize and
returned  in  D0.   In  its worst case, the compressed data will become 1/8
longer  than the source data which is the reason why the destination memory
region has to be exactly 1/8 larger than the source region.  If you fail to
add this safety-distance innocent memory may be overridden!
   This  function  call  returns  zero  (=  0)  if the LhBuffer hasn't been
initialized correctly or the buffer allocated by CreateBuffer is too small.

                                     *

LhDecode - Perform adaptive Lempel-Ziv-Huffman data decompression

Usage: Size = LhDecode(LhBuffer)
        D0                A0

The  real  data  decompression  is  handled  by  this routine.  The calling
parameter  is  an  LhBuffer  structure  as  initialized by CreateBuffer and
listed below:

        struct LhBuffer
        {
        /* 0*/  APTR  lh_Src;
        /* 4*/  ULONG lh_SrcSize;

        /* 8*/  APTR  lh_Dst;
        /*12*/  ULONG lh_DstSize;

        /*16*/  APTR  lh_Aux;
        /*20*/  APTR  lh_AuxSize;

        /*24*/  ULONG lh_Reserved;
        };

lh_Src ........ Points to the beginning of the memory region to decompress.
lh_SrcSize .... Denotes the size of the source memory region.

lh_Dst ........ Points to the beginning of the memory region to send the
                decompressed data to.

                NOTE: The size of the memory region pointed  to  by  lh_Dst
                      MUST be larger than or equal  to  the  original  size
                      of the data before compression.

lh_DstSize .... Size of the memory region to send the decompressed data to.

lh_Aux,
lh_AuxSize .... Private data, DO NOT TOUCH!

lh_Reserved ... Currently unused, leave it zero.

   The  size of the decompressed data will both be stored in lh_DstSize and
returned in D0.
   This  function  call  returns  zero  (=  0)  if the LhBuffer hasn't been
initialized correctly.

                                     *

   Do not allocate an LhBuffer of your own and do not peek or poke into the
private  fields  following  the  public  portion of the LhBuffer structure!
Future  library  versions  may  support  more  structure  tags  or  require
less/more memory for data compression / decompression.
   As  far  as  error  checking  is  possible  within  the library, illegal
arguments  (such  as passing NULL to a library function or leaving parts of
the  LhBuffer structure uninitialized) are rejected.  Bear the notes on the
lh_Dst  memory  region  in  mind  to  avoid  unexpected  results and system
crashes!
   Due  to  limitations in the tree structure built by the data compression
routine  more  than 65535 equal bytes in a row can - but need not - lead to
problems.   The  same  difficulties  arise with the original LhArc program.
The  most  imminent tree construction error to be found in the original 'C'
program has been fixed in Lh.
   As  a  rule of thumb, the longer the data compression takes, the smaller
the resulting compressed data file will become.

   Examples  how  to  access  the lh.library routines from 'C' are supplied
through  `LhEncode.c'  and  `LhDecode.c'.  Both programs have been compiled
using  the  Manx Aztec 'C' Compiler version 5.0d and require arp.library to
run.  Feel free to send us assembly language demonstration programs.

========================== How to use Decode.bin ==========================
===========================================================================
The Decode.bin data file was added to support standalone applications which
are  not to require the library to perform data decompression.  The file is
a raw dump of the assembly language decompression routine which can also be
found  in the library (i.e.  it obeys the Amiga library calling conventions
in  preserving  all  registers  except  for  d0/d1  and a0/a1).  Result and
calling  parameter  are the same as with LhDecode.  Note that you will have
to  initialize  the auxilary decompression buffer on your own.  The pointer
to  the  buffer  immediately  follows  lh_DstSize and must be at least 4500
bytes  in  size.   The  single  decompression  routine does not require the
Reserved long word.
   Since   the   decompression   routine  uses  pc-relative  adressing  and
pc-relative  branches  only  it  can  be  freely relocated and moved to any
memory location.  The raw code will work fine on any MC680x0 based computer
system (Apple MacIntosh, NeXT, SUN workstations, Atari ST/TT, etc.).
   Here's the beef, an example assembly fragment follows:

   ; This is just an example, don't expect too much!

   ; Decode - Decode data previously encoded by LhEncode

   ; Inputs:  d0 - size of source region
   ;          a0 - pointer to source region
   ;          a1 - pointer to destination region
   ;          a2 - pointer to beginning of auxilary buffer (4500 bytes)
   ;
   ; Outputs: d0 - size of destination region (after decompression)

   ; Note:    Previous contents of d0/d1, a0/a1 must be considered
   ;          gone.

   Decode: clr.l   -(sp)         ; Size of auxilary buffer (unused)
           pea     (a2)          ; Auxilary buffer

           clr.l   -(sp)         ; Size of destination buffer (unused)
           pea     (a1)          ; lh_Dst

           move.l  d0,-(sp)      ; lh_SrcSize
           pea     (a0)          ; lh_Src

           lea     (sp),a0       ; At this point we have created a
                                 ; properly initialized LhBuffer-
                                 ; sized structure right on the stack.

           lea     DecodeDump,a1 ; DecodeDump is the starting address
                                 ; of Decode.bin (can be located
                                 ; anywhere).

           jsr     (a1)          ; Decompress data...

           lea     6*4(sp),sp    ; Restore previous stack pointer

           rts                   ; and return

   While the library code includes a couple of sanity checks the Decode.bin
raw  code  is  the  bare-bone decompression routine only.  You will have to
make  sure  that  the values you are calling the routine with make sense to
avoid undefined behaviour.
   Think  twice  before  using  the  raw  code instead of the library.  The
library  code  can be shared by a number of applications while the raw code
cannot.

================================= Credits =================================
===========================================================================
The  original  Lzhuf.c  adaptive  Huffman compression code was developed by
Haruyasu Yoshizaki, thanks a lot for placing it in the public domain.

============= Shareware fee & how to become a registered user =============
===========================================================================
A good amount of time and work was required to create Lh and the associated
utilities.   Needless  to say, we didn't do it just for fun.  Include Lh in
any  program  which  has  need  of  it  but  don't  forget  us!  Any humble
contribution  of  at  least,  say  15$  US  or  DM  20,-  will  insure your
registration  (i.e.   you will receive Lh updates as they become available)
and  encourage  us  to  continue working on Lh (we know that Lh can be made
faster  and more efficient with a bit of extra work, but time - we both are
students of Medical Informatics at Hildesheim, Germany - does currently not
permit us to make severe enhancements).

  Please keep the following in mind if you include Lh in your program(s):

Public domain program - No need to register Lh with us as  long as  you  do
                        not intend to make money with your program.

Shareware program     - Register Lh with us once to distribute an unlimited
                        number of copies of your program.

Commercial program    - Lh will need to be licensed for each copy  of  your
                        program.

Lh was written by Holger P.  Krekel & Olaf 'Olsen' Barthel.  Copyright 1990
by  Holger  P.   Krekel  &  Olaf  'Olsen'  Barthel.   Shareware, all rights
reserved.   No  guarantee of any kind is made that the program(s) described
in  this  document  are  100%  reliable.  You use this material on your own
risk.

                Send suggestions and registration fees to:

                           Olaf 'Olsen' Barthel
                             Brabeckstrasse 35
                            D-3000 Hannover 71

                        Federal Republic of Germany


=============== Revision history (most recent change first) ===============
===========================================================================

V1.8    Bumped the minimum sequence length LhEncode starts to compress to 2
        bytes which makes compression both faster and more efficient.

V1.7    First public release.

V1.0-   Not released.

                                  *

             Do only its possibilities make it an Amiga?

                        WHERE IS THE MAGIC ???