NAME:     forward - packet radio mail forwarding program.AUTHOR:     Eric Williams  WD6CMU, 71336,1424SYSTEM CONFIGURATION:     OS9/68K, MW C v2.0SYNTAX:     forward [options] <port> <callsign> <callsign>...DESCRIPTION:     forward allows for mail forwarding to other W0RLI-compatible packetradio mailboxes.  It integrates both with the mailbox mail database andthe host mode translator program.     The first argument to forward specifies the port through which thetarget mailbox(s) can be connected to.  It is the device name (minus the'/') of the SCF device which is connected to the TNC.  This device mustalso have associated with it a background task which is running the hostmode translator (host).  The port name is used to build the names of pipesthrough which forward communicates with host.     The remainder of the arguments specify the callsigns of themailboxes to which mail might be forwarded.  These callsigns aretranslated into file names and these forwarding files are assumed toexist in the directory FWDIR directory as defined in mailbox.h. Translation involves appending ".fwd" to the callsign and translatingthe hyphen for the ssid (if any) to underline.  For example, "w6cus-1"would become "w6cus_1.fwd".  If the forwarding file does not exist,forwarding to that mailbox is aborted.      Forwarding files are text files which contain information about thepath or paths to that mailbox and callsigns of stations whose mail shouldbe sent to the mailbox.  If a line in the forward file begins with "VIA",the remainder of the line is used as a path for connection to the mailbox. If more than one such lines are in the forward file, connection will beattempted using the first such path.  Should that fail, the second pathwill be tried, and so on until the last path.  If no "VIA" lines arepresent in the forwarding file, the path is assumed to be a direct connect. Callsigns in a VIA line that have a leading "*" specify NET/ROM nodes. An "*" all by itself as the last call indicates that the station is a G3RUHnode, and that the "BBS" command is needed to access the mailbox port.     Lines which begin with "@" contain a filename path to anotherforward file which will be inserted into the current file at that point. Such inserted files may contain other insertion lines.  (Note thatrelative paths are relative to /dd/MAILBOX.)     Lines that begin with a ";" are comments and are ignored by theprogram.     Other lines in the forward file are assumed to contain a singlecallsign.  Wildcard characters are allowed in these callsign lines: a '?'will match any single character, while a '*' will match any number of anycharacters     The sequence of events during execution of forward is as follows: Thefirst forward file is opened and its contents read.  Then the mail databaseis searched for any messages destined for this mailbox.  If there are any,then communication with the host translator is established.  Using thefirst of the paths specified in the forward file, a connection with themailbox is attempted.  If the link fails, then the next path in the file isattempted.  Once connection is established with the mailbox, the messagesfor it are sent and then deleted from the mail system (except for type Bmessages or those to a distribution designator).  The next mailbox in thecommand line is then processed.      Distribution designators are special BBS addresses that indicatethat messages to these addresses should be copied to more than one BBS. Distribution designators are specified by placing a file with a nameconsisting of the designator followed by ".dis" in the directoryspecified by the DISDIR definition in mailbox.h.  These files contain alist of bbs callsigns (one per line, no SSID) to which bulletinscarrying the designator are to be distributed.  IMPORTANT NOTE: Thedesignator address must also appear in each of the forward filescorresponding to the BBSs listed in the distribution file.      As the bulletins is forwarded to each BBS in the distribution list,that BBS is checked off in a bit field in the mail directory record for thebulletin.  This 16-bit field can be examined by using the 'E' option tothe list command of the mailbox program and is displayed as a 4-digit hexnumber, the LSB of which corresponds to the first BBS in thedistribution list, etc.  Examining the value of this field and comparingit to the distribution list file corresponding to the message's addresscan help the sysop to diagnose forwarding hangups.     The following options are currently available:     -r       Inhibit reverse forward prompt.     -s       Don't do any forwarding, but only prompt for reverse forward.     -m<num>  Set the maximum connect time to <num> minutes.  (Note that              reverse-forwarding is under control of the other system,              and that the connect time cannot be limted by this option.)     -b<num>  Set the maximum forwarded message size to <num> kilobytes.     -p<str>  Set the message type priority.  <str> is one or more              characters, each one specifying a type of message that              will be forwarded before other types.  The message types are:                   *  any message                   p  any non-bulletin message                   x  any message of type 'x'              For example, the option "-pt*" means to forward NTS              messages (type 'T'), and then any other messages.  Note              that this option may have to be quoted to prevent wild-              card expansion by shell.     Periodic execution of forward can be accomplished with the crondaemon.  Messages that have been successfully forwarded will create anentry in /dd/MAILBOX/logfile with the callsign "AUTOFW".  The entry willuse the code 'f' and be followed by the message number and the callsign ofthe mailbox forwarded to.  Mail which has been refused forward by the otherBBS will be entered with the code 'r' in the log file, followed by the textof the message sent by the refusing BBS.      Verbose debugging output is created by forward during operation ifit was compiled with the DEBUG flag defined.  This can be used to trackits progress and any problems in its execution.  If such output is notdesired, it can be redirected to the /nul device. BUGS:     forward has been known to hang during the forwarding process forunknown reasons.  The sysop should check regularly to make sure hissystem is operating properly.