NAME:     host - WA8DED host mode translator.AUTHOR:     Eric Williams  WD6CMU, 71336,1424SYSTEM CONFIGURATION:     OS9/68K, MW C v2.0SYNTAX:     host <path>DESCRIPTION:     The  WA8DED host mode translator (host) allows programs to enjoy anOS9 standard I/O interface with a packet radio TNC.  host will poll theTNC for data via the serial line and unpack the data, passing it to theapplication program via a pipe.  Similarly, data from the application isread from a pipe, separated into packets, and passed to the TNC.  Multipleconnections are supported and is integrated with OS9 multi-tasking.     The argument to host must be a path to a SCF-type device which isconnected to a TNC running WA8DED host mode firmware.  It is suggested thatthe I/O buffer for this SCF device be enlarged to at least 512.  The baudrate of the port must, of course, match that of the TNC, but theconfiguration of the OSK system (for instance, if a DMA disk controller isnot available) may require that the baud rate may have to be lowered toavoid dropped characters.      host is designed to run in the background and should be executed withthe shell '&' option.  It will lower its priority to 100 duringinitialization.  The attached TNC will be placed in host mode and will bepolled at least once every 2 seconds, more often as data availabilityrequires.  The maximum number of connects allowed is set to 3 andmonitoring is disabled.      Incoming connections to the TNC will cause a child process to beforked.  This process will execute the program "mailbox".  The standardI/O paths for the child process will be redirected to unnamed pipesthrough which the TNC data will pass.  No special I/O practices are neededfor this program.  The arguments passed to the child process will be thecallsign of the connected station, the TNC port (minus the '/'), and thedigipeaters the station connected through, if any.     If a station disconnects from the TNC or the link fails, the pipethrough which the child process receives input is closed.  If the outputpipe from the child process goes EOF, a wait will be executed for thatchild and the associated TNC channel will be disconnected once all datadestined for the connected station has been acknowledged.  If a ^Ccharacter is received from the station, an interrupt signal (signal value3) is sent to the associated child process.      host creates four named pipes upon execution.  These pipes all havenames that end in ".<port>" where <port> is the path to the TNC specifiedon startup, minus the '/'.     The pipe "monitor.<port>" is an output pipe and will contain anymessages received from TNC channel 0.  This includes monitored packets andheaders and attempted connect messages if no channels are available.  Ifthe pipe is full, any subsequent messages will be discarded by host.     The pipe "beacon.<port>" is an input pipe and anything written to itwill be written to TNC data channel 0.  This will cause the information tobe transmitted in an unproto packet via whatever path the channel wasinitialized to before host was executed.      The pipe "hostlog.<port>" is used for debugging output and willcontain messages from the host program.  If the pipe is full, anysubsequent messages will be discarded by host.     The pipe "command.<port>" is an input pipe through which commands canbe given to the host program.  Commands are given as a single line,terminated by newline.  The first character of the line specifies thecommand.  The following commands are currently supported:         m<string>\n - This will send the line as a command to the TNC on         channel 0.  It can be used to enable or disable the monitoring of         information.  Monitored information appears in the pipe         "monitor.<port>".         o<pid>\n - This causes host to allocate the highest numbered         available TNC channel and open four named pipes.  <pid> is the         (ASCII) process id of the program giving the command and is used         to create unique names for the pipes.  The pipe "data_in.<pid>"         will contain incoming data from the TNC, while data sent to the         pipe "data_out.<pid>" will be sent to the TNC.  The pipe         "ctl_in.<pid>" will contain TNC channel status and error         messages, while information sent to the pipe "ctl_out.<pid>" will         be sent as commands to the TNC.  In this way, a complete         separation exists between channel data and status/command         information.         c<pid>\n - The channel allocated by the corresponding o command         (above) is deallocated and the associated named pipes are closed.         It is a good idea to make sure the channel is disconnected before         issuing this command.         u <path> - Sets the digipeater path for UI (beacon) frames.     Outgoing packets are limited in length to 236 by host.  (Larger packetswould be broken by NET/ROM.)  Within these 236-byte packets, host will place asmany complete lines of text as will fit.  If there are characters after thelast newline, they will be saved until the next polling period.  If no newlineis received by then, the data will be sent even if it is not terminated with anewline.  In this way, data transparency is maintained while the majority ofpackets will end with a newline character.  You should note that host will notperform any editing on incoming data.  In particular, line terminatorcharacters will be passed unchanged, even the linefeed of a carriage-return/linefeed pair.  This extra linefeed may cause difficulty to mailboxprograms, and users should be cautioned to turn off their TNC LFADD (orequivalent) flag.      If a quit signal is received by host, the program will disable allmonitoring from the TNC, set the maximum number of connections to zero (noconnections), return the TNC to terminal mode, and exit.BUGS: