NAME:     hostube - packet host mode terminal interface.AUTHOR:     Eric Williams  WD6CMU, 71336,1424SYSTEM CONFIGURATION:     OS9/68K, MW C v2.0SYNTAX:     hostube <port>DESCRIPTION:     hostube provides a terminal-mode interface for use with the host modetranslator program (host) in order to allow operator access to packetradio without interrupting host mode mailbox operations.     The argument to hostube is the name of the SCF device which isconnected to the TNC through which the operator wishes to communicate,minus the '/'.  hostube will use this port name to construct the pipenames through which it will communicate to the host translator.  Ifhostube makes successful contact with the host translator, the message"Connection established..." is printed, after which communication with asingle channel of the TNC can take place.  If no response is received fromhost, the hostube program will abort.     Communication from the TNC to the terminal is on a character-by-character basis: any characters received from the TNC will be displayed onthe user's terminal.  No distinction is made between channel data andstatus messages, other than the form of the text.     Communication from the terminal to the TNC is on a line basis inorder to make use of the standard OS9 line editing features.  As soon as acharacter is typed on the terminal, output from the TNC pauses.  The userthen completes the editing of the line and types carriage return, at whichpoint the line is sent to the TNC (assuming that it is a line of data).Output from the TNC will then continue.     If information other than data is to be sent, it is differentiatedfrom data by the first character of the line.  If the first character isan escape (echoed by OS9 as '.'), the rest of the line is sent as acommand to the TNC channel.  If the first character is a backslash ('\'),then the second character is interpreted as a hostube command.  Thefollowing commands are supported:     \q: Quit.  Close all files and halt hostube/host communications.  No         disconnect of the TNC channel is performed.     \c: CHD.  hostube will prompt for the new default data directory.     \r: Receive.  hostube will prompt for a file name.  All subsequent         text received will be sent to the file.  If receiving is in         progress, the command will halt it.     \t: Transmit.  hostube will prompt for a file name.  The contents of         the file will be sent as data to the TNC channel.  If         transmission is in progress, the command will halt it.     \s: Escape to shell.  hostube will spawn a task and execute shell.         To return to hostube, type ESC.     If a character was typed on the terminal by mistake, TNC to terminalcommunication can be resumed by typing a line with a single backslash onit.