AX.25 Version 2                          Multi-channel                          TNC  FIRMWARE                          (version 1.2)            Copyright 1986, Ronald E. Raikes (WA8DED)     This firmware supports the full AX.25  link-layer  protocol,version 2.0 as described in the ARRL specification dated  October1984,  as  well  as   the   pre-existing   version   1.x.    Thisimplementation supports multiple  simultaneous  link  connectionswith either version protocol.  This release  has  been  assembledfor a maximum of four connections, although any reasonable numberof connections is possible by changing one MAXLNK symbol  in  thesource equate file.     The firmware  is  contained  in  two  2764  EPROMs,  and  isintended to be installed in a TAPR TNC-1 (or equivalent, such  asthe AEA PKT-1 or Heath HD-4040) in sockets  U11  (C000)  and  U12(E000).  This assumes that a 6264 RAM  is  already  installed  insocket U7, with additional  6264  RAMs  optionally  installed  insockets U8, U9, and U10 in any combination (verify that pin 26 isconnected to +5v).  Additional RAM is highly desirable if  multi-channel or unattended operation is anticipated.  When  installingthe EPROMs (including newer versions), it will  be  necessary  tostart the tnc with the PARAMETER SOURCE switch set  to  the  PROMposition.  This will cause default parameters to be written  intoNOVRAM  memory  but  not  PERMed.   The  RS-232  port   will   beinitialized to 300  baud  with  xon/xoff  handshaking.   The  tncsource call sign will be all blanks, and should be set  with  the'I' command, as well as any other default parameters  that  mightneed changing, before issuing a 'PERM' command.  At  this  point,the PARAMETER SOURCE switch may be set to NOVRAM  for  subsequentoperation.  If the terminal baud rate has been changed,  the  newvalue will take effect following a reset.  If the tnc source callsign is left blank, the tnc will not activate the transmitter PTTline.     Commands and information are sent to the tnc in the form  oflines.  Lines may be up to 256  characters  long,  including  theterminating CARRIAGE RETURN.  If the 256th character  entered  isnot a CARRIAGE RETURN, it will be discarded and a BELL  characterwill be output to the terminal.  BACKSPACE and DELETE may be usedto remove single characters from the line.  The entire  line  maybe permanently backspaced out by entering a CONTROL-U or CONTROL-X.  A CONTROL-R will temporarily backspace out any  partial  lineto allow incoming frames to be  displayed.   A  second  CONTROL-Rwill then restore  the  line  to  allow  continuation  of  entry.During the time a partial line is saved, only  another  CONTROL-Rwill be  accepted  from  the  keyboard  (with  the  exception  ofxon/xoff, of course).  BELL characters are echoed to the terminalwhen entered or  removed.   Lines  which  begin  with  an  ESCAPEcharacter (echoed as '* ') are interpreted  as  commands.   If  acommand is issued with no parameter, the current  value  of  thatcommands parameter is displayed.  An embedded NULL character in acommand will cause the remainder  of  the  line  to  be  ignored.Lines without a leading ESCAPE character are sent as information.     The firmware provides the operator  with  five  virtual  tncchannels, numbered 0 to 4.  The terminal is logically attached toonly one of these  channels  at  a  time,  selected  by  the  'S'command.  Information sent on channel 0 is always  unproto.   Theunproto path may be set by issuing a 'C' command when  channel  0is selected.  Channels 1 - 4 are also unproto  if  they  are  notcurrently connected.  Outgoing connect requests may be issued  onany unconnected channel, while incoming connect requests will usethe first available  channel  (provided  the  maximum  number  ofconnections set  by  the  'Y'  command  will  not  be  exceeded).Information received on a connected channel that is not currentlyselected will remain queued there until that channel is  selected(the 'L' command is useful in determining if there is informationwaiting on other channels).  Information for transmission is sentonly to the currently selected channel.   When  a  connection  isended,  any  information  that  has  not  been   transmitted   oracknowledged will be discarded.  Received information will remainqueued,  however,  until  it  has  been  displayed.   If  a   newdigipeater  path  is  desired  while  a   connection   is   beingestablished or is in progress, it is not necessary to  disconnectfirst.  Simply re-issuing the 'C' command will  re-establish  theconnection via the new path  without  any  loss  of  information.Attempting to connect to  the  same  station  on  more  than  onechannel is not permitted.     Which protocol version is used to initiate a  connection  iscontrolled by the 'V' command, but the version  will  be  changedautomatically, if necessary, to conform to the version of the tncresponding.  Version 2 protocol is more  effecient  in  terms  ofnetwork  throughput  and   loading,   especially   under   severeconditions.  Version 2 protocol is the default and should be usedwhenever possible.  (NOTE:  The  existing  firmware  supplied  byTAPR for the TNC-1 (v3.x) will NOT digipeat version  2  protocol.This is expected to  remedied  in  v4.0.   All  other  tnc's  anddigipeaters encountered to date  digipeat  version  2  properly.)When version 2 protocol is used, a  watch-dog  timer  is  startedwhenever information  is  not  being  transmitted.   If  the  tncremains idle for three minutes, it will poll  the  other  tnc  todetermine if the link is still established.  If  no  response  isreceived after the number of tries set by the  'N'  command,  thetnc will attempt to re-establish the connection.  This  procedurewill also detect the case where someone connects and then  leaveswithout disconnecting.  Changing the protocol  version  during  aconnection is not permitted.     The 'F', 'N', 'O',  and  'V'  commands  maintain  individualparameters for each channel.  The value stored in  channel  0  isthe value that is  saved  in  NOVRAM.   This  value  is  used  toinitialize channels 1 - 4 after a  reset,  and  to  re-initializechannels 1 - 4 after a disconnect.  This allows the values to  bechanged independently on each channel,  prior  to  and  during  aconnection, and then automatically revert back  to  the  standardvalues when the connection is ended.  A 'D' command issued  on  adisconnected channel 1 - 4 will also re-initialize that channel.     Frame monitoring is controlled  by  the  'M'  command.   Thecommand parameter determines the types of frames  monitored,  andis a list of desired  frames  chosen  from  the  letters  in  thefollowing table:     LTR       FRAME     ---       -----      N        None      I        I frames      U        UI frames      S        Supervisory frames      C        Monitor while connected      R        Monitor received frames (addressed to)      T        Monitor transmitted frames (addressed from)      +        Call signs to be included (maximum of 8)      -        Call signs to be excluded (maximum of 8)The '+' and '-' parameters may not be used together.   If  eitheris used, it must be the last parameter (followed by one to  eightcall signs,  if  applicable).   If  no  list  of  call  signs  isspecified to be included or excluded,  all  call  signs  will  becandidates for monitoring.  Entering a '+' or '-'  with  no  callsigns will empty the list.An asterisk displayed after a call sign in  the  digipeater  listindicates the frame was transmitted by that station.  The controlfield displayed will be one of the following:     NAME   DESCRIPTION     ----   -----------     RRa  - Receive Ready     RNRa - Receive Not Ready     REJa - Reject     UI   - Unnumbered Information     DM   - Disconnected Mode     SABM - Connect Request     DISC - Disconnect Request     UA   - Unnumbered Acknowledge     FRMR - Frame Reject     Iab  - Information     ?ccH - Unknown     a  = Next expected frame number (0 - 7)     b  = Frame number of this frame (0 - 7)     cc = Hexadecimal valueIn addition, one of the following characters will  be  displayed,reflecting the protocol version, command/response bits,  and  thepoll/final bit: (blank) = version 1 frame without poll/final bit       ! = version 1 frame with poll/final bit       ^ = version 2 command frame without poll bit       + = version 2 command frame with poll bit       - = version 2 response frame with final bit       v = version 2 response frame without final bitThe protocol identifier field is displayed in hexadecimal,  whichis currently  always  an  F0,  signifying  that  no  layer  3  isimplemented.     An unattended mode, controlled by the 'U' command,  providesfor sending user supplied text to a connecting station, and  thenallows that station to leave a  brief  message.   This  mode  canoperate on all channels simultaneously, but in no way limits  theoperators ability to interact with one of the connected  channelsor  the  ability  to  make  outgoing  connect   requests.    Whenunattended mode is enabled, link status messages  are  queued  tothe associated channel and not output to the terminal unless thatchannel  is  currently  selected.   Link  status  messages   willtherefore  be  displayed  in   chronological   order   with   theinformation from that channel.  In addition, text supplied by theuser with the 'U' command  will  be  sent  to  any  station  thatconnects.  If channel 0  is  left  selected,  stations  may  thenconnect and leave messages on channels 1 - 4 (limited by the  'Y'parameter, of course).  The 'L' command may be used to  determineif messages have been left on any channel.  Selecting  a  channelcontaining messages will cause all link  status  and  informationfrom that channel to be displayed.  If  xon/xoff  handshaking  isenabled, CONTROL-S and CONTROL-Q may  be  used  to  regulate  theoutput to  the  terminal  to  allow  comfortable  reading.   Alsoprovided,  but  intended  to  be  used  very  sparingly,  is   anunattended QST facility.  In this mode, user supplied text may beautomatically transmitted unproto to the path set on  channel  0,at periodic intervals spaced  1  -  65,535  minutes  apart.   Theinterval and text must be entered each time QST mode is  enabled.Use of unattended QST messages is generally degrading to  networkperformance and is considered by many to  be  an  annoyance,  andshould only be used when absolutely necessary.     The tnc parallel port supplies link status  information  forchannel 1 on lines PA0, PA1, and PA2 for  use  with  an  externalstatus indicator.  The following link states are possible:                    1 = Disconnected                    2 = Link Setup                    3 = Frame Reject                    4 = Disconnect Request                    5 = Information Transfer     The firmware source is written in  6809  assembly  language.Emphasis was  placed  on  using  a  state  table  driven  design,utilizing the state tables provided in  the  ARRL  specification.The source was assembled using a 6809 cross assembler  from  2500AD Software running on a Z-80/8086  TurboDOS  development  system(CP/M & MS-DOS compatable).NOTE:   A  very  small  number  of  Western  Digital  1933   HDLCController ICs manufactured in 1981 and 1982 have been  found  tobe defective.  The symptoms are erratic and unreliable  operationof the tnc, due to the hdlc controller  occasionally  failing  tointerrupt  upon  successful  completion  of  frame  transmission.These defective parts can be identified by  inspecting  the  masknumber on the underneath side of  the  IC.   The  defective  masknumber begins with the letters 'BA', and should be replaced.  Thecurrent replacement part is called 1935 and requires no changes.                         COMMAND SUMMARY                         ===============COMMAND        PARAMETER               DESCRIPTION-------        ---------               -----------  A (1)            0             Auto linefeed disabled                   1             Auto linefeed enabled  B (6)           1-15           Terminal baud rate  C        Cs1 [Cs2 ... Cs9]     Connect path (0=unproto path)  D                              Disconnect  E (1)            0             Echo input disabled                   1             Echo input enabled* F (3)           1-15           Frame acknowledge (seconds)  G               [0]            Get information (host mode)                  [1]            Get link status (host mode)  H (1200)       50-9600         HDLC baud rate  I                Cs            Tnc source call sign  JHOST (0)        0             Terminal mode enabled                   1             Host mode enabled  K               1-2            Calibrate  L              [0-4]           Display channel status  M (IU)       NIUSCRT+-         Monitor mode* N (10)          0-255          Number of tries (0=forever)* O (4)           1-7            Number of outstanding I frames  PERM                           Save parameters to NOVRAM  QRES                           Re-start firmware  R (1)            0             Repeater disabled                   1             Repeater enabled  S (1)           0-4            Select channel (0=unproto)  T (30)          0-127          Transmitter delay (10ms)  U (0)   0      [text]          Unattended mode disabled          1      [text]          Unattended mode enabled          2    interval  text    QST mode enabled* V (2)            1             Version 1 protocol initiated                   2             Version 2 protocol initiated  W (16)          0-127          Repeater wait (10ms)  X (1)            0             Transmitter PTT disabled                   1             Transmitter PTT enabled  Y (1)           0-4            Maximum connections  Z (3)            0             Flow disabled, xon/off disabled                   1             Flow enabled, xon/off disabled                   2             Flow disabled, xon/off enabled                   3             Flow enabled, xon/off enabled  @   B                          Display number of free buffers      C  (0)       0             Fast clock disabled                   1             Fast clock enabled      P  (F0)     0-FF           Protocol id (hex)      S                          Display current link state      T2 (100)    0-255          Timer T2 interval (10ms)      T3 (18000)  0-32767        Timer T3 interval (10ms)   Default values are shown in parenthesis*  These commands are applicable to each connection channel     (Values set on channel 0 are used after a reset and      disconnect to initialize each connection channel)                       COMMAND DESCRIPTION                       ===================     The 'A' command is used to enable or disable  the  automaticinsertion of LINEFEED characters after CARRIAGE RETURN charactersto the terminal.  This parameter is stored in NOVRAM.     The 'B' command is used to set the terminal baud rate, usingone of the following parameters:     Parameter     Baud rate     ---------     ---------         1            50         2            75         3            110         4            135         5            150         6            300         7            600         8            1200         9            1800        10            2400        11            3600        12            4800        13            7200        14            9600        15            19200After setting the baud rate with the 'B' command, the value  mustbe PERMed, and will then take effect  following  a  reset.   Baudrates above  4800  may  not  be  reliable  with  sustained  input(commands or information) from a host computer due  to  the  slowcpu clock rate and non-vectored interrupt architecture.     The 'C' command is used to initiate a link connection.  Notethat NO 'v' or 'via' is used between the  destination  call  signand the digipeater call signs.  A 'C' command may be issued on  achannel already in use to change the digipeater call  signs,  butnot the destination call sign.  A 'C' command issued when channel0 is selected sets the unproto path.  Attempting  to  connect  tothe same station on more than one channel is not permitted.     The 'D' command is used to initiate a link disconnection.  A'D' command issued during the establishment or  dis-establishmentof a link will cause an  immediate  return  to  the  disconnectedstate.  A 'D' command issued on a disconnected channel  will  re-initialize the connection  dependent  parameters  to  the  valuesstored in channel 0.     The 'E' command is used to enable or disable the echoing  ofinput (commands and information) to the terminal.  This parameteris stored in NOVRAM.     The 'F' command is used to  set  the  frame  acknowledgementinterval.  This interval is used to compute the timeout  intervalbefore a packet is retransmitted, using the formula:     time (seconds) = frame ack * (2 * number of digipeaters + 1)A separate frame acknowlegement interval value is maintained  foreach connection channel.  The value stored in channel 0  is  usedto  initialize  each  connection  channel  after   a   reset   ordisconnection, and is the value that is stored in NOVRAM.     The 'G' command is used to interrogate virtual tnc  channelswhen host mode is enabled.  If no  parameter  is  specified,  thenext chronological item (information  or  link  status)  will  bereturned, provided there is one.   This  command  is  invalid  interminal  mode.   A  later  section  is  devoted  to  host   modeoperation.     The 'H' command is used to set the  HDLC  baud  rate.   Non-standard values are rounded down to the next possible baud  rate.In this case, use an 'H' command with no paramter to display  thevalue actually set.  This parameter is stored  in  NOVRAM.   HDLCrates up to 9600 baud are supported if the  fast  clock  mode  isenabled.     The 'I' command is used to set the  tnc  source  call  sign.The initial value is all blanks.  After the source call sign  hasbeen entered, the 'PERM' command should be used to  save  it  foruse during subsequent operation.  Changing the  tnc  source  callsign while connected is not permitted.  If the  tnc  source  callsign is left blank, the tnc will not activate the transmitter PTTline.     The 'JHOST' command is used to select between  terminal  andhost modes.  A later section is devoted to host mode operation.     The 'K' command is used to calibrate  the  tnc  modem.   Thefollowing parameters set the calibration modes listed:     Parameter         Calibration     ---------         -----------         1          FREQUENCY COUNTER         2          TONE LEVEL & NULLThe frequency counter mode will display the measured  frequencieson the terminal.  When each mode is  selected,  jumpers  settingsare displayed as well as the appropriate ajustment  points.   Thevalues shown in parenthesis are the normal targets for 1200  baudoperation.     The 'L' command is used to display the link status of one orall channels.   Information  displayed  includes  the  connectionpath, number of receive frames not yet displayed, number of  sendframes not yet transmitted, number of transmitted frames not  yetacknowledged, and the  current  retry  count.   A  '+'  characterpreceeding the channel number indicates  the  currently  selectedchannel.  Operation of this command when host mode is enabled  issomewhat different, and is described in a later section.     The 'M' command is used to set the  frame  monitoring  mode.The command parameter determines the types of  frames  monitored,and is a list of desired frames chosen from the  letters  in  thefollowing table:     LTR       FRAME     ---       -----      N        None      I        I frames      U        UI frames      S        Supervisory frames      C        Monitor while connected      R        Monitor received frames (addressed to)      T        Monitor transmitted frames (addressed from)      +        Call signs to be included (maximum of 8)      -        Call signs to be excluded (maximum of 8)The '+' and '-' parameters may not be used together.   If  eitheris used, it must be the last parameter (followed by one to  eightcall signs,  if  applicable).   If  no  list  of  call  signs  isspecified to be included or excluded,  all  call  signs  will  becandidates for monitoring.  Entering a '+' or '-'  with  no  callsigns will empty the list.  This parameter is stored in NOVRAM.     The 'N' command is used to set the maximum number of times aframe  will  be  transmitted  without  receiving  an  appropriateacknowledgement, before a link failure is  assumed.   A  separatemaximum number of tries value is maintained for  each  connectionchannel.  The value stored in channel 0  is  used  to  initializeeach connection channel after a reset or  disconnection,  and  isthe value that is stored in NOVRAM.     The 'O' command  is  used  to  set  the  maximum  number  ofunacknowledged I frames that may be outstanding at any one  time.A separate maximum number of unacknowledged  I  frames  value  ismaintained for each connection  channel.   The  value  stored  inchannel 0 is used to initialize each connection channel  after  areset or disconnection, and  is  the  value  that  is  stored  inNOVRAM.     The 'PERM' command is used to change  the  parameter  valuesstored in NOVRAM to those that are currently set.     The 'QRES' command is used to restart the firmware as  if  ahardware reset had been issued.     The 'R' command is used to enable or disable the digipeatingof frames.  This parameter is stored in NOVRAM.     The 'S' command  is  used  to  select  the  current  channelnumber.  This parameter is stored in NOVRAM.     The 'T' command is used to set the transmitter  keyup  delayinterval.  The parameter is specified in 10ms  increments.   Thisparameter is stored in NOVRAM.     The 'U' command is used  to  enable  or  disable  unattendedmodes.  If QST mode is not used, previously entered text will  beretained if new text is not provided.  If QST mode  is  selected,the interval and text must be  supplied.   The  QST  interval  isspecified in minutes from 1 - 65,535.     The 'V' command is used to select whether  version  1  or  2protocol will be used to initiate a link connection.  A  separateprotocol version value is maintained for each connection channel.The value  stored  in  channel  0  is  used  to  initialize  eachconnection channel after a reset or  disconnection,  and  is  thevalue that is stored in  NOVRAM.   Interrogating  this  parameterduring a connection will reflect the protocol  version  currentlybeing used on that channel.  Changing the protocol version duringa connection is not permitted.     The 'W' command is used to set the digipeater wait interval.The parameter is specified in 10ms increments.  This parameter isstored in NOVRAM.     The 'X' command is used to enable or disable the transmitterPTT line.  This parameter is stored in NOVRAM.     The 'Y' command  is  used  to  set  the  maximum  number  ofconnections that may  established  by  incoming  requests.   Thiscommand has no  effect  on  the  operators  ability  to  initiateoutgoing  connection  requests.   This  parameter  is  stored  inNOVRAM.     The 'Z' command is used to enable or  disable  flow  controland xon/xoff handshaking to the terminal.   If  flow  control  isenabled, output to the terminal will be inhibited while  enteringcommands or information.  If flow control is disabled, output  tothe terminal will not be restricted.  Flow control  and  xon/xoffhandshaking should be disabled during periods in which the tnc isoperated without a terminal, to  avoid  suspending  output  whichwill consume buffers.  If xon/xoff handshaking  is  enabled,  crtscrolling may be stopped and started using CONTROL-S and CONTROL-Q characters.  Flow control  and  xon/xoff  handshaking  are  notperformed when host mode is enabled.  This parameter is stored inNOVRAM.     The '@'  command  is  a  software  maintenance  command.   Aparameter of 'B' will display the  number  of  free  buffers.   Aparameter of 'C0' will select timing parameters  for  the  slowercpu  clock  rate.   A  parameter  of  'C1'  will  select   timingparameters for the faster cpu clock rate.  The 'C'  parameter  isstored in NOVRAM and must be PERMed if the change is to  stay  ineffect following a reset.  The 'P' parameter is used to  set  theprotocol id byte for each channel and is supplied  and  displayedin hexadecimal.  A parameter of 'S' will display the current linkstate.  The 'T2' parameter is used to set the timer T2  interval,just as the 'T3' parameter is used to set the timer T3  interval.The timer intervals are specified in 10ms  increments,  and  bothare stored in NOVRAM.  Timer T2  controls  the  amount  of  delaybetween the time an information frame is received  and  the  timethe resulting response frame is sent.  This delay allows multipleframes to be acknowledged with a single response.   Timer  T3  isused maintain link integrity.  If there is no activity during theT3 interval, the tnc will poll to verify the distant  station  isstill connected.                       HOST MODE OPERATION                       ===================     Host mode is intended to provide a user  interface  suitablefor operation under control of a host  processor.   Commands  andinformation to the tnc, as well as status  and  information  fromthe tnc, are clearly identified to allow orderly and  unambiguouscommunication.  To alleviate any need for  hardware  or  softwarehandshaking,  the  tnc  will  not  send  to  the  host  processorunsolicited,  and  all  exchanges  are  limited  to  256   bytes.Information transfers are fully transparent.     When host mode is enabled, the first byte sent  to  the  tncmust be a channel number.  If  information  is  being  sent,  thesecond byte must be a binary 0.  If a command is being sent,  thesecond byte must be a binary 1.   The  third  byte  must  be  thebinary length of the actual information or  command,  decrementedby 1 (vacuous information or commands are  not  permitted).   Theactual  information  or   command   bytes   must   follow   last.Information sent to channel 0 will be sent unproto.   Informationsent to an unconnected channel 1 - 4 will be discarded.  The  tncwill respond to both information  and  commands  with  a  channelnumber first, followed by a binary code of 0, 1, or 2, signallingsuccess or failure.  Codes of 1 or 2 will be followed by  a  nullterminated message.  Channels may be  interrogated  for  incominginformation or link status by using  the  'G'  command.   Monitorheaders and monitor information will always be sent to channel 0,along with connect request link status messages.  All other  linkstatus messages will be sent to the  appropriate  channel,  alongwith that channels connected information.  In response to  a  'G'command, the tnc  will  respond  with  a  channel  number  first,followed by a binary code of 0 if  nothing  is  available,  or  abinary code of 3 - 7, identifying the bytes that follow.  A  codeof  4  indicates  the  monitored  frame  does  not   contain   aninformation field.  A code of 5  indicates  the  monitored  framedoes contain an information field, and the next  'G'  command  onchannel 0 will return that information field, preceeded by a codeof 6.         Host to Tnc         -----------CHANNEL   CODE           DESCRIPTION-------   ----           -----------   n       0        Information (preceeded by length-1)   n       1        Command     (preceeded by length-1)         Tnc to Host         -----------CHANNEL   CODE           DESCRIPTION-------   ----           -----------   n       0        Success (nothing follows)   n       1        Success (message follows, null terminated)   n       2        Failure (message follows, null terminated)   n       3        Link Status (null terminated)   n       4        Monitor Header (null terminated)   n       5        Monitor Header (null terminated)   n       6        Monitor Information (preceeded by length-1)   n       7        Connect Information (preceeded by length-1)Success messages----------------{channel status}{parameter value}CHANNEL NOT CONNECTEDFailure messages----------------INVALID COMMANDTNC BUSY - LINE IGNOREDCHANNEL ALREADY CONNECTEDSTATION ALREADY CONNECTEDLink Status messages--------------------BUSY fm {call} via {digipeaters}CONNECTED to {call} via {digipeaters}LINK RESET fm {call} via {digipeaters}LINK RESET to {call} via {digipeaters}DISCONNECTED fm {call} via {digipeaters}LINK FAILURE with {call} via {digipeaters}CONNECT REQUEST fm {call} via {digipeaters}FRAME REJECT (x y z) fm {call} via {digipeaters}FRAME REJECT (x y z) to {call} via {digipeaters}x y z = FRMR information bytesMonitor Header format---------------------fm {call} to {call} via {digipeaters} ctl {name} pid {hex}Channel Status format---------------------a b c d e fa = Number of link status messages not yet displayedb = Number of receive frames not yet displayedc = Number of send frames not yet transmittedd = Number of transmitted frames not yet acknowledgede = Number of tries on current operationf = Link state    Possible link states are:     0 = Disconnected     1 = Link Setup     2 = Frame Reject     3 = Disconnect Request     4 = Information Transfer     5 = Reject Frame Sent     6 = Waiting Acknowledgement     7 = Device Busy     8 = Remote Device Busy     9 = Both Devices Busy    10 = Waiting Acknowledgement and Device Busy    11 = Waiting Acknowledgement and Remote Busy    12 = Waiting Acknowledgement and Both Devices Busy    13 = Reject Frame Sent and Device Busy    14 = Reject Frame Sent and Remote Busy    15 = Reject Frame Sent and Both Devices BusyNOTE 1:  Only items a and b are displayed for channel 0.NOTE 2:  Only states 0 - 4 are possible if version 1 is in use.                       DEFAULT PARAMETERS                       ==================     In some instances, it  may  be  desirable  to  have  defaultparameters which differ from the standard values.  To allow  easyaccess, all default parameters have been placed at the  beginningof the EPROM.  The following listing defines the layout  of  thisarea:     TYPE     VALUE          DESCRIPTION     ----     -----          -----------     BYTE      1BH           COMMAND CHARACTER     BYTE    '      ',60H    SOURCE CALL SIGN (SEE NOTE 1)     WORD     000AH          HDLC BAUD RATE DIVISOR (SEE NOTE 2)     BYTE      06H           TERMINAL BAUD RATE     BYTE      01H           MAXIMUM CONNECTIONS     BYTE      03H           MONITOR MODE (SEE NOTE 3)     BYTE      01H           REPEATER DISABLE/ENABLE     BYTE      10H           REPEATER WAIT (10ms)     BYTE      1EH           TRANSMITTER DELAY (10ms)     BYTE      03H           FLOW CONTROL MODE     BYTE      01H           TRANSMITTER PTT DISABLE/ENABLE     BYTE      01H           CHANNEL NUMBER     BYTE      01H           AUTO LINEFEED DISABLE/ENABLE     BYTE      01H           ECHO COMMAND LINE DISABLE/ENABLE     BYTE      01H           VERSION 2 INITIATED DISABLE/ENABLE     BYTE      04H           MAXIMUM UNACKNOWLEDGED FRAMES     BYTE      0AH           MAXIMUM TRY COUNT     BYTE      03H           FRAME ACKNOWLEDGE INTERVAL     BYTE      00H           FAST CLOCK DISABLE/ENABLE     BYTE      64H           TIMER T2 INTERVAL (10ms)     WORD     4650H          TIMER T3 INTERVAL (10ms)     BYTE      F0H           PROTOCOL ID     BYTE    'CQ    ',60H    UNPROTO CALL SIGN (SEE NOTE 1)     BYTE      01H           VALIDATE CALL SIGN ENABLE/DISABLE     BYTE      00H           STOP BIT/WORD LENGTH (SEE NOTE 4)     BYTE      00H           PARITY (SEE NOTE 5)  DISABLE = 00H / ENABLE = 01HNOTE 1:  The secondary station id must be shifted  left  one  bitand or'ed with 60H.NOTE 2:  The  HDLC  baud  rate  divisor  is  computed  using  theformula:SLOW CLOCK:     divisor = (14400 / buad rate) - 2FAST CLOCK:     divisor = (28800 / buad rate) - 2The HDLC baud rate divisor is stored most significant byte first.NOTE 3:  The monitor mode is composed from the following bits:     BIT       FRAME     ---       -----      0        I frames      1        UI frames      2        Supervisory frames      3        Monitor while connected      4        Monitor received frames (addressed to)      5        Monitor transmitted frames (addressed from)NOTE 4:  Stop bit and word length is controlled by the  followingbit assignments:     BIT 7     STOP BIT     -----     --------       0       1 stop bit       1       2 stop bits       1       1.5 stop bits (word length=5/parity disabled)       1       1 stop bit (word length=8/parity enabled)     BIT 6-5   WORD LENGTH     -------   -----------       0 0     8 bits       0 1     7 bits       1 0     6 bits       1 1     5 bitsBits 4-0 MUST be set to 0.NOTE 5:  Parity is controlled by the following bit assignments:     BIT 7-6   PARITY CONTROL     -------   --------------       0 0     Odd parity transmitted/received       0 1     Even parity transmitted/received       1 0     Mark parity transmitted/parity check disabled       1 1     Space parity transmitted/parity check disabled     BIT 5     PARITY ENABLE     -----     -------------       0       Parity disabled       1       Parity enabledBits 4-0 MUST be set to 0.