WA8DED HOST MODE USER'S GUIDE                           Paul T. Williamson, KB5MU                                  23 May 1986  Abstract:  This  document  explains  the use of Host mode with WA8DED's AX.25Version 2 Multi-channel TNC Firmware, Version 1.1 for the TAPR TNC-1.    It  isbased  on  the  information  provided in the WA8DED document (Version 1.0), theW6IXU mailbox software (13 May 1986 revision),  and  the  WA8DED  Split  ScreenTerminal  Emulator  (SS,  28 April 1986 version).  It is intended for use by anapplication programmer attempting to communicate with the TNC in Host mode, andassumes that the programmer is already familiar with user-mode operation of theWA8DED firmware.                                   Chapter 1                              What Is Host Mode?  WA8DED's TNC firmware provides two entirely independent user interfaces.  Thedefault  user  interface is designed for use by a human operator at a terminal.Host mode, on the other hand, is  designed  for  use  by  a  specially-designedcomputer  program.    It  allows the computer to maintain strict control of thecomputer-TNC link, and to obtain control information that  would  otherwise  bedifficult to extract from the normal data stream.  One  of  the most common bugaboos of computer-TNC interfacing has always beenflow control.  The TNC is capable of sending data faster than the computer  canprocess  it,  and  likewise the computer is capable of sending data faster thanthe TNC can transmit it.  It is theoretically possible to  solve  this  problemwith  either  hardware  flow  control  (RTS/CTS  wires  in  the RS-232 link) orsoftware flow control (XON/XOFF characters inserted in the data stream).   Bothof  these  methods  are tricky and error-prone, however.  Hardware flow controlmay not always be available, and software flow  control,  even  when  it  worksadequately,  leads  to data transparency problems (i.e., what if the data beingtransmitted contains XON or XOFF?).  If everything is not exactly  right,  datawill be lost.  WA8DED's Host mode solves this problem by    1. Speaking only when spoken to, and   2. Limiting all data bursts to 256 bytes.The  first  point  allows  the  computer  program to go off and do other things(write data out to disk, handle the  console,  make  coffee)  without  worryingabout  data  coming  from  the TNC and dropping on the floor.  The second pointallows computers that have a hard time  handling  fast  serial  data  (e.g.,  aCommodore  64  with no UART) to concentrate on the receiving task to fill a 256byte buffer, then go off and process the data without worrying about additionaldata  arriving  before  it has time to process that batch.  This scheme is veryforgiving of inefficient serial routines, so that faster computers can get awaywith simple byte-level polling (e.g., a program for the IBM PC can use the BIOSserial port routines).  On the subject of serial routines, notice that the TNC does not handle eitherhardware  or  software flow control when in Host mode.  You must make sure thatyour serial drivers will not send unwanted XON and XOFF characters to the TNC.  Since the TNC speaks only when spoken to, the computer must  constantly  pollthe  TNC  to  find  out what is happening on the link.  In user mode, connecteddata received over the AX.25 link is immediately displayed (if that channel  isselected).    In  Host  mode,  the  TNC  is  not  allowed  to  send informationunsolicited, so the program must ask the  TNC  for  data  periodically.    Thisimplies  that  the  computer-TNC  link will be busy most of the time.  Frequentpolling and a relatively high baud rate (say 4800 or 9600 baud)  are  desirablefor  applications that require quick response times.  A user monitoring data inreal time will notice delays if the delay between polls is too great.  The format of these short computer-TNC exchanges is  carefully  specified  toeliminate  ambiguity  and  minimize overhead.  The computer sends to the TNC inthe following format:    {channel}{info/cmd}{count}{data...}  Channel is the channel number to which the transmission pertains.    Info/cmddistinguishes  between  information  to be transmitted and commands to be actedupon by the TNC.  Count specifies the number of bytes to  follow,  and  Data...are the actual data bytes or command bytes.  The details of this format will bediscussed later.  All computer-to-TNC transmissions must follow this format.  The TNC sends to the computer one of several different formats:      {channel}{code=0}                      short formator     {channel}{code=1-5}{data...}{0}        null-terminated formator     {channel}{code=6-7}{count}{data...}    byte-count format]  Notice that you can always tell what is to follow  from  the  code  received.The  last  format is very similar to the computer-to-TNC format. The details ofthese formats will be described later.  All computer-to-TNC transmissions  willfollow one of these formats.                                   Chapter 2                        Entering and Exiting Host Mode  Host mode is entered by giving a JHOST 1 command to the TNC in the usual way.This sounds simple enough.  Just send <ESC>JHOST1<CR> to the TNC.  But what  ifsomething  has  already  been sent to the TNC (say by powerup transients)?  The<ESC> will be treated as data (echoed as ^[ by the TNC) and the command will belost.    We can work around this by sending a ^U or ^X first, to clear the junkout.  It might also be a good idea to send an XON, in case the junk included anXOFF.  So  we  send  ^Q^X^[JHOST1^M  (or,  if  you  prefer the ASCII mnemonics,<DC1><CAN><ESC>JHOST1<CR>):              11 18 1B 4A 48 4F 53 54 31 0D            ^Q ^X ^[ J  H  O  S  T  1  CRThis will work every time, if the TNC is in user mode.  If the TNC is  in  Hostmode  already, we should detect that fact and recover.  Host mode recovery willbe discussed later in this document.  Exiting Host mode is a simple matter of sending a JHOST0 command to the  TNC.The  TNC  will  acknowledge  the  JHOST0 command in the usual Host-mode fashionbefore  returning  to  user  mode,  so  you  can  use  your  regular  Host-modetransaction routine.  Note  that  a  QRES  command issued in Host mode will dump you back into usermode.  It does not acknowledge in Host-mode fashion before doing so.  The  Hostmode  parameter  is not stored in NOVRAM, so it is not possible to "wake up" inHost mode.  It is, however, possible to PERM other parameters from Host mode.                                   Chapter 3                              Commanding the TNC  OK, now that we're in Host mode, let's look at a simple command exchange.  Wewill  gloss  over  some of the details for this first look.  Suppose we want toturn off Unattended mode.  In normal user  mode,  we  would  type  <ESC>U0<CR>.That  is,  we would send a U0 command to the TNC.  To send a U0 command in Hostmode, we have  to  assemble  a  transmission  for  the  TNC  according  to  thecomputer-to-TNC format.  Recall that the computer-to-TNC format is:      {channel}{info/cmd}{count}{data...}The  first  byte,  channel,  is  the  channel number.  In user mode, it doesn'tmatter what channel you are on when you give a U command.   Likewise,  in  Hostmode,  it  doesn't matter which channel you send this command to.  Let's choosechannel 0.  The second byte is info/cmd; this is a command, so this byte has tobe  1.    The  command data we are going to send is simply "U0", the same ASCIIstring we would have used between <ESC> and <CR> to do the same thing  in  usermode.    This  is  two bytes long, so the count byte should indicate two bytes.Count is encoded as (length - 1), so the third byte of the  message  should  be2 - 1 = 1.  The  following is an illustration of the required transmission.  The top linelists the bytes to be sent in hex notation.  The first  byte  sent  is  on  theleft.    Below  each byte of the top line is an explanation of that byte.  Thisformat  will  be  used  throughout  this  document  to  illustrate  Host   modetransmissions.              00 01 01 55 30            |  |  |  U  0            |  |  |            |  |  +-- Count = 1    (two bytes)            |  +----- Info/cmd = 1 (this is a command)            +-------- Channel = 0  Note  that  no  carriage  return is required or allowed.  As soon as the bytecount is fulfilled (i.e., when the last byte has been received) the TNC acceptsthe transmission as complete.  How do we know the TNC got the command OK?  Simple: it responds with a statusmessage.  A U0 command can't fail, so we can guess that the status message willbe  a success message.  A U0 command doesn't return any information, either, sono data field will be present.  So, we can guess that the TNC will respond witha transmission in the short format:              00 00            |  |            |  +--- Code = 0 (Success, no data follows)            +------ Channel 0  Now  we  can  see  the  general  shape  of  any computer-TNC transaction: thecomputer sends a command to the TNC, and the TNC responds with  an  appropriatemessage.    In  writing  a program to interface with Host mode, we will have totake care of building these  outgoing  frames  and  interpreting  the  incomingframes.    If  we take a hint from WA8DED and W6IXU, we will implement a singleroutine that does the dirty work of sending a transmission  and  receiving  theresponse.  In  receiving  the  response,  the  routine  will  have  to  decide  how manycharacters to read from the serial port by looking at the code  in  the  secondbyte of the TNC's message.  This code tells it in which format the transmissionwill be: short format with no following data, null-terminated format with  somedata  ending  in  a  null,  or byte-count format with a count and the specifiednumber of bytes of information.  Notice that the routine that receives the response doesn't have to  have  anyknowledge  of  the  current  state  of the TNC or the application program.  Themeaning and encoding of the TNC's response is completely determined by the datain  that  response.   This simplifies the routine that receives the response byisolating it from the complexities of the application program.                                   Chapter 4                        Polling the TNC: the G command  The most essential, basic transaction in Host mode is the  G  command,  whichpolls  a  specific channel of the TNC for events and data.  A typical Host-modeapplication program will constantly send G commands to the  TNC  and  interpretthe  responses.    Since  the G command is a query to a specific channel of theTNC, it is necessary to send G commands to all of the channels that may  be  inuse.    Data  received from a station connected on channel 1 (or 2, or 3, or 4)will be sent to the computer as a response to a G command directed to channel 1(or 2, or 3, or 4).  Monitored data will be sent to the computer as a G commanddirected to channel 0.  The G command has three forms.  A command of  "G"  will  return  any  of  thepossible  responses  that  is  available.    A command of "G0" will return onlyinformation.  A command of "G1" will return only link status responses.    Thisis  useful  when  you  are  waiting for a link status change and do not wish tohandle data, or vice versa.  The only other thing that changes in a G command is the channel number.    Besure  to send G commands to all channels that may be active.  You need not sendG commands to channel 4 if Y is 3, for instance, but you must send  G  commandsto  channels 0 through 3.  The unrestricted G command has the following format:            0x 01 00 47            |  |  |  G            |  |  |            |  |  +--- Count = 0    (one byte of data)            |  +------ Info/cmd = 1 (this is a command)            +--------- Channel = x  (where x is 0, 1, 2, 3, or 4)  There are only a few possible responses to a G command.  If the program pollsthe  TNC  constantly  with  G  commands,  most  of the replies will be "nothingavailable".  This simply means nothing new has happened on the link  since  thelast  poll.   This response applies to any of the three forms of the G command.Each of the other possible responses indicates an event on the AX.25 channel: achange  in Link Status (such as "DISCONNECTED"), which is evoked by G or G1, orreceipt of a frame of monitored or connected data, which is evoked by G or  G0.The  detailed  formats  of  these  responses  will  be  discussed later in thisdocument.  Monitored information is handled specially by the G command.  Monitored  datais  handled  on  channel  0  of  the  TNC.    The monitor header is transmittedseparately from the monitor  information.    The  monitor  header  transmissionindicates  whether  or  not  there is an associated information transmission tocome.  If there is, it will be the next response on channel 0.  This scheme hastwo  results:  it  spares  the  programmer  the  task  of  parsing  out monitorinformation from the monitor header (if such is  desired),  and  it  keeps  themaximum  transmission  length  down to the maximum data field size, rather thanthe data field size plus the monitor header size (and thus allows the count  tobe a single byte).  This  scheme  for  monitored data might be considered a violation of the rulethat each computer-TNC transmission  is  self-contained  and  self-explanatory.The   monitored  information  transmission  is  qualified  by  the  immediatelypreceding monitor header transmission.  You many want to treat a monitor headerwith  information  as  a  special case in the application program, and grab thecorresponding monitor information transmission immediately.                                   Chapter 5                       Details of Computer-to-TNC Format  As we said before, the computer-to-TNC transmissions must always follow  thisformat:      {channel}{info/cmd}{count}{data...}  The  three  header  bytes  (channel,  info/cmd,  and  count) are expressed inbinary.  For instance, to specify 0 for any of these values, send a  NULL  (^@,'\0' for C fans, CHR$(0) for BASIC fans).  DON'T send the ASCII character '0'.  The data field will contain one of the following:     1. Data to be transmitted via the AX.25 link.   2. A command string just like you might issue from the normal user mode      (the part strictly between the <ESC> and the <CR>).   3. "G", the Host-mode poll command.    If data for the AX.25 link is to be sent, the  info/cmd  byte  must  be  zero(binary  zero,  remember, not ASCII "0").  The data field may contain any byteswhatsoever, but not more than 256 of  them.    Count  up  the  data  bytes  andsubtract one to find the value of the count byte.  So if you're connected to meon channel 2, and you want to say            Helloto me, send the TNC this transmission:              02 00 05 48 65 6C 6C 6F 0D            |  |  |  H  e  l  l  o  CR            |  |  |                 |            |  |  |                 +---- (this is a data byte)            |  |  +- Count = 5    (six bytes of data)            |  +---- Info/cmd = 0 (this is information to be sent)            +------- Channel = 2  (since I'm on your channel 2)Note that the CR is sent as data, and will be  transmitted  through  the  AX.25link.  It is not part of the transmission format.  If  the  information  is  sent  to  channel  0, it will go out unproto to theaddress on channel 0 (default CQ).  If information is sent on  channel  1  -  4while that channel is not connected, it is ignored.  If  a  command string is to be sent, the info/cmd byte must be one.  The datafield should contain the ASCII command string.  It does not  contain  <ESC>  or<CR>, just the characters that would go between them to form a normal user-modecommand.  For instance, to set TXDELAY to 30, send the TNC this transmission:              00 01 02 54 33 30            |  |  |  T  3  0            |  |  |            |  |  +- Count = 2    (three bytes of data)            |  +---- Info/cmd = 1 (this is a command)            +------- Channel = 0  (doesn't matter here)  The channel number is significant for the  C,  D,  F,  G,  L,  N,  O,  and  Vcommands.    C,  D, F, N, O, and V commands are channel specific in exactly thesame way as they are in user mode.  The L command is different  in  Host  mode,and  will  be discussed later in this document.  The G command has already beendiscussed.  The channel number is not significant for other commands.  You  mayuse  whatever  channel  number  is  convenient.    (WA8DED and W6IXU send thesecommands to channel 0).  The byte-count format for the computer-to-TNC transmissions is  used  becauseit  provides  "data  transparency".    This means that any bytes whatsoever mayappear in the data field.  The TNC can just accept the next so many bytes  fromthe  computer  without  thinking about it.  If a special character were used tosignal the end of the data, that character could not occur in the  data.    Thenull-terminated  format  can  use  this  scheme,  since  the  data  in these isguaranteed not to contain a null.  Unfortunately, the byte-count scheme is not very robust.  If a  character  islost  or  a spurious character is inserted, the computer and TNC could stay outof synch forever.  We must take pains to detect loss of synch  and  to  recoverfrom  the  fault.   Fortunately, the first byte of a transmission has only fivevalid values (0-4) and the second byte has only two valid values (0 and 1),  soit is possible to detect a loss of synchronization in most cases.  Timeouts canalso be used to detect synch failures.  Once the error is detected, recovery ispossible.  Host mode recovery will be discussed later in this document.                                   Chapter 6                       Details of TNC-to-Computer Format  The  TNC-to-computer  transmission  format is a bit more complicated than thecomputer-to-TNC format.  The key to decoding a transmission from the TNC is thecode  byte that follows the channel number byte.  The following table gives thecode values:                             TNC-TO-COMPUTER CODES          Code Meaning                       Format          ==== =======                       ======          0    Success, nothing follows      short format               (Nothing available)          1    Success, message follows      null-terminated format          2    Failure, message follows      null-terminated format          3    Link status                   null-terminated format          4    Monitor header/no info        null-terminated format          5    Monitor header/info           null-terminated format          6    Monitor information           byte-count format          7    Connected information         byte-count format  These various formats are used for different purposes.  Codes 0, 1, and 2 areresponses  to  an  information or command transmission from the computer.  If abatch of information was queued for transmission successfully or if  a  commandcompletes successfully without returning any information, a code 0 transmissionwill be the reply:              02 00            |  |            |  +---- Code = 1    (Success, nothing follows)            +------- Channel = 2 (same as the info or command sent)If the command is successful and returns information (like any command  withoutan  argument), a code 1 transmission will be the reply.  The returned data willfollow the code, "null terminated".  This just means that a 0 byte will  appearafter the last information byte.  For example, consider an M command without anargument.  In user mode, the user would type  <ESC>M<CR>,  and  the  TNC  woulddisplay something like     * IUSCRT *In Host mode, the command would be             00 01 00 4D            |  |  |  M            |  |  |            |  |  +---- Count = 0    (one data byte)            |  +------- Info/cmd = 1 (this is a command)            +---------- Channel = 0  (Doesn't matter here)and the response might be             00 01 49 55 53 43 52 54 00            |  |  I  U  S  C  R  T  |            |  |                    +---- Null termination            |  |            |  +---- Code = 1    (Success with info)            +------- Channel = 0 (same as in the query)If  the command failed, or the information cannot be queued for transmission, acode 2 transmission with one of these error messages will be the reply:                                 FAILURE MESSAGES                                INVALID COMMAND                            TNC BUSY - LINE IGNORED                           CHANNEL ALREADY CONNECTED                           STATION ALREADY CONNECTED  For example if you send a data line:              03 00 0C 48 65 6C 6C 6F 20 74 68 65 72 65 2E 0D            |  |  |  H  e  l  l  o     t  h  e  r  e  .  CR            |  |  |                                      |            |  |  |            (this is a data byte) ----+            |  |  +---- Count = 12   (thirteen data bytes)            |  +------- Info/cmd = 0 (this is information)            +---------- Channel = 3  (for instance)when the TNC has no RAM available to buffer the data line, it will respond witha code 2 failure message to inform you of the condition:              03 02 544C432042555359202D204C494C452049474C4F524544 00            |  |  T N C   B U S Y   -   L I N E   I G N O R E D  |            |  |                                                 |            |  +---- Code = 2 (Failure)      Null terminator ----+            +------ Channel = 3 (same as the info sent)If you send a bad command:              00 01 03 4A 55 4C 4B            |  |  |  J  U  N  K            |  |  |            |  |  +---- Count = 3    (four data bytes)            |  +------- Info/cmd = 1 (this is a command)            +---------- Channel = 0  (Doesn't matter here.)It will complain about it with a code 2 failure message:              00 02 49 4E 56 41 4C 49 44 20 43 4F 4D 4D 41 4E 44 00            |  |  I  N  V  A  L  I  D     C  O  M  M  A  N  D  |            |  |                                               |            |  +---- Code = 2 (Failure)     Null termination --+            +------- Channel = 0 (same as the command sent)  The  remaining  codes,  3 through 7, are used only as responses to a "G" pollcommand.  A 0 code can also be a response to a G poll.  A  0  code  means  thatnothing is available for that channel: that is, no events worthy of notice havetaken place on the channel polled.  This is the most common  response  to  a  Gcommand.              0x 00            |  |            |  +---- Code = 0    (Nothing available)            +------- Channel = x (same as the G command)  A code of 3 signifies a Link Status message.  These messages are:                               LINK STATUS MESSAGES               ({n}) BUSY fm {call} via {digipeaters}               ({n}) CONNECTED to {call} via {digipeaters}               ({n}) LINK RESET fm {call} via {digipeaters}               ({n}) LINK RESET to {call} via {digipeaters}               ({n}) DISCONNECTED fm {call} via {digipeaters}               ({n}) LINK FAILURE with {call} via {digipeaters}               CONNECT REQUEST fm {call} via {digipeaters}               ({n}) FRAME REJECT (x y z) fm {call} via {digipeaters}               ({n}) FRAME REJECT (x y z) to {call} via {digipeaters}  These messages should look familiar, since they are identical to the messagesdisplayed by the TNC in user mode.  {n} is the channel number.  Notice that thechannel number in the message is redundant information.  The channel number maybe omitted from this message in a future release.  For instance, if I connect to you direct on channel 2, a poll  of  channel  2(not  necessarily the next one, depending on what else is going on) will returnthe event:           02 03 28322920434F4E4E454354454420746F204B42354D55 00         |  |  ( 2 )   C O N N E C T E D   t o   K B 5 M U  |         |  |                                               |         |  +---- Code = 3 (Link Status) Null termination --+         +------- Channel = 2  Codes of 4 and 5 both signify a monitor header.  This  is  a  null-terminatedformat message containing the     fm {call} to {call} via {digipeaters} ctl {name} pid {hex}string  that  forms  a monitor header.  The monitor header is also identical tothe monitor header displayed in user mode.  If the code was  4,  the  monitoredframe contained no information field, so the monitor header is all you get.  Ifyou monitor KB6C responding to a connect request from me and then poll  channel0, you'll get:      0004666D204B42364320746F204B42354D552063746C2055612070494420463000    | | f m   K B 6 C   t o   K B 5 M U   c t l   U A   p i d   F 0 |    | |                                                             |    | +---- Code = 4 (Monitor, no info)        Null termination ----+    +------- Channel = 0 (Monitor info is always on channel 0)  If  the code was 5, the monitored frame did contain an information field.  Inthis case, another G command to channel 0 will return the monitored informationwith  a code of 6.  Since data transmissions must be transparent, the monitoredinformation is passed as a byte-count format transmission.    That  is,  it  ispreceded  by a count byte (one less than the number of bytes in the field).  Nonull terminator is used in this case.  Since codes  4,  5,  and  6  pertain  tomonitored  information,  they will be seen only on channel 0.  If you hear KB6Csay "Hi" to NK6K, and then poll channel 0, you'll get:      0005666D204B42364320746F204E4B364B2063746C204930302070494420463000    | | f m   K B 6 C   t o   N K 6 K   c t l   I 0 0   p i d   F 0 |    | |                                           | |               |    | |                           or whatever ----+-+               |    | |                                                             |    | +---- Code = 5 (Monitor, info follows)   Null termination ----+    +------ Channel = 0 (Monitor info is always on channel 0)and then the very next poll to channel 0 will get:           00 06 02 48 69 0D         |  |  |  H  i  CR         |  |  |        |         |  |  |        +----    (this is a data byte)         |  |  +---- Count = 2   (three bytes of data)         |  +------- Code = 6    (monitored information)         +---------- Channel = 0 (Monitor info is always on channel 0)  A code of 7 signifies connected information, so it will only  be  seen  on  aconnected  channel  1  through  4.  It is a byte-count format transmission, fordata transparency.  If you're connected to me on channel 4 and I  say  "Hi",  apoll of channel 4 will return:              04 07 02 48 69 0D            |  |  |  H  i  CR            |  |  |        |            |  |  |        +----    (this is a data byte)            |  |  +---- Count = 2   (three bytes of data)            |  +------- Code = 7    (connected information)            +---------- Channel = 4 (info was received on channel 4)                                   Chapter 7                    Querying Channel Status: the L command  One  of the most powerful features of the Host mode is the ability to ask theTNC for a status report on a given channel.  This  report  is  similar  to  thereport  given by the L command in user mode, but more extensive.  To obtain theChannel Status report, send an L command to the channel of interest.   The  TNCwill  (barring  error)  respond with a code 1 packet.  The information field ofthis packet will contain six decimal number in ASCII delimited by spaces.  A typical Channel Status query:              01 01 00 4C            |  |  |  L            |  |  |            |  |  +---- Count = 0    (one data byte)            |  +------- Info/cmd = 1 (this is a command)            +---------- Channel = 1  (give me a report on channel 1)A typical Channel Status report:              01 01 30 20 30 20 30 20 30 20 30 20 30 00            |  |  0     0     0     0     0     0  |            |  |                                   |            |  |              null termination ----+            |  +------- Code = 1    (Success with info)            +---------- Channel = 1 (this is a report on channel 1)  Channel 0 does not have as much state information as  a  regular  connectablechannel, so a Channel Status query to channel 0:              00 01 00 4C            |  |  |  L            |  |  |            |  |  +---- Count = 0    (one data byte)            |  +------- Info/cmd = 1 (this is a command)            +---------- Channel = 0  (give me a report on channel 0)Will return a Channel Status report similar to this one.              00 01 30 20 33 00            |  |  0     3  |            |  |           |            |  |           +---- null termination            |  +------- Code = 1    (Success with info)            +---------- Channel = 0 (this is a report on channel 0)  The interpretation of the returned information is as follows:                               CHANNEL STATUS FORMAT          a b c d e f          a = Number of link status messages not yet displayed          b = Number of receive frames not yet displayed          c = Number of send frames not yet transmitted          d = Number of transmitted frames not yet acknowledged          e = Number of tries on current operation          f = Link state              Possible link states are:               0 = Disconnected               1 = Link Setup               2 = Frame Reject               3 = Disconnect Request               4 = Information Transfer               5 = Reject Frame Sent               6 = Waiting Acknowledgement               7 = Device Busy               8 = Remote Device Busy               9 = Both Devices Busy              10 = Waiting Acknowledgement and Device Busy              11 = Waiting Acknowledgement and Remote Busy              12 = Waiting Acknowledgement and Both Devices Busy              13 = Reject Frame Sent and Device Busy              14 = Reject Frame Sent and Remote Busy              15 = Reject Frame Sent and Both Devices Busy          NOTE 1:  Only items a and b are displayed for channel 0.          NOTE 2:  Only states 0 - 4 are possible if version 1 is in use.  How  you  will use the Channel Status report will depend on your application.An interactive terminal program  might  simply  display  some  or  all  of  theinformation and leave it at that.  A mailbox program might want to wait for allpackets  to  be  acknowledged  before  starting  a  timeout  timer  or   beforedisconnecting.    A  mail  forwarder  would  want  to  make  sure  all data wasacknowledged before considering its task done.  Any program might want to  giveup  if  throughput is too low.  These functions are easy to implement with Hostmode.                                   Chapter 8                           Host Mode Error Recovery  What happens if something goes wrong on the computer-TNC link?   Maybe  thereis  a  loose  wire,  or  maybe  RF  got into the RS-232 lines.  Maybe it's justMurphy.  For whatever reason, the data on the line got corrupted.  RS-232 linksare  very  reliable, so you may never see an error, but the application programshould be ready to cope with one.  The error recovery program must assume  that  the  TNC  is  in  a  completelyunknown state.  It might be expecting more bytes to fill a byte count (if bytescoming from the computer were  lost).    It  might  be  simply  waiting  for  atransmission,  but  the computer thought there was an error since data was lostor corrupted on its way from the TNC.  What we want to do is hit the TNC with astream  of  data that will eventually bring it into a known state.  Preferably,this process should generate little or no spurious data on the AX.25 link.  The first thing to do is dump any further data that may be  coming  from  theTNC.  We don't know what it is, and so we can't use it.  The possibility existsthat this is connected information we're dropping on the floor.  This  is  justtoo bad.  There is nothing we can do.  Next,  we just send ^A's one at a time until the TNC responds.  The first few^A's may go to fulfill a byte count that the TNC  is  waiting  for.    If  thishappens  to  be a connected information transmission, these ^A's will go out onthe AX.25 link. Tough.  When any outstanding byte count is fulfilled  (no  morethan 256 should be required), the following five ^A's will be seen as a commandon channel 1.  This is why ^A is chosen: to make the TNC  interpret  the  extratransmission as a command.              01 01 01 01 01            |  |  |  ^A ^A            |  |  |            |  |  +-- Count of two bytes.            |  +----- This is a command.            +-------- Channel #1.A  command  of  "^A^A"  doesn't mean anything, so the TNC should respond with afailure message:              01 02 49 4E 56 41 4C 49 44 20 43 4F 4D 4D 41 4E 44 00            |  |  I  N  V  A  L  I  D     C  O  M  M  A  N  D  |            |  |                                               |            |  +---- Failure message.       Null termination --+            +------- Same channel as the command specifiedWe don't really care what the response is, though.  It may not be exactly  whatwe  expect.    For  instance,  the  first  ^A might fulfill the byte count of agarbled command.  This would usually generate an error message  of  some  othertype.   All we need is to get the first response.  Then we know that the TNC iswaiting for a command.  This implies that we have to wait between ^A's long enough to see if there isa  response yet.  This can make the recovery process a slow one.  For instance,if the TNC spuriously receives 00 00 FF, it  expects  to  see  256  data  bytesfollowing,  so  we  will  have to send 256 ^A's before we get a response (whichwill probably be a success message, since this is just a data  transmission  tothe TNC).  Fortunately, this error recovery process is not required very often.                                   Chapter 9                         Acknowledgements and Comments  Thanks are of course due to Ronald E. Raikes, WA8DED, for creating the WA8DEDAX.25 Version 2 Multi-channel TNC Firmware, for writing SS,  the  split  screenterminal  emulator that takes advantage of Host mode, and for proofreading thisdocument for accuracy.  Thanks are also due to Mike Busch, W6IXU,  for  writingthe mailbox software which was my first exposure to Host mode.  Comments  on  this document would be appreciated.  You can send them to me bypacket (KB5MU  KA6IQA on WestNet),  by  CompuServe  (75265,367),  by  telephone(619-458-1238) or by mail:          Paul T. Williamson, KB5MU        6583 Edmonton Ave.        San Diego, CA  92122Heck, you could even send an NTS radiogram.  SS,  the split screen terminal emulator, is an excellent example of Host-modesoftware.  It is available for non-commercial, non-profit use.  It runs  on  anIBM   PC   or  moderately  compatible,  and  provides  connect  status  displaycontinuously for all five TNC channels, a typing  buffer,  a  transmitted  databuffer,  a  receive buffer, and a Link Status line at the bottom of the screen.It is written in C for the Microsoft C Compiler version 3.0, with  a  trace  ofassembly  language for interface to console services.  I would be happy to senda copy of it to anyone who is interested and sends me a  diskette  with  returnpostage at the above address.  The  W6IXU  Mailbox  software is not available for distribution at this time.It will become available for distribution by some means when it stabilizes  anda suitable means of distribution is found.