THE N3EMO ORBIT SIMULATOR                                  VERSION 3.7                            Robert W. Berger, N3EMO                                 March 7, 19901 IntroductionThe N3EMO orbit program simulates the motions of earth satellites. The programwas written for use by amateur radio operators, but is useful to others, suchas astronomers interested in observing artificial satellites, spaceenthusiasts tracking shuttle missions, and meteorologists using weathersatellites.  The program is distributed in source form in the C language, andhas been used on a wide variety of computers, from micros to mainframes.2 Changes  The following changes have been made since the last public  release  (version2.3):   - The  internal  calculation  routines  have been rewritten to increase     performance, readability, and modularity.  This  facilitates  use  of     orbit's routines from other programs.   - A  new sidereal time reference is generated for each run. This allows     the program to maintain its accuracy without  having  to  be  updated     every year.   - Predicted  doppler  shifts  are much more accurate. The instantaneous     range-rate is now calculated  directly  instead  of  by  differencing     successive  range  samples.  The  doppler  shift displayed is now the     correct one for the sample time,  instead  of  an  average  from  the     preceding sample interval.   - Eclipses are optionally reported.   - Data for 0-180 degree elevation rotators is optionally provided.   - Satellite names may contain spaces.   - Single  character  abbreviations are provided for up to 62 satellites     (up from 26).   - A program is provided to convert  NASA  two-line  keplerians  to  the     AMSAT format used by the program.3 Compiling OrbitThe details of how to compile the program vary with the host machine. The mainprogram is in orbit.c, and the calculation subroutines are in orbitr.c.  Thesetwo files should be compiled and linked together to form the orbit executable.4 Data FilesTwo data files are required to run orbit; a third is optional.  The firstrequired data file, called "kepler.dat", contains the database of satellites."kepler.dat" is distributed by the Amateur Satellite Corporation (AMSAT), anon profit organization that designs and operates amateur radio satellites.The following is a sample entry from "kepler.dat":    Satellite: AO-13    Catalog number: 19216    Epoch time:      90054.30232176    Element set:      77    Inclination:       57.0658 deg    RA of node:       167.4162 deg    Eccentricity:    0.6899473    Arg of perigee:   221.7453 deg    Mean anomaly:      57.5228 deg    Mean motion:    2.09701313 rev/day    Decay rate:      -9.10e-07 rev/day^2    Epoch rev:            1301Satellite keplerians are also distributed by NASA in a format called the NASAtwo-line format.  The program in nasa.c converts a file from NASA format toAMSAT format for use with orbit.Keplerian sets for various interesting satellites are regularly posted to therec.ham-radio and sci.space usenet newsgroups.  The Datalink RBBS at (214)394-7438 has keplerians, as well as lots of other information of interest tosatellite and space enthusiasts.The second required data file is a site file which describes the observersposition and other station related data. Multiple site files are supported,with each one named after the corresponding observation site. The followingfile is "pgh.sit", a site file for station W3VC in Pittsburgh:    W3VC  Pittsburgh    40.45361                Latitude    79.94417                Longitude    300                     Height (Meters)    0                       Min Elevation (Degrees)    Eclipse    FlipThe first five lines are required, and give the name of the site, itsgeographic location, and the minimum satellite elevation above the horizonwhich is to be considered visible.The last two lines contain optional keywords which enable features of theorbit program. "Eclipse" enables reporting of eclipse times for thesatellites.  "Flip" enables alternative bearing/elevations for 0-180 degreeantenna rotators, such as the Kenpro rotators. By offering a choice of twosettings for any sky position, such rotators allow a satellite to be trackedthrough a pass without requiring the bearing rotor to be reoriented afterhitting a rotation stop.The optional data file, "mode.dat", allows orbit to provide scheduling andoperation data for a satellite. The following is an example of a "mode.dat":    Satellite: UO-11    Beacon:           145.8260 MHz    Satellite: AO-13    Beacon:           145.8260 MHz    Mode: B         from 0 to 165    Mode: JL        from 165 to 195    Mode: S         from 195 to 200    Mode: BS        from 200 to 205    Mode: B         from 205 to 256    Satellite: MIR    Beacon:           143.6250 MHz    Satellite: RS-10/11    Beacon:           29.357 MHzMode.dat may contain data for multiple satellites. The most common entry is"Beacon", which is the frequency orbit uses for calculating doppler shifts.5 Running OrbitWhen run, orbit will ask which satellite in "kepler.dat" you wish to simulate.Type the full satellite name, or the single character next to the satellitename. Orbit will then ask for the name of the site. If your site file is"foo.sit", type "foo".  Next enter the UTC date of the start of the simulationperiod. Years may be 2 or 4 digits. For example, 1990 may be entered as "1990"or simply "90". The UTC hour of the start of the simulation period is thenentered. Next comes the duration in days, followed by the time between samplesin minutes.  The final input is the name of the file for the output; hittingthe "Return" key places the output on the terminal. Here is the start of asample run:N3EMO Orbit Simulator  v3.7Available satellites:        a) AO-10        b) UO-11        c) RS-10/11        d) AO-13        e) UO-14        f) UO-15        g) AO-16        h) DO-17        i) WO-18        j) LO-19        k) FO-20        l) NOAA        	m) MET-2/15	n) MET-2/16        o) MET-2/17        p) MET-3/2        q) NOAA-11        r) MET-2/18        s) MET-3/3        t) SALYUT 7        u) MIRLetter or satellite name :dSite name :pghStart date (UTC) (Month Day Year) :3 10 90Starting Hour (UTC) :0Duration (Days) :1Time Step (Minutes) :10Output file (RETURN for TTY) :AO-13 Element Set 77W3VC  PittsburghDoppler calculated for freq = 145.826000 MHzSaturday 10 Mar 1990  ----Orbit # 1332----- U.T.C.   Az  El   Az'  El' Doppler Range Height  Lat  Long  Phase(256)0120:00  130   1  310  179   -1199  19383  14156  -15    32   24  B0130:00  127   6  307  174   -1152  20834  16051  -10    31   28  B0140:00  124  10  304  170   -1098  22222  17833   -6    31   32  B   EclipseThe output contains a line for each sample time at which the satellite'selevation above the horizon is equal to or greater than the "Min Elevation"entry in the site file. The first two columns are the bearing and elevation ofthe satellite from the observer's site. If "Flip" is enabled, the next twocolumns are the alternate form of the bearing and elevation, with theelevation greater than 90 degrees. The next column is the doppler shift of thesatellites beacon frequency, followed by the range from the satellite to theobserver, in meters, and the satellites height above the earth. Next is thelatitude and longitude of the point on earth directly underneath thesatellite. The phase is then printed, followed by any applicable operatingmodes from the satellites "mode.dat" entry.  If "Eclipse" is enabled in thesite file, and the satellite is in the earth's shadow, the word "Eclipse" isprinted.  If the satellite is in a highly elliptical orbit, a separate line is printedfor the exact time of the apogee.