Packet Driver Protocol                                  G. L. Chesson                               Bell Laboratories           Abstract                     These notes describe the packet driver link proto-               col that was supplied with the Seventh Edition of UNIX*               and is used by the UUCP program.           General                Information flow between a  pair  of  machines  may  be          regulated  by  first  representing  the  data  as  sequence-          numbered packets of data and then  establishing  conventions          that  govern the use of sequence numbers.  The PK, or packet          driver, protocol is a particular instance of  this  type  of          flow-control  discipline.   The  technique  depends  on  the          notion of a transmission window to determine upper and lower          bounds  for  valid  sequence  numbers.   The  transmitter is          allowed to retransmit packets having sequence numbers within          the  window  until  the receiver indicates that packets have          been correctly received.  Positive acknowledgement from  the          receiver  moves  the  window; negative acknowledgement or no          acknowledgement causes retransmission.   The  receiver  must          ignore  duplicate  transmission,  detect  the various errors          that may occur, and inform the transmitter when packets  are          correctly or incorrectly received.                The following paragraphs describe the  packet  formats,          message exchanges, and framing used by the protocol as coded          in the UUCP  program  and  the  UNIX  kernel.   Although  no          attempt will be made here to present internal details of the          algorithms that were used, the checksum routine is  supplied          for the benefit of other implementors.           Packet Formats                The protocol is defined in terms of  message  transmis-          sions  of  8-bit  bytes.   Each message includes one control          byte plus a data segment of zero or more information  bytes.          The  allowed data segment sizes range between 32 and 4096 as          determined by the formula 32(2k) where k is a 3-bit  number.          The  packet  sequence numbers are likewise constrained to 3-          bits; i.e. counting proceeds modulo-8.                The control byte is partitioned into  three  fields  as          depicted below.                   bit  7  6  5  4  3  2  1  0                       t  t  x  x  x  y  y  y           The  t  bits  indicate  a  packet  type  and  determine  the          interpretation  to be placed on the xxx and yyy fields.  The          various interpretations are as follows:                     tt      interpretation                     00      control packet                    10      data packet                    11      `short' data packet                    01      alternate channel           A data segment accompanies all  non-control  packets.   Each          transmitter  is constrained to observe the maximum data seg-          ment size established during initial synchronization by  the          receiver  that  it  sends  to.  Type 10 packets have maximal          size data segments.  Type 11, or `short', packets have  zero          or more data bytes but less than the maximum.  The first one          or two bytes of the data  segment  of  a  short  packet  are          `count'  bytes that indicate the difference between the max-          imum size and the number of bytes in the short segment.   If          the difference is less than 127, one count byte is used.  If          the difference exceeds 127, then the low-order seven bits of          the  difference are put in the first data byte and the high-          order bit is set as an indicator that the remaining bits  of          the  difference are in the second byte.  Type 01 packets are          never used by UUCP and need not be discussed in detail here.                The sequence number of a non-control packet is given by          the  xxx  field.   Control  packets  are not sequenced.  The          newest sequence number, excluding  duplicate  transmissions,          accepted  by  a  receiver is placed in the yyy field of non-          control packets sent to the `other' receiver.                There are no  data  bytes  associated  with  a  control          packet,  the  xxx field is interpreted as a control message,          and the yyy field is a value accompanying the  control  mes-          sage.   The  control messages are listed below in decreasing          priority.  That is, if several control messages  are  to  be          sent, the lower-numbered ones are sent first.                xxx     name    yyy                1       CLOSE   n/a               2       RJ              last correctly received sequence number               3       SRJ             sequence number to retransmit               4       RR              last correctly received sequence number               5       INITC           window size               6       INITB           data segment size               7       INITA           window size                The CLOSE message  indicates  that  the  communications          channel  is  to  be  shut  down.  The RJ, or reject, message          indicates that the receiver has detected an  error  and  the          sender should retransmit after using the yyy field to update          the window.  This mode of retransmission is usually referred          to  as  a  `go-back-N'  procedure.   The  SRJ,  or selective          reject, message carries with it the  sequence  number  of  a          particular  packet to be retransmitted.  The RR, or receiver          ready, message indicates that the receiver has  detected  no          errors;  the  yyy  field  updates  the sender's window.  The          INITA/B/C messages are used to set window and  data  segment          sizes.  Segment sizes are calculated by the formula 32(2yyy)          as mentioned above, and window sizes may range between 1 and          7.                Measurements of the protocol running  on  communication          links  at rates up to 9600 baud showed that a window size of          2 is optimal given a packet  size  greater  than  32  bytes.          This  means that the link bandwidth can be fully utilized by          the software.  For this reason the SRJ  message  is  not  as          important  as  it  might  otherwise  be.  Therefore the UNIX          implementations no longer generate or respond  to  SRJ  mes-          sages.   It  is mentioned here for historical accuracy only,          and one may assume that SRJ is no longer part of the  proto-          col.           Message Exchanges                   Initialization                Messages are exchanged between four  cooperating  enti-          ties:  two  senders  and two receivers.  This means that the          communication channel  is  thought  of  as  two  independent          half-duplex  data paths.  For example the window and segment          sizes need not be the same in each direction.                Initial synchronization is accomplished with two  3-way          handshakes:  two  each  of  INITA/INITB/INITC.   Each sender          transmits INITA messages repeatedly.  When an INITA  message          is received, INITB is sent in return.  When an INITB message          is received and an INITB message has  been  sent,  an  INITC          message  is  sent.   The INITA and INITB messages carry with          them the packet and window size that each receiver wants  to          use,  and  the  senders  are  supposed  to  comply.   When a          receiver has seen all three INIT messages,  the  channel  is          considered to be open.                It is possible to design  a  protocol  that  starts  up          using   fewer   messages  than  the  interlocked  handshakes          described above.  The  advantage  of  the  more  complicated          design  lies  in  its use as a research vehicle: the initial          handshake sequence is completely symmetric, a handshake  can          be initiated by one side of the link while the connection is          in use, and the software to do this can  utilize  code  that          would ordinarily be used only once at connection setup time.          These properties were used in experiments  with  dynamically          adjusted  parameters.   That  is attempts were made to adapt          the window and segment sizes to changes observed in  traffic          while a link was in use.  Other experiments used the initial          handshake  in a different way for  restarting  the  protocol          without  data loss after machine crashes.  These experiments          never worked well in the packet driver  and  basically  pro-          vided the impetus for other protocol designs.  The result as          far as UUCP is concerned  is  that  initial  synchronization          uses  the  two  3-way  handshakes, and the INIT messages are          ignored elsewhere.                   Data Transport                After initial  synchronization  each  receiver  sets  a          modulo-8  incrementing  counter  R  to 0; each sender sets a          similar counter S to 1.  The value of R is always the number          of  the most recent correctly received packet.  The value of          S is always the first sequence number in the output  window.          Let  W  denote window size.  Note that the value of W may be          different for each sender.                A sender may transmit packets with sequence numbers  in          the  range  S  to  (S+W-1) mod-8.   At any particular time a          receiver expects arriving packets to  have  numbers  in  the          range  (R+1) mod-8  to  (R+W) mod-8.  Packets must arrive in          sequence number order are are only  acknowledged  in  order.          That  is, the `next' packet a receiver will acknowledge must          have sequence number (R+1) mod-8.                A receiver acknowledges  receipt  of  data  packets  by          arranging  for  the value of its R counter to be sent across          the channel where it will be used to update  an  S  counter.          This is done in two ways.  If data is flowing in both direc-          tions across a channel then each receiver's current R  value          is  carried in the yyy field of non-control packets.  Other-          wise  when  there  is  no  bidirectional  data  flow,   each          receiver's R value is transmitted across the link as the yyy          field of an RR control packet.                Error handling is up to the discretion of the receiver.          It  can ignore all errors in which case transmitter timeouts          must provide for retransmission.  The receiver may also gen-          erate  RJ error control packets.  The yyy field of an incom-          ing RJ message replaces the S value of the local sender  and          constitutes  a  request  for retransmission to start at that          sequence number.  The yyy field of an incoming  SRJ  message          selects a particular packet for retransmission.                The resemblance between the flow control  procedure  in          the  packet driver and that defined for X.25 is no accident.          The packet driver protocol  began  life  as  an  attempt  at          cleaning  up  X.25.   That  is  why,  for  example,  control          information is uniform in length (one byte), there is no RNR          message  (not  needed), and there is but one timeout defined          in the sender.                   Termination                The CLOSE message is used to terminate  communications.          Software on either or both ends of the communication channel          may initiate termination.  In any case when one end wants to          terminate it sends CLOSE messages until one is received from          the other end or until a programmable limit on the number of          CLOSE  messages  is  reached.   Receipt  of  a CLOSE message          causes a CLOSE message to be sent.  In the UNIX  environment          it  also  causes  the  SIGPIPE or `broken pipe' signal to be          sent to the local process using the communication channel.                   Framing                The term framing is used to  denote  the  technique  by          which  the  beginning  and end of a message is detected in a          byte stream; error  control  denotes  the  method  by  which          transmission  errors  are  detected.  Strategies for framing          and error control depend upon additional  information  being          transmitted  along  with  the control byte and data segment,          and the choice of a particular strategy usually  depends  on          characteristics  of  input/output  devices  and transmission          media.                Several framing techniques are in used in support of PK          protocol  implementations, not all of which can be described          in detail here.  The technique used on  asynchronous  serial          lines will be described.                A six byte framing envelope is  constructed  using  the          control  byte C of a packet and five other bytes as depicted          below.                    <DLE><k><c0><c1><C><x>          The <DLE> symbol denotes the ASCII ctrl/P character.  If the          envelope  is  to  be followed by a data segment, <k> has the          value log2(size) - 4; i.e. 1 <= k <= 8.  If k is 9, then the          envelope  represents  a  control  packet.  The <c0> and <c1>          bytes are the low-order and high-order bytes respectively of          0xAAAA  minus  a 16-bit checksum.  For control packets, this          16-bit checksum is the same as the control byte C.  For data          packets,  the  checksum  is calculated by the program below.          The <x> byte is the exclusive-or of  <k><c0><c1><C>.   Error          control  is  accomplished  by  checking  a  received framing          envelope for compliance with the definition, and comparing a          checksum function of the data segment with <c0><c1>.                This particular framing strategy assumes data  segments          are constant-sized: the `unused' bytes in a short packet are          actually transmitted.  This  creates  a  certain  amount  of          overhead  which  can  be  eliminated  by  a more complicated          framing technique.  The advantage of this strategy  is  that          i/o  devices  can  be  programmed  to  take advantage of the          constant-sized framing envelopes and data segments.                The checksum calculation is  displayed  below  as  a  C          function.   Note that the code is not truly portable because          the definitions of short and char are not  necessarily  uni-          form  across  all machines that might support this language.          This code assumes that short and  char  are  16  and  8-bits          respectively.           /* [Original document's version corrected to actual version] */               chksum(s,n)               register char *s;               register n;               {                       register short sum;                       register unsigned short t;                       register short x;                        sum = -1;                       x = 0;                        do {                               if (sum<0) {                                       sum <<= 1;                                       sum++;                               } else                                       sum <<= 1;                               t = sum;                               sum += (unsigned)*s++ & 0377;                               x += sum^n;                               if ((unsigned short)sum <= t) {                                       sum ^= x;                               }                       } while (--n > 0);                        return(sum);               }           The checksum routine used in  gnuucp  has  been  updated  to          avoid  depending  on  the particular sizes of char and short          variables.  As long as a char holds 8 bits or  more,  and  a          short  holds  16  bits or more, the code will work.  To test          it, uncomment the ``#define short long'' below.  A good com-          piler  produces the same code from this function as from the          less portable version.                #define HIGHBIT16       0x8000               #define JUST16BITS      0xFFFF               #define JUST8BITS       0x00FF               #define MAGIC           0125252 /* checksum is subtracted                                                  from this */               int               pktchksum(msg, bytes)                       unsigned char *msg;                       int bytes;               {                       return (JUST16BITS &                              (MAGIC - (chksum(&msg[6], bytes)                              ^ (JUST8BITS & msg[4]))));               }                int               chksum(s,n)               register unsigned char *s;               register n;               {               /* #define short long   /* To make sure it works with                                          shorts > 16 bits */                       register short sum;                       register unsigned short t;                       register short x;                        sum = (-1) & JUST16BITS;                       x = 0;                       do {                     /* Rotate "sum" left by 1 bit, in a 16-bit barrel */                               if (sum & HIGHBIT16)                               {                                       sum = (1 + (sum << 1)) & JUST16BITS;                               }                               else                                       sum <<= 1;                               t = sum;                               sum = (sum + (*s++ & JUST8BITS)) & JUST16BITS;                               x += sum ^ n;                               if ((unsigned short)sum <= t)                                       sum = (sum ^ x) & JUST16BITS;                       } while (--n > 0);                        return(sum);               #undef short            /* End of debugging check */               }