Technical Notes

                                        SKSH

                           A ksh-like Shell for the Amiga

                                     Version 1.2


                                  (Copyright) 1989 

                                     Steve Koren

                                  November 19, 1989











































          Implementation Notes

            SKsh is the result of over 3 month's  of  evening  and  weekend
            work on an Amiga 2000 with a Xetec hard disk  controller,  85mb
            Seagate drive, and 3mb of ram.  The parser,  lexical  analyzer,
            and program architecture were completed very quickly;  most  of
            the time was spent  trying  to  figure  out  how  to  do  Amiga
            specific things (like directories) and working around  compiler
            bugs.

            SKsh has a parser that  was  generated  using  Amiga  yacc  and
            modified by hand to deal with some  special  features  of  SKsh
            (such as  command  substitution).   The  lexical  analyzer  was
            written by hand, since I needed some capabilities  not  present
            in Lex.  SKsh is composed of 49 .c files ranging  from  100  to
            1100 lines, 21 .h files, and one .y file.

            Internally, SKsh uses hash tables to keep track  of  variables,
            aliases, functions, and keywords.  A stack of  hash  tables  is
            maintained, and each time a function  is  called,  a  new  hash
            table  is  pushed  onto  the  stack.   Then,  when  a  name  is
            referenced, it is looked up in the hash  table  stack  starting
            with the most recent hash table.  When a  function  exits,  the
            most recent  hash  table  is  popped  off  the  stack  and  its
            contents are freed.  Hash  table  entries  have  an  associated
            type (variable, function, etc),  and  a  value,  which  can  be
            either a text  string  (such  as  an  alias  definition)  or  a
            pointer to a parse tree (for a function).

            SKsh was written  to  be  reentrant,  so  that  in  the  future
            interprocess pipes may be used between  internal  and  external
            commands.  Thus, all evaluation is done using only  information
            passed around in an "EVAL_PACKET" structure so that no  globals
            are referenced.  Each  execution  of  the  command  interpreter
            generates its own hash table stack, its own  pointer  to  input
            and output files, etc.  The few parts of  SKsh  which  are  not
            reentrant  are  written   using   a   semaphore-based   locking
            mechanism.  This locking mechanism is intelligent; it does  not
            lock out all other tasks  from  the  system  (as  Forbit()  and
            Permit() do), but simply allows only a single task  to  execute
            a given section of program code at one time.

            All output is done through a single low  level  routine  which,
            given an EVAL_PACKET and some text, will route it to  either  a
            file or a string (in the  case  of  command  substition).   The
            length of the space allocated for this string is  kept  in  the
            EVAL_PACKET, and if the new text  would  cause  the  string  to
            overflow its allocated space, more space is allocated  and  the
            original  is  copied  into  the  new  space.    Thus,   command
            substition and variables can  deal  with  text  of  any  length
            limited only by free memory.

            There are no hard-coded  branches  to  routines  which  execute
            SKsh  builtin  commands.   A  single  structure  contains   all


          SKSH Amiga Shell             Page 2              Technical Notes









            necessary information for  builtin  commands,  including  their
            name, a pointer to their execution routine,  and  a  few  other
            things.  This architecture makes it trivial to add new  builtin
            commands.  Keywords are dealt with in the same way.

            A series of test scripts  is  run  whenever  SKsh  is  changed.
            These scripts test all  the  SKsh  commands  and  syntax.   The
            output of these tests are compared against known  good  results
            to verify that  no  previously  working  commands  were  broken
            inadvertantly.  The entire series  of  21  test  scripts  takes
            about 10 minutes to run on a stock 7.x mHz Amiga 2000.

            Since the entire SKsh project was implemented on an Amiga,  and
            SKsh was designed for Amigas, it  currently  runs  only  there.
            It was, however, designed with machine  independence  in  mind.
            The  machine  specific  code  is  enclosed  in   #ifdef   AMIGA
            statements,  and  could  conceivably  be  replaced  with   code
            specific to another machine.






































          SKSH Amiga Shell             Page 3              Technical Notes