EtherVision 

                      The Ethernet LAN monitor 


DESCRIPTION 

Ethervision is designed to monitor and display activity of an Ethernet Local 
Area Network (LAN).  EtherVision works with all Ethernet media types including 
coax, twisted pair, and fiber. Operations exist to monitor Ethernet traffic 
activity and errors in real-time, show network utilization, assign user names 
to network addresses, and more.  Such information about traffic activity 
enables the user to determine network loading, show traffic generated by 
individual stations (also called nodes), and resolve problems. 

There are two real-time monitoring display modes available while monitoring 
traffic.  These modes are: 

   - normal  -- Tracks packets and kilobytes sent by each station 
   - skyline -- Aggregate network traffic display over time + network 
                utilization 

Within each display mode, there are error counters and numerous options to 
tailor the display. 

Alphanumeric names may be associated with network addresses making it easier to 
interpret network activity displays.  This information is stored in a file 
which may be recalled and changed at anytime. The basic operations available 
in EtherVision are summarized in 

OPERATION 

The demo for EtherVision (which monitors a simulated network) is run by typing 
EV_DEMO from the directory containing EV_DEMO.EXE. When EtherVision is first 
invoked, the user is presented with a main menu.  An action from this menu may 
be selected by pressing the first letter of the option or moving the cursor 
up/down with the up/down arrow keys and then pressing Enter.  As a shortcut, 
pressing the first letter of the option causes immediate action. The user may 
return to the main menu at any time by pressing the Esc key.  Each menu option 
is described in more detail below. 

Assigning Names 

Selecting the ASSIGN NAMES from the main menu allows you to associate names 
with network addresses.  For example, the name 'Robert' may be given to the 
address 0000860005FC (address are always 12 hex digits = 48 bits), making it 
easier to remember what devices and workstations are at what network adapter 
addresses. Upon selecting this option, a screen appears in which two new 
windows are presented along with the function key options at the bottom of the 
display.  The Name Assignments window displays a column of network addresses 
(in hex) followed by the name.  If no name has been assigned by the user, then 
the default appears which consists of the station address preceded by "NAME?-".  If there are more names than can be displayed, an arrow will appear in the 
lower left-hand corner of the window.  Then, the names which are displayed in 
the window can be changed by moving the highlight bar up and down using the 
arrow keys or PgUp/PgDn (page up/page down) keys.  Arrows will appear in the 
upper left-hand corner and/or lower right-hand corner of the window to 
indicate the presence of more names above or below the ones displayed. The 
lower window is for user input.  To change a name, select the station address 
by moving the highlight bar up and down using the arrow keys or PgUp/PgDn keys 
and press Enter. 

To perform other functions, use the function keys as follows: Function key F2 
(Add Name) allows a name to be added or changed. If the network has been 
actively monitored prior to assigning names, the network addresses that were 
active are displayed, followed by name currently associated with that network 
address. Pressing F2 allows the user to input a new or different name for a 
given address.  Function key F3 (Del Name -- Delete Name) will prompt the user 
to delete the name currently selected at the highlight bar.  Function key F4 
(Sort Addr -- Sort Address) sorts the entries in ascending order by station 
address. Function key F5 (Sort Name) sorts the entries in ascending order by 
alphanumeric name.  Function key F6 (Load -- Load File) allows the user (in 
the operational version only) to load a previously created name file.  The 
file may be created with a spreadsheet (with ASCII comma delimited 
import/export capability), word processor, or within EtherVision itself.  
Function key F7 (Save -- Save File) will (in the operational version only) 
save the name assignments to a file, in ASCII comma delimited format.  
Function key F8 (CLR --Clear) will clear all of the name entries.  To leave 
Assign Logical Names, press the Esc key to return to the main menu. 

Monitoring Traffic 

Selecting MONITOR TRAFFIC from the main menu puts EtherVision into its real-
time monitoring mode showing various activity on the Ethernet.  The top of 
this display shows the date and time when monitoring began or when the 
displayed was cleared using the F7 function key.  Most of the display is 
devoted to showing the stations (up to 80; use the arrow keys or PgUp/PgDn to 
show additional stations if there are more) and their packet counts (those 
packets sent by that station). 

The bottom portion of the display shows other counters and conditions.  From 
left to right, these counters and status indicators are explained as follows:  
STNS or stations, shows the total number of active stations (counting the 
number of stations on the display would yield the same result).  If there are 
more stations (over 80) than can be displayed on the screen, then the up/down 
arrow keys and the PgUp/PgDn keys may be used to show the additional stations. 
Packets shows the grand total of all packets counted. Kbytes or kilobytes 
shows grand total, in thousands of bytes, of all packets counted. Bcast or 
Broadcast, shows the number of packets that were broadcast to all stations. 
PPS/Peak indicates the packets per second and peak packets per second since 
monitoring began. 

CRC shows the number of packets in which the cyclic redundancy check performed 
on the packet by the EtherVision adapter did not agree with the value in the 
packet, indicating garbled bits within the packet.  Each time a CRC error 
occurs, a "beep" will be heard. Align or alignment shows the number of packets 
in which the bits have "shifted" out of alignment. Whenever an alignment error 
occurs, a "beep" will be heard. Frgmt or Fragment shows the number of packets 
which have truncated prematurely.  Fragment errors usually indicate 
collisions.  Each occurrence of a fragment error will cause a "beep" to be 
heard.  MU or Missed/Unprocessed indicate the inability for the hardware 
and/or software to keep up with Ethernet traffic.  A triangle under the M 
indicates that the hardware (adapter/PC) missed a packet.  A triangle under 
the U indicates that the software (EtherVision itself) was unable to process 
the packet before its buffer filled. On an 80386-based PC, this should rarely 
happen.  On an 80286-based PC this may happen during periods of heavy, 
sustained traffic. This "MU" feature is unique to EtherVision -- many 
competing monitor programs will not indicate that packets could not be 
processed in time. Elapsed indicates the elapsed time since monitoring began 
or was cleared using function key F7. 

The bottom most line displays the function keys and their assignments.  These 
function keys are discussed in more detail as follows:

Function key F2 (Stn ID -- Station Identification) is used to change the way 
in which the station IDs are displayed.  The default is either the node 
address or the station's logical name. The logical name is shown if the user 
loaded names or assigned names prior to monitoring, using the Assign Names 
option from the Main Menu (if there is a name assigned to an address which is 
not active, then a '-' will appear after the name instead of a packet count.)   
If the logical name is not chosen for display, then the station ID is shown as 
the station's network addresses in hex notation.   Pressing function key F2 
will toggle between these three different formats. 
  
Function key F3 (Sort STN -- Sort Station) will sort the station by IDs, in 
ascending order.  The ordering is determined by the way the station IDs are 
displayed.  For example, if the station names are displayed, then the sort 
will be by name.  Likewise, if the station addresses are displayed, then the 
sort will be by station address. Both sorts are in ascending order. 

Function key F4 (Sort CNT -- Sort Count) will sort the stations by the number 
of packets.  The sort is in descending order such that the most active 
stations appear first. 

Function key F5 (Cnt/Pct -- Station Count/Percent) toggles between displaying 
of either the station packet counts or percentage of total packets counted. 

Function key F6 (Pkt/Sky -- Packet/Skyline) Toggles between the packet count 
display and skyline/network utilization display.  If the skyline is chosen, 
then the screen will display total packet counts on a logarithmic scale by the 
second or by the minute, for the last 60 seconds or 60 minutes respectively.  
The second or minute mode is selected when the skyline is displayed by 
pressing function key F8.  The network utilization scale is update once per 
second and will show a solid bar when the network is utilized more than 1 
percent.  The peak utilization is marked with a triangle. 

EQUIPMENT REQUIREMENTS FOR OPERATIONAL VERSION 

EtherVision is designed to work with virtually all PC/MS-DOS machines with a 
Novell NE2000 compatible Ethernet adapter card installed.  PC/MS-DOS 3.1 or 
higher and a minimum of 384K of free RAM is required (more RAM gives 
EtherVision more buffers).  Since Ethernet can accommodate in excess of 16,000 
packets per second, best possible network monitoring performance is achieved 
with a PC with a fast 80286 (12 Mhz or better) or 80386 processor (a feature 
unique to EtherVision is notification of packets that could not be processed 
because the hardware (adapter + PC) could not keep up and notification if the 
software (EtherVision) could not keep up).  A monochrome or color display may 
be used.  EtherVision is not copy-protected but is serialized. 

ORDERING INFORMATION 

The operational EtherVision is priced at $225, which includes a user's 
manual, and choice of 3 1/2" or 5 1/4" diskette.  EtherVision with a Triticom 
certified 16-bit Ethernet adapter is priced at $525.  For more information or 
to order contact Triticom at P.O. Box 11536, St. Paul, MN 55111; (612) 937-
0772.