Installing or UpgradingNetWare Lite v1.1

Install NetWare Lite v1.1

Use these procedures when the workstation does not have a copy of
NetWare Lite v1.0.If you install the same copy of NetWare Lite v1.1
on more than one computer on your network, you get a license
violation error.

For Server-only, Client-only, or Client-server Workstations Loading
from a Hard Drive   

1.   Place the NetWare Lite v1.1 PROGRAM diskette into a disk
drive. With the DOS prompt set to the disk drive, type INSTALL and
press <Enter>. 

2.   Follow the instructions on the screen.

For Client-only Workstations Loading from a Client Diskette (Except
those Loading from a Bootable 5.25-inch, Low-density Client
Diskette) 

1.   Format a diskette (either bootable or non-bootable).   

2.   Place the NetWare Lite v1.1 PROGRAM diskette into a disk
drive. With the DOS prompt set to the disk drive, type INSTALL and
press <Enter>. 

3.   Select "Make this machine a client."    

4.   When the "Install Client" form appears, change the "Target
directory for CLIENT software" field to a disk drive letter, press
<Enter>, and follow the instructions on the screen.Files are copied
to memory and a prompt appears.    

5.   When prompted for the target diskette, insert the formatted
diskette into the specified disk drive, press <Esc>, and follow the
instructions on the screen.

For Client-only Workstations Loading from a Bootable 5.25-inch,
Low-density Client Diskette   

1.   Format a blank, non-bootable diskette.  

2.   Format a blank bootable diskette.  

3.   Place the NetWare Lite v1.1 PROGRAM diskette into a disk
drive. With the DOS prompt set to the disk drive, type INSTALL and
press <Enter>. 

4.   Select "Make this machine a client."    

5.   When the "Install Client" form appears, change the "Target
directory for CLIENT software" field to the same disk drive that
the PROGRAM diskette is in, press <Enter>, and follow the
instructions on the screen.Files are copied to memory and a prompt
appears.  

6.   When prompted for the target diskette, remove the PROGRAM
diskette from the disk drive, insert the non-bootable diskette into
the same disk drive, press <Esc>, and follow the instructions on
the screen.    

7.   Delete NET.HLP from the non-bootable diskette.This removes the
online help function, but makes enough space to copy the files to
a bootable diskette.     

8.   Copy the files from the non-bootable diskette to the bootable
diskette. See your DOS documentation for copy instructions. 

9.   Boot the computer using the NetWare Lite v1.1 bootable client
diskette.

Upgrade From NetWare Lite v1.0 to v1.1

Use the upgrade option to change a workstationÕs NetWare Lite v1.0
to v1.1. You can upgrade all computers on the network running
NetWare Lite v1.0 to v1.1 with only one copy of NetWare Lite v1.1

For Server-only, Client-only, or Client-server Workstations Loading
from a Hard Drive   

1.   Place the NetWare Lite v1.1 PROGRAM diskette into a disk
drive. With the DOS prompt set to the disk drive, type INSTALL and
press <Enter>. 

2.   Select "Upgrade this machine to v1.1."  

3.   Follow the instructions on the screen.

For Client-only Workstations Loading from a Client Diskette (Except
those Loading from a Bootable 5.25-inch, Low-density, Client
Diskette) 

1.   Place the NetWare Lite v1.1 PROGRAM diskette into a disk
drive. With the DOS prompt set to the disk drive, type INSTALL and
press <Enter>. 

2.   Select "Upgrade this machine to v1.1."  

3.   When the "Type the directory path of NWLITE 1.0" prompt
appears, type the disk drive letter and press <Enter>.Files are
copied to memory and a prompt appears.  

4.   When prompted for the target diskette, insert the
workstationÕs client diskette into the specified disk drive and
press <Esc>.   

5.   Follow the instructions on the screen.

For Client-only Workstations Loading from a Bootable 5.25-inch,
Low-density, Client DisketteNetWare Lite v1.1 client software fits
on a non-bootable 5.25- inch, low-density diskette, but it does not
fit on a bootable diskette.   

1.   Format a blank, non-bootable diskette.  

2.   Copy the NetWare Lite v1.0 CLIENT.EXE from the original
NetWare Lite v1.0 PROGRAM diskette or from your NetWare Lite v1.0
client diskette to the non-bootable diskette. (See your DOS
documentation for copy instructions.)   

3.   Place the NetWare Lite v1.1 PROGRAM diskette into a disk
drive. With the DOS prompt set to the disk drive, type INSTALL and
press <Enter>. 

4.   Select "Upgrade this machine to v1.1."  

5.   When the "Type the directory path of NWLITE v1.0" prompt
appears, if your PROGRAM diskette is in drive A:, type A: and press
<Enter>; if your PROGRAM diskette is in drive B:, type B: and press
<Enter>.Files are copied to memory and a prompt appears.    

6.   When prompted for the target diskette, remove the PROGRAM
diskette from the disk drive, insert the non-bootable diskette with
the copy of NetWare Lite v1.0 CLIENT.EXE on it into the same drive,
and press <Esc>.    

7.   After CLIENT.EXE is upgraded and the other files are copied to
the diskette, delete NET.HLP.This removes the online help function,
but makes enough space to copy the files to a bootable diskette. 

8.   Copy the files from the non-bootable diskette to your NetWare
Lite v1.0 bootable client diskette. See your DOS documentation for
copy instructions.  

9.   Reboot the computer using the Netware Lite v1.0 bootable
client diskette.