NMI  Version 1.03
                                  by Dennis Lee


             Have you ever seen the message 'PARITY CHECK' on your
          display?  If you have, you've probably noticed that it
          always seems to happen at the most inopportune time.  You're
          cruising along putting the finishing touches on something
          that you've worked long and hard, just to look up from the
          keyboard to a blank display with only the words 'PARITY
          CHECK' in the upper left corner.  Your heart sinks into your
          shoes, your face gets flush, and palms begin to sweat, as
          you try franticly to figure a way out of this one... but you
          KNOW that you've lost everything!  Your only option is to
          power off and start over.

             NMI is a resident program to replace the non-maskable
          interrupt handler that the PC uses to handle parity errors.
          In the event of a parity error, NMI will interrupt the
          currently executing program(s) and begin testing memory,
          looking for the error.  It will continue testing until
          either it locates a failing address, or you interrupt it by
          pressing a key.  If a failure is located, NMI will display
          the failing 64K bank, exact memory address, and if possible,
          the failing bit(s). You have the option to continue or
          terminate testing.  If you interrupt the memory test, or
          elect not to continue testing after an error is detected,
          you are given the options to return to the interrupted
          program(s) with or without parity checking enabled, or to
          reboot the system.

             The memory test is of a nondestructive type, in that it
          will preserve the current contents of memory.  It can be
          executed any time without regard for concurrently executing
          processes.  It's also a very thorough test, reading and
          writing each byte of memory with several different bit
          patterns and checking for parity errors following each read
          or write operation.  Every memory location is tested,
          including the locations used by NMI.

             This all sounds a bit like insurance doesn't it?  It
          doesn't do you a bit of good unless you have a tragedy on
          your hands.  Well, I like programs that you can play with,
          and since you've got this neat little memory test just
          sitting there in memory, why not be able to use it? NMI will
          execute the memory test any time you like, as many times as
          you like!

             If you're like me (a memory miser), the question in your
          mind right now is... 'Just how much memory does this thing
          eat?'.  The answer, approximately 1.8K including the Program
          Segment Prefix and a normal size environment.  In English,
          that means about 1.8K TOTAL!  Even I can afford that.







                                     Page 1





                                NMI  Version 1.03
                                  by Dennis Lee


          PROGRAM LOADING
          ---------------

             NMI /Q/I/T####
                  | | |
                  | | Test memory #### times.
                  | |
                  | |   If the number of test repetitions is 0 or
                  | |   blank, then the memory test loops indefinitely
                  | |   until an error is detected or you interrupt it
                  | |   by pressing a key.  This option may be used to
                  | |   invoke the memory test from the command line
                  | |   or a batch file.  NMI need not be installed to
                  | |   run the memory test.
                  | |
                  | Install NMI.
                  |
                  |   This option must be selected the first time NMI
                  |   is executed if you desire to replace the current
                  |   non-maskable interrupt handler.  It need not,
                  |   and should not be specified again.
                  |
                  Quiet

                    This option is selected to suppress display of the
                    program logo when NMI is installed.


          *  If no parameters are specified, or the specified
             parameters are invalid, NMI will display the program logo
             followed by a summary of valid parameters.

          *  Parameters need not be separated, however, they may be
             separated by one or more spaces, tabs, commas, slashes,
             or semicolons.

          *  Alphabetic parameters may be upper or lower case.

          *  Parameters may be entered in any order or combination so
             long as the number of test repetitions follows the 'T'
             parameter and they are not separated by another
             parameter.














                                     Page 2





                                NMI  Version 1.03
                                  by Dennis Lee


          +--------------------------+
          |   TESTING ####K MEMORY   |
          | Bank    Bit     Address  |
          |  00  P76543210 0000:0000 |
          |        0000 Passes       |
          +--------------------------+

             When the memory test is invoked, either as the result of
          a parity error, or from the command line, the above window
          will be displayed in the upper left corner of the screen.
          This window indicates the size of the memory being tested,
          as sensed by NMI, the 64K bank currently being tested, and
          the number of successful test repetitions.  In the interest
          of speed, the 'Address' field is updated only for each 64K
          bank in this window.  The 'Bit' field is used to indicate
          failing bits and will not change unless an error is
          detected.

             If the 'Esc' key is pressed, the memory test will be
          terminated with parity checking enabled, and control passed
          to the interrupted process. Any other key will exit the
          memory test and display the termination options.

             Pass one of the memory test is always executed in a read
          only mode.  This increases the possibility of detecting the
          failing address.  If an error is detected in the first pass,
          the address will will be written to in hopes of detecting
          the failing bit.  The memory test takes approximately 35
          seconds per 64K bank, longer depending upon other system
          activity.


          +--------------------------+
          |   ** ERROR DETECTED **   |
          | Bank    Bit     Address  |
          |  00  P76543210 0000:0000 |
          | Continue testing? _      |
          +--------------------------+

             In the event that an error is detected during the memory
          test, the above window will be displayed.  This window
          indicates the failing 64K bank, exact address, and bit(s).
          Depending upon the display type and video mode active at the
          time of the failure, the failing bit(s) will be indicated
          either by blinking, or non-display.  These bit(s) directly
          correspond to the failing chip(s) in the indicated 64K bank.
          In the event that the failing bit cannot be isolated, all
          bits in the failing address will be indicated.

             Pressing 'Y' (or ENTER) will continue the memory test
          starting with the next byte.  The number of successful
          passes will be reset to zero. Pressing 'N' will exit the
          memory test and display the termination options.



                                     Page 3





                                NMI  Version 1.03
                                  by Dennis Lee


          +--------------------------+
          | 1) Continue with parity  |
          | 2) Continue w/o  parity  |
          | 3) Reboot system         |
          | Enter selection: _       |
          +--------------------------+

             The termination option window is displayed as a result of
          any key other than 'Esc' being pressed during the memory
          test, or electing not to continue testing following an error
          detection.  Selecting option 1 will return to the
          interrupted process with parity checking enabled. Selecting
          option 2 will resume the interrupted process without parity
          checking.  Option 3 will reboot the system.  Pressing ENTER
          will restart the memory test.


          RETURN CODES
          ------------

             If NMI is invoked from within a batch file, or by another
          process, a return code may be retrieved indicating any
          errors.  For batch files, the return code may be
          interrogated using the 'IF ERRORLEVEL' batch subcommand.
          The following table indicates possible return codes for the
          current release.

               0 - Successful, no errors detected.

               1 - Error detected in parameters, program aborted.

               2 - NMI was invoked with the 'I' parameter, but is
                   already installed.  Installation aborted.

               4 - Memory test already active, no memory test
                   performed.  This error can occur in multi-partition
                   systems if memory test is called while active in
                   another partition.

             It is possible for more than one error to be returned in
          the return code.  For example, a return code of 6 indicates
          both errors 2 and 4 occurred.














                                     Page 4





                                NMI  Version 1.03
                                  by Dennis Lee


          PROGRAM DESIGN CONSIDERATIONS
          -----------------------------

             Certain performance and function trade-offs are made in
          the design of every program.  These trade-offs are usually
          made in an attempt to provide the most function within the
          constraints imposed by the operating environment in which
          the program must run.  In this case, the following criteria
          were taken into consideration.

          1) All resident programs must use the smallest possible
             amount of memory.

          2) During the memory test, it is assumed that a memory
             failure has occurred.  It is possible that the memory
             failure occurred in the resident portion of DOS.  For
             this reason, DOS function calls must not be used within
             the resident NMI code.

               No attempt is made to save and restore the contents of
               graphics screens.  This would have required additional
               code and buffer space within the resident portion of
               the program.  If a disk file had been used to save the
               video buffer, DOS function calls would have been
               required, increasing the possibility of program check
               during the memory test.

          3) The memory test should first attempt to find the failure
             using a read operation, so that the original failure
             remains undisturbed.  If the read operation fails to
             produce the error, only then should write operations be
             used.  Furthermore, the failure should be located in a
             single pass through memory, if possible.  This method
             will provide the best odds of locating an intermittent
             failure.





















                                     Page 5