TABLE OF CONTENTS

dopus5.library/AppXXX_routines
dopus5.library/AllocAppMessage
dopus5.library/AppWindowData
dopus5.library/ChangeAppIcon
dopus5.library/CheckAppMessage
dopus5.library/FindAppWindow
dopus5.library/FreeAppMessage
dopus5.library/GetWBArgPath
dopus5.library/ReplyAppMessage
dopus5.library/SetAppIconMenuState
dopus5.library/SetWBArg

dopus5.library/AppXXX_routines                 dopus5.library/AppXXX_routines

    PURPOSE

    The dopus5.library installs patches into the system when it loads to
    intercept calls to the workbench.library AddAppXXX() functions. This
    allows DOpus to show AppIcons, AppMenuItems, and support drag and drop
    onto AppWindows.

    The emulation is transparent as far as a third-party application is
    concerned, but it is possible to access additional features that DOpus
    provides (especially for AppIcons). Obviously these are only available
    through DOpus, and not through Workbench.

    Using tags with the AddAppIcon() function, it is possible to control
    the DOpus-only features of AppIcons. Workbench ignores these tags, and
    so if Workbench is running as well it will just see the plain AppIcon
    itself.

    The tags are as follows :

        DAE_Local

        This tag causes the icon to only be added to DOpus. If Workbench is
        running as well, it will not see this icon. Supplying this tag
        is probably a good idea if your AppIcon depends on some of the other
        DOpus-specific functions.

        DAE_Snapshot

        Indicates that this icon can support the Snapshot function. If this
        tag is specified, the Snapshot item in the icon popup menu will be
        enabled, and the Snapshot item in the main Icon menu will work.
        Use of this tag generates AppSnapshotMsgs, see below for more
        information.

        DAE_Close

        Turns the 'Open' item in the icon popup menu into a 'Close' item.
        APPSNAPF_CLOSE will be set in the AppSnapshotMsg that is
        generated.

        DAE_Info

        Indicates that this icon can support the Information function.
        This is similar in operation to the DAE_Snapshot tag. The
        APPSNAPF_INFO flag will be set in the AppSnapshotMsg.

        DAE_Menu

        This tag can be used several times for one icon. It allows you to
        specify additional entries for the icon popup menu. ti_Data points
        to a string that is displayed for the menu item. The order these
        tags are supplied specifies the order they are displayed, and
        also controls the ID that is returned in AppSnapshotMsgs.

        DAE_ToggleMenu

        Similar to DAE_Menu, this allows you to specify a menu item for
        the icon popup menu. The only difference is that the menu item
        is a toggle-select item (analagous to CHECKIT for Intuition menus).

        DAE_ToggleMenuSel

        The same as DAE_ToggleMenu, but specifies that the item is to be
        selected by default (analagous to CHECKED for Intuition menus).

        DAE_MenuBase

        This tag allows you to specify a base ID for menu IDs that
        are generated via the DAE_Menu, DAE_ToggleMenu and DAE_ToggleMenuSel
        tags. Menu IDs usually start at 0 for the first menu and increase
        from there. If you specify the DAE_MenuBase tag, the menu IDs will
        start from your supplied value.

        DAE_Background

        This allows you to specify a pen to use to render the background
        colour of the icon. If not supplied, the default is pen 0.

        DAE_Locked

        This tag specifies that the icon position is to be locked.
        That is, the user will be unable to reposition the icon from the
        initial coordinates. This flag can be changed later using the
        ChangeAppIcon() function.


    Using the new tags can cause special messages to be sent to your
    message port. These are an extension of the normal AppMessages,
    and can be identified by an am_Type of MTYPE_APPSNAPSHOT.

    The events you will get special messages for are :

        Snapshot

        If the DAE_Snapshot tag was specified and the user snapshots your
        icon, you will receive a message containing the icon position
        (AppSnapshotMsg->position_x and AppSnapshotMsg->position_y).
        It is your responsibility to save these values, and use them
        when adding the AppIcon in the future.

        If the APPSNAPF_WINDOW_POS flag is set in the AppSnapshotMsg->flags
        field, the position in AppSnapshotMsg->window_pos is also valid.

        Un-Snapshot

        If the DAE_Snapshot tag was specified and the user unsnapshots
        your icon, you will receive a message with the APPSNAPF_UNSNAPSHOT
        flag set.

        Close

        If DAE_Close was specified, and the user selects the Close item
        in the icon popup menu, you will receive a message with the
        APPSNAPF_CLOSE flag set.

        Information

        You will receive a message with the APPSNAPF_INFO flag set if you
        specified the DAE_Info tag, and the user selects Information on your
        icon.

        Menu

        If menus were added with the DAE_Menu tags, you will receive a
        message with the APPSNAPF_MENU flag set when the user selects one
        of your menu items. The AppSnapshotMsg->id field contains the
        item ID. If the user pressed the help key on one of the items,
        the APPSNAPF_HELP flag will also be set.

    Directory Opus also sends additional information to AppWindows. If you
    receive an AppMessage of type MTYPE_APPWINDOW, you should check to see
    if it is an Opus message using the CheckAppMessage() function. If so,
    the message is a DOpusAppMessage, which contains additional information.
    The extra fields are :

        da_DropPos

        This field contains an array of Point structures. Each structure
        gives the offset from the origin of each file in the message.
        This allows you to maintain the relative positions of all icons
        dropped in a multiple-file operation.

        da_DragOffset

        This Point structure gives you the offset of the primary icon
        from the mouse pointer. That is, if the user clicked on the primary
        icon in the top-left corner, this offset would be 0,0. If they
        picked up the icon from the bottom-right corner, it might be 32,18.

        da_Flags

        The only flag supported so far is DAPPF_ICON_DROP. This indicates
        that the files dropped were in fact icons (ie from an icon mode
        lister).

    The da_DropPos and da_DragOffset fields enable you to calculate the
    exact position that the user dropped the files on. Normal AppMessages
    only provide the position of the mouse pointer, which is useless if you
    want to maintain the relative and correct positions of the icons.


dopus5.library/AllocAppMessage                 dopus5.library/AllocAppMessage

    NAME
        AllocAppMessage - allocate a DOpusAppMessage

    SYNOPSIS
        AllocAppMessage(memory, port, count)
                          A0     A1     D0

        DOpusAppMessage *AllocAppMessage(APTR, struct MsgPort *, short);

    FUNCTION
        This function allows you to create a DOpusAppMessage (an extended
        AppMessage) easily.

    INPUTS
        memory - memory handle or NULL (see memory.doc)
        port - address of reply port
        count - number of arguments

    RESULT
        Allocates a DOpusAppMessage, including space for count arguments
        (both da_Msg.am_ArgList and da_DropPos will be initialised).

    NOTES
        Unless you actually want to send an AppMessage to a DOpus window
        with relative icon positions, you don't really need this function.
        It does provide a convenient way to allocate an AppMessage, though,
        and there's no reason you can't use DOpusAppMessages totally in
        place of AppMessages if you want to.

    SEE ALSO
        FreeAppMessage(), SetWBArg()


dopus5.library/AppWindowData                     dopus5.library/AppWindowData

    NAME
        AppWindowData - extract data from an AppWindow

    SYNOPSIS
        AppWindowData(appwindow, idptr, userdataptr)
                         A0        A1       A2

        struct MsgPort *AppWindowData(APTR, ULONG *, ULONG *);

    FUNCTION
        This function returns the ID, Userdata and Message port associated
        with the specified AppWindow. These are the parameters that are
        supplied in the call to AddAppWindow.

    INPUTS
        appwindow - AppWindow handle
        idptr - pointer to ULONG to contain the ID
        userdataptr - pointer to ULONG to contain the Userdata

    RESULT
        The AppWindow ID and Userdata are stored in the variables supplied,
        and the address of the AppWindow's message port is returned.

    SEE ALSO
        FindAppWindow(), workbench.library/AddAppWindow()


dopus5.library/ChangeAppIcon                     dopus5.library/ChangeAppIcon

    NAME
        ChangeAppIcon - make changes to an AppIcon

    SYNOPSIS
        ChangeAppIcon(icon, render, select, label, flags)
                       A0     A1      A2      A3     D0

        void ChangeAppIcon
             (APTR, struct Image *, struct Image *, char *,
              ULONG);

    FUNCTION
        This function allows you to make changes to an AppIcon that
        was previously added to DOpus. It has no effect on the icon
        on Workbench, so you should use the DAE_Local tag when adding
        the icon if your program depends on this function.

        You are able to change both frames of the icon's image and the
        icon's label. You can also lock or unlock the icon's position,
        and make it busy.

    INPUTS
        icon - icon to act on, as returned by AddAppIcon()
        render - new main image for the icon
        select - new select image for the icon
        label - new label for the icon
        flags - control flags. The available flags are :

                CAIF_RENDER     - change the main image
                CAIF_SELECT     - change the select image
                CAIF_TITLE      - change the label
                CAIF_LOCKED     - change the 'locked' flag
                CAIF_SET        - use with CAIF_LOCKED
                CAIF_BUSY       - make icon busy
                CAIF_UNBUSY     - make icon unbusy

    NOTES
        To lock an icon, pass CAIF_LOCKED|CAIF_SET. To unlock it, pass
        CAIF_LOCKED by itself. The render, select and label parameters are
        ignored unless their corresponding flags are set. You can specify
        any combination of these flags at once. To reduce the visible
        effects, you should make as many changes with the one call as
        possible.

    SEE ALSO
        SetAppIconMenuState(), workbench.library/AddAppIcon


dopus5.library/CheckAppMessage                 dopus5.library/CheckAppMessage

    NAME
        CheckAppMessage - check if an AppMessage is from DOpus

    SYNOPSIS
        CheckAppMessage(msg)
                         A0

        BOOL CheckAppMessage(DOpusAppMessage *);

    FUNCTION
        This function allows you to discover whether an AppMessage is
        actually an extended DOpusAppMessage.

    INPUTS
        msg - AppMessage to test

    RESULT
        Returns TRUE if the message is a DOpusAppMessage.

    NOTES
        You MUST only pass AppMessages (or DOpusAppMessages) to this
        function. Passing other types of messages (eg IntuiMessages)
        results in undefined behaviour.

    SEE ALSO
        AllocAppMessage()


dopus5.library/FindAppWindow                     dopus5.library/FindAppWindow

    NAME
        FindAppWindow - test to see if a window is an AppWindow

    SYNOPSIS
        FindAppWindow(window)
                        A0

        APTR FindAppWindow(struct Window *);

    FUNCTION
        This routine allows you to discover whether a Window is in fact
        an AppWindow.

    INPUTS
        window - pointer to the window to test

    RESULT
        Returns the AppWindow handle if it is an AppWindow, or NULL if not.

    NOTES
        You should only use the returned value within a Forbid()/Permit(),
        as the window in question could disappear at any time. Also note that
        the system patches are not installed until the dopus5.library is
        loaded. Any AppWindows added to the system before the patches are
    	installed are undetectable.

    SEE ALSO
        AppWindowData(), workbench.library/AddAppWindow()


dopus5.library/FreeAppMessage                   dopus5.library/FreeAppMessage

    NAME
        FreeAppMessage - frees a DOpusAppMessage

    SYNOPSIS
        FreeAppMessage(msg)
                        A0

        void FreeAppMessage(DOpusAppMessage *);

    FUNCTION
        This function frees the supplied DOpusAppMessage. It is only
        designed for messages allocated with AllocAppMessage.

    INPUTS
        msg - message to free

    NOTES
        You should not use this routine for AppMessages you receive
        (ie are sent by another process). You should ReplyMsg() those
        messages as normal. This function is used to free DOpusAppMessages
        that YOU create, usually when they are replied to by another
        task.

    SEE ALSO
        AllocAppMessage()


dopus5.library/GetWBArgPath                       dopus5.library/GetWBArgPath

    NAME
        GetWBArgPath - extract pathname from WBArg

    SYNOPSIS
        GetWBArgPath(wbarg, buffer, size)
                      A0      A1     D0

        BOOL GetWBArgPath(struct WBArg *, char *, long);

    FUNCTION
        This function is provided as a convenient method of extracting
        the pathname of a file/directory from a WBArg structure (usually
        within an AppMessage).

    INPUTS
        wbarg - pointer to the WBArg structure
        buffer - buffer to write pathname to
        size - size of buffer

    RESULT
        The full path and name of the object referred to by the WBArg
        structure is copied to the supplied buffer. This routine returns
        TRUE if it was successful.


dopus5.library/ReplyAppMessage                 dopus5.library/ReplyAppMessage

    NAME
        ReplyAppMessage - reply to an AppMessage

    SYNOPSIS
        ReplyAppMessage(msg)
                         A0

        void ReplyAppMessage(DOpusAppMessage *);

    FUNCTION
        This function is the best way to reply to a DOpusAppMessage. Its
        operation is quite straightforward - if the message has a reply
        port set, it calls ReplyMsg() as normal. Otherwise, it calls
        FreeAppMessage. This allows messages to be sent with no reply
        needed. Directory Opus will never send an AppMessage without a
        reply port, but you might want to use this routine among your
        own processes.

    INPUTS
        msg - message to reply to

    RESULT
        The message is replied or freed.

    SEE ALSO
        FreeAppMessage()


dopus5.library/SetAppIconMenuState         dopus5.library/SetAppIconMenuState

    NAME
        SetAppIconMenuState - change the state of an icon popup menu

    SYNOPSIS
        SetAppIconMenuState(icon, item, state)
                             A0    D0     D1

        long SetAppIconMenuState(APTR, long, long);

    FUNCTION
        This allows you to set the state of a toggle-select menu item in
        the icon popup menu of AppIcons. These menu items would have been
        added with the DAE_ToggleMenu and DAE_ToggleMenuSel tags.

    INPUTS
        icon - icon to act on, as returned by AddAppIcon()
        item - number of item to change (in the order they were added)
        state - new state for the item (TRUE=selected)

    RESULT
        Returns the old selection state of the item.

    NOTES
        This routine uses 0 as a base ID for the menu items, even if you
        specified a new base with DAE_MenuBase.

    SEE ALSO
        ChangeAppIcon(), workbench.library/AddAppIcon


dopus5.library/SetWBArg                               dopus5.library/SetWBArg

    NAME
        SetWBArg - fill out a WBArg entry in a DOpusAppMessage

    SYNOPSIS
        SetWBArg(msg, item, lock, name, memory)
                  A0   D0    D1    A1     A2

        BOOL SetWBArg(DOpusAppMessage *, short, BPTR, char *, APTR);

    FUNCTION
        This routine makes it easy to initialise the WBArg structures
        in an AppMessage (or a DOpusAppMessage).

    INPUTS
        msg - AppMessage to initialise
        item - item to initialise (starting at 0)
        lock - lock on parent directory
        name - name of file
        memory - memory handle or NULL

    RESULT
        The specified WBArg in the AppMessage is initialised with the
        lock and name specified. This routine returns TRUE if it was
        successful.

    NOTES
        'lock' is the lock of the item's parent directory in the case of
        files, or on the item itself in the case of directories. For files,
        'name' is the name of the file. 'name' is null for directories.
        The lock and name you supply are both copied, so they do not need
        to remain valid once this call is complete.