IBM 8230 Token Ring Network CAU Maintanence Facility V2 Release 3
-----------------------------------------------------------------
This package is made up of the following files:
8230V2R3 DOC01AK4 - This document
8230V2R3 DSK01AK4 - LOADDF Fix diskette

The file once downloaded with the binary option, needs to be
unpacked using LOADDF onto a 3.5" 1.44MB diskette.



The contents of USERGUID.DOC have been included below:
8230 TOKEN-RING NETWORK CONTROLLED ACCESS UNIT MAINTENANCE
                  FACILITY USER'S GUIDE

SUMMARY OF CHANGES

Changes have been made to the microcode of the Maintenance Facility.
Please read the SUMMARY.CHG file on this disk for a complete history
of the changes.

There were no changes to the Maintenance Facility User's Guide.

TRADEMARKS

The following terms, denoted by an asterisk (*) in this publication,
are trademarks of IBM Corporation in the United States or other
countries or both:

    IBM

    PS/2

    PS/55


SIXTH EDITION (AUGUST 1993)

This edition applies to the RELEASE of this product.

Order publications through your IBM representative or the IBM branch
office serving your locality.

(C) COPYRIGHT INTERNATIONAL BUSINESS MACHINES CORPORATION 1991, 1993.
ALL RIGHTS RESERVED.



OVERVIEW
________

The IBM 8230 Controlled Access Unit Maintenance Facility (Maintenance
Facility) shows the status for up to 16 active IBM 8230 Token-Ring
Network Controlled Access Units (IBM 8230s).  Using the Maintenance
Facility, you can:

o   Enable and disable lobes

o   Obtain the status of a Lobe Attachment Module (LAM) attached to an
    8230

o   Change the status of a lobe on a LAM attached to an 8230

o   Load microcode into an 8230

o   Change the wrap state of an 8230.


PACKAGE CONTENTS

This electronic release of the Maintenance Facility contains one 3.5-inch
diskette image.  You may copy the 3.5-inch diskette to a 5.25-inch
1.2-MB diskette or to 5.25-inch 360-KB diskettes; see "Converting the
Diskette" below.


WHAT YOU NEED

To use the Maintenance Facility, you need the hardware described here:

o   Any ONE of these personal computers:
    -   IBM* PS/2* computer with one 3.5-inch diskette
    -   IBM PS/55* computer with one 3.5-inch diskette drive
    -   IBM Personal Computer with at least 640 KB of memory and one
        3.5-inch or 5.25-inch diskette drive (or an equivalent
        machine).
o   An IBM Token-Ring Network Adapter (either 4 or 16 Mbps, depending
    on your network) installed as the primary adapter (adapter 0) for
    your personal computer.


LOADING THE MAINTENANCE FACILITY
________________________________


You must load the Maintenance Facility into a workstation that is
physically attached to the same ring segment as the IBM 8230.  Remember
that only on one network management program (such as the Maintenance
Facility or the IBM LAN Network Manager) can control the ring segment
at any given time.

1.  Insert the Maintenance Facility diskette into your computer's
    diskette drive.
2.  Turn the computer on, or reboot it by pressing CTRL-ALT-DELETE.  The
    DIAGNOSTIC CONTROL PROGRAM will be displayed.
3.  Press 0 to choose OPTION - Run Maintenance Facility.
4.  Press ENTER.
5.  The logo panel will be displayed.
6.  Press ENTER to begin.


HOW TO USE THE MAINTENANCE FACILITY
___________________________________

Once the Maintenance Facility has been loaded and started, it issues
commands that obtain the status for up to 16 active IBM 8239s.  The
logical address for each 8230 is displayed on the main screen, along
with any error codes.  The wrap status for each 8230 is also given.
To view details of any 8230 address that is displayed, use the up and
down arrow keys to move the cursor to the desired address and press
Enter.  Details of the selected 8230 will be displayed.

You may obtain further information by moving the up and down arrow keys
to select an 8230 LAM and pressing Enter.

Where shown, press F9 to update the screen.  The Maintenance Facility
captures and displays a "snapshot" of the status.


USING THE HELP

EXITING THE MAINTENANCE FACILITY

To exit the Maintenance Facility at any time, follow these steps:

1.  Press ESC until the MAIN LIST PANEL is displayed.
2.  Press F3.  The DIAGNOSTIC CONTROL PROGRAM menu will be displayed.
3.  Type 9 to choose OPTION 9 - EXIT DIAGNOSTIC CONTROL PROGRAM and
    press ENTER.


CONVERTING THE DISKETTE
_______________________

If you have 3.5-inch and 5.25-inch diskette drives or if you can copy
files over your network, you can copy to a 5.25-inch diskette.

To copy to one 5.25-inch 1.2-MB diskette:

1.  Format the (target) diskette.  Be sure to use the /S option.
2.  Copy all files onto the diskette.

To copy to 5.25-inch 360-KB diskettes:

1.  Make the 3.5-inch disk drive the default drive.
2.  Enter

      make525

    at the command prompt.

This will start a batch file on the Maintenance Facility disk, which
will provide the number and format of the disks needed; the batch file
will also perform the copy operations required for placing the correct
files on the diskettes.