IBM PS2 SCSI Netware Adapter Support Diskette    (PS2SCSIA.EXE)
PS2SCSIA.DSK v1.02 for Netware v3.1x and v4.0x
---------------------------------------------------------------

This package is made up of the following files:

PS2SCSIA DOC10GH4 - Document
PS2SCSIA EXE10GH4 - Binary self-extracting file

The file, once downloaded with the binary option, needs to be
run as it is a self-extracting file.

---------------------------------------------------------------

      *******************************************************
          IBM PS2 SCSI Netware Adapter Support Diskette
      *******************************************************

   This README file contains instructions for installing the
   IBM* PS2 SCSI adapter device drivers for Novell** Netware**
   Versions 3.1X and 4.0 or later. It is recommended that you
   print this README file prior to installing the files.

   The NetWare drivers and NLM's provide an ASPI interface
   which has been tested with the following vendor tape backup
   software. A phone number for further information on each
   vendor product is provided.

   Palindrome Corporation**  Network Archivist** (708-505-3300)
   Cheyenne Software, Inc.** ARCserve**          (516-484-5110)

    This version of the driver has not been certified by
    Novell, Inc.
    The changes made to this version from the last version
    (1.01) are to fix a potential data integrity problem when
    using the ASPI interface to backup data.  We suggest all
    users upgrade to this new version of the driver as soon as
    possible.

    This driver also provides the necessary interfaces for
    NetFinity to get management information from the SCSI
    subsystem.  The NetWare version of NetFinity is not yet
    available but is planned for the near future.

  This PS2SCSIA.EXE file contains the following files.  Extract
  the files by typing PS2SCSIA -d at the command line.

  1. README.TXT   - This file, explains the use of other files
                    and patches.

  2. PS2SCSIA.DSK - IBM PS2 SCSI disk device driver for Novell
                    3.xx or 4.xx
                    The PS2SCSIA.DSK replaces a customers
                    PS2OPT.DSK or PS2SCSI.DSK wishing to use
                    ASPI. This module is loaded first.

  3. IBMASPI.NLM  - IBM/PALINDROME ASPI manager for Novell 3.xx
                    or 4.xx which exports ASPI_Entry point.
                    This module in turn sends ASPI passthru
                    IOCTL's to the PS2SCSIA.DSK. This
                    module is loaded after PS2SCSIA.DSK.

  4. IBMENTRY.NLM - IBM/PALINDROME ASPI manager for Novell 3.xx
                    or 4.xx (optional) which exports IBM_Entry
                    point. The IBMENTRY.NLM file is provided
                    for systems which already have another SCSI
                    vendor card configured and use the exported
                    ASPI_Entry point.  The export name of
                    "IBM_Entry" is provided to ASPI vendors for
                    an alternate entry point in this  tuation.
                    This allows a customer to use both an IBM
                    adapter as well as another vendor adapter
                    in the same system as Novell only allows
                    the 'export' of one ASPI_Entry point.

  5. ASPI50.NLM   - If you plan to run Cheyenne ARCserve
                    running DOS Version (optional) 4.0 or
                    Windows Version 5.0 or earlier you must
                    install this new version of ASPI50.NLM with
                    your ARCserve software.

  6. SCSISCAN.NLM - Palindrome NLM which will scan the scsi
                    bus. This module is (optional) provided to
                    aid in verifying that the customer has
                    successfully installed the PS2SCSIA.DSK,
                    IBMASPI.NLM, IBM SCSI adapter and devices.
                    Successful execution of this NLM will
                    result in a screen display showing all
                    attached SCSI devices and id's. It is
                    recommended that this NLM be run prior to
                    installing tape backup software.

  7. D854.TXT and   The Novell certification bulletins for this
     D855.TXT       device driver.
                    (Version 1.01 was certified, version 1.02
                    is not yet.)


  In addition the following Novell Operating system patches are
  required for when running 3.12.  These files are in the NW312
  directory, and are in a self-extracting zip file These files
  can be found in PATCH312.ZIP:

     Name            Description
     ------          -----------
  1. DAICCFIX.NLM    1076 bytes 02-07-94
  2. PM312.NLM       9586 bytes 08-31-93
  3. REALMFIX.NLM    3207 bytes 02-07-94


  In addition the following Novell Operating system patches are
  required for when running 4.XX.  These files are in the NW4XX
  directory, and are in a self-extracting zip file These files
  can be found in PATCH4XX.ZIP:


     Name            Description
     ------          -----------
  1. DAICCFIX.NLM    1031 bytes 02-07-94
  2. PM401.NLM       8113 bytes 08-26-93
  3. REALMFIX.NLM    2756 bytes 02-07-94


_______________________________________________________________

  Installing Device Drivers for Novell NetWare Versions 3.1X or
  4.X
---------------------------------------------------------------

       Use the instructions in this section if you have Novell
       NetWare Version 3.1X or 4.X installed.


  NOTE: Tape drives which do not support 4K block sizes will
        result in a warning message that they must use ASPI
        tape backup software.


       1. Turn on the display and system unit.

       2. Prepare the NetWare startup drive according to the
          instructions
          in the NetWare manual.

       3. Insert the IBM PS2 SCSI Adapter Device Drivers
          Diskette which contains the PS2SCSIA.DSK driver and
          other files required for Netware support into the
          diskette drive.

       4. Type the following:

                 copy a:\PS2SCSIA.DSK d:

          (where d: is the NetWare startup drive) and press
          Enter.

          The PS2SCSIA.DSK driver is the base device driver for
          the IBM PS2 SCSI PCI Bus Adapter which supports hard
          disks, IBM CD-ROM drives, IBM tape drives, and IBM
          Rewritable Optical Disk drives.  Additional Netware
          Loadable Modules (NLMs) described below are also
          provided to support Netware ASPI compliant device
          drivers required by SCSI device drivers and Netware
          compatible server backup software packages.

       5. Type the following:

                 copy a:\IBMASPI.NLM d:

          (where d: is the NetWare startup drive) and press
          Enter.

          The IBMASPI.NLM exports the "ASPI_Entry" entry point
          and sends IOCTL commands to the PS2SCSIA.DSK module.
          These two modules are usually all that is required
          for both disk and ASPI support.

       6. Type the following:

                 copy a:\SCSISCAN.NLM d:

          (where d: is the NetWare startup drive) and press
          Enter.

          Use of this module is optional and is provided to aid
          in verifying that the customer has successfully
          installed the PS2SCSIA.DSK, IBMASPI.NLM, IBM PS2 SCSI
          adapter and devices. Successful execution of this NLM
          will result in a screen display showing all attached
          SCSI devices and their ID's. It is recommended that
          this NLM be run prior to installing tape backup
          software.

       7. Type the following:

                 copy a:\IBMENTRY.NLM d:

          (where d: is the NetWare startup drive) and press
          Enter.

          Use of the IBMENTRY.NLM file is optional and is
          provided for systems which already have another
          vendor's SCSI adapter configured to use the exported
          "ASPI_Entry" entry point. The export name of
          "IBM_Entry" is provided to ASPI device drivers as
          an alternate entry point in this situation.

       8a. If you are using Netware version 3.12, the following
           system patches also must be copied.

          Type the following:

                 copy a:\NW312\DAICCFIX.NLM d:

          (where d: is the NetWare startup drive) and press
          Enter.

          Type the following:

                 copy a:\NW312\REALMFIX.NLM d:

          (where d: is the NetWare startup drive) and press
          Enter.

          Type the following:

                 copy a:\NW312\PM312.NLM d:

          (where d: is the NetWare startup drive) and press
           Enter.

       8b. If you are using Netware version 4.xx, the following
           system patches also must be copied.

          Type the following:

                 copy a:\NW4XX\DAICCFIX.NLM d:

          (where d: is the NetWare startup drive) and press
          Enter.

          Type the following:

                 copy a:\NW4XX\REALMFIX.NLM d:

          (where d: is the NetWare startup drive) and press
          Enter.

          Type the following:

                 copy a:\NW4XX\PM401.NLM d:

          (where d: is the NetWare startup drive) and press
          Enter.

       9. If you are using Cheyenne ARCserve server backup
          software for DOS Version 4.0 or for Windows Version
          5.0 or earlier, you must also install the following
          new version of ASPI50.NLM.

          Type the following:

                 copy a:\ASPI50.NLM d:

          (where d: is the NetWare startup drive) and press
          Enter.

      10. To start the NetWare operating system, type the
          following at the command prompt:

                 SERVER

          and press Enter.

      11. At this time, make sure all activity on the server
          has stopped.
          Then load the DAICCFIX.NLM and REALMFIX.NLM NetWare
          patch files in that order if they were copied in step
          8a or 8b above and you are using Netware version 3.12
          or 4.xx.

          NOTE: The PM312.NLM or PM401.NLM patch files will be
                loaded automatically.

      12. At the NetWare server console prompt, type the
          following:

                 LOAD d:PS2SCSIA

          (where d: is the NetWare startup drive) and press
          Enter.

           This loads the basic device driver required for
           Netware support.  The appropriate NLMs that you
           chose to copy above should also be loaded at this
           time depending on your version of Netware and other
           installed equipment/software.

   In summary a customer should first load PS2SCSIA.DSK then
   IBMASPI.NLM.  Finally it is recommended that a customer load
   SCSISCAN.NLM which will do an SCSI scan of the bus using the
   ASPI interface to verify that the SCSI adapter, SCSI
   devices, NLM and DSK are loaded and operating properly. Any
   problems up to this point should be directed to IBM
   customer support.

   NOTE: Before creating or deleting NetWare disk partitions
         with the NetWare INSTALL.NLM utility while running
         NetWare 3.12 or 4.xx, the IBMASPI.NLM and/or
         IBMENTRY.NLM must be unloaded.

      __________
      TRADEMARKS
      ----------

      The following terms, denoted by an asterisk (*)
      in this file, are trademarks of the IBM Corporation
      in the United States or other countries:

      The following terms, denoted by a double asterisk (**)
      in this file, are trademarks of other companies as
      follows:

      Novell                        Novell, Inc.
      NetWare                       Novell, Inc.
      Cheyenne                      Cheyenne Software, Inc.
      ARCserve                      Cheyenne Software, Inc.
      Palindrome                    Palindrome Corp.
      Network Archivist             Palindrome Corp.

      IBM DISCLAIMS ALL WARRANTIES, WHETHER EXPRESSED OR
      IMPLIED, INCLUDING WITHOUT LIMITATION, WARRANTIES OF
      FITNESS AND MERCHANTABILITY WITH RESPECT TO THE
      INFORMATION IN THIS DOCUMENT.  BY FURNISHING THIS README,
      IBM GRANTS NO LICENSES TO ANY RELATED PATENTS OR
      COPYRIGHTS.

      Copyright IBM Corporation - 1994 all rights reserved.


---------------------------------------------------------------