NetWare 1.3B Maintenance                           (SAA013.EXE)
---------------------------------------------------------------
This package is made up of the following files:

SAA013 DOC29PK4 - This document
SAA013 EXE29PK4 - Binary self-extracting file.

---------------------------------------------------------------
NOVELL PRODUCT and VERSION:
NetWare for SAA 1.3B

ABSTRACT:

SAA013.EXE & SAA008.EXE, together, are the current maintenance
patch for SAA 1.3B and must be used together.  The patch is
recommended for all SAA 1.3B installations and for all SAA 1.3
installations that have installed the PTF 410 series.  Do Not
Apply to COMMEXEC and NWSAA versions below 1.3.42]  Check
Product Options Under "Load Install" First]  NOTE: SAA008 HAS
NOT changed. Please apply SAA013 and SAA008 before calling Tech
Support.
---------------------------------------------------------------
DISCLAIMER
THE ORIGIN OF THIS INFORMATION MAY BE INTERNAL OR EXTERNAL TO
NOVELL.  NOVELL MAKES EVERY EFFORT WITHIN ITS MEANS TO VERIFY
THIS INFORMATION.  HOWEVER, THE INFORMATION PROVIDED IN THIS
DOCUMENT IS FOR YOUR INFORMATION ONLY.  NOVELL MAKES NO
EXPLICIT OR IMPLIED CLAIMS TO THE VALIDITY OF THIS INFORMATION.

---------------------------------------------------------------

SYMPTOM

General Symptoms
1. Not compatible with NetSoft and DCA emulators.
2. Unexpected disconnects.
3. Failure to attach with Password Encryption turned on.
4. Multiple line RUNCMD responses limited to 110 characters.
5. Problems gathering statistics through SSM.
6. Problems using the verb CNOS.
7. If user terminated a session when running the DCA emulator
using mod 5, subsequent users would get 4B? on the OIA line
when trying to get a new session.
8. Definite response with pacing on, caused sense code 200A.
9. Test frames being sent causing the link to reset.
10. 3174 X.25 RPQ failure to connect with NWSAA.
11. Several different state transition errors; event=1 state=5
and event=7 state=7.
12. Several LU6.2 problems, including send error in recv state
problems.
13. Failure to respond to a Null XID when configured as a PU
type 2.1 over a SDLC link.


Symptoms Related to R3SDLC & SDLCS
1. Server hang in a multidrop environment, if another device
kept RTS high.

2. RTS toggled to Low even if CSCON was configured to set it
constantly High.

3. Spurious interrupt/missed poll messages.

4. Pressing Attention during a Logoff could result in a Profile
Unload.

5. Failure to re-establish connection with host.

6. Failure to respond to a DISC from NCP.

7. "DLCI ERROR:unable to attach to a logical board" when
loading both a PU2.0 and a PU2.1 profile to the same board.

8. Failure of link to come up.

Symptoms WITH SNALINKS
1. Even when SNALINKS was configured for Auto Connect, after a
link was downed, the connection might not be brought up
automatically.
2. Incompatibility with MPR 3.0.

Symptoms with SAACOPY
1. "Unable to open file"
2. Downstream LUs unable to establish host sessions.
3. Unable to copy between a 1.3 and a 1.4 Communication Server.
4. "No more WCM connection"
5. "Error on Attach"
6. After a profile was copied onto a NetWare 4.01 server, an
attempt to run CSCON from the same NetWare drive would cause
the workstation to hang.
7. The use of SAACOPY, then CSCON, could result in the DOS
prompt being changed to "%p".
8. SAACopy set the wrong model number.

Symptoms with AS/400
1. Unable to access Shared Folders.
2. Invalid XID messages on the console.

Symptoms Related to OS/2
1. Lack of OS/2 DOS Box support for CSCON.
2. Problems using OS/2 Connection Manager.

Symptom Using Netview
Server crash when NetView issues a REQMS.

Symptom using Data Link Switch/Custom link
Errors when session data spanned multiple data blocks.

Symptoms When Using MPA Boards
1. System crash when using MPA driver and PS/2 model 9585.
2. MPA driver not compatible with servers over 16 meg of RAM.

New Features

Compatibility added for the new "LINKSNA", due out in the near
future.  Added TCPIP support for the as400pcs.nlm for the
netsoft router.  (This was the same file that was in nsrout.exe
on compuserve.)  Compatibility added for the new data link
switch product.

SOLUTION
Apply SAA013 and SAA008

Self-Extracting File Name:  SAA013.EXE     Revision:  A

Files Included     Size     Date      Time

\
  SAA013.TXT         (This File)
     DLM.NLM     107523   11-15-94   10:21a  * 599, 613, 666
     SMA.NLM      28138   03-28-94    2:36p  * 582
     WCM.DLL      33309   03-08-94   10:48a  * 573
   CMTCP.NLM      39644   12-15-93    9:09a  * 553
   CSCFG.EXE     113445   04-18-94   10:07a  * 558
   CSCON.EXE      41183   04-18-94   10:05a  * 558
   NWSAA.001        855   11-17-94    8:46a  * 629,624,610,659
   NWSAA.NLM     367462   11-04-94    3:49p  * 637,650,652,629
                                               624,610,659
   NWSAA.RMV       1839   07-07-94    6:20p  * 629,624,610,637
                                               650,652
   ROUTE.NLM       5033   06-09-94    6:11p
   SDLCS.NLM      40905   04-19-94    3:01p  * 590,586,578
  CS_ERR.DAT       9451   02-26-90    6:52p  * 588
  CS_MSG.DAT      24812   12-14-89    4:52p
  R3SDLC.LAN      22551   04-29-94    9:18a  * 590,586,578
 CS_HELP.DAT       3722   09-01-89   12:00p
 LLC8022.NLM      34606   09-01-94   11:02a  * 638, 644
 MPASDLC.LAN      10809   08-04-94   11:37a  * 622,636
 PBTRACE.NLM       2735   04-19-94    3:00p  * 590
 PRODUCT.DEF        434   11-02-94    5:40p  * 659
 SAACOPY.EXE     262121   09-26-94    3:55p  * 541,646
 SPC_ERR.DAT       9451   02-26-90    6:52p  * 646
 SPC_FRM.FRM       1387   10-07-92   11:24a  * 646
 SPC_FRM.HLP      67975   10-11-93    5:15p  * 541,646
 SPC_MSG.DAT      24812   12-14-89    4:52p
 STRNRTR.EXE      41757   10-22-93    4:39p  * 541
AS400PCS.NLM      20838   03-31-94    4:00p  * 535
CPIC_SAA.NLM      32756   01-10-94    2:01p  * 560
CSCONFRM.HLP       4425   07-23-92    4:26p  * 588
CSINSTAL.HLP       2336   03-09-93    6:44p  * 629,624,610
CSINSTAL.NLM        802   06-10-93   11:28a  * 629,624,610
NOVELLRT.OVL       6678   10-22-93    4:39p  * 535
PB_NWSAA.NLM      28622   04-19-94    3:00p  * 590
PINSTALL.NLM      87963   06-10-93   11:29a
SPC_HELP.DAT       3722   09-01-89   12:00p  * 646


*Novell internal control number.
Note: ROUTE.NLM released in SROUTE.EXE (included here as a
convenience), see text about the use of this file]] Note:
AS400PCS.NLM netsoft router support

Installation Instructions:
1. Install this patch ONLY IF you have NetWare for SAA 1.3B or
have installed the PTF410 series.

2. Put SAA013.EXE into an empty directory, called SAA013, on a
hard disk or network drive.  Make sure the directory path is
available to the server(s) you are updating.

3. Unzip SAA013.EXE.
                  SAA013  <Enter>

4. Have you ever applied SAA008?  If you have, you are
currently at version 1.3.46.  If you are currently at version
1.3.46 skip to step #6.  Do NOT apply SAA008 a second time.

Put SAA008.EXE into an empty directory, called SAA008, on a
hard disk or network drive.  Make sure the directory path is
available to the server(s) you are updating.

5. Unzip SAA008.EXE.

  SAA008  <Enter>

6. Do a CSDOWN so that COMMEXEC will not be running.

7. LOAD Install.

8. Select Product Options.

9. Press <Insert>. You should select the directory path created
above ie, sys:\saa013 or c:\saa013

10. Select server to update.

11. Press <Enter>.

12. Wait for the update to complete.

13. Press <Esc>.  You should see NWSAA 1.3.60

14. If you have never applied SAA008, press <Insert>.select
directory path for SAA008 ie, sys:\SAA008 or c:\SAA008.

15. Select the server to update.

16. Press <Enter>

17. Wait for the update to complete.

18. Press <Esc>.  You should see COMMEXEC 1.3.46.

***]]]]]] IMPORTANT NOTE:

Never manually copy COMMEXEC.NLM or NWSAA.NLM into the system.
The install scripts must be used]  If you copy in manually, the
version information will be incorrect.  If you have ever
applied an ETF that required copying NWSAA.NLM into the system
directory manually, please recopy the NWSAA.NLM that was on the
system just prior to installing the ETF, and then be sure the
version number under Product Options for NWSAA is lower than
the one in this patch.  If an ETF was applied with an install
script, you do not have to recopy NWSAA.NLM (however, be sure
the version you have is lower than the one in this patch).  If
the version number is equal than or greater than the one to be
installed by this patch, the install will fail.

]]]]************

19. Reload COMMEXEC.

20. Reload the profile.

21. Copy the new STRNRTR.EXE and NOVELLRT.OVL over any copies
that may exist outside of the SYS:\SYSTEM\NWSAA\AS400
directories.

22. Read SAACOPY.TXT for instructions on the use of SAACOPY.
Please note that there was a patch to SAACOPY that created an
incorrect directory.  The INCORRECT PATH is
SYS:\SYSTEM\SAACOPY.  Please delete the contents and the
directory.  The CORRECT directory path is
SYS:\SYSTEM\NWSAA\SAACOPY.  SAA013 will install the files here.

23. The CONFIG.SYS for the workstation from which you run
SAACOPY must contain FILES=20 (or greater).  If it does not,
you will receive the following error message when you try to
back up or restore SAA service files:

  MESSAGE

  Unable to Open File

24. If you are using the MPA board: The new MPA driver uses
interrupt 3 and is non-shareable, run reference setup to make
sure no other device uses Interrupt 3]

25. If you are using the MPA board with OS/2: Load MPASDLC
Name=board mode=ns

26. In order to use 3174 X.25 RPQ you must use the ROUTE.NLM
provided with this patch and load it with the GBR option]
(specifies that all General Broadcast frames are to be sent as
All Routes Broadcast Frames.)  Please also note that the new
ROUTE.NLM must be manually copied to the system directory in
the event that the route you have installed is older than the
one provided here.

Patch History:

SAA013 supersedes SAA001, SAA003, SAA004, and SAA007.
SAA001 contained CSMPX.NLM dated 2/17/94, which randomized
CSLIST.  Such randomization is not desirable at many sites.

SAA001 and SAA002 superseded PTF 443, PTF 435 and PTF 438.
These files also replace the NetWire file SAACPY.EXE that
introduced the problem of restored downstream LUs being unable
to establish host sessions and PTF 431 that was the first PTF
for SAA 1.3B.

SAA008 superseded SAA002.


Solution Specifics: (for some of the symptoms listed above)

GENERAL

1. CMTCP.NLM modified to handle multiple QELs in a single
packet.  This was done for compatibility.

4. RUNCMD responses will now be limited to 220 characters.  If
in excess of 220 characters, will be truncated.  Single line
RUNCMD responses will be broken down into 220 character chunks.

6. When changing the number of sessions (CNOS) from X to Y,
must be at 0 first before the change can be made.

9. DLM.NLM and LLC8022.NLM modified so that test frames will be
turned around once the link is established.

12. Many fixes for LU6.2, including adding sense code for FMH-7
10086040,CNOS fixes, chaining and bracketing fixes,etc.

13. DLM.NLM modified.


SOLUTIONS RELATED to R3SDLC & SDLCS

5. R3SDLC and SDLCS were modified so that DTR is not toggled
when SAA receives a disconnect command in a leased line
configuration.

8. SDLCS.NLM modified so that the link will no longer fail to
come up when a DISC immediately follows a SNRM/UA.



SAACOPY

4. Connections will now clear.  They had not been, and as new
connections were made the maximum number would be reached.

8. Model numbers will now transfer correctly.



AS/400
1. Corrected by adding support for the "query conversation
state" service verb.


OS/2
2. WCM.DLL modified.


USING NETVIEW
DLM.NLM modified so that a server crash will no longer result
from a REQMS resulting in a DLM_GET_STATISTICS or
DLM_RESET_STATISTICS.

DATA LINK SWITCH/CUSTOM DATA LINK
Support provided for data spanning multiple data blocks,
instead of being required to remain in one data block.  This
also effects Custom data link configurations as well.

---------------------------------------------------------------
Any trademarks referenced in this document are the property of
their respective owners.  Consult your product manuals for
complete trademark information.
---------------------------------------------------------------