QUARTERDECK TECHNICAL NOTE
February 5, 1990

LANTASTIC NETWORK OPERATING SYSTEM
Artisoft
Artisoft Plaza
575 E. River Road
Tuscon, AZ  85704
(602) 293-6363

We have tested the starter package with DESQview versions 2.25 
and 2.26, The LAN starter kit consists of (2) 2mbps lan adapters 
and a system disk. 

Installation was rather easy, and the instructions in the manual 
are complete.  If you are installing this system on a 386 and are 
using QEMM 4.23, you must exclude the lan adapter rom address 
space.  These are documented in the Lan Adapter user manual on 
Pg. 6 (table 2).  Default is D800-DFFF.

     LANBIOS.EXE is the program that activates the network 
     adapter in your PC.  It uses 1K and can be loaded high.

     REDIR.EXE is the networking software.  Each PC has to run 
     this to be on the network.  It uses 11K and can be loaded 
     high. 

     SERVER.EXE is an additional program that enables the PC
     running it to be accessed as a file server rather than just 
     as a workstation.  It takes about 22K and in most cases can 
     also be loaded high.

Lantastic uses DOS SHARE.EXE to provide basic file protection and 
locking.  Non-network versions of software can be run by only one 
user at a time.  

We find that with DESQview 2.25, you may want to try using an 
undocumented parameter, /DT.  This tells DESQview to inform DOS
when DESQview closes files.  Generally, DESQview is able to run 
many programs without using DOS, and for the sake of speed we 
don't tell DOS when we close files.  Network software that 
requires running SHARE.EXE may need /DT to keep things straight.  
This may help if you are experiencing lock-ups running DESQview 
on a Lantastic server.

I have been able to run DESQview 2.26 from the workstation as 
well as from the server.  But as a rule, each workstation
should run DESQview locally or run it from a unique directory on 
the server.  

Since the servers in Lantastic are not dedicated, DESQview can
be run on a pc designated as a server.  If you do this, you must 
login to the server like the workstations do, to minimize
degradation of performance of the network as a whole. 

There are also two other programs, net and net_mgr, which can be
run on a dos command line or as a network menu program if no 
parameters are given to them.  This is the only part of Lantastic
that could be run in a DESQview window, but is not recommended as
it may cause lockups.

The network drivers (lanbios.exe, redir.exe and server.exe) MUST 
be run before invoking DESQview.

Also it has been noted that when running DESQview on the server and
using the Lantastic print spooler, DESQview's "Manage Printer
Contention" option should be set to [N].

        Copyright (C) 1990 by Quarterdeck Office Systems
             * * *   E N D   O F   F I L E    * * *