Quarterdeck Office System
Technical Note

Documnetaion for NOFF.SHR
by Stan Young

What is NOFF.SHR and why might I want to run it?

NOFF.SHR is a DESQview 2.X shared program that can be run with 
some DESQview/TopView Aware programs which will improve the 
performance of those programs (in DESQview, not in TopView).

To understand why this program might improve performance, it is 
important to understand how a program that wants to be TopView 
aware must write to the screen.  

Essentially, such a program first makes a call to see if TopView 
or DESQview is there.  It then makes a call (we call it the "FE" 
call) to find out the address in memory to write to.  The program 
then uses this address instead of writing to the hardware screen 
address.

At this point, TopView and versions of DESQview prior to 2.0 
diverge.  TopView requires that the program make another call 
(called the "FF" call) each time it wants to update the screen.  
Used efficiently, this call can produce very fast screen updating 
since it is possible to update only the portion of the screen 
that has changed.

DESQview prior to version 2.0 however ignores the "FF" call and 
takes on the task of determining when the screen must be updated 
itself.  This was done so that programs could be easily "DESQview 
aware" without going to the trouble to be TopView aware.  It is 
quite efficient, although perhaps not as efficient as properly 
using the "FF" call.

SO, WHY NOFF?  Well, starting with DESQview version 2.0, DESQview 
will detect the "FF" call, and if a program makes one, it will 
not ignore the call, but will update the screen using the 
"TopView" method.  By supporting the "FF" call, DESQview 2.0 can 
run some programs faster that previous versions of DESQview 
could.  An example are the DESQview Companions, all of which use 
the "FF" call to advantage.

However, it has come to our attention that some DESQview/TopView 
aware programs that use the "FF" call seem to use it rather 
inefficiently, constantly updating the entire screen instead of 
just the portion that changed.  Since DESQview 2.0 pays attention 
to the "FF" call and can't really make judgements as to whether 
the call is used efficiently, these programs run slower in 
DESQview 2.0 than in 1.XX.

                        LOADING NOFF.SHR
NOFF loads into your program window as a shared program (on the 
Change a Program Advanced Options menu).  Once loaded, it tells 
DESQview to ignore the "FF" call even if it receives one.  This 
makes the programs update the screen faster and could eliminate 
some screen abnormalities caused by improper implementation of 
the "FF" call.

The following is a list of some DESQview Aware programs that seem 
to benefit from NOFF.SHR and a few that work better without it.  

SEEM TO BENEFIT FROM NOFF.SHR:

     WordPerfect  }        MUST install NOFF if you want to 
                           run in 43 line EGA mode.

     Norton Commander
     Relay Gold and Silver
     Watson     

WORK BETTER WITHOUT NOFF.SHR:

     All of the DESQview Companions
     Crosstalk
     LIST
             * * *   E N D   O F   F I L E    * * *