SIM_R3.DOC
    I. Introduction
       A. Who wrote sim_r3 and why
       B. Disclaimer
    II. Using sim_r3.exe
       A. Items on the display
       B. Explanation of commands
    III. Recompiling sim_r3
       A. For the IBM-PC
          1. Using Microsoft C 5.0 or higher
          2. Using another compiler
       B. For non-IBM compatible machines

I. Introduction
I. A. Who wrote sim_r3 and why

     All files in this archive were written entirely by myself, 
     Joseph Schachner.  I can be contacted via Compuserve 
     (73637,3437).

/* I, Amir Bernstein, have made several improvements and fixed
   minor bugs, I can be contacted on FREEWARE BBS */


     sim_r3 was written to support a project where I work which  
     is planning to use a 68705R3.  Because the 68705 program and 
     data memory is compeletly internal, debugging a running 68705 
     is nearly impossible.  Of course, the 68705 can be emulated 
     by hardware, at a cost of several thousand dollars.  This is 
     an excellent debugging solution.  However, simulation with 
     software provides a very good debugging environment for 
     almost no cost.  sim_r3 is in use by another engineer at my 
     workplace, and has already found several bugs.


I. B. Disclaimer

     Although I am an experienced 6800 family programmer, and I 
     took great care to insure the accuracy of this emulation, and 
     several bugs have been found and fixed as the program has 
     been used, I make no representation that this program in its 
     current form is either bug free or will precisely meet your 
     needs.  The source code is distributed in this archive for 
     you to add (or change) any feature.  If you change and 
     recompile sim_r3.exe, PLEASE do not distribute it without 
     noting your changes in this file!

     Changes:
     V1.21 - added clear of latched external interrupt to 
          simulated reset routine in instr.c.  This change is 
          present in the source code in this archive.  This was an 
          omission in 1.2 and earlier, but the only symptom is, if 
          you issue 'I' and then reset before simulating servicing 
          the interrupt the interrupt persists. 8-July-1989 Joe 
	  Schachner
/*   V2.00 - The major changes are the symbol table support (5 chars/label)
	    and the requirement(!) for VGA in order to support 50 line mode,
	    the source code can always be changed to allow for different
	    numbers of line per screen.
	     Additional changes to files are noted:
	     INSTR.C  -  Add MUL (actually implements MUL).
			 Add STOP, WAIT (do not actually STOP or WAIT).
			 Update timings for HC05 devices.
			 Add symbol table reference by "linked list".
	     INSTR2.C -  Add symbol table reference to JMP, JSR, BRANCH
			  these do not appear as cleanly in "assignment"
			  column but it is clear enough.
			 Add STOP, WAIT (CCR modify).
			 Fix TAX,TXA by masking off the upper byte.
			 Fix ROR,ROL by masking off the upper byte.
V  I         SIM_MEM.C - sym_nmbr[], sym_tbl[] memory reference.
E  M                     load_sym() is identical to load() but it is very
R  P                     important(!!!) to specify the correct file with
Y  O                     the symbol table since otherwise the program will
   R                     get lost (it searches for the \f charcater the
   T                     assembler inserts in the output listing in
   A                     the load_sym_data() routine).
   N                     sym_writef_init() initialized the memory "image"
   T                     sym_writef() actually sets the "linked list".
	     SIM_R3.C -  sym_nmbr[], sym_tbl[] memory allocation.
			 add 'y' condition for keyboard input.

*/


II. Using sim_r3.exe

     Normally, one develops for a 6805 family processor using an 
     assembler and possibly a linker.  The output from the 
     development tools is a file containing Motorola hex format 
     records (S0, S1 and S9).

     The simulator loads in the Motorola hex file in response to 
     the 'L' command (see below).  By default trace display and 
     log file capture are on.  The simulator responds to your 
     commands input in either upper or lower case.

     Note: the simulator's trace log file is named "sim_r3.log" 
     and is created in the current directory when the simulator 
     is started.  If a file with the same name existed, it is 
     replaced by the new (empty) file.

     sim_r3 is a very small program.  When compiled with Microsoft 
     C 5.0, it is about 55,000 bytes.  /* QuickC yeilds 45K */
     Therefore, even 256K of memory is more than enough.  If you
     plan to turn on the log file (to capture the trace on disk),
     it helps to have a hard disk to keep execution speed up.

II. A. Items on the display

     When sim_r3 is started, it puts up the following on the top 
     seven lines of the display:

68705R3 Simulator V1.2  6-July-1989              Disp+log ON    Halted
R - disp/chg regs       L file - load Sx & reset        E - toggle TIE  G - Go
T - trace on/off        B addr - Break at address (go)  I - /INT      S - Step
X - Reset       M addr - Mem view/mod   Z - Disassem    H - Halt      Q - Quit

/*                                                      Y - symbol table    */
______________________________________________________________________________

     The top line (line 1) shows program status.  The next three 
     lines list commands, which will be explained below. The fifth 
     line is always blank.  The sixth line is where all commands 
     appear as you type them, and where prompts and messages 
     appear; this line will be referred to as the "prompt line".

     The next line (line 7) is a solid bar separating the fixed 
     top portion of the screen from the trace display, which 
     scrolls up from line 24 to line 8 and vanishes.  Disassembly 
     also appears on lines 8 to 24.

     The status line shows the program revision, whether trace 
     results will be displayed (and optionally captured to a 
     file), and whether simulation is in progress.  The next 
     section, "Explanation of commands", provides more information 
     on these fields.

II. B. Explanation of commands

    R - display / change registers
     Text similar to the following appears on the prompt line:

     PC= 100, A= 00, X= 00, SP= 07F, CCR=08 (I)  Change?(reg) _

     The user may enter (at least the first character of) the name 
     of any register shown, sim_r3 will prompt for a new value.  
     Press return without entering a register name to end this 
     command without changing a register.  Note: the values of the 
     registers are displayed and entered in hex.  Bits that are on 
     in the condition code register are also shown using the 
     characters HINZC.

    L file - Load Sx and reset
     sim_r3 reads motorola hex records.  Only S1 and S9 records 
     are significant.  Checksums are ignored.  Loading is 
     extremely fast.  When the "S9" record is encountered the load 
     terminates.  End of file without an "S9" record causes an 
     error message to be displayed.

     If the load completes without error, a message similar to the 
     following is displayed:

     File test.sx loaded

     When a hex file has been loaded, a simulated reset is 
     automatically performed (see 'X' command), below.

    E - Toggle TIE in
     sim_r3 simulates all four timer modes.  The 'E' command 
     changes the state of the timer's external input.  The current 
     state is displayed on the prompt line.  The effect of 
     changing the state of the timer's external input depends on 
     the mode set by bits 4 and 5 (TIE and TIN) in the Timer 
     Control Register.  See section 5.3 of the MC68(7)05 R/U 
     Series technical data book, Motorola ADI-977.

    G - Go
     The 'Halted' label changes to 'Running' and simulation 
     commences at the current PC.  The breakpoint address is 
     unchanged.  Simulation will halt when the PC equals the 
     breakpoint address on an opcode fetch, or if the 'H' command 
     is entered (see below).

    T - Trace display (and logfile) on/off
     If display is on when this command is entered, it is turned 
     off.  Logfile capture is always off when display is off.  If 
     display is off when this command is entered, the prompt 
     "Enable logfile also?(Y/N) " will appear.  After the prompt 
     is answered, the label on line one will say either "Display 
     ON" or "Disp+Log ON".  The format of the log file is 
     identical to that of the trace display.

     Note: simulation proceeds MUCH faster if the trace display is 
     turned off.

     An example trace display (part of a log file) appears below.  
     It was generated by the commands 'L test.sx', 'B 10b'.

100  A6 55         LDA   #$55           101=>55 ACCUM<=55                     2
102  48            LSLA                 ACCUM=>55 ACCUM<=AA                   6
103  47            ASRA                 ACCUM=>AA ACCUM<=D5                  10
104  97            TAX                  X_REG<=D5                            12
105  BF 50         STX   $50            050<=D5                              17
107  3C 50         INC   $50            050=>D5 050<=D6                      23
109  26 FC         BNE   $107                                                27
107  3C 50         INC   $50            050=>D6 050<=D7                      33
109  26 FC         BNE   $107                                                37
^    ^             ^                     ^                                   ^
|    |             |                     addr=>data (read)                   |
|    |             |                     addr<=data (write)        Cycle count
|    |             |                     All values in hex.         in decimal
|    |             Assembly              Register names ACCUM,
|    |             Mnemonics             X_REG, SP may appear.
|    |
|    Opcode and operand bytes for this instruction, in hex.
|
PC for opcode, in hex

     The example trace continues until finally location $50 
     becomes zero and the BNE is not taken:

109  26 FC         BNE   $107                                               437
107  3C 50         INC   $50            050=>FF 050<=00                     443
109  26 FC         BNE   $107                                               447

     At this point the prompt line shows "Breakpoint reached" and 
     the simulation is halted.

    B addr - Go and break at addr
     The breakpoint address is set from the address (in hex) 
     following the 'B'. After that, operation is the same as 'G', 
     above.  See 'T', above,  for an example of this command's 
     usage.

    I - /INT
     Latches an external interupt.  If the interrupt mask is not 
     set sim_r3 will simulate interrupt response prior to 
     beginning the next simulated instruction.

    S - Step
     Simulate one instruction at the current PC.  Similar to 'G' 
     except simulation is automatically halted after one 
     instruction.  The breakpoint address is unchanged.

    X - Reset
     sim_r3 simulates a reset, loading the PC from the reset 
     vector, initializing the data direction registers and the 
     timer, and the timer control register from the Mask Options 
     Register, and setting the interrupt mask and resetting the 
     stack pointer to 7F, and (version 1.21 and higher) also 
     clears internal latched interrupt if any.

    M addr - memory view/change
     The address (in hex) is read as if read by a program running 
     in the 68705, and the address and value are displayed on the 
     prompt line.  If 'Enter' is pressed, the next location is 
     displayed.  If a hex value is entered, the value is written 
     to the displayed location and then the next location is 
     displayed.  To get out of this routine, enter a non-hex-digit 
     ascii character, for example 'q'.
     Example: M 100
     100 A6      
     101 55      
     102 48  q

    Z - disassemble
     Z displays assembly mnemonics for the next 15 instructions in 
     memory starting at the current program counter, or, if an 
     address is entered, for the next 15 instructions starting at 
     that address.  The display looks similar to a trace display 
     except no read/write data is shown and machine cycles are not 
     shown.  Disassembly has no effect on simulation state.

    H - halt
     If simulation is in progress, it is stopped.  The 'Running' 
     label on the first line changes to 'Halted'.

    Q - quit
     Leave sim_r3.  The following appears on the prompt line:
     Logfile closed - normal exit

    Y - load symbol table.  As stipulated above it is necessary to
     specify the correct file with the symbol table (generated by
     the FREEWARE assembler on the BBS) to prevent the program from
     locking up.

   Enter -
     Just pressing 'Enter' does nothing but cause the line under 
     the prompt line to be redrawn.  This is useful in case you 
     accidentally press "Escape" and DOS blows away the line.

III. Recompiling sim_r3

III. A. For the IBM-PC
III. A. 1. Using Microsoft C 5.0 or higher

     This supplied code may be compiled without changes.  The 
     supplied make file, makefile.mak, is for Polytron's POLYMAKE 
     to invoke the Microsoft C compiler.  The makefile is written 
     in a manner which makes it very easy to convert for 
     Microsoft's make, which is supplied with Microsoft C.  Only a 
     few lines need to be moved.  Exact direction are in a comment 
     in makefile.mak.

III. A. 2.Using another compiler

     Most of this program is "plain vanilla" C, and will port 
     unchanged.  However, the functions which clear the screen and
     position the text cursor are not portable.  clearscreen and 
     settextposition call routines from Microsoft C 5.0's 
     graphics library.  Most C compilers will supply library 
     routines for these functions, which may be substituted.
     Delete_line uses the Microsoft C function "int86" to invoke 
     one of the DOS BIOS services.  Again, most C compiles for the 
     PC will have some way to invoke the BIOS services, which may 
     be substituted.

     If your compiler does NOT have cursor position and screen 
     functions, you may use ANSI.SYS to supply these functions.  
     ANSI.SYS is a file supplied with IBM DOS.  It may be built 
     into the DOS of some clones.  ANSI.SYS must be memory 
     resident.  This requires the statement "DEVICE=ANSI.SYS" in 
     your config.sys file when you boot.  Then, simply writing a 
     special sequence of characters to stdout will cause ANSI.SYS 
     to perform these functions.  See the IBM DOS technical 
     reference for documentation on control codes for ANSI.SYS.  
     The code for using ANSI.SYS will look a lot like the code for 
     driving a VT-52 (a Digital Equipment Corp terminal), which is 
     included.  However, the control codes are not the same: 
     ANSI.SYS uses DEC VT-100 control codes.

     sim.h includes a #define for the type of graphics routines, 
     at the moment either MSC or VT52.  I suggest you add another 
     #define and add your new C code right after each occurance of 
     "#ifdef VT52 ... #endif" in the routines settextposition and 
     clearscreen, both in sim_r3.c; and in the routine delete_line 
     in instr.c.

III. B. For non-IBM compatible machines

     As long as your machine has an 80x25 character text display, 
     the only changes which need to be made are to support the 
     functions settextposition, clearscreen, and delete_line.

     sim.h includes a #define for the type of graphics routines, 
     at the moment either MSC or VT52.  I suggest you add another 
     #define and add your new C code right after each occurance of 
     "#ifdef VT52 ... #endif" in the routines settextposition and 
     clearscreen, both in sim_r3.c; and in the routine delete_line 
     in instr.c.

     Note that if your computer emulates a DEC VT 52 terminal, or 
     if you will use this on a computer that actually drives a 
     terminal that can handle VT 52 control codes, then all you 
     have to do is uncomment "#define VT52" instead of "#define 
     MSC" in sim.h and recompile.

     It is interesting to note that exactly the same parts of the 
     program need to be changed for a non-IBM compatible as for a 
     true IBM compatible but not Microsoft C 5.0 or higher.  This 
     is because of the lack of standardization of even the most 
     rudimentary graphics functions; each compiler is different.  
     Perhaps X Windows will finally change this sad situation.

     One further reflection on graphics standardization: I 
     mentioned above that sim_r3 was about 55,000 bytes when 
     compiled by Microsoft C 5.0.  When compiled by Mark Williams 
     C for the Atari ST it is only about 36,000 bytes.  This 
     difference is due mostly to the fact that support for the 
     needed graphics functions and VT52 emulation is part of the 
     ST's operating system, but requires routines from Microsoft C 
     5.0's graphics library in the IBM version.  Consider the 
     amount of memory wasted in a multitasking environment if each 
     application includes the graphics library and ten or twenty 
     applications are running...  This has nothing to do with 
     sim_r3, but it's one of my favorite subjects!  My apologies.  
     I hope sim_r3 is useful to you.

     --- Joe Schachner 8-July-1989
/* Amir Bernstein 27-November-1991, Happy Thanksgiving Joe in case you
   get this before Thanksgiving */