ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ·
      ³                                                                   º Û
      ³                                                                   º Û
      ³                           A M I s e t u p                         º Û
      ³                                                                   º Û
      ³ Documentation                                                     º Û
      ³                                                                   º Û
      ³ Copyright (c) Robert Muchsel 1992-1995                            º Û
      ³ All rights reserved.                                              º Û
      ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼ Û
       ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß

      AMIsetup is an external setup program for 386/486/Pentium PCs with
      `HighFlex BIOS' or `WinBIOS' from AMI.

      If you ever considered your built-in setup as incomprehensible,
      boring, inconvenient or incomplete, you've been waiting for
      AMIsetup.

      AMIsetup can save your configuration on disk and restore it. You
      can even change setup options missing in your BIOS! AMIsetup cracks
      your password and prints your setup as a list. You can install IDE
      hard disks automatically! Add comprehensive on-line help, Soundblaster
      support and an on-line reference that explains many setup options.
      You can even print a personal BIOS manual!

      For diagnostic purposes, AMIsetup can on many machines measure the
      DMA frequency (avoid burnout of the DMA chip due to overload) and
      display the CMOS error flags. You can display the revision of your
      keyboard controller, change setup registers manually (experts only)
      and display the BIOS ID. Switch AMIsetup to high resolution video
      mode (EGA/VGA) and use the mouse...

      And once you are finished, AMIsetup can reboot your computer.

      Professionals will like the batch mode of AMIsetup. Configure
      identical computers in blitz speed!


      Important
      ÄÄÄÄÄÄÄÄÄ

       ÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜÜ
      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
      ³                                                                    ³
      ³                         USE AT YOUR OWN RISK!                      ³
      ³  This program is based on undocumented data structures.            ³
      ³  Improper use, program errors or bad luck can cause hardware,      ³
      ³  software and stored data of the computer be irreversibly damaged! ³
      ³  The user is advised always to make adequate Back Ups of all       ³
      ³  valuable files or Data. Because he can have no control over how   ³
      ³  this program is used                                              ³
      ³          THE AUTHOR ACCEPTS NO LIABILITY FOR ANY DAMAGE!           ³
      ³                                                                    ³
      ÔÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¾
       ßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßßß

      No part of this documentation may be reproduced, transmitted,
      transcribed, stored in any retrieval system, or translated into any
      other language or computer language in whole or in part, in any form
      or by any means, whether it be electronic, mechanical, magnetic,
      optical, manual or otherwise, without prior written consent of the
      author, Robert Muchsel.

      The author disclaims all warranties as to this software, whether
      express or implied, including without limitation any implied warranties
      of merchantability, fitness for a particular purpose, functionality,
      data integrity or protection, in so far as permitted by applicable
      legislation.

      All trademarks are property of their respective owners and appear for
      identification purposes only.



      Shareware
      ÄÄÄÄÄÄÄÄÄ

      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
      ³  Writing this program has taken lots of work. If you continue     ³
      ³  using it after a reasonable trial period of 30 days, you have    ³
      ³  to pay a small fee to the author.                                ³
      ³                                                                   ³
      ³  SHAREWARE is NOT FREE SOFTWARE. You can, however, test shareware ³
      ³  before purchasing it.                                            ³
      ³                                                                   ³
      ³  For detailed information, see appendix A.                        ³
      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

      You are encouraged to copy and pass on the unregistered shareware
      version of this program, if
      - the program is distributed in its original form
        (complete, unmodified, uninstalled)
      - the distribution fee does not exceed the equivalent of DM 15.-.

      It is forbidden to distribute the program bundled with books,
      magazines, etc. (including `bookware'). To do this, you must obtain
      a written permission from the author.

      The information contained in the on-line reference for registered users
      must not be copied, published or separated from the program. The author
      has taken every care to ensure the technical correctness of the
      information, but cannot accept any liability in case of any error.



      If you have comments or find an error, please send them to the author!



                                     Contents
                                     ÄÄÄÄÄÄÄÄ

        1   Caution!
        2   Starting the program
        3   Menus in detail
            3.1 System menu
            3.2 Diagnostic menu
            3.3 Backup menu
            3.4 Setup
                1. Standard setup
                2. Extended/chipset setup
                3. Change register
                4. Password
                5. Load ROM setup defaults, load ROM power-on defaults
                6. Print current setup
                7. Print reference manual
                8. Analyze BIOS ID
                9. Save changes and quit
               10. Exit without saving
            3.5 Tools menu
            3.6 Help menu
        4   Key shortcuts

            Appendix

        A   Registration, limits of the shareware version,
            addresses, upgrades, about the author
        B   AMIsetup and OS/2, AMI BIOS and OS/2, Windows, Windows NT
        C   Trouble shooting
            1. Is AMIsetup compatible with your BIOS?
            2. Frequent errors with compatible BIOS versions
            3. Stopgap: -O
            4. Additional trouble shooting options
        D   Glossary
        E   If the machine won't boot...
        F   Switching to the English user interface
        G   Soundblaster
        H   EISA
        I   Batch mode
        J   Obtaining new or bug fixed program revisions
        K   Tested BIOS revisions


            What's new

            Changes are described in a separate file, AMISETUP.NEW.



      1  Caution!
      ÄÄÄÄÄÄÄÄÄÄÄ

      If you are not familiar with setup options or if you don't know
      what they do, please consider whether changing the setup options
      is really necessary.

      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
      ³  On many PCs, the DMA clock speed can be changed.                 ³
      ³  This may work at first, but later the DMA chip may be destroyed, ³
      ³  thus making the motherboard useless!                             ³
      ³                                                                   ³
      ³  Another critical point is the password option. Since you cannot  ³
      ³  erase CMOS RAM on some main boards (see appendix E), it may      ³
      ³  happen that because of - forgetfulness, BIOS errors, different   ³
      ³  keyboard layout, etc. - you are irreversibly locked out of your  ³
      ³  computer.                                                        ³
      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

      Before making ANY change, ask yourself:
      - is it necessary?
      - what are the consequences?

      AMIsetup saves your configuration into a file after installation
      and whenever you invoke the program. However, this works only if
      you don't use AMIsetup on a write protected diskette.


      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
      ³  N E V E R   C H A N G E   A   R U N N I N G   S Y S T E M  !!!   ³
      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

      WHEN DID YOU DO YOUR LAST COMPLETE BACKUP???


      2  Starting the program
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      First of all, please read the manual and the file `AMISETUP.NEW'.

      The program needs write access to the current directory. Diskettes
      must not be write protected if file operations are to be used.

      Normally, you start AMIsetup without additional command-line options.
      There are exceptions though (see appendix C). You should read
      appendix B if you want to use AMIsetup under OS/2.

      If you are using an LCD screen, invoke AMIsetup by `AMISETUP -MONO'
      (or execute `MODE MONO' or `MODE BW80' first).

      Adaptec SCSI Controllers: Be sure to use the ASPI4DOS driver to avoid
      possible problems with the memory management unit.

      Virus scanners from Central Point Software: The memory resident
      virus scanner from Central Point thinks there was a `TH TH' virus
      in AMIsetup. The non-resident version and scanners from other vendors
      will show you that this is not true.

      If using AMIsetup for the first time, you have to choose the desired
      language:

              ÚÄÄÄÄÄÄÄÄÄÄÄÄ Welcome / Willkommen ! ÄÄÄÄÄÄÄÄÄÄÄÄ¿
              ³                                                ³
              ³  This is a bilingual version of AMIsetup.      ³
              ³  For English help texts and user interface,    ³
              ³  press [E].                                    ³
              ³                                                ³
              ³  Dies ist eine zweisprachige Version von       ³
              ³  AMIsetup. Dr�cken Sie [D] f�r deutsche Hilfe- ³
              ³  texte und Benutzeroberfl„che.                 ³
              ³                                                ³
              ³  [E] English version     [D] deutsche Version  ³
              ³                                                ³
              ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄAMIsetupÄÙ

      Should you decide on the German version, please continue reading in
      the file `AMISETUP.DOK'.

      Next you must to accept the warning message with a `Y':

              ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ C A U T I O N ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
              ³                                                ³
              ³              USE AT YOUR OWN RISK!             ³
              ³                                                ³
              ³  This program is based on undocumented data    ³
              ³  structures. Hard- and software and stored     ³
              ³  data could be damaged irrevocably!            ³
              ³                                                ³
              ³ THE AUTHOR WILL NOT BE LIABLE FOR ANY DAMAGES! ³
              ³                                                ³
              ³ [Y] accept and start program   [N] back to DOS ³
              ³                                                ³
              ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄAMIsetupÄÙ

      If you have set a password under `System|Options', you will be prompted
      to enter it.

                   ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Password ÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                   º                                      º
                   º AMIsetup is password protected.      º
                   º Please enter the current password.   º
                   º                                      º
                   º  Password    ****                    º
                   º                                      º
                   º                                      º
                   º          OK   Ü      Help  Ü         º
                   º        ßßßßßßßß     ßßßßßßßß         º
                   ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      Next, a dialogue box containing program revision and registration
      number (or `UNREGISTERED') appears. If you haven't yet paid for
      AMIsetup and a registration number appears anyway, you've got an
      (illegal) pirated copy. Please contact the author.

                  ÉÍ[þ]ÍÍÍÍÍÍÍÍÍÍ Information ÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                  º                                         º
                  º             AMIsetup v2.99              º
                  º         REGISTERED (#.........)         º
                  º                                         º
                  º  Copyright (c) 1992-95 Robert Muchsel   º
                  º           All rights reserved           º
                  º                                         º
                  º                                         º
                  º           Heap memory:  84080           º
                  º               PCI System                º
                  º                                         º
                  º            OK    Ü     Help   Ü         º
                  º          ßßßßßßßßß    ßßßßßßßßß         º
                  ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼



      Quick start
      ßßßßßßßßßßß

      In most parts, AMIsetup should explain itself. All explanations
      are included in the on-line help. However, please note the
      warning messages and the license restrictions of the personal
      BIOS manual.


      3  Menus in detail
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      Using the mouse or pressing <F10>, you get to the main menu bar.
      There, you have the following pull down menus at your disposal:


        System  Diagnostic  Backup  Setup  Tools  Help
      °°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°°

      Pressing <F1> gets you help. The on-line help contains nearly all of
      the manual.

      Hint for mouse users: The right button is equivalent to <Esc>.


      3.1 System menu
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

       System
      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
      ³ Options...        ³ 3.1.1
      ³ Video mode  Alt-V ³ 3.1.2
      ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
      ³ Reboot...         ³ 3.1.3
      ³ Exit        Alt-X ³ 3.1.4
      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

      3.1.1 Options...

        ÚÄ[þ]ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ Options ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
        ³                                                              ³
        ³  Preferences                                                 ³
        ³   [ ] Auto start setup                  BIOS source... Ü     ³
        ³   [X] Enable reboot command             ßßßßßßßßßßßßßßßß     ³
        ³   [X] Beep on error                      Password...   Ü     ³
        ³   [ ] Reverse mouse buttons             ßßßßßßßßßßßßßßßß     ³
        ³   [ ] Use Soundblaster                                       ³
        ³   [ ] German language                                        ³
        ³                                                              ³
        ³  Display setup options                                       ³
        ³   [X] þ Hidden options                       Save      Ü     ³
        ³   [ ] ¨ Deleted options                 ßßßßßßßßßßßßßßßß     ³
        ³                                             Cancel     Ü     ³
        ³  Backup file path                       ßßßßßßßßßßßßßßßß     ³
        ³   C:\AMISETUP\                               Help      Ü     ³
        ³                                         ßßßßßßßßßßßßßßßß     ³
        ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

        Here you can customize the program to your own needs.

        Auto start setup
          Instead of selecting Setup manually each time using the menu,
          `Setup' can also be started automatically.

        Enable reboot command
          If this box is blank, the Reboot function in the System menu is
          disabled.

          In addition, you will not be asked whether you want to reboot after
          saving your setup.

        Beep on error
          If this option is checked, the program beeps if you enter incorrect
          values in input boxes.

        Reverse mouse buttons
          You can reverse right and left mouse buttons (for left-handers or
          southpaws).

        Soundblaster
          See appendix G.

        German language
          You can disable the English user interface and work with the German
          one instead.

        Display setup options
          There are two types of hidden options in the ROM BIOS.

          `þ' shows that the option is hidden in the built-in BIOS setup.
          The `þ' options work correctly in most cases.

          `¨' shows that the option is hidden in the built-in BIOS setup and
          that AMIsetup cannot find a textual description of the possible
          settings. Often `¨' options don't work.

          You can enable and disable both types. If neither `þ' nor `¨' are
          enabled, then AMIsetup shows the same set of options as the ROM
          setup.

        Backup file path
          You can change the directory of the backup files.

        BIOS source
          The following explanation is very technical. If do not fully
          understand it, please leave the BIOS source at `Protected Mode'.

          AMIsetup must completely read your BIOS. Since parts of the BIOS
          are frequemtly hidden by memory managers or the chip set itself
          after the system has booted, AMIsetup offers three different
          methods of accessing the BIOS:

           Protected Mode

          This mode is the default mode. AMIsetup switches to protected mode
          and thereby circumvents memory managers.

           Conventional Memory

          AMIsetup stays in real mode and reads the BIOS from F000:0000 (or
          E000:0000). Problems are to be expected if a memory manager or
          shadow RAM is enabled.

           Image File

          AMIsetup reads the BIOS from a file, which can be created by e.g.
          `Tools|Create BIOS image' If the image is OK, this mode shouldn't
          cause any trouble.

        Password
          You can define a password under `System|Options', which will be
          needed at program start. Password protection reduces misuse of the
          AMIsetup.

          Changes of the password are written into the file AMISETUP.EXE
          that must not be write protected for this operation.

      3.1.2 Video mode

        Toggles the display mode between 25 lines and 43/50 lines and
        requires an EGA/VGA graphics adaptor. AMIsetup automatically stores
        the last used video mode.

      3.1.3 Reboot

        Executes a cold boot. The keyboard controller is programmed to
        trigger a hardware reset.

        The `Reboot' function can be turned off using `System|Options'.

        CAUTION! If you use a hard disk cache or hard disk doubler, this
        function could possibly cause data loss.

        AMIsetup first tries to flush the SmartDrive cache (if it is
        installed, you can disable this feature using the command line
        argument `-NOSM'), waits 2 seconds and then resets the computer.

        Under OS/2, only the program is closed.

      3.1.4 Exit

        Exits the program.


      3.2 Diagnostic menu
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

       Diagnostic
      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
      ³ BIOS version                ³ 3.2.1
      ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
      ³ CMOS RAM checksums          ³ 3.2.2
      ³ CMOS RAM information        ³ 3.2.3
      ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
      ³ Keyboard controller         ³ 3.2.4
      ³ Co-processor status         ³ 3.2.5
      ³ DMA clock speed             ³ 3.2.6
      ³ Compare DOS/real time clock ³ 3.2.7
      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

      3.2.1 BIOS version

        Verifies whether the BIOS and AMIsetup are compatible. This check
        is executed automatically whenever you start Setup.

        If this test fails, ensure the BIOS source is set to `Protected
        Mode' under `System|Options'.

        See the trouble shooting section (appendix C) for more information
        about compatible BIOS versions.

      3.2.2 CMOS RAM checksums

        Verifies the CMOS RAM checksums. There are two areas - the first is
        in all AT computers, the second only in PCs with an AMI BIOS. If one
        of these two tests fails, the program declines to run Setup.

        If you have written your Setup to a file before this error occurred,
        you can correct the problem through `Backup|Restore CMOS RAM'.

        AMIsetup saves your configuration automatically
         - when you first use the program into the file SAVECMOS.SAV
         - whenever you invoke the program into the file CMOSBKUP.SAV.

        See the trouble shooting section (appendix C) for information on
        possible errors.

      3.2.3 CMOS RAM information

        Shows the date of the RTC, the alarm time and information about
        errors at system boot.

        ÉÍÍÍÍ Information about CMOS RAM contents ÍÍÍÍÍ»
        º                                              º
        º  Date ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿                  º
        º  ³ 09/16/1995             ³                  º
        º  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ                  º
        º                                              º
        º  Alarm ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿                  º
        º  ³ 00:00:00           off ³       OK    Ü    º
        º  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ    ßßßßßßßßßß    º
        º                                              º
        º  Status ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿     Print   Ü    º
        º  ³ Battery:             û ³    ßßßßßßßßßß    º
        º  ³ Power:               û ³                  º
        º  ³ Checksum:            û ³      Help   Ü    º
        º  ³ Configuration:       û ³    ßßßßßßßßßß    º
        º  ³ Memory size:         û ³                  º
        º  ³ Hard disk C:         û ³                  º
        º  ³ Time:                û ³                  º
        º  ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ                  º
        ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        Date: The current system date of the real time clock (RTC).

        Alarm: The RTC supports an `alarm clock' mode. You need an external
        program (TSR) that processes the RTC message and then activates.

        Status: Shows possible errors from the last system boot. A `û' means
        `no error found'.

        - Battery: CMOS battery is discharged and CMOS contents were invalid

        - Power: RTC power supply failed

        - Checksum: CMOS checksums were invalid

        - Configuration: Self test results and CMOS configuration were
        different

        - Memory size: Memory size determined by self test and memory size
        stored in CMOS were different

        - Hard disk C: Hard disk C: (if available) couldn't be initialized and
        couldn't be booted from

        - Time: Time was invalid

        Errors often disappear after a reboot (e.g. Checksum).

      3.2.4 Keyboard controller

        Tries to detect vendor and revision of the keyboard controller.

        AMIsetup knows chips from American Megatrends, Inc. and Award, Inc.
        All other vendors are shown as `unknown'.

        This function is disabled under OS/2.

      3.2.5 Co-processor status

        This function performs a coprocessor hardware check and compares the
        result with the BIOS coprocessor presence bit, which is set during
        system boot.

        If both results correspond (i.e. `Coprocessor present' and `Status
        bit set' or `No coprocessor present' and `Status bit not set'),
        everything is OK.

        If both results do not correspond (`*ERROR*' is displayed in
        addition), the BIOS most probably doesn't sense the coprocessor.

        If you have problems with applications which support a math
        coprocessor and the above error is shown, you should first look into
        `Setup|Extended SetupŽ and see if you can enable `Numeric Coprocessor'
        or `Numeric Coprocessor Test'.

        If no such setting is available, you can create a small `SETNPU'
        program and add it to your AUTOEXEC.BAT.

         Please copy all characters exactly as shown:

         C:\> DEBUG SETNPU.COM
         The specified file name expression was not found.
         -a
         ....:0100 mov ax,40
         ....:0103 mov ds,ax
         ....:0105 or byte ptr [10],2
         ....:010A mov ax,4c00
         ....:010D int 21
         ....:010F                     [Press Enter]
         -rcx
         CX 0000
         :0f
         -w
         Writing 000F bytes
         -q
         C:\>

      3.2.6 DMA clock speed

        Tries to determine the current DMA clock speed (this operation is
        very hardware dependent and it is possible it won't work - `Error'
        is displayed then).

        The measured clock speed is displayed in

          green  (up to 4.25 MHz): Everything OK
          yellow (up to 5.10 MHz): Caution, possibly decrease DMA clock
                                   speed
          red    (from  5.10 MHz): The clock is too fast and can cause
                                   damage!

        Conditioned by `DMA waits' it is possible that too low a clock is
        shown (especially on fast i486 systems). I.e.: If AMIsetup detects a
        `red' DMA clock, then it is truly time to decrease it - the DMA chip
        can be destroyed by overclocking!

        On many systems, DMA clock is coupled with bus clock (e.g. ETEQ,
        OPTI, SIS, UMC).

        You can compute the bus clock using the following formula:

         Bus Clock = 2 * DMA Clock

        Depending on the DMA waitstates, the factor can be 2.75 (1 Waitstate)
        or 3 (2 Waitstates) instead of 2.

        It is neither possible to measure the bus clock nor the number of
        DMA waitstates directly.

        This function is disabled under OS/2.

      3.2.7 Compare DOS/real time clock

        Compares the current DOS time and the RTC time and is used for
        reference purposes only. If the difference is more than about 2
        seconds, you should check hard and software.


      3.3 Backup menu
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

       Backup
      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
      ³ Save CMOS RAM...      ³ 3.3.1
      ³ Restore CMOS RAM...   ³ 3.3.2
      ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
      ³ Save EISA NVRAM...    ³ 3.3.3
      ³ Restore EISA NVRAM... ³ 3.3.3
      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

      3.3.1 Save CMOS RAM...

        Saves the CMOS RAM to a file. You can change the default directory
        under `System|Options'.

      3.3.2 Restore CMOS RAM...

        Reads an image file back to CMOS RAM and restores the saved state.
        Time and date are not changed.

      3.3.3 Save and Restore EISA NVRAM...

        On some EISA computers, you can also save and restore the EISA NVRAM
        (parts of the configuration data are stored in the EISA NVRAM on
        these machines).

        See appendix H for more information.


      3.4 Setup
      ÄÄÄÄÄÄÄÄÄ

      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ Setup ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
      ³05/05/91(C)1990 American Megatrends Inc., All Rights Reserved
      ³
      ³
      ³
      ³
      ³                      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
      ³                      ³        Standard Setup         ³
      ³                      ³    Extended/Chipset Setup     ³
      ³                      ³        Change Register        ³
      ³                      ³           Password            ³
      ³                      ³    Load ROM Setup Defaults    ³      WARNING:
      ³                      ³  Load ROM Power-On Defaults   ³      Improper
      ³                      ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´      Setup may
      ³                      ³      Print Current Setup      ³      severe pr
      ³                      ³    Print Reference Manual     ³
      ³                      ³        Analyze BIOS ID        ³
      ³                      ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
      ³                      ³     Save Changes and Quit     ³
      ³                      ³      Exit without Saving      ³
      ³                      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ
      ³ 30-0201-ABCDEF-00101111-050591-OPWB
      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      Please read the warnings at the beginning of this document.


      3.4.1 Standard setup
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      You can change the following settings (to change date and time,
      please use the DOS commands DATE and TIME).

      ÉÍ[þ]ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Standard setup ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
      º                                                                  º
      º Base memory:       640K                                          º
      º Extended memory: 16384K           Auto detect hard disks Ü       º
      º                                   ßßßßßßßßßßßßßßßßßßßßßßßß       º
      º Drive A         Drive B           HDD 0 Ü         HDD 1 Ü        º
      º                                   ßßßßßßß         ßßßßßßß        º
      º  ( ) None        ( ) None          Type:    47    NONE / SCSI    º
      º  ( )  360K 5¬"   ( )  360K 5¬"     Cyl:   1024                   º
      º  ( )  1.2M 5¬"   (x)  1.2M 5¬"     Heads:   64                   º
      º  ( )  720K 3«"   ( )  720K 3«"     S/Trk:   26                   º
      º  (x) 1.44M 3«"   ( ) 1.44M 3«"     Size:  832M                   º
      º  ( ) 2.88M 3«"   ( ) 2.88M 3«"                                   º
      º                                                                  º
      º Display adapter      Options                                     º
      º  ( ) Not installed    [X] Keyboard installed                     º
      º  ( ) Color 40x25                                                 º
      º  ( ) Color 80x25                                                 º
      º  ( ) Monochrome                                                  º
      º  (x) VGA/PGA/EGA                  OK   Ü    Cancel Ü     Help  Ü º
      º                                 ßßßßßßßß    ßßßßßßßß    ßßßßßßßß º
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      At top, the memory size as determined by the BIOS is displayed.

      Drive A
      Drive B
        Allows you to change the type of installed floppy disk drives.

        2.88 MB disk drives:
          Using AMIsetup, you can configure the drive type `2.88 MB' on
          any computer. To run a ED drive, you need a diskette controller
          capable of the 1 Mbps data rate (e.g. AHA1542CF).

          If your BIOS does not support 2.88 MB drives, AMIsetup displays
          a warning message (BIOS versions earlier than 06/12/91).

          Lack of BIOS support can cause the following problems:
          - Problems booting from diskette (especially 720 KB diskettes)
          - The built-in ROM `Standard setup' displays a line containing
            garbage characters (this does not adversely affect other setup
            functions).
          - You'll need software support for your floppy drive. OS/2
            automatically detects 2.88 MB drives. DOS 5.0 or later requires
            a device `DRIVER.SYS' (please consult your DOS manual). The
            author is currently developing a flexible BIOS enhancement which
            must be installed in CONFIG.SYS, supporting 360 KB to 2.88 MB
            floppy drives on any port, IRQ or DMA channel.
          - Dependent on your hardware, it might be better instead to tell
            the BIOS the drive was 1.44 MB.
          You can disable the warning message (displayed if your BIOS does
          not support 2.88 MB drives) using the command line parameter
          `-288'.

      Display adapter
        With this you set the type of the installed graphics adapter.

             ( ) Not installed
             ( ) Color 40x25
             ( ) Color 80x25   = CGA
             ( ) Monochrome    = MDA, Hercules
             (x) VGA/PGA/EGA

        On older main boards, you have to change a jumper in addition to
        this setting.

      Options - Keyboard installed
        If the keyboard should be checked at system boot, check this box.
        Should the keyboard not be checked or if there is no keyboard
        installed (e.g. LAN server), leave it empty.

      Auto detect hard disks
        You don't need to enter the parameters of your hard disks manually
        if you have IDE type drives installed.
        AMIsetup can detect the correct cylinder/head/sector values
        automatically (non-OS/2 systems only).

        ÉÍ[þ]ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Confirm ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
        º                                                    º
        º               Install the following                º
        º              hard drives into setup?               º
        º                                                    º
        º  HDD 0: Conner Peripherals 170MB, CP30174E         º
        º  HDD 1: Not installed / SCSI                       º
        º                                                    º
        º                                                    º
        º           Yes   Ü      No    Ü     Help   Ü        º
        º         ßßßßßßßßß    ßßßßßßßßß    ßßßßßßßßß        º
        ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        If no hard disks are found, it's most likely you have SCSI type
        drives (or old MFM or RLL drives).
        In the case of MFM/RLL type drives, you must enter the disk
        parameters manually; this also holds true for some SCSI
        controllers.

      HDD 0
      HDD 1
        With this you can set the type of installed MFM, RLL or IDE
        hard drives. Using a SCSI controller, you mustn't define a hard disk
        here - please read your controller and hard disk manual to prevent
        momentous wrong settings!

        The current parameters are displayed below the push-button - type
        (number) of the disk, cylinders, heads, sectors per track and the
        calculated size.
        Note: The disk size is displayed in real Megabytes, 2^20 bytes.
        Many disk vendors calculate in 10^6 bytes (this number is larger!).

        If you push the button, a list of predefined disk types appears:

             ÉÍ[þ]ÍÍÍÍÍÍÍÍÍ Hard disk 0 parameters ÍÍÍÍÍÍÍÍÍÍÍÍÍ»
             º Type³ Cyls. ³Heads³ Precomp³ LZone ³S/Trk³  Size º
             ºÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÄÄº
             º  32 ³  1024 ³  15 ³   NONE ³  1024 ³  17 ³  128M >
             º  33 ³  1024 ³   5 ³   1024 ³  1024 ³  17 ³   43M ±
             º  34 ³   816 ³  15 ³   NONE ³   816 ³  32 ³  191M ±
             º  35 ³  1024 ³   9 ³   NONE ³  1024 ³  17 ³   77M ±
             º  36 ³  1024 ³   8 ³    512 ³  1024 ³  17 ³   68M ±
             º  37 ³   615 ³   8 ³    128 ³   615 ³  17 ³   41M ±
             º  38 ³   745 ³   4 ³    512 ³   745 ³  28 ³   41M ±
             º  39 ³   987 ³   7 ³    987 ³   987 ³  17 ³   57M ±
             º  40 ³   820 ³   6 ³    820 ³   820 ³  17 ³   41M ±
             º  41 ³   977 ³   5 ³    977 ³   977 ³  17 ³   41M ±
             º  42 ³   981 ³   5 ³    981 ³   981 ³  17 ³   41M ±
             º  43 ³   755 ³  16 ³   NONE ³   755 ³  17 ³  100M ±
             º  44 ³   887 ³  13 ³   NONE ³   887 ³  34 ³  191M ±
             º  45 ³   968 ³  10 ³   NONE ³   968 ³  34 ³  161M ±
             º  46 ³   751 ³   8 ³      0 ³   751 ³  17 ³   50M þ
             º¯ 47 ³ USER DEFINED³        ³       ³     ³      ®<
             ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        The columns contain type (number) of the disk, number of cylinders,
        heads, the precompensation cylinder (see glossary), landing zone,
        number of sectors per track and the calculated size (rounded) in
        megabytes. Please compare these items with the data sheet of your
        hard disk.

        It's likely you CANNOT find the specifications of the hard disk to
        be installed in this list. In this case, select type 47 (USER
        DEFINED).
        The following dialogue appears:

             ÉÍ[þ]ÍÍÍÍÍÍÍ  Change type 47 parameters  ÍÍÍÍÍÍÍÍÍÍÍÍ»
             º                                                    º
             º                                                    º
             º     615 ¯Cylinders                                 º
             º                                                    º
             º       4  Heads                                     º
             º                                                    º
             º     300  Precompensation (65535 for NONE)          º
             º                                     [  Save   ]    º
             º     615  Landing zone                              º
             º                                     [ Cancel  ]    º
             º      17  Sectors/track                             º
             º                                     [  Help   ]    º
             º                                                    º
             ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

        Here you can set the parameters yourself. Note that the value of
        precompensation has a special meaning: 65535 means DISABLED for the
        whole hard disk. 0 means ENABLED for the whole disk.
        Modern drives ignore precompensation and landing zone. For reasons
        of software compatibility, set precompensation to `NONE' and landing
        zone to the highest available cylinder.


      3.4.2 Extended/chipset setup
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      A list of options and their current settings is displayed:

      ÉÍ[þ]ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Extended setup ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ
      º            Option            ³Register³Bits ³ Current setting
      ºÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÁÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
      º¯  Typematic Rate Programming ³ 11  10000000 ³ 10000000  Enabled     ®
      º   Typematic Rate Delay (msec)³ 11  01100000 ³ 00000000  250
      º   Typematic Rate (Chars/Sec) ³ 11  00011111 ³ 00000011  21.8
      º ¨ Mouse Support Option       ³ 13  10000000 ³ 10000000   <1>
      º   Above 1 MB Memory Test     ³ 13  01000000 ³ 00000000  Disabled
      º   Memory Test Tick Sound     ³ 13  00100000 ³ 00000000  Disabled
      º   Memory Parity Error Check  ³ 13  00010000 ³ 00010000  Enabled
      º   Hit <ESC> Message Display  ³ 13  00001000 ³ 00000000  Disabled
      º   Hard Disk Type 47 Data Area³ 13  00000100 ³ 00000000  0:300
      º   Wait For <F1> If Any Error ³ 13  00000010 ³ 00000010  Enabled
      º   System Boot Up Num Lock    ³ 13  00000001 ³ 00000001  On
      º þ Numeric Processor          ³ 14  00000010 ³ 00000010  Present
      º   Weitek Processor           ³ 2D  10000000 ³ 00000000  Absent
      º   Floppy Drive Seek At Boot  ³ 2D  01000000 ³ 00000000  Disabled
      º   System Boot Up Sequence    ³ 2D  00100000 ³ 00000000  C:, A:
      º   System Boot Up Speed       ³ 50  00000100 ³ 00000000  High
      º   Cache Memory               ³ 2D  00001000 ³ 00001000  Enabled
      º ¨ Internal Cache Memory      ³ 2D  00000100 ³ 00000100   <1>
      ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

      The four columns have the following meaning:

      Option
        The name of the setting to be changed, peeked from the BIOS.

        The signs `þ', `¨' and `x' in the first column have a special
        meaning:

        `þ' shows that the option is hidden in the built-in BIOS setup.
        The `þ' options work correctly in most cases.

        `¨' shows that the option is hidden in the built-in BIOS setup and
        that AMIsetup cannot find a textual description of the possible
        settings. Often `¨' options don't work.

        If you change settings of options marked in this way, be especially
        careful. You can disable the display of these options selectively
        under `System|Options'.

        `x' shows that the BIOS has currently deactivated the option (e.g.
        because the option is only valid for a 486 processor, but there is a
        386 processor installed or because the option can only be activated
        in conjunction with some other option).

        By the way, blame the BIOS manufacturer for reversed letters in this
        column (however, AMIsetup has a built-in spell checker since version
        2.99).

      Register
        Hexadecimal number of the CMOS register that stores the setting.
        This information may help experienced users to change settings
        manually using Change Register. If a `+' sign is displayed after the
        register number, there might be other registers affected.

      Bits
        Bit mask for the setting. Only Bits marked with a `1' are used for
        the specified setting (see also Register).

      Current setting
        Bit mask of the setting stored in the program copy of CMOS RAM and
        the corresponding text in clear. If plain language is not available,
        a decimal value in acute brackets is shown. Example: <2> denotes the
        third possible setting, since <0> is valid, too.


      Now you can select an option with the mouse or the enter key, as
      appropriate. A new window is displayed (see below).

      Instead of pressing the enter key, <Ctrl><RightArrow>, <Ctrl><Enter> or
      <Ctrl><LeftArrow> increase or decrease the current setting respectively
      by one (for the hurried user).

       List:                                       Radio buttons:
       ÉÍ[þ]ÍÍÍÍÍÍÍÍ Typematic Rate (Chars/Sec)    ÉÍ[þ]ÍÍÍÍ Typematic Rat
       º                                           º
       º   ¯Options                 Bits           º   ¯Options
       º     30.0             <     00000011       º    ¯(x) Disabled®
       º     26.7             ±    À00011111Ù      º     ( ) Enabled
       º     24.0             þ                    º
       º    ¯21.8            ®±              [     º
       º     20.0             ±                    º
       º     18.5             ±              [     º
       º     17.1             ±                    º
       º     16.0             ±              [     º
       º     15.0             >                    º
       º                                     [     º
       º                                           º
       ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ    ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ

      Marked below `Options' or `Setting' is the current setting. To change
      the setting, scroll the list or press the appropriate button.

      The `Bits' field shows you which bit mask corresponds to the selected
      setting. Listed below the bit field are once again the bits that can be
      affected by the option.

      `Save' copies the changed setting into the program copy of CMOS RAM
      (use Save Changes and Quit to make the change permanent), `Cancel'
      cancels the operation.

      Caution: Some settings are `Reserved' or `RESERVED'. Do consider
      whether you really want to set an option to `Reserved'. For safety
      reasons, these changes have to be confirmed.

      `BIOS help': Sometimes, the BIOS ROM has an own (English) help text to
      the respective option. You can view this text using `BIOS help', e.g.:

       ÉÍ[þ]ÍÍÍÍÍÍÍÍÍ BIOS help ÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       ºThe base address changes in           º
       ºsteps of 16k and 512k                 º
       ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      `Reference': Registered users can look up explanations to the setup
      options (only one in five explanations will be shown to unregistered
      users).

      Options that are controlled entirely by the BIOS (these usually change
      more than eight bits and are marked with a `+') display a window
      containing the buttons `® < > ¯'; you can also use (<Ctrl>)<RightArrow>
      and (<Ctrl>)<LeftArrow>. The buttons `® ¯' are intended for fast
      leafing and don't work on all machines. On some machines, a window
      appears after pressing `® < > ¯'. Here you can enter data - this input
      window is controlled by the BIOS, so mouse input and function keys are
      disabled.

      Setting controlled by BIOS:
       ÉÍ[þ]ÍÍÍÍÍÍÍÍ Non-Cacheable Block-0 Base ÍÍÍÍÍÍÍÍÍÍÍÍ»
       º                                                    º
       º                                                    º
       º                                                    º
       º                                      [BIOS help]   º
       º   Setting                                          º
       º   _0 KB_______________________       [Reference]   º
       º                                                    º
       º    [ ® ]  [ < ]  [ > ]  [ ¯ ]        [  Save   ]   º
       º                                                    º
       º                                      [ Cancel  ]   º
       º                                                    º
       º                                      [  Help   ]   º
       º                                                    º
       ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      Note that some options affect each other!


      3.4.3 Change register
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      You may not be able to set the CMOS the way you want from the
      `Extended/Chipset Setup' menu. In this case, you can make the change
      manually.

      Caution: Use this function only if you are absolutely, positively sure
      about what you're doing!

      First, you have to enter the register number in hexadecimal and then
      the new value.


      3.4.4 Password
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      This function enables you to display the current CMOS password and to
      change it.

      This password can be called for at system boot or when entering the
      ROM setup.

             ÉÍ[þ]ÍÍÍÍÍÍÍÍÍÍ Password ÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
             º                                      º
             º Current password is `AMISET'.        º
             º                                      º
             º                                      º
             º                                      º
             º  [Change]    [Cancel]    [ Help ]    º
             º                                      º
             ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

             ÉÍ[þ]ÍÍÍÍÍÍ Change password ÍÍÍÍÍÍÍÍÍÍÍ»
             º                                      º
             º  New password: FIDO__                º
             º                                      º
             º                                      º
             º                                      º
             º  [  OK  ]    [Cancel]    [ Help ]    º
             º                                      º
             ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      Caution! If you use a foreign language keyboard (i.e. non-USA),
      note that no foreign keyboard support is loaded at boot time.
      Example: On German keyboards, `Z' and `Y' are reversed.

      Often you can enable the US-American keyboard by pressing
      <Ctrl><Alt><F1> and then test which keys are which. Use <Ctrl><Alt><F2>
      to re-enable the foreign keyboard.

      On some machines the password function has to be activated by the
      `Password' option in `Extended/Chipset Setup'.

      CAUTION! If you set the `Password' option to `Always', you cannot
      boot your machine if you forget the password!

      Hint: Try the setting `Setup' first.


      3.4.5 Load ROM Setup Defaults, Load ROM Power-On Defaults
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      There are two tables of predefined CMOS settings in the ROM. One of
      those, the `power-on defaults' is used to eliminate all possible
      hardware problems; thus the processor is switched to low speed, the
      cache is turned off, etc. Using `power-on defaults', the machine should
      boot in any case.

      Using this function, you can load a predefined configuration or simply
      view it for reference purposes, since all settings will be written to
      the program copy of CMOS RAM first and only be saved if you use `Save
      Changes and Quit'.


      3.4.6 Print current setup
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      With this function, you can print the current settings of the program
      copy of CMOS RAM.

       º  Format                             º
       º   (x) Standard (current/possible)   º
       º   ( ) Alternate (current bin&hex)   º

      First the settings of Standard setup will be printed; then, a list:

      Standard: The list is formatted as follows:

                   Option             ³ Current  ³ Possible settings
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
         Typematic Rate Programming   ³ Enabled  ³ Disabled
         Typematic Rate Delay (msec)  ³ 250      ³ 500 750 1000
         Typematic Rate (Chars/Sec)   ³ 24.0     ³ 30.0 26.7 21.8 [...]
       ¨ Mouse Support Option         ³ <1>      ³
       þ Above 1 MB Memory Test       ³ Disabled ³ Enabled
       ùùù

      `Margin' (61-254) is the maximum width of the list. `Possible settings'
      will be truncated to `[...]' if exceeding the maximum width.

      Alternate: The list looks as the list displayed in Extended/Chipset
      Setup. `Margin' is ignored.

                   Option             ³Register³Bits ³ Current setting
       ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÁÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
         Typematic Rate Programming   ³ 13  10000000 ³ 10000000  Enabled
         Typematic Rate Delay (msec)  ³ 13  01100000 ³ 00000000  250
         Typematic Rate (Chars/Sec)   ³ 13  00011100 ³ 00010000  15
       þ Mouse Support Option         ³ 11  10000000 ³ 10000000  Enabled
       ùùù

      Hint: If you disable `þ' and `¨' under `System|Options', you can create
      a list of those settings that can be changed from the ROM setup. For
      example, you could distribute this list to your customers as a
      reference.


      3.4.7 Print Reference Manual
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      This function prints a personal BIOS manual (the unregistered
      version prints only one in five explanations).

      Please read the license restrictions!


      3.4.8 Analyze BIOS ID
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      This function explains the meaning of the BIOS ID string displayed
      in the lower left corner.

      Note: The information determined by AMIsetup is not always 100 per cent
      correct, since not all manufacturers adhere to the standard (this is
      especially true for `Required processor').

      The ID string displayed at boot time shows the keyboard controller
      revision level in addition to the information displayed by
      AMIsetup (see also `Diagnostic|Keyboard controller')

      Example: 30-0201-ABCDEF-00101111-050591-OPWB-KF, where F is the
      revision level.

           ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ Analyze BIOS ID string ÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
           º                                                      º
           º  30-0201-ABCDEF-00101111-050591-OPWB                 º
           º  23H-0-0000-00-00-0000-00-00-000                     º
           º  23H-1-0000-00-00-0000-00-00-00-2                    º
           º                                                      º
           º  Required processor:   386                OK    Ü    º
           º  BIOS size:            64 KB           ßßßßßßßßßß    º
           º  Version:              2.01                          º
           º  Reference number:     ABCDEF           Print   Ü    º
           º  BIOS date:            05/05/91        ßßßßßßßßßß    º
           º  Chipset ID:           OPWB                          º
           º  Clock switching pin:  23                Help   Ü    º
           º  Cache control pin:    23              ßßßßßßßßßß    º
           º  BIOS modified flag:   02                            º
           º                                                      º
           ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼

      Use `Print' to print the information or to write it into a file.


      3.4.9 Save Changes and Quit
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      Not until you use this function will changes be made permanent. `Save
      Changes and Quit' writes all CMOS settings from the program copy of
      CMOS RAM into the real CMOS RAM and exits setup.

      If `System|Options', `Enable reboot' is enabled, you will be asked
      whether you  want to reboot your computer (cf. `Reboot').


      3.4.10 Exit without Saving
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      Quits setup without changing the CMOS RAM.



      3.5 Tools menu
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

       Tools
      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
      ³ Create BIOS image...       ³ 3.5.1
      ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
      ³ Print CMOS RAM contents... ³ 3.5.2
      ³ Clear CMOS RAM             ³ 3.5.3
      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

      3.5.1 Create BIOS image...

        Using this function, you can create a `BIOS image' file. This file is
        necessary mainly for diagnostic purposes.

        To create a `BIOS image' file, do the following:

        1. Select and execute `Tools|Create BIOS image' and enter a file name
        (e.g. `ETEQ.ROM' and a description (e.g. `ETEQ-386 baseboard').

        2. Select `Protected Mode' as BIOS source.

      3.5.2 Print CMOS RAM contents...

        Prints the CMOS RAM contents and is used for diagnostic and reference
        purposes only. To get a readable, plain English print, use
        `Setup|Print current setup'.

        Data is written in the following format:

         Reg ³ Current value
         ÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
          00 ³ 13  00010011
          01 ³ 23  00100011
         ...    ...
          7E ³ 00  00000000
          7F ³ 00  00000000

        Opposite to the register number (hexadecimal), the current value is
        printed in hexadecimal and binary format.

      3.5.3 Clear CMOS RAM

        Caution: This function erases the complete CMOS RAM contents,
        including checksums, date/time, hard disk parameters, etc. Please
        make a paper backup of your configuration before clearing the CMOS
        RAM!


      3.6 Help menu
      ÄÄÄÄÄÄÄÄÄÄÄÄÄ

        Help
      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
      ³ About AMIsetup...  Shift-F10 ³ 3.6.1
      ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
      ³ Contents                     ³ 3.6.2
      ³ View AMISETUP.DOC            ³ 3.6.3
      ³ Help about registering...    ³ 3.6.4
      ³ Print order form...          ³ 3.6.5
      ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
      ³ On-line reference            ³ 3.6.6
      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

      3.6.1 About AMIsetup

        Shows a dialogue box containing program revision and registration
        number (or `Unregistered Shareware').

        If you haven't yet paid for AMIsetup and a registration number
        appears anyway, you've got an (illegal) pirated copy. Please contact
        the author.

      3.6.2 Contents

        Gives an overview about on-line help.

      3.6.3 View AMISETUP.DOC

        You can view AMISETUP.DOC without leaving AMIsetup. It is necessary
        that AMISETUP.DOC be installed in the same directory as AMISETUP.EXE.

      3.6.4 Help about registering

        See Appendix A.

      3.6.5 Print order form

        To order AMIsetup, you can print an order form to the printer or
        to a file.

      3.6.6 On-line reference

        AMIsetup contains explanations of approx. 200 of the most widespread
        setup options (unregistered users will see only one in five
        explanations).

        Select `On-line reference', and the index is displayed.

        Next, you can mark one of the bold terms using <Tab> or the mouse and
        get a closer explanation. The cursor keys are for scrolling.


      4 Key shortcuts
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      <F1>         Help
      <Alt><F3>    Close active window
      <F5>         Zoom active window
      <Ctrl><F5>   Move active window (Cursor keys)
                   Change window size (<Shift>+Cursor keys)
      <F9>         Start Setup
      <F10>        Activate main menu
      <Shift><F10> Show program information
      <Alt><X>     Exit Setup or program
      or <Alt><F4>

      NB:  <>            = <Shift>
           <Return>, <Ù> = <Enter>
           <>            = <Tab>


                                   A P P E N D I X
                                   ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      A  Registration
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      Thank your for trying the shareware version of AMIsetup. The shareware
      version is lacking some features of the registered version.

      You may test the shareware version thoroughly for 30 days. You may
      copy it and share it with your friends.

      The author makes no money out of the shareware version - if you paid
      for it, the payment only covers the shareware vendor's cost of copying
      and shipping the software.

      If you'd like to purchase the latest registered version, which includes
      the complete feature set and does not display this message, please
      print the order form using `Help|Print order form'.
      Only the registered version entitles you to use the program for more
      than 30 days.

      If you do not like the program contrary to expectations, just delete it.
      But maybe you'd like to suggest a future improvement first, so that the
      author will be able to fit the program to your needs.

      See the registration form for the registration fee valid for your
      country (DM 40.- to DM 55.- depending on the country).

      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
      ³ Please use the form `REGISTER.FRM' included with this program.    ³
      ³ You can print it using `Help|Print order form' directly from      ³
      ³ AMIsetup.                                                         ³
      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

      Japanese users: Please print the file REGISTER.JPN instead.

      Commercial users in the European Union ONLY: Please provide your
      VAT registration number and save 15% VAT!

      Send DM Eurocheques (other cheques: add DM 10.-), cash or postal
      money order to the following address:


      How to Contact the Author
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      Please address all correspondence to:

        Robert Muchsel
        Hegaublick 2
        D-78465 Konstanz
        Germany

        Fax: +49-7533-3151

        Electronic Mail (this is a lifetime address):
          Internet:   muchsel@acm.org
          CompuServe: >INTERNET:muchsel@acm.org


      Upgrades
      ÄÄÄÄÄÄÄÄ

      If the user has a modem, upgrades are free. Other registered users
      only have to pay the fee of their shareware vendor.

      Upgrades will not be free if
      - there are too many illegal pirated copies
      - there are major enhancements

      Read README.!!! on your registration diskette for more information.


      The Author
      ÄÄÄÄÄÄÄÄÄÄ

      ...studies Computer Science at the ETH (Swiss Federal Institute of
      Technology) in Zurich/Switzerland (this is the explanation of the
      `Additional contributions' field on the order form).



      B  AMIsetup and OS/2, Windows, Windows NT
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ


      OS/2 Versions 2.1, 2.11, 3
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
      The program will run in a DOS session of OS/2. Some closely hardware
      related functions will be disabled to preserve system integrity.


      OS/2 Version 2.0
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
      The program will not run in a DOS session of OS/2 2.0, not even in a
      DOS image (VDM). Write accesses to the CMOS RAM are redirected to a
      buffer by OS/2, which is discarded when exiting the virtual machine
      (source: `Redbooks, Vol. 2: DOS and Windows-Environment, Virtual CMOS
      Device Driver'; IBM Document Number GG24-3731-00).


      OS/2 in General
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
      An OS/2 version of AMIsetup is impossible, since AMIsetup directly
      executes code of the real mode BIOS.

      If you create a DOS boot disk and copy AMIsetup as well as a disk
      editor there, then you've got a sort of `emergency disk'.

      AMI BIOS and OS/2
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ
      There are NO general problems with OS/2 and the BIOS versions supported
      by AMIsetup. OS/2 runs with BIOS versions PRIOR to 05/05/91 and with
      keyboard controller revision -K8.

      However, problems might arise e.g. when using faulty memory chips, too
      low refresh rates, wrongly installed cache memory, faulty EIDE chips
      (on PCI boards) or wrong bus clock. Because of the protected mode
      architecture, OS/2 is much more sensitive to errors than DOS software,
      which often ignores or doesn't even notice them.


      Windows
      ÄÄÄÄÄÄÄ
      Running AMIsetup under Windows is not recommended.
      The icon file, AMISETUP.ICO, contains an OS/2 icon which cannot
      be displayed under Windows.


      Windows NT
      ÄÄÄÄÄÄÄÄÄÄ
      The Windows NT DOS emulator is not compatible with AMIsetup.


      C  Trouble shooting
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      1. Is AMIsetup compatible with your BIOS?

      For technical reasons, AMIsetup only works with two generations of
      the AMI BIOS, the so-called `Hi-Flex BIOS' and `WinBIOS'. Both versions
      are manufactured by `American Megatrends, Inc.' (`AMI'). This you can
      see when powering on your computer.

      Currently, AMIsetup does not support the AMI-BIOS on later Intel
      baseboards (Plato, Endeavour, Premiere, Batman, etc.).

      Example of a power-on screen on HighFlex or WinBIOS:

       ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
       ³ 05/05/91(C)1990 American Megatrends Inc., All Rights Reserved ³
       ³                                                               ³
       ³ (C)1990 American Megatrends Inc.,                             ³
       ³                                                               ³
       ³                                                               ³
       ³                                                               ³
       ³                                                               ³
       ³                                                               ³
       ³                                                               ³
       ³                                                               ³
       ³ 30-0101-ABCDEF-00011001-050591-FORX                           ³
       ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

      The HighFlexBIOS has three levels of setup (`Standard', `Advanced' and
      `Advanced Chipset'), `Password' and `Hard Disk Utility'.

       ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
       º          BIOS SETUP PROGRAM-AMI BIOS SETUP UTILITIES         º
       º    (C) 1990 American Megatrends Inc., All Rights Reserved    º
       ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
       º                                                              º
       º                     STANDARD CMOS SETUP                      º
       º                     ADVANCED CMOS SETUP                      º
       º                   ADVANCED CHIPSET SETUP                     º
       º            AUTO CONFIGURATION WITH BIOS DEFAULTS             º
       º          AUTO CONFIGURATION WITH POWER-ON DEFAULTS           º
       º                       CHANGE PASSWORD                        º
       º                      HARD DISK UTILITY                       º
       º                    WRITE TO CMOS AND EXIT                    º
       º                DO NOT WRITE TO CMOS AND EXIT                 º
       º                                                              º
       ÌÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¹
       º                                                              º
       º  Standard CMOS Setup for Changing Time, Date, Hard Disk, etc.º
       º                                                              º
       ÈÍÍÍÍÍµ ESC:Exit |-|-:Sel F2/F3:Color F10:Save & Exit ÆÍÍÍÍÍÍÍÍ¼

      Older, custom-made BIOS versions are NOT compatible with AMIsetup, even
      though they are from AMI. These have a so-called `XCMOS Setup' (and they
      are black & white).

      The setup built into the WinBIOS has Windows-like icons and should be
      easily recognized.


      2. Frequent errors with compatible BIOS versions

      The BIOS source is not correctly set. Verify that the BIOS source under
      `System|Options' is set to `Protected Mode'.

      3. Stopgap: -O

      As a last resort you can start the program with the command-line option
      `-O' (CAPITAL letters). This option disables all error messages; faulty
      operation or a locked-up computer may result, though.

      4. Additional trouble shooting options

      If the program hangs when you start the `Extended setup', you may want
      to try the command line argument `-N'.


      D  Glossary
      ÄÄÄÄÄÄÄÄÄÄÄ

      Some frequently used abbreviations and terms (explanations for setup
      options only on-line):

      AMI
        American Megatrends Inc., a BIOS manufacturer

      BIOS
        Basic routines contained in a nonvolatile memory (ROM) of the PC
        which e.g. drive the hard disk, but are also needed for system boot
        and system setup.

      BIOS Checksum
        The AMI BIOS calculates a 16 bit checksum (addition w/ overflow) over
        the BIOS ROM. If this checksum is 0, it is assumed that the BIOS
        is OK.

      CMOS RAM
        This chip can be read from and written to; unlike normal memory the
        contents are buffered by a battery or an accumulator after turning
        off the PC. CMOS RAM contains data like type of installed floppy
        disk drives, the time, etc.

      CMOS RAM Checksum
        A checksum is calculated for parts of the CMOS and stored in CMOS.
        If checksum and CMOS RAM contents differ, either the battery is
        defect or the CMOS RAM contents are invalid. In any case you must
        reenter the data, possibly replace the battery or accumulator,
        too.

      EISA
        See appendix H.

      Extended Character Set, Graphic characters
        Characters like „”� or æþ¨. Some printers cannot print these.

      NVRAM
        See appendix H.

      Precompensation
        Precompensation is used with some hard disks to compensate for the
        higher recording density in the inner tracks during write.
        Normally, precompensation and reduced write current begin
        approximately at half the cylinder count. The precompensation
        logic shifts certain bit patterns by +/- 12-15ns.
        Precompensation only affects writing, not reading of data.
        Many hard drives work perfectly with or without precompensation,
        newer hard disks ignore the setting (you should turn it off then).

      ROM
        Read Only Memory - memory that can only be read from and not
        written to.


      E  If the machine won't boot...
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      If the setup has been altered so that the PC doesn't even display
      `Press <DEL> for Setup', some models have the following possibilities:

      1. On newer models, you can press <Ins> while powering on. All
         settings will be reset to standard values.

      2. On many machines there is a jumper on the main board which you can
         use to erase CMOS RAM. Sometimes this takes several hours.

      3. Often there is the possibility of connecting an external battery
         pack. To install it, you have to remove a jumper residing on a
         4 pinned connector. This jumper does the same as (2).

      4. Only when encountering password errors and only with BIOS from
         12/12/91 on: Pin 32 of the keyboard controller can be grounded
         to erase the password.

      Please note that after these steps all configuration data must be
      reentered. Make certain that you set the correct hard disk parameters!
      If you are not a hardware expert, you should contact your dealer first
      before destroying your hardware by wrong handling!


      F  Switching to the English user interface
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      If you have installed the German version and want to switch,
      do the following:

      Disable `German language' or `Deutsche Oberfl„che' under
      `System|Options'. Select OK, exit and restart AMIsetup.


      G  Soundblaster
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      To make the monotonous task of setting up computers a little more fun,
      AMIsetup supports the Soundblaster audio card (by Creative Labs).
      Soundblaster support must be explicitly enabled (AMIsetup is, after
      all, a serious program).

      - Turn on `Soundblaster' under `System|Options' (default: OFF)

      - The environment variable `BLASTER' must be set correctly, e.g.: SET
      BLASTER=A220 I5 D1

      The BLASTER variable has the following meaning:

       A220 : Port address of Soundblaster card
       I5   : IRQ (Interrupt) level
       D1   : DMA channel

      (all other settings, e.g. T4, will be ignored)

      If the variable is NOT set, the default values A220 I7 D1 will take
      effect.

      Note: The program could crash if a wrong DMA channel is given!

      - You must have the VOC files. To save disk space and transfer time,
      the unregistered version contains only a small subset of the files.

      All versions include:

       ERROR.VOC    - Replaces the error beep

      In addition, the registered version is shipped with:

       CONFIRM.VOC  - Confirmation
       COPYRIGH.VOC - About AMIsetup
       ERRORBOX.VOC - Error
       EXIT.VOC     - Program exit
       WARNING.VOC  - Warning

      Not included:

       HELP.VOC     - Help


      AMIsetup has its own, built-in Soundblaster driver. This built-in
      driver should work with all Soundblaster and compatible cards with DSP
      level 1.05 and higher.

      If the driver CTVDSK.DRV is included with your Soundblaster card,
      AMIsetup can use it and adapt itself to the special features of your
      card (e.g. Stereo sound).

      AMIsetup looks for CTVDSK.DRV in the following directories:

      1. in the current directory

      2. in the directory of AMISETUP.EXE

      3. in the subdirectory `DRV\' of the directory specified by the
      environment variable `SOUND'

      4. in the subdirectory `DRV\' of the directory specified by the
      environment variable `CPSPRO4'

      5. in the PATH

      The built-in driver will only be activated if CTVDSK.DRV cannot be
      found.

      You can delete single VOC files and the corresponding action will be
      `quiet'.

      You can replace these files with files from your own sound collection.

      AMIsetup can play files any size you want; if disk activity is too
      heavy, you can increase the replay buffer which defaults to 4*4 KB.
      Set the DOS enviroment variable SBBUF to the desired value.

      Example: SET SBBUF=16 -> replay buffer will be set to 4*16 KB.

      All sounds are turned off immediately when the corresponding action is
      aborted/finished.

      If the program hangs when you activate Soundblaster support, you can
      force the program to use its built-in driver. Type `SET SOUND=' at
      the DOS command prompt.

      If you cannot get sound support to work at all, don't be sad -
      AMIsetup's real functionality will not be affected by this gadget.


      H  EISA
      ÄÄÄÄÄÄÄ

      EISA is an `Extended' and faster bus architecture found in better
      machines. AMIsetup tells you whether you have a standard ISA, a
      PCI or EISA system.

      On some EISA computers, parts of the setup data are stored in the
      EISA NVRAM (Non Volatile RAM). On these machines, AMIsetup needs to
      access the NVRAM. On others, AMIsetup doesn't need to know about EISA
      NVRAM and simply ignores it.

      Since EISA NVRAM access is chipset dependent, AMIsetup uses EISA.CFG
      (see EISA.CFG for explanation of the syntax).

      If AMIsetup detects an EISA system and EISA.CFG contains valid
      data, `Backup³Save EISA NVRAM...' and `Backup³Restore EISA
      NVRAM...' are automatically enabled. Setup registers 40h to 7F are
      mapped into the EISA NVRAM.

      However, it is possible that AMIsetup doesn't know about YOUR
      particular EISA computer and displays `The BIOS register table
      contains invalid entries!'. Please mail a copy of your BIOS.DAT,
      CMOS.SAV and EISANVR.SAV (if available). EISA.CFG can then be extended
      to include your computer.


      I   Batch mode
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      You can use AMIsetup in batch mode. This is especially useful if you
      - want to configure several identical machines (you don't have to use
        time consuming ECU, CMOS setup any more!)
      - want to document CMOS settings and/or save CMOS/EISA NVRAM
        automatically

      The batch mode of AMIsetup understands the following commands:
        -SAVE:CMOS:FILENAME          Save CMOS RAM into FILENAME.
        -SAVE:EISA:FILENAME          Save EISA NVRAM into FILENAME.
        -RESTORE:CMOS:FILENAME       Restore CMOS RAM from FILENAME.
        -RESTORE:EISA:FILENAME       Restore EISA NVRAM from FILENAME.
        -PRINT:DEVICE                Print setup to DEVICE.
        -PRINT:ALT:DEVICE            Print setup (alternate style) to
                                     DEVICE.

      Examples:
        You want to save CMOS & EISA NVRAM in a file:
          AMISETUP -SAVE:CMOS:CMOS.BIN
          AMISETUP -SAVE:EISA:EISA.BIN
        And now configure several more machines with the same settings:
          AMISETUP -RESTORE:CMOS:CMOS.BIN
          AMISETUP -RESTORE:EISA:EISA.BIN
        Finally, print setup to a parallel printer:
          AMISETUP -PRINT:LPT1


      J   Obtaining new or bug fixed program revisions
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      There are lots of different BIOS/chipset combinations out there.

      If the program doesn't work with your machine, please do the
      following:

      1. Read the manual, especially appendix C (you did, didn't you?).

      2. Use the latest version of the program only. You can get it from
         your shareware vendor or, if you have a modem, from the mccs BBS
         in Singen/Germany.

         mccs BBS Singen/Germany (Sysop Martin Grass, Fido 2:246/8100-8104)

         Line 1: Phone +49-7731-65833

         FidoNet users: Request the file using the `magic' name AMISETUP.

         Others: Please log in as `GAST', password `GAST' and download
         AMISETUP directly from the main menu.

         You can also get the AMIsetup shareware from the Internet.
         SimTel ftp server and its mirrors (e.g. nic.switch.ch) carry the
         latest version in the directory msdos/sysutl.


      3. ONLY if the latest version doesn't work and you are sure it should
         work (appendix C!):

         Send a BIOS image and a CMOS RAM image produced by AMIsetup to
         the author.

         Please follow the instructions in the manual; ensure that NO
         memory manager is loaded.


         Thank you.


      K   Tested BIOS revisions
      ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ

      Among others, the program has been successfully tested on the
      following chip set/BIOS combinations (the list was generated
      automatically):

        Chip set ID- BIOS Date

        4X521      - 04/04/93
        80486      - 07/07/91
        80486      - 12/15/93
        80X86      - 06/06/92
        ACC2046    - 06/06/92
        ACC2046    - 12/12/91
        ACER1217   - 07/07/91
        ALI1419    - 12/12/91
        ALI1429    - 08/08/93
        AMI/S50    - 12/12/91
        AMI/S61    - 12/12/91
        BENG386    - 12/12/91
        BENG486    - 12/12/91
        CAESAR     - 07/07/91
        CTQ386&486 - 12/12/91
        CTQ596     - 06/06/92
        ET/386H    - 02/02/91
        ET/486H    - 05/05/91
        FORX       - 05/05/91
        FORX       - 07/07/91
        ITOPDX     - 05/05/91
        MERCISA    - 12/15/93
        NxVL       - 11/11/92
        O546822    - 06/15/94
        O546822    - 07/25/94
        OP802G     - 12/15/93
        OPEISA     - 12/12/91
        OPT4 498   - 06/06/92
        OPT495SX   - 11/11/92
        OPTI597    - 08/08/93
        OPTI802    - 07/25/94
        OPTi895    - 12/15/93
        OPTIEISA   - 07/07/91
        OPWB       - 05/05/91
        OPWBSX     - 06/06/91
        OVIPER     - 10/10/94
        PCI82420   - 01/25/94
        PCI82430   - 04/06/94
        PCI82430   - 06/16/94
        PEAKDM_B   - 05/05/91
        PICO168    - 06/06/92
        SATURN     - 08/08/93
        SATURN_1   - 12/15/93
        SHASTA     - 11/11/92
        SIS-EISA   - 06/06/92
        SIS-EISA   - 12/12/91
        SIS3486    - 06/06/92
        SIS3486    - 11/11/92
        SIS401     - 08/08/93
        SIS461     - 08/08/93
        SIS471     - 07/25/94
        SIS471     - 12/15/93
        SIS471G    - 07/25/94
        SIS486     - 07/07/91
        SIS496AB   - 07/25/94
        SIS50X     - 07/25/94
        SIS550X    - 07/25/94
        SISD       - 07/07/91
        SISEISA    - 06/06/92
        SUMMIT_C   - 12/12/91
        SYM-486    - 05/05/91
        SYM486B    - 07/07/91
        SYMP       - 03/15/91
        SYMP       - 05/05/91
        SYMP       - 12/12/91
        SYM_386B   - 05/05/91
        TIEISA/S   - 12/12/91
        TOPCATSX   - 05/05/91
        U4800VLX   - 11/11/92
        UMC480     - 06/06/92
        UMC480     - 11/11/92
        UMC480B    - 11/11/92
        UMC491C    - 04/04/93
        UMC491f    - 04/04/93
        UMC498     - 07/25/94
        Ver1.00    - 06/06/92
        Ver1.01    - 06/06/92
        VIAEISA    - 06/06/92
        VIPER      - 10/10/94

      10/01/1995