INTRODUCTION TO OCTAMED PLAYER ROUTINES
=======================================

This drawer contains the material, which is required for using OctaMED
music in your own programs. You are allowed to freely use these routines in
your own non-commercial programs. For commercial products, you will have to
licence the routines. (See the files ReadMe.doc and Licence.doc for the
details.)

You have basically two choices - you can either incorporate the player
routine (written in assembler) to your program, or you can use the provided
external player libraries.

1. Embedded player routines (proplayer/pro8player)

These are the most often used routines. They are usually the best choice
for embedded game music, module player programs etc. Easy switches are
provided for turning off unnecessary features. As the assembler source is
provided, you can modify the code or add hooks to suit your specific
purpose. The rest of this document contains instructions for the proplayer
routines.

2. Player libraries (medplayer.library/octaplayer.library)

These are shared libraries that any application program may call. (Only one
task can be using them at a time, though.) The libraries contain basically
the same functionality as proplayer routines, but no tailoring can be made.
An obvious advantage is that library upgrades are transparent to your
application. The user can simply replace the libraries. See the file
Library.doc for details on using the libraries.

Note: medplayer.library and octaplayer.library are located in the LIBS
drawer of OctaMED_Disk_2.

Note: If you need a feature that currently does not exist, send us your
exact requirements, and we'll do our best to help you.

    Instructions for using "proplayer.a", the stand-alone playroutine.
===========================================================================

"proplayer" is a piece of code which is linked with your program and plays
MED and OctaMED modules.

"proplayer" contains the following routines:
	InitPlayer
	RemPlayer
	PlayModule
	ContModule
	StopPlayer
	SetTempo

The arguments are passed in registers, and return values are returned in d0.
These routines will trash registers d0-d1 and a0-a1.

And now the descriptions of each one:
~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
InitPlayer -- initialize everything

Before you can call the other functions, you must call this function.
It allocates the audio channels, timer, serial port (if MIDI) etc...

ARGUMENTS:	none

RETURNS:	0 if everything is ok, otherwise something failed.
		If something failed, you can still call the other
		routines - they just don't do anything.

~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
RemPlayer -- return everything back

Call this when your program exits. It frees the audio channels, timer,
serial port etc.

ARGUMENTS:	none

RETURNS:	nothing

~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
PlayModule -- start playing a module

When you want to start playing, call this routine.

ARGUMENTS:	a0 = pointer to the module. See below for instructions
		how to obtain the pointer.

RETURNS:	nothing

~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
StopPlayer -- stop playing

ARGUMENTS:	no arguments

RETURNS:	nothing

~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
ContModule -- continue playing

This routine continues playing the module from the point it was stopped.

ARGUMENTS:	a0 = pointer to the module

RETURNS:	nothing

~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
SetTempo -- set the playback tempo

(This routine has not much use.)

ARGUMENTS:	d0 = new tempo (1 - 240)

RETURNS:	nothing

~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~

"proplayer.a" is the source code of the music routine. It contains stuff
that may be unnecessary for your purposes, just taking time and memory.
There are some "switches" at the beginning of the source, that allow you
to turn off features you don't need. They are:

MIDI		If only the Amiga audio channels are used, set this to 0.
AUDDEV		For some purposes, you may want to disable the code that
		allocates the audio channels using "audio.device", e.g.
		in a non-multitasking environment. Normally this should
		be 1.
SYNTH		If synth/hybrid sounds are not in use, this can be set to
		zero.
CHECK		This does some checkings to ensure that several values are
		correct (e.g. is the sample in memory, no Amiga effects on
		MIDI-tracks etc..). If you know that the song is correct,
		you can safely turn the checks off.
RELVOL		If you don't need the "relative volume", this can be zero.
IFFMOCT		If the song doesn't contain multi-octave IFF samples
		this can be zero.
HOLD		This turns off the hold/decay features.
PLAYMMD0	If set, the play routine will also handle old MMD0 type
		modules. Useful for player programs.
AURA		Aura output can be enabled by using this flag. (The file
		"aura.a" must exist.)


There's an additional flag, EASY. If set, the usage of the player routines
is even more simplified, and you enter the module name into an INCBIN
statement. There are two routines (_startmusic, _endmusic) you call
to start and stop the music (the music can be started ONLY ONCE). The
EASY option is suitable for demos etc. where only a single tune is
required.

"proplayer.a" also supports multi-modules. It defines a UWORD modnum
(in assembler: _modnum). Set this variable to the number of the song
you want to play before calling PlayModule (0 is the first, 1 is the
second song etc..). For example:
	#include "proplayer.h" /* defines 'modnum' */
	...
	modnum = 1; /* Play the second module */
	PlayModule(module);
	...
Assembler:
	xref	_modnum
	xref	_PlayModule
	...
	move.w	#1,_modnum
	lea	_module,a0
	jsr	_PlayModule(pc)
	...

Timing
======
If you need vertical blanking timing, you can set VBLANK to 1 and CIAB to 0.
In normal use this is not recommended (because of the 16 % difference in
playing speed with NTSC and PAL Amigas), but if tight synchronization to
vertical blanking (e.g. in most demos/games) is required, VBLANK can be
used.

For VBlank timing, the song has to be composed with primary tempo of about
33. The primary tempo cannot be changed with command F. Only the secondary
tempo control can be used (command 9).

Assembling
==========
"proplayer.a" can be assembled by using HiSoft's Devpac Assembler without
changes. Other assemblers may need some small changes to work correctly
(mostly because the directives they support may be slightly different). If
you're working on a linker environment (e.g. programming in C), you've to
include the resulted "proplayer.o" in your .lnk-file.

===========================================================================

And how to get some music?

You have two ways to get the music:
1. Include the module in your final executable.
2. Save the module as a separate disk file and load it when needed
   (this is probably the best way if you have more than one song, and
    you don't want to use multi-modules).

First I cover the first method:
~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
Including the module in your final executable:

There's a utility, Objconv, which loads the module and dumps it into an
object file. Here's an example how to use it:

- Assemble 'reloc.a' to 'reloc.o'.
- Save the song as a module
- Use Objconv e.g. objconv medmodule mod.o
- Objconv requests the symbol name, enter "song" (without "'s), for example.
- Now there's a file 'mod.o'. Link this file, and the file 'reloc.o'
  with your program.
- In your program, you define the module:
	#include "proplayer.h"
	...
	extern struct MMD0 far song;
  You must relocate the module before it's used. Do this only once!
  This is done by
	RelocModule(&song);
  RelocModule expects the argument in stack, so use __stdargs, if you've
  turned registerized parameters on.

In assembler, you'd do exactly in the same way, except:
	xref	_song
	xref	_RelocModule
	xref	_PlayModule

	... (assuming all init stuff is here)

	lea	_song,a0
	move.l	a0,-(sp)	;push into stack
	jsr	_RelocModule(pc)
	addq.l	#4,sp		;reset stack pointer
	lea	_song,a0	;this is passed in register a0
	jsr	_PlayModule
	...

Note: if you've got an assembler that supports 'incbin' directive or
equivalent, you can use it instead of Objconv. Relocation is required in
any case.

And the second method (loading modules from disk):
~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
File "loadmod.a" contains three routines:
	LoadModule
	UnLoadModule
	RelocModule

You usually need only the first two of them. RelocModule is used by
LoadModule.

~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
LoadModule -- loads a module from disk

This function loads a module from disk. Note that relocation is done
automatically, so you must not RelocModule() a module obtained by using
this routine.

ARGUMENTS:	a0 = pointer to file name

RETURNS:	d0 = pointer to the module, if something failed: 0

~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~
UnLoadModule -- free the module from memory

Frees the module. Remember to StopPlayer() before you unload the module
that is currently playing. Also remember to free all modules you've loaded
before you exit the program.

ARGUMENTS:	a0 = pointer to the module (may be 0)

RETURNS:	nothing

~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~~

===========================================================================

REMEMBER:	All functions expect the arguments in registers. This is
		automatically (??) handled by you when you program in
		assembler, but it is not automatically handled when
		you're programming in C.

If you have SAS/C V5 or later, this is done automatically if you include
"proplayer.h" in all your code modules which call proplayer. If you have a
compiler which doesn't support argument passing in registers, then you have
to write the stub routines in assembler.

See also the small example sources.

===========================================================================

	pro8player.a
	~~~~~~~~~~~~

"pro8player.a" is the play-routine for OctaMED 5 - 8 channel songs. This
can be used exactly in the same way as "proplayer.a". The functions just
have slightly different names:
	InitPlayer8
	RemPlayer8
	PlayModule8
	ContModule8
	StopPlayer8
	modnum8

Note that this player have some restrictions, as opposed to "proplayer.a".
They're listed in OctaMED documents. It also takes quite a lot of processor
time, depending on how many splitted channels there are.

You can use the same RelocModule() and (Un)LoadModule() routines with
5 - 8 channel songs.

The eight channel player has a byte flag _hq (assembler)/hq (C), which
controls the HQ mode. Set this to 1 prior to calling PlayModule8 to
activate the HQ mode.

===========================================================================