ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
 º          HWiNFO ù Copyright (c)1995-99 Martin Mal¡k - REALiX(tm)           º
 º ÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ º
 º                 Version 4.5.1; Last Update: Mar-03-1999                  º
 ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼






                 ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                 ³  USE THIS PROGRAM ONLY AT YOUR OWN RISK  ³
                 ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ





  CONTENTS

    1.  Intro
    2.  Updates and download
    3.  Requirements
    4.  Utilities distributed with HWiNFO
    5.  Registration
    6.  Creating a logfile
    7.  Limitations
    8.  Running HWiNFO under V86 Memory Managers and Windows
    9.  Resetting the CPU
   10.  HWiNFO Crash
   11.  Secondary Video Info
   12.  PCI chipsets comparison
   13.  IDE Disk Transfer Modes
   14.  Miscellaneous notes
   15.  Some abbreviations
   16.  Codenames
   17.  Thanks
   18.  Disclaimer






 ## 1. Intro ##################################################################


  HWiNFO is a *POWERFUL* hardware detection program. It is simple, quick and
  on most systems very efficient. It "tries" to give only important information
  about all the hardware devices in your computer so that you need not look
  inside the PC to see what's there.




 ## 2. Updates and download ###################################################


  The newest version is always (immediately) available at:

  My homepage   - http://www.svf.stuba.sk/~malik/hwinfo.html

  SAC ftp       - ftp.elf.stuba.sk/pub/pc/utildiag
                  http://ftp.elf.stuba.sk/packages/pub/pc/utildiag
  SAC BBS       - +421 7 5438 232   (19,200 Baud)
                  +421 7 5438 295   (28,800 Baud)

  At other sitez/BBS later...
  SimTel        - ftp.simtel.net/pub/simtelnet/msdos/sysinfo
  SAC mirrors   - ftp.uakom.sk/pub/mirrors/sac/utildiag
                  ftp.intec.sk/sac/utildiag
                  ftp.vse.cz/pub/msdos/SAC/pc/utildiag
                  ftp.cs.tu-berlin.de/pub/msdos/mirrors/stuba/pc/utildiag
                  ftp-beer.bke.hu/vol1/pub/sac/pc/utildiag
                  ftp.pwr.wroc.pl/pub/pc/sac/utildiag
                  cert.unisa.it/pub/PC/SAC/utildiag
                  ftp2.itb.it/pub/PC/SAC/utildiag
                  ftp.nsysu.edu.tw/PC/SAC/utildiag
                  192.217.228.45/SAC/pub/pc/utildiag
                  ftp.comp.hkbu.edu.hk/pub/sac/utildiag
                  ftp.cdrom.com/pub/sac/utildiag




 ## 3. Requirements ###########################################################



    - 80386 or better CPU
    - cca. 400 (+50) KBytes of free System Memory
    - cca. 700 KBytes of free XMS Memory (XMS manager preferred)





 ## 4. Utilities distributed with HWiNFO ######################################


  There are four utilities distributed along with HWiNFO:

  GETBIOS.COM     This utility retrieves all BIOS images and saves them to
                  files <BIOSseg>.ROM
                  This program doesn't run in V86 mode in order to avoid
                  BIOS relocation.

  GETDDC.COM      This utility saves VESA Display Data Channel data to file
                  DDC.DAT if your video card and monitor support DDC

  GETPCI.EXE      This utility stores all data from PCI configuration space
                  registers into files <VendorID><DeviceID>.PCI

  GETPNPRS.EXE    This utility saves resource data for all Plug-and-Play
                  capable devices into files PNP<CSN>.RES

  GETPIROM.EXE    This utility gets the content of Processor Information ROM
                  (P.I.ROM) and stores into file PIROM.DAT. This feature is
                  available only on Intel Pentium(R) II Xeon(TM) Processors.


  These utilities are free and are designed to help me improve HWiNFO if
  you send me the results.




 ## 5. Registration ###########################################################


  HWiNFO is shareware, meaning that you can test the program for free whilst
  checking if it is useful for you. The public (unregistered) version has all
  the features as the registered version except the "Create report file"
  feature. The other disadvantage is the message that HWiNFO isn't registered
  and that you have to press a random key while the results are shown.

  If you think you could use this program and don't want to see that stupid
  message, or if you continue using it after a trial period of 14 days, you
  should register. Otherwise after this period HWiNFO becomes an illegal copy
  and you have to delete it (ho-ho-ho :-)).

  If you decide to register, you should print out the file REGISTER.FRM,
  fill it and send to the address in the file.

  If you include your Internet e-mail address, you will receive the
  key file via e-mail, otherwise snail mail.

  Once you have obtained the key file needed to register, copy it to the
  HWiNFO directory and the current version will become registered. Of course,
  you mat not distribute the key file, it's only for your personal use.



  Well, the Registration fee is:

                    ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍËÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
                    º  Non-Commercial  º    Commercial    º
                    ÌÍÍÍÍÍÑÍÍÍÍÍÑÍÍÍÍÍÍÎÍÍÍÍÍÑÍÍÍÍÍÑÍÍÍÍÍÍ¹
                    º DEM ³ US$ ³ Sk/KCº DEM ³ US$ ³ Sk/KCº
    ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÎÍÍÍÍÍØÍÍÍÍÍØÍÍÍÍÍÍÎÍÍÍÍÍØÍÍÍÍÍØÍÍÍÍÍÍ¹
    º 1 User        º  35 ³  20 ³  500 º  70 ³  40 ³ 1000 º
    ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ×ÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÄ×ÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÄ¶
    º 2-10 Users    º* 30 ³* 16 ³* 450 º  60 ³  32 ³  900 º per copy
    ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ×ÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÄ×ÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÄ¶
    º 11-20 Users   º* 25 ³* 13 ³* 400 º  50 ³  26 ³  800 º per copy
    ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ×ÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÄ×ÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÄ¶
    º 21-50 Users   º* 20 ³* 10 ³* 300 º  40 ³  20 ³  600 º per copy
    ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ×ÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÄ×ÄÄÄÄÄÅÄÄÄÄÄÅÄÄÄÄÄÄ¶
    º 51-100 Users  º* 15 ³*  7 ³* 200 º  30 ³  14 ³  400 º per copy
    ÇÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ×ÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÄ×ÄÄÄÄÄÁÄÄÄÄÄÁÄÄÄÄÄÄ¶
    º UNLIMITED     ºContact the authorºContact the authorº
    ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÊÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼
     * for schools, educations, etc.


  When registering with Eurocheque or bank transfer please add 10% to
  the total price to cover bank transfer costs.

  For any special requirements contact the author.

  A registration is valid for all future versions.
  And there will be a lot of newer versions of course.

  You should register NOW !






 ## 6. Creating a logfile #####################################################


  There are three possible methods how to create a logfile:

  1. Simple log
     After pressing the <F2> key, HWiNFO adds the results from current screen
     to a logfile.

  2. Report file ("-r" switch) [REGISTERED VERSION ONLY]
     HWiNFO creates AUTOMATICALLY a COMPLETE logfile at startup.
     This logfile has the same format as the one created with <F2> key, but
     there's no need to navigate HWiNFO through all the screens.

  3. Short report file ("-s" switch) [REGISTERED VERSION ONLY]
     HWiNFO creates AUTOMATICALLY a logfile, which contains only the
     MOST IMPORTANT items. This format is suitable for further automatical
     processing (or printing) of logfiles (e.g. if you would like to create
     an inventory of more machines). Here's a sample of the format:

       CPU=Intel Pentium II Xeon, 400.0 MHz
       Bus=ISA + PCI + A.G.P.
       Chipset=Intel 82440GX AGPset
       Memory=128 MBytes
       ...
       VideoChipset=3DLabs Permedia 2
       VideoMemory=8192 KBytes
       3Daccel=3Dfx Voodoo 2
       ...

  The default log filename is "HWiNFO.LOG". You can change its name if you
  enter it as a paramater to HWiNFO (e.g. "HWiNFO.EXE -r HOME.LOG").



 ## 7. Limitations ############################################################



  The Mainboard Chipset identification works only on newer (÷ 1991 and above)
  AMI and newer AWARD BIOSes. HWiNFO is also able to detect some chipsets, not
  depending on the type of BIOS (see HWiNFO.LST).


  Fixed Disk Buffered Data Transfer rate reads data from one physical sector
  until 4 seconds. Some caches (like Hyperdisk; but NCACHE or SMARTDRV don't)
  could cause invalid results. Also some mainboards, which have incompatible
  timers could cause problems.


  Fixed Disk Average Seek receives results while seeking permanently 100* from
  cylinder 0 to a cylinder, which is 1/3 of the max. cylinder number. Thus some
  programs could report another result if they seek to an another cylinder.
  SCSI disks and some Cache programs (Hyperdisk) don't generate Seek requests,
  thus the Seek and RPM result is abnormal and HWiNFO displays <N/A>.


  PCMCIA detection requires Socket Services or Card Services to be installed.
  If you want more info about sockets, install Card Services.


  The VESA Local Bus can be detected only if a VLB card is present.


  CD-ROM benchmark requires MSCDEX.EXE (Microsoft CD-ROM Extensions) to
  be installed and an inserted data CD.




 ## 8. Running HWiNFO under V86 Memory Managers and Windows ###################


  In order to achieve best results, HWiNFO accesses directly the hardware.
  Some of the routines (privileged) require to be run in Real mode or at
  privilege level 0 (PL0, most privileged), but in V86 mode are all
  applications run at PL3. This means, if such a routine is run, the CPU
  raises an exception, which is handled by the V86 manager. Note, that
  V86 mode is the only way to run a DOS application (Real mode) under
  MS Windows (Protected mode). EMM (Expanded Memory Manager) also use the
  V86 mode to provide paging.


  But HWiNFO v3.00+ is able to run the privileged routines in V86 mode under
  some circumstances. There is a special call (called WINDOWS INIT BROADCAST),
  which can be used to force an V86 manager to switch to Real mode (of course,
  the V86 manager must support it). This call was originally used by
  MS Windows while starting, while an Expanded Memory Manager was running
  (this is needed, because EMM is running in Protected mode and Windows too).

  Such known EMM managers are:
   - Microsoft EMM386 Expanded Memory Manager
   - Quarterdeck QEMM386 Expanded Memory Manager
   - Qualitas 386MAX Expanded Memory Manager
   - Nu-Mega Soft-ICE Debugger
   ...

  So HWiNFO uses this call to force the manager to switch back to Real mode.
  HWiNFO works best under EMM386 (I haven't found any problems).

  But there are some disadvantages while runnig in V86 mode:

   - The FPU benchmark returns another results (it's slower) as in real mode.

   - Some V86 managers are able to relocate BIOSes, so HWiNFO won't be able
     to identify BIOS type and some video cards.

   - A crash while detecting the CPU type could happen on some older
     CPUs requiring CPU RESET to identify them properly.


  The other case is, if a manager doesn't support the call. This happens if
  you are running under Microsoft Windows95 OSR2 or Windows98 DOS mode.
  If these managers receive the Windows INIT BCAST, they display a message
  about running an incompatible application and stop. So the only way is
  to skip the privileged routines.

  Pre v4.4.1 of HWiNFO refused to run under this circumstances, but
  later versions run with the following restrictions (skip privileged routs):

   - CPU frequency can't be measured using TSC
   - CPU RESET can't be performed (this is needed only for older CPUs)
   - TI486 Potomac CPUs can't be identified
   - L2 cache ECC presence can't be detected (P-II, Xeon)
   - CPU Update Revision can't be reported (PPro and above)
   - Cache state, branch prediction and instruction execution can't be reported


  If you try to run HWiNFO directly from Microsoft Windows (DOS box), it will
  refuse to continue. This is because Windows controls also access to some
  ports and doesn't allow a direct access from a DOS application. This
  means, that if HWiNFO wouldn't refuse to run, but continue, it would be
  unable to return info about IDE/ATAPI drives, COM/LPT ports, BIOS scan,
  PnP resources, Benchmarks wouldn't be accurate...
  Windows NT VDM (Virtual DOS Machine) is even more strict.





 ## 9. Resetting the CPU ######################################################


  The CPU ID is available only on 386+ CPUs and HWiNFO uses three ways to
  obtain this ID:

  Method 1 - Resets the CPU while A20 is Enabled.
             This method works on all systems, but the Reset handler gets
             control after BIOS. And some BIOSes (some newer AMI/Award BIOSes)
             destroy CPU ID (EDX) and therefore this ID could be invalid.
             This method is default <Enabled> in Setup section.

  Method 2 - Resets the CPU while A20 is Disabled.
             This method works only on some machines, which do have a
             Fully-Terminated bus. It's the best way to obtain CPU ID, because
             it gets control immediately after Reset (the BIOS can't destroy
             EDX). I've found some problems with this method while running
             with Norton cache.
             This method is default <Disabled> in Setup section.

  Method 3 - Try to use this method if your BIOS destroys CPU ID. But it works
             only on systems, which do not have Main BIOS (area at 0F000:0)
             Write-Protected, because it modifies it for a bit, and then
             restores back. This method is on some machines the only way
             to obtain CPU ID.
             This method is default <Enabled> in Setup section.



  HWiNFO tries to determine CPU ID this way, via: 1. CPUID instruction
                                                  2. BIOS (INT 15h)
                                                  3. Method 2 (if Enabled)
                                                  4. Method 3
                                                  5. Method 1

  If you have an UMC U5SX/SD/SLV/486DX2/SX2, Enhanced Am486DX2/DX4/DX4-WB,
  AMD-K5 and above, Intel 486DX/SX/DX2 SL-Enhanced, IntelDX4, IntelSX2,
  IntelDX2 W-B Enh. or Intel Pentium(R) and above, there is no need to Reset
  the CPU (these CPU support CPUID instruction). Most CPUs today support
  CPUID instruction.

  Note: NexGen Nx586 does NOT support the CPUID instruction.
        Cyrix 5x86 and above support the CPUID instruction only if CPUIDEN bit
        in CCR4 register is set. HWiNFO 3.0.7+ sets this bit automatically.

  Disabling "CPU ID detection via Method 1, 2 and 3" reduces your CPU
  detection ability. And if there's no other way to obtain this ID
  (via BIOS or CPUID instruction), it won't identify 386SL, i386CX/EX,
  486DX2, IBM 486... and some other CPUs. Do this only if your system
  hangs while attempting CPU detection.

  Some BIOSes simply OVERWRITE the CPU ID (EDX) :-< ! In this case an
  invalid CPU ID is displayed and the CPU is probably incorrectly identified.
  If this problem occurs, try to use Method 3 (but your Main BIOS must be
  Write-Enabled !). If it doesn't work, try to use Method 2 (but you must
  have a Fully-Terminated bus !). And if HWiNFO still displays, that Method 1
  was used to obtain CPU ID, not Method 2 nor 3 can obtain it.




 ## 10. HWiNFO Crash ##########################################################



  - S3 ViRGE cards seem to crash while performing the TV Tuner test.
    If so, disable the "Check TV Tuner" option in Setup.

  - Stacker Compression Card and 3Com EtherLink III Adapter detection
    routines can cause crashes with some Network cards. You can disable
    them in the Configuration section (Stacker check is default disabled;
    3Com EtherLink III detection is enabled).

  - If HWiNFO crashes while starting or while the "Flushing Disk Caches..."
    message is displayed, disable the "FlushDiskCache" option in HWiNFO.INI
    or HWiNFO|Setup.

  - The test for a TIGA graphics adapter may cause problems with some
    adapters.



 ## 11. Secondary Video Info ##################################################


  RISC Graphics Processor: currently identifies only Hitachi HD63484 ACRTC
  Scanning for TMS: checks for TMS340x0 processor on several ports and tries
                    to get vendor and device name (detection routine from
                    SPEA GDC drivers, I don't know if it works with other TMS
                    cards too)
  TMS Boot EEPROM: gets info from Boot Software; this won't probably work
                   with other cards than SPEA (I don't know :-( )
  TIGA driver: gets info from TIGA driver if it's loaded (TIGACD.EXE)
  Also found as: identifies all SPEA Graphiti series cards from GDCINI.DAT
                 and checks for HP IGC-20 and NEC MultiSync Graphics Engine

  You can obtain info such as:

  e.g.: RISC Graphics Processor:   Hitachi HD63484 (ACRTC)
        Scanning for TMS:          N/A
        TMS Boot EEPROM:           N/A
        TIGA driver:               N/A
        Also found as:             SPEA Graphiti Flash 1G2-HE

  or:   RISC Graphics Processor:   N/A
        Scanning for TMS:          (C) SPEA Software AG HILITE1024
        TMS Boot EEPROM:           SPEA HiLite1024 
        TIGA driver:               N/A
        Also found as:             SPEA Graphiti HiLite1024

  or:   RISC Graphics Processor:   N/A
        Scanning for TMS:          <I really don't know what it'll display>
        TMS Boot EEPROM:                             -||-
        TIGA driver:               HP A1083A Intelligent Graphics Controller 20
        Also found as:             Hewlett Packard IGC-20 A1083A







 ## 12. PCI chipsets comparison ###############################################



ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄ¿
³ Chipset        ³ Intel ³ Intel ³ Intel ³ Intel ³ Intel ³ Intel ³ Intel ³
³                ³ 430LX ³ 430NX ³ 430FX ³ 430VX ³ 430HX ³ 430MX ³ 430TX ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ North Bridge   ³82434LX³82434NX³82437FX³82437VX³82439HX³82437MX³82379TX³
³                ³ PCMC  ³ PCMC  ³  TSC  ³  TVX  ³  TXC  ³ MTSC  ³ MTXC  ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ Supported      ³  P5   ³  P5,  ³ P54C  ³ P54C  ³ P54C  ³ P54LM ³ P54C, ³
³ CPUs           ³       ³  P54C ³ K5,   ³ K5,   ³ K5,   ³mobile ³ P55C, ³
³                ³       ³       ³ M1    ³ M1    ³ M1    ³       ³ K5,K6 ³
³                ³       ³       ³       ³       ³       ³       ³ M1,M2 ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ Max. bus freq. ³  66   ³  66   ³  66   ³  66   ³  66   ³  66   ³  66   ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ SMP (max CPUs) ³   -   ³   -   ³   -   ³   -   ³   2   ³   -   ³   -   ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ Max. memory    ³ 192M  ³ 512M  ³ 128M  ³ 128M  ³ 512M  ³ 128M  ³ 256M  ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ Supported      ³  SPM  ³  SPM  ³  SPM, ³  FPM, ³  FPM, ³  SPM, ³  FPM, ³
³ Memory         ³       ³       ³  EDO  ³  EDO, ³  EDO  ³  EDO  ³  EDO, ³
³ Types          ³       ³       ³       ³ SDRAM ³       ³       ³ SDRAM ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ ECC/Parity     ³   -   ³   -   ³   -   ³   -   ³   X   ³   -   ³   -   ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ Cacheability   ³ 192M  ³ 512M  ³  64M  ³  64M  ³  512M ³  64M  ³  64M  ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ South Bridge   ³82378IB³82378IB³82371FB³82371SB³82371SB³82371MX³82371AB³
³                ³  SIO  ³  SIO  ³ PIIX  ³ PIIX3 ³ PIIX3 ³ MPIIX ³ PIIX4 ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ PCI support    ³  2.0  ³  2.0  ³  2.0  ³  2.1  ³  2.1  ³  2.0  ³  2.1  ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ A.G.P.         ³   -   ³   -   ³   -   ³   -   ³   -   ³   -   ³   -   ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ Concurrent PCI ³   -   ³   -   ³   -   ³   X   ³   X   ³   -   ³   X   ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ USB            ³   -   ³   -   ³   -   ³   X   ³   X   ³   -   ³   X   ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ Power Mgmt.    ³   -   ³   -   ³   -   ³   -   ³   -   ³SMI/APM³ ACPI  ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ Ultra-DMA mode ³   -   ³   -   ³   -   ³   -   ³   -   ³   -   ³   2   ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÙ


ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄ¿
³ Chipset        ³ Intel ³ Intel ³ Intel ³ Intel ³ Intel ³ Intel ³ Intel ³ Intel ³ Intel ³
³                ³ 440FX ³ 450GX ³ 450KX ³ 440LX ³ 440EX ³ 440BX ³ 440ZX ³ 440GX ³ 450NX ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ North Bridge   ³82441FX³82453GX³82453KX³82443LX³82443EX³82443BX³82443ZX³82443GX³82451NX³
³                ³  PMC  ³82454GX³82454KX³  PAC  ³  PAC  ³       ³       ³       ³82454NX³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ Supported      ³ P6,   ³ P6    ³ P6    ³ P-II  ³ P-II, ³ P-II  ³ P-II, ³ P-II, ³ Xeon  ³
³ CPUs           ³ P-II  ³       ³       ³       ³Celeron³       ³Celeron³ Xeon  ³       ³
³                ³       ³       ³       ³       ³       ³       ³optimi-³       ³       ³
³                ³       ³       ³       ³       ³       ³       ³  zed  ³       ³       ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ Max. bus freq. ³  66   ³  66   ³  66   ³  66   ³  66   ³  100  ³  100  ³  100  ³  100  ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ SMP (max CPUs) ³   2   ³   4   ³   2   ³   2   ³   -   ³   2   ³   -   ³   2   ³   4   ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ Max. memory    ³  1G   ³  8G   ³  1G   ³1G(EDO)³ 256M  ³  1G   ³ 256M  ³  2G   ³  8G   ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ Supported      ³FPM,EDO³  FPM  ³  FPM  ³ EDO,  ³ EDO,  ³ EDO,  ³ SDRAM ³ SDRAM ³  EDO  ³
³ Memory         ³ BEDO  ³       ³       ³ SDRAM ³ SDRAM ³ SDRAM ³       ³       ³       ³
³ Types          ³       ³       ³       ³       ³       ³   **  ³       ³       ³       ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ ECC/Parity     ³   X   ³   X   ³   X   ³   X   ³   -   ³   X   ³   -   ³   X   ³   X   ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ Cacheability   ³  ***  ³  ***  ³  ***  ³  ***  ³  ***  ³  ***  ³  ***  ³  ***  ³  ***  ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ South Bridge   ³82371SB³optio- ³optio- ³82371AB³82371AB³82371EB³82371EB³82371EB³82371EB³
³                ³ PIIX3 ³ nal   ³ nal   ³ PIIX4 ³ PIIX4 ³PIIX4E ³PIIX4E ³PIIX4E ³PIIX4E ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ PCI support    ³  2.1  ³  2.0  ³  2.0  ³  2.1  ³  2.1  ³  2.1  ³  2.1  ³  2.1  ³  2.1  ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ A.G.P.         ³   -   ³   -   ³   -   ³  2x   ³  2x   ³  2x   ³  2x   ³  2x   ³   -   ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ Concurrent PCI ³   X   ³ ****  ³ ****  ³   X   ³   X   ³   X   ³   X   ³   X   ³   X   ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ USB            ³   X   ³ ****  ³ ****  ³   X   ³   X   ³   X   ³   X   ³   X   ³   X   ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ Power Mgmt.    ³  SMM  ³  SMM  ³  SMM  ³ ACPI  ³ ACPI  ³ ACPI  ³ ACPI  ³ ACPI  ³ ACPI  ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ Ultra-DMA mode ³   -   ³   -   ³   -   ³   2   ³   2   ³   2   ³   2   ³   2   ³   2   ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÙ


ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄ¿
³                ³  VIA  ³  VIA  ³  VIA  ³  VIA  ³  VIA  ³  VIA  ³  VIA  ³
³ Chipset        ³Apollo ³Apollo ³Apollo ³Apollo ³Apollo ³Apollo ³Apollo ³
³                ³  VP1  ³  VPX  ³  VP2  ³  VP3  ³  MVP3 ³  Pro  ³ProPlus³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ North Bridge   ³82C585 ³82C585 ³82C595 ³82C597 ³82C598 ³82C691 ³82C693 ³
³                ³  VP   ³  VPX  ³       ³  /AT  ³  /AT  ³       ³       ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ Supported      ³ P54C, ³ P54C, ³ P54C, ³ P54C, ³ P54C, ³ P6,   ³ P-II, ³
³ CPUs           ³ K5,   ³ P55C, ³ P55C, ³ P55C, ³ P55C, ³ P-II  ³Celeron³
³                ³ M1    ³ K5,K6 ³ K5,K6 ³ K5,K6 ³ K5,K6 ³       ³       ³
³                ³       ³ M1,M2 ³ M1,M2 ³ M1,M2 ³ M1,M2 ³       ³       ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ Max. bus freq. ³  66   ³  75   ³  66   ³  100  ³  100  ³  100  ³  100  ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ SMP (max CPUs) ³   -   ³   -   ³   -   ³   -   ³   -   ³   -   ³   -   ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ Max. memory    ³ 512M  ³ 512M  ³ 768M  ³  1G   ³  1G   ³  1G   ³  1G   ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ Supported      ³ FPM,  ³ FPM,  ³ FPM,  ³FPM,EDO³FPM,EDO³FPM,EDO³FPM,EDO³
³ Memory         ³ EDO,  ³ EDO,  ³ EDO,  ³SDRAM, ³SDRAM, ³SDRAM, ³SDRAM, ³
³ Types          ³ SDRAM ³ SDRAM ³ SDRAM ³SDRAM2 ³SDRAM2 ³SDRAM2 ³  VCM  ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ ECC/Parity     ³   -   ³   -   ³   X   ³   X   ³   X   ³   X   ³   X   ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ Cacheability   ³ 512M* ³ 512M* ³ 512M* ³ 512M *³ 512M *³  ***  ³  ***  ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ South Bridge   ³82C586 ³82C586B³82C586B³82C586B³82C586B³82C596A³82C596A³
³                ³       ³       ³       ³       ³       ³       ³       ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ PCI support    ³  2.1  ³  2.1  ³  2.1  ³  2.1  ³  2.1  ³  2.1  ³  2.1  ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ A.G.P.         ³   -   ³   -   ³   -   ³  2x   ³  2x   ³  2x   ³  2x   ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ Concurrent PCI ³   X   ³   X   ³   X   ³   X   ³   X   ³   X   ³   X   ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ USB            ³   X   ³   X   ³   X   ³   X   ³   X   ³   X   ³   X   ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ Power Mgmt.    ³  APM  ³  ACPI ³  ACPI ³ ACPI  ³ ACPI  ³ ACPI  ³ ACPI  ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ Ultra-DMA mode ³   -   ³   2   ³   2   ³   2   ³   2   ³   4   ³   4   ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÙ



ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄ¿
³ Chipset        ³ SiS   ³  SiS  ³ SiS   ³ SiS   ³ SiS   ³ SiS   ³
³                ³ 5511  ³  5596 ³ 5571  ³ 5581  ³ 5597  ³ 5591  ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ North Bridge   ³ 5511  ³ 5596  ³ 5571  ³ 5581  ³ 5597  ³ 5591  ³
³                ³ PCMC  ³       ³       ³       ³       ³       ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ Supported      ³ P54C, ³ P54C, ³ P54C, ³ P54C, ³ P54C, ³ P54C, ³
³ CPUs           ³ K5,   ³ K5,   ³ P55C, ³ P55C, ³ P55C, ³ P55C, ³
³                ³ M1    ³ M1    ³ K5,K6,³ K5,K6,³ K5,K6,³ K5,K6,³
³                ³       ³       ³ M1,M2 ³ M1,M2 ³ M1,M2 ³ M1,M2 ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ Max. bus freq. ³  66   ³  66   ³  75   ³  75   ³  75   ³  66   ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ SMP (max CPUs) ³   -   ³   -   ³   -   ³   -   ³   -   ³   -   ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ Max. memory    ³ 512M  ³ 512M  ³ 384M  ³ 384M  ³ 384M  ³ 768M  ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ Supported      ³ FPM,  ³ FPM,  ³ FPM,  ³ FPM,  ³ FPM,  ³ FPM,  ³
³ Memory         ³ EDO   ³ EDO   ³ EDO,  ³ EDO,  ³ EDO,  ³ EDO,  ³
³ Types          ³       ³       ³ SDRAM ³ SDRAM ³ SDRAM ³ SDRAM ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ ECC/Parity     ³   -   ³   -   ³   -   ³   -   ³   -   ³   -   ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ Cacheability   ³ 256M *³ 256M *³ 128M *³ 128M *³ 128M *³ 256M *³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ South Bridge   ³ 5513  ³ 5513  ³ 5513  ³ 5513  ³ 5513  ³ 5595  ³
³                ³       ³       ³integr.³integr.³integr.³       ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ PCI support    ³  2.0  ³  2.0  ³  2.1  ³  2.1  ³  2.1  ³  2.1  ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ A.G.P.         ³   -   ³   -   ³   -   ³   -   ³   -   ³  2x   ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ Concurrent PCI ³   X   ³   X   ³   X   ³   X   ³   X   ³   X   ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ USB            ³   -   ³   -   ³   X   ³   X   ³   X   ³   X   ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ Power Mgmt.    ³  SMM  ³  SMM  ³  SMM  ³ ACPI  ³ ACPI  ³ ACPI  ³
ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄ´
³ Ultra-DMA mode ³   -   ³   -   ³   -   ³   2   ³   2   ³   2   ³
ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÙ



 *    - Depends on L2 cache size:
        ÚÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
        ³ cache ³   cacheable   ³
        ³ size  ³    region     ³
        ÃÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
        ³ 256K  ³64M-cache_size ³
        ³ 512K  ³128M-cache_size³
        ³ 1M    ³256M-cache_size³
        ³ 2M    ³512M-cache_size³
        ÀÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ

 **   - EDO and SDRAM cannot be mixed
 ***  - no L2 cache on-board (depends on on-chip L2 cache size in CPU)
 **** - available if 82371SB PIIX3 is used



 ## 13. IDE Disk Transfer Modes ###############################################


  HWiNFO reports transfer modes for all IDE/ATAPI drives, which support it.

  Max. PIO transfer mode:   PIO x
  DMA Transfer Modes:       SW: a1 (m1), MW: a2 (m2), Ultra: a3 (m3)

  Where:
  x = Maximum supported PIO transfer mode
  SW = Singleword DMA transfer mode
  MW = Multiword DMA transfer mode
  Ultra = Ultra-DMA transfer mode
  a1, a2, a3 = Current active mode
  m1, m2, m3 = Max. supported mode


                      ÚÄÄÄÄÄÄÄÄÄÄÄÄÄÂÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ¿
                      ³ Transfer    ³ Maximum       ³
                      ³ Mode        ³ Transfer rate ³
                      ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
                      ³ PIO 0       ³    3.33 MB/s  ³
                      ³ PIO 1       ³    5.22 MB/s  ³
                      ³ PIO 2       ³    8.33 MB/s  ³
                      ³ PIO 3       ³   11.11 MB/s  ³
                      ³ PIO 4       ³   16.66 MB/s  ³
                      ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
                      ³ DMA 0       ³    4.16 MB/s  ³
                      ³ DMA 1       ³   13.33 MB/s  ³
                      ³ DMA 2       ³   16.66 MB/s  ³
                      ÃÄÄÄÄÄÄÄÄÄÄÄÄÄÅÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄ´
                      ³ Ultra-DMA 0 ³   16.66 MB/s  ³
                      ³ Ultra-DMA 1 ³   25.00 MB/s  ³
                      ³ Ultra-DMA 2 ³   33.33 MB/s  ³ Ultra-DMA/33
                      ³ Ultra-DMA 3 ³   44.44 MB/s  ³ Ultra-DMA/44
                      ³ Ultra-DMA 4 ³   66.66 MB/s  ³ Ultra-DMA/66
                      ÀÄÄÄÄÄÄÄÄÄÄÄÄÄÁÄÄÄÄÄÄÄÄÄÄÄÄÄÄÄÙ




 ## 14. Miscellaneous notes ###################################################


  On some old motherboards, random numbers are obtained from unused I/O ports
  and this may cause invalid identification of some hardware (e.g. WSS).
  I don't know how to solve this problem.


  Video Throughput benchmark depends only on External CPU frequency and the
  type of Video board used; e.g. 486DX-33 with the same graphics board as an
  i486DX4-100 (running at 3*33 MHz) report the same Video Throughput speed !


  Intel Pentium(R) and above CPUs do not report, that the "APIC on-chip"
  feature is present. Most of them (P54C yes, but P54CQS and P54LM don't)
  have an on-chip APIC, but don't report it, if it isn't supported by
  external hardware.


  Dhrystone benchmark tests the performance of CPU and Memory, but only in
  16-bit code. Therefore a 150 MHz Pentium Pro (which is designed and tuned
  especially for 32-bit code) returns a rather low Dhrystone result.
  So its performance while running with 16-bit applications is comparable
  to a 100 MHz Pentium P54C.


  If you have an Intel 420LX/420NX/430FX/430HX/430VX/430MX/430TX,
  SiS 85C501/5120/5511/5571/5581/5596/5597/5591, AMD-640 chipset or
  VIA Apollo VP-1/VPX/VP-2/VP3/MVP3, HWiNFO is able to detect the type of
  External Cache and its size direct from the PCI chipset registers.



  The report of CPU temperature sensor requires:
   - Temperature sensor connected to CPU:
     - National Semiconductor LM75 sensor or
     - Mobile Intel Pentium(R) II Processor or
     - Intel Pentium(R) II Mobile Module or
     - Intel Pentium(R) II Xeon(TM) Processor
   - Intel 82371AB PIIX4 (or 82371EB PIIX4E) south bridge
   - SMBus

  The report of MB temperature, voltages and FAN speed requires:
   - National Semiconductor LM78 or compatible sensors
     Compatible are: - National Semiconductor LM79
                     - National Semiconductor LM80
                     - National Semiconductor LM81
                     - Winbond W83781D
                     - Dallas Semiconductor DS1780 (maybe SMBus interface only)
                     - Analog Devices ADM1024 (maybe SMBus interface only)
   - These chips must be present at standard ISA I/O locations 280h or 290h





 ## 15. Some abbreviations ####################################################



    FPM           = Fast-Page Mode (old standard DRAM type)
    EDO           = Extended Data-Out
    SDRAM         = Synchronous DRAM
    DDR SDRAM II  = Double Data Rate SDRAM II
    BDDR SDRAM II = Bi-directionally strobed DDR SDRAM II
    BEDO          = Burst EDO
    EC            = Error Check only
    ECC           = Error Check and Correction

    DRAM          = Dynamic RAM
    VRAM          = Video RAM
    WRAM          = Window RAM
    SDRAM         = Synchronous DRAM
    SGRAM         = Synchronous Graphics RAM
    RDRAM         = Rambus DRAM
    MDRAM         = Multibank DRAM
   
    VRT           = Voltage Reduction Technology
    APIC          = Advanced Programmable Interrupt Controller (required for DP)
    DP            = Dual Processing
    FRC           = Functional Redundancy Checking (requires DP)
    MMX           = Multimedia Extensions 
                    (57 new instructions, SIMD architecture, 64-bit regs)
    MMX-2         = 3D Multimedia Instructions (Intel)
    3DNow!        = Additional floating point MMX instructions (AMD, Cyrix)
    KNI           = Katmai New Instructions
                    (70 SIMD floating-point instructions, that can be run
                    in a special CPU mode)
    ISSE          = Internet Streaming SIMD Extensions
                    (official name of KNI)
    S.E.C         = Single Edge Contact
    MPS           = Multi-Processor System
    P.I.ROM       = Processor Information ROM

    TLB           = Translation Lookaside Buffer
                    (small cache for page translation)

    PnP           = Plug-and-Play
    ESCD          = Extended System Configuration Data
    DMI           = Desktop Management Interface
    ACPI          = Advanced Configuration and Power Interface
    APM           = Advanced Power Management

    VESA/VBE      = Video Electronics Standards Association / 
                    Video BIOS Extensions
    DDC           = Display Data Channel
                    (DDC1: Monitor->PC, DDC2B: Monitor<->PC)




 ## 16. Codenames #############################################################



  Codenames for Intel Processors:

  P5          - Intel Pentium(R) Processor:
                Old 50/50 (Engineering Sample), 60/60 and 66/66 MHz.

  P54C        - Intel Pentium(R) Processor:
                Later 75/50, 90/60, 100/50, 100/66, 120/60, 133/66, 150/60,
                166/66, 180/60, 200/66 and 233/66 MHz without VRT, with
                on-chip APIC, Dual Processing Features and FRC support.

  P54CM       - Intel Pentium(R) Update Processor:
                Old 90MHz Slave processor in Dual Processor system.

  P54CQS      - Intel Pentium(R) Processor:
                75/50, 100/66, 120/60, 133/66, 166/66 and 200/66 MHz
                without VRT, on-chip APIC, Dual Processing Features, Upgrade
                and FRC support.

  P54LM       - Intel Pentium(R) Mobile Processor:
                75/50, 120/60, 133/66 and 150/60 Low Power versions (2.9 V)
                supporting VRT. These Processors are shipped without APIC
                on-chip, Dual Processing Features, Upgrade and FRC support.

  P24T        - Intel Pentium(R) OverDrive(R) Processor:
                PODP5V63 63/25 MHz and PODP5V83 83/33 MHz OverDrive
                for 486 CPUs.

  P24CT       - Intel Pentium(R) OverDrive(R) Processor:
                OverDrive for IntelDX4(TM) Processor.

  P5T         - Intel Pentium(R) OverDrive(R) Processor:
                PODP5V120 120/60 MHz and PODP5V133 133/66 MHz OverDrive for
                Intel Pentium(R) P5 60/60 and 66/66 MHz Processors.

  P54CT       - Intel Pentium(R) OverDrive(R) Processor:
                PODP3V125 125/50 MHz, PODP3V150 150/60 MHz and
                PODP3V166 166/66 MHz OverDrive for Intel Pentium(R) P54C
                75/50, 90/60 and 100/66 MHz Processors.

  P55C        - Intel Pentium(R) Processor with MMX(TM) Technology:
                166/66, 200/66, 233/66 and 266/66 MHz
                MMX, 32 KBytes First Level Cache and better Branch Prediction.

  P55LM
  Tillamook   - Intel Mobile Pentium(R) Processor with MMX(TM) Technology:
                200/66, 233/66, 266/66, 300/60 and 300/66 MHz,
                VccCORE=1.6-2.1 V, VccIO=2.3-2.6 V

  P55CTP      - Intel Pentium(R) OverDrive(R) Processor with MMX(TM) Technology:
                PODPMT60X150 125/50, 150/60, PODPMT66X166 166/66,
                PODPMT60X180 180/60 and PODPMT66X200 200/66 for Intel Pentium(R)
                75/50, 90/60 and 100/66 Processors.

  P6          - Intel Pentium(R) Pro Processor:
                133/66 (Engineering Sample), 150/60, 166/66, 180/60 and 200/66,
                256K, 512K and 1024K of L2 cache.

  P6T         - Intel Pentium(R) Pro OverDrive(R) Processor.

  P6L
  Klamath     - Intel Pentium(R) II Processor:
                233/66, 266/66 and 300/66,
                P6 with MMX(TM) Technology and without Level-2 on-chip cache,
                S.E.C. cartridge, Slot 1, 512K half speed ECC/Non-ECC L2
                cache on substrate, .35 æm, VccCORE=2.8V or 1.6V,
                up to 2 CPUs in MPS

  Deschutes   - Intel Pentium(R) II Processor:
                333/66, 350/100, 400/100 and 450/100 MHz,
                512K ECC half speed L2 cache, MMX, .25 æm, VccCORE=2.0V

  Mobile
  Deschutes   - Mobile Intel Pentium(R) II Processor:
                233/66, 266/66 MHz and 300/66, VccCORE=1.7V or 1.6V,
                ECC L2 cache

  P6X         - Intel Pentium(R) II Xeon(TM) Processor:
                400/100 and 450/100 MHz, 512K, 1M or 2M o full speed L2 cache,
                MMX, Slot 2, up to 8 CPUs in MPS, full ECC, FRC,
                SMBus (thermal sensor, P.I. ROM, scratch EEPROM)

  P6C
  Covington   - Intel Celeron(TM) Processor:
                266/66 and 300/66 MHz, no L2 cache, MMX, no MPS, Slot 1

  Mendocino   - Intel Celeron(TM) Processor:
                300A/66, 333/66, 366/66 and 400/66 MHz, 128K on-chip L2 cache,
                Slot 1 or PPGA (Socket 370)

  Dixon       - Intel Mobile Pentium(R) II Processor:
                266PE/66, 300PE/66, 333/66 and 366/66, 256K on-chip L2 cache,
                VccCORE=1.6 V, Mini-cartridge, MMC-1 or MMC-2 for Mobile Module
                or BGA package

  Katmai      - Intel Pentium(R) III Processor:
                450/100, 500/100 and 550/100, ISSE, 512K half speed L2 cache,
                Slot 1

  Tanner      - Intel Pentium(R) III Xeon(TM) Processor:
                500/100 MHz, ISSE, Slot 2, 512K/1M/2M full speed CSRAM L2 cache

  Coppermine  - 533 MHz, .18 æm, Slot 1, 512K half speed L2 BSRAM cache,
                133 MHz FSB

  Cascades    - 600 MHz, .18 æm, Slot 2, 256K full speed L2 cache,
                133 MHz FSB

  Willamette  - .18 æm, 800 MHz

  Merced      - Intel + HP project
                IA64 architecture, EPIC, PA-RISC compatible

  Foster      - For servers, 1 GHz





 ## 17. Thanks ################################################################


 I want especially to thank:

 ù Beta testers: Boris Hur¡nek [BHsoft] (hurinek@axa.sk)
                 Erik Francisci (jumper!franci@dec3.dcs.elf.stuba.sk)
                 Igor Junas (junas@axis.sk)
                 Mat£s Rosa (rosa@???.sk)
                 Milan Marusinec (marusin@lithec.sk)
 ù Alex V. Potemkin and Potemkin's Hackers Group (avp@stelth.dvm.msk.ru)
 ù Aad Offerman (offerman@einstein.et.tudelft.nl) - CHIPLIST
 ù J n G£cik (jan.gucik@vslib.cz) - IntroScope
 ù Tom s Lehuta (lehuta@elf.stuba.sk) - GUS Memory routs, hints
 ù Peter Hubinsky (hubak@elf.stuba.sk; SAC fileadmin) - distribution
 ù Emil Laurentiu (lcarmen@u1.ici.ro) - hints
 ù Andrew Nelson (anelson@atlas.co.uk) - English language suggestions :-)
 ù Marek Smihla (ceit@internet.sk) - reports & hints
 ù Jiang Hong (zlzhang@pku.edu.cn) - BL3 & hints
 ù Intel and its support (support@intel.com) - excellent dox, insight CD
 ù Tamas Miklos (fieryofup@geocities.com) - WSS&Modem rout, hints, ASMDEMO
 ù ESCOM CS (escom_support@brn.pvtnet.cz) - info, reports
 ù Olivier Cahagne (cahagn_o@epita.fr) - SysInfo observatory, reports
 ù Thomas Mainka (100112.2132@compuserve.com) - reports
 ù Christian Klak (drk-soft@gmx.net) - Acer info
 ù Gershon Mikulsky (mikuls@shani.net) - ATI info
 ù Janusz Bubik (j.bubik@micronic.cz) - reports
 ù EliCZ (elicz@post.cz) - AMD-K6 DRx bug
 ù ATI Developer Relations (devrel@atitech.com) - id of ATI chips

 ù All other people, who have sent bug reports and suggestions (*!*@*.*)





 Greetings to:

 ù Lubos Vrtik (vrtik@vuje.sk) - cracking <-> protecting impressions, HMVS

 ù C00LMAN [Siam Hacker's Gang] - KeY GeNeRaToR 4 HWiNFO v<4.0.0
   (I'm waiting 4 keYGen 4 HWiNFO v4.0.0+)

 ù eGIS [pCE] - *v3Ry nICE* K3YG3N 4 HWiNFO ó4.2.4, 4.2.5
   (No idea how to receive the true magic numbers for v4.0.0+ ?)

 ù EliCZ [pCE] - {Ni<E W<>rK} - keygen 4 HWiNFO <4.4.4
   (A little bit complicated, but at least something new.
   Let's see what comes as next...)

 ù dEVIL [uCF] - *nICE* kEYZ 4 HWiNFO v4.2.2, ReGGeD v4.3.0
   (try brute force attack ;-))

 ù Dark Paw - Nice Try (also w/ comments)
   (Still waiting for registered users ?)

 ù lorian [uCF] - The first usable keymaker for HWiNFO <4.5.0 !

 ù All unknown members of HWiNFO <Ra<KiNG challange :-)






 ## 18. Disclaimer ############################################################


 ÉÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ»
 º  All product names are copyright and registered trademarks/tradenames of   º
 º                        their respective owners.                            º
 ÈÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍÍ¼


           HWiNFO IS COPYRIGHTED MATERIAL AND PROTECTED BY APPLICABLE
               COPYRIGHT LAWS AND INTERNATIONAL TREATY PROVISIONS.


    THE PROGRAM AND ITS DOCUMENTATION ARE COPYRIGHTED BY THE ORIGINAL
    PROGRAMMER/AUTHOR (COPYRIGHT HOLDER). ALL RIGHTS ARE RESERVED CONCERNING
    FUTURE CHANGES OF THE NAME AND CONTENTS OF THIS DISTRIBUTION PACKAGE. NO
    CHANGES MUST BE MADE FOR ANY REASONS AT ANY TIME BY ANYBODY IN ANY ASPECT,
    INCLUDING, BUT NOT LIMITED TO, MODIFICATION OF THE COPYRIGHT NOTICE OR
    CHANGES OF THE COMPILED BINARIES HEREBY ALTERING THE ORIGINALLY INTENDED
    PROGRAM EXECUTION FLOW.

    REALiX SPECIFICALLY DISCLAIMS ALL WARRANTIES, EXPRESS OR IMPLIED, AND
    ALL LIABILITY, INCLUDING CONSEQUENTIAL AND OTHER INDIRECT DAMAGES, FOR
    THE USE OF THIS SOFTWARE, INCLUDING LIABILITY FOR INFRINGEMENT OF ANY
    PROPRIETARY RIGHTS. REALiX DOES NOT ASSUME ANY RESPONSIBILITY FOR ANY
    ERRORS WHICH MAY APPEAR IN THIS CODE NOR ANY RESPONSIBILITY TO UPDATE IT.

    THE PERSON USING THE SOFTWARE BEARS ALL RISKS AS TO THE QUALITY AND
    PERFORMANCE OF THIS SOFTWARE.


 ## END #######################################################################