The G8BPQ AX25 Networking Package.


1. Introduction.

This software allows an IBM PC, or similar machine, equiped with suitable
Communications hardware, to act as a Node in a NET/ROM compatible AX25 
network, and/or to support a multiuser Mailbox, or other similar applications.

The switch section of the code supports up to 16 AX25 ports, and the
application interface supports up to 64 connections. The basic applications
interface is called 'BPQ Host Mode', and is defined in file BPQHOST.DOC.
Additional drivers are provided to convert this to other common Amateur
interface standards (eg TNC2 via COMBIOS, and WA8DED Host Mode).


Note the software is NOT Public Domain. It may be used only by licenced
Radio Amateurs in Amateur Packet Radio systems.



2 Hardware Requirements.

The system is written in 8086 assembler, and is currently only available for
the MSDOS/PCDOS environment, although once loaded it makes no use of operating
system facilities. It has been tested on IBM PC and XT machines, and a number
of similar machines. (AST Premium, Toshiba T1100+, OPUS). The software needs
about 48 - 80k RAM, varying with number of buffers, comms links and COMBIOS
ports configured.

The software supports the following comms hardware:

	PAC-COM  PC120 card
	DRSI PCPA card
	Software Forge HDLC card for the Toshiba T1100 (with external modem).
	KISS mode TNC via a standard PC ASYNC card or QUADRAM Quadport .
	Link to NET/ROM or TheNet Async port.
	RLC100 4 port HDLC card.
 

A version is also available for the Kantronics Data Engine.



3. Networking Facilities.

The system is designed to be operationally compatible with existing NET/ROM
or TheNet nodes, but there are a few minor differences. As it can support
an integrated BBS, it has 2 Callsign/Alias pairs, one for accessing the node,
and the other the BBS. Note, however, that a multiport node does not need a
different callsign for each port. Because of the multiport support, the 
'Downlink' connect command needs a port number as the first parameter (eg
C 2 G8BPQ). A connect to another Node doesnt need this - the system selects
the 'best' port as found from the NODEs and ROUTEs lists.

Although multiple applications are allowed, only one (BBS) has its own
Callsign/Alias pair. Others are accessed by connecting to the switch, then
entering the service name.

There are  extra commands for normal use (BBS, or other application name, to
connect to the applications, and PORTS to display available port descriptions),
and 2 commands intended primarily for the system operator (STATS and LINKS).

Two extra commands PACLEN and L4T1 are available to set Paclen for NODE
generated messages (nodes lists, etc), and the Transport timeout. At the
moment these are primarily for me to experiment with, but feel free to fiddle.


The system is also able to link to the 'back end' async port on a normal
NET/ROM or TheNet node.



4 Getting Started.



A. Decide what you want.


The software can be configured as a mailbox access system, a packet switching
node, or a combination of both. I would expect most intallations to use either
one or the other, but if you run a well sited BBS (particularly if multiband),
and there is a shortage of nodes in your area, you may wish to run both.


B® Chooså youò hardwarå anä software.


You need an IBM PC/XT/AT or compatible. A switch needs very little RAM (
about 128k), but a BBS system will probably need a minimum of 640K. You can
connect your radios via an internal packet adaptor (PC120 from PACCOM, 
PCPA from DRSI, etc), or via normal TNC's running in KISS mode (or both). For
a new installation I recommend the internal card, as it will normally be 
cheaper (especially for multiport nodes), and faster, but if you already have
a TNC which has (or can be fitted with) a KISS option, then by all means use 
it.

The software has been tested with the BBS systems written by W0RLI, F6FBB,
G1NNA, and G4YFB, and with AK1A's PacketCluster. It is likely to work with
other system which use a similar interface - if in doublt, consult the 
author of the program concerned.


C. Edit the configuration file (BPQCFG.TXT)


I hope the comments in the file make it largely self-documenting. You need
one Callsign/Alias pair for BBS access, and one for the Node. If you are
running both, they must be different, but if you are running only one or
the other, you must still put BOTH entries in the file, but they MUST be the
SAME. The software doesn't currently verify this, so be careful!


Most of the configuration params can be left alone - the ones to look at
are:

IDMSG and INFOMSG

BBS, NODE	to select BBS support and NODE support as required 

ROUTES		to 'Lock In' the routes you want to use


Note that the supplied Networking parameter conform (more or less) to the
recommendations made at SYSOPS 5.



There are sample 'PORTS' configuration files for the various link types 
supported in file PORTS.DOC - copy and customise the ones you want to use.



D. Run BPQCFG.


This will convert the configuration file to a format suitable for use by the
main software. Validation isn't wonderful, but it may produce error messages.



E. Load it.


I suggest you test the system first using a simple terminal program, before
trying it with the BBS (if required).  I have included on the disk a suitable
terminal program (PAC4), which may be used with the system.


When running with a multitasker (eq DesqView), you must load my software
before the multitasker. You should run BPQCODE, then any required interface
drivers. The available drivers are described in DRIVERS.DOC, but for initial
testing, just run BPQHTNC2. A copy of my AUTOEXEC.BAT file follows (I use
W0RLI BBS). Once the switch is running, load Desqview (if required), then
your BBS or other application programs.


My AUTOEXEC.BAT:

cd \bbs
LM
SHARE
cd \net
bpqcode
bpqhtnc2 
cd \bbs
mbinit
cd \dv
dv

The BBS software is loaded by a Desqview script file. The following saves
the ROUTES and NODES to disk before shutting down.

cd \net
bpqnodes







Appendix 1 - Fowarding files

Both MBL and RLI BBS software requires that the reply to the first connect in
a forward file connect sequence is of the form *** CONNECTED to xxxx. This is
not normally provided by the switch code, as the first connect is effectively
at the Net/Rom level. To get round this, I have provided a dummy command, 
C SWITCH, which returns the string '*** CONNECTED to SWITCH'. This should be
included as the first entry in each set of forwarding commands. See below
for sample forwarding files for MBL and RLI.

MBL:

FA GB7NTS
00-23
@SWITCH
.C LRG7 
?u
+to
.c GB7NTS-7
+to
?u
G4MTP
GB7NTS
-----

RLI:

CC SWITCH
NC GB7NTS
HB0023GB7NTS
GB7NTS
_271
_1111
*** EOF



John Wiseman, G8BPQ
76,Haywood Road,
Mapperley,
Nottingham.
NG3 6AE.

Phone 0602 522669    (Please phone only between 20:00 - 22:00 UTC)

31 August 1992.