-----------------------------------------------------------------------
                              cFos Modem Command Set
    -----------------------------------------------------------------------

        A       Force Answer

        Bn      Select protocol ONLY for outgoing calls
                0       X75 without B3 protocoll, 64000bps      ("ISDNC")
                1       V110 async, 38400bps, 8n1               ("ISDNB")
                2       V110 async, 19200bps, 8n1               ("ISDNA")
                3       128kbps Bundle Protokoll
                4       X75, Framelen=256, Win.Size=7 (ELINK mode)
                5       Datex-J (BTX)

        D..     Dial
                L       dial last number
                S       dial stored number (hardcoded, 0=Zaphods BBS)
                V       flag connection as SPV
                0..9    digits
                A..D#*  special "digits"

        En      Command Echo
                0       echo off
                1       echo on

        Hn      On/Off Hook control
                0       on hook, terminate an active connection
                1       off hook, reject an incoming call

        In      Inquiry
                0       product identification and CAPI version and
                        manufacturer
                1       status line output
                2       last call statistics
                4       last 10 CAPI info dumps

        O       Return On-line

        Qn      Quiet mode, result codes display
                0       display result codes
                1       supress result code; be Quiet

        Sr=n    Set register r to value n (registers are unsigned 16bit ints)
        Sr.b=n  Set bit b to n
        Sr,b=n  Set bit b to n
        Sr?     Query register r
        SrH=n   Set high byte of register r to value n
        SrL=n   Set low byte of register r to value n

        Vn      Verbal mode
                0       numeric result codes
                1       verbal result codes

        Xn      Result code options
                0       modem looks like a standard 9600 bps modem
                1       enables CONNECT <rate>
                2       enables RINGING
                3       enables RING <incoming caller's id>
                4       enables CONNECT[...]/<protocols..>
                5       enables ?
                6       enables /<cause> on ERROR, NO CARRIER, NO ANSWER
                        and NO DIAL TONE

        Zn      Restore profile from number n (out of the file PROFILE).
                This will further reregister the application at the CAPI.
                If no number is given, 0 will be default.


        Fn      \
        Kn       |
        Ln       |
        Mn       |  ignored for compatibility
        Nn       |
        P        |
        T       /


    -----------------------------------------------------------------------
                        cFos extended Modem Command Set
    -----------------------------------------------------------------------

{+}     &Bn     Number of Channels to use for 'cFos' Channel Bundling, for
                next dial command

        &Dn     Debug mode
                0       disable status bar (default)
                1       enable status bar (only if port is initialized)
                2       enable status bar (only if carrier is high)

        &En     EAZ: n = '0' ... '9': changes register 18. Default is
                EAZ 0.

        &F      Reset to Factory defaults and reset (like ATZ)

        &Lnnn   Listen to what EAZ's; changes register 13; takes multiple
                digits or '*' for all. Default is EAZ 1.

        &Onnn   Outdial Number. This number will be used as prefix for
                all phone numbers dialed with the ATD command. Default is
                none.

        &V      View profile

        &Wn     Write profile to number n (into a file named PROFILE). If
                no number is given, it defaults to 0.


    -----------------------------------------------------------------------
                    cFos extended debug Modem Command Set
    -----------------------------------------------------------------------

      [ #C      Clear the alternate screen ]

        #Rn     Reregister the application if all ports are idle; use
                #R1 to force reregister (and lockout of all active
                connections!)

        #T      TRANX: set the clock to the actual time/date (gotten from
                the last connection attempt).


      Commands in brackets '[' and ']' are only available in debug
      versions;  in the release version these commands are invalid.


    -----------------------------------------------------------------------
                             cFos Modem Register Chart
    -----------------------------------------------------------------------

      Reg#      Description                                     Default

        S0      Auto Answer on (>=1) / off (==0)                0

        S1      Ring count                                      0

        S2      Escape code                                     '+'

        S3

        S4

        S5

        S6

        S7      Number of seconds modem waits for a carrier     60

        S8

        S9      Bit-mapped register:                            32737
                .0      enable any further result code
                .1      enable CONNECT <rate>, otherwise
                        CONNECT 9600 is always returned
                .2      enable RINGING
                .3      enable RING <number>
                .4      enable /X75.. after CONNECT
                .5      enable ERROR/<cause>
                .6      enable NO CARRIER/<cause>

        S10     Bit-mapped register:                            0
                .0      enable CONNECT.../ID=<callerid>
                .1      disable full status line, just display
                        the callerid on the left side
                .2      display numerical values fuer service
                        indicator / add. si instead of names

        S11     Status line line number (0 - screen length-1)   0
                Note: only displayed if at&d1

        S12

        S13     Serviced EAZ Mask                               2
                Every bit from bit0.. bit9 enables RING on
                this EAZ ('0' - '9')
                ex:     0000000010b     answer on '1'
                        0100000000b     answer on '8'
                        0001111111b     answer on '0' - '6'
                        1111111111b     answer all calls

                This register is also modified by the AT&L... command.

        S14     Serviced SI Mask                                0x80

        S15     B-Channel Identification (ffs. 1.TR.6,          0x83
                3.2.3.4.4.7)

        S16     Source Service Indicator                        7

        S17     Source Additional Service Indicator             0

        S18     Source EAZ (character: '0'=48.. '9'=57)         '0'
                Sent with connect_req message; information only

                This register is also modified by an AT&En
                command.

        S19     Inactivity timer: modem disconnects if          0
                no traffic in N minutes; 0==disabled

        S20     B-Channel, level 2 protocol                     1
                1       X.75 SLP Basis Operation Mode,
                        mit Implementation Rules nach T.90
                2       Transparent-HDLC mit Bit-Stuffing,
                        Frame-Erkennung und CRC-Check
                3       Bittransparent
                4       SNA-SDLC
                5       X.75 Btx
                8       V110 mit transparentem B2 protokoll
                9       V110 SNA-SDLC
                10      V110 X75 SLP nach T.90

        S21     B-Channel, level 3 protocol                     4
                1       T70 NL f�r Leitungsvermittlung (CSPDN)
                2       ISO 8208 (DTE/DTE)
                3       Level 3 according to T.90, Appendix II
                4       transparent

        S22     SELECT_B2_PROTOCOL_REQ: Data-length             2048

        S23     SELECT_B2_PROTOCOL_REQ: Link-Address-A          3

        S24     SELECT_B2_PROTOCOL_REQ: Link-Address-B          1

        S25     SELECT_B2_PROTOCOL_REQ: Modulo-Mode             8

        S26     SELECT_B2_PROTOCOL_REQ: Window-Size             1

        S27     SELECT_B2_PROTOCOL_REQ: V110 user rate          64

        S28     Maximum SEND B2-Framesize                       2048

        S29     B3-Protocol-Overhead in Bytes                   0
                b3 == 1 (t70nl): 2
                b3 == 2 (iso8208): 3
                b3 == 4 (transparent): 0

        S30     SELECT_B3_PROTOCOL_REQ: LIC                     0

        S31     SELECT_B3_PROTOCOL_REQ: HIC                     0

        S32     SELECT_B3_PROTOCOL_REQ: LTC                     0

        S33     SELECT_B3_PROTOCOL_REQ: HTC                     0

        S34     SELECT_B3_PROTOCOL_REQ: LOC                     0

        S35     SELECT_B3_PROTOCOL_REQ: HOC                     0

        S36     SELECT_B3_PROTOCOL_REQ: Modulo-Mode             8

        S37

        S38

        S39     Numbering Type/Plan                             83

        S40     Controller                                      0

        S41     Info-Mask-low                                   63

        S42     Info-Mask-high                                  0

        S43     Default V110 user rate & Protocol               64

        S44

        S45

        S46

        S47

        S48

        S49

        S50    \
        S51     |
        S52     |   Default Additional Service Indicator and B2-Protocol
        S53     |   for every EAZ:
        S54     |   If the incoming AddSI is 0 then we get the AddSI
        S55     |   from the low byte of register 50+EAZ; the B2-Protocol
        S56     |   is got from the high byte.
        S57     |
        S58     |
        S59    /

    -----------------------------------------------------------------------