NOBLINK.COM is a short utility for EGA, VGA and MCGA display cards only.  
Normally, you can only use hi-intensity attributes for the foreground; 
hence, it is impossible to have a yellow background for example.  
NOBLINK alters the system settings to provide hi-intensity instead of 
blinking.  It is not a TSR, and the settings will revert to normal if 
the screen mode changes.  It is free to anyone who wants it... I simply 
used it when I was playing with programming the VGA card.  Technically, 
the effect is achieved by call Int 10, sub-function 10, minor function 
03 with a value in BL to enable hi-intensity backgrounds.