PEDAL.COM

Author:		Keith Walker 	76505,2411
Date:		92.11.29

Description:
	A memory-resident (TSR) routine to use a foot pedal (connected to the 
	game port) as a remote spacebar.  This allows the pedal to be used to 
	start and stop playback in CAKEWALK.

Call:
	C> PEDAL	Installs the TSR routine
	C> PEDAL/r	Removes the TSR routine from memory
			NOTE: no space before "/", "r" is lowercase

Messages:
	PEDAL installed		   Normal result of installation
	PEDAL already installed	   Attempt to reinstall when already installed
	PEDAL removed		   Normal result of removal
	PEDAL is not installed	   Attempt to remove when not installed

Special Hardware Required:
	Requires a game port
	Requires a normally-closed foot switch, with ground wire connected to
	pin 4 of the game port, and the live wire connected to pin 2.