R T T Y   2 2 0 0 . 0 0   for IBM-PC MSDOS SYSTEMS

                       BY Perry Taylor, W0SE

                          JAN 1st., 1986

       The  RTTY  2000  series of Amateur Radio Teletype Programs
    were originally developed for  Heathkit  Computers,  and  are
    based  on much of the original work of Irv Hoff, W6FFC, Keith
    Peterson, W8SDZ, and others, on the Heath Computer net.  This
    series of programs has added split screen,  and  consolidated
    some of the concepts and programs, originated by the group on
    the net.

       One  of  features  of the program, that may be new to many
    who first use this program, is the 3rd and 4th level transmit
    and receive of ASCII characters, via the BAUDOT  level  code.
    By  adding a third and fourth level shift, to the two already
    available in the BAUDOT code, it is possible to send all  the
    ASCII  characters,  over the BAUDOT channel.  This is done by
    making a third shift of BLANK-FIGS, and a  fourth  of  BLANK-
    LTRS.   The  use  of this feature is explained in the body of
    this file.

       Prior  to  using this version of RTY.EXE, please remove or
    erase any previous RTY.CFG file. Set TIME/DATE for MS-DOS, as
    this  is used in the RTY program.  Use all "UPPER-CASE" while
    configuring the RTY program.

       This  version  of  RTY  requires  192k or more of RAM, and
    version 2.0 or higher of MSDOS.  The FILES parameter  in  the
    CONFIG.SYS  file  should  be  reviewed.  See page 9.19 in the
    MSDOS version 2.0 Heath Manual for details.  This program can
    use as many as four files at one  time,  and  the  CONGIF.SYS
    file should be set for 4 or more FILES.

    OPERATION:

       When  calling  up  RTY.EXE  for  the first time, the first
    thing that will be shown is the "TITLE SCREEN".  Hit any key,
    and the "CONFIGURATION" screen will be available.  Enter  the
    values  on  this  screen to fit your requirements and station
    hardware.  This builds a configuration record  which  can  be
    saved  on  disk  by pressing the "f7" key.  The next time the
    program is called, this configuration  record  will  be  read
    from disk.




















                Page 2 - RTTY 2200 IBM PC (MSDOS)


    CONFIGURATION ITEMS:

        Using all capital letters, fill in the items shown on the
    screen, customized as desired.

    ITEM:                               COMMENTS:

    File Name for Sending:              File name of file to be
                                        sent or saved with "Alt-N"   
    File Name Disk Out:                 File name for file copy

    Max File Size:                      File copy max size

    Margin:                             Custom left margin

    Baud Rate Index (RTTY):             Index from chart at right

    Transmit Line Length:               Length of line sent

    Call Sign:                          Your station call sign

    Time Zone:                          Your time zone

    Pace:                               Delay between chars sent

    Length of Diddle:                   Number of chars in callup
                                        diddle line

    RTTY Port (A or B):                 Port A=COM1, B=COM2      

    ASCII Printer Port (A, B, or Z):    Which port for Printer?

    Baud Rate Index (Printing):         From index at right

    Printer Ready Low(Y or N)           DTS High="N"

    Printer Line Length:                How long a printer line

    Print Received (Y or N):            Print incoming data

    Print Sent (Y or N):                Print outgoing data

    Disk Out Mode ( R, T, B, of N):     What do you want to copy?

    Pix Mode (Y or N):                  Pix, anyone?

    Auto Run Mode:                      Start with RUN SCREEN

    New Line for BAUDOT:                What will you have?

    New Line for ASCII:                 Ditto.

    Screen Saver:                       "Y" for 10 min. blank

    Split Line Location:                Split line location

    WRU on callsign only (Y or N):      Yes=response on ZW only




                Page 3, RTTY 2200.00 IBM PC (MSDOS)

    DISCUSSION:

    DISK COPY:

       This  program  can  "LOG" both incoming and outgoing copy.
    In the field "DISK OUT MODE", "R" means "RECEIVE", "T"  means
    "TRANSMIT",  "B"  means  "BOTH"  and "N" means "NEITHER".  If
    this field has been programmed "N", and when  in  "RUN",  the
    CONTROL-Y is pressed, the "N" will change to "R".  "DISK COPY
    MODE"  comes  up automatically if "CONFIGURED" for "R","T" or
    "B" and a fname.ext has  been  entered  in  the  "DISK  COPY"
    field.   It is suggested that a fname.ext such as "JAN01.AAA"
    be  used  so  that  each  day's  DISK  COPY  can  be   easily
    identified.

    MAX DISK OUT SIZE:

       The  number  of  characters  for a disk output file can be
    specified, to allow editing of the  file  by  small  editors.
    When  the  output  file  reaches  this  size it is closed and
    another is opened, with an incremented fname.ext.  If set  to
    zero  of  blank, then the maximum will be the amount of space
    left on the disk.

    FILE NAMES :

       All disk file names can include directory names.  The only
    restriction is that the fully qualified name length can be no
    more  than 26 characters.  For directory display, a path name
    can be used and all files at the end of that  path  name  are
    listed.   A blank path name defaults to the current drive and
    directory.  If all files on a non-default  drive  are  to  be
    listed, then the colon must be used.  e.g.  "d:"

    OUTPUT FILE NAME:

        The output file name is incremented in the last character
    shown, even if there is no extension.

    e.g. FILEA, FILEB, FILEC,......,FILEZ if named without an
         extension.
         FILEA.RYA, FILEA.RYB,......,FILEA.RYZ if named with an 
         extension, such as RYA...

    END OF LINE SEQUENCES:

       This  controls  the  sequence  sent whenever a new line is
    started from the transmitted text.  It is  triggered  by  the
    RETURN  key,  automatic wrap of a line being entered into the
    buffer, or by a NEWLINE (0AH, same as  LINE  FEED)  character
    from  a disk input file.  Baudot allows CARRIAGE RETURN (CR),
    LINE FEED (LF), LETTERS (LTRS), or FIGURES (FIGS).  ASCII
    allows CARRIAGE RETURN (CR), LINE FEED (LF), or NULL (00H).
    If left blank, the default sequence is LINE FEED (one).

    PROGRAMMABLE LINES:

       Program the "PROGRAMMABLE LINES "A" and "B".  Line "A" and
    "B" will be put into the "CONFIGURATION" record, but each can
    be  changed  by  going  to  the "CONFIGURATION" screen at any
    time.



                Page 4, RTTY 2200.00 IBM PC (MSDOS)

    AUTO RUN:

       A  new  option has been added on the CONFIGURE screen that
    allows specifying "AUTOMATIC or MANUAL" operation,  when  the
    program  is  called.   This  will make possible the automatic
    re-booting of the program, after a power glitch  or  failure,
    and  continued operation of the RTY program.  The RTY program
    will start with the RUN screen, if the item "AUTO  RUN  MODE"
    is  a "Y".  To modify the configuration, the CONFIGURE screen
    is still available by hitting the F1 key.  Of course, the RTY
    program must be called from an "AUTOEXEC.BAT" file,  for  the
    "AUTO RUN MODE" to be effective, upon a re-boot.

    BAUD RATES:

       The  lower  right  corner of the screen will show "Receive
    Mode" if receiving and "Send Mode" if transmitting.  Just  to
    the left of the Mode indication there will be a letter "B" or
    "A"  and  a baud rate.These are from the configuration screen
    and indicate Baudot or ASCII and the baud rate for  the  RTTY
    input  and  output  speed.  The input and output speed can be
    set from the "RUN" screen by hitting keys  "f2  or  f3".   f2
    will program 45 baud BAUDOT, and f3 will step through all the
    normal BAUDOT and ASCII baud rates.

    PRINTER:

       If  the printer has been programmed "ON" and the middle of
    the 24th line shows "PRINTER", this means that the printer is
    either not "READY" of the "HANDSHAKE" line  is  not  properly
    set.

    3RD AND 4TH LEVEL OPERATION:

       One  of the newest features of this program is called "3rd
    and 4th level BAUDOT".   This  is  a  programming  method  of
    sending  the  full ASCII character set over a BAUDOT channel.
    This  program  always  transmits  with  3rd  and  4th   level
    characters, and is always available.

      Unlock the "CAPS LOCK", to send lower case data.  The print
   on  a TTY machine, or on a CRT (with other than this program),
   will show as if it were  normal  Baudot.   Of  course,  normal
   ASCII at 100 WPM can also be used, if desired.

      Toggle  3rd  and 4th level receive by hitting the "f7 key",
   (while in RUN) and note the "3/4" on the  left  of  the  Split
   line,  which  means  that  the  3rd  and  4th level receive is
   active.  The program comes up in 3/4 mode. 

       Irv  Hoff's  IRTTY  HDOS  program will receive 3rd and 4th
    level BAUDOT and some of his HDOS and CP/M drivers will  send
    3rd and 4th level.

    DISK OPERATIONS:

      When using "DISK COPY or DISK TRANSMIT", a word in the left
   half  of  the 24th line will show "IN" or "OUT", meaning "Disk
   INput of Disk OUTput".  If there is an error, then  the  error
   will be indicated next to the "IN" or "OUT" depending on which
   has the problem.



                Page 5, RTTY 2200.00 IBM PC (MSDOS)

       From  the  "RUN" screen, "Alt-N" will allow you to enter a
    "d:fname.ext"  to  send  without  going  to  the  "CONFIGURE"
    screen.   The entry made will be placed into the field called
    "Filename for Sending".  End by typing RETURN.

       "CTRL-D"  calls  up  the  file  to  be  sent, and a second
    "CTRL-D", stops or aborts the file.  Call up the  file  where
    ever in the pre-typing or transmit, the file should be sent.

       SAVE  PRE-TYPE  BUFFER  TO  DISK.   Prepare the doc in the
    pre-type buffer that you wish to put into a special fname.ext
    file.  Then hit "Alt-N", and then follow  directions  on  the
    lower  area  of  the  screen.   The  contents of the pre-type
    buffer will remain unchanged but the data will be written  to
    the  disk.  The pre-type buffer can then be cleared by typing
    "Alt-V".  After that, the file can be reloaded, at  any  time
    to send it, by typing "CRTL-D" in the normal manner.

       DELETE  FILE  FROM  DISK.  To delete a file from disk, hit
    the "Alt-N", and follow directions given on the lower lines.

    HELP SCREEN:

       From  the  "RUN"  screen,  hit  "Alt-H"  to see all of the
    programs controls that are available.  Type "RETURN" to  exit
    the  Help screen.  No incoming data will be lost when looking
    at the control  menu.   The  unsent  pre-type  data  will  be
    scrolled  back  into  the  pre-type area when the "RETURN" is
    hit.  Transmit will stop while in the "HELP" screen, but will
    resume when "RETURN" is hit.

       DISPLAY OF DISK DIRECTORY.  Type "CTRL-A" while the "HELP"
    screen  is displayed.  Then type the ID (in UPPERCASE) of the
    drive on which there is a disk  mounted,  that  you  want  to
    display the directory.Type "A","B","C", or "D" for the MS-DOS
    drive  directory.   Type  "RETURN"  to  return  to the "HELP"
    screen, and a second "RETURN" to return to the "RUN" mode.

    FAST BREAKIN:

       This  mode  is  toggled by "Alt-B".  The letters "bk" will
    appear  on  the  left  of  the  split  line,  when  operating
    "BREAKIN".   The  "CTRL-G" will send "-BK-", and turn off the
    transmitter with out the 4 N's.  "CTRL-X" will  send  only  4
    diddles,  and then the pre-typed data, when in this mode.  Do
    not use "BREAKIN" mode unless you are truely using  "BREAKIN"
    as  most  demodulators  can  not  start  printing with so few
    start-up diddles.
       
    RELAY:

       In   the  "RELAY"  mode,  there  is  a  timer  to  prevent
    untransmitted  relay  messages  to  linger  in  the  Pre-type
    buffer.   Ths  timer  is  one  hour long, which prohibits any
    relay message longer than 30 minutes.  If the timer  expires,
    the  relay message is cleared and the relay function is armed
    for another usage.







                Page 6, RTTY 2200.00 IBM PC (MSDOS)

    NOTE: To use the relay system, follow these steps:

    1.   Send  call  of  station having a RTY program operational
    with ZC.
   
        callsignZC "CR" (puts relay station into RELAY MODE)
        callsignZC "CR" (send a second time to assure reception)

    2. Send normal message to station: "W0NW de W0SE etc."

    3. Send "CR" then "four N's" and a "CR"

    4. Send call of station being used for relay,with ZR

           callsignZR (tells relay station to relay)

    5. Hit CTRL-V to leave the air immediately

    6. Watch relay being made.

    PIX:

       In  the  "PIX  MODE",  the "UNSHIFT ON SPACE" is disabled.
    The shift stays the same as it was before the space. 

    BUFFERS:

       Depending  of the amount of RAM available, the size of the
    buffers is displayed at the  bottom  of  the  "CONFIGURATION"
    screen.   There  are  three  buffers  of  this size: Received
    Characters, Pretype for sending, and DISK OUTPUT.

    LENGTH OF DIDDLE:

        The number of diddles (LTRS in BAUDOT, NULL in ASCII),
    sent at the start of each "non break-in" mode transmission,
    can be specified. The value can be from 1 to 99, and if left
    blank or set to zero, then the default value of 32 is used.

    WRU on CALLSIGN:

        If this item is set to "Y", the WRU will not respond to
    the :DISK of :TIME command, but only to callsignZW. This mode
    is indicated on the left of the split line by a reverse video
    "I". A count is kept of the number of times a WRU is requested
    of the station (whether it is sent of not). The count is dis-
    played on the right of the split line. This count will alert
    the operator of possible messages in the copy.

    PACE:

       To  smooth  out the transmitted output, when a slow typist
    is typing in "real time", a delay between characters  can  be
    programmed  on the line called "PACE".  Any number from blank
    to 999 will  add  from  none,  to  999  millaseconds  between
    characters, thus smoothing out the output. Characters are
    still send at the programmed rate, but the average speed is
    reduced to smooth out the typing.







                Page 7, RTTY 2200.00 IBM PC (MSDOS)

    Following are the controls for RTTY 2200.00 (MS-DOS)

       CTRL-x means key x, while holding down the CONTROL key.

                CTRL-A - Play string A
                CTRL-B - Play BELL
                CTRL-C - Enter twice to return to MS-DOS
                CTRL-D - Toggle Disk Input to Transmit ON/OFF
                CTRL-E - Play String B
                CTRL-F - Replay Previous or Manual (ZR)
                CTRL-G - Go to Receive After NNNN 
                CTRL-K - Kill Transmitter Immediately
                CTRL-L - Turn up newline/fancy margin
                CTRL-N - Play Station ID
                CTRL-R - Play RYRY (U*U*U* in ASCII)
                CTRL-T - Play Time/Date
                CTRL-U - Send WRU
                CTRL-V - Go to Receive Mode without NNNN
                CTRL-W - Force DISK COPY write
                CTRL-X - Go to Send Mode with X diddles
                CTRL-Y - Toggle Disk Copy ON/OFF
                CTRL-Z - Toggle Gimic ON/OFF (fig in upper right)
                CTRL-_ - Clear Receive Screen


                f1 Key - Toggle RUN/CONFIGURATION Screens
                f2 Key - 45.45 baud (Baudot 60 WPM)
                f3 Key - 50 baud to 9600 baud stepping 

                Alt-A - Toggle 3/4 Level Receive
                Alt-B - Toggle Break Mode
                Alt-C - Same as Ctl_C
                Alt-F - Force Relay Record
                Alt-H - Display This Screen (HELP)
                Alt-N - Enter DIsk Input Fname
                        (or Save Pretype BUffer
                        or Delete File)
                Alt-P - Clear Print Buffer
                Alt-Q - Play "Quick Brown Fox etc."
                Alt-R - Toggle Relay Mode
                Alt-V - Clear Pretype Buffer

                ESC-RETURN - Send Bare CR (PIX ONLY)


       This version of RTY will respond to the following incoming
    commands, if preceeded by either a CR of LF, and the Pre-type
    buffer of the called station, is clear or empty.

        callsignZC - Set RELAY to copy incoming
        callsignZR - Relay message, with VIA etc.
        callsignZP - Replay previous transmission
        callsignZD - Put incoming to disk, if in DISK COPY
        callsignZW - Play WRU
        callsignZL - See Below Explanation for Remote WRU
        callsignZM - See Below Explanation for Remote WRU
        :TIME - Play all WRU'S
        :DISK - Play all WRU'S if in DISK COPY
        :xTIME - Play x call area WRU's (use 0 to 9 for x)
        :xDISK - Play x call area WRU's (use 0 to 9 for x)







                Page 8, RTTY 2200.00 IBM PC (MSDOS)

    REMOTE WRU FUNCTION:

       To  determine  if a remote station is active, when you can
    not hear the  station  on  a  direct  path,  the  REMOTE  WRU
    function is available.  The function will only work when this
    version of the RTY program is in use at the relay station and
    the  remote  station.   Any  local  station  can activate the
    function.

       By  the use of specific "Z" signals, a remote, but unheard
    station, can be triggered to send its WRU,  through  a  relay
    station, and thus be heard by the originating station.

        Following is the procedure to activate this feature:

        ------------        -----------          -----------
        : Original :        : Relay   :          : Remote  :
        : Station  :----\---: Station :-----\----: STATION :
        :          :        :         :          :         :
        ------------        -----------          -----------

    Callsigns:
           aaaaa              bbbbb                ccccc

    Action:                             Comments:

    aaaaa Sends:                        Calling station
    bbbbbZLccccc<ret>                   Request bbbbb to call WRU
    NNNN                                Hit CTRL-G, for NNNN's
    -
    bbbbb Sends:                        Response from bbbbb
    cccccZMbbbbb                        Ask ccccc to relay WRU
    NNNN                                Normal 4 N's
    -
    ccccc Sends:                        Response from ccccc
    bbbbbZC                             Set relay at bbbbb
    WRU for ccccc                       Normal WRU from ccccc
    bbbbbZR                             Request bbbbb relay
    -
    bbbbb then relays the WRU of ccccc, for all to hear.
    -
       No operator intervention is required at any station, other
    than  at the originating station.  The remote station must be
    "ON", and its Pre-type buffer empty.
     

    Have FUN!!!!  And have any kind of a day you would like.....

    de W0SE AND W0NW...